D	Cosmos 974	1978-O1 A	1978 Jan 6.66	Sphere-	6.5 long?	1978 Jan 7.5	62.81	89.61	6634	178	334	0.012	78

R	[Soyuz 11A511U] 	[10554]	12.60 days	cylinder	2.4 dia	1978 Jan 14.2	62.81	89.49	6678	175	325	0.011	74

PLE	1978 Jan 19.26	6300?

D	Cosmos 974	1978-01 B	1978 Jan 6.66	Cylinder	7.5 long	1978 Jan 8.7	62.80	89.09	6609	168	293	0.009	70

Block I 3rd stage 	[10555]	5 days	2500?	2.6 dia

1978 Jan 11

D	Cosmos 974	1978-01 D	1978 Jan 6.66	Cone	1.5 long?	1977 Jan 19	62.8	89.47	6627	189	308	0.009	-

engine	[10601]	20 days	600? full	2 dia?

1978 Jan 26

D	Fragment	1978-O1 C	[10556]	1978 Jan 25	19 days

D	Fragment	1978-O1 E	[10602]	1978 Jan 21	15 days

Intelsat 4A-3	1978-02 A	1978 Jan 7.01	Cylinder	2.82 long	1978 Jan 7.0	21.82	640.44	24612	549	35918	0.719	179

[Atlas SLV-3D AC-46	[10557]	> million	1500 full	2.39 dia	1978 Mar 15.5	0.37	1436.12	42165	3@783	3@790	0.0001	-

Centaur-D 1AR 5026D] CC-LC36B	years	795 empty		2004 Jul 5.47	12.27	1441.35	42268	35859	35919	0.0007	72

Intelsat 4A-3	1978-02 B	1978 Jan 7.01	Cylinder	8.6 long	1978 Jan 20.3	21.60	648.98	24830	612	36292	0.719	188

Centaur 46 stage	[10722]	6000 years	1815	3.0 dia	2004 Jul 6.00	21.11	649.43	24842	692	36235	0.715	320

D	Soyuz 27*	1978-03 A	1978 Jan 10.52	Sphere-	7.5 long	1978 Jan 10.6	51.71	88.71	6592	190	237	0.004	90

2M	[Soyuz 11A511U] 	[10560]	64.95 days	cylinder	2.3 dia	1978 Jan 10.8	51.58	89.90	6651	241	304	0.005	227

R		BAI	1978 Mar 16.47	6570?		1978 Jan 11.6	51.60	91.28	6718	330	350	0.002	101

D	Soyuz 27	1978-03 B	1978 Jan 10.52	Cylinder	7.5 long	1978 Jan 10.8	51.64	88.68	6590	193	231	0.003	79

Block I 3rd stage 	[10583]	3 days	2500?	2.6 dia

1978 Jan 13

*	Soyuz 27 docked with Salyut 6 (first airlock) on 1978 Jan 11.59; undocked from Salyut 6 on 1978	Mar 16.33 but landed with the Soyuz 26 crew.

The Soyuz 27 cosmonauts returned to Earth in the Soyuz 26 craft, which undocked from Salyut 6 (	second airlock) on 1978 Jan 16.

D	Cosmos 975	1978-04 A	1978 Jan 10.56	Cylinder	5 long?	1978 Jan 12.4	81.22	97.62	7022	634	653	0.001	57

[Vostok 8A92M] 	[10561]	8653 days	2 vanes?	1.5 dia?	2001 Sep 19.14	81.14	87.80	6544	162	170	0.0006	218

PLE	2001 Sep 19	2500?

Cosmos 975	1978-04 B	1978 Jan 10.56	Cylinder	3.8 long	1978 Jan 19.6	81.23	97.63	7022	594	694	0.007	146

Block E 3rd stage 	[10582]	60 years	1440	2.6 dia	2004 Jul 10.82	81.19	93.43	6821	433	453	0.001	313

Cosmos 976 *	1978-05 A	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 12.9	74.03	115.14	7839	1457	1465	0.0005	77

[Kosmos 11K65M 	[10581]	9000 years	40?	0.8 dia?	2004 Jul 6.43	74.03	115.08	7838	1455	1463	0.0006	268

53716-319]	PLE

Cosmos 977 *	1978-05 B	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 14.9	74.03	114.54	7812	1403	1465	0.004	81

[10584]	7000 years	40?	0.8 dia?	2004 Jul 5.86	74.03	114.47	7810	1399	1463	0.004	93

Cosmos 978 *	1978-05 C	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 18.6	74.03	114.74	7821	1421	1465	0.003	87

[10585]	8000 years	40?	0.8 dia?	2004 Jul 6.14	74.03	114.68	7819	1418	1463	0.003	166

Cosmos 979 *	1978-05 D	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 14.5	74.03	114.95	7831	1440	1465	0.002	86

[10586]	9000 years	40?	0.8 dia?	2004 Jul 4.89	74.03	114.88	7828	1436	1463	0.002	220

Cosmos 980 *	1978-05 E	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 13.9	74.03	115.36	7850	1465	1478	0.0008	287

[10587]	10000 years	40?	0.8 dia?	2004 Jul 5.59	74.03	115.30	7847	1462	1475	0.0008	191

Cosmos 981 *	1978-05 F	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 12.7	74.03	115.59	7860	1465	1498	0.002	264

[10588]	10000 years	40?	0.8 dia?	2004 Jul 5.22	74.03	115.53	7858	1463	1495	0.002	227

Cosmos 982 **	1978-05 G	1978 Jan 10.87	Spheroid	1.0 long?	1978 Jan 13.9	74.03	115.81	7870	1465	1518	0.003	273

[10589]	10000 years	40?	0.8 dia?	2004 Jul 5.91	74.03	115.75	7868	1463	1515	0.003	300

Cosmos 983 **	1978-05 H	1978 Jar 10.87	Spheroid	1.0 long?	1978 Jan 18.6	74.03	116.05	7881	1465	1540	0.005	258

[10590]	10000 years	40?	0.8 dia?	2004 Jul 4.90	74.03	115.98	7879	1463	1537	0.005	4

Cosmos 976-983	1978-05 J	1978 Jan 10.87	Cylinder	7.4 long	1978 Jan 14.0	74.03	117.74	7957	1465	1693	0.014	268

2nd stage	[10591]	20000 years	2200?	2.4 dia	2004 Jul 6.82	74.03	117.70	7956	1463	1693	0.014	115

*	Strela-1M

D	Cosmos 984	1978-06 A	1978 Jan 13.64	Sphere-	5.0 long	1978 Jan 14.6	62.81	89.45	6627	206	291	0.007	80

R	[Soyuz 11A511U] 	[10592]	12.7 days	cylinder	2.4 dia

PLE	1978 Jan 26.3	5700?

D	Cosmos 984	1978-06 B	1978 Jan 13.64	Cylinder	7.5 long	1978 Jan 14.7	62.79	89.31	6620	207	276	0.005	74

Block I 3rd stage 	[10593]	9 days	2500?	2.6 dia

1978 Jan 22

Cosmos 985*	1978-07 A	1978 Jan 17.14	Cylinder	2.1 long	1978 Jan 17.6	82.94	104.79	7362	945	1022	0.005	298

[Kosmos 11K65M 	[10599]	1200 years	810	2.0 dia	2004 Jul 5.21	82.94	104.62	7355	938	1014	0.005	300

53716-327]	PLE

Cosmos 985	1978-07 B	1978 Jan 17.14	Cylinder	7.4 long	1978 Jan 23.7	82.94	104.66	7356	943	1012	0.005	279

2nd stage	[10600]	600 years	2200?	2.4 dia	2004 Jul 6.98	82.94	104.48	7349	936	1004	0.005	244

Fragment	1978 07 C #	[11587]			1979 Oct 17.22	82.95	104.58	7354	960	990	0.002	283

2004 Jul 6.29	82.93	100.68	7169	780	802	0.002	306

1978 07 D	[23836]			1996 Mar 27.97	82.94	104.03	7328	912	986	0.005	32

2004 Jul 9.92	82.94	103.45	7300	887	957	0.005	55

*	Navigation satel1ite.

#	Re-assigned from 1979 90 C

D	Progress 1*	1978-08 A	1978 Jan 20.35	Sphere-	7 9 long	1978 Jan 20.5	51.61	88.73	6593	173	256	0.005	86

[Soyuz 11A511U	[10603]	18.81 days	cylinder	2.3 dia	1978 Jan 21.7	51.66	90.29	6670	250	334	0.006	199

E15000-075]	BAI-LC31	1978 Feb 8.16	7020		1978 Jan 22.4	51.60	91.25	6717	329	348	0.002	-

D	Progress 1	1978-08 B	1978 Jan 20.35	Cylinder	7.5 long	1978 Jan 20.7	51.65	88.66	6589	188	234	0.004	79

Block I 3rd stage 	[10604]	3 days	2500?	2.6 dia

1978 Jan 23

*	Unmanned fuel-and-supplies ferry, without Soyuz descent capability. Docked with Salyut 6 (second airlock) on 1978 Jan 22.42. Separated Feb 6.25.

De-orbited over Pac	ific Ocean two days later.

D	Molniya-3 9	1978-09 A	1978 Jan 24.29	Windmill	4.2 long?	1978 Jan 26.4	62.81	736.26	27010	646	40618	0.740	288

[Molniya 8K78M] 	[10605]	11.9 years	6 vanes	1.6 dia	1978 Feb 1.0	62.78	718.01	26563	652	39718	0.735	288

PLE-LC43/3	1989 Dec 5?	1500?

D	Molniya-3 9	1978-09 B	1978 Jan 24. 29	Cylinder	7.5 long	1978 Jan 24.4	62.78	92.95	6798	215	624	0.030	117

Block I 3rd stage 	[10606]	47 days	2500?	2.6 dia

1978 Mar 12

D	Molniya-3 9	1978-09 C	1978 Jan 24.29	Irregular	-	1978 Jan 24.5	62.81	93.18	6809	219	643	0.031	120

4th stage casing 	[10608]	38 days

1978 Mar 3

D	Molniya-3 9	1978-09 E	1978 Jan 24.29	Cylinder	2.0 long	1979 Jun 30.0	63.2	732.6	26920	813	40272	0.733	-

Block L 4th stage 	[10802]	4573 days	440	2.0 dia

1990 Aug 9

D	Molniya-3 9	1978-09 D	1978 Jan 24.29

Ullage motor	[10610]	43 days

1978 Mar 8

D	Cosmos 986**	1978-10 A	1978 Jan 24.41	Sphere-	6.5 long?	1978 Jan 25.1	65.01	89.39	6623	172	318	0.011	70

R	[Soyuz 11A511U] 	[10607]	13.8 days	cylinder	2.4 dia	1978 Jan 25.7	65.02	89.64	6636	171	344	0.013	68

BAI	1978 Feb 7.2	6300?

D	Cosmos 986	1978-10 B	1978 Jan 24.41	Cylinder	7.5 long	1978 Jan 24.5	65.01	89.29	6618	172	308	0.010	67

Block I 3rd stage 	[10609]	4 days	2500?	2.6 dia

1978 Jan 28

**	Cosmos 986 manoeuvred, but no jettisoned engine was apparently tracked or designated.

D	FSW-0 3 (China 8)*	1978-11 A	1978 Jan 26.21	Cylinder?	-	1978 Jan 26.7	57.03	90.90	6698	161	479	0.024	160

r	[CZ2C-3]	[10611]	12 days	3600

JQ-LA2	1978 Feb 7	then 1200?

D	FSW-0 3	1978-11 B	1978 Jan 26.21	Cylinder	7 long	1978 Jan 26.7	57.02	90.79	6693	160	469	0.023	159

rocket	[10612]	11 days		3.35 dia

1978 Feb 6

*	Capsule, weight 1850 kg, returned to Earth on 1978 Jan 30.

IUE 1**	1978-12 A	1978 Jan 26.73	Octagonal-	4.3 long	1978 Jan 26.8	28.71	840.64	29505	173	46081	0.778	257

[Delta 2914 628	[10637]	>million	cylinder	1.3 dia	1978 Jan 28.3	28.63	1435.7	42157	25669	45888	0.240	257

#138]	CC-LC17A	years	669 full		1996 Oct 10.37	35.64	1439.04	42222	30216	41472	0.133	61

2004 Jun 18.37	40.28	1438.92	42220	29187	42496	0.158	120

D	IUE 1	1978-12 B	1978 Jan 26.73	Cylinder	6.4 long	1978 Jan   26.8	28.74	96.56	6972	164	1024	0.062	254

Delta 2nd stage	[10638]	26 days	annulus	1.52 and

1978 Feb 21	350?	2.44 dia

IUE 1	1978-12 C	1978 Jan 26.73	Sphere-	1.32 long	1978 Jan 27.0	28.71	846.69	29648	177	46367	0.779	257

Star-37E PKM	[10723]	50 years	cone	0.94 dia	2004 Jul 6.13	29.28	391.23	17720	266	22417	0.625	171

66

Fragment	1978-12 D#	[33000]			2008 Jun 4.74	43.38	1434.57	42135	27380	44133	0.199	168

YO-weight	1978-12 E	[37762]			2011 Jul 26.33	24.65	698.92	26089	3688	35732	0.614	3

**	IUE is International Ultraviolet	Explorer, launched by NASA; shut down 1996 Sep 30.78

#	1978 12 D 26785 re-assigned to 1984 35 C. ID changed from E to D in 2011 Oct.

D	Cosmos 987	1978-13 A	1978 Jan 31.62	Sphere-	6.5 long?	1978 Feb 1.5	62.80	89.44	6626	175	321	0.011	71

R	[Soyuz 11A511U] 	[10639]	13.6 days	cylinder	2.4 dia	1978 Feb 6.1	62.80	89.72	6640	173	351	0.013	71

PLE	1978 Feb 14.2	6300?

D	Cosmos 987	1978-13 B	1978 Jan 31.62	Cylinder	7.5 long	1978 Feb 2.2	62.80	89.18	6613	169	301	0.010	67

Block I 3rd stage 	[10640]	4 days	2500?	2.6 dia

1978 Feb 4

D	Cosmos 987	1978-13 E	1978 Jan 31.62	Cone	1.5 long?	1978 Feb 13	62.8	88.56	6582	166	241	0.006	-

engine*	[10671]	20 days	600?	2.0 dia?

1978 Feb 20	full

D	Fragment	1978-]3 C	[10641]	1978 Feb 5	5 days

D	Fragment	1978-]3 D	[10670]	1978 Feb 20	20 days

*	Jettisoned from Cosmos 987 about 1978 Feb 13.

Kyokko (Exos A)**	1978-14 A	1978 Feb 4.29	Cylinder	0.8 long	1978 Feb 7.8	65.37	134.27	8687	642	3975	0.192	334

[Mu-3H #2]	[10664]	300 years	103	0.95 dia	2004 Jul 4.76	65.37	133.93	8672	641	3945	0.191	160

KAG-M

D	Kyokko	1978-14 B	1978 Feb 4.29	Cylinder?	-	1978 Feb 5.9	65.09	94.26	6862	331	636	0.022	160

Mu-3H 4th stage	[10665]	373 days

1979 Feb   12

Fragments	1978-14 C-H	6 pieces, 2 have decayed		For orbital information see extra pages at the end of the year

**	Japanese contribution to International Magnetospheric Study; Kyokko means aurora.

D	Cosmos 988	1978-15 A	1978 Feb 8.51	Sphere-	5.9 long	1978 Feb 11.8	72.84	89.87	6646	201	335	0.010	66

R	[Soyuz 11A511U] 	[10666]	11.80 days	cylinder	2.4 dia

PLE	1978 Feb 20.31	5900?

D	Cosmos 988	1978-15 B	1978 Feb 8.51	Cylinder	7.5 long	1978 Feb 12.8	72.84	89.35	6620	195	289	0.007	52

Block I 3rd stage 	[10667]	9 days	2500?	2.6 dia

1978 Feb 17

D	Capsule	1978-15 F	1978 Feb 8.51	Ellipsoid	0.9 long	1978 Feb 20	72.8	89.26	6615	203	271	0.005	-

[10680]	31 days	200?	1.9 dia

1978 Mar 11

D	Fragment	1978-15 C-E,G	  4 pieces, all have decayed		For orbital information see extra pages at the end of the year

Fleetsatcom 1	1978-16 A	1978 Feb 9.89	Hexagonal	1.27 long	1978 Feb 9.9	26.46	634.16	24451	167	35978	0.732	182

[Atlas SLV-3D AC-44	[10669]	> million	cylinder	2.44 dia	1979 Jun 30.0	1.7	1436.0	42163	35755	35816	0.001	-

Centaur D-1AR 5024D] CC-LC36A	years	1884 full		No TLE found

D	Fleetsatcom 1	1978-16 C	1978 Feb 9.89	Cylinder	8.6 long	2004 Aug 28.04	26.24	108.17	7520	221	2062	0.122	197

Centaur 44 stage	[12908]	10161 days 	1815	3.0 dia	2005 Dec 5.16	26.14	87.45	6527	131	165	0.003	256						2005 Dec 5

D	Fragment	1978 16 B	[10724]	1982 Aug 31	1664 days	1978 Feb 9.9	26.40	620.40	24096	172	35263	0.728	182

D	Fragment	1978-16 D	[13998]	1989 Jun 21	4150 days

D	Fragment	1978-16 E	[25145]	1998 Jan 27	7292 days	1998 Jan 23.52	26.23	97.96	7039	248	1074	0.059	151

D	Cosmos 989	1978-17 A	1978 Feb 14.40	Sphere-	5.9 long?	1978 Feb 20.1	65.05	89.36	6622	169	318	0.011	67

R	[Soyuz 11A511U] 	[10672]	13.8 days	cylinder	2.4 dia

BAI	1978 Feb 28.2	5900?

D	Cosmos 989	1978-17 B	1978 Feb 14.40	Cylinder	7.5 long	1978 Feb 15.4	65.06	89.28	6618	165	314	0.011	72

Block I 3rd stage 	[10673]	3 days	2500?	2.6 dia

1978 Feb 17

D	Capsule?#	1978-17 C	1978 Feb 14.40	Ellipsoid	0.9 1ong	1978 Feb 28	65.0	88.86	6598	175	264	0.007	-

[10690]	15 days	200?	l.9  dia

1978 Mar 1

D	Fragment	1978-17 D	[10691]	1978 Feb 28	14 days

#	Possibly an engine.

Ume 2* (ISS 2)	1978-18 A	1978 Feb 16.17	Cylinder	0.82 long	1978 Feb 18.7	69.37	107.25	7478	975	1224	0.017	202

[Nu-1 N-4(F)]	[10674]	1400 years	140	0.94 dia	2004 Jul 10.24	69.36	107.18	7474	973	1219	0.016	173

TAN-O

Ume 2	1978-18 B	1978 Feb 16.17	Cylinder	1.74 long	1978 Feb 18.7	69.36	107.24	7477	975	1223	0.017	202

Nu 3rd stage	[10675]	700 years	66?	1.65 dia	2004 Jul 6.93	69.36	107.10	7471	973	1213	0.016	171

Fragment	1978-18 C	[13132]

*	Japanese Ionospheric Sounding Satellite.

Cosmos 990	1978-19 A	1978 Feb 17.69	Cylinder	2 long?	1978 Feb 18.2	74.05	100.80	7174	783	809	0.002	359

[Kosmos 11K65M 	[10676]	120 years	paddles?	1 dia?	2004 Jul 6.94	74.04	100.32	7152	761	786	0.002	235

53746-312]	PLE		750?

Cosmos 990	1978-19 B	1978 Feb 17.69	Cylinder	7.4 long	1978 Feb 19.9	74.04	100.67	7168	774	805	0.002	21

2nd stage	[10677]	100 years	2200?	2.4 dia	2004 Jul 11.09	74.04	100.08	7141	751	774	0.002	175

Fragment	1978-19 C	[13500]			2004 Jul 7.36	74.06	98.97	7088	701	718	0.001	311

Fragment	1978-19 D	[14803]			2004 Jul 7.08	74.04	97.63	7024	642	648	0.0004	111

Fragment	1978-19 E	[18501]			2004 Jul 7.72	74.06	99.07	7093	706	723	0.001	354

Navstar 1	1978-20 A	1978 Feb 22.99	Cylinder +	-	1978 Mar 7.0	63.27	718.67	26580	20095	20308	0.004	348

(GPS)*	[10684]	1 million	4 vanes		2004 Jul 6.19	64.04	727.00	26783	20259	20549	0.005	170

[Allas 64 F/SGS-1]	VDB-SLC3E	years	871 full

525 empty

D	Navstar 1	1978-20 B	1978 Feb 22.99	Cone-	1.85 long?	1978 Feb 23.2	63.00	354.81	16605	161	20292	0.606	158

Star-37E PKM	[10801]	12589 days	cylinder?	0.63 to	2004 Jul 4.92	63.67	268.18	13776	513	14282	0.500	22

2012 Aug 11	163?	1.65 dia?	2012 Aug 11.16	62.77	89.35	6621	106	377	0.020	44

*	Global Positioning System

SDS 4 (Jumpseat 5)	1978-21 A	1978 Feb 25.2?	Cylinder	-	1978 Feb 25	63.15	703.7	26222	311	39377	0.745	270**

[Titan 34B-2 3B-49	[10688]	100 years?			No elements available

Ascent Agena D]	VDB-SLC4W

SDS 4	1978-21 B	1978 Feb 25.2?	Cylinder	6 long?			Orbit similar to 1978-21A

Agena D stage	[10689]	100 years?	700?	1.5 dia	No elements available

** Approximate orbit

Cosmos 991	1978-22 A	1978 Feb 28.28	Cylinder	2.1 long	1978 Mar 1.1	82.98	104.84	7364	963	1009	0.003	301

[Kosmos 11K65M 	[10692]	1200 years	810	2.0 dia	2004 Jul 6.51	82.99	104.63	7356	949	1006	0.004	41

53716-323]	PLE

Cosmos 991	1978-22 B	1978 Feb 28.28	Cylinder	7.4 long	1978 Mar 2.2	82.98	104.74	7359	960	1002	0.003	287

2nd stage	[10693]	600 years	2200?	2.4 dia	2004 Jul 7.09	82.98	104.55	7352	958	989	0.002	350

D	Soyuz 28 #	1978-23 A	1978 Mar 2.64	Sphere-	7.5 long	1978 Mar 2.9	51.63	88.82	6597	192	246	0.004	86

2M	[Soyuz 11A511U] 	[10694]	7.93 days	cylinder	2.3 dia	1978 Mar 3.3	51.62	90.02	6657	251	306	0.004	283

R		BAI-LC1	1978 Mar 10.57	6570?		1978 Mar 3.9	51.62	91.35	6722	334	353	0.001	233

D	Soyuz 28	1978-23 B	1978 Mar 2.64	Cylinder	7.5 long	1978 Mar 3.2	51.63	88.80	6596	1 91	245	0.004	87

Block I 3rd stage 	[10695]	3 days	2500?	2.6 dia

1978 Mar 5

#	Soyuz 28 docked with Salyut 6 (2nd airlock) on 1978 Mar 3.715, with one Russian and one Czechoslovak cosmonaut; undocked 1978 Mar 10.43

D	Molniya-1 39	1978-24 A	1978 Mar 2.92	Windmill +	3.4 long	1978 Mar 5.0	62.82	738.14	27056	617	40739	0.741	288

[Molniya 8K78M] 	[10696]	5121 days	6 vanes	1.6 dia	1978 Mar 13.1	62.83	717.79	26557	615	39743	0.737	288

PLE	1992 Mar 9	1000?		1992 Mar 8.32	61.70	158.48	9701	78	6567	0.334	264

D	Molniya-1 39	1978-24 B	1978 Mar 2.92	Irregular	-	1978 Mar 4.5	62.83	92.70	6786	210	605	0.029	116

4th stage casing 	[10697]	39 days

1978 Apr 10

D	Molniya-1 39	1978-24 C	1978 Mar 2.92	Cylinder	7.5 long	1978 Mar 4.2	62.76	92.48	6775	219	575	0.026	118

Block I 3rd stage 	[10698]	38 days	2500?	2.6 dia

1978 Apr 9

D	Molniya-1 39	1978-24 D	1978 Mar 2.92	Cylinder	2.0 long	1979 Jun 30.0	63.9	729.4	26843	671	40259	0.737	-

Block L 4th stage 	[10803]	5398 days	440	2.0 dia

1992 Dec 11

D	Cosmos 992	1978-25 A	1978 Mar 4.32	Sphere-	5.0 long	1978 Mar 4.8	71.34	89.79	6641	203	323	0.009	59

R	[Soyuz 11A511U] 	[10699]	12.9 days	cylinder	2.4 dia

BAI	1978 Mar 17.2	5700?

D	Cosmos 992	1978-25 B	1978 Mar 4.32	Cylinder	7.5 long	1978 Mar 4.8	71.34	89.63	6633	201	309	0.008	50

Block I 3rd stage 	[10700]	6 days	2500?	2.6 dia

1978 Mar 10

D	Fragment	1978-25 C	[10701]	1978 Mar 5	1 day

Landsat 3	1978-26 A	1978 Mar 5.75	Cone +	3.0 long	1978 Mar 5.8	99.14	103.21	7287	900	918	0.001	307

(ERTS 3)	[10702]	100 years	2 paddles	1.45 dia	2004 Jul 5.59	99.39	103.12	7284	895	916	0.001	198

[Delta 2914 621	VDB-SLC2W		960	3.96 span

# 139]

Oscar 8	1978-26 B	1978 Mar 5.75	Rectangular	0.43 x	1978 Mar 5.9	98.99	103.23	7288	903	917	0.001	221

[10703]	100 years	box	0.30 x	2004 Jul 11.20	99.09	102.95	7277	893	903	0.0007	104

27	0.15?

Landsat 3	1978-26 C	1978 Mar 5.75	Cylinder	6.4 long	1978 Mar 5.9	98.95	103.22	7288	906	913	0.001	306

Delta 2nd stage*	[10704]	disintegrated	annulus	1.52 and	2004 Jul 6.79	99.02	103.78	7316	883	992	0.007	85

350?	2.44 dia

Fragments	1978-26 D- KL  248 pieces, 93 have decayed		For orbital information see extra pages at the end of the year

*	Carried PIX 1, a 34 kg Plasma Interaction Experiment.

Landsat 3 second stage disintegrated about 1981 Jan 27.19 over Antarctica near 80 deg South, 61 deg West.

D	Cosmos 993	1978-27 A	1978 Mar 10.45	Sphere-	6.5 long?	1978 Mar 11.8	72.86	89.63	6634	171	340	0.013	79

R	[Soyuz 11A511U] 	[10725]	12.7 days	cylinder	2.4 dia	1978 Mar 18.1	72.85	90.15	6660	170	393	0.017	64

PLE	1978 Mar 23.2	6300?

D	Cosmos 993	1978-27 B	1978 Mar 10.45	Cylinder	7.5 long	1978 Mar 11.3	72.86	89.32	6618	170	310	0.011	76

Block I 3rd stage 	[10726]	4 days	2500?	2.6 dia

1978 Mar 14

D	Cosmos 993	1978-27 D	1978 Mar 10.45	Cone	1.5 long?	1978 Mar 23	72.8	89.04	6604	180	272	0.007	-

engine	[10739]	14 days	600? full	2 dia?

1978 Mar 24

D	Fragment	1978-27 C	[10727]	1978 Mar 12	2 days

Cosmos 994	1978-28 A	1978 Mar 15.66	Cylinder	1.3 long?	1978 Mar 18.4	82.93	105.05	7374	980	1011	0.002	261

[Kosmos 11K65M 	[10731]	1200 years	700?	1.9 dia?	2004 Jul 5.55	82.93	104.88	7367	973	1004	0.002	231

53746-315]	PLE

Cosmos 994	1978-28 B	1978 Mar 15.66	Cylinder	7.4 long	1978 Mar 18.4	82.93	104.93	7368	977	1003	0.002	245

2nd stage	[10732]	600 years	2200?	2.4 dia	2004 Jul 7.45	82.93	104.72	7360	966	996	0.002	110

D	KH 9-14	1978-29 A	1978 Mar 16.78	Cylinder	15 long	1978 Mar 23.2	96.43	88.52	6578	160	240	0.006	125

[Titan 3D 23D-20]	[10733]	179 days	13300? full	3.0 dia

VDB-SLC4E	1978 Sep 11

Farrah 2	1978-29 B	1978 Mar 16.78	Octagon?	0.3 long?	1978 Mar 19.8	95.83	97.59	7020	639	645	0.0004	290

[10734]	60 years	60?	0.9 dia	No elements available

D	Titan 3D	1978-29 C	1978 Mar 16.78	Cylinder	6 long	1978 Mar 17	96.4	88.50	6577	166	231	0.005	-

2nd stage	[10737]	1 day	1900	3.0 dia

1978 Mar 17

D	Cosmos 995	1978-30 A	1978 Mar 17.45	Sphere-	5.0 long	1978 Mar 18.5	81.34	89.05	6604	217	235	0.001	52

R	[Soyuz 11A511U] 	[10735]	12.85 days	cylinder	2.4 dia

PLE	1978 Mar 30.30	5700?

D	Cosmos 995	1978-30 B	1978 Mar 17.45	Cylinder	7.5 long	1978 Mar 17.8	81.34	88.81	6592	208	220	0.001	8

Block I 3rd stage 	[10736]	3 days	2500?	2.6 dia

1978 Mar 20

Cosmos 996	1978-31 A	1978 Mar 28.06	Cylinder	2.1 long	1978 Mar 28.3	82.93	104.80	7362	957	1010	0.004	299

[Kosmos 11K65M 	[10744]	1200 years	810	2.0 dia	2004 Jul 4.88	82.92	104.63	7356	949	1004	0.004	150

53746-314]	PLE

Cosmos 996	1978-31 B	1978 Mar 28.06	Cylinder	7.4  long	1978 Mar 31.5	82.92	104.70	7357	957	1000	0.003	288

2nd stage	[10745]	600 years	2200?	2.4  dia	2004 Jul 6.97	82.93	104.48	7349	943	997	0.004	44

D	Cosmos 997	1978-32 A	1978 Mar 30.00	Cone	3.6 long			Orbit similar to	 1978-32 C

R	[Proton 8K82K 	[10770]	< 1 day	4250	2.8 dia max

292-01]	BAI-LC81P	1978 Mar 30

D	Cosmos 998	1978-32 B	1978 Mar 30.00	Cone	3.6 long			Orbit similar to 1978-32 C

R		[10771]	< 1 day	4250	2.8 dia max

1978 Mar 30

D	Cosmos 997	1978-32 C	1978 Mar 30.00	Cylinder	6.5 long?	1978 Mar 30.1	51.60	88.45	6579	188	213	0.002	237

third stage	[10772]	3 days		4 dia

1978 Apr 2

D	Fragment	1978-32 D	[10775]	1978 Apr 3	4 days

D	Cosmos 999	1978-33 A	1978 Mar 30.33	Sphere-	5.9 long?	1978 Mar 31.3	71.39	89.79	6641	174	352	0.013	55

R	[Soyuz 11A511U] 	[10773]	12.89 days	cylinder	2.4 dia

BAI	1978 Apr 12.22	5900?

D	Cosmos 999	1978-33 B	1978 Mar 30.33	Cylinder	7.5 long	1978 Mar 31.4	71.40	89.43	6623	174	316	0.011	50

Block I 3rd stage 	[10774]	4 days	2500?	2.6 dia

1978 Apr 3

D	Capsule?#	1978-33 E	1978 Mar 30.33	Ellipsoid?	0.9 long?	1978 Apr 12	71.3	89.39	6621	189	297	0.008

[10800]	25 days	200?	1.9 dia?

1978 Apr 24

D	Fragment	1978-33 C	[10798]	1978 Apr 13	14 days

D	Fragment	1978-33 D	[10799]	1978 Apr 16	17 days

#	Possibly an engine.

Cosmos 1000*	1978-34 A	1978 Mar 31.58	Cylinder	2.1 long	1978 Mar 31.9	82.93	104.90	7367	965	1012	0.003	290

[Kosmos 11K65M 	[10776]	1200 years	810	2.0 dia	2004 Jul 4.98	82.94	104.72	7360	956	1006	0.003	199

53768-307]	PLE

Cosmos 1000	1978-34 B	1978 Mar 31.58	Cylinder	7.4 long	1978 Mar 31.9	82.94	104.78	7361	964	1001	0.003	294

rocket	[10777]	600 years	2200?	2.4 dia	2004 Jul 6.97	82.94	104.57	7353	954	994	0.003	114

Fragment	1978 34 C %	[13474]			1981 Mar 3.77	82.94	104.35	7342	949	979	0.002	184

*	Navigational beacon.

%	Renamed from 1981 53 FW.

Intelsat 4A-6	1978-35 A	1978 Mar 31.98	Cylinder	2.82 long	1978 Apr 1.0	21.85	641.03	24627	549	35949	0.719	179

[Atlas SLV-3D AC-48	[10778]	> million	1500 full	2.39 dia	1978 Jul 15.0	0.3	1436.1	42165	35768	35806	0.0005	-

Centaur D-1AR 5028D] CC-LC36B	years	795 empty		2004 Jul 8.28	12.22	1435.97	42162	35746	35821	0.0009	71

Intelsat 4A-6	1978-35 B	1978 Mar 31.98	Cylinder	8.6 long	1978 Apr 25.9	21.90	647.40	24790	596	36227	0.719	195

Centaur 48 stage	[10779]	6000 years	1815	3.0 dia	2004 Jul 6.23	21.63	647.00	24780	622	36180	0.717	332

D	Cosmos 1001	1978-36 A	1978 Apr 4.63	Sphere-	7.5 long	1978 Apr 4.8	51.52	88.71	6@92	199	228	0.002	84

R?	[Soyuz-U 11A511U	[10783]	10.87 days	cylinder	2.7 dia	1978 Apr 6.2	51.63	89.28	6620	196	288	0.007	66

D15000-123]	BAI	1978 Apr 15.50	6850		1978 Apr 11.6	51.61	90.73	6691	307	318	0.001	302

D	Cosmos 1001	1978-36 B	1978 Apr 4.63	-	-	1978 Apr 4.8	51.63	88.59	6586	198	217	0.001	90

Block I 3rd stage 	[10784]	2 days

1978 Apr 6

D	Fragments	1978-36 C-F	4 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1002	1978-37 A	1978 Apr 6.39	Sphere-	5.0 long	1978 Apr 8.8	65.05	89.37	6622	205	283	0.006	52

R	[Soyuz 11A511U] 	[10785]	12.84 days	cylinder	2.4 dia

BAI	1978 Apr 19.23	5700?

D	Cosmos 1002	1978-37 B	1978 Apr 6.39	Cylinder	7.5 long	1978 Apr 1.3	65.05	89.13	6610	197	267	0.005	28

Block I 3rd stage 	[10786]	4 days	2500?	2.6 dia

1978 Apr 10

D	Fragment	1978-37 C	[10790]	1978 Apr 24	18 days

D	Fragment	1978-37 D	[10791]	1978 Apr 24	18 days

Rhyolite 3 *	1978-38 A	1978 Apr 7.03	Cylinder	1.7 long?	1978 Apr 8.0	29.9	87.72	6547	149	189	0.003	-

[Atlas SLV-3A	[10787]	> million	700 full?	1.4 dia?	1978 Apr 8.4	28.4	615.5	23970	150	35033	0.728	-

5505 A Agena D	CC-LC13	years	350 empty?		Probably entered	synchronous orbit similar to 1977-114 A

1554]					No elements available

D?	Rhyolite 3	1978-38 B	1978 Apr 7.03	Cylinder	6 long?	Orbit similar to 1978-38 A second orbit

Agena D stage	[10788]	10 years?	700	1.5 dia	No elements available

*	Early warning satellite development. (Aquacade 3)

Yuri 1 (BSE l)**	1978-39 A	1978 Apr 7.92	Irregular	3.09 long	1978 Apr 8.7	27.23	627.64	24287	164	35653	0.731	180

[Delta 2914 626	[10792]	> million	678 full	1.32 wide	1978 Apr 9.5	0.10	1415.75	41766	35115	35662	0.007	266

#140]	CC-LC17B	years	327 empty	1.2 deep	1978 Apr 26.5	0.08	1436.0	42163	35784	35786	0	247

2004 Jul 9.97	14.56	1435.13	42146	35663	35872	0.002	90

Yuri 1	1978-39 B	1978 Apr 7.92	Cylinder+	6.4 long	1978 Apr 7.9	28.64	92.93	6796	165	671	0.037	173

Delta 2nd stage	[10793]	250 years	annulus	1.52 and	1978 Apr 20.2	28.23	111.35	7673	569	2021	0.095	143

350?	2.44 dia	2004 Jul 6.44	28.23	110.47	7627	568	1928	0.089	115

D	Yuri 1	1978-39 C	1978 Apr 7.92	Sphere	1.32 long	1978 Dec 19.6	26.92	392.40	17750	225	22520	0.628	206

Star-37E PKM	[10794]	7455 days	-cone	0.94 dia

1998 Sep 4	66

**	Broadcasting Satellite Experiment launched for Japan by NASA.

D	Cosmos 1003	1978-40 A	1978 Apr 20.65	Sphere-	6.5 long?	1978 Apr 20.9	62.81	89.54	6631	178	328	0.011	71

R	[Soyuz 11A511U] 	[10811]	13.6 days	cylinder	2.4 dia	1978 Apr 23.9	62.81	88.89	6599	162	279	0.009	52

PLE	1978 May 4.3	6300?

D	Cosmos 1003	1978-40 B	1978 Apr 20.65	Cylinder	7.5 long	1978 Apr 21.2	62.80	89.32	6620	169	315	0.011	68

Block I 3rd stage 	[10812]	3 days	2500?	2.6 dia

1978 Apr 23

D	Cosmos 1003	1978-40 D	1978 Apr 20.65	Cone	1.5 long?	1978 May 4	62.8	89.00	6604	167	284	0.009

engine	[10821]	14 days	600? full	2 dia?

1978 May 4

D	Fragment	1978-40 C	[10813]	1978 Apr 22	2 days

D	Fragment	1978-40 E	[10822]	1978 May 4	14 days

D	HCMM (AEM 1)*	1978-41 A	1978 Apr 26.43	Hexagonal	0.64 long	1978 May 1.4	97.60	96.72	6979	560	641	0.006	245

[Scout D-1 S201C]	[10818]	1336 days	prism	0.7 wide	1980 Aug 30	97.66	95.47	6919	537	546	0.001	257

VDB-SLC5	1981 Dec 22	134

D	HCMM	1978-41 B	1978 Apr 26.43	Cylinder	1.50 long	1978 Apr 30.1	97.60	96.89	6987	564	653	0.006	250

Scout 4th stage	[10819]	943 days	24	0.46 dia

1980 Nov 24

*	Heat Capacity Mapping Mission (Applications Explorer Mission)

AMS 3	1978-42 A	1978 May 1.13	Irregular	6.40 long	1978 May 1.9	98.71	101.47	7206	820	835	0.001	212

[Thor DSV-2U #143]	[10820]	80 years	513	1.68 dia	2004 Jul 6.97	98.51	100.50	7160	775	789	0.001	17

VDB-SLC10W

D	AMS 3	1978-42 B	1978 May 1.13			1991 Oct 21.60	98.23	98.48	6627	239	258	0.001	155

Burner 2 stage	[10853]	4921 days

1991 Oct 21

Fragment	1978-42 C-E	3 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1004	1978-43 A	1978 May 5.65	Sphere -	5.0 long	1978 May 6.3	62.81	89.43	6626	205	290	0.006	78

R	[Soyuz 11A511U] 	[10846]	12.6 days	cylinder	2.4 dia

PLE	1978 May 18.3	5700?

D	Cosmos 1004	1978-43 B	1978 May 5.65	Cylinder	7.5 long	1978 May 5.9	62.80	89.27	6618	200	279	0.006	65

Block I 3rd stage 	[10847]	4.24 days	2500?	2.6 dia

1978 May 9.89

D	Nauka Capsule	1978-43 G	1978 May 5.65

[10852]	42 days

1978 Jun 16

D	Fragments	1978-43 C-F	4 pieces, all have decayed		For orbital information see extra pages at the end of the year

OTS 2  *	197B-44 A	1978 May 11.96	Hexagonal box	2.13 long	1978 May 12.0	27.32	633.80	24442	184	35943	0.732	179

[Delta 3914 627	[10855]	> million	865 full	1.68 wide	1980 Jun 30	0.0	1436.2	42168	35756	35819	0.0007	-

#141]	CC-LC17A	years	444 empty	2.39 high	2004 Jul 10.13	13.57	1452.48	42485	36083	36130	0.0006	76

OTS 2	1978-44 B	1978 May 11.96	Cylinder	6.4 long	1978 May 11.9	28.45	107.09	7470	180	2004	0.122	173

Delta 2nd stage	[10856]	60000 years	annulus	1.52 and	1978 May 15.3	27.93	139.69	8924	1568	3524	0.110	86

350?	2.44 dia	2004 Jul 6.91	27.94	139.83	8925	1568	3523	0.110	240

D	OTS 2	1978-44 C	1978 May 11.96	Sphere	1.32 long	1978 May 12.0	27.32	633.17	24436	182	35933	0.732	179

Star-37E PKM	[10857]	5644 days	-cone	0.94 dia

1991 Oct 23	66

*	Orbital Test Sate11ite 1aunched for ESA by NASA (OTS 1 fai1ed to enter orbit on 1977 Sep 13).	Entered synchronous orbit on 1978 May 13.

D	Cosmos 1005	1978-45 A	1978 May 12.17	Cylinder	5 long?	1978 May 16.6	81.24	97.54	7018	627	653	0.002	0

[Vostok 8A92M] 	[10860]	8069 days	2 vanes?	1.5 dia?

PLE	2000 Jun 14.91	2500?

Cosmos 1005	1978-45 B	1978 May 12.17	Cylinder	3.8 long	1978 May 15.2	81.25	97.69	7025	603	691	0.006	167

Block E 3rd stage 	[10861]	60 years	1440	2.6 dia	2004 Jul 10.18	81.20	94.05	6851	454	491	0.003	85

D	Cosmos 1006	1978-46 A	1978 May 12.46	Cylinder?	4 long?	1978 May 14.8	65.85	92.45	6773	382	408	0.002	342

[Kosmos 11K65M 	[10862]	306 days		2 dia?

53746-318]	PLE	1979 Mar 14

D	Cosmos 1006	1978-46 B	1978 May 12.46	Cylinder	7.4 long	1978 May 13.9	65.85	92.33	6767	373	405	0.002	7

2nd stage	[10863]	208 days	2200?	2.4 dia

1978 Dec 6

Navstar 2 (GPS)	1978-47 A	1978 May 13.44	Cylinder +	-	1978 May 22.0	63.13	711.30	26396	19952	20084	0.003	98

[Atlas 49F/SGS-1]	[10893]	1 million	4 vanes		2004 Jul 5.38	62.84	714.18	26467	19239	20938	0.032	27

VDB-SLC3E	years	871 full

525 empty

Navstar 2	1978-47 B	1978 May 13.44	Cone -	1.85 long?	1978 May 16.1	63.07	350.45	16466	162	20014	0.603	158

Star-37E PKM	[10894]	30 years	cylinder?	0.63 to	2004 Jul 4.96	63.86	286.21	14391	534	15492	0.520	4

163?	1.65 dia?

Fragment	1978-47 C	[29197]			2006 Jun 6.54	64.17	200.75	11358	579	9379	0.387	319

D	Cosmos 1007	1978-48 A	1978 May 16.45	Sphere-	6.5 long?	1978 May 16.7	72.83	89.69	6637	168	350	0.014	82

R	[Soyuz 11A511U] 	[10895]	12.7 days	cylinder	2.4 dia	1978 May 16.9	72.84	89.80	6643	170	359	0.014	83

PLE	1978 May 29.2	6300?

D	Cosmos 1007	1978-48 B	1978 May 16.45	Cylinder	7.5 long	1978 Ray 17.1	72.83	89.57	6631	170	336	0.013	80

Block I 3rd stage 	[10896]	4 days              2500?	2.6 dia

1978 May 20

D	Cosmos 1007	1978-48 D	1978 May 16.45	Cone	1.5 long?	1978 May 28.7	72.80	89.27	6616	158	317	0.012	53

engine	[10921]	15 days	600? full	2 dia?

1978 May 31

D	Fragment	1978-48 C	[10897]	1978 May 18	2 days

D	Fragment	1978-48 E 	[10922]	1978 Jul 3	48 days

D	Cosmos 1008	1978-49 A	1978 May 17.61	Cylinder	2 long?	1978 May 21.5	74.04	95.12	6902	499	549	0.004	332

[Kosmos 11K65M 	[10898]	967 days	paddles?	1 dia?

53798-316]	PLE	1981 Jan 8	900?

D	Cosmos 1008	1978-49 B	1978 May 17.61	Cylinder	7.4 long	1978 May 21.3	74.05	95.00	6896	488	548	0.004	334

2nd stage 	[10899]	996 days	2200?	2.4 dia

1981 Feb 6

D	Fragments	1978-49 C-F	4 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1009 *	1978-50 A	1978 May 19.02	Cylinder?	4 long?	Initial transfer orbit simil	ar to l978-50B

[Tsyklon 2]	[10904]	0.17 day?	1400	2 dia?	1978 May 19.1	65.86	108.64	7543	966	1364	0.026	41

1978 May 19.l9?

D	Cosmos 1009	1978-50 B	1978 May 19.02	Cylinder	8 long?	1978 May 19.9	65.14	97.41	7014	147	1125	0.070	57

2nd stage	[10905]	17 days	1500?	2.5 dia?

1978 Jun 5

D	Fragment	1978-50 C	[10906]	1978 Jul 17	59 days

D	Fragment	1978-50 D	[10907]	1978 May 23	4 days

*	May have passed close to Cosmos 967 (1977-116 A). Probably re-entered near 10(	N, 147(E?

D	Pioneer Venus 1 #	1978-51 A	1978 May 20.55	Cylinder	1.2 long	Solar orbit	2.3?	365 days?	0.70?	1.30?	0.30?	-

(Orbiter)	[10911]	5257.26 days	580 full	2.4 dia	1978 Dec 4.67	105	1391.4	38564	378	64645	0.833	-$

[Atlas-3D(R) AC-50	CC-LC36A	1992 Oct 9.81	370 empty		1978 Dec 6.83	105	1423.9	39160	233**	65983	0.839	-$

Centaur D-1AR 5030]

Pioneer Venus 1	1978-51 B	1978 May 20.55	Cylinder	8.6 long	Orbit similar to solar orbit of 1978-51 A

Centaur 50 stage	[10912]	Indefinite	1815	3.0 dia	heliocentric orbit

#	Pioneer Venus 1 entered Venus orbit on 1978 Dec 4.67; main thruster propellant exhausted 1992 Oct 3, transmissions ceased Oct 8, decayed in Venusian’s

atmosphere at an altitude of 128 km after fuel exhausted.

-$ Venus orbit

**	Periapsis height was reduced by manoeuvres to 149 km by 1979 Jan 1.

D	Cosmos 1010	1978-52 A	1978 May 21.32	Sphere -	5.9 long	1978 May 24.2	81.37	88.99	6602	217	230	0.001	55

R	[Soyuz 11A511U] 	[10915]	12.83 days	cylinder	2.4 dia

PLE-LC43/4	1978 Jun 5.15	5900?

D	Cosmos 1010	1978-52 B	1978 May 23.32	Cylinder	7.5 long	1978 May 23.4	81.37	88.91	6598	212	227	.0.001	16

Block I 3rd stage 	[10916]	3 days	2500?	2.6 dia

1978 May 26

D	Capsule	1978-52 C	1978 May 23.32	Ellipsoid	0.9 long	1978 Jun 5	81.3	88.41	6573	191	198	0.0005	-

[10928]	15 days	200?	1.9 dia

1978 Jun 7						-

Cosmos 1011	1978-53 A	1978 May 23.70	Cylinder	2.1 long	1978 May 24.9	82.91	104.90	7367	961	1016	0.004	286

[Kosmos 11K65M 	[10917]	1200 years	810	2.0 dia	2004 Jul 5.21	82.92	104.72	7360	954	1009	0.004	3

53768-310]	PLE

Cosmos 1011	1978-53 B	1978 May 23.70	Cylinder	7.4 long	1978 May 24.2	82.92	104.78	7361	961	1004	0.003	283

2nd stage	[10918]	600 years	2200?	2.4 dia	2004 Jul 6.74	82.91	104.57	7353	953	995	0.003	277

D	Cosmos 1012	1978-54 A	1978 May 25.61	Sphere -	5.0 long	1978 May 26.6	62.80	89.15	6612	202	265	0.005	51

R	[Soyuz 11A511U] 	[10919]	12.6 days	cylinder	2.4 dia

PLE	1978 Jun 7.2	5700?

D	Cosmos 1012	1978-54 B	1978 May 25.61	Cylinder	7.5 long	1978 May 26.1	62.80	88.90	6599	189	253	0.005	25

Block I 3rd stage 	[10920]	3 days	2500?	2.6 dia

1978 May 28

Molniya-1 40	1978-55 A	1978 Jun 2.51	Windmill	3.4 long	1978 Jun 3.1	62.85	736.26	27010	422	40842	0.748	280

[Molniya 8K78M] 	[10925]	100 years?	6 vanes	1.6 dia	1978 Jun 9.7	62.81	718.15	26567	423	39954	0.744	280

PLE		1000?		2004 Jul 5.01	63.99	717.75	26555	2549	37804	0.664	276

D	Molniya-1 40	1978-55 B	1978 Jun 2.51	Irregular	-	1978 Jun 3.0	62.85	90.85	6695	211	422	0.016	130

Block I 3rd stage 	[10926]	19 days

1978 Jun 21

D	Molniya-1 40	1978-55 C	1978 Jun 2.51	Cylinder	7.5 long	1978 Jun 3.1	62.84	90.83	6694	195	436	0.018	120

4th stage casing 	[10927]	15 days	2500?	2.6 dia

1978 Jun 17

Molniya-1 40	1978-55 E	1978 Jun 2.51	Cylinder	2.0 long	1979 Jun 30.0	63.2	732.5	26917	619	40460	0.740	-

Block L 4th stage 	[10949]	100 years?	440	2.0 dia	2004 Jul 6.11	63.88	731.00	26881	2044	38961	0.687	279

D	Molniya-1 40	1978-55D	1978 Jun 2.51

Ullage motor	[10929]	23 days

1978 Jun 25

Cosmos 1013 *	1978-56 A	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 11.5	74.02	116.40	7897	1480	1557	0.005	239

[Kosmos 11K65M 	[10930]	10000 years	40?	0.8 dia?	2004 Jul 6.22	74.03	116.33	7894	1478	1554	0.005	297

53716-321]	PLE

Cosmos 1014 *	1978-56 B	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 11.9	74.02	116.15	7885	1480	1534	0.003	234

[10931]	10000 years	40?	0.8 dia?	2004 Jul 5.75	74.03	116.08	7883	1478	1531	0.003	225

Cosmos 1015 *	1978-56 C	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 11.4	74.02	115.93	7875	1475	1519	0.003	212

[10932]	10000 years	40?	0.8 dia?	2004 Jul 4.89	74.03	115.87	7873	1473	1516	0.003	142

Cosmos 1016 *	1978-56 D	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 11.4	74.02	115.70	7865	1473	1501	0.002	186

[10933]	10000 years	40?	0.8 dia?	2004 Jul 5.76	74.03	115.63	7863	1471	1497	0.002	47

Cosmos 1017 *	1978-56 E	1978 Jun 7.91	Spheroid	1.0 long7	1978 Jun 11.5	74.02	115.49	7856	1460	1495	0.002	153

[10934]	9000 years	40?	0.8 dia?	2004 Jul 5.25	74.02	115.42	7853	1457	1491	0.002	311

Cosmos 1018 *	1978-56 F	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 10.9	74.02	115.27	7846	1444	1491	0.003	131

[10935]	9000 years	40?	0.8 dia?	2004 Jul 5.17	74.02	115.22	7843	1441	1488	0.003	228

Cosmos 1019 *	1978-56 G	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 11.5	74.02	115.06	7836	1425	1491	0.004	122

[10936]	8000 years	40?	0.8 dia?	2004 Jul 5.84	74.02	115.00	7834	1423	1488	0.004	160

Cosmos 1020 *	1978-56 H	1978 Jun 7.91	Spheroid	1.0 long?	1978 Jun 10.9	74.02	114.85	7827	1410	1487	0.005	108

[10937]	8000 years	40?	0.8 dia?	2004 Jul 4.74	74.02	114.78	7824	1407	1484	0.005	82

Cosmos 1013-1020	1978-56 J	1978 Jun 7.91	Cylinder	7.4 long	1978 Jun 10.5	74.02	117.95	7967	1486	1691	0.013	262

2nd stage	[10938]	20000 years	2200?	2.4 dia?	2004 Jul 6.93	74.02	117.88	7964	1480	1691	0.013	20

*	Strela-1M

D	Cosmos 1021	1978-57 A	1978 Jun 10.36	Sphere-	6.5 long?	1978 Jun 11.8	65.03	89.35	6621	173	313	0.011	59

R	[Soyuz 11A511U] 	[10939]	12.85 days	cylinder	2.4 dia	1978 Jun 18.4	65.03	89.46	6627	171	326	0.012	56

BAI	1978 Jun 23.21	6300?

D	Cosmos 1021	1978-57 B	1978 Jun 10.36	Cylinder	7.5 long	1978 Jun 10.5	65.04	89.29	6618	172	308	0.010	58

Block I 3rd stage 	[10940]	3 days	2000?	2.6 dia

1978 Jun 13

D	Cosmos 1021	1978-57 D	1978 Jun 10.36	Cone	1.5 long7	1978 Jun 24.3	65.02	88.72	6590	167	256	0.007	52

engine	[10964]	16 days	600? full	2 dia?

1978 Jun 26

D	Fragment	1978 57 C	[10963]	1978 Jun 25	15 days

Chalet 1 (IMEWS 8)	1978-58 A	1978 Jun 10.80	-	-	1978 Jun 11.0	26.3	633.0	24445	295	35840	0.727	180

(Vortex 1)	[10941]	>million years			1978 Jul 1.0	12.0	l446.3	42362	29929	42039	0.143	-

[Titan 3C 23C-15]	CC-LC40				2009 Jul 6.00	3.48	1438.63	42215	29828	41844	0.142	291 *

2020 Mar 26.49	8.44	1438.48	42211	29653	42013	0.146	17

Transtage 33	1978-58 B	1978 Jun 10.80	Cylinder	6 long?			Orbits similar to 1978- 58 A

[10942]	>million years	1500?	3.0 dia	No elements available

D	Titan 3C	1978-58 C	1978 Jun 10.80	Cylinder	6 long	1978 Jun 10.8	29.98	91.14	6716	152	524	0.028	125

second stage	[10943]	4 days	1900	3.0 dia

1978 Jun 14

*	No elements available; orbits from amateur observations.

D	Cosmos 1022	1978-59 A	1978 Jun 12.44	Sphere-	6.5 long?	1978 Jun 14.4	72.84	89.67	6636	171	344	0.013	77

R	[Soyuz 11A511U] 	[10944]	12.76 days	cylinder	2.4 dia	1978 Jun 22.6	72.84	89.69	6637	167	350	0.014	60

PLE	1978 Jun 25.20	6300?

D	Cosmos 1022	1978-59 B	1978 Jun 12.44	Cylinder	7.5 long	1978 Jun 12.8	72.85	89.54	6629	167	335	0.013	80

Block I 3rd stage 	[10945]	4 days	2500?	2.6 dia

1978 Jun 16

D	Cosmos 1022	1978-59 C	1978 Jun 12.44	Cone	1.5 long?	1978 Jun 24.7	72.86	89.48	6626	166	330	0.012	51

engine	[10965]	16 days	600? full	2 dia?

1978 Jun 28

D	Fragment	1978-59 D	[10966]	1978 Jun 28	16 days

D	KH 11-2 Kennan	1978-60 A	1978 Jun 14.77	Cylinder	15 long	1978 Jun 15.7	96.96	91.90	6744	223	509	0.021	159

[Titan 3D 23D-18]	[10947]	11 66 days	13300?	3.0 dia	1978 Jun 16.5	96.82	92.42	6771	276	509	0.017	155

VDB-SLC4E	1981 Aug 23	full

D	Titan 3D	1978-60 B	1978 Jun 14.77	Cylinder	6 long	1978 Jun 15.3	96.96	91.74	6736	221	495	0.020	158

2nd stage	[10948]	40 days	1900	3.0 dia

1978 Jul 24

D	S77-2(1)?	1978-60 C	[10951]	1978 Jun 18	4 days

D	S77-2(2)?	1978-60 D	[10957]	1978 Jun 18	4 days

D	S77-2(3)?	1978-60 E	[10958]	1978 Jun 18	4 days

D	S77-2(4)?	1978-60 F	[10959]	1978 Jun 18	4 days

These objects are probably Titan 3D fragments.

D	Soyuz 29*	1978-61 A	1978 Jun 15.85	Sphere-	7.5 long	1978 Jun 16.0	51.63	88.85	6599	193	248	0.004	74

2M	[Soyuz 11A511U] 	[10952]	79.64 days	cylinder	2.3 dia	1978 Jun 16.2	51.64	90.07	6659	253	309	0.004	262

R		BAI	1978 Sep 3.49	6570?		1978 Jun 22.6	51.63	91.39	6724	338	353	0.001	32

D	Soyuz 29	1978-61 B	1978 Jun 15.85	Cylinder	7.5 long	1978 Jun 16.4	51.62	88.63	6588	186	233	0.004	76

Block I 3rd stage 	[10956]	3 days	2500?	2.6 dia

1978 Jun 18

*	Soyuz 29 docked with Salyul 6 (first airlock) 1978 Jun 16.92; undocked from Salyut 6 on 1978 Sep 3, but landed with the Soyuz 31 crew.

GOES 3 *	1978-62 A	1978 Jun 16.46	Cylinder +	2.30 long	1978 Jun 16.5	23.90	649.03	24832	198	36709	0.735	178

[Delta 2914 625	[10953]	>million years	boom	1.90 dia	1978 Jun 17.1	1.78	1446.85	42375	35473	36521	0.012	164

#142]	CC-LC17B		627 full		1979 Jun 30.0	0.3	l436.1	42165	35781	35794	0	-

243 empty		2004 Jul 7.53	13.53	1436.18	42166	35763	35812	0.0006	48

2016 Jun 15.53	13.84	1436.05	42164	35769	35802	0.0004	177

2016 Jun 16.48	13.84	1438.02	42203	35807	35841	0.0004	209

2016 Jun 21.47	13.84	1443.50	42310	35908	35954	0.0005	192

2016 Jun 24.00	13.83	1443.75	42315	35929	35943	0.0002	221

2016 Jun 27.60	13.83	1446.78	42374	35981	36010	0.0003	215

2016 Jun 30.00	13.83	1449.58	42428	36027	36072	0.0005	217

Graveyard orbit	2016 Jul 7.56	13.82	1449.25	42422	36034	36053	0.0002	283

GOES 3	1978-62 B	1978 Jun 16.46	Cylinder +	6.4 long	1978 Jun 16.5	28.42	93.83	6B40	178	746	0.042	165

Delta 2nd stage	[10954]	200 years	annulus	1.52 and	1978 Jun 20.4	28.43	108.01	7520	553	1730	0.078	97

350?	2.44 dia	2004 Jul 6.16	28.43	106.80	7457	549	1608	0.071	153

D	GOES 3	1978-62 C	1978 Jun 16.46	Sphere-cone	1.32 long	1978 Jun 16.5	23.79	655.06	24988	167	37053	0.738	177

Star-37E PKM	[10955]	1891 days	66	0.94 dia

1983 Aug 20

GOES 3	1978-62 D	1978 Jun 16.46	-	-	Orbit similar to second 1978-62 A orbit

Star-37 AKM	[20801]	>million years	384 full		2004 Jul 7.80	15.15	1447.48	42387	35553	36465	0.011	226

*	Goes 3 was transferred to the National Science Foundation’s U.S. Antartic Program in the late 1990s.

In 2016 June it was send to a graveyard orbit.

Cosmos  1023	1978-63 A	1978 Jun 21.40	Cylinder	2 long?	1978 Jun 24.7	74.08	100.76	7172	783	805	0.002	356

[Kosmos 11K65M 	[10961]	120 years	paddles?	1 dia?	2004 Jul 7.57	74.07	100.30	7151	763	782	0.001	56

53716-317]	PLE		750?

Cosmos 1023	1978-63 B	1978 Jun 21.40	Cylinder	7.4 long	1978 Jun 24.7	74.08	100.63	7166	773	803	0.002	18

2nd stage	[10962]	100 years	2200?	2.4 dia	2004 Jul 6.79	74.08	100.02	7138	741	777	0.003	335

Fragment	1978-63 C	[13497]			2004 Jul 6.51	74.05	99.43	7110	721	742	0.001	86

D	Fragment	1978-63 D	[14804]	2007 Jun 10	10581 days	2004 Jul 7.17	74.00	94.63	6880	494	507	0.0009	172

2007 Jun 9.76	73.96	88.23	6566	181	193	0.001	276

L	Seasat 1	1978-64 A	1978 Jun 27.05	Cylinder +	21 long	1978 Jun 27.4	108.02	100.63	7166	776	800	0.002	263

[Atlas 23F	[10967]	200 years	4 wings	1.5 dia	2004 Jul 10.13	108.00	99.87	7131	750	754	0.0003	267

Agena D]	VDB-SLC3W		2300	11 span

Fragments	1978-64 B-W	20 pieces, 14 have decayed		For orbital information see extra pages at the end of the year

D	Soyuz 30*	1978-65 A	1978 Jun 27.65	Sphere-	7.5 long	1978 Jun 27.8	51.64	88.82	6597	194	244	0.004	64

2M	[Soyuz 11A511U] 	[10968]	7.91 days	cylinder	2.3 dia

R		BAI-LC1	1978 Jul 5.56	6570?

D	Soyuz 30	1978-65 B	1978 Jun 27.65	Cylinder	7.5 long	1978 Jun 28.4	51.64	88.53	6583	184	226	0.003	52

Block I 3rd stage 	[10969]	3 days	2500?	2.6 dia

1978 Jun 30

*	Soyuz 30 docked with Salyut 6 (second airlock) and Soyuz 29 on 1978 Jun 28.71, with one Russian and one Polish cosmonaut; 	Soyuz 30 undocked 1978 Jul 5.43

Cosmos 1024	1978-66 A	1978 Jun 28.13	Windmill +	4.2 long?	1978 Jun 30.2	62.83	724.73	26728	605	40094	0.739	318

[Molniya 8K78M] 	[10970]	100 years?	6 vanes?	1.6 dia	1978 Jul 18.2	62.76	717.41	26547	617	39721	0.736	318

PLE-LC43/3		1250?		2004 Jul 4.69	67.72	717.48	26549	3889	36451	0.613	147

D	Cosmos 1024	1978-66 B	1978 Jun 28.13	Cylinder	7.5 long	1978 Jun 28.2	62.82	92.12	6758	212	547	0.025	124

Block I 3rd stage 	[10971]	33 days	2500?	2.6 dia

1978 Jul 31

D	Cosmos 1024	1978-66 C	1978 Jun 28.13	Irregular	-	1978 Jun 28	62.9	92.42	6773	185	605	0.031

4th stage casing 	[10972]	14 days

1978 Jul 12

Cosmos 1024	1978-66 D	1978 Jun 28.13	Cylinder	2.0 long	1980 Jun 30	63.2	720.2	26615	1643	38831	0.699	-

Block L 4th stage 	[10998]	100 years?	440	2.0 dia	2004 Jul 6.14	67.85	720.35	26619	3815	36666	0.617	145

Cosmos 1024	1978-66 E	1978 Jun 28.13			2004 Jun 29.97	67.09	704.33	26223	3351	36338	0.629	143

Auxilary motor	[26974]

Cosmos 1024	1978-66 F	1978 Jun 28.13			2004 Jul 9.59	68.63	700.13	26119	4259	35221	0.593	140

Auxilary motor	[26975]

Fragment	1978-66 G	[27890]			2003 Dec 21.01	67.00	709.30	26346	3461	36474	0.627	153

1978-66 H	[32968]			2008 Jun 4.37	68.93	730.23	26862	5385	35581	0.562	132

D	Cosmos 1025	1978-67 A	1978 Jun 28.73	-	-	1978 Jul 4.4	82.49	97.84	7032	640	668	0.002	276

[Tsyklon 3]	[10973]	10482 days			2004 Jul 10.20	82.47	92.93	6796	414	422	0.0006	37

PLE	2007 Mar 10			2007 Mar 10.44	82.41	87.23	6516	131	143	0.001	255

Cosmos 1025	1978-67 B	1978 Jun 28.73	Cylinder	7.4 long	1978 Jun 30.1	82.49	97.81	7031	638	667	0.002	297

2nd stage	[10974]	60 years	2200?	2.4 dia	2004 Jul 10.97	82.48	96.95	6991	599	626	0.002	124

Comstar 1C	1978-68 A	1978 Jun 29.93?	Cylinder	6 32 long	1978 Jun 30.0	21.80	639.16	24579	550	35852	0.718	179

[Atlas SLV-3D(R)	[10975]	>million years	1520 full	2.36 dia	1978 Jul 13.0	0.08	1428.15	42008	35470	35780	0.004	-

AC-41 Centaur D-1AR	 CC-LC36B		790 empty		1979 Jun 30.0	0.0	1436.0	42166	35783	35792	0	-

5021]					2004 Jul 9.76	12.26	1451.60	42468	35993	36186	0.002	97

Comstar 1C	1978-68 B	1978 Jun 29.93?	Cylinder	8.6 long	1980 Jun 30	21.1	649.7	24849	869	36372	0.720	-

Centaur 41 stage	[10976]	6000 years	1815	3.0 dia	2004 Jul 5.40	22.10	648.02	24806	592	36263	0.719	238

Fragment	1978-68 C	[25253]			1998 Jan 8.96	21.47	640.28	24608	878	35581	0.705	108

2004 Jul 10.10	21.16	640.12	24604	831	35620	0.707	66

D	Cosmos 1026	1978-69 A	1978  Jul 2.40	-	-	1978 Jul 2.7	51.78	88.99	6606	207	248	0.003	40

R	[Soyuz 11A511U] 	[10977]	4.02  days

BAI	1978  Jul 6.42

D	Cosmos 1026	1978-69 B	1978  Jul 2.40	Cylinder	7.5  long?	1978 Jul 2.7	51.78	88.94	5603	206	244	0.003	35

Block I 3rd stage 	[10978]	5 days	2500?	2.6  dia?

1978 Jul 7

D	Progress 2*	1978-70 A	1978 Jul 7.48	Sphere-	7.9 long	1978 Jul 7.7	51.62	88.60	6586	182	234	0.004	109

[Soyuz 11A511U	[10979]	27.63 days	cylinder	2.3 dia	1978 Jul.9.2	51.63	89.98	6655	245	308	0.005	210

S15000-128]	BAI-LC31	1978 Aug 4.11	7020

D	Progress 2	1978-70 B	1978 Jul 7.48	Cylinder	7.5 long	1978 Jul 8.1	51.63	88.62	6587	182	236	0.004	88

Block I 3rd stage 	[10980]	3 days	2500?	2.6 dia

1978 Jul 10

*	Progress 2 docked with Salyut 6	(2nd airlock) - Soyuz 29 complex 1978 Jul 9.54; undocked 1978 Aug 2.21. De-orbited over Pacific Ocean two days later.

ESA-GEOS 2	1978-71 A	1978 Jul 14.45	Cylinder	1.10 long	1978 Jul 14.7	25.85	626.60	24256	214	35542	0.728	179

[Delta 2914 631	[10981]	>million years	573 full	1.62 dia	1978 Jul 18.0	0.80	1421.17	41874	35377	35614	0.003	313

#143]	CC-LC17A		273 empty		1979 Jun 30.0	0.2	1436.0	42167	35754	35815	0.001	-

2004 Jul 8.01	14.65	1449.07	42418	36014	36065	0.0006	120

D	ESA-GEOS 2	1978-71 B	1978 Jul 14.45	Cylinder	6.4 long	1978 Jul 14.5	28.73	88.41	6574	158	233	0.006	3

Delta 2nd stage	[10982]	150 days	annulus	1.52 and	1978 Jul 14.7	28.09	123.80	8232	165	3543	0.205	40

1978 Dec 11	3507	2.44 dia

D	ESA-GEOS 2	1978-71 C	1978 Jul 14.45	Sphere-	1.32 long	1978 Aug 31.6	25.42	626.82	24262	197	35571	0.729	211

Star-37E PKM	[10983]	10324 days	cone 66	0.94 dia	2004 Jul 10.90	25.64	247.97	13075	189	13203	0.498	282

2006 Oct 19			2006 Oct 19.36	25.46	88.82	6594	120	311	0.014	146

D	Molniya-1 41	1978-72 A	1978 Jul 14.63	Windmill +	3.4 long	1978 Jul 15.7	62.83	736.44	27015	607	40666	0.741	288

[Molniya 8K78M] 	[10984]	4957 days	6 vanes	1.6 dia	1978 Jul 24.8	62.83	718.15	26566	606	39769	0.737	288

PLE	1992 Feb 8	1000?		1992 Feb 7.94	61.76	98.23	7053	75	1273	0.085	267

D	Molniya-1 41	1978-72 B	1978 Jul 14.63	Cylinder	7.5 long	1978 Jul 16.2	62.84	92.66	6784	215	597	0.028	1 21

Block I 3rd stage 	[10985]	47 days	2500?	2.6 dia

1978 Aug 30

D	Molniya-1 41	1978-72 C	1978 Jul 14.63	Irregular	-	1978 Jul 16.2	62.84	92.74	6788	204	616	0.030	116

4th stage casing 	[10986]	40 days

1978 Aug 23

D	Molniya-1 41	1978-72 D	1978 Jul 14.63	Cylinder	2.0 long	1980 Jun 30	64.3	732.7	26923	646	40443	0.739	-

Block L 4th stage 	[11073]	5025 days	440	2.0 dia	1992 Mar 14.37	61.81	535.97	21857	78	30879	0.705	259

1992 Apr 16

Raduga 4	1978-73 A	1978 Jul 18.92	-	-	1978 Jul 19.2	0.50	1477.84	42980	36473	36730	0.003	62

[Proton 8K82K 	[10987]	>million	2000?		2004 Jul 6.98	14.71	1434.98	42143	35711	35819	0.001	154

292-02/11S86 10L]	BAI	years

D	Raduga 4	1978-73 B	1978 Jul 18.92	Cylinder	6.5 long?	1978 Jul 19.2	51.63	88.06	6559	170	192	0.002	281

third stage	[10988]	2 days		4 dia

1978 Jul 20

D	Raduga 4	1978-73 C	1978 Jul 18.92	Irregular	-	1978 Jul 19.2	51.62	88.00	6556	161	195	0.003	183

4th stage casing 	[10989]	1 day

1978 Jul 19

D	Raduga 4	1978-73 D	1978 Jul 18.92

Ullage motor	[11074]	218 days

1979 Feb 21

D	Raduga 4	1978-73 E	1978 Jul 18.92

Ullage motor	[11077]	360 days

1979 Jul 13

Raduga 4	1978-73 F	1978 Jul 18.92	Cylinder	5.5 long	1980 Sep 30.7	1.23	1475.86	42941	36497	36628	0.0015	166

Block D 4th stage	[11941]	> million	17300 full	4.0 dia	2004 Jul 7.34	15.57	1475.87	42940	36503	36619	0.0014	331

years

Cosmos 1027	1978-74 A	1978 Jul 27.20	Cylinder	1.3 long?	1978 Aug 17.4	82.94	104.82	7363	966	1004	0.003	226

[Kosmos 11K65M 	[10991]	1200 years	700?	1.9 dia?	2004 Jul 6.53	82.94	104.63	7356	957	998	0.003	115

53716-313]	PLE

Cosmos 1027	1978-74 B	1978 Jul 27.20	Cylinder	7.4 long	1978 Aug 2.9	82.93	104.71	7358	968	991	0.002	273

2nd stage	[10992]	600 years	2200?	2.4 dia	2004 Jul 7.07	82.93	104.53	7351	957	988	0.002	56

D	SDS 5 *	1978-75 A	1978 Aug 5.27	Cylinder	-	1978 Aug 31	62.5	697.1	26062	315	39053	0.743	-

[Titan 34B-7 3B-57	[10993]	8223 days

Ascent Agena D]	VDB-SLC4W	2001 Feb 8

D	SDS 5	1978-75 B	1978 Aug 5.27	Cylinder	6 long?	1978 Aug 21	63.3	700.2	26120	310	39175	0.744	270*

Agena D stage	[10994]	8725 days	700?	1.5 dia	2002 Jun 25.11	62.69	89.28	6618	157	321	0.012	125

2002 Jun 25

*	USAF payload launched from Vandenberg, California.  Orbit and launch time unconfirmed.

D	Cosmos 1028	1978-76 A	1978 Aug 5.63	Sphere-	7 long?	1978 Aug 6.2	67.14	88.66	6587	170	247	0.006	78

R	[Soyuz 11A511U] 	[10995]	29.5 days	cylinder	2.4 dia	1978 Aug 7.8	67.14	89.54	6631	168	337	0.013	65

PLE-LC43/3	1978 Sep 4.1	6700?

D	Cosmos 1028	1978-76 B	1978 Aug 5.63	Cylinder	7.5 long	1978 Aug 6.2	67.14	88.52	6580	169	234	0.005	87

Block I 3rd stage 	[10996]	2 days	2500?	2.6 dia

1978 Aug 7

D	Cosmos 1028	1978-76 D	1978 Aug 5.63	Cone	1.5 long?	1978 Sep 4.2	67.13	88.88	6598	149	290	0.011	69

engine	[11014]	30 days	600? full	2 dia?

1978 Sep 4

D	Fragment	1978-76 C	[10997]	1978 Aug 8	3 days

D	Progress 3 * 	1978-77 A	1978 Aug 7.94	Sphere-	7.9 long	1978 Aug 8.2	51.64	88.66	6589	190	232	0.003	77

[Soyuz 11A511U] 	[10999]	15.84 days	cylinder	2.3 dia	1978 Aug 9.6	51.63	89.36	6624	243	249	0.0004	334

BAI-LC31	1978 Aug 23.78	7020		1978 Aug 21.7	51.62	91.35	6722	335	352	0.001	256

D	Progress 3 	1978-77 B	1978 Aug 7.94	Cylinder	7.5 long	1978 Aug 8.1	51.64	88.55	6584	185	226	0.003	77

Block I 3rd stage 	[11000]	2 days	2500?	2.6 dia

1978 Aug 9

*	Progress 3 docked with Salyut 6 (2nd airlock) - Soyuz 29 complex on 1978 Aug 10.00; undocked 1978 Aug 21 and later de-orbited over Pacifi	c Ocean.

D	Pioneer Venus 2	1978-78 A	1978 Aug 8.31	Cylinder	2.4 dia	Solar orbit	2.3?	316 days?	0.70?	1.11?	0.23?	-

multiprobe bus	[11001]	123.54 days	309*	1.2 long*	Decayed in Venus atmosphere near 33( S, 70( W

[Atlas SLV 3D(R)	CC-LC36A	1978 Dec 9.85

AC-51 Centaur D-1AR 5031D]

D	Pioneer Venus 2	1978-78 B	1978 Aug 8.31	Cylinder	20 long	1978 Aug 8.3	28.67	87.57	6536?	150?	165?	0.001?	-

Atlas stage	[11002]	< 0.7 day	3400	3.0 dia

1978 Aug 8

Pioneer Venus 2	1978-78 C	1978 Aug 8.31	Cylinder	8.6 long	Solar orbit similar to 1978-78 A

Centaur 51 stage	[11003]	indefinate	1815	3.0 dia	heliocentric orbit

D	Pioneer Venus 2	1978-78 D	1978 Aug 8.31	Sphere + cone	1.5 dia	Ejected from Bus 1978 Nov 16.11

Large probe 	[12103]	123.51 days	316		Venus landing 1978 Dec 9 at 19:43 near 0( S, 43( W

(Sounder)		1978 Dec 9.82

D	Pioneer Venus 2	1978-78 E	1978 Aug 8.31	Sphere + cone	0.8 dia	Ejected from Bus 1978 Nov 20.55

Small probe 1	[12104]	123.51 days	93		Venus landing 1978 Dec 9 at 19:46 near 75( N, 20( E

(North)		1978 Dec 9.82

D	Pioneer Venus 2	1978-78 F	1978 Aug 8.31	Sphere + cone	0.8 dia	Ejected from Bus 1978 Nov 20.55

Small probe 2	[12105]	123.51 days	93		Venus landing 1978 Dec 9 at 19:51 near 26( S, 45( W

(Day)		1978 Dec 9.82			Transmitted for over an hour after impact

D	Pioneer Venus 2	1978-78 G	1978 Aug 8.31	Sphere + cone	0.8 dia	Ejected from Bus 1978 Nov 20.55

Small probe 3	[12106]	123.51 days	93		Venus landing 1978 Dec 9 at 19:55 near 27( S, 43( E

(Night)		1978 Dec 9.82

ISEE 3 (ICE)*	1978-79 A	1978 Aug 12.63	Cylinder	1.61 long	1978 Aug 12.7	28.89	73702	582300	180	1151664	0.989	320

[Delta 2914 633	[11004]	Indefinite	469 full	1.73 dia	Solar orbit	0.0	359 days		0.973	1.006	0.017	-

#144]	CC-LC17B				1990 Jan	0.1	355 days		0.93	1.03	-	-

D	ISEE 3	1978-79 B	1978 Aug 12.63	Cylinder	6.4 long	1978 Aug 13.9	28.73	100.86	7184	176	1436	0.088	327

Delta 2nd stage	[11005]	72 days	+ annulus	1.52 and

1978 Oct 23	350?	2.44 dia

ISEE 3	1978-79 C	1978 Aug 12.63			Initial elements not available

Delta 3rd stage	[11006]

ISEE 3	1978-79 D	1978 Aug 12.63	Sphere	1.32 long		Orbit similar to 1978-79 A transfer orbit.

Star-37E stage	[13413]	Indefinite	- cone	0.94 dia	No elements available

66

*	Entered heliocentric orbit - a 'halo'orbit around the Sun-Earth/Moon libration point, at distance of 1.6 million km from Earth on Earth-Sun line and maintained location by use of microthrusters. During early Oct 1982, manoeuvred from this 'dayside'libration point, back across the Moon's orbit (1982 Oct 16), and out to a 'nightside'apogee of about 1.6 million km on 1982 Dc 22. Several manoeuvres in 1983 led to close Moon passages and finally on 1983 Dec 22.78 to a 119.4 km 'slingshot pass towards the comet Giacobini-Zinner and name changed to International Cometary Explorer. It passed through the tail of the comet, 7800 km from its nuclues on 1985 Sep 11.46 and made observations of comet Halley from 35 million km on 1986 Mar 22. ICE may return to the Earth-Moon system in August 2014.

D	Molniya-1 42 	1978-80 A	1978 Aug 22.99	Windmill	3.4 long	1978 Aug 23.6	62.87	735.68	26996	443	40793	0.747	280

[Molniya 8K78M] 	[11007]	13503 days	+6 vanes	1.6 dia	1978 Aug 29.7	62.83	718.23	26568	464	39915	0.743	280

PLE	2015 Aug 11	1000?		2004 Jul 5.30	64.62	622.70	24155	1273	34280	0.683	281

2015 Aug 11.35	62.29	94.70	6883	72	936	0.063	264

D	Molniya-1 42	1978-80 B	1978 Aug 22.99	Cylinder	7.5 long	1978 Aug 23.9	62.81	90.95	6700	190	454	0.020	114

Block I 3rd stage 	[11008]	24 days	2500?	2.6 dia

1978 Sep 15

D	Molniya-1 42	1978-80 C	1978 Aug 22.99	Irregular	-	1978 Aug 24.5	62.82	91.01	6703	211	439	0.017	124

4th stage casing 	[11009]	15 days

1978 Sep 6

D	Molniya-1 42	1978-80 D	1978 Aug 22.99	Cylinder	2.0 long	1980 Jun 30	63.1	732.4	26913	1321	39749	0.714	-

Block ML 4th stage	[11075]	6889 days	440	2.0  dia

1997 Jul 2

D	Soyuz 31*	1978-81 A	1978 Aug 26.62	Sphere-	7.5 long	1978 Aug 26.8	51.62	88.80	6596	193	243	0.004	62

2M	[Soyuz 11A511U] 	[11010]	67.84 days	cylinder	2.3 dia	1978 Aug 27.1	51.63	90.23	6667	256	322	0.005	281

R		BAI-LC1	1978 Nov 2.46	6570?		1978 Aug 28.4	51.63	91.40	6725	339	354	0.001	306

D	Soyuz 31	1978-81 B	1978 Aug 26.62	Cylinder	7.5 long	1978 Aug 27.1	51.62	88.64	6588	191	229	0.003	57

Block I 3rd stage 	[11011]	2 days	2500?	2.6 dia

1978 Aug 28

*	Soyuz 31 docked with Salyut 6 (2nd airlock) and Soyuz 29 on 1978 Aug 27.69, with one Russian and one East German cosmonaut. The crew returned to

Earth in Soyuz 29, undocking 1978 Sep 3. Soyuz 31 (piloted by Soyuz 29 crew) undocked from 2nd airlock and re-docked with first 	airlock 1978 Sep 7.

Soyuz 31 finally undocked from Salyut 6 on 1978 Nov 2.32, landing the Soyuz 29 crew with a duration record for manned spaceflight of 139.61 days.

D	Cosmos 1029	1978-82 A	1978 Aug 29.63	Sphere-	6.5 long?	1978 Aug 30.7	62.81	89.57	6633	179	330	0.011	76

R	[Soyuz 11A511U] 	[11012]	9.68 days	cylinder	2.4 dia	1978 Aug 31.2	62.81	89.33	6621	171	314	0.011	63

PLE	1978 Sep 8.31	6300?

D	Cosmos 1029	1978-82 B	1978 Aug 29.63	Cylinder	7.5 long	1978 Aug 31.0	62.80	89.21	6615	173	300	0.010	72

Block I 3rd stage 	[11013]	5 days	2500?	2.6 dia

1978 Sep 3

D	Cosmos 1029	1978-82 C	1978 Aug 29.63	Cone	1.5 long?	1978 Sep 8.1	62.81	89.46	6628	168	332	0.012	70

P	engine **	[11018]	13.07 days	600? full	2 dia?

1978 Sep 11.70

D	Fragment	1978-82 D	[11019]	1978 Sep 10	12 days

**	A 20kg, 0.6m piece	was picked up near Garnal-sur-Engievre (Allier), France

D	Cosmos 1030	1978-83 A	1978 Sep 6.13	Windmill +	4.2 long?	1978 Sep 9.2	62.80	725.64	26749	613	40129	0.739	318

[Molniya 8K78M] 	[11015]	 9477 days	6 vanes?	1.6 dia	1978 Sep 19.2	62.80	719.16	26591	654	39771	0.735	318

PLE-LC43/4	2004 Aug 17	1250?		2004 Jun 28.00	62.18	503.05	20953	104	29044	0.691	200

D	Cosmos 1030	1978-83 B	1978 Sep 6.13	Cylinder	7.5 long	1978 Sep 6.2	62.79	92.51	6777	213	585	0.027	121

Block I 3rd stage 	[11016]	32 days	2500?	2.6 dia

1978 Oct 8

D	Cosmos 1030	1978-83 C	1978 Sep 6.13	Irregular	-	1978 Sep 6.4	62.87	92.48	6776	173	622	0.033	119

4th stage casing 	[11017]	15 days

1978 Sep 21

Cosmos 1030	1978-83 D	1978 Sep 6.13	Cylinder	2.0 long	1978 Oct 1.3	62.97	723.36	26693	605	40025	0.738	318

Block L 4th stage 	[11076]	25 years	440	2.0 dia	2004 Jul 5.53	66.34	723.25	26690	2717	37906	0.659	164

Fragments	1978-83 E-T	14 pieces,  2 have decayed		For orbital information see extra pages at the end of the year

Venus 11	1978-84 A	1978 Sep 9.15	Cylinder +	2.3 dia	Solar orbit	2.3?	284 days		0.69	1.01	0.19	-

Transit module	[11020]	Indefinate	2 panels	2.7 long	Passed 35000 km from Venus on 1978 Dec 25.

[Proton 8K82K 	BAI-LC81L		2380? Empty	5.7 span	heliocentric orbit

296-01/11S824M 3L]

D	Venus 11	1978-84 B	1978 Sep 9.15	Irregular	-	1978 Sep 9.3	51.55	88.19	6566	170	205	0.003	0

4th stage casing 	[11021]	1 day

1978 Sep 10

D	Venus 11	1978-84 C	1978 Sep 9.15	Sphere-	2.4 dia	Attached to 1978-84 A until 1978 Dec 23 and ejected onto inpact path

Lander	[12027]	106.99 days	annulus	sphere	Soft-landed 1978 Dec 25 at 03:24 at 14(S, 299(. Surface transmissions

1978 Dec 25.14	1560?		lasted 95 min. Venus 11 and 12 landers are 800 km apart.

Venus 11	1978-84 E	1978 sep 9.15	Cylinder	3.9 long?

Proton 4th stage	[NNA]	Indefinate	1900?	3.9 dia

D	Cosmos 1031	1978-85 A	1978 Sep 9.63	Sphere-	6.5 long?	1978 Sep 10.2	62.82	89.59	6634	182	329	0.011	82

R	[Soyuz 11A511U] 	[11022]	12.60 days	cylinder	2.4 dia	1978 Sep 11.2	62.82	89.33	6621	171	314	0.011	83

PLE	1978 Sep 22.23	6300?

D	Cosmos 1031	1978-85 B	1978 Sep 9.63	Cylinder	7.5 long	1978 Sep 10.1	62.81	89.47	6628	178	321	0.011	80

Block I 3rd stage 	[11023]	5 days	2500?	2.6 dia

1978 Sep 14

D	Cosmos 1031	1978-85 D	1978 Sep 9.63	Cone	1.5 long?	1978 Sep 22.1	62.82	89.12	6610	161	303	0.011	74

engine	[11031]	15 days	600 full	2 dia?

1978 Sep 24

D	Fragment	1978-85 C	[11024]	1979 Apr 17	220 days

Venus 12	1978-86 A	1978 Sep 14.11	Cylinder +	2.3 dia	Solar orbit	2.3?	284 days		0.69	1.01	0.19	-

Transit module	[11025]	Indefinate	2 panels	2.7 long	Passed 35000 km from Venus on 1978 Dec 25.

[Proton 8K82K 	BAI-LC81P		2380? Empty	5.7 span	Observed Comet Bradfield 1980 Feb 13 at 190.373.790 km from Earth

296-02/11S824M 4L]					heliocentric orbit

D	Venus 12	1978-86 B	1978 Sep 14.11	Irregular	-	1978 Sep 14.3	51. 51	88.1P-	6564	164	207	0.003	0

4th stage casing 	[11026]	1 day

1978 Sep l5

D	Venus 12	1978-86 C	1978 Sep 14.11	Sphere-	2.4 dia	Attached to 1978-86 A until 1978 Dec 19 and ejected onto inpact path

Lander	[12028]	98.03 days	annulus	sphere	Soft-landed 1978 Dec 21 at 03:30 at 7(S, 294(. Surface transmissions

1978 Dec 21.14	1560?		lasted 110 min. Venus 11 and 12 landers are 800 km apart.

Venus 12	1978-86 E	1978 Sep 14.11	Cylinder	3.9 long?

Proton 4th stage	[NNA]	Indefinate	1900?	3.9 dia

D	Jikiken (Exos B)	l978-87 A	1978 Sep 16.21	12-sided	-	1978 Sep 16.4	31.09	532.82	21772	230	30558	0.697	-

[Mu-3H M-3H-3]	[11027]	14461 days	polygon		2004 Jul 8.68	31.33	315.78	15361	269	17697	0.567	23

KAG-M	2018 Apr 23	70		2018 Apr 22.46	30.98	88.17	6562	115	252	0.010	6

Jikiken	1978-87 B	1978 Sep 16.21	Cylinder?		1979 Jan 1.0	31.1	517.9	21363	215	29754	0.691	-

rocket	[11028]	20 years			2004 Jul 10.93	31.29	257.15	13396	266	13767	0.504	214

Fragment	1978-87 C	[27731]			2004 Mar 9.79	31.36	265.03	13668	288	14291	0.512	241

D	Cosmos 1032	1978-88 A	1978 Sep 19.34	Sphere-	5.9 long	1978 Sep 19.9	81.34	88.93	5599	215	226	O.0O1	59

R	[Soyuz 11A511U] 	[11029]	12.83 days	cylinder	2.4 dia

PLE	1978 Oct 2.17	5900?

D	Cosmos 1032	1978-88 B	1978 Sep 19.34	Cylinder	7.5 long	1978 Sep 19.9	81.35	88.73	6589	204	217	0.001	329

Block I 3rd stage 	[11030]	3 days	2500?	2.6 dia

1978 Sep 22

D	Cosmos 1032	1978-88 D	1978 Sep 19.34

Nauka Capsule	[11038]	14 days

1978 Oct 3

D	Fragment 	1978-88 C	[11037]	1978 Oct 2	13 days

D	Cosmos 1033 	1978-89 A	1978 Oct 3.46	Sphere-	5.9 long	1978 Oct 6.4	81.37	88.95	6600	212	231	0.001	102

R	[Soyuz 11A511U] 	[11039]	12.84 days	cylinder	2.4 dia

PLE-LC43/3	1978 Oct 16.30	5900?

D	Cosmos 1033 	1978-89 B	1978 Oct 3.46	Cylinder	7.5 long	1978 Oct 3.8	81.37	88.92	6599	206	235	0.002	118

Block I 3rd stage 	[11041]	3 days	2500?	2.6 dia

1978 Oct 6

D	Capsule 	1978-89 C	1978 Oct 3.46	Ellipsoid	0.9 long	1978 Oct 15.3	81.36	88.43	6574	189	202	0.001	64

[11063]	14 days	200?	1.9 dia

1978 Oct 17

D	Progress 4*	1978-90 A	1978 Oct 3.96	Sphere-	7.9 1ong	1978 Oct 4.2	51.65	88.75	6594	185	247	0.005	98

[Soyuz 11A511U	[11040]	22.74 days	cylinder	2.3 dia	1978 Oct 7.5	51.64	91.19	6714	325	347	0.002	81

Ye15000-152]	BAI-LC1	1978 Oct 26.70	7020		1978 Oct 21.8	51.64	91.68	6739	359	362	0.0002	338

D	Progress 4	1978-90 B	1978 Oct 3.96	Cylinder	7.5 long	1978 Oct 4.1	51.65	88.66	6590	184	239	0.004	97

Block I 3rd stage 	[11043]	2 days	2500?	2.6 dia

1978 Oct 5

*	Progress 4 docked with Salyut 6 (2nd air1ock)-Soyuz 31 comp1ex on 1978 Oct 6.04; undocked 1978 Oct 24.55 and 1ater de-orbited over Pacific Ocean.

Cosmos 1034 *	1978-91 A	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 4.7	74.03	114.97	7832	1423	1484	0.004	110

[Kosmos 11K65M 	[11042]	8000 years	40?	0.8 dia?	2004 Jul 5.28	74.03	114.90	7830	1421	1481	0.004	285

53782-429]	PLE

Cosmos 1035 *	1978-91 B	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 8.8	74.03	114.74	7822	1405	1482	0.005	90

[11044]	7000 years	40?	0.8 dia?	2004 Jul 4.95	74.04	114.68	7819	1402	1479	0.005	207

Cosmos 1036 *	1978-91 C	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 4.7	74.04	115.19	7842	1443	1484	0.003	114

[11045]	9000 years	40?	0.8 dia?	2004 Jul 5.46	74.03	115.12	7839	1442	1480	0.002	347

Cosmos 1037 *	1978-91 D	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 8.9	74.03	115.41	7852	1463	1484	0.001	123

[11046]	9000 years	40?	0.8 dia?	2004 Jul 5.20	74.03	115.35	7850	1461	1481	0.001	73

Cosmos 1038 *	1978-91 E	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 8.9	74.03	115.64	7862	1480	1488	0.001	202

[11047]	10000 years	40?	0.8 dia?	2004 Jul 6.43	74.03	115.58	7860	1476	1486	0.0006	216

Cosmos 1039 *	1978-91 F	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 8.9	74.03	116.38	7896	1481	1554	0.005	252

[11048]	10000 years	40?	0.8 dia?	2004 Jul 6.29	74.03	116.32	7893	1478	1551	0.005	111

Cosmos 1040 *	1978-91 G	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 8.9	74.03	116.11	7883	1481	1529	0.003	257

[11049]	10000 years	40?	0.8 dia?	2004 Jul 6.52	74.03	116.05	7881	1479	1527	0.003	41

Cosmos 1041 *	1978-91 H	1978 Oct 4.16	Spheroid	1.0 long?	1978 Oct 7.8	74.03	115.88	7873	1480	1510	0.002	235

[11050]	10000 years	40?	0.8 dia?	2004 Jul 5.52	74.03	115.82	7871	1477	1508	0.002	315

Cosmos 1034-1041	1978-91 J	1978 Oct 4.16	Cylinder	7.4 long	1978 Oct 8.9	74.04	118.06	7972	1484	1703	0.014	266

2nd stage	[11051]	20000 years	2200?	2.4 dia	2004 Jul 6.94	74.04	117.98	7969	1481	1699	0.014	206

*	Strela-1M

D	Cosmos 1042	1978-92 A	1978 Oct 6.65	Sphere-	6.5 long?	1978 Oct 8.9	62.80	89.26	6617	179	299	0.009	72

R	[Soyuz 11A511U] 	[11052]	12.64 days	cylinder	2.4 dia

PLE	1978 Oct 19.29	6300?

D	Cosmos 1042	1978-92 B	1978 Oct 6.65	Cylinder	7.5 long	1978 Oct 7.7	62.79	88.99	6604	174	277	0.008	67

Block I 3rd stage 	[11053]	4 days	2500?	2.6 dia

1978 Oct 10

D	Cosmos 1042	1978-92 C	1978 Oct 6.65	Cone	1.5 long?	1978 Oct 19	62.8	89.24	6616	171	304	0.010	-

engine?	[11070]	15 days	600? full	2 dia?

1978 Oct 21

D	Fragment	1978-92 D	[11071]	1978 Oct 21	15 days

Naystar 3	1978-93 A	1978 Oct 7.02	Cylinder +	-	1978 Oct 17.1	62.81	722.61	26677	20285	20312	0.0005	127

(GPS)	[11054]	1 million	4 vanes		2004 Jul 4.94	62.49	744.17	27202	20653	20995	0.006	202

[Atlas 47F/SGS-1]	VDB-SLC3E	years	871 full

525 empty

D	Navstar 3	1978-93 B	1978 Oct 7.02	Cone-	1.85 long?	1978 Oct 7.4	62.95	350.79	16477	158	20040	0.603	159

Star-37E PKM	[11078]	4827 days	cylinder?	0.63 to	1991 Dec 24.94	62.82	86.98	6503	85	164	0.006	265

1991 Dec 25	163?	1.65 dia?

D	Cosmos 1043 **	1978-94 A	1978 Oct 10.82	Cylinder +	5 long?	1978 Oct 12.9	81.20	97.31	7007	622	635	0.001	301

[Vostok 8A92M] 	[11055]	7081 days	2 vanes?	1.5 dia?

PLE	1998 Feb 28	2500?

D	Cosmos 1043	1978-94 B	1978 Oct 10.82	Cylinder	3.8 long	1978 Oct 14.5	81.21	97.38	7010	579	685	0.008	178

Block E 3rd stage 	[11056]	8503 days	1440	2.6 dia

2002 Jan 20

D	Fragment	1978-94 C	[22536]	1993 Mar 11	5261 days	1993 Feb 23.73	81.17	93.37	6814	438	441	0.0008	206

**	No other satellite of this type has experienced an anomalous event. The piece was cataloged on 28 Feb 93 and decayed on 11 Mar 93. Given prior cataloguing practices, other spacecraft could have experienced similar events which went unrecorded.

Molniya-3 10	1978-95 A	1978 Oct 13.22	Windmill +	4.2 long?	1978 Oct 13.8	62.79	736.21	27009	432	40829	0.748	280

[Molniya 8K78M] 	[11057]	25 years*	6 vanes	1.6 dia	1978 Oct 24.9	62.82	717.65	26524	424	39928	0.744	280

PLE-LC43/3		1500?		2004 Jul 5.58	63.98	614.92	23954	1282	33868	0.680	276

D	Molniya-3 10	1978-95 B	1978 Oct 13.22	Cylinder	7.5 long	1978 Oct 14.5	62.82	90.97	6701	213	433	0.016	127

Block I 3rd stage 	[11058]	15 days	2500?	2.6 dia

1978 Oct 28

D	Molniya-3 10	1978-95 C	1978 Oct 13.22	Irregular	-	1978 Oct 14.5	62.79	90.47	6677	175	422	0.019	114

4th stage casing 	[11059]	7 days

1978 Oct 20

Molniya-3 10	1978-95 E	1978 Oct 13.22	Cylinder	2.0 long	1979 Jun 30.0	63.2	734.5	26967	397	40781	0.749	-

Block L 4th stage 	[11079]	30 years*	440	2.0 dia	2004 Jul 4.64	63.76	648.44	24824	1435	35456	0.685	273

D	Molniya-3 10	1978-95 D	1978 Oct 13.22

Ullage motor	[11064]	18 days

1978 Oct 31

*	Decay possible in 1994 when perigee falls below 200 km

Tiros 11	1978-96 A	1978 Oct 13.47	Cylinder	3.71 long	1978 Oct 16.7	98.91	102.12	7236	850	866	0.001	256

[Atlas 29F	[11060]	500 years	734	1.88 dia	2004 Jul 6.92	98.67	101.60	7213	826	842	0.001	138

Star-37S-ISS]	VDB-SLC3W

Fragments	1978-96 B-H	7 pieces, 5 have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1044	1978-97 A	1978 Oct 17.63	Sphere-	5.0 long	1978 Oct 18.4	62.82	89.46	6627	203	295	0.007	69

R	[Soyuz 11A511U] 	[11065]	12.65 days	cylinder	2.4 dia

PLE	1978 Oct 30.28	5700?

D	Cosmos 1044	1978-97 B	1978 Oct 17.63	Cylinder	7.5 long	1978 Oct 18.4	62.82	89.30	6619	211	271	0.005	78

Block I 3rd stage 	[11066]	5 days	2500?	2.6 dia

1978 Oct 22

D	Fragment	1978-97 C	[11067]	1978 Oct 21	4 days

D	Fragment	1978-97 D	[11068]	1978 Oct 21	4 days

D	Fragment	1978-97 E	[11069]	1978 Oct 21	4 days

Nimbus 7	1978-98 A	1978 Oct 24.34	Conical	3 long	l978 Oct 25.0	99.29	104.08	7327	943	953	0.0007	240

[Delta 2910 630	[11080]	1000 years	skeleton?	2 dia	2004 Jul 11.32	99.10	104.03	7328	943	955	0.0008	316

#145]	VDB-SLC2W		832?

Nimbus 7	1978-98 B	1978 Oct 24.34	Cylinder +	6.4 long	1978 Oct 26.3	99.28	104.08	7327	943	953	0.0007	252

Delta 2nd stage*	[11081]	500 years	annulus	1.52 and	2004 Jul 6.85	99.36	103.95	7324	924	966	0.003	209

350?	2.44 dia

D	Fragment	1978-98 C	[18605]	1986 Feb 22	2678 days

1978-98 D	[36295]

*	Carried CAME0 - Chemical1y Active Materials Ejected in Orbit (Barium released 1978 Oct 29, and Lithium released 1978 Nov 6). Weight 89 kg.

D	Intercosmos 18	1978-99 A	1978 Oct 24.79	Octagonal	1.8 long?	1978 Oct 25.5	82.97	96.40	6963	406	764	0.026	166

(Magic)**	[11082]	875 days	ellipsoid	1.5 dia?

[Kosmos 11K65M 	PLE-LC132/1	1981 Mar 17	550?

65055-106]

D	Intercosmos 18	1978-99 B	1978 Oct 24.79	Cylinder	7.4 long	1978 Oct 29.1	82.96	96.30	6958	403	757	0.025	153

2nd stage	[11083]	932 days	2200?	2.4 dia

1981 May 13

D	Magion  1 #	1978-99 C	1978 Oct 24.79	Prism	0.30 x	1978 Nov 17.5	82.95	96.36	6961	404	762	0.026	89

[11110]	1053 days	15	0.30 x

1981 Sap 11		0.15

#	Czechoslovak MAGnetospheric and 10Nospheric satellite, ejected from Intercosmos 18 on 1978 Nov 14.74

**	Magnetospheric Intercosmos.

Cosmos 1045	1978-100 A	1978 Oct 26.29	Cylinder +	5 long?	1978 Oct 29.1	82.55	120.41	8078	1689	1710	0.001	173

[Tsyklon 3]	[11084]	15000 years	2 wings	1.5 dia?	2004 Jul 7.18	82.55	120.32	8074	1685	1705	0.001	146

PLE-LC32		2670

Radio 1	1978-100 B	1978 Oct 26.29	Cylinder +	0.39 long	1978 Oct 29.1	82.55	120.39	8077	1688	1709	0.001	183

[11085]	15000 years	bar    40	0.42 dia	2004 Jul 5.21	82.55	120.33	8075	1685	1707	0.001	153

Radio 2	1978-100 C	1978 Oct 26.29	Cylinder +	0.39 long	1978 Oct 28.6	82.55	120.40	8077	1689	1709	0.001	181

[11086]	15000 years	bar    40	0.42 dia	2004 Jul 6.21	82.55	120.32	8074	1685	1706	0.001	147

Cosmos 1045	1978-100 D	1978 Oct 26.29	Cylinder	7.4 long	1978 Oct 30.1	82.55	120.35	8075	1688	1705	0.001	175

2nd stage	[11087]	15000 years	2200?	2.4 dia	2004 Jul 4.72	82.55	120.28	8072	1685	1702	0.001	138

Fragments	1978-10O E-AX	 42 pieces, 9 have decayed		For orbital information see extra pages at the end of the year

D	Prognoz 7	1978-101 A	1978 Oct 30.23	Spheroid	1.8 dia?	1978 Oct 30.2	64.91	5881.1	107928	472	202627	0.937	290

[Molniya 8K78M/SOL]	[11088]	713 days	+ 4 vanes

BAI	1980 Oct 22	915?

D	Prognoz 7	1978-101 B	1978 Oct 30.23	Cylinder	7.5 long	1978 Nov 4.9	65.02	90.79	6692	206	422	0.016	59

Block I 3rd stage 	[11090]	18 days	25007	2.6 dia

1978 Nov 17

D	Prognoz 7	1978-101 C	1978 Oct 30.23	Irregular	-	1978 Nov 4.9	64.99	91.13	6709	233	429	0.015	63

4th stage casing 	[11089]	26 days

1978 Nov 25

D	Prognoz 7	1978-101 D	1978 Oct 30.23	Cylinder	2.0 long			Orbit similar to 1978-101 A

rocket	[NNA]	747 days?	440	2.0 dia

1980 Nov 15?

D	Cosmos 1046	1978-102 A	1978 Nov 1.50	Sphere-	5.9 long	1978 Nov 5.2	72.86	89.77	6541	202	324	0.009	62

R	[Soyuz 11A511U] 	[11098]	11.78 days	cylinder	2.4 dia

PLE	1978 Nov 13.28	5900?

D	Cosmos 1046	1978-102 B	1978 Nov 1.50	Cylinder	7.5 long	1978 Nov 5.4	72.86	88.83	6595	180	253	0.006	50

Block I 3rd stage 	[11099]	6 days	2500?	2.6 dia

1978 Nov 7

D	Capsule	1978-102 D	1978 Nov 1.50	Ellipsoid	0.9 long	1978 Nov 13	72.9	91.43	6724	209	482	0.020	-

[11104]	14 days	2007	1.9 dia

1978 Nov 15

D	Fragment	1978-102 C	[11103]	1978 Nov 14	13 days

D	Fragment	1978-102 E	[11105]	1978 Nov 15	14 days

D	Fragment	1978-102 F	[11106]	1978 Nov 14	13 days

D	Fragment	1978-102 G	[11107]	1978 Nov 14	13 days

D	HEAO 2	1978-103 A	1978 Nov 13.23	Hexagonal	5.8 long	1978 Nov 17.2	23.51	95.07	6909	520	541	0.002	345

[Atlas SLV-3D(R)	[11101]	1228 days	cylinder	2.4 dia

AC-52 Centaur D-1AR	 CC-LC36B	1982 Mar 25	2720

5032D]

D	HEAO 2	1978-103 B	1978 Nov 13.23	Cylinder	8.6 long	1978 Nov 18.0	23.51	92.86	6801	379	467	0.006	10

Centaur 52 stage	[11102]	120 days	1815	3.0 dia

1979 Mar 13

D	Cosmos 1047	1978-104 A	1978 Nov 15.49	Sphere-	6.5 long?	1978 Nov 15.5	72.86	89.77	6641	171	354	0.014	80

R	[Soyuz 11A511U] 	[11108]	12.77 days	cylinder	2.4 dia

PLE	1978 Nov 28.26	6300?

D	Cosmos 1047	1978-104 B	1978 Nov 15.49	Cylinder	7.5 long	1978 Nov 18.0	72.86	88.85	6595	160	274	0.009	69

Block I 3rd stage 	[11109]	4 days	2500?	2.6 dia

1978 Nov 19

D	Cosmos 1047	1978-104 C	1978 Nov 15.49	Cone	1.5 long?	1978 Nov 30.3	72.86	88.74	6590	159	265	0.008	45

engine	[11120]	17 days	600? full	2 dia?

1978 Dec 2

Cosmos 1048	1978-105 A	1978 Nov 16.91	Cylinder	2 long?	1978 Nov 17.1	74.03	100.89	7179	785	816	0.002	350

[Kosmos 11K65M 	[11111]	120 years	paddles?	1 dia?	2004 Jul 6.68	74.03	100.45	7158	766	793	0.002	132

53755-111]	PLE		750?

Cosmos 1048	1978-105 B	1978 Nov 16.91	Cylinder	7.4 long	1978 Nov 17.1	74.04	100.81	7175	777	816	0.003	358

2nd stage	[11112]	100 years	2200?	2.4 dia	2004 Jul 9.56	74.03	100.28	7150	748	796	0.003	73

Fragment	1978-105 C	[11113]			2004 Jul 5.71	74.04	98.83	7081	696	710	0.001	142

Fragment	1978-105 D	[11114]			2004 Jul 4.81	74.02	98.45	7063	679	690	0.0008	93

NATO 3C	1978-106 A	1978 Nov 19.04	Cylinder	2.23 long	1978 Nov 19.1	27.20	632.80	24416	185	35890	0.731	171

[Delta 2914 634	[11115]	> million	706 full	2.18 dia	1978 Nov 30.2	4.41	1428.6	42020	35516	35768	0.003	217

#146]	CC-LC17B	years	346 empty		2004 Jul 6.50	12.41	1462.13	42673	36268	36321	0.0006	94

D	NATO 3C	1978-106 B	1978 Nov 19.04	Cylinder	6.4 long	1978 Nov 21.1	28.24	93.50	6831	174	732	0.041	179

Delta 2nd stage	[11116]	23 days	annulus	1.52 and

1978 Dec 12	350?	2.44 dia

D	NATO 3C	1978-106 C	1978 Nov 19.04	Sphere	1.32 long	1978 Nov 19'	27.2	632.76	24414	183	35889	0.731	171

Star-37E PKM	[11117]	1470 days	-cone	0.94 dia

1982 Nov 28	66

D	Cosmos 1049	1978-107 A	1978 Nov 21.50	Sphere-	6.5 long?	1978 Nov 22.8	72.86	89.59	6632	169	338	0.013	80

R	[Soyuz 11A511U] 	[11118]	12.76 days	cylinder	2.4 dia	1978 Nov 26.2	72.86	89.65	6635	169	344	0.013	71

PLE	1978 Dec 4.26	6300?

D	Cosmos 1049	1978-107 B	1978 Nov 21.50	Cylinder	7.5 long	1978 Nov 21.7	72.86	89.56	6630	169	335	0.012	82

Block I 3rd stage 	[11119]	5 days	2500?	2.6 dia

1978 Nov 26

D	Cosmos 1049	1978-107 E	1978 Nov 21.50	Cone	1.5 long?	1978 Dec 4	72.8	89.58	6630	181	322	0.011	-

engine	[11127]	20 days	600? full	2 dia?

1978 Dec 11

D	Fragment	1978-107 C	[11125]	1978 Dec 10	19 days

D	Fragment	1978-107 D	[11126]	1978 Dec 8	17 days

D	Cosmos 1050	1978-108 A	1978 Nov 28.68	Sphere-	6.5 long?	1978  Nov 30.1	62.80	89.81	6644	254	278	0.002	126

R	[Soyuz 11A511U] 	[11121]	13.62 days	cylinder	2.4 dia	1978  Dec 3.2	62.80	89.43	6625	224	270	0.003	77

PLE	1978 Dec 12.30	6300?

D	Cosmos 1050	1978-108 B	1978 Nov 28.68	Cylinder	7.5 long	1978  Dec   2.7	62.79	89.41	6624	240	252	0.001	73

Block I 3rd stage 	[11122]	10 days	2500?	2.6 dia

1978 Dec 8

D	Cosmos 1050	1978-108 E	1978 Nov 28.68	Cone	1.5 long?	1978  Dec  12.2	62.80	89.07	6607	160	298	0.011	230

engine	[11143]	17 days	600? full	2 dia?

1978 Dec 15

D	Fragments	1978-108 C	[11123]	1979 Jan 2	35 days

D	Fragments	1978-108 D	[11124]	1979 Jan 2	35 days

Cosmos 1051	1978-109 A	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 8.4	74.02	114.72	7820	1397	1487	0.006	102

[Kosmos 11K65M 	[11128]	7000 years	40?	0.8 dia?	2004 Jul 4.70	74.02	114.65	7818	1394	1485	0.006	323

53716-320]	PLE

Cosmos 1052 *	1978-109 B	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 6.1	74.02	114.92	7829	1412	1490	0.005	117

[11129]	8000 years	40?	0.8 dia?	2004 Jul 6.24	74.01	114.87	7828	1410	1487	0.005	30

Cosmos 1053 *	1978-109 C	1978 Dec 5.76	Spheroid	1.0 long	1978 Dec 8.3	74.02	115.12	7839	1433	1488	0.003	119

[11130]	9000 years	40?	0.8 dia?	2004 Jul 4.93	74.02	115.07	7837	1429	1487	0.004	95

Cosmos 1054 *	1978-109 D	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 9.2	74.02	115.33	7848	1449	1491	0.003	129

[11131]	9000 years	40?	0.8 dia?	2004 Jul 5.53	74.02	115.27	7846	1446	1489	0.003	163

Cosmos 1055 *	1978-109 E	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 8.2	74.02	115.5	7858	1460	1500	0.002	160

[11132]	10000 years	40?	0.8 dia?	2004 Jul 6.49	74.02	115.48	7856	1464	1491	0.002	242

Cosmos 1056 *	1978-109 F	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 8.3	74.02	115.77	7868	1472	1508	0.002	197

[11133]	10000 years	40?	0.8 dia?	2004 Jul 5.85	74.01	115.70	7866	1472	1503	0.002	349

Cosmos 1057 *	1978-109 G	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 8.3	74.02	115.99	7878	1482	1518	0.002	231

[11134]	9000 years	40?	0.8 dia?	2004 Jul 5.87	74.01	115.93	7876	1480	1515	0.002	89

Cosmos 1058 *	1978-109 H	1978 Dec 5.76	Spheroid	1.0 long?	1978 Dec 9.2	74.02	116.24	7889	1481	1541	0.004	236

[11135]	10000 years	40?	0.8 dia?	2004 Jul 5.18	74.02	116.18	7887	1480	1537	0.004	166

Cosmos 1051-1058	1978-109 J	1978 Dec 5.76	Cylinder	7.4 long	1980 Jun 30	74.0	118.06	7973	1484	1706	0.014	-

2nd stage	[11136]	20000 years	2200?	2.4 dia	2004 Jul 6.81	74.01	118.10	7974	1491	1700	0.013	347

*	Strela-1M

D	Cosmos 1059	1978-110 A	1978 Dec 7.65	Sphere-	6.5 long?	1978 Dec 7.8	62.81	89.67	6637	180	338	0.012	80

R	[Soyuz 11A511U] 	[11137]	12.63 days	cylinder	2.4 dia	1978 Dec 9.4	62.81	89.35	6621	172	314	0.011	72

PLE	1978 Dec 20.28	6300?

D	Cosmos 1059	1978-110 B	1978 Dec 7.65	Cylinder	7.5 long	1978 Dec 7.8	62.80	89.53	6630	177	327	0.011	77

Block I 3rd stage 	[11138]	4 days	2500?	2.6 dia

1978 Dec 11

D	Cosmos 1059	1978-110 C	1978 Dec 7.65	Cone	1.5 long?	1978 Dec 19.4	b2.84	89.76	6642	168	359	0.014	66

engine	[11157]	16 days	600? full	2 dia?

1978 Dec 23

D	Fragment	1978-110 D	[11160]	1978 Dec 23	16 days

D	Cosmos 1060	1978-111 A	1978 Dec 8.40	Sphere-	5.0 long	1978 Dec 8.5	65.03	89.47	6627	206	292	0.006	53

R	[Soyuz 11A511U] 	[11139]	12.8 days	cylinder	2.4 dia

BAI	1978 Dec 21.2	5700?

D	Cosmos 1060	1978-111 B	1978 Dec 8.40	Cylinder	7.5 long	1978 Dec 8.5	65.03	89.32	6620	201	282	0.006	36

Block I 3rd stage 	[11140]	5 days	2500?	2.6 dia

1978 Dec 13

Navstar 4	1978-112 A	1978 Dec 11.18	Cylinder	-	1978 Dec 14.2	63.27	722.38	26670	20267	20316	0.001	88

(GPS)	[11141]	1 million	4 vanes		2004 Jul 6.34	64.16	746.52	27260	20718	21045	0.006	26

[Atlas 39F/SGS-1]	VDB-SLC3E	years	871 full

525 empty

Navstar 4	1978-112 B	1978 Dec 11.18	Cone-	1.85 long?	1978 Dec 13.8	63.09	349.31	16431	120	19986	0.605	162

Star-37E PKM	[11142]	30 years	cylinder?	0.63 to	2004 Jul 5.14	64.10	269.45	13819	911	13970	0.472	49

163?	1.65 dia?

DSCS 2-11*	1978-113 A	1978 Dec 14.03	Cylinder +	1.83 long	1978 Dec 14.8	2.49	1452.2	42482	35796	36412	0.007	2

[Titan 3C 23C-18]	[11144]	> million	2 dishes	2.74 dia	1979 Mar 7.7	2.27	1436.2	42168	35784	35796	0.0001	204

CC-LC40	years	590		1993 May 31.00	9.38	1454.04	42016	36133	36142	0.012	103

2004 Jul 9.20	14.60	1531.37	44010	37500	37765	0.003	12

DSCS 2-12*	1978-113 B	1978 Dec 14.03	Cylinder	1.83 long	1978 Dec 14.8	2.50	1464.3	42715	36 261	36413	0.002	352

[11145]	> million	2 dishes	2.74 dia	1979 Feb 28.8	2.30	1436.0	42164	35776	35796	0.0002	268

years	590		2004 Jul 6.00	14.02	1462.82	42686	36279	36336	0.0007	9

D	Titan 3C	1978-113 C	1978 Dec 14.03	Cylinder	6 long	1978 Dec 14.6	28.59	87.90	6556	150	206	0.004	121

second stage	[11146]	<1 day	1900	3.0 dia

1978 Dec 14

Transtage 36	1978-113 D	1978 Dec 14.03	Cylinder	6 long?	1978 Dec 14.8	2.50	1452.0	42478	35788	36412	0.007	2

[11147]	> million	1500?	3.0 dia	2004 Jul 9.51	16.35	1535.88	44096	36530	38905	0.027	227

years

*	DSCS-2 9 and 10 failed to reach orbit in 1978 March. DSCS-2 11 and 12 deactivated 1993 Dec 13.

D	Cosmos 1061	1978-114 A	1978 Dec 14.64	Sphere-	5.9 long	1978 Dec 15.6	62.82	89.62	6635	203	310	0.008	78

R	[Soyuz 11A511U] 	[11148]	12.63 days	cylinder	2.4 dia

PLE	1978 Dec 27.27	5900?

D	Cosmos 1061	1978-114 B	1978 Dec 14.64	Cylinder	7.5 long	1978 Dec 15.1	62.81	89.42	6625	200	293	0.007	73

Block I 3rd stage 	[11149]	6 days	2500?	2.6 dia

1978 Dec 20

D	Nauka Capsule	1978-114 C	1978 Dec 14.64	Ellipsoid	0.9 long	1978 Dec 27	62.8	89.56	6632	212	295	0.006	-

[11167]	21 days	200?	1.9 dia

1979 Jan 4

D	Cosmos 1062	1978-115 A	1978 Dec 15.56	Cylinder +	2 long?	1978 Dec 16.9	74.04	95.18	6905	504	550	0.003	350

[Kosmos 11K65M 	[11150]	857 days	paddles?	1 dia?

53782-408]	PLE	1981 Apr 20	900?

D	Cosmos 1062	1978-115 B	1978 Dec 15.56	Cylinder	7.4 long	1978 Dec 16.9	74.04	95.09	6901	494	551	0.004	357

2nd stage	[11151]	918 days	2200?	2.4 dia

1981 Jun 20

D	Fragment	1978-115 C	[11152]	1979 Mar 7	82 days

Telesat 4	1978-116 A	1978 Dec 16.01	Box + vanes	2.14 high	1978 Dec 16.0	27.25	632.91	24419	185	35896	0.731	178

(Anik B1)	[11153]	> million	922 full	2.17 square	1979 Jan 31.6	0.03	1435.9	42164	35781	35790	0.0001	58

[Delta 3914 632	CC-LC17A	years	474 empty		2004 Jul 7.87	11.89	1442.53	42291	35877	35947	0.0008	52

#147]

D	Telesat 4	1978-116 B	1978 Dec 16.01	Cylinder	6.4 long	1978 Dec 16.7	28.42	107.68	7504	183	2069	0.126	181

Delta 2nd stage	[11154]	128 days	annulus	1.52 and

(DRIMS)*		1979 Apr 23	350?	2.44 dia

D	Telesat 4	1978-116 C	1978 Dec 16.01	Sphere-	1.8 long		Orbit similar to 1978-116 A transfer orbit

third stage	[13915]	3294 days	cone	0.94 dia

1987 Dec 23	66

*	Delta Redundant Inertia] Measurement Systems

D	Cosmos 1063	1978-117 A	1978 Dec 19.07	Cylinder	5 long?	1978 Dec 21.8	81.23	97.38	7011	631	634	0.0002	55

[Vostok 8A92M] 	[11155]	8377 days	2 vanes?	1.5 dia?	2001 Nov 24.57	81.16	88.08	6558	177	182	0.004	249

PLE	2001 Nov 25	2500?

D	Cosmos 1063	1978-117 B	1978 Dec 19.07	Cylinder	3.8 long	1978 Dec 22.0	81.24	97.44	7014	581	690	0.008	170

Block E 3rd stage 	[11156]	8737 days	1440	2.6 dia	2002 Nov 19.56	81.21	87.80	6544	160	170	0.0008	235						2002 Nov 20

Gorizont 1	1978-118 A	1978 Dec 19.52	Cylinder +	-	1918 Dec 20.4	11.3	1420	41850	22580	48365	0.308	70

[Proton 8K82K 	[11158]	> million years	dish +		1978 Jun 30.0	11.3	1436.1	42166	22553	49023	0.314	-

295-02/11S86 17L]	BAI-LC200P		panels		2004 Jul 8.97	24.36	1435.62	42155	21845	49708	0.330	22

2000?

D	Gorizont 1	1978-118 B	1978 Dec 19.52	Cylinder	6.5 long?	1978 Dec 20.1	51.61	88.08	6560	174	190	0.001	206

third stage*	[11159]	2 days		4 dia

1978 Dec 21

Gorizont 1	1978-118 C	1978 Dec 19.52	Cylinder	5.5 long	1980 Jul 24.7	10.75	1417.3	41798	22124	48715	0.318	28

Block DM 4th stage	[11926]	> million years	17300 full	4.0 dia	2004 Jul 3.08	23.85	1417.28	41796	21788	49047	0.326	26

D	Auxiliarry motor *1	1978-118 D	1978 Dec 19.52

[12784]	225 days

1979 Aug 1

D	Auxiliarry motor *2	1978-118 E	1978 Dec 19.52

[12783]	350 days

1979 Dec 4

*	There may have been a launcher in a similar orbit.

*1	Re-assigned from 1981 81 B.

*2 Re-assigned from 1982 07 N.

D	Cosmos 1064**	1978-119 A	1978 Dec 20.87	Cylinder	2.1 long	1978 Dec 21.9	82.95	98.69	7073	424	965	0.038	99

[Kosmos 11K65M 	[11161]	3980 days	810	2.0 dia

47182-425]	PLE-LC132	1989 Nov 12

D	Cosmos 1064	1978-119 B	1978 Dec 20.87	Cylinder	7.4 long	1978 Dec 21.2	82.95	98.58	7067	416	962	0.039	102

2nd stage	[11162]	3618 days	2200?	2.4 dia

1988 Nov 15

**	Possibly a navigation satellite	where the rocket failed to circularize the orbit at apogee.

D	Cosmos 1065	1978-120 A	1978 Dec 22.92	Octagonal	1.8 long?	1978 Dec 24.3	50.68	93.45	6824	344	548	0.015	151

[Kosmos 11K65M 	[11163]	222 days	ellipsoid?	1.5 dia?

65068-305]	KY-LC107	1979 Aug 1	550?

D	Cosmos 1065	1978-120 B	1978 Dec 22.92	Cylinder	7.4 long	1978 Dec 23.0	50.68	93.41	6822	344	544	0.015	144

2nd stage	[11164]	239 days	2200?	2.4 dia

1979 Aug 18

D	Fragments  %	1978-12O C-H	6 pieces, all have decayed		For orbital information see extra pages at the end of the year

%	These fragments are calibration targets.

Cosmos 1066 #	1978-121 A	1978 Dec 23.37	Cylinder +	5 long?	1978 Dec 23.5	81.24	102.05	7233	818	891	0.005	272

[Vostok 8A92M] 	[11165]	500 years	2 vanes	1.5 dia?	2004 Jul 7.09	81.24	102.03	7234	818	891	0.005	148

PLE		2750?

Cosmos 1066	1978-121 B	1978 Dec 23.37	Cylinder	3.8 long	1978 Dec 23.6	81.25	102.10	7235	816	898	0.006	246

Block E 3rd stage 	[11166]	400 years	1440	2.6 dia	2004 Jul 6.90	81.24	101.88	7226	799	897	0.007	39

Fragment	1978-121 C	[19643]			2004 Jul 7.88	81.24	101.80	7223	797	891	0.006	19

#	Probably an attempted Meteor-2 satellite.

Cosmos 1067	1978-122 A	1978 Dec 26.56	Spheroid	1.6 dia?	1978 Dec 26.8	82.97	109.07	7561	1158	1208	0.003	267

[Kosmos 11K65M 	[11168]	3000 years	paddles?		2004 Jul 6.10	82.97	109.08	7563	1156	1212	0.004	16

53782-430]	PLE		650?

Cosmos 1067	1978-122 B	1978 Dec 26.56	Cylinder	7.4 long	1978 Dec 26.7	82.97	108.95	7555	1157	1197	0.003	256

2nd stage	[11170]	2000 years	2200?	2.4 dia	2004 Jul 6.97	82.97	108.93	7556	1159	1195	0.002	281

D	Cosmos 1068	1978-123 A	1978 Dec 26.65	Sphere-	6.5 long?	1978 Dec 26.9	62.80	90.17	6662	177	391	0.016	74

R	[Soyuz 11A511U] 	[11169]	12.6 days	cylinder	2.4 dia	1978 Dec 27.6	62.80	89.40	6624	173	318	0.011	64

PLE	1979 Jan 8.3	6300?

D	Cosmos 1068	1978-123 B	1978 Dec 26.65	Cylinder	7.5 long	1978 Dec 27.1	62.78	89.92	6650	174	369	0.015	71

P	Block I 3rd stage 	[11171]	5.1 5days	2500?	2.6 dia

1978 Dec 31.80

D	Cosmos 1068	1978-123 D	1978 Dec 26.65	Cone	1.5 long?	1979 Jan 6.7	62.80	89.38	6623	166	324	0.012	62

engine	[11226]	14 days	600? full	2 dia?

1979 Jan 9

D	Fragment	1978-123 C	[11172]	1979 Jan 1	6 days

D	Fragment	1978-123 E	[11227]	1979 Jan 9	14 days

D	Cosmos 1069	1978-124 A	1978 Dec 28.69	Sphere-	5.9 long	1978 Dec 29.5	62.82	89.75	6641	241	285	0.003	188

R	[Soyuz 11A511U] 	[11173]	12.64 days	cylinder	2.4 dia

PLE	1979 Jan 10.33	5900?

D	Cosmos 1069	1978-124 B	1978 Dec 28.69	Cylinder	7.5 long	1978 Dec 29.5	62.82	89.62	6635	241	272	0.002	193

Block I 3rd stage 	[11174]	8 days	2500?	2.6 dia

1979 Jan 5

D	Capsule	1978-124 F	1978 Dec 28.69	Ellipsoid	0.9 long	1979  Jan 14.2	62.81	90.44	6676	242	354	0.008	319

[11237]	25 days	200?	1.9 dia

1979 Jan 22

D	Fragment	1978-124 C	[11175]	1978 Dec 31	3 days

D	Fragment	1978-124 D	[11176]	1979 Jan 16	19 days

D	Fragment	1978-124 E	[11228]	1979 Jan 11	14 days

*	Decay was observed over Europe and pieces were picked up near Hannover.

Text in box is from "History of on-orbit satellite fragmentations", 13th edition, May 2004.

Orbital Debris Program Office, Johnson Space Centre, NASA, Houston, TX 77058.

Kyokko fragments; 6 pieces, 2 have decayed.

1978-14 C	[12329]				2004 Jul 4.48	65.28	133.52	8653	635	3914	0.189	269

1978-14 D	[12330]				2004 Jul 5.66	65.37	133.73	8663	635	3934	0.190	160

1978-14 E	[12331]				2004 Jul 6.16	64.82	131.72	8576	640	3755	0.182	44

1978-14 F	[12406]				2004 Jul 4.72	65.91	132.40	8606	641	3814	0.184	253

First anomalous event (object 18816) may have occurred much earlier than the January 1988 date. Catalog actions taken at the end of 1988. The second event occurred in June 1992. Object 22008 led a short life, decaying on 2 August 1992.

D	1978-14 G	[18816]	1988 Nov 10	3932 days

D	1978-14 H	[22008]	1992 Aug 2	5293 days

Cosmos 988 fragments; 4 pieces, all have decayed.

D	1978-15 C	[10668]	1978 Mar 5	25 days

D	1978-15 D	[10678]	1978 Feb 22	14 days

D	1978-15 E	[10679]	1978 Mar 2	22 days

D	1978-15 G	[10681]	1978 Feb 24	16 days

Landsat 3 Delta 2nd stage fragments; 248 pieces, 93 have decayed.

This was the seventh Delta Second Stage to experience a severe fragmentation. The event occurred 1981 Jan 27 at 04:32 UT near 80ºS 301ºE, nearly 35 months after the successful deployment of the Landsat 3 payload. Cause of the explosion is assessed to be related to the estimated 100 kg of residual propellants on board and characteristics of the sun-synchronous orbit.

1978-26 D	[12164]				2004 Jul 4.68	98.62	100.83	7177	746	851	0.007	44

1978-26 E	[12165]				2004 Jul 6.18	98.86	102.15	7239	828	892	0.004	156

1978-26 F	[12166]				2004 Jul 6.52	98.79	101.82	7223	816	873	0.004	70

1978-26 G	[12167]				2004 Jul 6.54	98.99	102.12	7238	737	982	0.017	314

1978-26 H	[12168]				2004 Jul 5.70	98.89	103.57	7306	796	1058	0.018	170

1978-26 J	[12169]				2004 Jul 5.77	98.70	100.90	7180	749	853	0.007	231

1978-26 K	[12170]				2004 Jul 5.54	98.76	101.68	7217	805	871	0.005	358

1978-26 L	[12171]				2004 Jul 5.11	99.01	102.67	7263	857	913	0.004	105

1978-26 M	[12172]				2004 Jul 4.98	98.73	101.30	7199	775	866	0.006	92

D	1978-26 N	[12173]	2014 Jul 7	13273 days		2004 Jul 5.24	98.44	98.07	7045	643	689	0.003	355

2014 Jul 6.99	98.45	98.68	6588	198	221	0.002	226

1978-26 P	[12174]				2004 Jul 4.58	98.88	102.25	7243	834	895	0.004	235

1978-26 Q	[12175]				2004 Jul 5.90	98.86	103.30	7293	867	961	0.006	276

1978-26 R	[12176]				2004 Jul 5.21	99.03	103.75	7315	887	984	0.007	94

1978-26 S	[12177]				2004 Jul 4.95	98.70	103.58	7307	811	1045	0.016	178

1978-26 T	[12178]				2004 Jul 5.98	98.88	103.42	7299	874	965	0.006	309

1978-26 U	[12179]				2004 Jul 6.24	98.98	102.87	7273	761	1028	0.018	320

D	1978-26 V	[12180]	2000 May 18	8110 days

1978-26 W	[12181]				2004 Jul 6.53	98.81	101.13	7191	739	885	0.010	213

D	1978-26 X	[12182]	1989 Oct 28	4255 days

1978-26 Y	[12183]				2004 Jul 6.16	98.82	102.00	7232	827	880	0.004	249

1978-26 Z	[12184]				2004 Jul 5.42	98.76	98.57	7068	683	696	0.0009	227

1978-26 AA	[12185]				2004 Jul 6.21	99.13	102.22	7242	790	936	0.010	88

D	1978-26 AB	[12186]	1989 Dec 11	4299 days

D	1978-26 AC	[12187]	1988 Feb 12	3631 days

D	1978-26 AD	[12188]	1993 Mar 13	5487 days

1978-26 AE	[12189]				2004 Jul 5.35	99.41	103.43	7299	871	970	0.007	238

1978-26 AF	[12190]				2004 Jul 4.72	99.16	102.88	7273	882	907	0.002	254

D	1978-26 AG	[12191]	1989 Feb 28	4013 days

D	1978-26 AH	[12192]	1989 Mar 22	4035 days

1978-26 AJ	[12193]				2004 Jul 6.40	98.89	105.53	7398	811	1228	0.028	213

1978-26 AK	[12194]				2004 Jul 6.00	98.96	99.38	7107	687	771	0.006	136

1978-26 AL	[12195]				2004 Jul 5.54	98.99	103.48	7301	877	968	0.006	357

D	1978-26 AM	[12196]	2001 Jan 11	8348 days

D	1978-26 AN	[12197]	1982 Feb 5	3990 days

1978-26 AP	[12198]				2004 Jul 5.84	98.96	103.05	7281	817	988	0.012	314

D	1978-26 AQ	[12199]	1990 Feb 20	4370 days

1978-26 AR	[12200]				2004 Jul 5.57	98.83	100.78	7174	714	878	0.011	341

D	1978-26 AS	[12201]	2001 Oct 15	8625 days		2001 Oct 20.51	98.43	90.90	6697	307	330	0.002	339

D	1978-26 AT	[12202]	1983 Nov 12	2078 days

1978-26 AU	[12203]				2004 Jul 6.13	98.65	100.67	7169	740	840	0.007	175

1978-26 AV	[12204]				2004 Jul 5.52	98.73	101.02	7186	747	867	0.008	266

D	1978-26 AW	[12205]	1989 Jul 21	4156 days

1978-26 AX	[12206]				2004 Jul 5.90	98.84	103.42	7298	791	1048	0.018	263

D	1978-26 AY	[12207]	1984 Jul 16	2324 days

D	1978-26 AZ	[12208]	2001 Oct 22	8632 days		2001 Oct 19.19	98.73	93.83	6840	437	486	0.004	307

1978-26 BA	[12209]				2004 Jul 6.28	98.63	100.82	7175	752	841	0.006	305

D	1978-26 BB	[12210]	1990 Feb 11	4361 days

1978-26 BC	[12211]				2004 Jul 5.01	99.36	102.65	7262	793	974	0.012	285

1978-26 BD	[12212]				2004 Jul 5.30	99.33	103.10	7284	886	925	0.003	317

D	1978-26 BE	[12213]	2004 Aug 13	9658 days		2004 Jul 6.38	98.98	94.35	6866	467	508	0.003	326

D	1978-26 BF	[12214]	2003 Oct 28	9368 days

D	1978-26 BG	[12215]	2006 Oct 1 	10437 days		2004 Jul 5.64	98.88	95.97	6944	555	575	0.001	177

2006 Oct 1.48	98.84	88.08	6559	170	190	0.001	186

1978-26 BH	[12216]				2004 Jul 5.34	98.94	103.68	7311	776	1089	0.021	138

1978-26 BJ	[12217]				2004 Jul 6.17	98.79	101.73	7219	824	857	0.002	135

1978-26 BK	[12218]				2004 Jul 5.97	99.49	103.18	7288	870	948	0.005	0

D	1978-26 BL	[12219]	1989 Aug 10	4176 days

D	1978-26 BM	[12220]	1991 Mar 13	4756 days

D	1978-26 BN	[12221]	1994 Aug 1	5993 days

1978-26 BP	[12222]				2004 Jul 4.87	99.02	103.58	7306	874	981	0.007	38

1978-26 BQ	[12223]				2004 Jul 6.15	98.94	102.63	7262	853	914	0.004	96

D	1978-26 BR	[12224]	1992 Dec 31	5415 days

1978-26 BS	[12225]				2004 Jul 6.16	99.22	102.65	7262	855	912	0.004	168

1978-26 BT	[12226]				2004 Jul 6.18	98.96	103.50	7302	793	1054	0.018	174

1978-26 BU	[12227]				2004 Jul 5.34	98.77	98.17	7050	591	751	0.011	186

D	1978-26 BV	[12228]	1990 Oct 5	4597 days

D	1978-26 BW	[12229]	1981 May 5 A	1157 days

1978-26 BX	[12230]				2004 Jul 5.11	98.47	98.97	7086	648	767	0.008	192

D	1978-26 BY	[12231]	1993 Mar 19	5493 days

D	1978-26 BZ	[12232]	2014 Apr 7	13182 days		2004 Jul 5.76	99.03	98.75	7077	646	751	0.007	28

2014 Apr 7.48	99.03	88.88	6598	210	229	0.001	296

D	1978-26 CA	[12233]	1988 Feb 12	3631 days

1978-26 CB	[12234]				2004 Jul 6.37	99.03	102.68	7264	864	907	0.003	80

D	1978-26 CC	[12235]	1989 Feb 8	3993 days

1978-26 CD	[12236]				2004 Jul 5.54	98.80	104.37	7344	796	1134	0.023	16

1978-26 CE	[12237]				2004 Jul 6.54	98.84	105.68	7405	777	1275	0.034	104

D	1978-26 CF	[12238]	1982 Feb 15	1443 days

D	1978-26 CG	[12239]	1982 Feb 5	1433 days

D	1978-26 CH	[12240]	1984 Apr 16	2234 days

D	1978-26 CJ	[12241]	1982 Apr 11	1498 days

1978-26 CK	[12242]				2004 Jul 2.02	99.01	103.28	7293	863	965	0.007	8

D	1978-26 CL	[12243]	1995 Nov 24	6503 days

D	1978-26 CM	[12244]	1989 Jun 18	4123 days

D	1978-26 CN	[12245]	1989 Jul 15	4150 days

1978-26 CP	[12246]				2004 Jul 6.51	98.69	102.85	7272	846	941	0.007	183

D	1978-26 CQ	[12247]	1988 Jun 2	3742 days

D	1978-26 CR	[12248]	1981 Aug 17	1261 days

D	1978-26 CS	[12249]	1989 Apr 16	4090 days

1978-26 CT	[12250]				2004 Jul 4.69	98.70	101.37	7202	804	842	0.003	333

D	1978-26 CU	[12251]	1981 Feb 18	1109 days

D	1978-26 CV	[12252]	1981 Jan 2	1399 days

D	1978-26 CW	[12253]	1981 Dec 13	1379 days

D	1978-26 CX	[12254]	1989 Mar 20	4033 days

1978-26 CY	[12255]

Decay deleted 2011 Jun

1978-26 CZ	[12256]				2004 Jul 4.97	98.70	102.78	7269	814	967	0.010	110

1978-26 DA	[12257]				2004 Jul 5.09	99.35	102.83	7271	820	965	0.010	345

D	1978-26 DB	[12258]	1981 Jul 1	1214 days

D	1978-26 DC	[12259]	1989 Dec 15	4303 days

D	1978-26 DD	[12260]	1991 May 29	4833 days

D	1978-26 DE	[12261]	1991 Sep 27	4953 days

1978-26 DF	[12262]				2004 Jul 5.20	98.83	103.08	7283	814	996	0.012	336

1978-26 DG	[12263]				2004 Jul 6.18	98.93	109.52	7583	845	1563	0.047	71

D	1978-26 DH	[12264]	1981 Dec 10	1376 days

1978-26 DJ	[12265]				2004 Jul 6.27	98.83	102.43	7265	763	1011	0.017	266

1978-26 DK	[12266]				2004 Jul 4.91	98.78	104.17	7334	835	1075	0.016	327

D	1978-26 DL	[12267]	2002 Mar 7	8768 days		2002 Mar 6.64	98.71	89.03	6605	225	228	0.0002	298

D	1978-26 DM	[12268]	1993 Jul 18	5614 days

1978-26 DN	[12269]				2004 Jul 5.70	98.51	99.20	7099	666	775	0.008	4

1978-26 DP	[12270]				2004 Jul 6.35	98.99	103.63	7309	881	980	0.007	19

D	1978-26 DQ	[12271]	1998 Nov 18	1354 days

D	1978-26 DR	[12272]	1989 Aug 7	4173 days

1978-26 DS	[12273]				2004 Jul 5.98	98.74	97.32	7009	615	646	0.002	254

12274 re-assigned 2011 Jun to 1976-77 DF; old 1978 DU to ET moved up 1 character to 1978 26 DT to ES

D	1978-26 DT	[12275]	1981 Dec 27	1393 days

D	1978-26 DU	[12276]	1987 Apr 20	3333 days

D	1978-26 DV	[12277]	1989 Aug 17	4183 days

1978-26 DW	[12278]				2004 Jul 4.81	99.04	101.43	7205	786	867	0.006	11

1978-26 DX	[12279]				2004 Jul 6.40	98.90	100.30	7151	741	805	0.005	285

D	1978-26 DY	[12280]	1999 Jun 22	7779 days

D	1978-26 DZ	[12281]	1982 Nov 7	1708 days

D	1978-26 EA	[12282]	1982 Apr 29	1546 days

1978-26 EB	[12283]				2004 Jul 4.62	98.78	101.08	7189	743	877	0.009	205

1978-26 EC	[12284]				2004 Jul 6.22	99.05	103.23	7290	835	988	0.010	242

1978-26 ED	[12285]				2004 Jul 5.75	99.03	102.48	7254	835	916	0.006	177

D	1978-26 EE	[12286]	1981 Oct 14	1319 days

D	1978-26 EF	[12287]	1994 Jun 7	5938 days

1978-26 EG	[12288]				2004 Jul 6.23	99.03	102.07	7235	791	922	0.009	105

D	1978-26 EH	[12289]	1991 Nov 10	4998 days

1978-26 EJ	[12290]				2004 Jul 4.67	98.92	102.22	7242	802	925	0.009	302

1978-26 EK	[12291]				2004 Jul 5.72	99.19	101.88	7227	805	891	0.006	103

1978-26 EL	[12292]				2004 Jul 5.89	98.68	103.10	7284	861	949	0.006	219

D	1978-26 EM	[12293]	2014 Dec 1	13420 days		2004 Jul 6.13	98.27	98.02	7042	644	683	0.003	339

2014 Nov 30.47	98.17	90.08	6657	271	286	0.001	344

1978-26 EN	[12294]				2004 Jul 5.55	98.72	100.23	7148	697	843	0.010	174

1978-26 EP	[12372]				2004 Jul 6.19	82.98	103.78	7316	897	977	0.005	340

1978-26 EQ	[12373]				2004 Jul 5.65	99.08	102.77	7268	875	904	0.002	174

D	1978-26 ER	[12374]	1989 Dec 27	4315 days

1978-26 ES	[12375]				2004 Jul 6.34	99.01	98.70	7075	646	747	0.007	239

1978-26 ET	[12427]

Re-assigned 2011 Jun from 1981 36 E??

D	1978-26 EU	[12823]	1990 Dec 14	4698 days

D	1978-26 EV	[12824]	2003 Feb 2	9100 days

1978-26 EW	[12825]				2004 Jul 6.06	98.84	103.40	7298	874	964	0.006	300

1978-26 EX	[12826]				2004 Jul 6.02	98.97	97.27	7006	601	655	0.004	62

1978-26 EY	[13561]				2004 Jul 8.27	98.74	103.00	7279	764	1037	0.019	231

1978-26 EZ	[13562]				2004 Jul 9.10	98.66	101.10	7189	782	839	0.004	169

1978-26 FA	[13563]				2004 Jul 8.67	98.82	101.55	7210	799	864	0.005	340

1978-26 FB	[13564]				2004 Jul 8.74	98.92	104.10	7330	796	1107	0.021	89

1978-26 FC	[13565]				2004 Jul 8.86	98.99	103.38	7297	869	969	0.007	344

1978-26 FD	[13566]				2004 Jul 8.75	98.64	101.05	7187	781	836	0.003	149

1978-26 FE	[13567]				2004 Jul 8.72	98.86	104.32	7341	790	1135	0.023	332

D	1978-26 FF	[13568]	1990 Nov 17	5005 days

1978-26 FG	[13569]				2004 Jul 8.81	98.82	102.95	7277	808	988	0.012	236

1978-26 FH	[13570]				2004 Jul 8.66	98.58	100.63	7167	752	825	0.005	253

1978-26 FJ	[13571]				2004 Jul 7.69	98.58	100.38	7155	759	794	0.002	41

1978-26 FK	[13572]				2004 Jul 8.01	99.07	101.95	7229	733	968	0.016	88

1978-26 FL	[13573]				2004 Jul 8.80	99.01	103.77	7315	882	990	0.007	80

1978-26 FM	[13574]				2004 Jul 8.73	98.90	102.05	7235	828	884	0.004	274

1978-26 FN	[13575]				2004 Jul 8.54	98.95	102.60	7260	867	896	0.002	85

D	1978-26 FP	[13576]	2000 Jun 6	8129 days

D	1978-26 FQ	[13577]	2000 Apr 19	8081 days

D	1978-26 FR	[13578]	2005 Nov 11	10113 days		2004 Jul 9.14	98.90	96.33	6961	544	621	0.006	74

2005 Nov 11.84	98.86	89.03	6605	215	238	0.002	162

1978-26 FS	[13579]				2004 Jul 8.73	98.81	101.67	7216	822	853	0.002	182

D	1978-26 FT	[13580]	1983 Mar 6	1858 days

1978-26 FU	[13825]				2004 Jul 8.60	98.80	102.23	7243	748	980	0.016	75

1978-26 FV	[13826]				2004 Jul 8.59	98.48	99.43	7110	694	769	0.005	129

1978-26 FW	[13827]				2004 Jul 8.62	98.55	98.55	7127	688	808	0.008	139

D	1978-26 FX	[14457]	1991 Dec 26	5044 days

1978-26 FY	[14458]				2004 Jul 8.94	99.07	102.58	7259	830	932	0.007	236

D	1978-26 FZ	[14459]	1990 Oct 8	4600 days

1978-26 GA	[14460]				2004 Jul 8.75	98.83	106.22	7430	859	1244	0.026	267

1978-26 GB	[14461]				2004 Jul 8.32	99.24	101.88	7227	772	924	0.010	121

D	1978-26 GC	[14462]	1988 May 5	3714 days

1978-26 GD	[14463]				2004 Jul 8.93	98.67	102.50	7255	777	976	0.014	235

1978-26 GE	[14464]				2004 Jul 8.84	98.87	103.43	7299	876	965	0.006	305

1978-26 GF	[14465]				2004 Jul 8.78	98.87	103.12	7285	808	1004	0.013	321

1978-26 GG	[14559]				2004 Jul 8.35	99.02	100.00	7137	700	817	0.008	39

1978-26 GH	[14908]				2004 Jul 8.71	98.74	103.02	7280	821	981	0.011	174

1978-26 GJ	[14909]				2004 Jul 8.76	97.74	104.23	7337	833	1083	0.018	194

1978-26 GK	[14910]				2004 Jul 8.74	98.99	101.87	7225	834	859	0.002	245

D	1978-26 GL	[14911]	2002 Apr 15	8807 days		2002 Apr 11.44	99.00	92.13	6758	360	398	0.003	262

D	1978-26 GM	[14912]	2004 Oct 1	9707 days		2004 Jul 9.24	98.90	93.75	6836	449	466	0.001	117

1978-26 GN	[14913]				2004 Jul 8.78	98.72	101.45	7206	752	903	0.010	17

1978-26 GP	[14914]				2004 Jul 9.07	98.59	100.68	7170	757	825	0.005	281

D	1978-26 GQ	[14915]	2001 Jan 23	8360 days

D	1978-26 GR	[15778]	2001 Sep 9	8589 days		2001 Sep 6.63	98.74	89.37	6622	233	253	0.002	247

1978-26 GS	[15779]				2004 Jul 8.18	98.96	96.55	6972	573	614	0.003	358

1978-26 GT	[15788]				2004 Jul 9.13	98.84	103.97	7325	851	1041	0.013	97

1978-26 GU	[17027]				2004 Jul 8.72	98.30	98.10	7046	650	685	0.002	67

D	1978-26 GV	[17763]	1991 May 26	4830 days

D	1978-26 GW	[17764]	1989 Jun 5	4110 days

1978-26 GX	[17765]				2004 Jul 8.41	99.33	103.12	7285	875	937	0.004	309

D	1978-26 GY	[17766]	1991 Sep 6	4933 days

D	1978-26 GZ	[17767]	1989 Aug 12	4178 days

1978-26 HA	[17768]				2004 Jul 7.06	98.63	100.35	7154	715	835	0.008	295

D	1978-26 HB	[17769]	2000 May 18	8110 days

D	1978-26 HC	[18301]	1988 Oct 2	3864 days

1978-26 HD	[18302]				2004 Jul 8.41	98.76	104.70	7359	797	1163	0.025	21

1978-26 HE	[18467]				2004 Jul 4.53	98.78	101.37	7202	752	895	0.010	215

1978-26 HF	[18469]				2004 Jul 7.61	99.31	103.15	7286	874	941	0.005	293

D	1978-26 HG	[18679]	1991 Mar 22	4765 days

1978-26 HH	[18775]				2004 Jul 7.83	98.92	103.22	7289	863	958	0.006	266

1978-26 HJ	[18779]				2004 Jul 8.35	99.02	102.42	7252	799	947	0.010	162

D	1978-26 HK	[18814]	1989 Nov 11	4269 days

Re-assigned 2011 Jun to 1986 19 UP

D	1978-26 HL	[19319]	2002 Mar 16	8777 days		2002 Mar 12.34	98.40	91.47	6725	335	357	0.002	252

1978-26 HM	[19359]

Re-assigned 2011 Jun from 1963 14 EM

1978-26 HN	[19594]				2004 Jul 8.72	98.86	103.30	7293	799	1030	0.016	104

D	1978-26 HP	[19953]	2004 Nov 26	9765 days		2004 Jul 9.82	98.24	98.05	6851	467	478	0.0008	90

D	1978-26 HQ	[19967]	1993 Nov 26	5745 days

1978-26 HR	[20008]				2004 Jul 5.17	98.86	104.15	7333	800	1110	0.021	182

1978-26 HS	[20029]				2004 Jul 10.03	98.64	100.50	7161	733	831	0.007	95

D	1978-26 HT	[20047]	1999 Apr 11	7707 days

D	1978-26 HU	[26614]	1999 Apr 12	7708 days

Re-assigned 2011 May 23 from 1978 26 HV

1978-26 HV	[26861]				2011 May 23.30	98.49	100.88	7179	726	874	0.010	304

Assigned 2011 May 23

1978-26 HW	[37635]				2011 Jun 4.62	99.15	101.83	7224	801	889	0.006	169

1978-26 HX	[37636]				2011 Jun 10.04	99.93	102.82	7270	858	925	0.005	193

1978-26 HY	[37637]				2011 Jun 5.06	99.05	103.45	7300	866	977	0.008	165

1978-26 HZ	[37638]				2011 Jun 19.25	99.14	102.50	7255	830	923	0.006	11

1978-26 JA	[37639]				2011 Jun 7.96	98.77	104.20	7335	870	1044	0.012	90

1978-26 JB	[37640]				2011 May 16.64	99.00	102.00	7232	819	887	0.005	166

1978-26 JC	[37641]				2011 Jun 2.85	98.46	101.25	7197	761	875	0.008	238

1978-26 JD	[37642]				2011 Jun 8.67	98.12	97.95	7039	616	706	0.006	61

1978-26 JE	[37643]				2011 May 16.79	98.47	101.15	7192	779	847	0.005	53

1978-26 JF	[37644]				2011 Jun 2.25	99.03	101.93	7228	809	891	0.006	137

1978-26 JG	[37645]				2011 Jun 10.12	98.63	99.22	7099	685	757	0.005	237

1978-26 JH	[37646]				2011 Jun 5.31	98.95	102.83	7271	817	968	0.010	347

1978-26 JJ	[37647]				2011 Jun 11.53	98.82	105.57	7399	835	1205	0.025	23

1978-26 JK	[37648]				2011 May 24.33	98.50	100.88	7173	726	875	0.010	295

1978-26 JL	[37649]				2011 May 28.52	99.08	103.78	7316	896	978	0.006	211

1978-26 JM	[37650]				2011 Jun 6.01	99.05	98.68	7075	652	740	0.006	0

1978-26 JN	[37651]					2011 Jun 4.76	99.22	101.53	7210	801	862	0.004	308

1978-26 JP	[37652]				2011 Jun 5.98	98.68	101.88	7227	827	859	0.003	353

1978-26 JQ	[37653]				2011 May 21.24	98.70	102.60	7260	857	907	0.003	257

1978-26 JR	[37654]				2011 Jun 9.37	98.51	100.60	7166	705	869	0.011	32

1978-26 JS	[37655]				2011 May 23.85	98.65	102.47	7254	872	878	0.0004	273

1978-26 JT	[37656]				2011 May 19.86	98.61	102.23	7243	849	879	0.002	86

1978-26 JU	[37657]				2011 May 23.26	98.44	101.17	7192	794	833	0.003	187

1978-26 JV	[37658]				2011 Jun 7.75	99.15	103.20	7288	860	959	0.007	235

1978-26 JW	[37659]				2011 May 17.21	98.75	104.92	7369	875	1106	0.016	197

1978-26 JX	[37660]				2011 May 31.25	98.42	101.13	7191	797	827	0.002	180

1978-26 JY	[37661]				2011 Jun 4.64	98.93	108.20	7522	891	1396	0.034	64

1978-26 JZ	[37662]				2011 May 17.29	98.61	102.00	7232	827	880	0.004	271

1978-26 KA	[37663]				2011 May 17.23	98.56	101.68	7217	809	867	0.004	50

1978-26 KB	[37664]				2011 May 13.23	98.77	103.77	7315	880	993	0.008	151

1978-26 KC	[37665]				2011 May 28.40	99.21	101.42	7205	798	854	0.004	31

1978-26 KD	[37666]				2011 May 30.81	98.58	101.82	7223	816	873	0.004	187

1978-26 KE	[37667]				2011 Jun 4.30	98.16	99.57	7116	701	774	0.005	321

1978-26 KF	[37668]				2011 Jun 5.96	98.61	101.97	7231	822	882	0.004	132

1978-26 KG	[37669]				2011 Jun 8.47	98.70	102.57	7259	872	888	0.001	283

1978-26 KH	[37670]				2011 Jun 6.97	98.92	103.85	7319	889	992	0.007	247

1978-26 KJ	[37671]				2011 Jun 10.83	98.48	101.37	7202	800	846	0.003	221

1978-26 KK	[37672]				2011 Jun 5.47	98.62	102.13	7238	842	878	0.002	330

1978 26 KL	[44568]				2019 Oct 1.44	98.93	96.83	6985	587	627	0.003	327

Cosmos 1001 fragments; 4 pieces, all have decayed.

D	1978-36 C	[10804]	1978 Jun 1	58 days

D	1978-36 D	[10805]	1978 May 2	28 days

D	1978-36 E	[10806]	1978 Apr 25	21 days

D	1978-36 F	[10810]	1978 May 23	49 days

DMSP B5D1-3 fragments; 3 pieces, all have decayed

D	1978-42 C	[10854]	1992 Mar 6	5058 days

D	1978-42 D	[10913]	1986 May 1	2922 days

D	1978-42 E	[10914]	1989 Jun 16	4064 days		1989 Jun 14.66	98.54	91.07	6705	314	340	0.002	194

Cosmos 1004 fragments; 4 pieces, all have decayed

Analyses indicate that the Soyuz 3rd stage is the most likely debris source.

D	1978-43 C	[10848]	1978 May 9	4 days

D	1978-43 D	[10849] 	1978 May 9	4 days

D	1978-43 E	[10850]	1978 May 14	9 days

D	1978-43 F	[10851]	1978 Jun 8	34 days

Cosmos 1008 fragments; 4 pieces, all have decayed.

D	1978-49 C	[10900]	1978 Dec 17	224 days

D	1978-49 D	[10901]	1978 Dec 30	237 days

D	1978-49 E	[10902]	1978 Jul 17	61 days

D	1978-49 F	[10903]	1978 Sep 12	128 days

Seasat 1 fragments; 18 pieces, 14 have decayed

First anomalous event occurred 1983 July. Second event observed February 1985. Later events also detected. Most debris experience very rapid decay for this altitude.

D	1978-64 B	[14244]	1988 Oct 30	3047 days

D	1978-64 C	[18617]	1988 Mar 25	3559 days

D	1978-64 D	[18649]	1988 Mar 1	3535 days

D	1978-64 E	[18996]	1988 Aug 10	3697 days

D	1978-64 F	[19103]	1988 Jun 11	3637 days

D	1978-64 G	[23905]	1998 Aug 20	7359 days		1996 Jun 8.97	108.02	99.31	7104	715	736	0.002	164

D	1978-64 H	[23930]	1998 Aug 2	7341 days		1996 Jun 19.57	108.00	99.36	7106	717	739	0.002	166

D	1978-64 J	[25055]	1999 Jun 3	7646 days		1997 Nov 14.15	108.00	99.54	7115	731	742	0.0008	122

D	1978-64 K	[26963]	2001 Nov 30	8557 days		2001 Nov 22.57	108.00	94.87	6890	488	535	0.003	140

D	1978-64 L	[27637]	2002 Dec 31	8953 days

D	1978-64 M	[27889]	2006 Mar 28	10136 days		2004 Jul 6.95	108.00	98.52	7067	674	702	0.002	335

2006 Mar 28.76	107.93	89.70	6638	248	272	0.002	342

D	1978-64 N	[27956]	2003 Oct 3	9229 days

D	1978-64 P	[28146]	2001 Mar 14	9392 days

D	1978-64 Q	[28843]	2006 Sep 8	10300 days		2005 Sep 10.19	108.03	98.67	7073	654	736	0.006	185

2006 Sep 7.45	107.91	91.65	6734	338	372	0.003	325

1978-64 R	[31408]				2007 May 16.01	108.00	99.57	7116	699	777	0.005	137

1978 64 S	[32482]				2008 Jun 5.17	108.02	99.08	7093	614	815	0.014	192

1978 64 T	[43443]				2017 Apr 3.77	107.97	99.17	7098	689	749	0.004	206

1978 64 U	[43444]				2017 Mar 30.70	107.93	98.92	7085	637	776	0.010	309

1978 64 V	[49947]				2021 Dec 8.45	108.05	95.18	6906	508	547	0.003	353

1978 64 W	[49948]				2021 Dec 8.34	108.05	98.67	7073	677	712	0.002	227

Cosmos 1030 fragments; 13 pieces,  2 have decayed

Cosmos 1030 was another spacecraft of the Cosmos 862-type to experience a fragmentation 1978 Oct 10. After entering a Molniya-type transfer orbit on 6 September, Cosmos 1030 maneuvered about 14 September to enter an operational orbit. Elements on the first identifiable fragment did not appear until a year after the event. Official cataloguing of debris did not begin until three years after the event.

1978-83 E	[12907]				2004 Jul 6.55	67.56	718.98	26585	3385	37028	0.633	161

1978-83 F	[12919]				1983 Jul 26.61	63.96	719.57	26600	3020	37422	0.647	324

1978-83 G	[13959]				1993 Jul 12.01	63.72	721.77	26654	2948	37602	0.650	328

1978-83 H	[26915]				2004 Feb 23.67	62.50	717.83	26557	543	39814	0.739	190

D	1978-83 J	[27891]	2004 Apr 30	9368 days

1978-83 K	[27892]				2004 Jul 3.33	64.46	717.38	26546	1193	39142	0.715	177

D	1978-83 L	[28401]	2004 Aug 20	9480 days		2004 Aug 18.77	61.62	107.87	7506	123	2132	0.134	204

1978-83 M	[32969]				2008 Jun 7.46	66.38	709.08	26341	4481	35444	0.588	132

1978-83 N

1978-83 P

Fragments N and P were re-assigned to 1982 95 D and E

1978-83 Q	[32972]				2008 May 21.27	71.36	725.95	26757	6512	34245	0.518	146

1978-83 R	[32973]				2008 Jun 1.98	68.40	671.08	25391	3965	34060	0.593	120

1978-83 S	[32974]				2008 Jun 4.49	66.69	721.43	26646	3489	37045	0.630	142

1978 83 T	[39447]				2015 Feb 26.79	68.46	718.92	26584	5995	34415	0.535	69

Tiros 11 (Nimbus 7)fragments; 7 pieces, 5 have decayed

Both fragments  (D and E) from the first anomalous event, Sep 1987,  decayed rapidly during winter of 1988-89. A second event associated with 1978-096A occurred on 23 Feb 96 liberating 1 piece. (F)

Nimbus 7 R/B is designated Cameo in US Space Command Satellite Catalog in reference to scientific piggy-back payload attached to the Delta second stage. This satellite experienced an anomalous event prior to and after the event. Most fragments decayed very rapidly, preventing an accurate assessment of the event and its resulting debris cloud. No new objects were cataloged as a result of this event. The first event apparently occurred prior to 1981 Dec 26 0700 GMT. The second anomalous event apparently occurred about Jan 1987.

1978-96 B	[11061]				2004 Jul 5.58	98.90	98.32	7057	677	680	0.0003	109

1978-96 C	[11062]				2004 Jul 6.16	98.90	98.22	7052	671	676	0.0003	106

D	1978-96 D	[18532]	1988 Oct 20	3660 days

D	1978-96 E	[18786]	1989 Feb 25	3787 days

D	1978-96 F	[23935]	1999 Dec 18	7736 days		1996 Jun 26.71	98.89	101.29	7198	809	831	0.002	11

D	1978-96 G	[24639]	1998 Aug 11	7242 days		1996 Oct 24.10	98.88	101.28	7198	810	829	0.001	348

D	1978-96 H	[28267]	2005 May 9	9705 days		2004 Jul 6.38	98.44	100.88	7179	781	820	0.003	49

Cosmos 1045 2nd stage fragments; 42 pieces, 9 have decayed

This flight, which successfully carried three separate payloads, was the fifth orbital mission of the Tsyklon third stage. Propellants used were N2O4 and UDMH. Nearly 10 years elapsed from launch to break-up 1988 May 9 at 12:18 UT near 29ºS 126ºE. A second Tsyklon third stage breakup occurred after a similar length of time; see 1987-068B.

D	1978-100 E	[11177]	1989 Feb 2 A	3752 days

1978-100 F	[19133]				2004 Jul 8.09	82.39	116.60	7907	1481	1575	0.006	356

1978-100 G	[19134]				2004 Jul 7.50	82.35	115.62	7862	1365	1600	0.015	207

D	1978-100 H	[19135]	2013 Jun 14	12650 days		2004 Jul 8.25	82.26	109.03	7561	986	1378	0.026	15

2013 Jun 14.03	82.14	91.53	6728	305	394	0.007	207

1978-100 J	[19136]				2004 Jul 7.71	82.41	111.75	7686	971	1643	0.044	144

1978-100 K	[19137]				2004 Jul 7.57	82.31	116.65	7909	1462	1599	0.009	256

1978-100 L	[19138]				2004 Jul 7.73	82.33	117.23	7935	1419	1694	0.017	201

1978-100 M	[19139]				2004 Jul 7.17	82.14	123.07	8196	1699	1935	0.014	278

1978-100 N	[19142]				2004 Jul 8.09	82.27	105.35	7389	914	1107	0.013	233

1978-100 P	[19143]				2004 Jul 7.42	81.67	113.88	7783	1144	1665	0.033	347

1978-100 Q	[19144]				2004 Jul 7.89	82.62	121.12	8110	1693	1769	0.005	79

1978-100 R	[19174]				2004 Jul 7.98	81.91	117.90	7965	1466	1707	0.015	129

1978-100 S	[19175]				2004 Jul 7.63	82.41	114.07	7792	1337	1489	0.010	42

1978-100 T	[19176]				2004 Jul 6.14	82.09	120.55	8084	1572	1839	0.017	52

1978-100 U	[19178]				2004 Jul 7.86	82.13	118.75	8004	1598	1652	0.003	221

1978-100 V	[19226]				2004 Jul 8.08	82.53	120.13	8065	1648	1725	0.005	129

1978-100 W	[19227]				2004 Jul 7.22	82.15	114.70	7821	1163	1721	0.036	336

1978-100 X	[19228]				2004 Jul 8.28	82.45	114.33	7804	1276	1574	0.019	182

1978-100 Y	[19229]				2004 Jul 9.76	82.33	113.97	7787	1247	1569	0.021	159

1978-100 Z	[19230]				2004 Jul 10.20	82.53	120.15	8066	1673	1702	0.002	112

D	1978-100 AA	[19231]	2013 Jun 22	12658 days		2004 Jul 10.17	82.03	119.33	7574	1046	1346	0.020	341

2013 Jun 21.91	81.79	92.98	6799	393	447	0.004	316

1978-100 AB	[19232]				2004 Jul 10.40	82.35	123.22	8209	1671	1990	0.019	254

1978-100 AC	[19233]				2004 Jul 10.13	82.57	119.52	8038	1628	1690	0.004	353

1978-100 AD	[19234]				2004 Jul 8.74	82.42	122.12	8154	1688	1862	0.011	339

1978-100 AE	[19295]				2004 Jul 9.51	81.96	119.62	8042	1252	2075	0.051	183

D	1978-100 AF	[19352]	1992 Mar 29	4903 days

D	1978-100 AG	[19364]	1992 Jun 26	4992 days

1978-100 AH	[19450]				2004 Jul 9.56	82.55	120.20	8068	1677	1703	0.002	118

D	1978-100 AJ	[19578]	1993 May 23	5323 days

D	1978-100 AK	[19579]	1999 Nov 28	7703 days

1978-100 AL	[19580]				2004 Jul 8.19	82.65	114.72	7821	1196	1689	0.032	137

1978-100 AM	[19646]				2004 Jul 7.94	82.16	114.13	7794	1222	1609	0.025	52

D	1978-100 AN	[19830]	2000 Dec 20	8091 days

D	1978-100 AP	[20010]	2012 Nov 5	12429 days		2004 Jul 10.01	82.25	114.46	7568	951	1428	0.032	49

2012 Nov 4.89	82.17	92.20	6761	357	408	0.004	136

1978-100 AQ	[20016]				2004 Jul 4.67	82.48	117.58	7951	1154	1990	0.053	25

Fragments AR-AX were 2006 Apr reassigned to 1980-80; fragments AY-BD were renumbered AR-AW

1978-100 AR	[21913]				2004 Jul 10.20	82.54	120.15	8066	1669	1707	0.002	86

1978-100 AS	[21997]				2004 Jul 10.53	82.39	116.25	7890	983	2041	0.067	85

1978-100 AT	[25831]				2001 Apr 4.31	82.56	120.27	8072	1684	1702	0.001	331

1978-100 AU	[25832]				2004 Jul 8.17	82.54	120.25	8071	1682	1702	0.001	125

1978-100 AV	[25833]				2004 Jul 9.33	82.22	112.27	7709	1180	1481	0.020	170

1978-100 AW	[25834]				2004 Jul 9.27	82.24	112.47	7719	1181	1499	0.021	110

1978-100 AX	[29065]				2006 Apr 21.32	82.54	120.17	8067	1672	1704	0.002	243

Cosmos 1065 fragments; 6 pieces, all have decayed

Analyses indicate that the Cosmos 1065 payload is the most likely debris source.

D	1978-120 C	[11243]	1979 Mar 1	69 days

D	1978-120 D	[11244]	1979 Mar 2	70 days

D	1978-120 E	[11248]	1979 Mar 3	71 days

D	1978-120 F	[11249]	1979 Mar 1	69 days

D	1978-120 G	[11424]	1979 Jul 16	206 days

D	1978-120 H	[11426]	1979 Aug 5	226 days