Cosmos 1428	1983-01 A	1983 Jan 12.58	Cvlinder	2.1 long	1983 Jan 14.5	82.91	104.74	7360	957	1006	0.003	283

[Kosmos 11K65M 	[13757]	l200 years	810	2.0 dia	2004 Jul 7.28	82.91	104.60	7354	950	1001	0.003	336

65093-479]	PLE

Cosmos 1428	1983-01 B	1983 Jan 12.58	Cylinder	7.4 long	1933 Jan 14.1	82.91	104.63	7355	957	996	0.003	279

2nd stage	[13758]	600 years	2200?	2.4 dia	2004 Jul 7.70	82.91	104.47	7348	950	989	0.003	280

Fraqment	1983-01 C	[14568]			2004 Jul 7.22	82.89	102.15	7239	846	874	0.002	111

Cosmos 1429 *	1983-02 A	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 19.9	74.02	115.87	7873	1468	1521	0.003	259

[Kosmos 11K65M 	[13761]	10000 years	40?	0.8 dia?	2004 Jul 6.84	74.02	115.80	7871	1466	1518	0.003	148

53793-481]	PLE

Cosmos 1430 *	1983-02 B	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 21.6	74.02	115.65	7863	1468	1501	0.002	263

[13762]	10000 years	40?	0.8 dia?	2004 Jul 6.70	74.02	115.60	7861	1467	1498	0.002	106

Cosmos 1431 *	1983-02 C	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 21.6	74.02	115.47	7855	1467	1486	0.001	233

[13763]	10000 years	40?	0.8 dia?	2004 Jul 7.56	74.02	115.42	7852	1465	1483	0.001	27

Cosmos 1432 *	1983-02 D	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 19.7	74.02	115.27	7845	1465	1469	0	146

[13764]	10000 years	40?	0.8 dia?	2004 Jul 6.91	74.02	115.22	7844	1462	1468	0.0003	248

Cosmos 1433 *	1983-02 E	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 20.7	74.02	115.08	7837	1448	1469	0.001	1ll

[13765]	9000 years	40?	0.8 dia?	2004 Jul 6.97	74.02	115.02	7835	1445	1467	0.001	173

Cosmos 1434 *	1983-02 F	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 19.7	74.02	114.91	7829	1433	1469	0.002	103

[13766]	8000 years	40?	0.8 dia?	2004 Jul 6.94	74.02	114.85	7827	1430	1467	0.002	124

Cosmos 1435 *	1983-02 G	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 21.1	74.02	114.74	7821	1417	1469	0.003	103

[13767]	7000 years	40?	0.8 dia?	2004 Jul 6.96	74.02	114.41	7819	1414	1467	0.003	84

Cosmos 1436 *	1983-02 H	1983 Jan 19.10	Spheroid	1.0 long?	1983 Jan 20.7	74.02	114.56	7813	1401	1468	0.004	92

[13768]	6000 years	40?	0.8 dia?	2004 Jul 6.92	74.02	114.50	7811	1398	1466	0.004	28

Cosmos 1429-1436	1983-02 J	1983 Jan 19.10	Cylinder	7.4 long	1983 Jan 21.0	74.00	117.97	7967	1471	1707	0.015	272

rocket	[13769]	20000 years	2200?	2.4 dia	2004 Jul 7.93	74.01	117.90	7965	1478	1695	0.014	293

*	Strela-1M

Cosmos 1437	1983-03 A	1983 Jan 20.73	Cylinder +	5 long?	1983 Jan 23.4	81.17	97.61	7021	628	658	0.002	13

[Vostok 8A92M] 	[13770]	60 years	2 vanes?	1.5 dia?	2004 Jul 10.39	81.17	95.20	6907	514	542	0.002	52

PLE		2500?

Cosmos 1437	1983-03 B	1983 Jan 20.73	Cylinder	3.8 long	1983 Jan 22.5	81.17	97.65	7023	605	685	0.006	165

Block E 3rd stage 	[13771]	60 years	1440	2.6 dia	2004 Jul 7.97	81.16	96.00	6945	541	593	0.004	29

Fragment	1983-03 C	[35007]

IRAS*	1983-04 A	1983 Jan 26.10	Cylinder +	3.60 long	1983 Jan 26.8	99.1	103.11	7283	896	913	0.001	243

[Delta 3910	[13777]	600 years	panel	2.05 dia	2004 Jul 11.56	99.07	102.85	7272	887	900	0.0009	185

650 #166]	VDB-SLC2W		1073

IRAS	1983-04 B	1983 Jan 26.10	Cylinder +	6.4 long	1983 Jan 26.9	100.1	102.5	7254	860	892	0.002	274

Delta 2nd stage	[13778]	400 years	annulus	1.52 and	2004 Jul 7.80	100.03	102.23	7243	849	880	0.002	19

(+ PIX2)**			350?	2.44 dia

Fragments	1983-04 C #	[13783]			2004 Jul 6.55	99.02	102.67	7263	873	896	0.002	291

1983-04 D	[35394]

1983-04 E	[35395]

1983-04 F	[35396]

D	Cosmos 1438	1983-05 A	1983 Jan 27.36	Sphere~	6.5 long?	1983 Jan 27.5	70.39	88.89	6598	209	230	0.002	69

R	[Soyuz 11A511U] 	[13779]	10.9 days	cylinder	2.4 dia	1983 Jan 28.4	70.4	89.64	6633	167	344	0.013	222

BAI	1983 Feb 7.3	6300?

D	Cosmos 1438	1983-05 B	1983 Jan 27.36	Cylinder	7.5 long	1983 Jan 27.5	70.39	88.78	6592	209	219	0.001	48

Block I 3rd stage 	[13780]	3 days	2500?	2.6 dia

1983 Jan 30

D	Cosmos 1438	1983-05 F	1983 Jan 27.36	Cone	1.5 long?	1983 Feb 9.2	70.39	90.55	6681	243	363	0.009	307

engine	[13790]	17 days	600?	2 dia?

1983 Feb 13	full

D	Fragment	1983-05 C	[13787]	1983 Feb 12	16 days

D	Fragment	1983-05 D	[13788]	1983 Feb 8	12 days

D	Fragment	1983-05 E	[13789]	1983 Feb 11	15 days

*	Joint Netherlands-UK-USA Infra-Red Astronomical Satellite, launched by NASA.

**	Plasma Interaction Experiment.

#	Lens cover

Sakura 2A*	1983-06 A	1983 Feb 4.36	Cylinder	3.51 long?	1983 Feb 7.1	0.29	1444.69	42334	35145	36767	0.019	218

(CS-2A)	[13782]	> million	676 full?	2.18 dia?	2004 Jul 5.91	11.48	1448.55	42408	35997	36082	0.001	91

[Nu-2 N-10(F)]	TAN-O	years	340 empty?

D	Sakura 2A	1983-06 B	1983 Feb 4.36	Cylinder	1.74 long	1983 Feb 6.9	28.8	652.47	24930	191	36912	0.737	180

Nu-2 3rd stage	[13786]	4861 days	66?	1.65 dia

1996 May 27	empty

D	Cosmos 1439	1983-07 A	1983 Feb 6.48	Sphere-	7 long?	1983 Feb 7.5	70.36	88.71	6589	170	251	0.006	74

R	[Soyuz 11A511U] 	[13784]	16 days	cylinder	2.4 dia

BAI	1983 Feb 22	6700?

D	Cosmos 1439	1983-07 B	1983 Feb 6.48	Cylinder	7.5 long	1983 Feb 7.5	70.38	89.25	6616	167	308	0.011	64

Block I 3rd stage 	[13785]	4 days	2500?	2.6 dia

1983 Feb 10

D	Fragment	1983-07 C	[13843]	1983 Feb 22	16 days

NOSS 4	1983-08 A	1983 Feb 9.58	Cylinder	-	1983 Feb 14.3	63.43	107.76	7503	1063	1186	0.008	167

[Atlas 69F/6001H]	[13791]	1600 years	64?		2004 May 21.87	63.38	107.33	7481	649	1557	0.061	9   #

VDB-SLC3E				2020 Sep 26.79	63.30	105.93	7416	371	1704	0.090	97

2021 Jul 28.88	63.31	105.83	7412	377	1690	0.089	104

SSD**	1983-08 B	1983 Feb 9.58	Box +	0.3  x	1983 Feb 12.7	63.39	107.58	7494	1047	1184	0.009	167

(LIPS 2)	[13792]	1600 years	aerials?	0.9  x	No elements available

2.4?

Atlas H stage	1983-08 C	[13834]			No elements available

SSA**	1983-08 E	1983 Feb 9.58	Box +	0.3 x	1983 Feb 25.2	63.44	107.47	7488	1052	1168	0.008	157

[13844]	1600 years	aerials?	0.9 X	2004 May 19.92	63.38	107.35	7483	648	1560	0.061	8

2.4?

SSB**	1983-08 F	1983 Feb 9.58	Box +	0.3 x	1983 Feb 25.2	63.44	107.47	7488	1052	1168	0.008	157

[13845]	1600 years	aerials?	0.9 x	2004 Jul 3.33	63.38	107.35	7483	640	1568	0.062	14

2.4?

SSC**	1983-08 H	1983 Feb 9.58	Box +	0.3 x	1983 Mar 8.8	63.44	107.45	7488	1052	1167	0.008	205

[13874]	1600 years	aerials?	0.9 x	2004 Jul 3.32	63.38	107.35	7482	644	1564	0.061	14

2.4?

Fragment	1983-08 D	[13835]			No elements available

Fragment	1983-08 G	[13849]			No elements available

Fragment	1983-08 J	[28157]			No elements available

Fragment	1983-08 K	[31707]			No elements available

*	Japanese Communication Satellite.

**	SS is surveillance satellite.

# Orbits from amateur observations.

D	Cosmos 1440	1983-09 A	1983 Feb 10.30	Sphere-	6.5 long?	1983 Feb 12.3	82.33	89.89	6646	260	275	0.001	305

R	[Soyuz 11A511U] 	[13793]	13.9 days	cylinder	2.4 dia

PLE-LC41	1983 Feb 24.2	6300?

D	Cosmos 1440	1983-09 B	1983 Feb 10.30	Cylinder	7.5 long	1983 Feb 10.5	82.34	89.23	6613	211	258	0.004	102

Block I 3rd stage 	[13794]	5 days	2500?	2.6 dia

1983 Feb 15

D	Cosmos 1440	1983-09 C	1983 Feb 10.30	Cone	1.5 long?	1983 Mar 2.1	82.33	89.56	6630	244	260	0.001	243

engine	[13847]	33 days	600?	2 dia?

1983 Mar 15	full

D	Fragment	1983-09 D	[13848]	1983 Mar 2	20 days

D	Cosmos 1441	1983-1O A	1983 Feb 16.42	Cylinder +	5 long?	1983 Feb 18.5	81.11	97.47	7015	631	642	0.001	37

[Vostok 8A92M] 	[13818]	11588 days	2 vanes?	1.5 dia?	2004 Jul 8.31	81.08	94.63	6880	499	503	0.0003	93

PLE	2014 Nov 8	2500?		2014 Nov 8.36	81.02	87.35	6522	140	147	0.0005	238

Cosmos 1441	1983-10 B	1983 Feb 16.42	Cylinder	3.8 long	1983 Feb 18.1	81.12	97.51	7017	592	685	0.007	173

Block E 3rd stage 	[13819]	60 years	1440	2.6 dia	2004 Jul 11.56	81.11	95.77	6934	528	584	0.004	43

D	Tenma*	1983-11 A	1983 Feb  20.22	Polyhedral	0.8  long?	1983 Feb 21.4	31.49	94.38	6873	487	503	0.001	258

(ASTRO 2)	[13829]	2127 days	cylinder?	1.0  dia?

[Mu 3S M-3S-3]	KAG-M	]988 Dec  17	185?

D	Tenma	1983-11 B	1983 Feb  20.22	Sphere-	2.33 long?	1983 Feb 20.7	31.48	94.37	6873	485	504	0.001	225

4th stage	[13830]	2160 days	cone?	1.14 dia?

1989 Jan 19	230?

D	Fragments	1983-11 C	[13846]	1983 Mar 3	11 days

D	Fragments	1983-11 D	[14566]	1987 Aug 31	1653 days

D	Fragments	1983-11 E	[14567]	1984 Oct 8	596 days

D	Cosmos 1442	1983-12 A	1983 Feb 25.53	Sphere-	7 long?	1983 Feb 27.1	67.16	89.87	6647	170	367	0.015	69

R	[Soyuz 11A511U] 	[13850]	45 days	cylinder	2.4 dia

PLE-LC41/1	1983 Apr 11	6700?

D	Cosmos 1442	1983-12 B	1983 Feb 25.53	Cylinder	7.5 long	1983 Feb 27.5	67.14	88.97	6603	163	287	0.009	68

Block I 3rd stage 	[13851]	4 days	2500?	2.6 dia

1983 Mar 1

*	Japanese satellite; Tenma means Pegasus.

D	Cosmos 1443*	1983-13 A	1983 Mar 2.40	Cone-	13 long	1983 Mar 4.2	51.64	88.94	6603	191	259	0.005	83

r	[Proton 8K82K 	[13868]	201 days	cylinder +	4.0 dia

309-02]	BAI-LC200L	1983 Sep 19	2 wings	16.0 span

20000

D	Cosmos 1443	1983-13 B	1983 Mar 2.40	Cylinder	6.5 long?	1983 Mar 2.5	51.65	88.66	6589	192	230	0.003	78

third stage	[13869]	3 days		4 dia

1983 Mar 5

D	Cosmos 1343	1983-13 E	1983 Mar 2.40

Capsule	[NNA]	173 days

1983 Aug 22

D	Fragment	1983-13 C	[13872]

D	Fragment	1983-13 D	[14305]

D	Cosmos 1444	1983-14 A	1983 Mar 2.45	Sphere-	6.5 long?	1983 Mar 4.7	72.84	92.31	6765	358	416	0.004	209

R	[Soyuz 11A511U] 	[13870]	13.8 days	cylinder	2.4 dia

PLE	1983 Mar 16.2	6300?

D	Cosmos 1444	1983-14 B	1983 Mar 2.45	Cylinder	7.5 long	1983 Mar 2.9	72.85	90.16	6660	190	373	0.014	87

rocket	[13871]	9 days	2500?	2.6 dia

1983 Mar 11

D	Cosmos 1444	1983-14 F	1983 Mar 2.45	Cone	1.5 long?	1983 Mar 20.1	72.85	92.27	6763	356	414	0.004	176

engine	[13894]	339 days	600?	2 dia?

1984 Feb 4	full

D	Fragment	1983-14 C	[13891]	1983 Mar 16	14 days

D	Fragment	1983-14 D	[13892]	1983 Apr 20	49 days

D	Fragment	1983-14 E	[13893]	1983 May 26	85 days

Molniya-3 20	1983-15 A	1983 Mar 11.65	Windmill +	4.2 long?	1983 Mar 11.7	62.83	735.26	26986	419	40796	0.748	280

[Molniya 8K78M/ML]	[13875]	100 years?	6 vanes	1.6 dia	1983 Apr 10.7	62.85	717.82	26557	439	39918	0.743	280

PLE-LC41/1		1500?		2004 Jul 6.69	62.19	718.22	26566	653	39722	0.735	275

D	Molniya-3 20	1983-15 B	1983 Mar 11.65	Irregular	-	1983 Mar 12.9	62.83	90.99	6702	196	452	0.019	123

Block I 3rd stage 	[13876]	16 days

1983 Mar 27

D	Molniya-3 20	1983-15 C	1983 Mar 11.65	Cylinder	7.5 long	1983 Mar 13.0	62.85	91.02	6704	210	441	0.017	129

4th stage casing 	[13877]	21 days	2500?	2.6 dia

1983 Apr 1

*	Cosmos 1443 docked  with Salyut 7 on 1983 Mar 10.39 and separated from Salyut 7 on 1983 Aug 14

Cosmos 1443 was later de-orbited	over the Pacific.

D	Molniya-3 20	1983-15 D	1983 Mar 11.65

Ullage motor 	[13881]	15 days

1983 Mar 26

Molniya-3 20	1983-15 E	1983 Mar 11.65	Cylinder	2.0 long	1983 Mar 13.7	62.84	732.04	26907	422	40636	0.747	280

Block L 4th stage 	[13882]	100 years?	440	2.0 dia	2004 Jul 5.88	62.01	731.97	26904	1085	39967	0.723	272

Ekran 10	1983-16 A	1983 Mar 12.59	Cylinder	-	1983 Mar 17.2	0.13	1427.46	41997	35613	35625	0	31

[Proton 8K82K 	[13878]	> million	+ plate		1983 Apr 7.2	0.16	1436.04	42166	35778	35798	0.0002	234

304-02/11S86 34L]	BAI-LC200P	years	2000?		2004 Jul 9.70	14.90	1465.30	43701	37192	37454	0.003	181

D	Ekran 10	1983-16 B	1983 Mar 12.59	Cylinder	5.5 long?	1983 Mar 12.8	51.62	88.21	6567	184	194	0.001	257

third stage	[13879]	2 days		4 dia

1983 Mar 14

D	Ekran 10	1983-16 C	1983 Mar 12.59	Irregular	-	1983 Mar 12.8	51.6	88.29	6571	186	200	0.001	36

4th stage casing 	[13880]	1 day

1983 Mar 13

D	Ekran 10	1983-16 D	1983 Mar 12.59

Ullage motor	[13884]	2042 days

1988 Oct 13

D	Ekran 10	1983-16 E	1983 Mar 12.59

Ullage motor	[13885]	1116 days

1986 Apr 1

Ekran 10	1983-16 F	1983 Mar 12.59	Cylinder	5.5 long	1983 May 23.5	0.18	1424.37	41935	35487	35626	0.002	235

Block DM 4th stage 	[14086]	> million	17300 full	4.0 dia	2004 Jul 6.65	13.32	1424.33	41934	35484	35627	0.002	94

years

D	Cosmos 1445*	1983-17 A	1983 Mar 15.94	Delta wing	2.5 long?	1983     Mar 16.0	50.69	88.36	6575	176	217	0.003	315

R	[Kosmos 65 MP]	[13883]	0.08 day?	with fins	2.1 span?

KY-LC107	1983 Mar 16.02?	1000?

D	Cosmos 1445	1983-17 B	1983 Mar 15.94	Cylinder	7.4 long?	1983 Mar 16.5	50.69	88.3	6572	172	215	0.003	318

2nd stage	[13888]	2 days	2200?	2.4 dia?

1983 Mar 17

D	Fragment	1983-17 C	[13889]	1983 Mar 18	3 days

*	Test of subscale spaceplane, similar to Cosmos 1374. Launched from Kapustin Yar, water recovery 1.25 orbit	s later about 556 km south of

Cocos Islands (Indian Ocean).

D	Cosmos 1446	1983-18 A	1983 Mar 16.37	Sphere-	6.5 long?	1983 Mar 18.6	69.94	89.14	6610	222	242	0.001	83

R	[Soyuz 11A511U2] 	[13886]	13.9 days	cylinder	2.4 dia

BAI	1983 Mar 30.3	6300?

D	Cosmos 1446	1983-18 B	1983 Mar 16.37	Cylinder	7.5 long	1983 Mar 18.7	69.95	90.02	6653	223	327	0.008	53

rocket	[13887]	13 days	2500?	2.6 dia

1983 Mar 29

D	Cosmos 1446	1983-18 C	1983 Mar 16.37	Cone	1.5 long?	1983 Mar 30.3	69.96	88.86	6596	199	237	0.003	104

engine	[13951]	19 days	600?	2 dia?

1983 Apr 4	full

D	Fragments	1983-18 D	[13952]	1983 Mar 30	14 days

D	Fragments	1983-18 E	[13953]	1983 Mar 31	15 days

Molniya-1 56	1983-19 A	1983 Mar 16.76	Windmill	3.4 long	1983 Mar 18.3	62.81	736.53	27017	453	40825	0.747	280

[Molniya 8K78M/ML]	[13890]	100 years?	+ 6 vanes	1.6 dia	1983 Mar 29.9	62.80	717.73	26554	451	39902	0.743	280

PLE		1000?		2004 Jul 6.88	62.43	720.60	26625	1186	39307	0.716	273

D	Molniya-1 56	1983-19 B	1983 Mar 16.76	Cylinder	7.5 long	1983 Mar 18.7	62.82	91.04	6705	207	446	0.018	130

Block I 3rd stage 	[13895]	19 days	2500?	2.6 dia

1983 Apr 4

D	Molniya-1 56	1983-19 C	1983 Mar 16.76	Irregular	-	1983 Mar 18.3	62.82	91.05	6705	191	463	0.02	122

4th stage casing 	[13896]	15 days

1983 Mar 31

Molniya-1 56	1983-19 D	1983 Mar 16.76	Cylinder	2.0 long	1983 Mar 17.8	62.81	731.25	26888	382	40637	0.749	280

Block L 4th stage 	[13897]	100 years?	440	2.0 dia	2004 Jul 4.07	62.39	732.43	26916	1411	39664	0.711	274

D	Molniya-1 56	1983-19 E	1983 Mar 16.76

Ullage motor 	[13898]	15 days

1983 Mar 31

Astron 1*	1983-20 A	1983 Mar 23.53	Cylinder +	2.7 long?	1983 Mar 23.5	51.09	5879.2	107913	1950	201120	0.923	299

[Proton 8K82K 	[13901]	100 years?	2 panels?	2.3 dia?	2004 Jul 1.17	19.38	5936.90	108609	22807	181654	0.731	164

307-01/11S824M 7L]	BAI-LC200L		3250?	5.7 span?

D	Astron 1 ##	1983-20 B	1983 Mar 23.53

Ullage motor 	[13902]	818 days

1985 Jun 18

D	Astron 1	1983-20 C	1983 Mar 23.53

Ullage motor 	[13903]	866 days

1985 Aug 5

Astron 1	1983-20 D	1983 Mar 23.53	Cylinder	5.5 long		Orbit similar to 1983-20 A

Block DM 4th stage 	[20413]	100 years?	17300 full	4.0 dia	2004 Jul 9.42	18.98	5822.53	107210	20516	181147	0.749	158

Cosmos 1447	1983-21 A	1983 Mar 24.87	Cylinder	2.1 long	1983 Mar 26.5	82.95	104.88	7366	961	1015	0.004	290

(Cospas 2**)	[13916]	1200 years	810	2.0 dia	2004 Jul 11.48	82.94	104.73	7361	955	1009	0.004	218

[Kosmos 11K65M	PLE

53739-548]

Cosmos 1447	1983-21 B	1983 Mar 24.87	Cylinder	7.4 long	1983 Mar 25.3	82.95	104.76	7360	960	1004	0.003	293

2nd stage	[13917]	600 years	2200?	2.4 dia	2004 Jul 9.82	82.94	104.60	7355	955	997	0.003	146

NOAA 8 #	1983-22 A	1983 Mar 28.66	Box +	3.71 long?	1983 Mar 30.1	98.75	101.3	7197	808	830	0.002	258

[Atlas 73E]	[13923]	120 years	panel?	1.88 dia?	2004 Jul 7.97	98.74	100.87	7178	788	811	0.002	347

VDB-SLC3W		1712

D	NOAA 8	1983-22 B	1983 Mar 28.66			1991 Oct 12.23	98.48	90.48	6677	283	314	0.002	310

Star-37S AKM	[13924]	3120 days

1991 Oct 12

D	Fragments	1983-22 C-N	11 pieces, 8 have decayed		For orbital information see extra pages at the end of the year

*	Astrophysical observatory carrying Soviet UV telescope and French	X-ray spectrometers, to study	galactic r	adiation	sources.

**	Cosmos satellite for programme of air and sea rescue.

#	Includes SARSAT - Search And Rescue Satellite Aided tracking. Joint project with Cospas. NOAA 8 fragmented 1985 Dec 30.42.

##	Parent satellite was one of two small engine units which are routinely released after the first burn of the Proton fourth stage. The nature of these objects was identified by Dr. Boris V. Cherniatiev, Deputy Constructor for the Energiya NPO, in October 1992. The cause of this fragmentation, 1984 Sep 3 at 20:23 UT near 12ºS 352ºE, is assumed to be related to the residual hypergolic propellants on board and failure of the membrane separating the fuel and oxidizer. Element sets on 16 fragments were developed. None were officially cataloged. This was the first in a series of fragmentations of this object type.

Cosmos 1448	1983-23 A	1983 Mar 30.05	Cylinder	2.1 long	1983 Mar 31.3	82.96	104.81	7362	963	1006	0.003	283

[Kosmos 11K65M 	[13949]	1200 years	810	2.0 dia	2004 Jul 6.65	82.96	104.67	7358	958	1000	0.003	200

65019-522]	PLE

Cosmos 1448	1983-23 B	1983 Mar 30.05	Cylinder	7.4 long	1983 Apr 1.2	82.96	104.70	7357	963	995	0.002	276

2nd stage	[13950]	600 years	2200?	2.4 dia	2004 Jul 7.76	82.95	104.60	7355	949	1003	0.004	172

D	Cosmos 1449	1983-24 A	1983 Mar 31.45	Sphere-	6.5 long?	1983 Apr 2.4	72.87	92.30	6765	357	416	0.004	209

R	[Soyuz 11A511U] 	[13955]	14.8 days	cylinder	2.4 dia

PLE	1983 Apr 15.2	6300?

D	Cosmos 1449	1983-24 B	1983 Mar 31.45	Cylinder	7.5 long	1983 Apr 1.1	72.87	90.11	6657	195	363	0.013	84

Block I 3rd stage 	[13956]	9 days	2500?	2.6 dia

1983 Apr 9

D	Cosmos 1449	1983-24 G	1983 Mar 31.45	Cone	1.5 long?	1983 Apr 15.7	72.87	92.28	6764	357	414	0.004	181

engine	[13995]	360 days	600?	2 dia?

1984 Mar 25	full

D	Fragments	1983-24 C-F,H,J 6 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Molniya-1 57	1983-25 A	1983 Apr 2.09	Windmill +	3.4 long	1983 Apr 3.6	62.91	700.00	26116	470	39006	0.738	280

[Molniya 8K78M/ML] 	[13964]	6143.74 days	6 vanes	1.6 dia	1983 Apr 17.4	62.96	717.76	26555	492	39863	0.741	280

BAI	2000 Jan 26.83	1000?

D	Molniya-1 57	1983-25 B	1983 Apr 2.09	Cylinder	7.5 long	1983 Apr 5.4	62.95	91.17	6711	235	431	0.015	65

Block I 3rd stage 	13965]	29 days	2500?	2.6 dia

1983 May 1

D	Molniya-1 57	1983-25 C	1983 Apr 2.09	Irregular	-	1983 Apr 5.4	62.96	90.99	6702	189	459	0.02	60

4th stage casing 	[13966]	14 days

1983 Apr 16

D	Molniya-1 57	1983-25 D	1983 Apr 2.09	Cylinder	2.0 long	1983 Apr 6.0	62.86	699.29	26098	471	38969	0.738	280

Block L 4th stage 	[13967]	6346.34 d	440	2.0 dia

2000 Aug 16.43

D	STS 6*	1983-26 A	1983 Apr 4.77	Cylinder +	37.1 long	1983 Apr 7.5	28.46	90.03	6662	278	289	0.001	286

4M	(Challenger F])	[13968]	5.02 days	delta wing	17.4 high

R	[Shuttle]	CC-LC39A	1983 Apr 9.79	67876	23.8 span

empty

TDRS 1**	1983-26 B	1983 Apr 4.77	Irregular	6 high	1983 Apr 7.0	2.37	1085.98	35000	21857	35387	0.193	179

[13969]	> million	+ 2 dishes	17.4 span	1983 Dec 31.0	1.51	1436.2	42170	35765	35819	0.0006	5

years	2268		2004 Jul 10.09	11.89	1436.15	42166	35774	35801	0.0003	131

IUS	1983-26 C	1983 Apr 4.77	Double	2.0 to	1983 Apr 7.0	2.34	1089.38	35073	22025	35365	0.19	180

upper section	[13970]	> million	cone	3.2 long?	2004 Jul 6.72	5.34	1089.62	35076	22291	35104	0.183	24

years	3350? full	2.9 dia?

350? empty

IUS #	1983-26 D	1983 Apr 4.77	Cylinder	5 long?	1983 Apr 11.5	25.96	622.46	24152	247	35301	0.726	183

lower section	[13971]	100 years	114OO? full	2.9 dia?	2004 Jul 6.54	25.89	443.30	19259	238	25523	0.656	182

700? empty

D	Cosmos 1450	1983-27 A	1983 Apr 6.50	Cylinder?	4 long?	1983 Apr 9.7	65.86	94.44	6870	472	512	0.003	338

[Kosmos 11K65M 	[13972]	2611 days		2 dia?

53719-512]	PLE	1990 May 30

D	Cosmos 1450	1983-27 B	1983 Apr 6.50	Cylinder	7.4 long	1983 Apr 11.0	65.86	94.31	6864	459	512	0.004	334

2nd stage	[13973]	2178 days	2200?	2.4 dia

1989 Mar 23

*	Launched from Cape Canaveral; landed at Edwards AFB, California.

**	Tracking and Data Relay Satellite, ejected from Shuttle.  Was manoeuvred during May 1983 to achieve synchronous orbit on 1983 Jun 29.

#	Inertia] Upper Stage engine malfunction prevented synchronous orbit being achieved.

Raduga 12	1983-28 A	1983 Apr 8.20	-	-	1983 Apr 10.0	1.27	1443.02	42302	35873	35975	0.001	271

[Proton 8K82K 	[13974]	> million	2000?		1983 May 13.9	1.19	1436.93	42164	35782	35789	0.0001	226

315-02/11S86 38L]	BAI-LC200P	years			2004 Jul 9.04	12.93	1436.83	42160	35767	35796	0.0003	66

D	Raduga 12	1983-28 B	1983 Apr 8.20	Irregular	-	1983 Apr 8.4	51.64	88.14	6564	173	198	0.002	308

4th stage casing 	[13976]	< 0.8 day

1983 Apr 8

D	Raduga 12	1983-28 C	1983 Apr 8.20	Cylinder	6.5 long?	1983 Apr 8.4	51.64	88.27	6570	188	196	0.001	172

third stage	[13977]	2 days		4 dia

1983 Apr 10

D	Raduga 12	1983-28 D	1983 Apr 8.20

Ullage motor 	[13979]	403 days

1984 May 15

D	Raduga 12	1983-28 E	1983 Apr 8.20

Ullage motor 	[13980]	434 days

1984 Jun 15

Raduga 12	1983-28 F	1983 Apr 8.20	Cylinder	5.5 long	1983 Apr 10.0	1.28	1439.42	42232	35762	35945	0.002	325

Block DM 4th stage 	[13983]	> million	17300 full	4.0 dia	2004 Jul 6.35	12.95	1439.15	42225	35724	35968	0.003	8

years

D	Cosmos 1451	1983-29 A	1983 Apr 8.36	Sphere-	6.5 long?	1983 Apr 8.7	82.34	88.72	6585	180	236	0.004	98

R	[Soyuz 11A511U] 	[13975]	13.8 days	cylinder	2.4 dia	1983 Apr 9.5	82.35	90.04	6653	227	323	0.007	65

PLE	1983 Apr 22.2	6300?

D	Cosmos 1451	1983-29 B	1983 Apr 8.36	Cylinder	7.5 long	1983 Apr 8.7	82.34	88.5	6577	175	223	0.004	110

Block I 3rd stage 	[13978]	1 day	2500?	2.6 dia

1983 Apr 9

D	Cosmos 1451	1983-29 C	1983 Apr 8.36	Cone	1.5 long?	1983 May 3.6	82.35	89.54	6629	218	284	0.005	332

engine	[14016]	42 days	600?	2 dia?

1983 May 20	full

D	Fragment	1983-29 D	[14026]	1983 Apr 25	17 days

D	Fragment	1983-29 E	[14027]	1983 Apr 27	19 days

RCA Satcom 6	1983-30 A	1983 Apr 11.95	Box + vanes	1.42 x	1983 Apr 13.5	24.06	635.54	24498	191	36048	0.732	179

[Delta 3924	[13984]	> million	1121 full	1.62 x	1983 May 2.8	0.15	1435.93	42165	35746	35828	0.001	352

653 #167]	CC-LC17B	years	599 empty	1.75	2004 Jul 11.06	8.51	1442.10	42282	35857	35951	0.001	328

D	RCA Satcom 6	1983-30 B	1983 Apr 11.95	Cylinder +	6.4 long	1983 Apr 14.1	25.38	130.68	8538	302	4017	0.218	184

Delta 2nd stage	[13985]	6765 days	annulus	1.52 and	2001 Oct 17.84	25.29	88.35	6572	167	219	0.004	346

2001 Oct 18	350?	2.44 dia

D	RCA Satcom 6	1983-30 C	1983 Apr 11.95	Sphere-	1.32 long	1983 Apr 13.5	24.07	637.45	24547	196	36141	O@.732	179

PKM	[13990]	1295 days	cone	0.94 dia

1986 Oct 27 A	66

Cosmos 1452	1983-31 A	1983 Apr 12.76	Cylinder +	2 long?	1983 Apr 15.3	74.05	100.84	7176	785	810	0.002	359

[Kosmos 11K65M 	[13991]	120 years	paddles?	1 dia?	2004 Jul 8.30	74.05	100.53	7162	772	796	0.002	209

65019-519]	PLE		750?

Cosmos 1452	1983-31 B	1983 Apr 12.76	Cylinder	7.4 long	1983 Apr 15.1	74.05	100.74	7171	779	807	0.002	31

2nd stage	[13992]	100 years	2200?	2.4 dia	2004 Jul 8.57	74.05	100.35	7153	771	778	0.0005	107

Fragment	1983-31 C	[14812]			2004 Jul 6.29	74.06	100.15	7144	753	777	0.002	123

D	KH 8-52	1983-32 A	1983 Apr 15.78	Cylinder	8 long?	1983 Apr 17.2	96.52	88.85	6595	136	297	0.012	143

[Titan 24B-27	[14001]	128 days	3000?	1.5 dia

(3B-63) Agena D]	VDB-SLC4W	1983 Aug 21	full

D	Rohini 3*	1983-33 A	1983 Apr 17.24	Spheroid?	0.65 dia?	1983 Apr 19.4	46.6	97.02	6998	388	852	0.033	132

[SLV-3-D4]	[14002]	2559 days	42		1990 Apr 19.43	46.54	87.43	6526	144	150	0.0005	58

SRI	1990 Apr 19

D	Rohini 3	1983-33 B	1983 Apr 17.24	Cylinder?	1.5 long?	1983 Apr 19.4	46.6	97.07	7001	390	855	0.033	132

4th stage	[14003]	2162 days		0.4 dia?

1989 Mar 18

D	Fragments	1983-33 C-F	4 pieces, all have decayed		For orbital information see extra pages at the end of the year

*	Indian launch.

D	Cosmos 1453	1983-34 A	1983 Apr 19.50	Octagonal	1.8 long?	1983 Apr 21.3	74.03	94.5	6872	471	517	0.003	335

[Kosmos 11K65M 	[14006]	2211 days	ellipsoid	1.5 dia?

47119-520]	PLE	1989 May 8	550?

D	Cosmos 1453	1983-34 B	1983 Apr 19.50	Cylinder	7.4 long	1983 Apr 23.6	74.04	94.42	6868	463	517	0.004	330

2nd stage	[14007]	2167 days	2200?	2.4 dia

1989 Mar 25

D	Fragments #	1983-34 C-Z	22 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Soyuz-T 8*	1983-35 A	1983 Apr 20.55	Sphere-	7.5 long	1983 Apr 22.0	51.61	90.38	6675	287	306	0.001	315

3M	[Soyuz 11A511U 372]	[14014]	2.01 days	cylinder +2	2.3 to

R		BAI	1983 Apr 22.56	wings 6850	2.72 dia

D	Soyuz-T 8	1983-35 B	1983 Apr 20.55	Cylinder	7.5 long	1983 Apr 21.5	51.63	87.94	6554	175	177	0	167

Block I 3rd stage 	[14015]	2 days	2500?	2.6 dia

1983 Apr 22

D	Soyuz-T 8	1983-35 C	1983 Apr 20.55	Spheroid	2.3 dia	1983 Apr 24.5	51.62	90.28	6670	287	296	0.001	291

orbital module**	[14029]	37 days	1260?

1983 May 27

D	Cosmos 1454	1983-36 A	1983 Apr 22.61	Sphere-	7 long?	1983 Apr 24.2	67.14	89.64	6635	171	343	0.013	69

R	[Soyuz 11A511U] 	[14017]	30 days	cylinder	2.4 dia

PLE-LC41/1	1983 May 22	6700?

D	Cosmos 1454	1983-36 B	1983 Apr 22.61	Cylinder	7.5 long	1983 Apr 25.4	67.13	88.6	6584	156	255	0.008	71

rocket	[14028]	4 days	2500?	2.6 dia

1983 Apr 26

D	Fragment	1983-36 C	[14030]

Cosmos 1455	1983-37 A	1983 Apr 23.60	-	-	1983 Apr 25.2	82.51	97.77	7029	637	665	0.002	280

[Tsyklon 3] 	[14032]	60 years			2004 Jul 10.57	82.50	95.87	6939	553	567	0.001	247

PLE-LC32

*	Soyuz-T 8 passed near to Cosmos 1443/Salyut 7 complex about 1983 Apr 21.6, but failed to dock.

**	Part of 1983-35 A until 1983 Apr 22.

#	These fragments are probably calibration targets.

Cosmos 1455	1983-37 B	1983 Apr 23.60	Cylinder	7.4 long	1983 Apr 25.2	82.51	97.75	7028	636	664	0.002	285

3rd stage	[14033]	60 years	2200?	2.4 dia	2004 Jul 8.20	82.51	97.17	7001	611	635	0.002	188

D	Cosmos 1456	1983-38 A	1983 Apr 25.82	Windmill +	4.2 long?	1983 Apr 26.4	62.94	710.71	26382	620	39387	0.735	320

[Molniya 8K78M/2BL]	[14034]	5495 days	6 vanes	1.6 dia	1983 Apr 29.3	62.96	717.41	26547	622	39716	0.736	320

PLE-LC16/2	1998 May 11	1250?

D	Cosmos 1456	1983-38 B	1983 Apr 25.82	Cylinder	7.5 long	1983 Apr 26.9	62.88	92.41	6772	215	573	0.026	121

Block I 3rd stage 	[14036]	36 days	2500?	2.6 dia

1983 May 31

D	Cosmos 1456	1983-38 C	1983 Apr 25.82	Irregular	-	1983 May 3.2	62.88	91.97	6753	209	541	0.025	121

4th stage casing 	[14037]	12 days

1983 May 7

D	Cosmos 1456	1983-38 E	1983 Apr 25.82	Cylinder	2.0 long	1983 Apr 27.3	62.91	707.32	26297	620	39217	0.734	320

Block 2BL 4th stage	[14041]	5615 days	440	2.0 dia

1998 Sep 8

Fragments	1983-38 D,F-J 5 pieces, 4 have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1457	1983-39 A	1983 Apr 26.42	Sphere-	7 long?	1983 Apr 27.2	70.39	89.71	6638	171	349	0.013	68

R	[Soyuz 11A511U] 	[14039]	43 days	cylinder	2.4 dia

BAI	1983 Jun 8	6700?

D	Cosmos 1457	1983-39 B	1983 Apr 26.42	Cylinder	7.5 long	1983 Apr 26.8	70.4	89.56	6631	170	335	0.012	69

Block I 3rd stage 	[14040]	4 days	2500?	2.6 dia

1983 Apr 30

D	Cosmos 1458	1983-40 A	1983 Apr 28.35	Sphere-	5.9 long?	1983 Apr 30.4	82.32	89.1	6607	212	246	0.003	95

R	[Soyuz 11A511U] 	[14044]	12.8 days	cylinder	2.4 dia

PLE-LC41/1	1983 May 11.2	5900?

D	Cosmos 1458	1983-40 B	1983 Apr 28.35	Cylinder	7.5 long	1983 Apr 28.8	82.33	88.95	6600	210	234	0.002	100

Block I 3rd stage 	[14045]	4 days	2500?	2.6 dia

1983 May 2

D	Capsule	1983-40 E	1983 Apr 28.35	Ellipsoid	0.9 long	1983 May 11.5	82.31	88.86	6596	204	232	0.002	72

[14067]	19 days	200?	1.9 dia

1983 May 17

D	Fragment	1983-40 C	[14046]	1983 May 19	21 days

D	Fragment	1983-40 D	[14066]	1983 May 17	19 days

GOES 6	1983-41 A	1983 Apr 28.93	Cylinder	3.12 long	1983 May 1.7	0.49	1703.86	47257	33367	48390	0.159	257

[Delta 3914 #168]	[14050]	> million	836 full	2.15 dia	1983 May 23.2	0.38	1436.14	42168	35784	35795	0.0001	234

CC-LC17A	years	397 empty		2004 Jul 8.52	11.03	1436.58	42174	35770	35882	0.0006	52

GOES 6	1983-41 B	1983 Apr 28.93	Cylinder	7 long	1983 May 2.0	25.34	118.39	7994	404	2827	0.152	193

Delta 2nd stage	[14051]	50 years	350 ?	1.4 dia	2004 Jul 6.65	25.34	112.08	7701	396	2249	0.120	330

empty

GOES 6	1983-41 C	1983 Apr 28.93	-	-	1983 May 8.7	0.41	1707.34	47320	33501	48383	0.157	263

Apogee motor	[14069]	> million	439		2004 Jun 25.42	18.13	1707.35	47320	33209	48673	0.163	294

years	full

D	GOES 6	1983-41 D	1983 Apr 28.93	Sphere-	1.8 long	1983 Jul 18.6	24.87	884.27	30518	263	48017	0.782	215

Star-37E PKM	[14196]	2606 days	cone	0.94 dia

1990 Jun 16	66

Cosmos 1459	1983-42 A	1983 May 6.12	Cylinder	2.1 long	1983 May 8.7	82.97	104.77	7361	947	1019	0.005	296

[Kosmos 11K65M 	[14057]	1200 years	810	2.0 dia	2004 Jul 6.96	82.97	104.63	7356	941	1012	0.005	293

65019-513]	PLE

Cosmos 1459	1983-42 B	1983 May 6.12	Cylinder	7.4 long	1983 May 9.0	82.97	104.65	7355	947	1007	0.004	295

2nd stage	[14059]	600 years	2200 ?	2.4 dia	2004 Jul 8.51	82.97	104.48	7349	940	1001	0.004	214

D	Cosmos 1460	1983-43 A	1983 May 6.38	Sphere-	6.5 long?	1983 May 8.4	70.34	92.23	6762	351	417	0.005	212

R	[Soyuz 11A511U] 	[14058]	13.89 days	cylinder	2.4 dia

BAI	1983 May 20.27	6300?

D	Cosmos 1460	1983-43 B	1983 May 6.38	Cylinder	7.5 long	1983 May 8.6	70.33	89.76	6641	203	322	0.009	48

Block I 3rd stage 	[14060]	9 days	2500?	2.6 dia

1983 May 15

D	Cosmos 1460	1983-43 G	1983 May.6.38	Cone	1.5 long?	1983 May 24.0	70.34	92.19	6760	349	415	0.005	186

engine	[14079]	339 days	600?	2 dia?

1984 Apr 9	full

D	Fragments	1983-43 C-F,H-L 8 pieces, all have decayed		For orbital information see extra pages at the end of the year

Cosmos 1461*	1983-44 A	1983 May 7.44	Cylinder?	-	1983 May 10.0	65.03	93.3	6815	429	445	0.001	283

[Tsyklon 2] 	[14064]	100 years			1986 Jan 17.6	65.03	99.3	7104	584	868	0.02	142

BAI-LC90				2004 Jul 10.51	65.01	97.33	7009	550	711	0.012	96

D	Cosmos 1461	1983-44 B	1983 May 7.44	Cylinder	8 long?	1983 May 7.7	64.99	89.18	6613	112	357	0.019	54

2nd stage	[14065]	<0.6 day	1500?	2.5 dia?

1983 May 7

Fragments	1983-44 C-GW	187 pieces, 163 have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1462	1983-45 A	1983 May 17.34	Sphere-	6.5 long?	1983 May 20.4	82.32	89.88	6645	259	275	0.001	314

R	[Soyuz 11A511U] 	[14071]	13.9 days	cylinder	2.4 dia

PLE-LC41	1983 May 31.2	6300?

D	Cosmos 1462	1983-45 B	1983 May 17.34	Cylinder	7.5 long	1983 May 17.8	82.33	89.43	6623	207	282	0.006	78

Block I 3rd stage 	[14072]	6 days	2500?	2.6 dia

1983 May 23

D	Cosmos 1462	1983-45 F	1983 May 17.34	Cone	1.5 long?	1983 May 31.5	82.32	89.85	6644	258	273	0.001	285

engine	[14099]	34 days	600?	2 dia?

1983 Jun 20	full

D	Fragment	1983-45 C	[14073]	1983 May 21	4 days

D	Fragment	1983-45 D	[14074]	1983 Jun 9	23 days

D	Fragment	1983-45 E	[14098]	1983 Jun 7	21 days

*	Partially disintegrated 1985 Mar 11.

D	Cosmos 1463	1983-46 A	1983 May 19.50	Octaqonal	1.8 long?	1983 May 23.2	82.94	103.57	7304	301	1551	0.086	102

[Kosmos 11K65M 	[14075]	3538 days	ellipsoid	1.5 dia?

47119-511]	PLE	1993 Jan 24	550?

D	Cosmos 1463	1983-46 B	1983 May 19.50	Cylinder	7.4 long	1983 May 22.9	82.95	103.45	7298	300	1540	0.085	103

2nd stage	[14076]	2364 days	2200?	2.4 dia

1989 Nov 7

Intelsat 5-6	1983-47 A	1983 May 19.93	Box +	15.9 span	1983 May 20.0	23.4	634.17	24451	166	35980	0.732	178

[Atlas SLV-3D(R)	[14077]	> million	dishes	6.4  wide	1983 May 23.3	0.23	1436.05	42166	35767	35808	0.0005	112

AC-61 Centaur D-1AR		years	+ 2 vanes		1998 Jul 12.48	5.87	1452.12	42478	36062	36137	0.0009	67

5041D]			1928 full?		2004 Jul 10.72	9.56	1452.13	42478	36074	36125	0.0006	110

D	Intelsat 5-6	1983-47 B	1983 May 19.93	Cylinder	8.6 long	1983 May 19.9	28.32	89.55	6630	148	356	0.016	146

Centaur 61 stage	[14081]	1731 days	1815	3.0 dia	1983 May 27.4	23.6	611.19	23868	201	34778	0.724	184

1988 Feb 13

Cosmos 1464	1983-48 A	1983 May 24.12	Cylinder	2.1 long	1983 May 26.4	82.94	104.92	7368	968	1011	0.004	275

[Kosmos 11K65M 	[14084]	1200 years	810	2.0 dia	2004 Jul 6.95	82.94	104.78	7363	961	1008	0.003	49

47139-541	PLE

Cosmos 1464	1983-48 B	1983 May 24.12	Cylinder	7.4 long	1983 May 26.5	82.95	104.82	7363	968	1001	0.002	260

2nd stage	[14085]	600 years	2200?	2.4 dia	2004 Jul 7.96	82.94	104.65	7356	953	1003	0.003	0

D	Cosmos 1465	1983-49 A	1983 May 26.21	Octagonal	1.8 long?	1983 May 27.2	50.66	93.44	6824	349	543	0.014	149

[Kosmos 11K65M 	[14087]	608 days	ellipsoid?	1.5 dia?

65083-458]	KY-LC107	1985 Jan 23	550?

D	Cosmos 1465	1983-49 B	1983 May 26.21	Cylinder	7.4 long	1983 May 27.2	50.67	93.36	6820	347	537	0.014	146

2nd stage	[14088]	596 days	2200?	2.4 dia

1985 Jan 11

D	Fragments	1983-49 C-K	8 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1466	1983-50 A	1983 May 26.50	Sphere-	7 long?	1983 May 27.2	64.88	89.68	6638	174	345	0.013	60

R	[Soyuz 11A511U] 	[14089]	41 days	cylinder	2.4 dia

BAI	1983 Jul 6	6700?

D	Cosmos 1466	1983-50 B	1983 May 26.50	Cylinder	7.5 long	1983 May 27.4	64.89	89.42	6625	171	322	0.011	61

Block I 3rd stage 	[14090]	4 days	2500?	2.6 dia

1983 May 30

D	Fragment	1983-50 C	[14097]	1983 May 27	1 day

D	Exosat*	1983-51 A	1983 May 26.64	Cylinder	3.20 long	1983 May 28.0	72.46	5431.27	102347	356	191581	0.934	286

[Delta 3914 #169]	[14095]	1076 days	+ panel	2.10 dia

VDB-SLC2W	1986 May 6	510

Exosat	1983-51 B	1983 May 26.64	Cylinder	7.0 long	1983 May 26.7	72.49	103.70	7312	334	1533	0.082	270

Delta 2nd stage	[14096]	700 years	600?	2.44 dia	1983 May 28.4	72.33	119.18	8022	756	2531	0.111	330

2004 Jul 7.71	72.30	119.08	8017	759	2517	0.110	173

D	Exosat	1983-5I F	1983 May 26.64	Sphere-	1.83 long			Orbit similar to 1983-51 A

third stage	[NNA]	2.5 years?	cone?	2.44 dia

1985 Nov?

D	Fragment	1983-51 C	[14525]	1986 Apr 7	1047 days

D	Fragment	1983-51 D	[14526]	1989 Mar 6	2111 days

D	Fragment	1983-51 E	[14927]	1989 Mar 21	2126 days

D	Cosmos 1467	1983-52 A	1983 May 31.49	Sphere-	6.5 long?	1983 May 31.7	72.86	90.16	6660	199	364	0.012	85

R	[Soyuz 11A511U] 	[14100]	11.8 days	cylinder	2.4 dia	1983 Jun 2.4	72.86	92.31	6765	357	417	0.004	208

PLE	1983 Jun 12.3	6300?

D	Cosmos 1467	1983-52 B	1983 May 31.49	Cylinder	7.5 long	1983 May 31.7	72.85	90.08	6656	200	355	0.012	86

Block I 3rd stage 	[14101]	10 days	2500?	2.6 dia

1983 Jun 10

D	Cosmos 1467	1983-52 E	1983 May 31.49	Cone	1.5 long?	1983 Jun 13.7	72.86	92.25	6762	357	411	0.004	182

engine	[14116]	372 days	600?	2 dia?

1984 Jun 6	full

D	Fragments	1983-52 C,D,F-J 6 pieces, all have decayed		For orbital information see extra pages at the end of the year

*	European X-ray Observatory Satellite, launched by NASA.

Venus 15 Orbiter*	1983-53 A	1983 Jun 2.11	Cylinder	5 long?	Solarorbit	2.3?	293 days		0.71	1.01	0.17	-

[Proton 8K82K 	[14104]		+ 2 panels	2.3 dia	1983 Oct 10.13	80?	1440	39455	1605	65200	0.806	-

321-01/11S824M 8L]	BAI-LC200L		5200 full?	5.7 span	No TLE found

D	Venus 15	1983-53 B	1983 Jun 2.11	Cylinder	6.5 long?	1983 Jun 2.5	51.53	88.05	6559	160	202	0.003	51

third stage	[14105]	1 day		4 dia

1983 Jun 3

D	Venus 15	1983-53 C	1983 Jun 2.11	Irregular	-	1983 Jun 2.6	51.52	87.96	6555	158	195	0.003	53

4th stage casing 	[14106]	1 day

1983 Jun 3

Venus 15	1983-53 D	1983 Jun 2.11	Cylinder	3.9 long?	Solarorbit similar to 1983-53 A

4th stage	[NNA]	indefinate	1900?	3.9 dia

Venus 16 Orbiter**	1983-54 A	1983 Jun 7.11	Cylinder	5 long?	Solarorbit	2.3?	293 days		0.71	1.01	0.17	-

[Proton 8K82K 	[14107]		+ 2 panels	2.3 dia	1983 Oct 14	80?	1440	39455	1605	65200	0.806	-

321-02/11S824 9L]	BAI-LC200P		5200 full?	5.7 span	No TLE found

D	Venus 16	1983-54 B	1983 Jun 7.11	Cylinder	6.5 long?	1983 Jun 7.6	51.51	88.01	6557	159	199	0.003	51

third stage	[14108]	1 day		4 dia

1983 Jun 8

D	Venus 16	1983-54 C	1983 Jun 7.11	Irregular	-	1983 Jun 7.7	51.54	87.96	6555	157	196	0.003	46

4th stage casing	[14109]	1 day

1983 Jun 8

Venus 16	1983-54 D	1983 Jun 7.11	Cylinder	3.9 long?	Solarorbit similar to 1983-54 A

4th stage	[NNA]	indefinate	1900?	3.9 dia

D	Cosmos 1468	1983-55 A	1983 Jun 7.33	Sphere-	6.5 long?	1983 Jun 9.3	82.34	89.88	6646	255	280	0.002	289

R	[Soyuz 11A511U] 	[14110]	13.86 days	cylinder	2.4 dia

PLE-LC41	1983 Jun 21.19	6300?

D	Cosmos 1468	1983-55 B	1983 Jun 7.33	Cylinder	7.5 long	1983 Jun 7.8	82.35	89.15	6609	216	246	0.002	84

Block I 3rd stage 	[14111]	5 days	2500?	2.6 dia

1983 Jun 12

D	Cosmos 1468	1983-55 C	1983 Jun 7.33	Cone	1.5 long?	1983 Jun 21.5	82.33	89.85	6644	256	276	0.002	242

engine	[14140]	38 days	600?	2 dia?

1983 Jul 15	full

D	Fragment	1983-55 D	[14141]	1983 Jun 29	22 days

*	Venus 15 Orbiter entered orbit around Venus on 1983 Oct 10.13; radar-mapping spacecraft, Venus orbit is approximate.

**	Venus 16 Orbiter entered orbit around Venus on 1983 Oct 14; radar-mapping spacecraft, Venus orbit is approximate.

NOSS 5	1983-56 A	1983 Jun 9.97	Cylinder	-	1983 Jun 12.2	63.34	107.42	7486	1048	1168	0.008	153

[Atlas 69F 6002H]	[14112]	1600 years	64?		2004 Jul 6.90	63.38	107.33	7482	654	1553	0.060	7   #

VDB-SLC3E				2020 Nov 9.74	63.34	106.03	7421	375	1710	0.090	94

2021 Jun 13.98	63.28	105.97	7418	368	1710	0.090	99

NOSS 5	1983-56B	1983 Jun 9.97	-	-	1983 Jun 12.0	63.34	107.38	7484	1047	1165	0.008	151

rocket	[14113]	1000 years			No elements available

GB 1	1983-56C	1983 Jun 9.97	-	-	1983 Jun 22.3	63.43	107.48	7489	1051	1171	0.008	158

[14143]	1600 years			2004 Jul 5.98	63.38	107.35	7483	648	1560	0.061	12

GB 2	1983-56D	1983 Jun 9.97	-	-	1983 Jun 22.3	63.44	107.47	7489	1051	1170	0.008	158

[14144]	1600 years			2004 Jul 5.98	63.38	107.35	7483	649	1559	0.061	13

GB 3	1933-56G	1983 Jun 9.97	-	-	1983 Jun 19.3	63.45	107.47	7489	1051	1170	0.008	200

[14180]	1600 years			2004 Jul 6.92	63.38	107.37	7483	656	1553	0.060	7

Fragment	1983-56 E	[14145]			No elements available

Fragment	1983-56 F	[14146]			No elements available

Fragment	1983-56 H	[14181]			No elements available

#	Orbits from amateur observations.

D	Cosmos 1469	1983-57 A	1983 Jun 14.51	Sphere-        6.5 long?	1983 Jun 16.6	72.84	90.29	6666	232	344	0.008	66

R	[Soyuz 11A511U] 	[14123]	9.8 days	cylinder       2.4 dia

PLE	1983 Jun 24.3	6300?

D	Cosmos 1469	1983-57 B	1983 Jun 14.51	Cylinder       7.5 long	1983 Jun 14.9	72.84	90.07	6655	197	357	0.012	84

Block I 3rd stage 	[14124]	9 days	2500?          2.6 dia

1983 Jun 23

D	Cosmos 1469	1983-57 F	1983 Jun 14.51	Cone           1.5 long?	1983 Jun 25.5	72.85	89.33	6619	225	256	0.002	60

engine	[14150]	20 days	600?	2 dia?

1983 Jul 4	full

D	Fragment	1983-57 C	[14126]	1983 Oct 4	112 days

D	Fragment	1983-57 D	[14127]	1983 Jun 15	1 day

D	Fragment	1983-57 E	[14149]	1983 Jun 27	13 days

ECS 1*	1983-58 A	1983 Jun 16.50	Hexagonal      2.2 wide	1983 Jun 18.5	8.57	625.21	24233	215	35495	0.728	180

[Ariane-1 06]	[14128]	>million	box +          2.4 long	1983 Jun 24.3	0.05	1427.64	42000	35464	35780	0.004	7

KOU-ELA1	years	2 panels       14 span	1997 Apr 4.50	6.16	1456.42	42562	36150	36217	0.0008	319

1050 full		2004 Jul 4.92	10.28	1456.40	42561	36118	36247	0.002	12

610 empty

*	European Communications Satellite. Aka Eutelsat 1-1. (Ariane 1-05 launcher failed in 1982 September)

Oscar 10*	1983-58 B	1983 Jun 16.50	Box?	0.6 x 0.4	1983 Jun 18.9	8.6	624.33	24211	197	35469	0.728	180

[14129]	50 years	44?	x 0.2?	2004 Jul 10.45	26.48	699.48	26102	4022	35426	0.602	106

D	Ariane-1 06	1983-58 C	1983 Jun 16.50	Cylinder	8.6 long	1983 Jun 20.2	8.61	623.37	24187	197	35421	0.728	182

H-8 3rd stage	[14130]	4447 days	1634	2.6 dia

1995 Aug 19

D	Ariane-1 06	1983-58 D	1983 Jun 16.50

Sylda upper half	[14151]	1113 days

1986 Jul 3

D	Fragment	1983-58 E	[17302]	1990 Oct 10	2673 days

D	Fragment	1983-58 F	[17331]	1991 Mar 3	2817 days

D	STS 7**	1983-59 A	1983 Jun 18.48	Cylinder +	37.1 long	1983 Jun 20.5	28.46	90.52	6686	295	320	0.002	261

5M	(Challenger F2)	[14132]	6.10 days	delta wing	17.4 high

R	[Shuttle}	CC-LC39A	1983 Jun 24.58	67876 empty	23.8 span

Telesat 7 #	1983-59 B	1983 Jun 18.48	Cylinder	2.82 to	1983 Jun 19.8	22.98	640.39	24622	287	36201	0.729	359

(Anik C2)	[14133]	> million	1238 full	6.7 long	1984 Dec 28.0	0.02	1436.1	42170	35783	35800	0.0002	129

years	660 empty	2.16 dia	1998 Jan 7.88	4.93	1452.73	42490	35935	36289	0.004	205

2004 Jul 6.93	9.13	1452.68	42489	35963	36257	0.003	269

Palapa 3 ##	1983-59 C	1983 Jun 18.48	Cylinder	2.82 to	1983 Jun 20.5	25.52	660.14	25125	318	37175	0.733	0

(Flight Bl)	[14134]	> million	1200 full	6.7 long	1983 Jun 21.0	0.83	1394.02	41338	32707	37213	0.055	1

years	650 empty	2.16 dia	2004 Jul 9.86	9.82	1436.82	42179	35791	35809	0.0002	316

Telesat 7	1983-59 D	1983 Jun 18.48	Cylinder	2.29 long	1983 Jun 22.5	23.14	640.31	24620	316	36168	0.728	1

PAM -D PKM	[14135]	100 years	2154	1.5 dia	2004 Jul 6.67	23.14	569.12	22749	329	32411	0.705	312

full

Palapa 3	1983-59 E	1983 Jun 18.48	Cylinder	2.29 long	1983 Jun 20.5	25.63	662.04	25172	323	37265	0.734	359

PAM-D PKM	[14136]	100 years	2154	1.5 dia	2004 Jul 5.25	25.35	582.28	23099	270	33171	0.712	230

full

D	SPAS-Ol ###	1983-59 F	1983 Jun 18.48	Irregular	3.0 long?	1983 Jun 22.4	28.46	90.2	6670	289	294	0.0004	285

R		[14142]	6.10 days	box	1.8 wide?

1983 Jun 24.58	1500	0.6 deep?

*	West German amateur radio satellite.

**	Launched from Cape Canaveral (4	men, 1 woman); landed at Edwards AFB, California.  Cargo bay carried OSTA-2 pallet (not separated	).

#	Canadian satellite ejected from Shuttle 1983 Jun 18.88.

##	Indonesian satellite ejected from Shuttle 1983 Jun 19.57.

###German Shuttle PAllet Satellite	released by Shuttle arm Jun 22.34; retreated to 0.3 km; retrieved again Jun 22.52.

D	KH 9-18	1983-60 A	1983 Jun 20.78	Cylinder	15 long	1983 Jun 23.2	96.45	88.50	6577	169	229	0.005	148

[Titan 34D-5 04D-3]	[14137]	275 days	13300?	3.0 dia

VDB-SLC4E	1984 Mar 21	full

D	Titan 3D	1983-60 B	1983 Jun 20.78	Cylinder	6 long	1983 Jun 21.3	96.45	88.40	6572	157	231	0.006	136

2nd stage	[14138]	2 days	1900	3.0 dia

1983 Jun 22

Racquel 7	1983-60 C	1983 Jun 20.78	Octagon?	0.3 long?	1983 Jun 23.3	96.67	111.41	7668	1289	1291	0.0002	133

[14139]	5000 years	60?	0.9 dia?	2004 Jun 17.12	96.67	111.30	7665	1284	1289	0.0003	210

No TLE available; orbit from amateur observations

2009 Apr 18.87	96.66	111.30	7665	1285	1288	0.0002	147

Cosmos 1470	1983-61 A	1983 Jun 23.00	-	-	1983 Jun 25.3	82.52	97.80	7031	635	670	0.002	289

[Tsyklon 3] 	[14147]	60 years			2004 Jul 9.83	82.51	96.03	6947	556	580	0.002	148

PLE-LC32

Cosmos 1470	1983-61 B	1983 Jun  23.00	Cylinder	7.4 long	1983 Jun 24.9	82.52	97.77	7029	633	668	0.002	296

3rd stage	[14148]	60 years	2200?	2.4 dia	2004 Jul 10.57	82.52	97.20	7003	607	641	0.002	10

D	Soyuz-T 9*	1983-62 A	1983 Jun 27.38	Sphere-	7.5 long	1983 Jun 29.3	51.61	91.08	6709	325	337	0.001	297

2M	[Soyuz 11A511U 379]	[14152]	149.45 days	cylinder	2.3 to

R		BAI	1983 Nov 23.83	+ 2 wings	2.72 dia

6850

D	Soyuz-T 9	1983-62 B	1983 Jun 27.38	Cylinder	7.5 long	1983 Jun 27.7	51.61	88.56	6584	190	222	0.002	112

Block I 3rd stage 	[14153]	2 days	2500?	2.6 dia

1983 Jun 29

D	Soyuz-T 9	1983-62 C	1983 Jun 27.38	Spheroid	2.3 dia	1983 Nov 24.9	51.62	90.99	6705	318	335	0.001	107

orbital module	[14519]	264 days	1260?

1984 Mar 17

*	Soyuz-T 9 docked with Cosmos 1443 - Salyut 7 on 1983 Jun 28.45.

Hilat 1* (S83-1)	1983-63 A	1983 Jun 27.65	Octagon	0.75 long?	1983 Jun 29.2	82.03	101.02	7184	772	839	0.005	267

[Scout d-1 S205C]	[14154]	120 years	+ 4 vanes	0.45 dia?	2004 Jul 7.56	82.02	100.38	7155	747	807	0.004	358

VDB-SLC5		113

Hilat 1	1983-63 B	1983 Jun 27.65	Cylinder	1.50 long	1983 Jun 29.9	82.03	101.02	7184	773	838	0.005	265

Scout 4th stage	[14155]	100 years	24	0.46 dia	2004 Jul 6.89	82.02	100.18	7145	739	795	0.004	313

Fragment	1983-63 C	[14222]			2004 Jul 7.52	82.37	98.93	7086	691	724	0.002	70

Fragment	1983-63 D	[14223]			2004 Jul 6.83	81.65	100.43	7157	737	820	0.006	332

Fragment	1983-63 E	[23906]			1996 Jun 10.68	82.02	100.57	7164	756	815	0.004	199

2004 Jul 9.34	82.01	96.95	6991	602	623	0.002	107

D	Cosmos 1471	1983-64 A	1983 Jun 28.63	Sphere-	7 long?	1983 Jul 1.3	67.15	89.79	6643	185	344	0.012	75

R	[Soyuz 11A511U] 	[14156]	30 days	cylinder	2.4 dia

PLE-LC41	1983 Jul 28	6700?

D	Cosmos 1471	1983-64 B	1983 Jun 28.63	Cylinder	7.5 long	1983 Jun 29.5	67.15	89.46	6626	171	325	0.012	71

Block I 3rd stage 	[14157]	5 days	2500?	2.6 dia

1983 Jul 3

D	Fragment	1983-64 C	[14232]	1983 Jul 28	30 days

D	Fragment	1983-64 D	[14233]	1983 Jul 28	30 days

Galaxy 1	1983-65 A	1983 Jun 28.96	Cylinder	2.82 to	1983 Jul 2.9	0.07	1437.35	42191	35194	36432	0.015	9

[Delta 3920 #170]	[14158]	> million	+ Skirt	6.7 long#	2004 Jul 10.10	7.83	1438.47	42211	35813	35852	0.0005	33

CC-LC17B	years	1218 full	2.16 dia

520 empty

D	Galaxy 1	1983-65 B	1983 Jun 28.96	Cylinder	6.4 long	1983 Jul 2.5	26.51	90.75	6697	276	362	0.006	124

Delta 2nd stage	[14159]	44 days	+ annulus	1.52 and

1983 Aug 11	350?	2.44 dia

D	Galaxy 1	1983-65 C	1983 Jun 28.96	Cylinder	2.29 long	1983 Jul 1.9	23.31	641.63	24654	201	36351	0.733	180

PAM-D PKM	[14168]	5862 days	2154	1.5 dia

1999 Jul 16	full

Gorizont 7	1983-66 A	1983 Jul 1.00	Cylinder +	-	1983 Jul 1.8	1.35	1478.07	42984	36566	36646	0.001	232

[Proton 8K82K 	[14160]	> million	dish +		1983 Jul 20.0	1.35	1435.91	42163	35745	35826	0.001	311

314-02/11S86 39L]	BAI-LC200L	years	panels		2004 Jul 2.88	12.96	1464.10	42713	36286	36382	0.001	124

2000?

*	HIgh-LATitude ionospheric research satellite (modified Transit).

#	Length before and after hollow solar-cell skirt was extended.

D	Gorizont 7	1983-66 B	1983 Jul 1.00	Cylinder	6.5 long?	1983 Jul 1.5	51.61	88.09	6561	178	188	0.001	242

third stage	[14161]	2 days		4 dia

1983 Jul 3

D	Gorizont 7	1983-66 C	1983 Jul 1.00	Irreqular	-	1983 Jul 1.3	51.60	88.13	6563	180	190	0.001	125

4th stage casing 	[14162]	< lday

1983 Jul 1

D	Gorizont 7	1983-66 D	1983 Jul 1.00

Ullage motor 	[14166]	265 dyas

1984 Feb 22 A

D	Gorizont 7	1983-66 E	1983 Jul 1.00

Ullage motor 	[14167]	4165 days

1994 Nov 25

Gorizont 7	1983-66 F	1983 Jul 1.00	Cylinder	5.5 long	1984 Jul 31.4	0.45	1475.17	42929	36513	36589	0.001	308

Block DM 4th stage 	[15141]	>million	17300 full	4.0 dia	2004 Jul 6.75	13.22	1475.10	42925	36490	36603	0.001	359

years

D	Prognoz 9	1983-67 A	1983 Jul 1.51	Spheroid	1.8 dia?	1983 Jul 15.0	65.5	38448	366568	380	720000	0.982	-

[Molniya 8K78M/SOL]	[14163]	<1 month?	+ 4 vanes

BAI	1983 Jul?	1060?

D	Prognoz 9	1983-67 B	1983 Jul 1.51	Cylinder	7.5 long	1983 Jul 3.5	64.93	91.41	6723	229	460	0.017	66

Block I 3rd stage 	[14164]	35 days	2500?	2.6 dia

1983 Aug 5

D	Prognoz 9	1983-67 C	1983 Jul 1.51	Irregular	-	1983 Jul 3.5	65.01	91.29	6717	204	473	0.02	70

4th stage casing 	[14165]	24 days

1983 Jul 25

D	Prognoz 9	1983-67 D	1983 Jul 1.51	Cylinder	2.0 long			Orbit similar to 1983-67 A

rocket	[NNA]	<1 month?	440	2.0 dia

1983 Jul?

D	Cosmos 1472	1983-68 A	1983 Jul 5.33	Sphere-	6.5 long?	1983 Jul 5.6.	82.34	88.75	6588	183	236	0.003	90

R	[Soyuz 11A511U] 	[14169]	13.84 days	cylinder	2.4 dia	1983 Jul 7.3	82.35	91.56	6728	338	362	0.002	99

PLE	1983 Jul 19.17	6300?

D	Cosmos 1472	1983-68 B	1983 Jul 5.33	Cylinder	7.5 long	1983 Jul 5.8	82.35	88.54	6579	180	222	0.003	98

Block I 3rd stage 	[14170]	2 days	2500?	2.6 dia

1983 Jul 7

D	Cosmos 1472	1983-68 C	1983 Jul 5.33	Cone	1.5 long?	1983 Jul 20.0	82.34	91.53	6727	338	359	0.002	47

engine	[14197]	159 days	600?	2 dia?

1983 Dec 11	full

D	Fragment	1983-68 D	[14198]	1983 Sep 3	60 days

D	Fragment	1983-68 E	[14202]	1983 Aug 16	42 days

D	Fragment	1983-68 F	[14203]	1983 Aug 28	54 days

Cosmos 1473 *	1983-69 A	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.1	74.03	114.46	7809	1397	1465	0.004	86

[Kosmos 11K65M 	[14171]	6000 years	40?	0.8 dia?	2004 Jul 6.94	74.02	114.40	7807	1394	1462	0.004	254

47183-459]	PLE

Cosmos 1474 *	1983-69 B	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.5	74.03	114.65	7818	1414	1465	0.003	96

[14172]	7000 years	40?	0.8 dia?	2004 Jul 6.94	74.02	115.58	7815	1411	1463	0.003	309

Cosmos 1475 *	1983-69 C	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.1	74.03	114.84	7826	1431	1465	0.002	89

[14173]	8000 years	40?	0.8 dia?	2004 Jul 6.87	74.02	114.78	7824	1428	1462	0.002	349

Cosmos 1476 *	1983-69 D	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.5	74.03	115.03	7835	1448	1465	0.001	92

[14174]	9000 years	40?	0.8 dia?	2004 Jul 7.17	74.02	114.97	7832	1445	1462	0.001	33

Cosmos 1477 *	1983-69 E	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 6.5	74.03	115.22	7843	1463	1467	0	343

[14175]	10000 years	40?	0.8 dia?	2004 Jul 6.98	74.02	115.17	7841	1461	1464	0.0002	330

Cosmos 1478 *	1983-69 F	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.5	74.03	115.42	7852	1464	1484	0.001	257

[14176]	10000 years	40?	0.8 dia?	2004 Jul 7.22	74.02	115.37	7850	1462	1481	0.001	289

*	Strela-1M

Cosmos 1479 *	1983-69 G	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.5	74.03	115.62	7861	1464	1502	0.002	276

[14177]	10000 years	40?	0.8 dia?	2004 Jul 7.22	74.02	115.57	7859	1462	1499	0.002	356

Cosmos 1480 *	1983-69 H	1983 Jul 6.02	Spheroid	1.0 long?	1983 Jul 7.5	74.03	115.84	7871	1464	1522	0.004	265

[14178]	10000 years	40?	0.8 dia?	2004 Jul 6.81	74.02	115.78	7869	1462	1519	0.004	37

Cosmos 1473-1480	1983-69 J	1983 Jul 6.02	Cylinder	7.4 long	1983 Jul 7.5	74.03	117.54	7948	1464	1676	0.013	271

rocket	[14179]	20000 years	2200?	2.4 dia	2004 Jul 7.72	74.02	117.45	7945	1462	1670	0.013	60

Cosmos 1481 #	1983-70 A	1983 Jul 8.81	Windmill	4.2 long?	1983 Jul 11.8	62.93	707.39	26300	643	39200	0.733	318

[Molniya 8K78M/2BL]	[14182]	100 years?	+ 6 vanes	1.6 dia	2004 Jul 6.05	65.81	707.33	26298	2286	37552	0.671	149

PLE-LC43/4	disintegrated	1250?

D	Cosmos   1481	1983-70 B	1983 Jul 8.81	Cylinder	7.5 long	1983 Jul 10.4	62.82	92.44	6773	212	578	0.027	122

Block I 3rd stage 	[14183]	44 days	2500?	2.6 dia

1983 Aug 21

D	Cosmos 1481	1983-70 C	1983 Jul 8.81	Irregular	-	1983 Jul 10.4	62.93	92.28	6765	170	604	0.032	121

4th stage casing 	[14184]	16 days

1983 Jul 24

Cosmos 1481	1983-70 D	1983 Jul 8.81	Cylinder	2.0 long	1983 Jul 18.2	62.94	708.05	26316	763	39113	0.729	318

4th stage	[14191]	100 years?	440	2.0 dia	2004 Jul 5.88	65.52	708.00	26314	2201	37670	0.674	150

Cosmos 1481	1983-70 E	1983 Jul 8.81			2004 Jul 6.18	65.83	708.83	26334	2371	37541	0.668	146

Ullage motor 	[14192]

Cosmos 1481	1983-70 F	1983 Jul 8.81			2004 Jul 7.98	65.73	704.39	26231	1878	37826	0.685	160

Ullage motor 	[20412]

Fragment	1983-70 G	[26633]			2002 Jan 18.59	66.50	718.22	26567	1601	38774	0.700	147

Fragment	1983-70 H	[27906]			2004 Jul 6.09	67.00	702.47	26177	2772	36824	0.650	122

Fragment	1983-70 J	[27907]			2004 Jul 5.83	65.59	725.32	26741	2255	38470	0.677	146

1983-70 K	[33531]

1983 70 L	[48344]			2021 Apr 27.86	69.58	684.33	25724	4057	34634	0.594	319

1983 70 M	[48345]			2021 May 2.20	65.07	721.65	26651	892	39653	0.727	351

D	Cosmos 1482	1983-71A	1983 Jul 13.4	Sphere-	6.5 long?	1983 Jul 15.2	69.98	92.21	6761	352	413	0.004	214

R	[Soyuz 11A511U] 	[14185]	13.89 days	cylinder	2.4 dia

BAI	1983 Jul 27.29	6300?

*	Strela-1M

#	Cosmos 1481 was the twelfth spacecraft of the Cosmos 862-type to experience a fragmentation. The event apparently occurred 1983 Jul 9, within a day of launch. An expected orbital maneuver by Cosmos 1481 to move from its transfer orbit to an operational orbit about 3 days after launch was never performed.

D	Cosmos 1482	1983-71 B	1983 Jul 13.40	Cylinder	7.5 long	1983 Jul 13.9	69.98	90.08	656	209	347	0.01	58

Block I 3rd stage 	[14186]	12 days	2500?	2.6 dia

1983 Jul 25

D	Cosmos 1482	1983-71 H	1983 Jul 13.40	Cone	1.5 long?	1983 Jul 29.7	69.95	92.16	6758	360	400	0.003	177

engine	[14230]	348 days	600?	2 dia?

1984 Jun 25	full

D	Fragments	1983-71 C- G,J   6 pieces, all have decayed		For orbital information see extra pages at the end of the year

GPS 8*	1983-72 A	1983 Jul 14.4	3 Cylinder +	5.3 span	1983 Jul 15.9	62.84	725.78	26753	19952	20798	0.016	175

[Atlas 75E/SGS-2]	[14189]	1 million	4 vanes		2004 Jul 6.66	63.70	751.10	27371	20743	21424	0.009	37

VDB-SLC3W	years	871 full

525 empty

GPS 8 #	1983-72 B	1983 Jul 14.43	Cone-	1.85 long	1983 Jul 16.2	62.97	371.84	17130	549	20954	0.596	159

Star 48 PKM	[14190]	40 years?	cylinder?	0.63 to	2004 Jul 6.30	64.35	372.25	17142	1497	20030	0.541	38

163?	1.65 dia?

Fragment	1983-72 C	[25842]			2004 Jul 8.90	64.76	367.45	16994	1307	19924	0.548	10

Fragment	1983-72 D	[26916]			2004 Jul 7.94	64.03	368.55	17028	1121	20177	0.560	29

D	Molniya-1 58	1983-73 A	1983 Jul 19.64	Windmill	3.4 long	1983 Jul 24.1	62.94	699.96	26115	459	39014	0.738	280

[Molniya 8K78M/ML] 	[14199]	4237 days	+ 6 vanes	1.6 dia	1983 Aug 7.0	62.97	717.78	26556	468	39887	0.742	280

BAI	1995 Feb 23	1000?

D	Molniya-1 58	1983-73B	1983 Jul 19.64	Cylinder	7.5 long	1983 Jul 20.3	62.93	91.09	6707	235	423	0.014	59

Block I 3rd stage 	[14200]	32 davs	2500?	2.6 dia

1983 Aug 20

D	Molniya-1 58	1983-73 C	1983 Jul 19.64	Irregular	-	1983 Jul 20.3	62.93	91.4	6723	203	486	0.021	61

4th stage casing 	[14201]	23 days

1983 Aug 11

D	Molniya-1 58	1983-73 D	1983 Jul 19.64	Cylinder	2.0 long	1983 Jul 21.1	62.94	696.85	26036	463	38853	0.737	280

Block L 4th stage 	[14206]	2391 days	440	2.0 dia

1990 Feb 3

*	GPS 7 launch failed on 1981 Dec 18.

#	Analyses indicate that there may have been a break-up event of an unknown nature.

D	Cosmos 1483	1983-74 A	1983 Jul 20.33	Sphere-	6.5 long?	1983 Jul 22.4	82.32	89.88	6646	260	275	0.001	309

R	[Soyuz 11A511U] 	[14204]	13.9 days	cylinder	2.4 dia

PLE-LC43/3	1983 Aug 3.2	6300?

D	Cosmos 1483	1983-74 B	1983 Jul 20.33	Cylinder	7.5 long	1983 Jul 20.4	82.32	89.36	6620	215	268	0.004	83

Block I 3rd stage 	[14205]	6 days	2500?	2.6 dia

1983 Jul 26

D	Cosmos 1483	1983-74 E	1983 Jul 20.33	Cone	1.5 long?	1983 Aug 6.2	82.32	89.79	6641	253	273	0.002	262

engine	[14243]	37 days	600?	2 dia?

1983 Aug 26	full

D	Fragment	1983-74 C	[14239]	1983 Aug 11	22 days

D	Fragment	1983-74 D	[14242]	1983 Aug 11	22 days

D	Cosmos 1484*	1983-75 A	1983 Jul 24.25	Cylinder +	5 long?	1983 Jul 24.6	98.01	97.31	7007	594	663	0.005	10

(Resurs-0 3)	[14207]	10781 days	2 vanes?	1.5 dia?	2004 Jul 10.54	97.66	93.87	6842	450	476	0.002	216

[Vostok 8A92M]	BAI	2013 Jan 28	2500?		2013 Jan 28.02	97.57	87.07	6508	124	134	0.0007	230

Cosmos 1484	1983-75 B	1983 Jul 24.25	Cylinder	3.8 long?	1983 Jul 25.2	98.02	97.28	7006	591	664	0.005	310

Block Ye 3rd stage	[14208]	60 years	1440?	2.6  dia?	2004 Jul 11.10	97.93	95.93	6942	539	588	0.004	315

Fragments	1983-75 C-BG	53  pieces, 47 have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1485	1983-76 A	1983 Jul 26.50	Sphere-	6.5 long?	1983 Jul 28.2	72.85	92.3	6765	358	416	0.004	210

R	[Soyuz 11A511U] 	[14210]	13.8 days	cylinder	2.4 dia

PLE	1983 Aug 9.3	6300?

D	Cosmos 1485	1983-76 B	1983 Jul 26.50	Cylinder	7.5 long	1983 Jul 26.9	72.84	90.07	6655	197	357	0.012	82

Block I 3rd stage 	[14211]	10 days	2500?	2.6 dia

1983 Aug 5

D	Cosmos 1485	1983-76 F	1983 Jul 26.50	Cone	1.5 long?	1983 Aug 13.2	72.85	92.26	6763	358	412	0.004	174

engine	[14255]	385 days	600?	2 dia?

1984 Aug 14	full

D	Fragment	1983-76 C	[14216]	1983 Sep 14	50 days

D	Fragment	1983-76 D	[14253]	1983 Sep 29	65 days

D	Fragment	1983-76 E	[14254]	1983 Oct 30	96 days

*	New type of Earth resources satellite. Disintegrated 1993 Oct 18.

Telstar 301	1983-77 A	1983 Jul 28.95	Cylinder	2.77 to	1983 Aug 1.3	0.16	1435.93	42163	35436	36134	0.008	38

[Delta 3920 #171]	[14234]	> million	+ skirt	6.83 long*	1997 Apr 4.91	2.70	1446.93	42377	35897	36100	0.002	248

CC-LC17A	years	1225 full	2.16 dia	2004 Jul 7.51	8.01	1446.85	42375	35882	36111	0.003	318

653 empty

D	Telstar 301	1983-77 B	1983 Jul 28.95	Cylinder	6.4 long	1983 Jul 31.6	26	91.35	6727	276	422	0.011	146

Delta 2nd stage	[14235]	62 days	+ annulus	1.52 and

1983 Sep 28	350?	2.44 dia

D	Telstar 301	1983-77 C	1983 Jul 28.95	Cylinder	2.29 long	1983 Aug 5.5	22.93	656.53	25034	188	37124	0.738	184

PAM-D PKM	[14236]	6623 days	2154	1.5 dia	2001 Sep 13.78	22.60	88.97	6602	150	297	0.011	84

2001 Sep 14	full

SDS 8 (Jumpseat 7)	1983-78 A	1983 Jul 31	Cylinder?	-	1983 Aug	63.4	717.7	26553	1028	39321	0.721	-				[Titan 34B-9 3B-65	[14237]	100 years?			No elements available

Ascent Agena D]	VDB-SLC4W

SDS 8	1983-78 B	1983 Jul 31	Cylinder	6 long			Orbit similar to 1983-78 A

rocket	[14238]	100 years?	700?	1.5 dia	No elements available

Fragment	1983-78 C	[23811]			No TLE found

Fragment	1983-78 D	[23812]			No TLE found

Fragment	1983-78 E	[25588]			No TLE found

Cosmos 1486	1983-79 A	1983 Aug 3.53	Cylinder +	2 long?	1983 Aug 15.4	74.05	100.78	7173	784	806	0.002	325

[Kosmos 11K65M 	[14240]	120 years	paddles?	1 dia?	2004 Jul 7.79	74.05	100.48	7160	771	791	0.001	36

53783-463]	PLE		750?

Cosmos 1486	1983-79 B	1983 Aug 3.53	Cylinder	7.4 long	1983 Aug 15.7	74.07	100.71	7170	778	805	0.002	1

2nd stage	[14241]	100 years	2200?	2.4 dia	2004 Jul 7.70	74.06	100.33	7153	762	787	0.002	81

Fragment	1983-79 C	[14813]			2004 Jul 6.92	74.04	100.18	7146	753	781	0.002	167

Fragment	1983-79 D	[15756]			2004 Jul 6.73	74.05	98.87	7083	697	712	0.001	153

D	Cosmos 1487	1983-80 A	1983 Aug 5.39	Sphere-	6.5 long?	1983 Aug 7.2	82.31	89.89	6646	261	275	0.001	312

R	[Soyuz 11A511U] 	[14245]	13.86 days	cylinder	2.4 dia

PLE-LC43/4	1983 Aug 19.25	6300?

*	Length before and a	fter hollow solar-cell skirt extended.

D	Cosmos 1487	1983-80 B	1983 Aug 5.39	Cylinder	7.5 long	1983 Aug 5.7	82.32	89.36	6620	213	270	0.004	94

Block I 3rd stage 	[14246]	6 days	2500?	2.6 dia

1983 Aug 11

D	Cosmos 1487	1983-80 E	1983 Aug 5.39	Cone	1.5 long?	1983 Aug 20.3	82.31	89.8	6642	255	272	0.001	236

engine	[14292]	37 days	600?	2 dia?

1983 Sep 11	full

D	Fragment	1983-80 C	[14249]	1983 Aug 11	6 days

D	Fragment	1983-80 D	[14291]	1983 Aug 26	21 days

D	Fragment	1983-80 F	[14295]	1983 Aug 28	23 days

Sakura 2B	1983-81 A	1983 Aug 5.85	Cylinder	3.2 long	1983 Aug 18.7	0.29	1450.71	42451	35535	36610	0.013	192

(CS-2B)	[14248]	> million	670 full	2.18 dia	2004 Jul 5.99	11.15	1457.30	42579	36195	36206	0.0001	5

[Nu-2 N-11(F)]	TAN-O	years	350 empty

D	Sakura 2B	1983-81 B	1983 Aug 5.85	Cylinder	5.4 long	1983 Aug 16.5	30.13	99.08	7099	165	1277	0.078	280

second stage	[14250]	53 days	550?	1.4 dia

1983 Sep 27

D	Sakura 2B	1983-81 C	1983 Aug 5.85	Cylinder	1.74 long	1983 Aug 19.1	28.77	644.78	24733	198	36512	0.734	186

third stage	[14287]	2850 days	66?	1.65 dia	1991 May 24.82	28.31	89.92	6649	123	418	0.022	268

1991 May 25

D	Cosmos 1488	1983-82 A	1983 Aug 9.48	Sphere-	6.5 long?	1983 Aug 15.2	72.86	92.3	6765	358	416	0.004	201

R	[Soyuz 11A511U] 	[14251]	13.7 days	cylinder	2.4 dia

PLE	1983 Aug 23.2	6300?

D	Cosmos 1488	1983-82 B	1983 Aug 9.48	Cylinder	7.5 long	1983 Aug 10.0	72.86	90.03	6653	195	355	0.012	83

Block I 3rd stage 	[14252]	9 days	2500?	2.6 dia

1983 Aug 18

D	Cosmos 1488	1983-82 D	1983 Aug 9.48	Cone	1.5 long?	1983 Aug 26.3	72.86	92.27	6764	356	415	0.004	177

engine	[14302]	393 days	600?	2 dia?

1984 Sep 5	full

D	Fragment	1983-82 C	[14298]	1983 Nov 13	96 days

D	Fragment	1983-82 E	[14303]	1983 Aug 28	19 days

D	Fragment	1983-82 F	[14347]	1983 Nov 13	96 days

D	Cosmos 1489	1983-83 A	1983 Aug 10.54	Sphere-	7 long?	1983 Aug 14.3	64.72	89.85	6646	171	365	0.015	66

R	[Soyuz 11A511U] 	[14256]	44 days	cylinder	2.4 dia

BAI	1983 Sep 23	6700?

D	Cosmos 1489	1983-83 B	1983 Aug 10.54	Cylinder	7.5 long	1983 Aug 11.2	64.73	89.1	6609	173	288	0.009	63

Block I 3rd stage 	[14257]	4 days	2500?	2.6 dia

1983 Aug 14

D	Fragments	1983-83 C	[14263]	1983 Aug 11	1 day

D	Fragments	1983-83 D	[14371]	1983 Sep 24	45 days

L	Cosmos 1490*	1983-84 A	1983 Aug 10.77	Cylinder	-	1983 Aug 28.1	64.84	678.28	25573	19157	19232	0.001	57

(Glonass 4)	[14258]	1 million	+ panels +		1983 Sep 8.4	64.83	675.73	25508	19088	19171	0.002	335

[Proton 8K82K 	BAI-LC200L	years	boom		2004 Jul 5.66	65.85	675.73	25508	19102	19157	0.001	338

317-01/11S861 2L]

L	Cosmos 1491*	1983-84 B	1983 Aug  10.77	Cylinder	-	1983 Aug 26.7	64.94	675.46	25502	19097	19150	0.001	292

(Glonass 5)	[14259]	1 million	+ panels +		1983 Sep 1.3	64.94	675.73	25508	19103	19156	0.001	306

years	boom		1984 Sep 30.0	64.83	679.5	25603	18948	19501	0.011	51

2004 Jul 7.40	65.66	668.42	25324	18863	19027	0.003	318

L	Cosmos 1492*	1983-84 C	1983 Aug 10.77	Cylinder	-	1983 Aug 15.4	64.82	676.83	25536	19152	19164	0.0002	204

(Glonass 6)	[14260]	1 million	+ panels +		2004 Jul 6.63	65.85	676.82	25535	19154	19159	0.0001	137

years	boom

D	Cosmos 1490	1983-84 D	1983 Aug 10.77	Irregular	-	1983  Aug  11.1	51.61	88.06	6560	178	185	0.001	132

4th stage casing 	[14261]	1 day

1983 Aug 11

D	Cosmos 1490	1983-84 E	1983 Aug 10.77	Cylinder	6.5 long?	1983  Aug  11.1	51.63	88.03	6558	169	191	0.002	272

third stage	[14262]	2 days		4 dia

1983 Aug 12

Cosmos 1490	1983-84 F	1983 Aug 10.77	Cylinder	5.5 long	1983 Aug 26.2	64.83	676.29	25523	19138	19151	0.0003	313

Block DM 4th stage 	[14264]	1 million	17300 ful1	4.0 dia	2004 Jul 6.71	65.85	676.28	25522	19128	19159	0.0006	197

years

*	Triple Glonass payload

Cosmos 1490	1983-84 G	1983 Aug 10.77			2004 Jul 7.25	51.93	309.30	15150	378	17165	0.554	349

Ullage motor 	[14277]

Cosmos 1490	1983-84 H	1983 Aug 10.77			2004 Jul 6.76	52.13	303.05	14946	330	16804	0.551	357

Ullage motor 	[14278]

D	Progress 17*	1983-85 A	1983 Aug 17.51	Sphere-	7.9 long	1983 Aug 19.2	51.64	90.23	6667	257	321	0.005	192

[Soyuz 11A511U	[14283]	31.5 days	cylinder	2.3 dia

Ts15000-302]	BAI-LC1	1983 Sep 18.0	7020

D	Progress 17	1983-85 B	1983 Aug 17.51	Cylinder	7.5 long	1983 Aug 17.9	51.64	88.58	6585	186	228	0.003	88

Block I 3rd stage 	[14284]	3 days	2500?	2.6 dia

1983 Aug 20

D	FSW-0 5(China 13)**	1983-86 A	1983 Aug 19.25	Cylinder?	-	1983 Aug 21.5	63.31	90.05	6656	173	382	0.016	145

r	[CZ-2C-5]	[14288]	15 days	3600

JIUQ-LA2	1983 Sep 3

D	FSW-0 5	1983-86 B	1983 Aug 19.25	Cylinder	7.0 long	1983 Aug 21.5	63.31	89.8	6643	170	360	0.014	145

2nd stage	[1289]	11 days		3.35 dia

1983 Aug 30

D	Fragments	1983-86 C-F	4 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1493	1983-87 A	1983 Aug 23.46	Sphere-	6.5 long?	1983 Aug 25.2	72.86	92.3	6765	360	414	0.004	207

R	[Soyuz 11A511U] 	[14299]	13.7 days	cylinder	2.4 dia

PLE	1983 Sep 6.2	6300?

D	Cosmos 1493	1983-87 B	1983 Aug 23.46	Cylinder	7.5 long	1983 Aug 25.3	72.85	89.78	6641	188	337	0.011	89

Block I 3rd stage 	[14300]	8 days	2500?	2.6 dia

1983 Aug 31

D	Cosmos 1493	1983-87 F	1983 Aug 23.46	Cone	1.5 long?	1983 Sep 11.7	72.85	92.24	6763	358	412	0.004	169

engine	[14324]	414 days	600?	2 dia?

1984 Oct 10	full

D	Fragments	1983-87 C-E,G,H  5 pieces, all have decayed		For orbital information see extra pages at the end of the year

*	Progress 17 docked with Soyuz-T 9 - Salyut 7 (2nd airlock) on 1983 Aug 19.57.		** Capsule, weight 1850	kg, returned to Earth

(Cosmos 1443 had separated from	lst airlock 1983 Au	g 14.59. Soyuz-T 9 then vacated	   on 1983 Aug 24.20.

2nd airlock 1983 Aug 16.60, and	re-attached to 1st	airlock.) Progress 17 undocked

on 1983 Sep 17.49, and de-orbited over the Pacific Ocean about 12 hours later.

Raduga 13	1983-88 A	1983 Aug 25.83	-	-	1983 Aug 27.6	1.35	1476.7	42958	36522	36638	0.001	255

[Proton 8K82K 	[14307]	> million	2000?		1983 Sep 17.7	1.29	1436.08	42167	35649	35928	0.003	208

316-02/11S86 40L]	BAI-LC200P	years			2004 Jul 7.67	13.06	1466.78	42763	36329	36440	0.001	225

D	Raduga 13	1983-88 B	1983 Aug 25.83	Cylinder	6.5 long?	1983 Aug 26.4	51.61	88.17	6565	184	190	0.0004	218

third stage	[14308]	3 days		4 dia

1983 Aug 28

D	Raduga 13	1983-88 C	1983 Aug 25.83	Irregular	-	1983 Aug 26.0	51.6	88.31	6572	]8i,	201	0.001	100

4th stage casing 	[14309]	1 day

1983 Aug 26

D	Raduga 13	1983-88 D	1983 Aug 25.83

Ullage motor	[14310]	316 days

1984 Jul 6

D	Raduga 13	1983-88 E	1983 Aug 25.83

Ullage motor	[14311]	1159 days

1986 Oct 27 A

Raduga 13	1983-88 F	1983 Aug 25.83	Cylinder	5.5 long	1983 Sep 8.9	1.33	1475.17	42950	36508	36636	0.001	284

Block I 3rd stage 	[14333]	> million	17300 full	4.0 dia	2004 Jul 10.55	13.23	1475.17	42926	36487	36608	0.001	308

years

D	STS 8*	1983-89 A	1983 Aug 30.27	Cylinder +	37.1 long	1983 Aug 30.4	28.46	90.31	6676	294	301	0.0005	290

5M	(Challenger F3)	[14312]	6.05 days	delta wing	17.4 high

R	[Shuttle]	CC-LC39A	1983 Sep 5.32	67876	23.8 span

empty

Insat 1B**	1983-89 B	1983 Aug 30.27	Box + sail	1.55 high	1983 Sep 2.6	0.49	1411.96	41693	33476	37154	0.044	186

[14318]	> million	+ antennae	1.42 deep	2004 Jul 6.99	10.17	1435.15	42146	35720	35815	0.001	29

years	1152 full	2.18 wide

Insat ]B	1983-89 C	1983 Aug 30.27	Cylinder	2.29 long	1983 Nov 28.8	23.91	659.01	25097	217	37220	0.737	237

PAM-D PKM	[14524]	70 years	2154	1.5 dia	2004 Jul 6.90	24.39	447.27	19374	267	25723	0.657	344

full

*	Night launch from Cape Canaveral; night landing at Edwards AFB California. Cargo bay carried PFTA, a 3384 kg dumbell, 6.0 m long, 4.7 m dia

(not separated).

**	Indian weather satellite ejected from Shuttle 1983 Aug 31.33.

D	Molniya-3 21	1983-90 A	1983 Aug 30.95	Windmill +	4.2 long?	1983 Sep 2.0	62.89	735.73	26998	430	40809	0.748	280

[Molniya 8K78M/ML]	[14313]	6475 days	6 vanes	1.6 dia	1983 Sep 22.1	62.87	717.75	26555	464	39890	0.742	281

PLE-LC41/1	2001 May 22	1500?		2001 May 21.68	62.14	103.60	7308	82	1776	0.116	270

D	Molniya-3 21	1983-90 B	1983 Aug 30.95	Cylinder	7.5 long	1983 Sep 3.6	62.84	90.35	6671	180	405	0.017	121

Block I 3rd stage 	[14314]	13 days	2500?	2.6 dia

1983 Sep 12

D	Molniya-3 21	1983-90 C	1983 Aug 30.95	Irregular	-	1983 Sep 2.6	62.85	90.6	6683	208	402	0.014	135

4th stage casing  	[14315]	26 days

1983 Sep 19

D	Molniya-3 21	1983-90 D	1983 Aug 30.95	Cylinder	2.0 long	1983 Sep 4.1	62.89	731.4	26892	440	40587	0.746	280

Block L 4th stage 	[14319]	6714 days	440	2.0 dia	2002 Jan 15.56	62.03	92.42	6772	88	698	0.045	286

2002 Jan 16

D	Cosmos 1494	1983-91 A	1983 Aug 31.27	Octagonal	1.8 long?	1983 Sep 3.2	50.68	93.46	6826	345	550	0.015	162

[Kosmos 11K65M 	[14316]	757 days	ellipsoid?	1.5 dia?

47139-547]	KY-LC107	1985 Sep 26	550?

D	Cosmos 1494	1983-91 B	1983 Aug 31.27	Cylinder	7.4 long	1983 Sep 1.9	50.68	93.39	6822	343	545	0.015	155

2nd stage	[14317]	632 days	2200?	2.4 dia

1985 May 24

D	Fragments *	1983-91 C, E-AC   25 pieces, all have decayed	For orbital information see extra pages at the end of the year

D	Cosmos 1495	1983-92 A	1983 Sep 3.43	Sphere-	6.5 long?	1983 Sep 5.3	82.32	89.04	6604	215	236	0.002	102

R	[Soyuz 11A511U] 	[14320]	12.85 days	cylinder	2.4 dia

PLE-LC43/4	1983 Sep 16.28	6300?

D	Cosmos 1495	1983-92 B	1983 Sep 3.43	Cylinder	7.5 long	1983 Sep 3.5	82.33	88.83	6593	199	231	0.002	238

3rd stage	[14321]	3 days	2500?	2.6 dia

1983 Sep 6

*	These fragments are calibration targets.

D	Cosmos 1495	1983-92 D	1983 Sep 3.43	Cone	1.5 long?	1983 Sep 17.4	82.32	88.81	6592	207	221	0.001	130

engine	[14338]	19 days	600?	2 dia?

1983 Sep 22	full

D	Fragment	1983-92 C	[14337]	1983 Sep 19	16 days

D	Cosmos 1496	1983-93 A	1983 Sep 7.56	Sphere-	7 long?	1983 Sep 7.7	67.18	89.62	6634	170	341	0.013	74

R	[Soyuz 11A511U] 	[14326]	42 days	cylinder	2.4 dia

PLE-LC16/2	1983 Oct 19	6700?

D	Cosmos 1496	1983-93 B	1983 Sep 7.56	Cylinder	7.5 long	1983 Sep 8.2	67.18	89.46	6626	171	324	0.012	73

Block I 3rd stage 	[14327]	4 days	2500?	2.6 dia

1983 Sep 11

RCA Satcom 7	1983-94 A	1983 Sep 8.95	Box+ vanes	1.42 x	1983 Sep 10.5	23.96	624.27	24252	182	35565	0.729	179

[Delta 3924 #172]	[14328]	> million	1121 full	1.62 x	1983 Sep 17.2	0.07	1435.98	42162	35725	35843	0.001	48

CC-LC17B	years	599 empty	1.75	2004 Jul 9.90	7.33	1448.42	42406	35976	36079	0.001	215

D	RCA Satcom 7	1983-94 B	1983 Sep 8.95	Cylinder +	6.4 long	1983 Sep 11.0	25.52	130.21	8517	292	3985	0.217	184

Delta 2nd stage	[14329]	20 years	annulus	1.52 and

1999 Apr 16.04	350?	2.44 dia

D	RCA Satcom 7	1983-94 C	1983 Sep 8.95	Sphere-	1.32 long	1983 Sep 10.5	23.93	624.76	24264	184	35588	0.73	179

Star-37E PKM	[14332]	256 days	cone	0.94 dia

1984 May 21	66

D	Cosmos 1497	1983-95 A	1983 Sep 9.46	Sphere-	6.5 long?	1983 Sep 11.2	72.85	92.30	6765	357	416	0.004	208

R	[Soyuz 11A511U] 	[14330]	13.7 days	cylinder	2.4 dia

PLE	1983 Sep 23.2	6300?

D	Cosmos 1497	1983-95 B	1983 Sep 9.46	Cylinder	7.5 lona	1983 Sep 9.6	72.85	90.17	6660	197	367	0.013	88

Block I 3rd stage 	[14331]	10 days	2500?	2.6 dia

1983 Sep 19

D	Cosmos 1497	1983-95 D	1983 Sep 9.46	Cone	1.5 long?	1983 Sep 26.2	72.85	92.27	6763	356	414	0.004	176

engine	[14368]	395 days	600?	2 dia?

1984 Oct 8	full

D	Fragment	1983-95 C	[14367]	1983 Dec 14	96 days

D	Fragment	1983-95 E	[14370]	1983 Nov 14	66 days

D	Fragment	1983-95 F	[14562]	1983 Dec 27	109 days

D	Cosmos 1498	1983-96 A	1983 Sep 14.44	Sphere-	6.5 long?	1983 Sep 15.9	82.31	89.89	6646	261	275	0.001	295

R	[Soyuz 11A511U] 	[14334]	13.85 days	cylinder	2.4 dia

PLE-LC41	1983 Sep 28.29	6300?

D	Cosmos 1498	1983-96 B	1983 Sep 14.44	Cylinder	7.5 long	1983 Sep 15.0	82.31	89.27	6615	210	264	0.004	89

rocket	[14335]	5 days	2500?	2.6 dia

1983 Sep 19

D	Cosmos 1498	1983-96 D	1983 Sep 14.44	Cone	1.5 long?	1983 Sep 29.1	82.31	89.75	6639	252	270	0.001	232

engine	[14374]	32 days	600?	2 dia?

1983 Oct 16	full

D	Fragment	1983-96 C	[14336]	1983 Sep 19	5 days

D	Fragment	1983-96 E	[14375]	1983 Oct 4	20 days

D	Fragment	1983-96 F	[14376]	1983 Oct 5	21 days

D	Cosmos 1499	1983-97 A	1983 Sep 17.47	Sphere-	6.5 long?	1983 Sep 19.2	72.85	92.3	6765	357	416	0.004.	199

R	[Soyuz 11A511U] 	[14339]	13.7 days	cylinder	2.4 dia

PLE	1983 Oct 1.2	6300?

D	Cosmos 1499	1983-97 B	1983 Sep 17.47	Cylinder	7.5 long	1983 Sep 19.1	72.84	89.93	6648	194	346	0.012	79

Block I 3rd stage 	[14340]	9 days	2500?	2.6 dia

1983 Sep 26

D	Cosmos 1499	1983-97 F	1983 Sep 17.47	Cone	1.5 long?	1983 Oct 2.4	72.84	92.28	6764	356	415	0.004	172

engine	[14384]	414 days	600?	2 dia?

1984 Nov 4	full

D	Fragments	1983-97 C-E,G,H  5 pieces, all have decayed		For orbital information see extra pages at the end of the year

Galaxy 2	1983-98 A	1983 Sep 22.93	Cylinder	2.82 to	1983 Sep 26.2	0.13	1436.34	42169	35770	35811	0.0005	357

[Delta 3920 #173]	[14365]	> million	+ skirt	6.7 long*	2004 Jul 6.44	7.75	1436.88	42180	35787	35817	0.0004	289

CC-LC17A	years	1218 full	2.16 dia

520 empty

D	Galaxy 2	1983-98 B	1983 Sep 22.93	Cylinder	6.4 long	1983 Sep 23.5	26.63	90.83	6701	283	363	0.006	94

Delta 2nd stage	[14366]	38 days	+ annulus	1.52 and

1983 Oct 30	350?	2.44 dia

D	Galaxy 2	1983-98 C	1983 Sep 22.93	Cylinder	2.29 long	1983 Sep 23.0	23.4	646.64	24771	185	36600	0.735	180

PAM-D PKM	[14369]	7 months?	2154	1.5 dia

1984 Apr	full

Cosmos 1500	1983-99 A	1983 Sep 28.33	Windmill	3.5 long?	1983 Oct 1.9	82.55	97.77	7029	635	667	0.002	262

[Tsyklon 3] 	[14372]	60 years	+ 4 vanes	0.9 dia?	2004 Jul 9.69	82.53	95.85	6938	548	571	0.002	45

PLE-LC32/1		+ 2 panels

Cosmos 1500	1983-99 B	1983 Sep 28.33	Cylinder	7.4 long	1983 Sep 29.7	82.54	97.76	7029	635	666	0.002	274

3rd stage	[14373]	60 years	2200?	2.4 dia	2004 Jul 11.46	82.54	97.17	7002	609	637	0.002	312

Ekran 11	1983-100 A	1983 Sep 29.74	Cylinder	-	1983 Oct 3.7	0.43	1435.61	42156	35768	35788	0.0002	147

[Proton 8K82K 	[14377]	5 million	+ plate		1983 Dec 1.5	0.26	1436.10	42167	35782	35796	0.0002	65

318-01/11S86 50L]	BAI-LC200P	years	2000?		2004 Jul 7.97	13.04	1436.30	42169	35762	35818	0.007	87

D	Ekran 11	1983-100 B	1983 Sep 29.74	Cylinder	6.5 long?	1983 Sep 29.9	51.60	88.33	6573	189	201	0.001	87

third stage	[14378]	3 days		4 dia

1983 Oct 2

D	Ekran 11	1983-100 C	1983 Sep 29.74	Irregular	-	1983 Sep 29.9	51.60	88.26	6570	190	193	0.0003

4th stage casing 	[14379]	1 day

1983 Sep 30

*	Length before and after hollow solar-cell skirt extended.

D	Ekran 11	1983-100 D	1983 Sep 29.74

Ullage motor	[14389]	261 days

1984 Jun 16

D	Ekran 11	1983-100 E	1983 Sep 29.74

Ullage motor	[14390]	211 days

1984 Apr 27

Ekran 11	1983-1OO F	1983 Sep 29.74	Cylinder	5.5 long	1983 Oct 3.7	0.67	1430.05	42047	35560	35778	0.003	344

Block DM 4th stage 	[14394]	5 million	17300 full	4.0 dia	2004 Jul 9.79	12.83	1425.07	41949	35494	35646	0.002	306

years

D	Cosmos 1501	1983-101 A	1983 Sep 30.46	-	-	1983 Oct 3.2	82.94	94.46	6869	468	514	0.003	326

[Kosmos 11K65M 	[14380]	2065 days

65093-482]	PLE	1989 May 26

D	Cosmos 1501	1983-1O1 B	19$3 Sep 30.46	Cylinder	7.4 long	1983 Oct 1.8	82.94	94.38	6865	460	514	0.004	338

2nd stage	[14381]	2008 days	2200?	2.4 dia

1989 Mar 30

D	Fragments *	1983-101 C-AB	 24 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 1502	1983-102 A	1983 Oct 5.50	Cylinder?	4 long?	1983 Oct 8.2	65.84	92.35	6769	369	412	0.003	326

[Kosmos 11K65M 	[14395]	2008 days		2 dia?

65039-540]	PLE	1985 Aug 29

D	Cosmos 1502	1983-102 B	1983 Oct 5.50	Cylinder	7.4 long	1983 Oct 9.7	65.84	92.27	6765	362	411	0.004	330

2nd stage	[14396]	240 days	2200?	2.4 dia

1984 Jun 1

Cosmos 1503	1983-103 A	1983 Oct 12.01	Cylinder +	2 long?	1983 Oct 16.5	74.05	100.89	7178	790	810	0.001	346

[Kosmos 11K65M 	[14401]	120 years	paddles?	1 dia?	2004 Jul 7.85	74.04	100.60	7165	777	797	0.001	243

65039-543]	PLE		750?

Cosmos 1503	1983-103 B	1983 Oct 12.01	Cylinder	7.4 long	1983 Oct 12.6	74.05	100.79	7173	781	809	0.002	8

2nd stage	[14402]	100 years	2200?	2.4 dia	2004 Jul 7.74	74.05	100.37	7154	756	795	0.003	202

*	These fragments are calibration targets.

D	Cosmos 1504	1983-104 A	1983 Oct 14.42	Sphere-	7 long?	1983 Oct 14.9	64.88	89.27	6617	173	305	0.01	62

R	[Soyuz 11A511U] 	[14403]	53 days	cylinder	2.4 dia

BAI	1983 Dec 6	6700?

D	Cosmos 1504	1983-104 B	1983 Oct 14.42	Cylinder	7.5 long	1983 Oct 15.0	64.88	89.00	6604	171	280	0.008	57

Block I 3rd stage 	[14404]	3 days	2500?	2.6 dia

1983 Oct 17

Intelsat-5 7	1983-105 A	1983 Oct 19.03	Box + dishes	15.9 span	1983 Oct 19.0	8.67	634.86	24469	180	36001	0.732	178

[Ariane-1 07]	[14421]	> million	+ 2 vanes	6.4 wide	1983 Oct 21.4	0.29	1387.66	41211	34102	35563	0.018	126

KOU-ELA1	years	1928 full?		1983 Nov 1.0	0.46	1433.3	42110	35513	35950	0.005	-

2004 Jul 1.93	9.75	1444.30	42325	35927	35966	0.0005	323

D	Ariane-1 07 #	1983-105 B	1983 Oct 19.03	Cylinder	8.6 long	1983 Oct    22.3	8.52	612.69	23896	163	34872	0.726	182

H 8 third stage	[14423]	1293 days	1634	2.6 dia

1987 May 4

Fragment 3th stage	1983 105 C	[48346]	1 piece, in orbit	2021 May 3.53	8.45	363.30	16866	565	20410	0.588	150

D	Progress 18*	1983-106 A	1983 Oct 20.42	Sphere-	7.9 long	1983 Oct 25.1	51.63	91.22	6716	329	347	0.001	352

[Soyuz 11A511U	[14422]	26.8 days	cylinder	2.3 dia

Ts15000-287]	BAI-LC31	1983 Nov 16.2	7020

D	Progress 18	1983-106 B	1983 Oct 20.42	Cylinder	7.5 long	1983 Oct 20.7	51.62	88.66	6589	185	237	0.004	89

Block I 3rd stage 	[14424]	2 days	2500?	2.6 dia

1983 Oct 22

D	Fragment	1983-106 C	[14488]	1983 Nov 20	31 days

D	Fragment	1983-106 D	[14489]	1983 Nov 22	33 days

D	Cosmos 1505	1983-107 A	1983 Oct 21.51	Sphere-	6.5 long?	1983 Oct 26.2	72.88	92.30	6765	358	415	0.004	203

R	[Soyuz 11A511U] 	[14425]	13.7 days	cylinder	2.4 dia

PLE	1983 Nov 4.2	6300?

D	Cosmos 1505	1983-107 B	1983 Oct 21.51	Cylinder	7.5 long	1983 Oct 21.9	72.87	89.87	6645	197	337	0.01	85

Block I 3rd stage 	[14426]	9 days	25OO?	2.6 dia

1983 Oct 30

*	Progress 18 docked	with Sovuz-T 9 - Salyut 7 (2nd airlock) on 1983 Oct 22.48,

unddcked on 1983 No	v 13.13 and was de-orbited over the Pacific Ocean.

#	Analyses indicate that there may have been a break-up event of an unknown nature.

D	Cosmos 1505	1983-107 C	1983 Oct 21.51	Cone	1.5 long?	1983 Nov 4.6	72.88	92.28	6764	357	414	0.004	182

engine	[14481]	415 days	600?	2 dia?

1984 Dec 9	full

D	Fragment	1983-107 D	[14482]	1984 Jan 3	74 days

D	Fragment	1983-107 E	[14560]	1984 Feb 1	103 days

D	Fragment	1983-107 F	[14561]	1984 Feb 26	128 days

D	Fragment	1983-107 G	[14674]	1984 Feb 1	103 days

Cosmos 1506	1983-108 A	1983 Oct 26.72	Cylinder	2.1 long	1983 Oct 28.0	82.93	104.80	7362	953	1015	0.004	289

[Kosmos 11K65M 	[14450]	1200 years	810	2.0 dia	2004 Jul 6.83	82.93	104.65	7357	945	1011	0.004	79

47122-331]	PLE

Cosmos 1506	1983-108 B	1983 Oct 26.72	Cylinder	7.4 long	1983 Oct 28.0	82.93	104.68	7356	953	1003	0.003	287

2nd stage	[14451]	600 years	2200?	2.4 dia	2004 Jul 7.82	82.93	104.52	7351	948	996	0.003	12

Meteor-2 10	1983-109 A	1983 Oct 28.38	Cylinder+	5 long?	1983 Oct 29.4	81.17	101.36	7200	754	890	0.009	260

[Vostok 8A92M] 	[14452]	500 years	2 vanes	1.5 dia?	2004 Jul 7.92	81.16	101.00	7185	740	872	0.009	44

PLE		2750?

Meteor-2 10	1983-109 B	1983 Oct 28.38	Cylinder	3.8 long	1983 Oct 30.2	81.17	101.39	7202	745	902	0.011	235

Block E 3rd stage 	[14453]	400 years	1440	2.6 dia	2004 Jul 7.99	81.17	101.12	7190	734	888	0.011	51

Fragment	1983-109 C	[14454]			2004 Jul 6.95	81.16	101.03	7186	738	878	0.010	42

1983-109 D	[38536]			2012 Jun 29.46	81.15	100.40	7156	730	824	0.007	203

1983-109 E	[38537]			2012 Jun 29.10	81.16	100.53	7162	730	838	0.008	222

1983-109 F	[38538]			2012 Jun 24.50	81.16	100.50	7161	726	838	0.008	227

D	Cosmos 1507	1983-11O A	1982 Oct 29.35	Cylinder?	-	1983 Oct 30.8	65.06	93.34	6817	435	443	0.001	266

[Tsyklon 2] 	[14455]	1390 days

BAI-LC90	1987 Aug 19

D	Cosmos 1507	1983-110 B	1983 Oct 29.35	Cylinder	8 long?	1983 Oct 29.6	65.05	89.18	6613	112	357	0.019	53

2nd stage	[14456]	< 0.7 day	1500?	2.5 dia?

1983 Oct 29

Cosmos 1508*	1983-111 A	1983 Nov 11.52	Octagonal	1.8 long?	1983 Nov 11.8	82.93	109.07	7561	400	1966	0.104	129

[Kosmos 11K65M 	[14483]	30 years	ellipsoid?	1.5 dia?	2004 Jul 7.91	82.91	105.50	7375	389	1604	0.082	16

65093-470]	PLE		550?

Cosmos 1508	1983-111 B	1983 Nov 11.52	Cylinder	7.4 long	1983 Nov 11.8	82.93	108.87	7551	391	1955	0.104	129

2nd stage	[14484]	30 years	2200?	2.4 dia	2004 Jul 10.88	82.85	98.98	7089	352	1091	0.051	42

D	Cosmos 1509	1983-112 A	1983 Nov 17.51	Sphere-	6.5 long?	1983 Nov 18.2	72.86	89.71	6638	227	292	0.005	76

R	[Soyuz 11A511U] 	[14490]	13.8 days	cylinder	2.4 dia

PLE	1983 Dec 1.3	6300?

D	Cosmos 1509	1983-112 B	1983 Nov 17.51	Cylinder	7.5 long	1983 Nov 17.6	72.85	89.23	6614	195	276	0.006	84

Block I 3rd stage 	[14498]	5 days	2500?	2.6 dia

1983 Nov 22

D	Cosmos 1509	1983-112 C	1983 Nov 17.51	Cone	1.5 long?	1983 Dec 2.6	72.85	89.62	6633	227	283	0.004	43

engine	[14535]	40 days	600?	2 dia?

1983 Dec 27	full

D	Fragment	1983-112 D	[14536]	1983 Dec 5	18 days

D	Fragment	1983-112 E	[14539]	1983 Dec 3	16 days

D	Fragment	1983-112 F	[14540]	1983 Dec 7	20 days

D	Fragment	1983-112 G	[14541]	1983 Dec 2	15 days

DMSP B5D2-02	1983-113 A	1983 Nov 18.27	Cylinder	6.4 span	1983 Nov 18.5	98.74	101.42	7203	816	833	0.001	247

[Atlas 58E]	[14506]	80 years	+ panel	6.4 long	2004 Jul 7.93	98.87	100.93	7181	792	810	0.001	286

VDB-SLC3W		751	1.68 dia?

D?	DMSP B5D2-02	1983-113 B	1983 Nov 18.27	1991 Sep 2?	2845 days?	1991 sep 14.46	9.41	1436.05	42164	35771	35800	0.0003	30

Star-37S AKM	[14553]

Fragments	1983-113 C-H	6 pieces, 5 have decayed.		For orbital information see extra pages at the end of the year

D	Molniya-1 59	1983-114 A	1983 Nov 23.70	Windmill	3.4 long	1983 Nov 27.7	62.81	702.23	26172	442	39145	0.739	280

[Molniya 8K78M/ML]	[14516]	6551 days	+ 6 vanes	1.6 dia	1983 Dec 18.3	62.81	717.70	26554	476	39875	0.742	280

PLE	2001 Oct 30	1000?		2001 Oct 29.28	62.53	98.25	7054	81	1269	0.084	273

D	Molniya-1 59	1983-114 C	1983 Nov 23.70	Irregular	-	1983 Nov 24.2	62.82	91.07	6706	207	449	0.018	135

4th stage casing 	[14518]	22 days

1983 Dec 15

*	2500th successful space launch.

D	Molniya-1 59	1983-114 B	1983 Nov 23.70	Cylinder	7.5 long	1983 Nov 24.5	62.82	90.92	6699	192	449	0.019	125

Block I 3rd stage 	[14517]	17 days	2500?	2.6 dia

1983 Dec 10

D	Molniya-1 59	1983-114 D	1983 Nov 23.70	Cylinder	2.0 long	1983 Nov 26.2	62.79	699.31	26101	443	39003	0.739	280

Block L 4th stage 	[14520]	6272.26 days	440	2.0 dia

2001 Jan 24.96

L	Cosmos 1510	1983-115 A	1983 Nov 24.52	-	-	1983 Nov 25.2	73.62	116.08	7882	1481	1526	0.003	281

[Tsyklon 3] 	[14521]	10000 years			2004 Jul 10.25	73.62	116.02	7880	1479	1524	0.003	290

PLE-LC32

Cosmos 1510	1983-115 B	1983 Nov 24.52	Cylinder	7.4 long	1983 Nov 25.5	73.62	116.03	7880	1480	1523	0.003	284

3rd stage	[14522]	10000 years	2200?	2.4 dia	2004 Jul 8.54	73.62	115.98	7878	1479	1520	0.003	287

D	STS 9*	1983-116 A	1983 Nov 28.67	Cylinder +	37.1 long	1983 Nov 30.6	57.02	89.39	6624	239	252	0.001	289

6M	(Columbia F6)	[14523]	10.32 days	delta wing	17.4 high

R	[Shuttle]	CC-LC39A	1983 Dec 8.99	69004	23.8 span

empty

D	Cosmos 1511	1983-117 A	1983 Nov 30.57	Sphere-	7 long?	1983 Dec 1.3	67.14	89.66	6636	172	343	0.013	71

R	[Soyuz 11A511U] 	[14530]	44 days	cylinder	2.4 dia

PLE-LC41/1	1984 Jan 13	6700?

D	Cosmos 1511	1983-117 B	1983 Nov 30.57	Cylinder	7.5 long	1983 Dec 1.1	67.14	89.52	6629	171	330	0.012	73

Block I 3rd stage 	[14531]	5 days	2500?	2.6 dia

1983 Dec 5

Gorizont 8	1983-118 A	1983 Nov 30.58	Cylinder +	-	1983 Dec 12.3	1.45	1436.18	42166	35718	35858	0.002	198

[Proton 8K82K 	[14532]	>million	dish+ panels		1983 Dec 16.3	1.43	1436.30	42171	35617	35968	0.004	82

308-02/11S86 41L]	BAI-LC200L	years	2000?		2004 Jul 5.07	12.72	1465.38	42736	36245	36470	0.003	344

D	Gorizont 8	1983-118 B	1983 Nov 30.58	Cylinder	6.5  long?	1983 Dec 1.0	51.63	88.18	6566	183	192	0.001	203

third stage	[14533]	2 days		4 dia

1983 Dec 2

*	Launched from Cape Canaveral; landed at Edwards AFB California.

Cargo bay carried European Spacelab 1 (not separated). Crew: five	US and one European.

D	Gorizont 8	1983-118C	1983 Nov 30.58	Irregular	-	1983 Nov 30.9	51.62	88.10	6562	178	189	0.001	124

4th stage casing 	[14534]	1 day

1983 Dec 1

D	Gorizont 8	1983-118 D	1983 Nov 30.58

Ullage motor	[14537]	892 days

1986 May 10 A

D	Gorizont 8	1983-118 E	1983 Nov 30.58

Ullage motor	[14538]	1759 days

1988 Sep 23

Gorizont 8	1983-1]8 F	1983 Nov 30.58	Cylinder	5.5 long	1983 Dec 3.4	1.46	1442.15	42282	35698	36110	0.005	109

Block DM 4th stage 	[14548]	>million	17300 full	4.0 dia	2004 Jul 10.01	12.34	1435.90	42161	35585	35979	0.005	125

years

D	Cosmos 1512	1983-119 A	1983 Dec 7.51	Sphere-	6.5 long?	1983 Dec 9.5	72.86	92.31	6765	356	418	0.005	207

R	[Soyuz 11A511U] 	[14542]	13.8 days	cylinder	2.4 dia

PLE	1983 Dec 21.3	6300?

D	Cosmos 1512	1983-119 B	1983 Dec 7.51	Cylinder	7.5 long	1983 Dec 8.8	72.86	90.00	6652	197	350	0.012	80

Block I 3rd stage 	[14543]	10 days	2500?	2.6 dia

1983 Dec 17

D	Cosmos 1512	1983-119 G	1983 Dec 7.51	Cone	1.5 long?	1983 Dec 22.1	72.86	92.25	6762	354	414	0.004	180

engine	[14575]	508 days	600?	2 dia?

1985 Apr 28	ful1

D	Fragments	1983-119 C-F,H-M 9 pieces, all have decayed		For orbital information see extra pages at the end of the year

Cosmos 1513	1983-120 A	1983 Dec 8.26	Cylinder	2.1 long	1983 Dec 8.6	82.94	104.94	7369	963	1019	0.004	294

[Kosmos 11K65M 	[14546]	1200 years	810	2.0 dia	2004 Jul 7.14	82.94	104.80	7364	958	1012	0.004	263

65019-528]	PLE

Cosmos 1513	1983-120 B	1983 Dec 8.26	Cylinder	7.4 long	1983 Dec 10.2	82.94	104.8	7362	962	1006	0.003	280

2nd stage	[14547]	600 years	2200?	2.4 dia	2004 Jul 8.53	82.93	104.58	7353	939	1010	0.005	131

D	Cosmos 1514*	1983-121 A	1983 Dec 14.29	Sphere-	5.0 long	1983 Dec 15.3	82.31	89.28	6616	215	260	0.003	81

B	(Bion 6)	[14549]	4.9 days	cylinder	2.4 dia

R	[Soyuz 11A511U] 	PLE-LC41/1	1983 Dec 19.2	5700?

D	Cosmos 1514	1983-121 B	1983 Dec 14.29	Cylinder	7.5 long	1983 Dec 14.8	82.31	89.17	6610	210	254	0.003	68

Block I 3rd stage 	[14550]	5 days	2500?	2.6 dia

1983 Dec 19

Cosmos 1515	1983-122 A	1983 Dec 15.52	-	-	1983 Dec 16.5	82.53	97.78	7030	638	665	0.002	282

[Tsyklon 3] 	[14551]	60 years			2004 Jul 11.20	82.52	95.87	6939	552	568	0.001	316

PLE-LC32

Cosmos 1515	1983-122 B	1983 Dec 15.52	Cylinder	7.4 long	1983 Dec 19.1	82.53	97.76	7029	637	664	0.002	280

3rd stage	[14552]	60 years	2200?	2.4 dia	2004 Jul 11.01	82.52	97.18	7002	612	635	0.002	226

D	Molniya-3 22	1983-123 A	1983 Dec 21.26	Windmill +	4.2 long?	1983 Dec 22.3	62.82	736.04	27005	618	40636	0.741	288

[Molniya 8K78M/ML]	[14570]	3528 days	6 vanes	1.6 dia	1984 Feb 19.2	62.89	717.78	26556	603	39752	0.737	288

PLE-LC41/1	1993 Aug 18	1500?

D	Molniya-3 22	1983-123 B	1983 Dec 21.26	Cylinder	7.5 long	1983 Dec 21.7	62.84	92.68	6785	215	599	0.028	121

Block I 3rd stage 	[14571]	55 days	2500?	2.6 dia

1984 Feb 14

D	Molniya-3 22	1983-123 C	1983 Dec 21.26	Irregular	-	1983 Dec 21.7	62.85	92.76	6789	197	625	0.031	117

4th stage casing 	[14572]	45 days

1984 Feb 4

D	Molniya-3 22	1983-123 D	1983 Dec 21.26	Cylinder	2.0 long	1983 Dec 27.4	62.83	732.61	26922	617	40470	0.740	288

Block L 4th stage 	[14582]	3777 days	440	2.0 dia

1994 Apr 24

*	Biological satellite: carried 2	monkeys, 18 rats, insects and plants.

D	Cosmos 1516	1983-124 A	1983 Dec 27.40	Sphere-	7 long?	1983 Dec 28.1	64.88	89.22	6614	197	275	0.006	74

R	[Soyuz 11A511U] 	[14583]	44 days	cylinder	2.4 dia

BAI	1984 Feb 9	6700?

D	Cosmos 1516	1983-124 B	1983 Dec 27.40	Cylinder	7.5 long	1983 Dec 27.8	64.89	88.98	6603	192	257	0.005	66

Block I 3rd stage 	[14584]	4 days	2500?	2.6 dia

1983 Dec 31

D	Cosmos 1517*	1983-125 A	1983 Dec 27.42	Delta wing	2.5 long?	1983 Dec 27.5	50.66	88.44	6579	180	221	0.003	309

R	[Kosmos 65MP]	[14585]	0.05 day	with fins	2.1 span?

KY-LC107	1983 Dec 27.47	1000?

D	Cosmos 1517	1983~125 B	1983 Dec 27.42	Cylinder	7.4 long?	1983 Dec 27.7	50.67	88.39	6576	179	217	0.003	307

2nd stage	[14586]	2 days	2200?	2.4 dia?

1983 Dec 29

D	Cosmos 1518	1983-126 A	1983 Dec 28.16	Windmill +	4.2 long?	1983 Dec 29.7	62.91	709.20	26345	585	39348	0.736	320

[Molniya 8K78M/2BL]	[14587]	5379 days	6 vanes	1.6 dia	1984 Feb 4.6	63.02	717.61	26551	622	39725	0.736	320

PLE-LC16/2	1998 Sep 19	1250?

D	Cosmos 1518	1983-126 B	1983 Dec 28.16	Cylinder	7.5 long	1983 Dec 28.8	62.83	92.05	6754	214	537	0.024	122

Block I 3rd stage 	[14588]	42 days	2500?	2.6 dia

1984 Feb 8						-

D	Cosmos 1518	1983-126 C	1983 Dec 28.16	Irregular	-	1983 Dec 28.7	62.87	92.43	6773	198	591	0.029	122

4th stage casing 	[14589]	38 days

1984 Feb 4

D	Cosmos 1518	1983-126 D	1983 Dec 28.16	Cylinder	2.0 long	1983 Dec 29.7	62.91	705.51	26251	584	39162	0.735	320

Block L 4th stage 	[14596]	5362 days	440	2.0 dia

1998 Sep 2

*	Subscale spaceplane launched from Kapustin Yar; water recovery 1 orbit later from Black Sea.

L	Cosmos 1519*	1983-127 A	1983 Dec 29.04	Cylinder	-	1983 Dec 31.3	64.75	673.84	25461	19026	19139	0.002	256

(Glonass 7)	[14590]	1 million	+ panels  +		1984 Jan 9.2	64.76	675.73	25508	19104	19156	0.001	204

[Proton 8K82K 	BAI-LC200P	years	boom		2004 Jul 6.95	65.39	675.72	25508	19098	19161	0.001	198

320-02/11S861 4L]

L	Cosmos 1520*	1983-127 B	1983 Dec 29.04	Cylinder	-	1983 Dec 31.3	64.75	673.54	25453	19004	19146	0.003	258

(Glonass 8)	[14591]	1 million	+ panels  +		1984 Jan 20.9	64.77	675.73	25508	19090	19170	0.002	210

years	boom		2004 Jul 6.48	65.38	675.72	25508	19061	19198	0.003	185

L	Cosmos 1521*	1983-127 C	1983 Dec 29.04	Cylinder	-	1983 Dec 31.3	64.76	673.42	25450	19010	19134	0.002	260

(Glonass 9)	[14592]	1 million	+ panels  +		2004 Jul 6.45	65.38	673.40	25449	18950	19192	0.005	205

years	boom

D	Cosmos 1519	1983-127 D	1983 Dec 29.04	Cylinder	6.5 long?	1983 Dec 29.6	51.62	88.04	6559	173	188	0.001	287

third stage	[14593]	2 days		4 dia

1983 Dec 31

D	Cosmos 1519	1983-127 E	1983 Dec 29.04	Irregular	-	1983 Dec 29.5	51.62	87.94	6554	162	189	0.002	242

4th stage casing 	[14594]	<1 day

1983 Dec 29

Cosmos 1519	1983-127 F	1983 Dec 29.04	Cylinder	5.5 long	1983 Dec 31.3	64.75	673.1	25442	19001	19127	0.002	265

Block DM 4th stage 	[14595]	1 million	17300 full	.0 dia	2004 Jul 6.19	65.36	673.08	25441	18925	19200	0.005	201

years

Cosmos 1519	1983-127 G	1983 Dec 29.04			2004 Jul 7.31	52.10	319.13	15470	447	17735	0.559	198

Ullage motor 	[14607]	100 years

Cosmos 1519	1983-127 H	1983 Dec 29.04			2004 Jul 6.83	51.55	312.03	15239	310	17411	0.561	319

Ullage motor 	[14608]	disintegrated

Fragments	1983-127 J-Q	7 pieces,  5 have decayed		For orbital information see extra pages at the end of the year

*	Triple Glonass payload.

Text in box is from "History of on-orbit satellite fragmentations", 13th edition, May 2004.

Orbital Debris Program Office, Johnson Space Centre, NASA, Houston, TX 77058.

NOAA 8 fragments; 11 pieces, 8 have decayed.

D	1983-22 C	[14477]	1991 May 21	2976 days

A malfunction on NOAA 8 caused a battery to overcharge, resulting in a minor explosion of the battery 1985 Dec 30 at 10:05 UT near 68ºS 300ºE. The spacecraft was operational at the time of the event. Six new fragments were detected and cataloged. All decayed by February 1989, leaving the parent still in orbit. New piece catalogued in 2005.

D	1983-22 D	[16442]	1986 Feb 9	1049 days

D	1983-22 E	[16443]	1986 Jan 16	1025 days

D	1983-22 F	[16444]	1986 Jan 20	1029 days

D	1983-22 G	[16502]	1988 Feb 21	1791 days

D	1983-22 H	[16503]	1989 Feb 19	2155 days

D	1983-22 J	[16504]	1986 Nov 13	1326 days

D	1983-22 K	[28604]	2005 Oct 16	8239 days		2005 Apr 30.03	98.78	98.40	7061	646	718	0.005	129

2005 Oct 16.13	99.07	91.70	6736	341	374	0.002	245

1983-22-L	[38839]				2012 Oct 2.84	98.47	100.43	7157	771	786	0.001	118

1983-22-M	[38840]				2012 Oct 4.82	98.47	100.70	7170	781	802	0.001	159

1983-22 N	[38841]				2012 Oct 4.26	98.47	100.57	7164	773	797	0.002	164

Cosmos 1449 fragments; 6 pieces, all have decayed.

D	1983-24 C	[13962]	1983 Apr 1	1 day

D	1983-24 D	[13963]	1983 Apr 10	10 days

D	1983-24 E	[13993]	1983 Apr 23	23 days

D	1983-24 F	[13994]	1983 May 18	48 days

D	1983-24 H	[13996]	1983 Jun 24	85 days

D	1983-24 J	[13997]	1983 Apr 22	22 days

Rohini 3 fragments; 4 pieces, all have decayed.

D	1983-33 C	[14004]	1987 Feb 10	1395 days

D	1983-33 D	[14224]	1988 Jun 6	1146 days

D	1983-33 E	[14225]	1989 Jan 4	2089 days

D	1983-33 F	[14397]	1984 Feb 4	293 days

Cosmos 1453 fragments; 22 pieces, aal have decayed.

Analyses indicate that the Cosmos 1453 payload is the most likely debris source. These fragments are probably calibration targets.

D	1983 34 C	[14577]	1984 Mar 25	341 days

D	1983 34 D	[14578]	1984 Apr 1	348 days

D	1983 34 E	[14597]	1984 Jun 8	416 days

D	1983 34 F	[14598]	1984 Dec 1	592 days

D	1983 34 G	[14730]	1984 May 21	398 days

D	1983 34 H	[14731]	1984 Apr 10	357 days

D	1983 34 J	[14853]	1984 May 30	407 days

D	1983 34 K	[14854]	1984 Jun 6	414 days

D	1983 34 L	[14936]	1984 Sep 5	505 days

D	1983 34 M	[14937]	1984 Aug 19	488 days

D	1983 34 N	[15007]	1984 Nov 2	563 days

D	1983 34 P	[15008]	1984 Nov 22	583 days

D	1983 34 Q	[15013]	1984 Dec 12	603 days

D	1983 34 R	[15014]	1984 Dec 3	594 days

D	1983 34 S	[15015]	1984 Dec 22	613 days

D	1983 34 T	[15016]	1984 Nov 14	575 days

D	1983 34 U	[15017]	1984 Nov 6	567 days

D	1983 34 V	[15018]	1984 Oct 24	554 days

D	1983 34 W	[15019]	1984 Oct 19	549 days

D	1983 34 X	[15020]	1984 Oct 14	544 days

D	1983 34 Y	[15376]	1985 Jul 15	818 days

D	1983 34 Z	[15377]	1985 May 22	764 days

Cosmos 1456 fragments; 5 pieces, all have decayed

Cosmos 1456 was another spacecraft of the Cosmos 862-type to experience a fragmentation. The spacecraft may have been active at the time of the event, having last made a station-keeping maneuver on 22 June 1983. The next station-keeping manoeuvre should have occurred in the second half of August or early September 1983. The spacecraft began drifting off station immediately after the event 1983 Aug 13 and never recovered.

Molniya Block I 3rd stage fragments

D	1983-38 D	[14038]	1983 May 17	22 days

D	1983-38 F	[14043]	1983 Aug 30	127 days

Cosmos 1456 fragments

D	1983-38 G	[14297]	1998 May 11	5495 days

D	1983-38 H	[14301]	1998 May 10	5494 days

D	1983-38 J	[14306]	1997 Nov 11	5307 days

Cosmos 1460 fragments; 8 pieces, all have decayed.

D	1983-43 C	[14061]	1983 May 21	15 days

D	1983-43 D	[14062]	1983 May 6	< 1 day

D	1983-43 E	[14063]	1983 May 8	2 days

D	1983-43 F	[14078]	1983 Jul 11	66 days

D	1983-43 H	[14080]	1983 Aug 8	94 days

D	1983-43 J	[14082]	1983 May 25	19 days

D	1983-43 K	[14083]	1983 May 27	21 days

D	1983-43 L	[14247]	1983 Aug 17	72 days

Cosmos 1461 fragments; 187 pieces, 163 have decayed.

Cosmos 1461 was the twelfth spacecraft of the Cosmos 699-type to experience a fragmentation. Cosmos 1461 entered a natural decay regime more than 13 months prior to first event. After the first event, 1985 Mar 11 at 09:40 UT near 4ºS 196ºE, as many as 20 fragments were detected but only six new objects were cataloged. The second event occurred 1985 May 13 at 01:33 UT near 10ºN 82ºE and produced considerably more debris. These events followed the pattern set by Cosmos 1220 and Cosmos 1260.

D	1983-44 C	[15601]	1985 Mar 23	686 days

D	1983-44 D	[15602]	1985 Mar 15	678 days

D	1983-44 E	[15603]	1986 Oct 29	1271 days

D	1983-44 F	[15604]	1985 Apr 23	717 days

D	1983-44 G	[15605]	1988 Sep 4	1947 days

D	1983-44 H	[15606]	1988 Oct 22	1995 days

D	1983-44 J	[15681]	1988 Aug 18	1930 days

D	1983-44 K	[15682]	1989 Feb 18	2114 days

D	1983-44 L	[15683]	1988 Aug 24	1936 days

D	1983-44 M	[15684]	1989 Oct 6	2344 days

D	1983-44 N	[15685]	1990 Dec 16	2780 days

D	1983-44 P	[15686]	1988 Oct 22	1995 days

D	1983-44 Q	[15687]	1989 Mar 27	2151 days

D	1983-44 R	[15688]	1987 Jul 4	1519 days

D	1983-44 S	[15689]	1987 Jul 24	1539 days

D	1983-44 T	[15690]	1989 Feb 1	2097 days

D	1983-44 U	[15691]	1988 Apr 7	1797 days

D	1983-44 V	[15692]	1989 Jan 17	2082 days

D	1983-44 W	[15703]	1989 Feb 17	2113 days

D	1983-44 X	[15704]	1989 Mar 9	2133 days

D	1983-44 Y	[15705]	1989 Apr 28	2183 days

D	1983-44 Z	[15706]	1989 Mar 26	2150 days

D	1983-44 AA	[15707]	1999 Dec 27	6078 days

D	1983-44 AB	[15708]	1989 Oct 21	2359 days

D	1983-44 AC	[15709]	1989 Mar 8	2132 days

D	1983-44 AD	[15710]	1989 Aug 5	2282 days

D	1983-44 AE	[15711]	1987 Aug 15	1561 days

D	1983-44 AF	[15712]	1988 Dec 16	2050 days

D	1983-44 AG	[15713]	1991 Aug 17	3024 days

D	1983-44 AH	[15716]	1989 May 23	2208 days

D	1983-44 AJ	[15717]	1989 Jun 3	2219 days

D	1983-44 AK	[15718]	1990 Sep 2	2675 days

D	1983-44 AL	[15719]	1991 Mar 22	2876 days

D	1983-44 AM	[15720]	1989 Mar 20	2144 days

D	1983-44 AN	[15721]	1987 Apr 15	1439 days

D	1983-44 AP	[15722]	1990 Apr 9	2529 days

D	1983-44 AQ	[15723]	1989 Feb 19	2115 days

D	1983-44 AR	[15724]	1989 Jun 26	2242 days

D	1983-44 AS	[15725]	1985 Jun 6	761 days

D	1983-44 AT	[15726]	1989 Mar 5	2129 days

D	1983-44 AU	[15727]	1989 Mar 16	2140 days

D	1983-44 AV	[15728]	1989 Nov 28	2427 days

D	1983-44 AW	[15729]	1990 Jul 18	2629 days

D	1983-44 AX	[15730]	1985 Jun 11	766 days

D	1983-44 AY	[15731]	1990 Apr 29	2549 days

D	1983-44 AZ	[15736]	1989 Jun 26	2242 days

D	1983-44 BA	[15737]	1988 Sep 14	1957 days

D	1983-44 BB	[15796]	1989 Jun 14	2230 days

D	1983-44 BC	[15797]	1989 Feb 4	2100 days

D	1983-44 BD	[15798]	1987 May 26	1480 days

D	1983-44 BE	[15799]	1990 Nov 15	2749 days

D	1983-44 BF	[15800]	1989 Apr 18	2173 days

D	1983-44 BG	[15801]	1990 Dec 1	2765 days

D	1983-44 BH	[15802]	1988 Feb 28	1758 days

D	1983-44 BJ	[15803]	1988 Oct 21	1994 days

D	1983-44 BK	[15812]	1988 Mar 4	1763 days

D	1983-44 BL	[15813]	1985 Oct 22	899 days

D	1983-44 BM	[15814]	1990 Jun 3	2584 days

D	1983-44 BN	[15815]	1992 Apr 29	3280 days		1992 Apr 29.23	64.97	88.65	6586	197	218	0.002	287

D	1983-44 BP	[15816]	1989 Jun 10	2318 days

D	1983-44 BQ	[15817]	1989 Apr 27	2185 days

D	1983-44 BR	[16774]	1989 Apr 11	2166 days

D	1983-44 BS	[16775]	1989 Mar 4	2128 days

D	1983-44 BT	[16776]	1989 Dec 16	2415 days

D	1983-44 BU	[16777]	1989 Feb 12	2108 days

D	1983-44 BV	[16778]	1989 Mar 29	2153 days

D	1983-44 BW	[16779]	1989 Jan 13	2078 days

D	1983-44 BX	[16780]	1990 Jul 2	2613 days

D	1983-44 BY	[16781]	1988 Dec 10	2044 days

D	1983-44 BZ	[16782]	1990 Jun 22	2603 days

D	1983-44 CA	[17010]	1989 Mar 22	2146 days

D	1983-44 CB	[17011]	1989 Jan 3	2068 days

D	1983-44 CC	[17012]	1989 Jun 22	2340 days

D	1983-44 CD	[17013]	1990 Apr 25	2545 days

D	1983-44 CE	[17014]	1989 Feb 27	2123 days

D	1983-44 CF	[17015]	1988 Dec 22	2056 days

D	1983-44 CG	[17016]	1989 May 13	2198 days

D	1983-44 CH	[17017]	1989 Aug 3	2280 days

D	1983-44 CJ	[17091]	1988 Mar 9	1768 days

D	1983-44 CK	[17096]	1989 Apr 17	2172 days

D	1983-44 CL	[17097]	1989 Apr 30	2185 days

D	1983-44 CM	[17098]	1990 Oct 21	2724 days

D	1983-44 CN	[17099]	1990 Mar 28	2517 days

D	1983-44 CP	[17163]	1989 Jun 13	2229 days

D	1983-44 CQ	[17171]	1989 Mar 17	2141 days

D	1983-44 CR	[17643]	1989 Apr 8	2163 days

D	1983-44 CS	[17644]	1988 Dec 18	2052 days

D	1983-44 CT	[17645]	1989 Apr 11	2166 days

D	1983-44 CU	[17646]	1989 Jan 25	2090 days

D	1983-44 CV	[17647]	1989 Feb 14	2110 days

D	1983-44 CW	[17733]	1988 Dec 22	2056 days

D	1983-44 CX	[17734]	1989 Sep 13	2221 days

D	1983-44 CY	[17735]	1989 May 11	2196 days

D	1983-44 CZ	[17736]	1988 Jan 22	1721 days

D	1983-44 DA	[17737]	1988 Nov 16	2020 days

D	1983-44 DB	[17738]	1989 Oct 2	2340 days

D	1983-44 DC	[17739]	1991 Feb 13	2839 days

D	1983-44 DD	[17740]	1989 Oct 15	2353 days

D	1983-44 DE	[17741]	1989 May 6	2191 days

D	1983-44 DF	[17742]	1988 Nov 3	2007 days

D	1983-44 DG	[17743]	1988 Apr 2	1792 days

D	1983-44 DH	[17744]	1990 Mar 22	2511 days

D	1983-44 DJ	[17745]	1989 Aug 30	2307 days

D	1983-44 DK	[17746]	1989 Oct 12	2350 days

D	1983-44 DL	[17747]	1989 Apr 10	2165 days

D	1983-44 DM	[17748]	1989 Apr 1	2156 days

D	1983-44 DN	[17749]	1989 Apr 17	2172 days

D	1983-44 DP	[17750]	1989 Jul 4	2250 days

D	1983-44 DQ	[17751]	1989 Jun 5	2221 days

D	1983-44 DR	[17752]	1989 Dec 27	2335 days

D	1983-44 DS	[17753]	1989 May 14	2199 days

D	1983-44 DT	[17833]	1989 May 11	2196 days

D	1983-44 DU	[17834]	1989 May 22	2207 days

D	1983-44 DV	[17835]	1989 Jan 19	2084 days

D	1983-44 DW	[17836]	1989 Apr 10	2165 days

D	1983-44 DX	[17837]	1989 Mar 29	2153 days

D	1983-44 DY	[18237]	1988 Dec 21	2055 days

D	1983-44 DZ	[18243]	1989 Sep 7	2253 days

D	1983-44 EA	[18244]	1989 Sep 13	2259 days

D	1983-44 EB	[18245]	1988 Nov 29	2033 days

D	1983-44 EC	[18246]	1989 Feb 13	2109 days

D	1983-44 ED	[18247]	1989 Feb 12	2108 days

D	1983-44 EE	[18248]	1989 Nov 21	2390 days

D	1983-44 EF	[18249]	1988 Dec 21	2420 days

D	1983-44 EG	[18378]	1989 Jul 2	2248 days

D	1983-44 EH	[18379]	1989 Jun 4	2220 days

D	1983-44 EJ	[18473]	1989 Apr 13	2168 days

D	1983-44 EK	[18474]	1990 Aug 28	2670 days

1983-44 EL	[18480]				2004 Jul 8.68	65.00	95.33	6913	493	576	0.006	50

D	1983-44 EM	[18481]	1988 Dec 30	2064 days

D	1983-44 EN	[18482]	1988 Mar 24	1783 days

D	1983-44 EP	[18483]	1989 Apr 23	2178 days

D	1983-44 EQ	[18484]	1988 Oct 18	1991 days

D	1983-44 ER	[18485]	1989 Jan 19	2084 days

D	1983-44 ES	[18493]	1988 Jun 2	1883 days

D	1983-44 ET	[18520]	1989 Jun 16	2232 days

D	1983-44 EU	[18544]	1989 May 23	2208 days

D	1983-44 EV	[18566]	1989 Apr 3	2158 days

D	1983-44 EW	[18694]	1988 Jan 22	1721 days

D	1983-44 EX	[18797]	1989 Aug 11	2288 days

D	1983-44 EY	[18812]	1991 Feb 12	2838 days

D	1983-44 EZ	[18868]	1988 Dec 26	2060 days

D	1983-44 FA	[18869]	1988 Nov 2	2006 days

D	1983-44 FB	[18975]	1988 May 24	1844 days

D	1983-44 FC	[19101]	1989 May 4	2189 days

D	1983-44 FD	[19172]	1989 Oct 27	2365 days

D	1983-44 FE	[19296]	1989 May 15	2200 days

D	1983-44 FF	[19303]	1989 Dec 4	2403 days

D	1983-44 FG	[19305]	1988 Nov 18	2022 days

D	1983-44 FH	[19308]	1989 May 27	2212 days

D	1983-44 FJ	[19310]	1989 Nov 30	2399 days

D	1983-44 FK	[19361]	1989 Apr 7	2162 days

D	1983-44 FL	[19426]	1989 Mar 5	2129 days

D	1983-44 FM	[19427]	1989 Mar 3	2127 days

D	1983-44 FN	[19668]	1990 Jan 16	2446 days

D	1983-44 FP	[19947]	1989 May 19	2204 days

D	1983-44 FQ	[20133]	1989 Jun 10	2256 days

D	1983-44 FR	[26537]	2001 Feb 15	6494 days

D	1983-44 FS	[27495]	2002 Dec 20	7167 days		2002 Dec 18.86	64.98	91.20	6712	321	346	0.002	285

D	1983-44 FT	[28456]	2007 Nov 25	8968 days		2004 Nov 22.15	65.01	97.27	7007	546	710	0.012	37

2007 Nov 23.09	65.06	90.47	6676	274	321	0.004	332

1983-44 FU	[29351]				2006 Aug 22.26	64.98	96.33	6961	522	643	0.009	161

1983-44 FV	[29352]				2006 Aug 22.26	65.00	96.52	6970	522	661	0.010	164

D	1983-44 FW	[29353]	2006 Aug 31	8517 days		2006 Aug 20.86	64.98	94.13	6855	451	503	0.004	180

Latest elset					2006 Dec 2.57	64.90	91.33	6718	330	349	0.001	1

D	1983-44 FX	[33485]	2013 Jan 3	10834 days

2012 Sep 2.51	64.99	94.83	6889	468	553	0.006	347

1983-44 FY	[33486]

D	1983-44 FZ	[33487]	2013 Jan 13	10844 days

2013 Jan 12.64	64.96	89.70	8638	248	271	0.002	321

1983-44 GA	[33488]

1983-44 GB	[33489]

1983-44 GC	[37785]				2011 Aug 24.65	65.01	97.08	6998	533	705	0.012	169

D	1983-44 GD	[38835]	2013 Jun 9	10991 days		2012 Oct 3.80	65.01	96.78	6983	526	683	0.011	353

2013 Jun 9.23	65.00	88.92	6600	205	237	0.002	228

1983 44 GE	[39053]				2012 Dec 25.19	65.00	95.32	6912	479	588	0.008	323

1983 44 GF	[42445]				2017 Apr 3.83	65.00	95.97	6942	517	610	0.007	68

1983 44 GG	[42446]				2017 Apr 3.18	65.00	96.20	6955	522	631	0.008	68

1983 44 GH	[42447]				2017 Apr 2.60	64.99	96.27	6958	524	635	0.008	68

1983 44 GJ	[42448]				2017 Apr 9.62	64.99	95.67	6930	508	594	0.006	61

1983 44 GK	[42449]				2017 Apr 8.15	64.99	94.77	6886	476	539	0.005	51

1983 44 GL	[42450]				2017 Apr 3.75	64.98	94.57	6876	467	528	0.004	50

1983 44 GM	[42451]				2017 Apr 2.60	64.99	95.70	6931	505	599	0.007	64

1983 44 GN	[43085]				2017 Dec 23.81	65.00	96.38	6964	506	663	0.011	322

1983 44 GP	[43086]				2017 Dec 24.52	65.00	96.38	6964	505	665	0.011	322

1983 44 GQ	[43303]				2018 Apr 13.47	65.00	95.72	6932	480	626	0.011	287

1983 44 GR	[43304]				2018 Apr 13.73	65.00	95.83	6938	483	634	0.011	286

1983 44 GS	[43305]				2018 Apr 13.32	65.01	96.20	6955	492	660	0.012	285

1983 44 GT	[43306]				2018 Apr 13.28	65.01	95.47	6920	476	607	0.010	283

1983 44 GU	[43307]				2018 Apr 13.85	65.00	95.42	6917	476	601	0.009	282

1983 44 GV	[43308]				2018 Apr 13.29	65.00	95.48	6921	478	608	0.009	287

1983 44 GW	[48161]				2021 Apr 14.53	65.02	96.28	6959	504	657	0.011	219

Cosmos 1465 fragments; 8 pieces, all have decayed. Fragments G-K are calibration targets.

Analyses indicate that the Cosmos 1465 payload is the most likely debris source.

D	1983-49 C	[14091]	1983 Jul 15	50 days

D	1983-49 D	[14092]	1983 Jul 2	37 days

D	1983-49 E	[14093]	1983 Jul 5	40 days

D	1983-49 F	[14094]	1983 Dec 9	197 days

D	1983-49 G	[14212]	1983 Nov 2	160 days

D	1983-49 H	[14213]	1983 Oct 31	158 dag

D	1983-49 J	[14214] 	1983 Oct 29	156 dag

D	1983-49 K	[14215] 	1983 Oct 25	152 dag

Cosmos 1467 fragments; 6 pieces, all have decayed.

D	1983-52 C	[14102]	1983 Jun 2	2 days

D	1983-52 D	[14103]	1983 Jun 2	2 days

D	1983-52 F	[14118]	1983 Sep 13	105 days

D	1983-52 G	[14119]	1983 Jun 19	19 days

D	1983-52 H	[14120]	1983 Jun 21	21 days

D	1983-52 J	[14121]	1983 Aug 7	68 days

Cosmos 1482 fragments; 6 pieces, all have decayed.

D	1983-71 C	[14187]	1983 Jul 15	2 days

D	1983-71 D	[14188]	1983 Dec 9	149 days

D	1983-71 E	[14217]	1983 Sep 20	69 days

D	1983-71 F	[14218]	1983 Oct 14	93 days

D	1983-71 G	[14219]	1983 Oct 20	99 days

D	1983-71 J	[14231]	1983 jul31	18 days

Cosmos 1484 fragments; 52 pieces, 47 have decayed

Cosmos 1484 was the third of four Resurs-0 prototypes flown in sun-synchronous orbits, and the only one to fragment 1993 Oct 18 at 12:04 UT near 7ºS 111ºE. This is the first sun-synchronous Russian satellite to ever fragment. The NAVSPOC generated 79 analyst satellites on this event.

The fragments C-F are from the Vostok Block Ye 3rd stage.

1983-75 C	[14209]				1983 Jul 25.71	98.02	97.22	7004	589	661	0.005	307

2004 Jul 6.52	97.88	95.58	6925	522	571	0.004	140

2020 Dec 16.75	97.20	94.82	6888	491	528	0.003	5

1983-75 D	[14229]				1983 Jul 27.62	97.95	97.75	7029	620	682	0.004	230

2004 Jul 7.32	97.96	96.50	6970	570	613	0.003	197

2020 Dec 16.88	97.62	96.12	6951	554	590	0.003	268

1983-75 E	[14631]				1984 Jan 10.22	97.91	97.18	7002	600	647	0.003	5

2004 Jul 6.72	97.82	95.28	6911	522	542	0.001	9

2020 Dec 17.04	97.70	93.87	6842	458	469	0.0008	28

1983-75 F	[14928]				1984 Apr 10.67	97.99	97.47	7016	609	665	0.004	168

2004 Jul 7.52	98.01	95.92	6942	536	590	0.004	343

2020 Dec 16.56	97.91	95.17	6905	504	549	0.003	173

D	1983-75 G	[22890]	2000 Feb 6	6041 days		1983 Oct 19.24	97.49	96.43	6967	546	630	0.006	346

2000 Feb 5.70	97.58	88.67	6587	203	213	0.0008	159

D	1983-75 H	[22891]	1994 Mar 12	3884 days		1983 Oct 20.07	97.60	94.27	6862	409	557	0.011	148

1994 Mar 11.66	97.55	88.83	6595	213	220	0.0005	19

D	1983-75 J	[22892]	1996 Mar 26	4629 days		1993 Oct 18.65	98.52	104.65	7357	544	1412	0.059	339

1993 Mar 26.38	98.48	90.23	6664	266	302	0.003	227

D	1983-75 K	[22893]	1994 Jul 9	4003 days		1993 Oct 19.32	97.34	97.33	7010	547	715	0.012	326

1994 Jul 9.03	97.24	89.88	6647	257	281	0.002	204

D	1983-75 L	[22894]	1994 Feb 26	3870 days		1993 Oct 19.09	98.14	94.15	6856	400	555	0.011	162

1994 Feb 25.06	98.09	89.37	6622	239	248	0.0007	57

D	1983-75 M	[22895]	1995 Feb 5	4214 days		1993 Oct 19.50	98.47	95.62	6927	483	614	0.009	86

1995 Feb 5.72	98.36	88.15	6562	174	192	0.001	210

D	1983-75 N	[22896]	1999 Jan 17	5656 days		1983 Oct 19.51	98.34	96.83	6985	526	687	0.011	40

1999 Jan 17.23	88.30	88.53	6580	196	207	0.0008	284

D	1983-75 P	[22897]	1999 Nov 21	5964 days		1993 Oct 19.12	98.17	98.50	7066	542	833	0.021	16

1999 Nov 21.14	97.96	89.50	6629	237	263	0.002	12

D	1983-75 Q	[22898]	1993 Nov 12	3764 days		1993 Oct 19.49	97.80	94.73	6884	457	553	0.007	154

1993 Nov 6.27	97.79	93.32	6816	412	462	0.004	111

D	1983-75 R	[22899]	1994 Apr 1	3904 days		1993 Oct 19.47	97.99	98.90	7085	553	859	0.022	358

1994 Mar 31.44	99.05	91.53	6728	323	375	0.004	210

D	1983-75 S	[22900]	1993 Dec 6	3788 days		1983 Oct 19.11	97.61	109.52	7583	549	1860	0.086	354

1993 Nov 20.11	98.13	105.62	7401	375	1670	0.087	280

D	1983-75 T	[22901]	1993 Nov 19	3771 days		1993 Oct 19.64	97.51	95.88	6940	544	578	0.002	291

1993 Nov 16.35	97.54	90.83	6694	304	327	0.002	188

D	1983-75 U	[22902]	1999 Jul 4	5824 days		1993 Oct 21.55	98.39	97.25	7005	536	718	0.013	21

1999 Jul 4.03	98.29	88.45	6577	192	204	0.001	180

D	1983-75 V	[22903]	1994 Jan 19	3832 days		1993 Oct 20.32	97.66	98.85	7552	552	1795	0.082	349

1994 Jan 9.59	97.55	96.16	6959	433	726	0.021	115

D	1983-75 W	[22918]	1995 Jul 11	4370 days		1993 Dec 1.62	97.53	95.83	6937	537	580	0.003	148

1995 ay 30.46	97.52	92.23	6763	374	394	0.001	9

D	1983-75 X	[22934] 	1995 Jul 11	4370 days		1993 Dec 15.69	97.51	95.92	6941	539	586	0.003	112

1995 Jun 3.08	97.45	91.87	6745	358	374	0.001	62

D	1983-75 Y	[22935]	1999 Aug 4	5855 days		1993 Dec 17.04	97.46	97.12	6999	552	689	0.010	166

1999 Aug 3.87	97.57	89.50	6628	233	266	0.003	147

D	1983-75 Z	[22936]	1995 Jun 2	4331 days		1993 Dec 16.60	97.51	95.88	6940	537	585	0.003	108

1995 Jun 2.62	97.46	89.13	6610	220	243	0.002	210

D	1983-75 AA	[22937]	1994 Nov 29	4146 days		1993 Dec 15.87	97.52	95.67	6929	531	570	0.003	84

1994 Nov 13.57	97.47	92.10	6756	372	383	0.0008	33

D	1983-75 AB	[22938]	1995 May 9	4307 days		1993 Nov 18.57	97.52	95.85	6938	537	582	0.003	194

1995 May 7.01	97.49	90.38	6672	283	304	0.002	209

D	1983-75 AC	[22939]	1995 May 30	4328 days		1993 Dec 16.79	97.50	95.85	6939	536	583	0.003	108

1995 May 20.74	97.49	91.10	6707	316	341	0.002	28

D	1983-75 AD	[22940]	1995 Aug 22	4412 days		1993 Dec 15.54	97.51	95.88	6940	537	586	0.004	109

1995 Jul 16.56	97.48	91.87	6745	363	370	0.0005	89

D	1983-75 AE	[22941]	1995 Apr 7	4275 days		1993 Dec 16.78	97.49	95.83	6937	534	583	0.004	110

1995 Mar 16.32	97.51	91.50	6727	340	357	0.001	323

D	1983-75 AF	[22942]	1995 Nov 13	4495 days		1993 Dec 15.71	97.50	95.85	6938	537	583	0.003	116

1995 Oct 23.50	97.49	92.92	6796	408	426	0.001	120

D	1983-75 AG	[22943]	1998 Apr 28	5392 days		1993 Dec 15.52	97.36	97.93	7038	546	774	0.016	149

1998 Apr 26.35	97.36	90.88	6697	297	339	0.003	183

D	1983-75 AH	[22944]	1995 Jun 23	4352 days		1993 Dec 15.54	97.51	95.92	6941	537	588	0.004	111

1995 Jun 16.06	97.46	90.60	6683	297	312	0.001	5

D	1983-75 AJ	[22945]	1995 Jun 4	4333 days		1993 Dec 19.03	97.51	95.82	6937	537	580	0.003	102

1995 Jun 2.00	97.42	88.25	6567	182	195	0.001	184

D	1983-75 AK	[22946]	1995 Aug 9	4399 days		1993 Dec 15.78	98.17	95.62	6927	510	587	0.006	242

1995 Aug 8.76	98.09	89.10	6608	214	246	0.002	278

D	1983-75 AL	[22947]	1994 Dec 2	4149 days		1993 Dec 15.57	97.50	95.50	6921	522	562	0.003	61

1994 Dec 2.06	97.06	89.78	6642	258	269	0.0008	228

D	1983-75 AM	[22948]	1999 Jun 24	5814 days		1993 Dec 15.52	98.33	97.38	7012	530	737	0.015	207

1999 Jun 24.42	98.22	89.38	6623	231	258	0.002	296

D	1983-75 AN	[22959]	1995 Apr 4	4272 days		1994 Jan 1.65	97.51	95.73	6932	532	576	0.003	51

1995 Apr 4.06	97.46	88.72	6589	203	218	0.001	203

D	1983-75 AP	[22960]	1995 Mar 22	4259 days		1994 Jan 1.65	97.52	95.73	6933	533	575	0.003	53

1995 Mar 22.52	97.46	89.23	6615	229	243	0.001	241

D	1983-75 AQ	[22961]	1995 May 1	4299 days		1994 Jan 2.06	97.52	95.75	6933	534	575	0.003	51

1995 Apr 29.04	97.44	89.42	6624	236	254	0.001	247

D	1983-75 AR	[22962]	1995 Apr 22	4290 days		1994 Jan 2.04	97.51	95.78	6935	532	581	0.004	49

1995 Apr 22.34	97.43	89.68	6637	247	270	0.002	218

D	1983-75 AS	[23148]	1994 Oct 18	4104 days		1994 Jul 8.00	97.46	93.63	6831	440	464	0.002	69

1994 Oct 18.05	97.44	88.47	6577	192	205	0.001	359

D	1983-75 AT	[23149]	1994 Nov 11	4128 days		1994 Jul 10.61	97.51	97.13	6855	462	491	0.002	100

1994 Nov 11.61	97.53	90.48	6677	291	306	0.001	101

D	1983-75 AU	[23150]	1995 Aug 27	4417 days		1994 Jul 9.04	97.50	94.30	6853	472	497	0.002	116

1994 Nov 19.05	97.48	92.90	6795	402	431	0.002	351

D	1983-75 AV	[23151]	1994 Dec 21	4168 days		1994 Jul 9.55	97.52	94.95	6895	498	534	0.003	108

1995 Mar 20.64	97.46	90.10	6658	271	287	0.001	227

D	1983-75 AW	[23152]	1995 Jul 14	4373 days		1994 Jul 8.02	97.49	94.98	6896	497	537	0.003	128

1995 Jul 13.55	97.47	90.68	6686	299	316	0.001	206

D	1983-75 AX	[23153]	1996 Jul 7	4732 days		1994 Jul 8.06	97.49	95.02	6898	501	537	0.003	127

1995 Jun 4.93	97.47	91.80	6741	357	368	0.0008	329

D	1983-75 AY	[23154]	1995 Feb 27	4236 days		1994 Jul 8.00	97.48	94.73	6884	488	524	0.003	131

1995 Feb 26.22	97.41	89.50	6628	244	256	0.0009	222

D	1983-75 AZ	[23155]	1995 Apr 17	4285 days			1994 Jul 8.02	97.50	94.97	6896	500	534	0.002	127

1995 Apr 13.05	97.49	91.12	6708	315	344	0.002	238

D	1983-75 BA	[23156]	1995 Jul 4	4363 days		1994 Jul 14.87	97.49	94.98	6896	499	536	0.003	102

1995 May 16.47	97.45	92.25	6764	678	392	0.001	161

D	1983-75 BB	[23157]	1995 Jun 6	4335 days		1994 Jul 8.02	97.48	95.03	6899	501	540	0.003	124

1995 Jun 4.97	97.46	89.97	6652	251	294	0.003	61

D	1983-75 BC	[23476]	1996 Nov 26	4874 days		1995 Feb 1.19	98.33	95.03	6898	492	547	0.004	273

1996 Nov 26.45	98.30	89.58	6632	249	258	0.0006	356

D	1983-75 BD	[23540]	1999 Jul 8	5828 days		1995 Feb 1.33	97.05	98.58	7069	522	859	0.024	256

1999 Jul 8.34	97.00	89.68	6638	232	286	0.004	316

D	1983-75 BE	[23551]	1997 Oct 21	5203 days		1995 Apr 7.04	97.48	95.87	6939	538	583	0.003	314

1997 Oct 18.65	97.43	90.45	6675	290	303	0.001	135

D	1983-75 BF	[26920]	2012 Apr 20	10498 days		2004 Jul 9.06	97.83	94.48	6872	465	521	0.004	281

2012 Apr 9.60	97.72	90.20	6663	264	305	0.003	322

1983 75 BG	[44997]				2020 Jan 14.04	97.42	96.88	6988	471	747	0.020	209

1983 75 BH	[47115]				2020 Dec 1.94	97.33	91.65	6734	348	362	0.001	216

FSW-0 5 fragments; 4 pieces, all have decayed.

D	1983-86 C	[14290]	1983 Aug 20	1 day

D	1983-86 D	[14293] 	1983 Aug 20	1 day

D	1983-86 E	[14294] 	1983 Aug 21	2 days

D	1983-86 F	[14296] 	1983 Aug 20	1 day

Cosmos 1493 fragments; 5 pieces, all have decayed.

D 1983-87 C	[14304]	1983 Aug 30	7 days

D 1983-87 D	[14322]	1983 Sep 18	26 days

D 1983-87 E	[14323]	1983 Dec 6	105 days

D 1983-87 G	[14325]	1983 Oct 29	67 days

D 1983-87 H	[14513]	1983 Dec 15	114 days

Cosmos 1494 fragments; 25 pieces, all have decayed.

Analyses indicate that the Cosmos 1494 payload is the most likely debris source.

D	1983-91 C	[14703]	1984 Apr 7 	220 days

D	1983-91 D	[14704]	1984 May 6	249 days

D	1983-91 E	[14705]	1984 Apr 5	218 days

D	1983-91 F	[14706]	1984 Apr 9	222 days

D	1983-91 G	[14707]	1984 Apr 7	220 days

D	1983-91 H	[14708]	1984 Apr 6	219 days

D	1983-91 J	[14709]	1984 Apr 8	221 days

D	1983-91 K	[14710]	1984 Apr 9	222 days

D	1983-91 L	[14711]	1984 Apr 5	218 days

D	1983-91 M	[14718]	1984 Apr 6	219 days

D	1983-91 N	[14719]	1984 Apr 8	221 days

D	1983-91 P	[14720]	1984 Apr 6	219 days

D	1983-91 Q	[14721]	1984 Apr 4	217 days

D	1983-91 R	[14744]	1984 Apr 4	217 days

D	1983-91 S	[14745]	1984 Apr 2	215 days

D	1983-91 T	[14746]	1984 Apr 4	217 days

D	1983-91 U	[14747]	1984 Apr 5	218 days

D	1983-91 V	[14748]	1984 Apr 10	223 days

D	1983-91 W	[14749]	1984 Apr 6	219 days

D	1983-91 X	[14750]	1984 Apr 5	218 days

D	1983-91 Y	[14751]	1984 Apr 6	219 days

D	1983-91 Z	[14752]	1984 Apr 9	222 days

D	1983-91 AA	[14753]	1984 Apr 8	221 days

D	1983-91 AB	[14754]	1984 Apr 10	223 days

D	1983-91 AC	[14755]	1984 Apr 10	223 days

Cosmos 1499 fragments; 5 pieces, all have decayed.

D	1983-97 C	[14341]	1983 Sep 19	2 days

D	1983-97 D	[14382]	1983 Dec 20	94 days

D	1983-97 E	[14383]	1983 Oct 9	22 days

D	1983-97 G	[14385]	1983 Nov 20	64 days

D	1983-97 H	[14391]	1984 Jan 4	109 days

Cosmos 1501 fragments; 24 pieces, all have decayed.

Analyses indicate that the Cosmos 1501 payload is the most likely debris source.

D	1983-101 C	[14732]	1984 Apr 27	210 days

D	1983-101 D	[14733]	1984 Apr 28	211 days

D	1983-101 E	[14947]	1984 Sep 5	341 days

D	1983-101 F	[14963]	1984 Sep 9	345 days

D	1983-101 G	[15108]	1985 Mar 1	518 days

D	1983-101 H	[15110]	1985 Feb 4	493 days

D	1983-101 J	[15203]	1986 Jul 29	1033 days

D	1983-101 K	[15204]	1986 Sep 4	1070 days

D	1983-101 L	[15277]	1986 Oct 13	1109 days

D	1983-101 M	[15278]	1986 Sep 26	1092 days

D	1983-101 N	[15374]	1985 Jul 11	650 days

D	1983-101 P	[15375]	1985 Jul 5	644 days

D	1983-101 Q	[15425]	1987 Feb 1	1220 days

D	1983-101 R	[15426]	1984 Dec 24	451 days

D	1983-101 S	[15412]	1985 Oct 6	737 days

D	1983-101 T	[15513]	1986 Jan 3	826 days

D	1983-101 U	[15586]	1985 Dec 23	815 days

D	1983-101 V	[15587]	1985 Nov 20	782 days

D	1983-101 W	[15588]	1985 Dec 20	812 days

D	1983-101 X	[15594]	1985 Nov 2	764 days

D	1983-101 Y	[15862]	1986 Mar 20	902 days

D	1983-101 Z	[15863]	1986 Mar 5	887 days

D	1983-101 AA	[15864]	1986 Feb 26	880 days

D	1983-101 AB	[15865]	1986 Mar 25	907 days

DMSP 5d-2 F7 fragments; 6 pieces; 5 have decayed.

D	1983-113 C	[14554]	1991 Oct 2	2875 days		1991 Oct 1.80	98.53	89.93	6650	258	285	0.002	148

D	1983-113 D	[14609]	1992 Jun 19	3136 days

D	1983-113 E	[14610]	1999 Nov 27	5853 days

D	1983-113 F	[28457]	2004 Nov 18	7671 days		2004 Nov 16.41	98.37	92.40	6771	362	422	0.004	340

D	1983-113 G	[28458]	2006 May 6	8205 days		2004 Nov 20.87	98.85	100.65	7168	755	824	0.005	247

1983-113 H	[34988]				2006 Apr 28.49	98.70	93.60	6829	433	467	0.003	329

Cosmos 1512 fragments; 9 pieces, all have decayed.

D	1983-119 C	[14544]	1983 Dec 9	2 days

D	1983-119 D	[14545]	1983 Dec 9	2 days

D	1983-119 E	[14573]	1984 Feb 16	71 days

D	1983-119 F	[14574]	1983 Dec 30	23 days

D	1983-119 H	[14576]	1984 Mar 20	104 days

D	1983-119 J	[14579]	1984 Jul 9	215 days

D	1983-119 K	[14580]	1983 Dec 28	21 days

D	1983-119 L	[14581]	1984 Jun 26	202 days

D	1983-119 M	[14673]	1984 Mar 30	114 days

Cosmos 1519 ullage motor fragments; 7 pieces,  5 have decayed.

Parent satellite was one of two small engine units which are routinely released after the first burn of the Proton fourth stage. The nature of these objects was identified by Dr. Boris V. Chernlatiev, Deputy Constructor for the Energiya NPO, in October 1992. The cause of this fragmentation, 1991 Feb 4 at 03:12 UT near 28ºN 106ºE, is assumed to be related to the residual hypergolic propellants on board and failure of the membrane separating the fuel and oxidizer. NAVSPASUR observed at least 12 fragments on the day of the event and approximately three dozen on 7 February. An element set was initially developed on only one new fragment. This was the third in a series of fragmentations of this object type.

1983-127 J	[21752]				2004 Jul 9.09	53.82	132.88	8626	1034	3462	0.141	166

D	1983-127 K	[21753]	2003 Nov 10	7256 days

D	1983-127 L	[21860]	1992 Aug 18	3155 days

1983-127 M	[21935]				2004 Jul 8.59	52.29	269.51	13833	804	14105	0.481	303

D	1983-127 N	[25656]	1999 Jul 11	5673 days		1999 Mar 15.32	50.63	147.12	9231	574	5132	0.247	302

D	1983-127 P	[27467]	2005 May 15	7808 days		2004 Jul 1.50	51.41	166.12	10010	964	6299	0.266	154

D	1983-127 Q	[27468]	2004 Jul 11	7500 days