D	Zuma (USA 280) *	2018 01 A	2018 Jan 8.042			No TLE’s issued

[Falcon 9b4]	[43098]	~ 0.09 day			Fate unknown. Could have remained attached to 2nd stage and decayed with it.

(F9-047, B1043-1)	CC-LC40	2018 Jan 8.13

D	Falcon 9 2nd stage	2018 01 B	2018 Jan 8.042	Cylinder	12.6 long	No TLE’s issued

[NNA]	~ 0.09 day	~ 4000	3.66 dia	De-orbited and decayed over south Indian Ocean some 135 min after launch.

2018 Jan 8.13			Fuel venting observed from Sudan and from aircraft over Sudan.

*	Clandestine US reconnaissance satellite.

The 1st stage landed at CC-LZ1 7 min 59 sec after lift-off.

Superview-1 03  #	2018 02 A	2018 Jan 9.142	Box +2 panels		2018 Jan 9.27	97.58	95.13	6904	516	534	0.001	282

[CZ-2D]	[43099]		+ cylinder		2018 Jan 12.31	97.58	95.23	6908	524	535	0.0008	259

JIUQ-LC9		560

Superview-1 04	2018 02 B	2018 Jan 9.142	Box +2 panels		2018 Jan 9.27	97.58	95.15	6904	516	535	0.001	287

[43100]		+ cylinder		2018 Jan 12.84	97.58	95.00	6897	509	528	0.001	281

560

CZ-2D 2nd  stage	2018 02 C	2018 Jan 9.142	Cylinder	10.9 long	2018 Jan 9.27	97.58	95.08	6901	511	534	0.002	283

[43101]		6050	3.35 dia	2018 Jan 9.87	97.58	95.17	6905	516	536	0.001	293

Fragments	2018 02 D-G		4 pieces, all in orbit	For orbital information see extra pages at end of year

#	Second pair of Goajing commercial imaging satellites with a big telescope for high resolution images up to 50 cm resolution in B&W and 2 m in color.

Beidou-3  M3  &	2018 03 A	2018 Jan 11.971	Box +2 panels		2018 Jan 12.21	55.01	787.15	28240	21530	22193	0.012	177

[CZ-3B/YZ1]	[43107]	1 milion years

XI-LC2

Beidou-3  M4  &	2018 03 B	2018 Jan 11.971	Box +2 panels		2018 Jan 12.23	55.00	787.48	28248	21546	22193	0.011	177

[43108]	1 milion years

Yuanzheng-1 	2018 03 C	2018 Jan 11.971			2018 Jan 12.13	55.05	812.42	28841	22178	22747	0.010	355

Upperstage	[43109]				2018 Jan 12.18	55.03	807.50	28725	22186	22507	0.006	346

CZ-3B 3rd stage	2018 03 D	2018 Jan 11.971	Cylinder	12.38 long	2018 Jan 12.09	54.94	328.03	15756	210	18545	0.582	171

[43110]		2740	3.0 dia

&	Chinese navigation satellites.

Cartosat 2F %1	2018 04 A	2018 Jan 12.166	Hexagonal box 	2.5 high	2018 Jan 12.22	97.55	94.67	6881	495	509	0.004	254

[PSLV]	[43111]		+ cylinder	2.4 dia

(C40)	SRI-LC1		+2 panels	   span

710

LEO Vantage 1  %5	2018 04 C	2018 Jan 12.166	Box	0.72x0.65	2018 Jan 12.36	97.55	94.63	6879	494	507	0.0009	264

[43113]		100	x0.65

ICEYE X1   %6	2018 04 D	2018 Jan 12.166	Box +2 panels		2018 Jan 12.36	97.55	94.62	6879	495	506	0.0008	271

[43114]		65

3.2 span

Carbonite 2   %4	2018 04 E	2018 Jan 12.166	Box +2 panels	0.72x0.65	2018 Jan 12.36	97.56	94.62	6879	494	506	0.0009	267

[43115]		100	x0.65

~ 1.80 span

INS-1C   %2	2018 04 F	2018 Jan 12.166	Box +2 panels	0.245x0227	2018 Jan 12.36	97.56	94.62	6878	494	505	0.0008	275

[43116]		11	x0.217

0.68 span

CANYVAL-X1   %14	2018 04	2018 Jan 12.166	1U cube	0.10 side	Satellite is not active.

“Jerry”	[43117]		0.810		2018 Jan 14.77	97.42	94.65	6880	494	510	0.001	241

Last TLE for 2018 04 G issued 2018 Mar 24.

2018 Mar 24	97.42	94.63	6879	492	509	0.001	1

2018 Jun 30  re-assigned to 1988 53 E.

Corvus-BC3  %11	2018 04 H	2018 Jan 12.166	6U Cube	0.30x0.20	2018 Jan 15.45	97.55	94.60	6878	493	506	0.0009	273

[43118]		+2 panels	x0.10

~0.30 span

Flock-3pp 3    %7	2018 04 J	2018 Jan 12.166	3U Cube	0.30x0.10	2018 Jan 14.84	97.56	94.60	6878	493	506	0.0009	270

[43119]		+2 panels	x0.10

5

Flock-3pp 2    %7	2018 04 K	2018 Jan 12.166	3U Cube	0.30x0.10	2018 Jan 14.84	97.56	94.60	6878	493	506	0.0009	270

[43120]		+2 panels	x0.10

5

Flock-3pp 1   %7	2018 04 L	2018 Jan 12.166	3U Cube	0.30x0.10	2018 Jan 15.39	97.56	94.60	6878	492	506	0.001	262

[43121]		+2 panels	x0.10

5

Flock-3pp 4    %7	2018 04 M	2018 Jan 12.166	3U Cube	0.34x0.10	2018 Jan 14.84	97.56	94.60	6878	493	505	0.0009	271

[43122]		+2 panels	x0.10

4.7	0.70 span

Lemur-2 70   %8	2018 04 N	2018 Jan 12.166	3U Cube	0.34x0.10	2018 Jan 15.11	97.56	94.60	6878	494	505	0.0008	267

McCafferty	[43123]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 68   %8	2018 04 P	2018 Jan 12.166	3U Cube	0.34x0.10	2018 Jan 14.83	97.56	94.60	6878	493	505	0.0009	272

PeterWebster	[43124]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 71   %8	2018 04 Q	2018 Jan 12.166	3U Cube	0.34x0.10	2018 Jan 14.70	97.56	94.60	6878	493	505	0.0009	274

Browncow	[43125]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 69   %8	2018 04 R	2018 Jan 12.166	3U Cube	0.34x0.10	2018 Jan 14.83	97.56	94.60	6878	493	505	0.0009	274

DaveWilson	[43126]		+2 panels	x0.10

4.6	0.54 span

DemoSat-2  %20	2018 04 S	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 14.83	97.56	94.60	6877	493	505	0.0009	275

[43127]			x0.10

MicroSat-TD   %3	2018 04 T	2018 Jan 12.166	Box +2 panels	1x1x0.6	2018 Jan 12.41	96.87	91.72	6737	345	372	0.002	355

[43128]		120	~ 2.4 span

D	PSLV 4th stage	2018 04 U	2018 Jan 12.166	Cylinder	2.60 long	2018 Jan 12.42	97.22	91.50	6727	326	369	0.003	85

[43129]	370 days	920	2.02 dia	2019 Jan 17.19	97.14	87.23	6516	132	142	0.0007	277

2019 Jan 17

Arkyd-6 (A6) %9	2018 04 V	2018 Jan 12.166	6U Cube	0.30x0.20	2018 Jan 14.83	97.56	94.60	6877	493	505	0.0009	275

[43130]		+2 panels	x0.10

10	0.60 span

MicroMAS-2   %12	2018 04 W	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 14.83	97.56	94.58	6877	493	504	0.0008	275

[43131]		+2 panels	x0.10

4	0.70 span

PicSat   %13	2018 04 X	2018 Jan 12.166	3U cube	0.34x0.10	2018 Jan 15.51	97.55	94.58	6877	496	502	0.0004	254

[43132]		+4 panels	x0.10

3.8	0.78 span

CNUSail 1 &15	2018 04 Y	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 1484	97.56	94.58	6877	493	505	0.0008	275

[43133]		+ sail	x0.10

4.0	2x2m sail

Sigma   %16	2018 04 Z	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 14.77	97.56	94.58	6877	493	504	0.0008	277

[43134]		+ boom	x0.10

3.2	0.5m boom

KAUSAT  %17	2018 04 AA	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 15.65	97.56	94.58	6877	495	502	0.0006	282

[43135]		+4 panels	x0.10

4	0.70 span

CANYVAL-X2   %14	2018 04 AB	2018 Jan 12.166	2U cube	0.20x0.10	2018 Jan 14.64	97.56	94.58	6877	493	504	0.0008	279

“Tom”	[43136]		+4 panels	x0.10

0.70 span

Fox 1D  %18	2018 04 AC	2018 Jan 12.166	1U cube	0.10 side	2018 Jan 14.70	97.56	94.58	6877	493	504	0.0008	279

(AO-92)	[43137]

STEP Cube Lab  %22	2018 04 AD	2018 Jan 12.166	1U cube	0.10 side	2018 Jan 14.77	97.56	94.58	6877	493	504	0.0008	279

[43138]

SpaceBEE 4  %21	2018 04 AE	2018 Jan 12.166	0.25U cube	0.10x0.10	2018 Jan 14.77	97.56	94.58	6877	493	504	0.0008	279

[43139]			x0.025

SpaceBEE 3  %21	2018 04 AF	2018 Jan 12.166	0.25U cube	0.10x0.10	2018 Jan 15.65	97.56	94.58	6877	495	501	0.0004	236

[43140]			x0.025

SpaceBEE 2  %21	2018 04 AG	2018 Jan 12.166	0.25U cube	0.10x0.10	2018 Jan 15.45	97.55	94.58	6877	492	504	0.0009	281

[43141]			x0.025

SpaceBEE 1  %21	2018 04 AH	2018 Jan 12.166	0.25U cube	0.10x0.10	2018 Jan 15.45	97.56	94.58	6877	492	504	0.0008	278

[43142]			x0.025

Cicero 7  %10	2018 04 AJ	2018 Jan 12.166	6U Cube	0.30x0.20	2018 Jan 15.45	97.56	94.55	6876	493	501	0.0006	286

[43143]			x0.10

Tyvak 61C  %19	2018 04 AK	2018 Jan 12.166	3U cube	0.30x0.10	2018 Jan 15.65	97.56	94.55	6875	492	501	0.0007	291

[43144]		+4 panels	x0.10

4	0.54 span

Fragment	2018 04 B	[43112]			2018 Jan 12.36	97.57	94.65	6880	495	508	0.0009	260

%1	Indian cartographic satellite.

$2	Indian Nano Satellite; an xperimental Earth observation mission with Miniature Multispectral payload Technology Demonstration (MMX-TD).

%3	Indian Earth observation satellite in a low earth orbit.

%4	UK technology demonstration satellite for Earth imaging.

%5	Canadian prototype communications satellite.

%6	Finish Synthetic Aperture Radar satellite

%7	15th Flock of Dove Earth observation cubesats from Planet

%8	From Spire Global

%9	From Planetary Resources to test asteroid exploration and mining.

%10 From GeoOptics outfitted with GPS and Galileo global satellite navigation systems for atmospheric occultation measurements to collect weather data and

detection of backscattered signals for ocean/ice surface properties.
%11 From Astro Digital for Earth remote sensing.

%12 Micro-sized Microwave Atmospheric Satellite equipped with a radiometer from MIT/LL, MIT/SSL and University of Massachusetts.

%13 French Astronomy CubeSat to observe the transit of the planet Beta Pictoris b across its host star.
%14 CubeSat Astronomy by NASA and Yonsei using Vision ALignment eXperiment and involves NASA’s Goddard Spaceflight Center, Korea’s Yonsei University and the

Korea Aerospace Research Institute (KARI) for demonstration of a very long baseline telescope. The 2 sats will maintain optical alignment over a distance of ten to 50 meters for time frames sufficient for astronomical observations. The 2 sats are deployed together and then separate.

%15 Chungnam National University Sail from South Korea to demonstrate a large sail as solar sail and as a deorbiting device for small satelltes.

%16 The Scientific cubesat with Instruments for Global Magnetic field and rAdiation – also known as KHUSAT 3 (Kyung Hee University Satellite) is a South

Korean CubeSat mission dedicated to the measurement of the global magnetic field via a magnetometer instrument and radiation in the Low Earth Orbit

environment via a Tissue Equivalent Proportional Chamber instrument.
%17 Korea Aviation University Satellite for Earth observations in Infra Red.

%18 Amateur radio and technology research satellite from AMSAT and 3 US universities.

%19 Technology demonstration and astronomy mission by California-based Tyvak Nano Satellite Systems with the primary objective of cataloging the variability

of luminous stars. 
%20 US satellite to test UHF radio.

%21 Demonstration of two-way satellite communications and data relay using an ultra-small satellite platforms.
%22 Space Technology Experimental Project Cubesat Laboratiry from Chosun University, South Korea.

FIA-Radar 5  $	2018 05 A	2018 Jan 12.924			2018 Jan 14	106.00	106.24		1048	1057

(USA 281, NROL-47)	[43145]				2020 Dec 30.84	106.01	106.82	7458	1078	1080	0.0002	221

[Delta IV M+(5,2)]	VDB-SLC6

D	Delta Cryogenic	2018 05 	2018 Jan 12.924	Cylinder	13.7 long	No TLE’s issued

Second Stage	[NNA]	~ 0.13 day	3490	5 dia	De-orbited and decayed over south Indian Ocean some 3 hours after launch.

2018 Jan 13.

$	Clandestine US reconnaissance radar satellite. Orbits from amateur radio and visual observations.

LKW-3 #	2018 06 A	2018 Jan 13.299	Hexagonal bus		2018 Jan 13.42	97.34	94.52	6874	488	503	0.001	255

[CZ-2D] (Y49)	[43146]		+ 3 panels

JIUQ-LC2

CZ-2D 2nd stage	2018 06	2018 Jan 13.299	Cylinder	10.9 long	De-orbited before being catalogued.

[NNA]			3.35 dia

Fragments	2018 06 B-E		4 pieces, all in orbit	For orbital information see extra pages at end of year

#	Chinese Land Survey Satellite (Ludi Kancha Weixing 3).

ASNARO-2  *	2018 07 A	2018 Jan 17.879	Box +2 panels		2018 Jan 18.97	97.37	94.60	6878	493	506	0.0009	194

[Epsilon]	[43152]		+ radarantenna

UCH-LP M		570

Post Boost Stage	2018 07 B	2018 Jan 17.879	Drum + discus	1.3 long	2018 Jan 17.97	97.37	94.38	6867	469	508	0.003	214

+ Equipment Mounting	[43153]		400 + 300 full	2.0-2.5 dia

Structure			255 + 300 dry

D	Fragment	2017 07 C	[43154]	1 piece, in orbit	For orbital information see extra pages at end of year

* Japanese radar imaging satellite: Advanced Satellite with New ARchitecture for Observation.

Xiaoxiang 2  &3	2018 08 A	2018 Jan 19.175	6U Cube 	0.30x0.20	2018 Jan 19.51	97.54	95.33	6913	523	547	0.002	298

[CZ-11]	[43155]		+2 panels	x0.10

(Y03)	JIUQ-LC-E2		8	0.70 span

Zhou Enlai  $4	2018 08 B	2018 Jan 19.175	2U Cube	0.20x0.10	2018 Jan 19.51	97.54	95.37	6915	527	546	0.001	311

[43156]		2.4	x0.10

KIPP 1  &5	2018 08 C	2018 Jan 19.175	6U Cube 	0.30x0.20	2018 Jan 19.51	97.55	95.38	6916	527	547	0.001	267

(Kepler-O)	[43157]		+2 panels	x0.10

8

QTT 1  &2	2018 08 D	2018 Jan 19.175	3U Cube	0.30x0.10	2018 Jan 19.51	97.54	95.38	6916	528	546	0.001	291

[43158]			X0.10

0.50 span

Jinlin 1-07 &1	2018 08 E	2018 Jan 19.175	Hexagonal box	1.2x1.1	2018 Jan 19.51	97.54	95.40	6916	528	547	0.001	289

[43159]		+ 2 telescopes

~ 208

Jinlin 1-08	2018 08 F	2018 Jan 19.175	Hexagonal box	1.2x1.1	2018 Jan 19.51	97.54	95.40	6916	529	547	0.001	291

[43160]		+ 2 telescopes

~ 208

CZ-11 4th stage	2018 08 G	2018 Jan 19.175	Cylinder		2018 Jan 19.53	98.49	100.83	7176	527	1069	0.038	198

[43161]

&1 Chinese remote sensing satellite from Chang Guang Satellite technology Ltd.

&2	QuanTuTong is a Chinese test satellite for an integrated navigation and communication system from Changsha Gaoxingu Tiany Research Institute.

&3	Astronomical satellite with a stabalized imaging system from Changsha Gaoxingu Tiany Research Institute.

&4 From Huaian Yoth Comprehensive Devolopment Base imaging satellite build by students. It has a 1.2 m2 sail to be deployed at the end of the mission

to accelerate orbital decay.

&5	Canadian technology validation satellite from Kepler Communications.

SBIRS GEO-4  *	2018 09 A	2018 Jan 20.033	Box +2 panels		No TLE’s issued

(USA 282)	[43162]	> million years	+ sunshade

[Atlas V 411]	CC-LC41		~ 4500

(AV-076)

D	Atlas V 2nd stage	2018 09	2018 Jan 20.033	Cylinder	12.68 long	After satellite deployment the centaur made a de-orbit burn.

(Centaur)	[NNA]		2243	3.05 dia	Decayed over the Pacific Ocean some hours after lift-off.

*	US Missile Warning satellite for the Space Based InfraRed System.

D	Dove Pioneer    %1	2018 10 A	2018 Jan 21.072	3U Cube	0.34x0.10	2018 Jan 21.11	82.93	92.78	6789	288	533	0.018	223

[Electron]	[43163]	609 days	+2 panels	x0.10	2019 Sep 22.15	82.88	88.08	6558	171	189	0.001	87

MAH-LC1	2019 Sep 22	4.7	0.70 span

Electron $4  	2018 10 B	2018 Jan 21.072	Cylinder	2.4 long	2018 Jan 21.11	82.93	95.02	6898	506	533	0.002	237

2nd stage	[43164]		250	1.2 dia

2150 full

Lemur-2 73   %2	2018 10 C	2018 Jan 21.072	3U Cube	0.34x0.10	2018 Jan 21.11	82.93	94.90	6893	494	534	0.003	232

Marshall	[43165]		+2 panels	x0.10

4.6	0.54 span

D	Electron Kick stage	2018 10 D	2018 Jan 21.072	Truncated cone	?? long	2018 Jan 21.11	82.93	92.72	6786	290	525	0.017	223

%5	[43166]	406 days		1-1.2 dia	2019 Mar 3.38	82.87	87.38	6524	140	150	0.0007	46

2019 Mar 3

Lemur-2 72   %2	2018 10 E	2018 Jan 21.072	3U Cube	0.34x0.10	2018 Jan 21.11	82.93	94.93	6894	497	533	0.003	245

Tallhamn-ATC	[43167]		+2 panels	x0.10

4.6	0.54 span

D	Humanity Star %3	2018 10 F	2018 Jan 21.072	Sphere	~1 dia	2018 Jan 21.11	82.92	92.82	6791	295	530	0.017	222

[43168]	60.5 days	10.34

2018 Mar 22.55

%1	Dove Pioneer satellite from Planet, USA.

%2 Ship and traffic tracking satellites from Spire Globe, USA.

%3	Sphere made of 65 triangles of one-millimeter thick carbon-fiber composite material with reflective surface.

%4	2nd test flight and the first to reach orbit from Mahia Launch Complex, New Zealand.

&5	3th stage to circulise the orbit

Weina 1A    #2	2018 11 A	2018 Jan 25.235			2018 Jan 25.35	34.99	96.67	6977	585	612	0.002	182

[43169]

XI-LC3

Yaogan 30 K #1	2018 11 B	2018 Jan 25.235	Box +2 panels		2018 Jan 25.35	35.00	96.73	6981	599	606	0.0005	354

[43170]	`			2018 Jan 25.75	34.99	96.62	6975	591	602	0.0008	280

Yaogan 30 L	2018 11 C	2018 Jan 25.235	Box +2 panels		2018 Jan 25.35	35.00	96.58	6974	588	602	0.001	271

[43171]	`			2018 Jan 27.83	34.99	96.62	6975	591	601	0.0007	293

Yaogan 30 M	2018 11 D	2018 Jan 25.235	Box +2 panels		2018 Jan 25.35	35.01	96.08	6949	534	607	0.005	234

[43172]	`			2018 Jan 25.78	35.00	96.63	6975	590	602	0.0008	277

CZ-2C 2nd stage	2018 11 E	2018 Jan 25.235	Cylinder	7.58 long	2018 Jan 25.62	34.96	94.60	6878	395	602	0.015	14

[43173]		3300	3.35 dia	2018 Jan 25.81	34.96	94.60	6877	395	603	0.015	15

#1	4th group of Chinese reconnaissance satellites.

$2	Nano satellite for technological experiments.

Al Yah 3  *2	2018 12 A	2018 Jan 25.930	Box +2 panels	5.18 x 3.35	2018 Jan 26.64	20.64	780.30	28076	232	42163	0.765	230

[Ariane 5]	[43174]		3795	x 2.87	2018 Feb 1.95	20.00	789.42	28294	677	43155	0.751	235

VA241	KOU-ELA3				2018 Feb 7.51	21.52	1009.88	33343	6140	47790	0.625	209

2018 Feb 12.70	9.33	1202.60	37461	14973	47192	0.430	234

2018 Feb 13.05	6.21	1350.92	40480	20923	47281	0.326	260

2018 Feb 16.51	5.90	1376.00	40980	16909	52294	0.432	266

2018 Feb 20.64	5.56	1415.73	41765	23343	47430	0.288	275

2018 Feb 25.19	5.27	1440.73	42256	24244	47509	0.275	269

2018 Apr 18.67	0.54	1451.75	42471	34966	37218	0.027	263

2018 Apr 19.46	0.41	1450.07	42438	35210	36908	0.020	261

2018 Apr 24.96	0.07	1439.92	42240	35856	35866	0.0001	9

2018 Apr 30.39	0.06	1438.77	42217	35811	35866	0.0006	310

2018 May 2.38	0.06	1436.08	42165	35781	35791	0.0001	117

SES 14  *1	2018 12 B	2018 Jan 25.930	Box +2 panels	7.0 x 5.4	2018 Jan 26.64	20.64	781.00	28093	231	43198	0.765	230

[43175]		4426	x 4.0	2018 Jan 27.47	20.55	783.18	28145	335	43198	0.761	231

2018 Jan 31.37	20.46	785.07	28190	383	43240	0.760	233

2018 Jan 31.98	20.47	790.23	28314	412	43459	0.760	233

2018 Feb 1.77	20.14	797.17	28479	528	43674	0.757	234

2018 Feb 2.88	19.97	804.88	28663	647	43921	0.755	235

2018 Feb 8.86	19.14	846.90	29652	1309	45237	0.741	239

2018 Feb 20.79	17.45	943.75	31871	2856	48130	0.710	245

2018 Feb 26.74	16.72	995.67	33030	3733	49569	0.694	248

2018 Mar 2.76	16.35	1028.20	33745	4341	50393	0.682	249

2018 Mar 5.71	15.73	1057.62	34386	7920	51095	0.671	250

2018 Mar 12.75	15.09	1104.32	35391	6657	51368	0.632	251

2018 Apr 17.75	10.23	1306.93	39597	14215	52222	0.480	261

2018 May 14.44	7.06	1379.55	41051	20905	48438	0.335	261

2018 Jun 12.91	3.20	1427.87	42004	28875	42375	0.161	263

2018 Jun 21.69	2.05	1435.50	42153	31470	40079	0.102	261

2018 Jul 1.86	1.45	1441.47	42270	32583	39200	0.078	261

2018 Jul 2.67	1.51	1437.48	42192	32612	39015	0.076	261

2018 Jul 17.67	0.11	1436.07	42164	35678	35893	0.003	165

2018 Jul 27.27	0.06	1441.48	42270	35847	35937	0.001	116

2018 Aug 3.27	0.03	1436.08	42164	35784	35787	0.00004	307

2018 Aug 5.26	0.04	1436.10	42165	35784	35788	0.00005	321

Ariane 5 2nd stage	2018 12 C	2018 Jan 25.930	Cylinder	5.84 long	2018 Jan 26.53	20.98	772.22	27882	182	42825	0.765	229

(ESC-A + VEB) *3	[43176]		5668	5.4 dia

Sylda upperpart	2018 12 D	2018 Jan 25.930	Barrel		2018 Jan 26.54	20.65	780.35	28077	232	43165	0.765	230

[43177]

*1 Communication satellite from Luxemburg.

On board is also the NASA GOLD (Global-scale Observations of the Limb and Disk) instrument for atmospheric measurements at the edge of space.

*2	Communication satellite from Abu Dhabi, UAE.

*3	Telemetry was lost from the 2nd stage a few seconds after 2nd stage ignition for the rest of the flight. However contact was established with both satellites some time after their planned separation. The rocket delivered the satellites to a 20-21 degrees and somewhat lower orbit then planned, the satellites will use their onboard propulsion to achieve geostationary orbit.

SES 16 / GovSat 1 *	2018 13 A	2018 Jan 31.893	Box +2 panels		Geostationary orbit; no TLE’s issued. Orbits from amateur observations.

[Falcon 9b3]	#	[43178]	> million years	4230		2020 Nov 20.55	0.01	1436.12	42165	35772	35801	0.0003	54

(F9-048 B1032-2)	CC-LC40

Falcon 9 2nd stage	2018 13 B	2018 Jan 31.893	Cylinder	12.6 long	Geostationary transfer orbit; no TLE’s issued, declassified in 2019 Jan.

[43179]		~ 4000	3.66 dia	2019 Jan 31.95	25.08	1086.18	35002	267	56981	0.810	179

2019 Mar 9.62	23.66	902.68	30940	368	48755	0.782	344

*	Communication satellite with combined payload from Luxemburg Goverment and SES.

#	The 1st stage has flown before with NROL-76 on 2017 May 1.

Kanopus-V 3  $1	2018 14 A	2018 Feb 1.088	Box +2 panels		2018 Feb 1.18	97.47	94.73	6884	503	508	0.0004	40

[Soyuz 2-1A/	[43180]		490		2018 Feb 1.49	97.47	94.77	6886	504	510	0.0004	79

Fregat M]	VOS

Kanopus-V 4  $1	2018 14 B	2018 Feb 1.088	Box +2 panels		2018 Feb 1.24	97.47	94.72	6883	499	510	0.0008	84

[43181]		490

Lemur-2 76 $3	2018 14 C	2018 Feb 1.088	3U Cube	0.34x0.10	2018 Feb 1.76	97.73	96.27	6958	571	589	0.001	241

Jin-Luen	[43182]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 77 $3	2018 14 D	2018 Feb 1.088	3U Cube	0.34x0.10	2018 Feb 1.76	97.73	96.27	6958	571	589	0.001	239

Uramchansol	[43183]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 74 $3	2018 14 E	2018 Feb 1.088	3U Cube	0.34x0.10	2018 Feb 1.76	97.73	96.27	6958	571	588	0.001	241

Kadi	[43184]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 75 $3	2018 14 F	2018 Feb 1.088	3U Cube	0.34x0.10	2018 Feb 1.76	97.72	96.27	6958	571	588	0.001	246

Thenickmodo	[43185]		+2 panels	x0.10

4.6	0.54 span

S-net D   &2	2018 14 G	2018 Feb 1.088	Cube	0.24 side	2018 Feb 4.94	97.73	96.23	6956	570	585	0.001	217

(Tubsat 16)	[43186]		< 8.5

S-net B   &2	2018 14 H	2018 Feb 1.088	Cube	0.24 side	2018 Feb 4.84	97.72	96.22	6956	571	585	0.001	223

(Tubsat 14)	[43187]		< 8.5

S-net A   &2	2018 14 J	2018 Feb 1.088	Cube	0.24 side	2018 Feb 4.84	97.73	96.22	6956	567	588	0.002	203

(Tubsat 13)	[43188]		< 8.5

S-net C   &2	2018 14 K	2018 Feb 1.088	Cube	0.24 side	2018 Feb 14.79	97.73	96.22	6956	571	584	0.001	193

(Tubsat 15)	[43189]		< 8.5

D-Star One v1.1  $4	2018 14	2018 Feb 1.088	3U Cube	0.30x0.10	Did not deploy from upperstage.

Phoenix	[NNA]		4	x0.10

D	Fregat M stage $5	2018 14	2018 Feb 1.088	Torus+spheres	1.85 high

[NNA]	0.177 day	930	3.35 dia

2018 Feb 1.265

$1	Two Russian remote sensing satellite.

$2	Four satellites from the Technical University of Berlin, Germany to investigate and demonstrate an inter-satellite communications network using an autonomous architecture for the management of large satellite constellations.

$3	Four satellites from Spire Globe for Earth observation, maritime monitoring, communications, meteorology and science.

$4	Reflight of the D-Star One mission that was lost in the 2017 Nov 28 Soyuz/Fregat failure. From German Orbital Systems for a technology demonstration for a planned CubeSat based communications constellation.

$5	The Fregat stage moved after the Kanopus deployment to a higher orbit for release of the secondary payloads. Then made a pair of orbit lowering manoeuvres and a de-orbit burn. The Fregat decayed over the Pacific Ocean.

FengMaNiu 1 &4	2018 15 A	2018 Feb 2.327	3U Cube	0.30x0.10	2018 Feb 2.45	97.34	94.58	6877	498	508	0.001	275

[CZ-2D]	[43192]			X0.10

JIUQ-LC2

Zhangheng-1 &1	2018 15 C	2018 Feb 2.327	Box + panel		2018 Feb 2.79	97.34	94.57	6876	487	508	0.002	262

(CSES)	[43194]		+ antenna’s

730

ÑuSat 4 &2	2018 15 D	2018 Feb 2.327	Box	0.75x0.45	2018 Feb 2.79	97.33	94.55	6875	486	508	0.002	265

(Ada)	[43195]		37	x0.43

Gomx-4B  &3	2018 15 E	2018 Feb 2.327	6U Cube	0.30x0.20	2018 Feb 2.72	97.33	94.50	6873	482	507	0.002	269

[43196]			0.10

Gomx-4A  &3	2018 15 F	2018 Feb 2.327	6U Cube	0.30x0.20	2018 Feb 2.72	97.34	94.52	6873	482	507	0.002	275

(Ulloriaq)	[43197]			0.10

Shaonian Xing  &5	2018 15 H	2018 Feb 2.327	3U Cube	0.30x0.10	2018 Feb 2.78	97.32	94.53	6874	485	507	0.002	267

[43199]			X0.30

ÑuSat 5 &2	2018 15 K	2018 Feb 2.327	Box	0.75x0.45	2018 Feb 5.01	97.33	94.55	6875	486	508	0.002	252

(Maryam)	[43204]		37	x0.43

CZ-2D 2nd stage	2018 15	2018 Feb 2.327	Cylinder	10.9 long	De-orbited before being catagued.

(Y38)	[NNA]			3.35 dia

Fragments CZ-2D	2018 15 B, G, J, L	4 pieces, all in orbit	For orbital info see extra pages at end of year.

&1	China Seismo-Electromagnetic Satellite.

&2	From Satellogic for collecting multi-band imagery in the Aleph-1 Earth Observation Satellite Constellation.

&3	From Danmark for aeronautical monitoring from ships and aircraft. GOMX4-B can follow with cold gas thrusters GOMX-4A for intersatellite communications.

GOMX-4B also houses HyperScout in a 1 cube volume to collect imagery with 40 m resolution.

&4	From Link Space Aerospace Technology to test panoramic miniature photo and video camera’s. It also host a amateur radio repeater.

&5	From SatChina for students to learn satellite development and mission operations.

D	TRICOM-1R ^	2018 16 A	2018 Feb 3.210	3U Cube	0.116x0.116	2018 Feb 3.30	30.90	107.25	7478	186	2012	0.122	78

(Tasuki)	[43201]	199 days	3	x0.346	2018 Aug 21.17	30.94	88.47	6577	142	255	0.009	114

[SS-520-5]	UCH LP-KS	2018 Aug 21

D	SS-520-5 2nd stage	2018 16 B	2018 Feb 3.210	Cylinder	0.8 long	2018 Feb 3.30	30.90	107.17	7474	188	2002	0.121	78

[43202]	139 days		0.52 dia	2018 Jun 22.32	30.86	88.23	6566	142	232	0.007	281

2018 Jun 22

^	Re-flight from 2017 Jan 14 failure with a satellite from University of Tokyo with a store and foreward communications radio and Earth-imaging cameras.

Tesla Roadster /	2018 17 A	2018 Feb 6	Car + Cyl		2018 Feb 6.94	29.02	164.52	9946	183	6952	0.340	180

Falcon 9H 2nd stage 	[43205]	indefinite	? + ~4000	+ 12.6 long 2018 Feb 7.06	29.02	164.53	9947	183	6952	0.340	180

[Falcon Heavy] #	CC-LC39A			  3.66 dia	2018 Feb 7.17	29.02	164.32	9938	180	6939	0.340	181

(FH-001 B1033,					2018 Feb 7.22	29.02	164.30	9937	173	6938	0.340	181

B1023-2, B1025-2)					Solar orbit between Earth and Mars orbit.

#	Test flight of the Falcon Heavy rocket. The 1st stage is made up of 3 Falcon 9 boosters. The 2 side boosters have flown before in 2016 for the Thaicom 8 and Dragon CRS-9 launch. They both landed back at CC LZ1 and 2. The central booster tried to land at the droneship OCISLY in the Atlantic Ocean, but ran out of igniter fuel to restart 3 engines for the landing burn and it crashed into the water.

The 2nd stage was in a highly elliptic orbit for some 6 hours and then restarted to escape earth’s gravity. The burn was observed from southwest USA.

Beidou-3  M5  &	2018 18 A	2018 Feb 12.210	Box +2 panels		2018 Feb 12.35	54.85	325.20	17537	159	22158	0.627	171

[CZ-3B]	[43207]	1 million years			2018 Feb 12.37	54.99	787.23	28242	21535	22192	0.012	178

XI-LC2				2018 Feb 27.17	54.98	773.22	27906	21508	21546	0.0007	316

Beidou-3  M6  &	2018 18 B	2018 Feb 12.210	Box +2 panels		2018 Feb 12.37	54.99	787.40	28246	21544	22192	0.011	178

[43208]	1 million years			2018 Feb 27.09	54.99	773.85	27921	21521	21565	0.0008	248

2018 Feb 27.98	54.97	773.32	27908	21506	21553	0.0009	279

2018 Mar 3.94	54.98	773.22	27906	21505	21550	0.0008	287

CZ-3B 3rd stage	2018 18 C	2018 Feb 12.210			2018 Feb 12.51	54.93	328.23	15755	163	18630	0.585	170

[43209]

Yuanzheng-1 	2018 18 D	2018 Feb 12.210			2018 Feb 12.37	54.79	803.95	28641	22186	22338	0.003	64

Upperstage	[43210]	1 million years			2018 Feb 13.48	54.79	804.22	28647	22191	22346	0.003	69

&	Chinese navigation satellites.

D 	Progress MS-08 *	2018 19 A	2018 Feb 13.134	Cyl+beehive+	7.5 long	2018 Feb 13.36	51.65	88.58	6583	186	222	0.003	75

[Soyuz-2.1A]	[43211]	198 days	+spheroid+	2.72 maxdia	2018 Feb 13.43	51.65	88.62	6584	189	223	0.003	68

BAI-LC31/6	2018 Aug 30	2 panels	2.3 dia	2018 Feb 13.78	51.64	90.93	6699	318	323	0.0003	86

7281		2018 Feb 14.60	51.65	90.98	6701	318	327	0.0007	65

2018 Feb 15.38	51.64	92.65	6783	402	407	0.0004	103

2018 Aug 21.76	51.64	92.67	6784	401	409	0.0006	82

2018 Aug 23.49	51.64	92.03	6752	346	402	0.004	246

2018 Aug 29.88	51.64	92.02	6752	346	401	0.004	271

D	Soyuz-2.1A 3rd stage	2018 19 B	2018 Feb 13.134	Cylinder	6.74 long	2018 Feb 13.36	51.64	88.60	6583	187	223	0.003	66

[43212]	3 days	2355	2.66 dia	2018 Feb 16.76	51.65	87.38	6524	140	150	0.0008	119

2018 Feb 16

*	Progress MS-08 docked 2018 Feb 15.443 with ISS (Zvezda port) with a cargo of 2494 kilograms. Undocked 2018 Aug 22.928 and will conduct several experiments before being de-orbited.

PAZ  *1	2018 20 A	2018 Feb 22.595	Box + panel		2018 Feb 22.66	97.46	94.77	6886	498	517	0.001	270

[Falcon 9b3]	[43215]		+ SAR antenna		2018 Feb 22.73	97.46	94.80	6888	501	517	0.001	274

(F9-049, B1038-2}	VDB-SLC4E				2018 Feb 24.58	97.46	94.83	6889	503	518	0.001	260

Tintin A  *2	2018 20 B	2018 Feb 22.595	Box		2018 Feb 22.65	97.46	94.73	6884	495	516	0.002	261

Microsat-2a	[43216]		400		2018 Feb 22.74	97.46	94.80	6887	500	517	0.001	281

Tintin B	2018 20 C	2018 Feb 22.595	Box		2018 Feb 22.66	97.46	94.75	6885	496	516	0.001	281

Microsat-2b	[43217]		400		2018 Feb 22.74	97.46	94.78	6886	499	516	0.001	283

D	Falcon 9 2nd stage #	2018 20 D	2018 Feb 22.595	Cylinder	12.6 long	2018 Feb 22.65	97.46	94.72	6884	495	515	0.001	269

[43218]	< 0.4 day	~ 4000	3.66 dia	2018 Feb 22.66	97.27	91.82	6742	210	516	0.023	263

2018 Feb 22

*1	Radar imaging satellite from Spain.

*2	Two satellites from Space-X for testing KU-band communications. Space-X plans to launch 4425 satellites in this network.

#	De-orbit burn or fuel dump observed from Scandinavia. The stage decayed over the Pacific Ocean.

IGS-O6  *	2018 21 A	2018 Feb 27.190			No TLE’s issued. Orbits from amateur observations.

[H-IIA 202]	[43223]				2020 Sep 4.04	97.35	94.25	6861	480	484	0.0003	357

(F38)	TAN-LP1

H-IIA 2nd stage	2018 21 B	2018 Feb 27.190	Cylinder		No TLE’s issued. Orbits from amateur observations.

[43224]				2020 Sep 6.96	97.27	94.38	6868	482	496	0.001	17

Fragments	2018 21 C D		2 pieces, 1 has decayed	For orbital information see extra pages at end of year

*	Japanese optical reconnaissance satellite.

GOES-17 $	2018 22 A	2018 Mar 1.918	Box + panel	6.1 x 5.6	2018 Mar 2.13	9.62	763.12	27663	7621	34947	0.494	178

[Atlas V 541]	[43226]	> million years	+ boom	x 3.9	2018 Mar 2.19	9.53	783.03	28142	8241	35285	0.481	180

(AV077)	CC-LC41		5211 full		2018 Mar 5.14	8.22	816.48	28938	9833	35285	0.440	180

2857 dry		2018 Mar 5.75	6.23	883.82	30507	12967	35290	0.366	180

2018 Mar 6.89	4.36	971.80	32500	16951	35291	0.282	181

2018 Mar 10.81	2.69	1089.53	35074	22101	35290	0.188	181

2018 Mar 12.39	1.30	1231.63	38061	28070	35295	0.095	182

2018 Mar 13.34	0.05	1421.63	41881	35310	35695	0.005	57

2018 Mar 16.61	0.06	1430.37	42053	35651	35696	0.0005	96

2018 Mar 17.09	0.07	1431.02	42065	35676	35697	0.0002	52

2018 Mar 19.49	0.03	1432.83	42101	35720	35724	0.00005	316							2018 Mar 20.47	0.06	1436.08	42165	35780	35792	0.0001	355

2018 Mar 23.50	0.05	1436.08	42164	35778	35794	0.002	31

2018 Apr 1.32	0.04	1436.12	42165	35778	35795	0.0002	41

2018 Apr 2.59	0.04	1436.07	42164	35777	35794	0.0002	57

2018 Apr 3.42	0.04	1436.08	42165	35777	35795	0.0002	54

Atlas V 2nd stage	2018 22 B	2018 Mar 1.918	Cylinder	12.68 long	2018 Mar 2.12	9.47	783.22	28146	8249	35286	0.480	179

(Centaur)	[43227]		2243	3.05 dia	2018 Mar 2.19	9.75	763.38	27669	7631	34950	0.494	178

$	USA weather satellite located at 137º W.

Hispasat 30W-6  *1	2018 23 A	2018 Mar 6.231	Box +2 panels	6.9 high	2018 Mar 6.46	26.97	387.30	17601	184	22260	0.627	177

[Falcon 9b4] #	[43228]	> million years	6092		2018 Mar 7.90	27.00	328.58	17640	287	22235	0.622	179

(F9-050, B1044)	CC-LC40			26.1 span	2018 Mar 9.55	27.02	448.53	19410	296	25767	0.656	181

2018 Mar 10.32	26.98	508.33	21649	308	30233	0.691	181

2018 Mar 12.30	27.03	636.72	24517	316	35960	0.727	183

2018 Mar 13.27	13.76	739.67	27093	5524	35905	0.561	183

2018 Mar 14.50	5.46	946.38	31931	15246	35858	0.323	184

2018 Mar 14.94	0.32	1367.93	40820	33114	35769	0.033	170

2018 Mar 16.58	0.14	1444.62	42331	35788	36118	0.004	179

2018 Mar 19.65	0.09	1436.07	42164	35781	35790	0.0001	31

2018 Mar 20.36	0.09	1436.08	42165	35784	35788	0.00005	17

Podsat 1 #2	2018 23 B	2018 Mar 6.231			2018 Mar 8.19	27.00	327.28	17600	191	22252	0.627	179

[43229]		90

Falcon 9 2nd stage	2018 23 C	2018 Mar 6.231	Cylinder	12.6 long	2018 Mar 6.46	26.93	326.57	17578	185	22215	0.627	177

[43230]		~ 4000	3.66 dia

*1	Spanish telecommunication satellite located at 30º W.

#2	Payload Orbital Delivery Satellite made up from 4 HiSAT satlets and deployed from the Hispasat 30W-6 while in geostationary transfer orbit.

It will test the use of small modules to make up larger satellites. The mission is sponsored by DARPA.

#	First stage not recovered due to severe weather conditions in the Atlantic Ocean recovery zone keeping the droneship in port.

O3b FM 15  %	2018 24 A	2018 Mar 9.715	Trapzodial box	3 long	2018 Mar 9.87	0.04	281.15	14216	7830	7846	0.0006	20

[Soyuz-ST.B/Fregat]	[43231]	> 100.000 years	+ 2 panels	1.6 maxwide

(VS18)	KOU-ELS		700 full

559 dry

O3b FM 16	2018 24 B	2018 Mar 9.715	Trapzodial box	3 long	2018 Mar 9.87	0.04	280.85	14206	7808	7848	0.001	300

[43232]	> 100.000 years	+ 2 panels	1.6 maxwide	2018 Mar 10.23	0.04	280.77	14204	7812	7838	0.0009	284

700 full

559 dry

O3b FM 14	2018 24 C	2018 Mar 9.715	Trapzodial box	3 long	2018 Mar 9.87	0.04	280.92	14209	7825	7836	0.0004	155

[43233]	> 100.000 years	+ 2 panels	1.6 maxwide	2018 Mar 10.03	0.04	280.92	14209	7820	7840	0.0007	175

700 full

559 dry

O3b FM 13	2018 24 D	2018 Mar 9.715	Trapzodial box	3 long	2018 Mar 9.86	0.05	280.85	14206	7820	7835	0.0005	135

[43234]	> 100.000 years	+ 2 panels	1.6 maxwide

700 full

559 dry

Fregat stage	2018 24 E	2018 Mar 9.715	Torus of	1.85 high	2018 Mar 10.03	0.08	276.18	14045	7654	7686	0.001	344

[43235]	> 100.000 years	spheres	3.35 dia

~1000 dry

~8100 full

%	Fourth launch with four O3b communication satellites for broadband data.

LKW-4 #	2018 25 A	2018 Mar 17.299	Hexagonal bus		2018 Mar 17.42	97.32	94.52	6874	491	499	0.0006	292

[CZ-2D] (Y49)	[43236]		+ 3 panels		2018 Mar 17.49	97.33	94.53	6874	489	502	0.0009	298

JIUQ-LC2

D	CZ-2D 2nd stage	2018 25 B	2018 Mar 17.299	Cylinder	10.9 long	2018 Mar 18.47	97.22	94.57	6876	485	510	0.002	56

[43237]			3.35 dia

Fragment	2018 25 C-E		3 pieces, all in orbit	For orbital information see extra pages at end of year

#	Chinese Land Survey Satellite (Ludi Kancha Weixing 4).

D	Soyuz MS-08 *	2018 26 A	2018 Mar 21.739	Cyl+beehive+	7.48 long	2018 Mar 21.76	51.63	88.77	6592	195	232	0.003	91

3M [Soyuz FG]	[43238]	196.751 days	+spheroid+	2.72 maxdia	2018 Mar 22.00	51.66	89.48	6628	241	257	0.001	63

R		BAI-LC1/5	2018 Oct 4.490	2 panels	2.2 dia	2018 Mar 22.05	51.64	90.83	6694	312	319	0.0006	120

7167	10.6 span	2018 Mar 24.77	51.64	92.65	6783	403	405	0.0001	246

2018 Oct 3.33	51.64	92.67	6784	403	408	0.0004	234

D	Soyuz-FG 3rd stage	2018 26 B	2018 Mar 21.739	Cylinder	6.74 long	2018 Mar 21.76	51.64	88.60	6584	190	221	0.002	65

(Blok I)	[43239]	3.320 day	2410	2.66 dia	2018 Mar 24.92	51.63	87.45	6527	144	152	0.0006	101

2018 Mar 25.059 #

*	Soyuz MS-08 with a 3 person crew (Artemyev, Feustel and Arnold) docked 2018 Mar 23.820 with ISS (Poisk port).

Undocked 2018 Oct 4.331 and landed in Kazachstan.

#	Decayed over Mediterranean Sea west of Italy; observed from France and Italy.

GSAT-6A  %	2018 27 A	2018 Mar 29.476	Box +2 panels	2.1 x 2.5	2018 Mar 29.28	20.69	643.77	24697	148	36489	0.736	178

[GSLV Mk II]	[43241]	> million years	+ mesh antenna	x 4.1	2018 Mar 30.60	11.96	740.60	27115	5029	36444	0.579	179

(F08)	SRI-LC2		reflector	9.6 span

2140	6 dia

D	GSLV 3rd stage	2018 27 B	2018 Mar 29.476	Cylinder	8.7 long	2018 Mar 29.28	20.67	635.47	24485	146	36066	0.734	178

[43242]	615 days	~2500	2.8 dia	2019 Dec 4.25	20.19	95.88	6940	104	1019	0.066	23

2019 Dec 4

%	Indian communication satellite at 83º E over the equator.

Cosmos 2525 (EMKA) *	2018 28 A	2018 Mar 29.735			2018 Mar 29.81	96.64	90.87	6696	315	318	0.0002	102

[Soyuz 2-1v]	[43243]

PLE-LC43/4

D	Soyuz 2-1v 2nd stage	2018 28 B	2018 Mar 29.735	Cylinder	6.74 long	2018 Mar 29.81	96.64	90.85	6694	315	316	0.00009	164

[43244]	220 days	2410	2.66 dia	2018 Nov 4.23	96.62	87.18	6513	130	139	0.0007	204

2018 Nov 4

*	Experimental small satellite from the Russian Ministry of Defence.

Beidou-3  M7  &	2018 29 A	2018 Mar 29.747	Box +2 panels		2018 Mar 29.99	55.00	787.23	28242	21535	22192	0.012	178

[CZ-3B/YZ1]	[43245]	1 milion years

XI-LC2

Beidou-3  M8  &	2018 29 B	2018 Mar 29.747	Box +2 panels		2018 Mar 30.09	55.00	787.32	28244	21540	22191	0.012	178

[43246]	1 milion years

CZ-3B 3rd stage 	2018 29 C	2018 Mar 29.747	Cylinder	12.38 long	2018 Mar 29.86	54.98	325.28	15668	193	18386	0.581	170			[43247]		2740	3.0 dia

Yuanzheng-1	2018 29 D	2018 Mar 29.747			2018 Mar 29.90	55.25	811.68	28824	22176	22714	0.009	351

Upperstage	[43248]				2018 Mar 31.03	55.26	810.93	28806	22162	22693	0.009	342

&	Chinese navigation satellites.

Iridium 144 *	2018 30 A	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 30.66	86.69	97.03	6995	605	628	0.002	239

[Falcon 9b4	[43249]		+2 panels	x1.5	2018 Mar 30.84	86.68	97.02	6994	606	625	0.001	252

(F9-051, B1041-2) #	VDB-SLC4E		860	9.4 span	2018 Apr 8.00	86.60	97.92	7038	650	669	0.001	222

2018 Apr 8.61	86.61	98.15	7048	669	671	0.0002	63

2018 Apr 9.30	86.57	98.53	7067	683	693	0.0007	144

2018 Apr 9.57	86.51	98.93	7086	705	710	0.0003	35

2018 Apr 26.49	86.44	99.88	7131	752	754	0.0001	21

2018 Apr 27.46	86.39	100.37	7155	775	777	0.0002	19

2018 Apr 28.02	86.40	100.40	7156	776	778	0.0002	82

Iridium 149	2018 30 B	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.71	86.68	97.03	6995	608	626	0.001	256

[43250]		+2 panels	x1.5	2018 Apr 8.40	86.61	97.97	7040	652	670	0.001	226

860	9.4 span	2018 Apr 9.22	86.61	98.18	7050	671	672	0.00008	91

2018 Apr 10.38	86.53	98.88	7084	701	709	0.0006	81

2018 Apr 12.38	86.52	98.90	7085	705	707	0.0001	21

2018 Apr 25.52	86.43	99.93	7134	755	756	0.0001	359

2018 Apr 25.59	86.41	100.25	7149	769	771	0.0002	38

2018 Apr 26.49	86.39	100.37	7154	775	777	0.0001	2

2018 Apr 26.70	86.39	100.40	7156	776	778	0.0002	85

Iridium 157	2018 30 C	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.71	86.68	97.03	6995	607	626	0.001	255

[43251]		+2 panels	x1.5	2018 Apr 5.10	86.60	97.98	7041	653	671	0.001	240

860	9.4 span	2018 Apr 7.74	86.52	98.73	7077	693	703	0.0007	206

2018 Apr 18.42	86.45	99.67	7121	742	743	0.00006	80

2018 Apr 19.68	86.39	100.35	7154	775	776	0.00008	52

2018 Apr 20.02	86.39	100.40	7156	775	779	0.0002	84

Iridium 140	2018 30 D	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.78	86.68	97.03	6995	607	626	0.001	253

[43252]		+2 panels	x1.5	2018 Apr 13.39	86.60	98.00	7041	654	672	0.001	205

860	9.4 span	2018 Apr 14.89	86.57	98.63	7059	682	699	0.001	346

2018 Apr 16.89	86.52	98.97	7088	707	710	0.0002	51

2018 May 5.53	86.44	99.90	7132	753	755	0.0001	42

2018 May 6.44	86.40	100.37	7154	775	776	0.0001	52

2018 May 6.86	86.40	100.38	7155	776	777	0.00007	141

2018 May 7.42	86.40	100.40	7156	777	778	0.00007	106

2018 Jun 28.25	86.40	100.40	7156	775	780	0.0004	86

Iridium 145	2018 30 E	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 30.80	86.68	97.02	6995	606	626	0.001	250

[43253]		+2 panels	x1.5	2018 Apr 4.36	86.61	97.97	7040	652	670	0.001	243

860	9.4 span	2018 Apr 5.72	86.60	98.18	7050	671	673	0.0001	57

2018 Apr 6.54	86.54	98.92	7085	702	712	0.0007	191

2018 Apr 16.68	86.39	100.38	7155	775	777	0.0001	17

2018 Apr 17.03	86.39	100.40	7156	777	777	0	98

Iridium 146	2018 30 F	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.71	86.68	97.02	6996	608	627	0.001	260

[43254]		+2 panels	x1.5	2018 Apr 6.72	86.62	98.00	7041	652	674	0.002	188

860	9.4 span	2018 Apr 7.87	86.62	98.23	7053	663	685	0.002	184

2018 Apr 8.22	86.65	98.67	7074	687	703	0.001	263

2018 Apr 9.53	86.59	98.95	7087	701	715	0.001	61

2018 Apr 22.46	86.45	99.77	7126	746	749	0.0002	70

2018 Apr 23.50	86.40	100.35	7154	774	775	0.00007	351

2018 Apr 27.06	86.39	100.40	7156	776	779	0.0002	103

Iridium 148	2018 30 G	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.71	86.68	97.02	6994	606	625	0.001	250

[43255]		+2 panels	x1.5	2018 Apr 10.76	86.58	97.42	7013	618	652	0.002	229

860	9.4 span	2018 Apr 14.15	86.59	97.40	7013	600	668	0.005	288

2018 Apr 16.86	86.52	98.93	7086	706	709	0.0002	105

2018 May 2.47	86.44	99.68	7122	736	750	0.001	273

2018 May 3.45	86.40	100.30	7152	772	774	0.0002	341

2018 May 3.72	86.40	100.37	7154	774	778	0.0003	79

2018 May 4.49	86.40	100.40	7156	775	779	0.0003	91

Iridium 142 $	2018 30 H	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 31.71	86.68	97.05	6996	608	626	0.001	258

[43256]		+2 panels	x1.5	2018 Apr 6.32	86.64	97.98	7041	650	675	0.002	316

860	9.4 span	2018 Apr 8.36	86.52	99.07	7092	713	714	0.00008	59

2018 Apr 18.35	86.51	99.20	7099	719	722	0.0002	18

2018 Apr 18.63	86.51	99.52	7114	729	742	0.0009	64

2018 Apr 18.90	86.44	99.85	7130	751	752	0.00008	35

2018 Apr 19.18	86.44	99.87	7131	752	753	0.00005	118

2018 Apr 19.67	86.41	100.25	7149	770	770	0	92

2018 Apr 19.88	86.39	100.37	7155	776	776	0	28

2018 Apr 20.85	86.39	100.40	7156	776	779	0.0002	93

Iridium 150	2018 30 J	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 30.80	86.68	97.05	6996	608	626	0.001	261

[43257]		+2 panels	x1.5	2018 Apr 9.55	86.62	97.80	7032	649	658	0.0007	127

860	9.4 span	2018 Apr 13.90	86.52	98.93	7086	706	709	0.0002	106

2018 Apr 16.90	86.52	99.10	7094	714	717	0.0002	69

2018 May 1.50	86.43	99.98	7136	756	759	0.0002	43

2018 May 2.47	86.40	100.37	7155	774	777	0.0002	39

2018 May 3.45	86.40	100.40	7156	775	779	0.002	82

Iridium 143	2018 30 K	2018 Mar 30.593	Trapzodial box	3.1 x 2.4	2018 Mar 30.80	86.69	97.05	6996	608	626	0.001	262

[43258]		+2 panels	x1.5	2018 Apr 3.14	86.60	97.97	7040	653	670	0.001	251

860	9.4 span	2018 Apr 4.37	86.54	98.82	7081	692	713	0.002	347

2018 Apr 5.54	86.52	99.00	7089	710	711	0.0001	3

2018 Apr 16.35	86.52	99.10	7094	714	717	0.0002	74

2018 Apr 27.43	86.39	100.40	7156	776	778	0.0001	106

Falcon-9 2nd stage	2018 30	2018 Mar 30.593	Cylinder	13 long	De-orbited after satellite deployment and decayed over Pacific Ocean.

[NNA]		3900	3.66 dia

*	Fifth launch with 10 Iridium Next satellites with all going to plane 1.

#	The 1st stage made a retro burn and performed a “landing at sea” with no drone ship available.

SpaceX planned a second recovery attempt of one half of the fairing using the specially modified boat Mr. Steven, but the parafoil twisted, which led to

the fairing half missing the boat.

Gaofen 1-02	2018 31 A	2018 Mar 31.140	Box +2 panels		2018 Mar 31.26	98.08	96.05	6947	493	644	0.011	33

[CZ-4C] (Y26)	[43259]		805		2018 Mar 31.80	98.04	97.53	7019	638	642	0.0003	265

WUZ-LC9

Gaofen 1-03	2018 31 B	2018 Mar 31.140	Box +2 panels		2018 Mar 31.26	98.03	97.48	7017	637	640	0.0003	266

[43260]		805		2018 Apr 3.24	98.04	97.47	7016	631	643	0.0009	318

2018 May 30.21	98.03	97.53	7019	636	644	0.0006	145

Gaofen 1-04	2018 31 D	2018 Mar 31.140	Box +2 panels		2018 Mar 31.26	98.02	97.53	7019	637	644	0.0004	277

[43262]		805		2018 Apr 3.39	98.02	97.58	7022	641	646	0.0004	197

2018 Jul 24.49	98.03	97.53	7019	638	642	0.0003	283

CZ-4C 3rd stage	2018 31 F	2018 Mar 31.140	Cylinder	4.9 long	2018 Mar 31.81	98.08	96.05	6947	491	647	0.011	29

[43264]		1760	2.9 dia

Fragments	2018 31 C, E, G-K	5 pieces, 1 has decayed	For orbital information see extra pages at end of year

#	Chinese Earth-Imaging satellites.

D	Dragon CRS-14 *	2018 32 A	2018 Apr 2.854	Blunt cone	4.4 high	2018 Apr 2.87	51.64	90.12	6658	203	356	0.011	49

[Falcon 9b4]  #	[43267]	32.940 days	+ cylinder	3.66 dia	2018 Apr 3.37	51.64	91.65	6734	352	358	0.0005	328

(F9-052, B-1039-2)	CC-LC40	2018 May 5.794	+ 2 panels	2.8 high 	2018 Apr 3.82	51.64	92.43	6772	391	396	0.0003	321

~ 8200 full	16.5 span	2018 Apr 4.14	51.65	92.58	6780	400	403	0.0002	325

2647 cargo		2018 Apr 4.22	51.64	92.65	6783	403	405	0.001	301

2018 Apr 4.79	51.64	92.65	6783	403	405	0.0002	304

2018 May 4.76	51.64	92.65	6783	402	406	0.0003	49

D	Fragments	2018 32 B, C  2 pieces, both have decayed		For orbital information see extra pages at end of year

Solar panel covers

%	Dragon CRS-14 (C110) rendezvoused with ISS and was 2018 Apr 4.445 grappled by the stations robotic arm and berthed 2018 Apr 4.628 to Harmony’s nadir port.

In the trunk of Dragon are 3 payloads to be installed on ISS by the robotic arms: Atmosphere and Space Interactions Monitor, Materials ISS Experiment		Flight Facility a material esposure experiment, Pump Flow Control Subassembly a spare part to be stowed outside ISS.

The Dragon capsule flew in space in April 2016 as CRS-08 and the 1st stage launched CRS-12 in Aug 2017.

CRS-14 was unberthed 2018 May 5 by Canadarm2. Released 2018 May 5.558 from the robotic arm. It brings back around 1800 kg of cargo.

Dragon CRS-14 landed some 625 km west of Baja California in the Pacific Ocean.

#	The 1st stage was used to perform experimental manoeuvres and made a hard splashdown in the Atlantic Ocean.

The 2nd stage was de-orbited after release of the Dragon.

Superbird 8/DSN 1 *	2018 33 A	2018 Apr 5.899	Box +2 panels		2018 Apr 5.99	3.00	631.40	24380	257	35746	0.728	178

(Kirameki 1)	[43271]	> million years	5348		2018 Apr 8.28	1.65	750.10	27347	6208	35729	0.540	179

[Ariane 5 ECA])	KOU-ELA3				2018 Apr 10.54	0.18	1336.27	40187	31895	35722	0.048	178

(VA242					2018 Apr 11.62	0.09	1434.22	42128	35712	35786	0.0009	320

2018 Apr 13.74	0.09	1436.08	42164	35779	35793	0.0002	90

2018 Apr 14.69	0.09	1437.12	42185	35792	35820	0.0003	301

2018 Apr 16.58	0.09	1436.03	42164	35781	35789	0.00009	129

2018 Apr 16.71	0.09	1436.08	42165	35781	35791	0.0001	129

2018 Apr 18.99	0.09	1436.10	42165	35780	35792	0.0001	116

Hylas 4 **	2018 33 B	2018 Apr 5.899	Box +2 panels		2018 Apr 5.98	3.03	630.15	24348	252	35686	0.728	178

[43272]	> million years	4050		2018 Apr 8.10	1.76	726.35	26766	5054	35722	0.572	179

2018 Apr 10.59	0.79	915.47	31231	13989	35716	0.348	180

2018 Apr 12.33	0.21	1216.82	37755	26900	35854	0.119	182

2018 Apr 13.75	0.11	1329.68	40055	31622	35732	0.051	155

2018 Apr 16.31	0.04	1431.90	42083	35677	35732	0.0007	158

2018 Apr 17.76	0.04	1433.48	42114	35733	35737	0.00005	141

2018 Apr 17.86	0.05	1434.25	42129	35727	35773	0.0006	339

2018 Apr 19.36	0.02	1436.08	42164	35779	35729	0.0002	164

2018 Apr 20.36	0.04	1436.10	42165	35785	35787	0.00002	0

2018 Jul 20.12	0.01	1440.05	42242	35852	35875	0.0003	185

2018 Jul 24.13	0.05	1443.88	42317	35896	38981	0.001	133

2018 Aug 17.19	0.06	1436.02	42163	35767	35802	0.004	27

2018 Aug 19.18	0.06	1436.07	42164	35768	35803	0.0004	34

2018 Aug 25.17	0.06	1436.08	42165	35766	35806	0.0005	39

Sylda upperpart	2018 33 C	2018 Apr 5.899	Barrel		2018 Apr 5.98	3.02	630.57	24359	251	35709	0.728	178

[43273]

Ariane 5 2nd stage	2018 33 D	2018 Apr 5.899	Cylinder	5.84 long	2018 Apr 5.95	3.02	623.25	24170	260	35322	0.725	177

(ESC-A + VEB) *3	[43274]		5668	5.4 dia

*	Japanse commercial and military satellite.

**	British communication satellite.

Yaogan 31 A #	2018 34 A	2018 Apr 10.184			2018 Apr 10.38	63.41	107.15	7473	1090	1099	0.0006	48

[CZ-4C]	[43275]				2018 Apr 10.70	63.41	107.10	7471	1086	1099	0.0009	39

JIUQ				2018 Jul 28.75	63.41	107.03	7468	1077	1102	0.002	6

Yaogan 31 B	2018 34 B	2018 Apr 10.184			2018 Apr 10.41	63.40	107.13	7472	1088	1099	0.0007	41

[43276]				2018 May 1.07	63.40	107.02	7467	1081	1097	0.001	353

2018 May 3.07	63.40	106.95	7464	1074	1096	0.001	9

2018 May 9.09	63.40	107.03	7468	1082	1097	0.001	7

Yaogan 31 C	2018 34 C	2018 Apr 10.184			2018 Apr 10.46	63.40	107.10	7471	1086	1099	0.0009	86

[43277]				2018 Apr 12.65	63.41	106.78	7456	1064	1092	0.002	2

2018 Apr 18.68	63.41	106.42	7440	1049	1073	0.002	4

2018 May 6.05	63.41	106.70	7452	1063	1085	0.002	359

2018 May 11.17	63.41	107.03	7468	1081	1098	0.001	8

CZ-4C 3rd stage	2018 34 D	2018 Apr 10.184	Cylinder	4.9 long	2018 Apr 10.45	63.45	105.82	7411	957	1108	0.010	19

[43278]		1760	2.9 dia

Weina 1B  ##	2018 34 E	2018 Apr 10.184			2018 Apr 10.46	63.40	107.08	7471	1084	1099	0.001	39

[43279]				2018 Jul 14.94	63.41	107.03	7468	1078	1101	0.002	16

Fragment	2018 34 F-K		5 pieces, all in orbit	For orbital information see extra pages at end of year

#	Chinese military reconnaissance satellites.

##	Nanosatellite for technological experiments.

IRNSS 1I  *	2018 35 A	2018 Apr 11.940	Box +2 panels	1.58 x 1.5	2018 Apr 11.83	19.21	362.38	16837	270	20648	0.605	178

[PSLV-XL] (C41)	[43286]	> million years	1425 full	x 1.5	2018 Apr 13.18	19.21	632.28	24403	293	35756	0.727	180

SRI-LC1		~600 dry	~6 span	2018 Apr 14.66	24.69	801.67	28596	8652	35763	0.474	180

2018 Apr 15.72	28.34	1374.13	40943	33149	35980	0.003	147

2018 Apr 16.21	28.53	1426.60	41979	35463	35737	0.003	182

2018 Apr 16.71	28.70	1716.18	47483	36926	45282	0.088	12

2018 Apr 16.73	28.55	1450.85	42453	35842	36307	0.005	3

2018 Apr 16.74	28.52	1426.68	41980	35462	35741	0.003	181

2018 Apr 30.58	28.56	1436.08	42165	35701	35871	0.002	189

PSLV 4th stage	2018 35 B	2018 Apr 11.940	Cylinder	2.6 long	2018 Apr 11.83	19.12	367.00	16980	269	20935	0.609	179

[43287]		920	2.02 dia	2018 Apr 18.18	19.12	367.12	16984	273	20938	0.608	187

*	Indian communication satellite.

CBAS (USA 283) #1	2018 36 A	2018 Apr 14.968			Geostationary orbit. No TLE’s issued. Orbits from amateur observations.

[Atlas V 551]	[43339]	> million years			2018 Apr 27.07	0.05	1408.97	41632	35232	35275	0.0005	126

(AV-079)	CC-LC41

EAGLE (USA 284) #2	2018 36 B	2018 Apr 14.968	Drum + panel	0.61 high	Super geosynchronous orbit. No TLE’s issued. Orbits from amateur obs.

(ESPA Platform)	[43340]	> million years	~ 450 dry	1.575 dia	2018 Apr 27.06	0.06	1409.93	41651	35258	35287	0.0003	117

~ 9 span	2020 Jun 21.79	1.07	1451.85	42473	36083	36105	0.0003	19

Atlas V 2nd stage	2018 36 C	2018 Apr 14.968	Cylinder	12.68 long	Geo transfer orbit. No TLE’s issued. Orbits from amateur obs.

(Centaur)	[43341]		2243	3.05 dia	2018 Apr 27.36	0.06	1329.50	40052	32002	35344	0.042	134

Mycroft #3	2018 36 E		Box + panel	~ 0.70x0.57	Super geosynchronous orbit. No TLE’s issued.

(USA 285)	[43445]			x 0.57

~ 2.5 span

ESPASat 2	2018 36 F				Geosynchronous orbit. No TLE’s issued.

(USA 286)	[43446]

ESPASat 3	2018 36 G				Geosynchronous orbit. No TLE’s issued. Orbits from amateur obs.

(USA 287)	[43465]				2019 Dec 16.27	0.58	1451.98	42475	36094	36098	0.00005	331

Atlas fragment	2018 36 D 	[43342]	1 piece, in orbit	No TLE’s issued.

#1	Continuous Broadcast Augmenting SATCOM is an USA military communications satellite.

#2	Evolved Expendable Launch Vehicle (EELV) Secondary Payload Adapter (ESPA) Augmented Geosynchronous Laboratory Experiment is a demonstration mission for a

maneuverable satellite design. Five secondary payloads are attached to EAGLE of which at least one (Mycroft, see *3) will be deployed.

#3	Deployed from EAGLE to conduct a space situational awareness experiment in which it will retreat to 35 km from EAGLe and then approach it to about 1 km.

Mycroft is probably named after the older brother of Sherlock Holmes from Arthur Conan Doyle’s books.

Cosmos 2526  %	2018 37 A	2018 Apr 18.925	Box + 2 panels		2018 Apr 19.63	48.65	632.73	24414	386	35685	0.723	0

(Blagnovest 12L)	[43432]	> million years	3000-3500		2018 Apr 25.84	0.09	1427.27	41992	35497	35730	0.003	150

[Proton-M/Breeze-M]	BAI-LC81/24				2018 Apr 27.88	0.09	1429.20	42030	35555	35747	0.002	147

2018 May 1.18	0.08	1432.30	42090	35650	35773	0.001	137

2018 May 7.51	0.05	1435.68	42157	35763	35793	0.0004	154

2018 May 9.58	0.04	1436.07	42164	35781	35790	0.0001	114

2018 Jun 1.57	0.05	1436.10	42165	35783	35789	0.00007	85

2018 Jun 17.11	0.04	1432.10	42087	35697	35719	0.0003	356

2018 Jun 19.57	0.05	1427.53	41997	35568	35669	0.001	341

2018 Jun 19.82	0.05	1426.70	41981	35589	35615	0.0003	344

2018 Jun 22.73	0.04	1426.30	41973	35580	35608	0.0003	320

2018 Jul 26.93	0.05	1436.12	42165	35786	35787	0.00002	312

2012 Jul 28.92	0.05	1436.05	42164	35784	35787	0.00005	15

Breeze-M stage	2018 37 B	2018 Apr 18.925	Cylinder	2.61 long	2018 Apr 24.80	0.08	1590.77	45141	35703	41820	0.068	163

[43433]		+ spheres	2.49 dia

D	Breeze-M tank	2018 37 C	2018 Apr 18.925	Torus	0.80 cross	2018 Apr 25.45	48.67	632.78	24416	387	35687	0.723	1

[43434]	437 days		4.0 dia	2019 Jun 26.81	48.25	93.23	6811	102	764	0.049	168

2019 Jun 29

Breeze-M fragment	2018 37 D	[43469]			2018 May 16.86	0.03	1588.28	45093	35126	42303	0.080	149

%	Russian military communication satellite. Blagovest means “Good News. To be stationed at 128° East.

TESS  *	2018 38 A	2018 Apr 18.952	Hexagonal Cyl	1.5 high	2018 Apr 19		8640		300	272000

[Falcon 9b4]  #	[43435]		+ cut cone	1.2 maxdia	2018 Apr 25.19	28.32	9048.03	143834	2233	272679	0.940	231

(F9-053, B1045-1)	CC-LC40		+ 2 panels	3.9 span	2018 Apr 25.29	28.38	13147.28	184523	2233	354056	0.953	231

362		2018 May 17		13.7 days		108000	376000

Falcon-9 2nd stage	2018 38 B	2018 Apr 18.952	Cylinder	13 long	2018 Apr 19	29.6			248	270461

[43436]		3900	3.66 dia	2018 Apr 19	Heliocentric orbit.

*	Transiting Exoplanet Survey Satellite will survey the sky in search of tell-tale dips in light from bright, nearby stars. The brief, slight reduction in brightness registered by TESS could be evidence of a planet passing in front of the star. Lunar flyby and gravity assist 2018 May 17. The orbit is in a 2:1 resonance with the moon; 2 orbits of TESS every 1 orbit of the moon around the Earth.

#	The 1st stage made a soft landing at the drone ship OCISLY in the Atlantic Ocean.

The 2nd stage fired its engine for a 3rd time to put it in a heliocentric disposal orbit.

Sentinel 3B  %	2018 39 A	2018 Apr 25.749	Box + panel	2.20x2.21	2018 Apr 25.90	98.62	100.93	7182	794	812	0.001	284

[Rockot/Breeze KM]	[43437]		1244 full	x3.71	2018 Apr 26.16	98.62	101.53	7187	802	814	0.0009	315

PLE-LC133/3		1124 dry	~ 10 span

Breeze KM stage	2018 39 B	2018 Apr 25.749	Cylinder	2.6 long	2018 Apr 25.89	98.69	106.12	6951	392	752	0.026	306

[43438]		1320	2.5 dia

%	European Land & Ocean Sensing satellite in the Copernicus Earth Observation Constellation.

Zhuhai-1 OHS-01	2018 40 A	2018 Apr 26.196	Box +2 panels		2018 Apr 26.32	97.40	94.68	6882	494	512	0.001	284

[CZ-11] (Y 04)	[43439]		80-100		2018 Apr 28.50	97.40	94.72	6884	497	514	0.001	260

JIUQ-LC-E2

Zhuhai-1 OVS-02	2018 40 B	2018 Apr 26.196 	Box +2 panels		2018 Apr 26.32	97.40	94.68	6882	494	512	0.001	284

[43440]		80-100

Zhuhai-1 OHS-02	2018 40 C	2018 Apr 26.196 	Box +2 panels		2018 Apr 26.32	97.40	94.67	6881	493	511	0.001	290

[43441]		80-100

Zhuhai-1 OHS-03	2018 40 D	2018 Apr 26.196 	Box +2 panels		2018 Apr 26.32	97.39	94.67	6881	493	511	0.001	280

[43442]		80-100

Zhuhai-1 OHS-04	2018 40 E	2018 Apr 26.196 	Box +2 panels		2018 Apr 26.32	97.40	94.65	6880	491	511	0.001	291

[43443]		80-100

CZ-11 3rd stage	2018 40 F	2018 Apr 26.196			2018 Apr 26.81	97.29	91.02	6703	117	532	0.031	310

[43444]	3 days			2018 Apr 29	97.25	86.89		92	149	from SATCAT

2018 Apr 26

*1	Four OHS satellites (OHS-2A – 2D) in the Zhuhai constellation for earth imaging in 32 spectral bands to gather more information about surface features than a typical optcal instrument.

*2	OVS-2A satellite in the Zhuhai constellation for video imaging in about 90 cm resolution.

APStar-6C  #	2018 41 A	2018 May 3.671	Box +2 panels	3.60 x 2.36	2018 May 3.77	27.18	752.75	27411	238	41827	0.759	180

[CZ-3B/E]	[43450]		~ 5200	x 2.10	2018 May 14.78	0.15	1436.08	42164	35783	35789	0.00007	233

XI-LC2			~15 span	2018 May 19.25	0.14	1436.10	42165	35784	35788	0.0005	205

CZ-3B 3rd stage 	2018 41 B	2018 May 3.671	Cylinder	12.38 long	2018 May 3.78	27.20	728.08	26809	198	40663	0.755	179

[43451]		2740	3.0 dia

#	Chinese build communication satellite for APStar of Hong Kong.

D	InSight *	2018 42 A	2018 May 5.462	Drum + 4 legs	6.0 x 1.56	Heliocentric orbit towards Mars.

[Atlas V 401]	[43457]		+2 solarpanels	x 1.0 with	2018 May 5	2.2			1.01 AU	1.43 AU

(AV-078)	VDB-SLC3E	2018 Nov 26	694 at launch	panels de-	Softlanded on Mars at 4.5° N, 135.0° E.

358 at landing	ployed

MARCO-A *1	2018 42 B	2018 May 5.462	6U Cube	0.366x0.243	Heliocentric orbit towards Mars.

(Wall-E)	[43458]		+2 panels	x 0.118	2018 May 5	2.2			1.01 AU	1.43 AU

13.5	0.60 span	2018 Nov 30	1.4			1.137	1.601

MARCO-B *1	2018 42 C	2018 May 5.462	6U Cube	0.30 x 0.20	Heliocentric orbit towards Mars.

(Eva)	[43459]		+2 panels	x 0.10	2018 May 5	2.3			1.01 AU	1.44 AU

13.5	0.60 span	2018 Nov 30	1.8			1.146	1.564

Atlas V 2nd stage	2018 42 D	2018 May 5.462	Cylinder	12.68 long	Parking orbit

(Centaur)   *2	[43460]		2243	3.05 dia	2018 May 5.52	63.97	88.02	6555	167	186	0.001	352

Heliocentric orbit towards Mars.

*	Interior exploration using Seismic Investigations, Geodesy and Heat Transport. During the flight to Mars Insight was inside the thermoshell and attached to the cruise stage. They separated shortly before atmosphere entry. The cruise stage burned up in the atmosphere.

Insight made a soft landing 2018 Nov 26.828 in Elysium Planitia. It deployed a seismometer and heat flow meter using a robotic arm.

*1	Two MARs Cube One cubesats for experimental communications in deep space. Passed 1625 km (Marco A) and 1749 km (Marco B) km from Mars and relayed radio signals from Insight. Last contact with Marco-A was 2018 Dec 28 and with Marco-B 2019 Jan 4. The satellites were 1.6 and 3.2 million km beyond Mars.

*2	After cruising in the parking orbit the Centaur re-ignited to send the spacecraft towards Mars.

Gaofen-5 %	2018 43 A	2018 May 8	Box + panel		2018 May 8.90	98.13	98.45	7063	681	688	0.0004	47

[CZ-4C]	[43461]				2018 May 14.43	98.12	98.78	7079	700	700	0	238

WUZ-LC9

CZ-4C 3rd stage	2018 43 B	2018 May 8	Cylinder	4.9 long	2018 May 8.83	98.11	97.18	7003	559	689	0.009	34

[43462]		1760	2.9 dia	2018 May 9.29	98.11	97.25	7005	560	694	0.010	34

%	Chinese civilian earth observing satellite.

Bangabandhu-1 *	2018 44 A	2018 May 11.843	Box +2 panels		2018 May 11.91	19.31	628.57	24307	308	35549	0.725	179

[Falcon 9b5]  #	[43463]				2018 May 13.96	11.02	729.12	26834	5399	35513	0.561	180

(F9-054, B1046-1)	CC-LC39A				2018 May 17.89	0.81	1285.45	39162	29889	35678	0.074	180

2018 May 23.37	0.05	1436.18	42167	35783	35792	0.0001	272

2018 May 23.73	0.04	1436.08	42165	35783	35788	0.00006	286

Falcon-9 2nd stage	2018 44 B	2018 May 11.843	Cylinder	13 long	2018 May 11.91	19.29	628.25	24299	305	35535	0.725	179

[43464]		3900	3.66 dia

*	Communication satellite for Bangladesh.

#	The 1st stage is the 1st Block 5 version of the Falcon 9. It soft landed on the drone ship OCISLY in the Atlantic Ocean

Queqiao *1	2018 45 A	2018 May 20.895	Box		2018 May 20.97	27.50	14628	198130	394	383109	0.966	171

[CZ-4C] (Y27)	[43470]		+2 panels		2018 Jun 13.458	Entered halo-orbit around Earth-Moon L-2 point.

XI-LC3		+ dish	4.2 dia

+3 antennas	5 long

Longjiang 1 *2	2018 45 B	2018 May 20.895	Cube		2018 May 20.97	27.50	14628	198130	394	383109	0.966	171

(DSLWP-A)	[43471]		47		In solar orbit.

D	Longjiang 2  *2	2018 45 C	2018 May 20.895	Cube		2018 May 20.97	27.50	14628	198130	394	383109	0.966	171

(DSLWP-B)	[43472]	437 days	47		Entered lunar orbit 2018 May 25

2019 Jul 31.514			Sent crashing into the moon 2019 Jul 31; impact 16.6956 N, 159.5170 E.

D?	CZ-4C 3rd stage *3	2018 45 D	2018 May 20.895	Cylinder	4.9 long	2018 May 20.97	27.50	14628	198130	394	383109	0.966	171

[43473]	128 days ?	1760	2.9 dia	2018 Jul 4.97	23.10	15625.60	207039	5458	395862	0.943	172

2018 Sep 25 ?			2018 Jul 15.78	21.82	16098.10	211192	6278	403348	0.940	171

2018 Jul 27.83	23.31	17920.48	226844	16762	424168	0.898	177

2018 Aug 3.74	24.67	17995.85	227479	15773	426429	0.903	178

2018 Aug 20.47	27.72	18250.05	229616	21809	424666	0.877	177

2018 Sep 2.27	30.63	17956.53	227148	19356	422182	0.887	179

2018 Sep 25.44	21.44	2449.82	60198	6925	100714	0.779	160

*1	Chinese relay satellite for the Chang’e-4 rover on the backside of the moon. It is stationed at the Earth-Moon L2 point behind the Moon about 455000 km from Earth. With the 5m dish it relays signals from the rover to Earth.

After the relay mission three 5 m antennas will be deployed (Netherlands Chinese Low-Frequency Explorer) to measure radio waves below 30 MHz originating from the period directly after the Big Bang, when the first stars and galaxies were formed.

*2	Discovering the Sky at Longest Wavelenghts Pathfinder A & B are communication test satellites.

Longjiang 1 suffered an anomaly during Earth-Moon transfer and did not enter lunar orbit.

*3	Orbit strongly influenced by Earth and Moon gravity. Space-Track (administately ?) decayed it 2018 Sep 25

D	Cygnus OA-9 #	2018 46 A	2018 May 21.364	Cylinder	6.39 long	2018 May 21.43	51.62	89.90	6648	223	316	0.007	141

S.S. J.R. Thompson	[43474]	70 days	+2 panels	3.07 dia	2018 May 21.60	51.61	90.90	6697	313	324	0.0008	9

[Antares 230]	WLI-LC0A	2018 Jul 30	6200		2018 May 22.22	51.64	91.70	6737	312	404	0.007	23

2018 May 22.23	51.62	91.78	6741	325	399	0.006	179

2018 May 23.34	51.64	92.37	6769	385	396	0.0008	290

2018 May 24.32	51.65	92.65	6783	402	407	0.0004	118

2018 Jul 14.56	51.64	92.65	6783	402	407	0.0004	314

2018 Jul 16.63	51.64	94.18	6858	476	492	0.0004	340

2018 Jul 22.04	51.64	94.22	6859	477	483	0.0005	49

2018 Jul 22.50	51.64	94.32	6864	480	490	0.0007	337

2018 Jul 30.47	51.64	92.47	6774	381	409	0.002	270

D	Antares 2nd stage	2018 46 B	2018 May 21.364	Cylinder	5.99 long	2018 May 21.43	51.61	89.38	6623	203	285	0.006	138

(Castor 30 XL)	[43475]	13 days	~2100	2.34 dia	2018 May 21.47	51.60	89.55	6630	201	303	0.008	140

2018 Jun 3			2018 Jun 3.70	51.59	88.23	6566	167	207	0.003	207

AeroCube 12A #2	2018 46 C	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 20.61	51.64	94.25	6861	477	488	0.0008	323

[43556]			x0.10

AeroCube 12B  #2	2018 46 D	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 20.55	51.64	94.25	6861	477	488	0.0008	324

[43557]			x0.10

Lemur-2 81 #1	2018 46 E	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 18.71	51.64	94.25	6861	477	487	0.0007	320

VU	[43558]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 80 #1	2018 46 F	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 19.88	51.64	94.25	6861	477	487	0.0008	327

Alexander	[43559]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 78 #1	2018 46 G	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 16.09	51.64	94.25	6861	477	488	0.0008	334

Tom Henderson	[43560]		+2 panels	x0.10

4.6	0.54 span

Lemur-2 79 #1	2018 46 H	2018 Jul 15	3U Cube	0.34x0.10	2018 Jul 20.14	51.64	94.25	6861	476	488	0.0008	336

Yuasa	[43561]		+2 panels	x0.10

4.6	0.54 span

#	Cygnus OA-9 rendezvoused and was grappled 2018 May 24.393 by the stations robotic arm. It was berthed to ISS 2018 May 24.509 on the Unity nadir port.

On board is 3268 kg of resupplies for the station including 9 cubesats for deployment from the ISS.

Mounted on the Cygnus is a 82 kg NanoRacks deployer with 6 Cubesats, which will be deployed in July after Cygnus has departed ISS.

Unberthed 2018 Jul 15.508 and released 2018 Jul 15.526 from the stations robotic arm.

Cygnus will raise its orbit to around 500 km before deploying the 6 Cubesats. It will stay in orbit till 2018 Jul 30 for more experiments.

Cygnus has some 3000 kg of trash and no longer needed hardware aboard for disposal by burning up in the atmosphere.

#1	From Spire Globe for surveying Earth’s atmosphere and tracking maritime traffic.

#2	From Aerospace Corp. to demonstrate new star-tracker imaging sensors, a variety of nanotechnology payloads, advanced solar cells, and an electric propulsion system on one of the two satellites.

Grace-FO 1  *1	2018 47 A	2018 May 22.825	Trapzodial box 1.942 width	2018 Mar 22.89	88.99	94.48	6872	483	504	0.002	274

[Falcon-9b4]  #	[43476]		487	3.123 long

(F9-055, B1043-2)	VDB-SLC4E			0.720 high

Grace-FO 2  *1	2018 47 B	2018 May 22.825	Trapzodial box	1.942 width	2018 Mar 22.89	88.99	94.48	6872	483	504	0.002	297

[43477]		487	3.123 long

0.720 high

Iridium 161   *2	2018 47 C	2018 May 22.825	Trapzodial box	3.1 x 2.4	2018 May 22.95	86.71	96.70	6979	493	707	0.015	333

[43478]		+2 panels	x1.5	2018 May 25.89	86.71	97.08	6997	524	714	0.014	323

860	9.4 span	2018 May 26.44	86.72	97.95	7039	605	715	0.008	322

2018 May 27.46	86.71	98.58	7069	663	718	0.004	322

2018 May 27.87	86.71	99.07	7093	711	717	0.0004	328

2018 May 28.49	86.71	99.17	7097	717	720	0.0002	76

2018 Jun 3.42	86.45	99.77	7126	746	748	0.0002	95

Iridium 152   *2	2018 47 D	2018 May 22.825	Trapzodial box	3.1 x 2.4	2018 May 22.94	86.69	96.82	6985	498	714	0.016	336

[43479]		+2 panels	x1.5	2018 May 25.76	86.71	97.33	7010	548	714	0.012	324

860	9.4 span	2018 May 25.90	86.71	97.58	7022	571	715	0.010	323

2018 May 26.51	86.71	97.95	7039	605	716	0.008	321

2018 May 27.32	86.71	98.88	7083	687	722	0.002	238

2018 May 27.95	86.71	99.08	7094	712	718	0.0004	327

2018 May 28.50	86.71	99.17	7098	718	720	0.0002	96

2018 Jun 1.56	86.49	99.18	7098	718	721	0.0002	100

2018 Jun 13.43	86.42	100.07	7140	759	763	0.0003	120

2018 Jun 14.48	86.40	100.40	7156	775	779	0.0003	88

Iridium 147   *2	2018 47 E	2018 May 22.825	Trapzodial box	3.1 x 2.4	2018 May 22.95	86.71	96.72	6980	496	707	0.015	333

[43480]		+2 panels	x1.5	2018 May 24.68	86.72	96.95	6991	504	722	0.016	333

860	9.4 span	2018 May 25.50	86.71	97.92	7038	602	716	0.008	324

2018 May 26.45	86.71	98.82	7080	690	713	0.002	290

2018 May 26.87	86.71	99.02	7090	705	718	0.0009	313

2018 May 27.42	86.72	99.18	7098	709	729	0.001	141

2018 Jun 1.17	86.43	99.20	7099	719	722	0.0002	85

2018 Jun 8.13	86.43	99.53	7115	735	737	0.0002	90

2018 Jun 8.83	86.41	100.08	7140	760	763	0.0002	120

2018 Jun 10.23	86.40	100.40	7156	776	779	0.0002	89

Iridium 110   *2	2018 47 F	2018 May 22.825	Trapzodial box	3.1 x 2.4	2018 May 22.95	86.71	96.68	6979	481	719	0.017	335

[43481]		+2 panels	x1.5	2018 May 25.49	86.71	97.75	7030	584	718	0.010	326

860	9.4 span	2018 May 25.83	86.71	98.00	7042	608	718	0.008	323

2018 May 26.45	86.71	98.25	7053	630	719	0.006	322

2018 May 26.79	86.71	98.83	7081	683	721	0.003	330

2018 May 26.86	86.71	98.93	7087	696	720	0.002	321

2018 May 27.41	86.71	99.17	7097	716	720	0.0003	342

2018 May 27.82	86.71	99.22	7100	720	723	0.0002	151

2018 Jun 1.24	86.43	99.22	7100	720	723	0.0002	125

2018 Jun 7.17	86.42	99.48	7113	721	747	0.002	142

2018 Jun 8.13	86.41	100.13	7143	762	767	0.0003	131

2018 Jun 8.56	86.40	100.37	7155	774	778	0.0003	135

2018 Jun 10.93	86.40	100.40	7156	775	779	0.0003	105

Iridium 162   *2	2018 47 G	2018 May 22.825	Trapzodial box	3.1 x 2.4	2018 May 22.95	86.71	96.75	6981	486	719	0.017	336

[43482]		+2 panels	x1.5	2018 May 26.77	86.71	97.12	6999	525	716	0.014	320

860	9.4 span	2018 May 27.52	86.71	97.98	7041	606	718	0.008	317

2018 May 28.54	86.72	99.02	7090	705	718	0.0009	309

2018 May 28.82	86.71	99.12	7095	712	720	0.0006	320

2018 May 29.50	86.71	99.22	7100	720	723	0.0002	80

2018 May 31.58	86.54	99.58	7117	738	740	0.0002	94

2018 Jun 1.55	86.45	99.77	7126	746	748	0.0002	99

D	Falcon 9 fragment	2018 47 H	2018 May 22.825 			2018 May 24.25	89.04	94.60	6858	479	500	0.001	250

[43483]	125 days			2018 Sep 21.32	89.03	91.03	6704	309	341	0.002	147

2018 Sep 24

Falcon-9 2nd stage	2018 47	2018 May 22.825	Cylinder	13 long	De-orbited after satellite release. It decayed over the Pacific Ocean.

[NNA]		3900	3.66 dia

%1	GRACE-FO (Gravity Recovery and Climate Experiment Follow On) to measure the tug of Earth’s gravity around the world. The satellites follow each other at 220 km and the distance between them is measured with high precession of a few microns.

%2	Sixth Iridium-Next launch with 3 satellites going to plane 1 and two satellites as spares.

Gaofen-6  *1	2018 48 A	2018 Jun 2.176	Box +2 panels		2018 Jun 2.30	98.05	97.53	7019	635	646	0.0008	270

[CZ-2D] (Y20)	[43484]		1064		2018 Jun 9.20	98.05	97.50	7017	631	646	0.001	258

JIUQ-LC2				2018 Jun 26.61	98.05	97.53	7019	634	647	0.0009	190

Luojia 1   *2	2018 48 B	2018 Jun 2.176	6U Cube	0.34x0.20	2018 Jun 2.31	98.05	97.53	7019	634	647	0.0009	282

[43485]			x0.10

CZ-2D 2nd stage	2018 48 C	2018 Jun 2.176	Cylinder	10.9 long	2018 Jun 2.37	98.05	97.53	7019	633	648	0.001	279

[43486]		6050	3.35 dia

CZ-2D fragments	2018 48 D	[43487]			2018 Jun 2.37	98.05	97.53	7019	632	648	0.001	289

2018 48 E	[43490]			2018 Jun 4.19	98.18	97.62	7023	621	668	0.003	243

2018 48 F	[44619]			2019 Oct 2.49	98.15	97.28	7007	615	642	0.002	247

*1	Chinese earth observation satellite.

*2	Earth observation satellite (prototype) from Wuhan University.

SES 12  *	2018 49 A	2018 Jun 4.198	Box +2 panels		2018 Jun 3.96	25.94	1115.12	35621	210	58275	0.815	168

[Falcon 9b4]  #	[43488]	> million years	5383 full		2018 Jun 3.97	25.98	1118.27	35688	249	58370	0.814	168

(F9-056, B1040-2)	CC-LC40				2018 Jun 5.57	25.86	1125.97	65852	423	58523	0.810	168

2018 Jun 11.68	24.76	1147.80	36314	777	59093	0.803	170

2018 Jun 26.85	19.96	1263.18	38708	2136	62523	0.780	172

2018 Jul 5.67	17.29	1352.03	40503	3323	64925	0.760	173

2018 Jul 10.83	15.78	1395.68	41370	4061	65922	0.748	174

2018 Jul 11.79	15.54	1403.67	41528	4194	66105	0.745	174

2018 Jul 12.64	15.10	1436.02	42163	5243	66326	0.724	174

2018 Jul 17.67	14.12	1443.95	42318	5058	66822	0.730	174

2018 Sep 5.77	5.61	1529.92	43982	14828	60378	0.518	175

2018 Oct 15.69	2.31	1483.82	43480	24527	49676	0.289	175

2018 Nov 6.72	1.29	1458.17	42596	28504	43930	0.181	176

2018 Nov 27.47	0.74	1445.63	42351	31604	40341	0.103	178

2018 Dec 6.48	0.59	1438.23	42207	32537	39119	0.078	178

2018 Dec 18.48	0.29	1432.68	42098	34856	36581	0.020	169

2018 Dec 26.42	0.05	1436.18	42167	35782	35794	0.0001	21

2018 Dec 28.42	0.05	1436.07	42164	35778	35793	0.0002	49

Falcon-9 2nd stage	2018 49	2018 Jun 4.198	Cylinder	13 long	2018 Jun 3.96	25.97	1123.68	35804	255	58595	0.815	168

[43489]		3900	3.66 dia

*	Communication satellite to replace NSS 6. It used xenon propellant for its electric thrusters to get to the geosynchronous orbit at 95 degrees east.

#	The 1st stage is a refurbished Block 4 stage that put the USAF X-37B spaceplane in orbit in September 2017.

FengYun 2H  %	2018 50 A	2018 Jun 5.549	Barrel		2018 Jun 5.74	24.56	633.75	24441	218	35905	0.730	181

[CZ-3A]	[43491]	> million years			2018 Jun 12.81	2.33	1436.02	42163	35772	35797	0.0003	235

XI-LC2				2018 Jul 18.80	2.26	1442.43	42289	35900	35920	0.0002	225

2018 Jul 28.91	2.24	1435.97	42162	35766	35802	0.0004	242

2018 Jul 29.49	2.23	1436.00	42163	35765	35803	0.0004	247

2018 Jul 31.85	2.23	1436.02	42163	35767	35803	0.0004	248

2018 Aug 24.12	2.18	1436.07	42164	35769	35803	0.0004	253

2018 Sep 7.62	2.15	1436.08	42165	35768	35804	0.0004	262

CZ-4C 3rd stage	2018 50 B	2018 Jun 5.549	Cylinder	4.9 long	2018 Jun 5.74	24.56	643.95	24702	287	36360	0.730	182

[43492]		1760	2.9 dia

FengYun 2H	2018 50 C	2018 Jun 5.549			2018 Jun 13.80	2.39	1439.18	42225	35482	36211	0.010	58

Apogee Kick Motor	[43497]	> million years

Fragment	2018 50 D	[43645]	1 piece, in orbit

%	Chinese geostationary weather satellite. It is the final of the spin-stabalized (100 rpm) FengYun 2 series satellites.

D	Soyuz MS-09 *	2018 51 A	2018 Jun 6.467	Cyl+beehive+	7.48 long	2018 Jun 6.52	51.63	88.87	6597	189	247	0.004	98

3M [Soyuz FG]	[43493]	196.743 days	+spheroid+	2.72 maxdia	2018 Jun 6.85	51.64	90.00	6653	272	276	0.0003	134

R		BAI-LC1/5	2018 Dec 20.210	2 panels	2.2 dia	2018 Jun 8.45	51.64	92.65	6783	402	407	0.0004	165

7167	10.6 span

D	Soyuz-FG 3rd stage	2018 51 B	2018 Jun 6.467	Cylinder	6.74 long	2018 Jun 6.77	51.64	88.63	6585	197	216	0.001	89

(Blok I)	[43494]	5 day	2410	2.66 dia	2018 Jun 11.12	51.61	87.52	6530	150	152	0.0002	151

2018 Jun 11

*	Soyuz MS-09 with 3 crewmembers (Prokopyev, Gerst and Auñun-Chancellor} docked 2018 Jun 8 with ISS (Rassvet port).

Undocked 2018 Dec 20.070 and landed in Kazachstan.

IGS Radar 6 $	2018 52 A	2018 Jun 12.180			No TLE’s issued. Orbits from amateur observations.

[H-IIA]	[43495]				2020 Sep 5.00	97.33	94.35	6866	483	492	0.0007	52

(F39)	TAN-LC1

H-IIA 2nd stage	2018 52 B	2018 Jun 12.180	Cylinder		No TLE’s issued. Orbits from amateur observations.

[43496]

Fragment	2018 52 C	1 piece, in orbit			For orbital information see extra pages at end of the year

$	Japanese Radar reconnaissance satellite

Cosmos 2527  *	2018 53 A	2018 Jun 16.908	Cyl + box		2018 Jun 17.10	64.83	675.97	25514	19116	19155	0.0008	232

[Soyuz 2-1b]	[43508]	1 million years	+ 2 panels		2018 Jun 17.18	64.77	676.90	25538	19124	19194	0.001	193

PLE-LC43/4		1400		2018 Jun 18.57	64.83	676.03	25516	19119	19155	0.0007	230

2018 Jun 23.21	64.82	676.05	25516	19121	19154	0.0006	232

Fregat upperstage	2018 53 B	2018 Jun 16.908	Torus+spheres	1.85 high	2018 Jun 17.15	64.80	683.55	25705	19152	19500	0.007	65

[43509]		930	3.35 dia	2018 Jun 17.17	64.80	683.60	25706	19153	19502	0.007	65

*	Russian Glonass M navigation satellite.

XJS A *	2018 54 A	2018 Jun 27.146			2018 Jun 27.40	34.99	94.08	6852	464	483	0.001	260

[CZ-2C]	[43518]				2018 Jun 27.47	35.01	94.22	6859	476	484	0.0006	295

XI-LC3				2018 Jun 29.49	35.00	94.28	6862	475	493	0.001	317

2018 Jun 30.56	35.01	94.28	6863	479	489	0.0007	347

2018 Jul 3.99	35.00	94.23	6860	477	486	0.0006	300

XJS B *	2018 54 B	2018 Jun 27.146			2018 Jun 27.40	35.00	94.22	6859	476	485	0.0007	263

[43519]				2018 Jun 27.47	35.00	94.25	6860	477	486	0.0007	281

Fragment	2018 54 C	[43520]			2018 Jun 27.47	35.00	94.18	6858	472	486	0.001	301

CZ-2C 2nd stage	2018 54 D	2018 Jun 27.146	Cylinder	7.58 long	2018 Jun 27.54	35.16	95.33	6913	476	593	0.008	242

[43521]		3300	3.35 dia

*	Chinese satellites to test inter-satellite network and Earth observation technologies.

D	Dragon CRS-15 *	2018 55 A	2018 Jun 29.405	Blunt cone	4.4 high	2018 Jun 29.48	51.64	90.65	6685	227	386	0.012	52

[Falcon 9b4]  #	[43522]	35.523 days	+ cylinder	3.66 dia	2018 Jul 1.24	51.65	91.80	6741	359	366	0.0005	302

(F9-057, B1045-2)	CC-LC40	2018 Aug 3.928	+ 2 panels	2.8 high 	2018 Jul 1.50	51.64	92.43	6772	391	396	0.0004	248

~ 8200 full	16.5 span	2018 Jun 2.26	51.64	92.65	6783	402	407	0.0003	253

2647 cargo		2018 Aug 2.64	51.64	92.67	6784	402	409	0.0005	19

D	Fragments	2018 55 B, C  2 pieces, both have decayed		For orbital information see extra pages at end of year

Solar panel covers

*	Dragon CRS-15 (C110) rendezvoused with ISS and was 2018 Jul 2.454 grappled by the stations robotic arm and berthed 2018 Jul 2.57 to Harmony’s nadir port.

Unbearthed and released 2018 Aug 3.526 from the robotic arm. It soft landed in the Pacific Ocean southwest of Los Angeles.

#	Last flight of a Falcon 9 Block 4. It was expended in the Atlantic ocean without girds and landing legs.

PakTES 1A   #2	2018 56 A	2018 Jul 9.164			2018 Jul 9.36	98.05	96.78	5983	588	622	0.002	277

[CZ-2C]	[43529]				2018 Jul 9.75	98.05	96.85	6986	588	627	0.003	285

JIUQ-LC2

PRSS 1   #1	2018 56 B	2018 Jul 9.164	Box +2 panels		2018 Jul 9.36	98.04	96.82	6985	587	625	0.003	286

[43530]

CZ-2C 2nd stage	2018 56 D	2018 Jul 9.164	Cylinder	7.58 long	2018 Jul 9.35	98.05	93.18	6809	234	626	0.029	170

[43532]		3300	3.35 dia

Fragment	2018 56 C E-J 6 pieces, 3 have decayed		For orbital information see extra pages at end of year

#1	Pakistan Remote Sensing Satellite

#2	Experimental Pakistan/South Africa remote sensing satellite

Beidou 2-IGSO7  #	2018 57 A	2018 Jul 9.874			2018 Jul 10.12	55.11	630.95	24369	201	35779	0.730	175

[CZ-3A]	[43539]	> million years			2018 Jul 16.58	55.06	1435.88	42161	35691	35873	0.002	183

XI-LC2

D	CZ-3A 3rd stage 	2018 57 B	2018 Jul 9.874	Cylinder	12.38 long	2018 Jul 10.09	55.11	626.32	24249	248	35493	0.727	175

[43540]	513 days	2740	3.0 dia	2018 Jul 10.25	55.05	625.88	24238	227	35491	0.727	175

2019 Dec 4			2019 Dec 4.47	54.90	88.57	6582	75	333	0.020	271

#	Chinese navigation satellite

D 	Progress MS-09 *	2018 58 A	2018 Jul 9.911	Cyl+beehive+	7.5 long	2018 Jul 9.93	51.63	88.65	6587	192	224	0.002	89

[Soyuz-2.1A]	[43537]	199.790 days	+spheroid+	2.72 maxdia	2018 Jul 10.04	51.65	92.27	6764	367	404	0.003	281

BAI-LC31/6	2019 Jan 25.701	2 panels	2.3 dia	2018 Jul 10.41	51.64	92.65	6783	402	407	0.0004	289

7281		2019 Jan 14.46	51.64	92.70	6786	404	410	0.0005	307

D	Soyuz-2.1A 3rd stage	2018 58 B	2018 Jul 9.911	Cylinder	6.74 long	2018 Jul 9.93	51.65	88.50	6579	186	215	0.002	64

[43538]	3 days	2355	2.66 dia	2018 Jul 12.54	51.66	87.67	6537	154	163	0.0007	93

2018 Jul 12

*	Progress MS-09 docked 2018 Jul 10.063 with ISS (Pirs port) just 3h40m after launch on the first fast 2 orbit track. It delivered 2566 kg of cargo.

Telstar 19 Vantage *	2018 59 A	2018 Jul 22.243	Box +2 panels		2018 Jul 22.33	27.00	317.95	15431	243	17862	0.571	174

[Falcon-9b5] #	[43562]	> million years	7075		2018 Jul 25.24	26.92	404.53	18119	299	23181	0.631	178

(F9-058, B1047-1)	CC-LC40				2018 Jul 26.66	26.88	467.73	19960	314	26849	0.665	179

2018 Jul 28.42	26.82	632.37	24405	323	35730	0.725	180

2018 Jul 30.57	10.69	788.40	28270	8043	35740	0.490	181

2018 Jul 31.62	4.66	985.22	32798	17370	35649	0.276	181

2018 Aug 1.12	0.36	1387.47	41287	33953	35704	0.021	171

2018 Aug 2.61	0.04	1436.47	42172	35746	35841	0.001	260

2018 Aug 2.65	0.08	1433.90	42122	35700	35787	0.001	312

2018 Aug 13.58	0.07	1436.07	42164	35777	35794	0.0002	307

2018 Aug 18.39	0.06	1436.08	42165	35780	35792	0.0001	313

2018 Aug 26.25	0.05	1436.10	42165	35775	35798	0.0003	261

2018 Aug 30.24	0.04	1436.13	42165	35776	35798	0.0003	283

2018 Sep 2.23	0.04	1436.08	42165	35776	35796	0.0002	297

2018 Sep 7.21	0.02	1436.12	42165	35777	35796	0.0002	338

Falcon 9 2nd stage	2018 59 B	2018 Jul 22.243	Cylinder	13 long	2018 Jul 22.33	27.00	317.87	15429	241	15429	0.571	174

[43563]		3900	3.66 dia

*	Canadian telecommunication satellite to be located over 63° W.

#	The first stage made a soft landing on the drone ship OCISLY in the Atlantic Ocean.

Galileo FM-25 ^	2018 60 A	2018 Jul 25.476	Box +2 panels	2.5 x 1.2	2018 Jul 25.84	56.33	831.48	29291	22896	22928	0.0006	328

Anna, Galileosat 2C1	[43564]	1 million years	716	x 1.1	2018 Jul 27.02	56.31	830.93	29278	22897	22902	0.0001	339

[Ariane 5 ES]	KOU-ELA3			14.67 span

Galileo FM-26	2018 60 B	2018 Jul 25.476	Box +2 panels	2.5 x 1.2	2018 Jul 25.84	56.31	831.38	29289	22902	22918	0.0003	343

Ellen,Galileosat 2C2	[43565]	1 million years	738	x 1.1	2018 Jul 26.44	56.31	830.93	29278	22897	22902	0.00008	126

14.67 span

Galileo FM-23	2018 60 C	2018 Jul 25.476	Box +2 panels	2.5 x 1.2	2018 Jul 25.85	56.23	832.15	29307	22908	22948	0.0007	317

Tara, Galileosat 2C9	[43566]	1 million years	716	x 1.1	2018 Jul 26.44	56.31	831.78	29298	22900	22938	0.0007	219

14.67 span

Galileo FM-24	2018 60 D	2018 Jul 25.476	Box +2 panels	2.5 x 1.2	2018 Jul 25.85	56.31	831.45	29290	22898	22925	0.0004	228

Samuel,Galileosat 2C0[43567]	1 million years	716	x 1.1

14.67 span

Ariane 2nd stage *	2018 60 E	2018 Jul 25.476	Drum + spheres	3.35 long	2018 Jul 25.85	56.30	831.97	29302	22907	22940	0.0006	231

(EPS + dispenser)	[43568]		1275 + 418	3.94 dia	2018 Jul 27.60	56.24	831.27	29301	22901	22914	0.0002	227

^	European GPS satellites in plane B of the constellation.

*	Last flight of the EPS upperstage.

Iridium 160 *	2018 61 A	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.68	97.03	6995	609	623	0.001	239

[Falcon 9b5] #	[43569]		+2 panels	x1.5	2018 Jul 31.53	86.58	98.17	7050	664	679	0.001	242

(F9-059, B1048-1)	VDB-SLC4E		860	9.4 span	2018 Aug 1.71	86.55	98.72	7076	695	700	0.0003	4

2018 Aug 3.13	86.50	99.08	7093	714	716	0.0001	39

2018 Aug 12.32	86.43	100.03	7139	758	762	0.0002	92

2018 Aug 13.85	86.40	100.40	7156	775	779	0.0003	99

Iridium 166 *	2018 61 B	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.02	6995	609	623	0.001	251

[43570]		+2 panels	x1.5	2018 Aug 5.50	86.50	99.08	7093	713	716	0.0002	75

860	9.4 span	2018 Aug 22.88	86.40	100.40	7156	776	778	0.0002	86

Iridium 158 *	2018 61 C	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.02	6995	609	623	0.001	254

[43571]		+2 panels	x1.5	2018 Jul 31.57	86.50	99.07	7093	713	715	0.0002	62

860	9.4 span	2018 Aug 10.50	86.40	100.37	7155	775	777	0.0001	79

2018 Aug 11.54	86.40	100.40	7156	776	778	0.0002	93

Iridium 165 *	2018 61 D	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.68	97.02	6994	609	623	0.001	254

[43572]		+2 panels	x1.5	2018 Aug 5.51	86.50	99.08	7093	713	716	0.0002	75

860	9.4 span	2018 Aug 16.46	86.43	100.03	7138	758	761	0.0002	76

2018 Aug 17.85	86.40	100.37	7155	774	778	0.0002	70

2018 Aug 18.27	86.40	100.40	7156	775	779	0.0002	90

Iridium 155 *	2018 61 E	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.02	6994	608	623	0.001	261

[43573]		+2 panels	x1.5	2018 Jul 31.59	86.50	99.08	7093	713	716	0.0002	96

860	9.4 span	2018 Aug 6.44	86.46	99.62	7118	738	742	0.0003	176

2018 Aug 7.49	86.41	100.13	7143	763	767	0.0003	93

2018 Aug 7.90	86.40	100.38	7155	774	779	0.0003	103

2018 Aug 10.48	86.40	100.40	7155	775	779	0.0003	66

Iridium 154 *	2018 61 F	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.68	97.00	6994	608	623	0.001	252

[43574]		+2 panels	x1.5	2018 Aug 5.05	86.58	98.10	7046	660	675	0.001	213

860	9.4 span	2018 Aug 5.46	86.58	98.28	7055	675	678	0.0002	64

2018 Aug 6.49	86.50	99.07	7092	713	715	0.0002	111

2018 Aug 22.40	86.43	99.97	7136	755	759	0.0003	112

2018 Aug 22.96	86.37	100.33	7153	772	777	0.0004	118

2018 Aug 23.79	86.40	100.37	7155	774	778	0.0003	109

2018 Aug 24.49	86.40	100.40	7156	775	779	0.0003	87

Iridium 163 *	2018 61 G	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.00	6994	607	623	0.001	252

[43575]		+2 panels	x1.5	2018 Jul 31.47	86.58	98.32	7056	677	679	0.0001	19

860	9.4 span	2018 Aug 1.63	86.52	99.13	7096	707	728	0.002	37

2018 Aug 15.48	86.44	99.78	7126	747	749	0.0001	225

2018 Aug 15.54	86.43	99.92	7133	743	766	0.002	173

2018 Aug 16.52	86.41	100.25	7149	769	771	0.0002	93

2018 Aug 17.35	86.40	100.37	7155	775	777	0.0002	108

2018 Aug 18.33	86.40	100.40	7156	776	779	0.0002	117

Iridium 156 *	2018 61 H	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.00	6993	607	623	0.001	254

[43576]		+2 panels	x1.5	2018 Jul 31.56	86.50	99.08	7093	714	715	0.0001	129

860	9.4 span	2018 Aug 10.42	86.40	100.37	7155	775	777	0.0002	120

2018 Aug 10.70	86.40	100.40	7156	776	778	0.0002	71

Iridium 164 *	2018 61 J	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.00	6993	607	623	0.001	259

[43577]		+2 panels	x1.5	2018 Aug 6.53	86.57	98.23	7053	670	678	0.0005	165

860	9.4 span	2018 Aug 7.42	86.58	98.35	7058	679	691	0.0001	89

2018 Aug 8.52	86.51	99.07	7092	713	715	0.0001	93

2018 Aug 24.50	86.43	100.03	7139	758	762	0.0003	118

2018 Aug 25.19	86.40	100.37	7155	774	778	0.0003	122

2018 Aug 26.38	86.40	100.40	7156	775	779	0.0002	86

Iridium 159 *	2018 61 K	2018 Jul 25.486	Trapzodial box	3.1 x 2.4	2018 Jul 25.80	86.67	97.00	6993	607	623	0.001	260

[43578]		+2 panels	x1.5	2018 Jul 31.60	86.65	98.02	7042	650	677	0.002	198

860	9.4 span	2018 Aug 1.64	86.60	98.33	7057	673	684	0.0008	355

2018 Aug 2.59	86.55	99.32	7104	713	738	0.002	4

2018 Aug 5.33	86.50	99.08	7093	714	715	0.0001	61

2018 Aug 15.40	86.41	100.18	7146	767	767	0	54

2018 Aug 16.51	86.40	100.38	7155	775	777	0.0001	98

2018 Aug 17.42	86.40	100.40	7156	775	779	0.0003	88

D	Falcon 9 2nd stage	2018 61	2018 Jul 25.486	Cylinder	13 long	De-orbit burn after satellite release and decayed over Pacific Ocean.

[NNA]	~0.06 day	3900	3.66 dia

2018 Jul 25.548

*	The 7th launch of Iridium Next communication satellites for telephone and messaging services. They will raise their orbit and go to plane 5 of the constellation.

#	The first stage soft landed on the drone ship “Just Read The Instructions” in the Pacific Ocean.

Beidou-3  M9  &	2018 62 A	2018 Jul 29.075	Box +2 panels		2018 Jul 29.42	54.99	787.27	28243	21533	22196	0.012	177

[CZ-3B/YZ1]	[43581]	1 milion years			2018 Jul 30.89	54.98	780.95	28092	21531	21896	0.006	182

XI-LC2

Beidou-3  M10  &	2018 62 B	2018 Jul 29.075	Box +2 panels		2018 Jul 29.42	54.99	787.05	28238	21521	22197	0.012	177

[43582]	1 milion years			2018 Jul 29.92	54.99	786.93	28235	21520	22193	0.012	177

D	CZ-3B 3rd stage 	2018 62 C	2018 Jul 29.075	Cylinder	12.38 long	2018 Jul 29.39	54.97	328.08	15758	203	18555	0.582	171

[43583]	356 days	2740	3.0 dia	2019 Jul 19.95	54.64	89.65	6636	86	428	0.026	335

2019 Jul 20

Yuanzheng-1	2018 62 D	2018 Jul 29.075			2018 Jul 29.42	55.05	805.65	28681	22227	22378	0.003	9

Upperstage	[43584]

&	Chinese navigation satellite.

Gaofen 11	2018 63 A	2018 Jul 31.125	Cylinder	4.92 long	2018 Jul 31.25	97.42	94.00	6849	248	693	0.032	172

[CZ-4B]	[43585]		1700	2.9 dia

WUZ-LC9

D	CZ-4B 3rd stage	2018 63 B	2018 Jul 31.125	Cylinder	4.92 long	2018 Jul 31.24	97.37	91.43	6723	219	470	0.019	144

[43586]	96 days	1700	2.9 dia	2018 Nov 4.63	97.33	87.03	6506	119	136	0.001	101

2018 Nov 4

* Chinese earth-imaging satellite.

Merah Putih  *	2018 64 A	2018 Aug 7.304	Box + 2 panels		2018 Aug 7.29	27.06	512.93	21226	193	29502	0.690	177

(Telkom 4)	[43587]	> million years	5800		2018 Aug 8.83	27.36	597.08	23489	511	33709	0.707	179

[Falcon 9b5]  #	CC-LC40				2018 Aug 10.12	27.13	672.93	23902	206	34842	0.725	179

(F9-060, B1046-2)					2018 Aug 10.74	27.06	635.38	24482	237	35970	0.730	179

2018 Aug 11.75	13.52	738.70	27069	5604	35777	0.557	180

2018 Aug 12.68	3.69	1046.07	34135	19740	35773	0.235	179

2018 Aug 14.55	0.10	1434.82	42140	35739	35784	0.0005	320

2018 Aug 14.92	0.09	1434.07	42125	35738	35755	0.0002	339

2018 Aug 22.70	0.07	1436.08	42164	35776	35795	0.0002	232

2018 Aug 24.78	0.07	1436.10	42165	35779	35794	0.0002	247

2018 Aug 26.77	0.07	1436.05	42164	35779	35792	0.0002	246

2018 Sep 2.75	0.06	1436.10	42165	35779	35793	0.0002	256

Falcon 9 2nd stage	2018 64 B	2018 Aug 7.304	Cylinder	13 long	2018 Aug 7.29	27.04	513.15	21232	181	29527	0.691	177

[43588]		3900	3.66 dia

*	Indonesian communication satellite to replace Telkom 1 which failed last year after shedding debris. The satellite is named after the red and white in the

Indonesian flag. It will be positioned over the equator at 108° E.

#	The 1st stage was used to launch the Bangabandhu satellite 2018 May 11 and then landed on the OCISLY drone ship. It soft landed on OCISLY again.

Parker Solar Probe *	2018 65 A	2018 Aug 12.313	Hexagonal	3 high	In heliocentric orbit; see footnote below for predicted orbits.

[Delta 4 Heavy]	[43592]	Heliocentric	cylinder	1 dia	See footnote: In red the actual date and time.

(#10)	CC-LC37B		+ sunshield	2.3 dia

+ 2 panels	~ 7 span

685 full

Delta 4 Heavy 	2018 65 B	2018 Aug 12.313	Cylinder	13.7 long	In heliocentric orbit

2nd stage	[43593]	Heliocentric	3490 dry	5 dia

(Delta Cryogenic

Second Stage – DCSS)

Star 48BV upperstage	2018 65 C	2018 Aug 12.313	Sphere + nozzle	In heliocentric orbit

[43594]	Heliocentric

*	The satellite is named for Eugene Parker, who in 1958 predicted correctly the existence of the solar wind.

Using 7 Venus fly-by’s the probe will fly closer and closer to the sun. In 2024 it will reach a perihelion of 6.16 million km.

The perihelion of the orbit will decrease from 1.02 to 0.73 Astronomical Unit; period 169 to 88 days with 11 days closer than 0.25 AU to the sun.

After the first Venus fly-by (2018 Oct 3.365 at ~ 2500 km), the probe will be in an elliptical orbit with a period of 150 days (two-thirds the period of Venus), making three orbits while Venus makes two. On the second fly-by (2019 Dec 21), the period shortens to 130 days. After less than two orbits (only 198 days later on 2020 Jul 6) it encounters Venus a third time at a point earlier in the orbit of Venus. This encounter shortens its period to half of that of Venus, or about 112.5 days. After two orbits it meets Venus a fourth time (2021 Feb 16) at about the same place, shortening its period to about 102 days. After 237 days (2021 Oct 11)it meets Venus for the fifth time and its period is shortened to about 96 days, three-sevenths that of Venus. It then makes seven orbits while Venus makes three. The sixth encounter (2023 Aug 16), almost two years after the fifth, brings its period down to 92 days, two-fifths that of Venus. After five more orbits (two orbits of Venus) it meets Venus for the seventh and last time (2024 Nov 2), decreasing its period to 88 or 89 days and allowing it to approach close to the Sun.

First close approach to the sun on 2024 Dec 19; followed by 4 more on 2025 Mar 18, Jun 14, Sep 10 and Dec 7.

Aeolus  #	2018 66 A	2018 Aug 22.889	Box + Cyl	4.00x4.35	2018 Aug 22.96	96.73	90.82	6693	314	316	0.0001	44

[Vega] (VV12)	[43600]		+ 2 panels	x1.60	2018 Aug 22.97	96.73	90.80	6692	314	314	0	312

KOU-ZLV		1357 full		2018 Aug 24.22	96.73	90.85	6695	315	318	0.0002	295

1091 dry

#	European satellite to measure aerosols and clouds

Vega AVUM upperstage de-orbited after satellite release.

Beidou 3 M11	2018 67 A	2018 Aug 24.995			2018 Aug 25.32	55.01	787.32	28244	21539	22193	0.012	177

[CZ-3B/YZ1]	[43602]

XI-LC2

Beidou 3 M12	2018 67 B	2018 Aug 24.995			2018 Aug 25.31	55.01	787.17	28241	21532	22193	0.012	177

[43603]				2018 Sep 1.27	55.02	773.73	27918	21532	21546	0.0003	271

D	CZ-3B 3rd stage	2018 67 C	2018 Aug 24.995	Cylinder	12.38 long	2018 Aug 25.36	55.02	329.07	15789	192	18630	0.584	171

[43604]	314 days	2740	3.0 dia 	2019 Jul 4.81	54.76	91.10	6707	104	553	0.033	321

2019 Jul 4

Yuangzheng-1	2018 67 D	2018 Aug 24.995			2018 Aug 28.51	54.74	805.37	28674	22194	22397	0.004	357

Upperstage	[43605]

$	Chinese navigation satellites.

Haiyang 1C  *	2018 68 A	2018 Sep 7.135			2018 Sep 7.20	98.60	100.40	7156	770	786	0.001	264

[CZ-2C]	[43609]		442		2018 Sep 9.00	98.60	100.40	7156	769	786	0.001	252

WUZ-LC9

CZ-2C 2nd stage	2018 68 B	2018 Sep 7.135			2018 Sep 7.27	98.60	99.03	7091	648	777	0.009	26

[43610]

*	Chinese marine observation satellite to monitor ocean pollution, measure sea temperatures and track ship movements. Haiyang is Chinese for ocean.

Telstar 18 Vantage *	2018 69 A	2018 Sep 10.281	Box +2 panels		2018 Sep 10.28	26.93	321.83	15557	259	18098	0.573	173

[Falcon-9b5]  #	[43611]	> million years	7060		2018 Sep 12.32	26.94	359.93	16761	291	20474	0.602	176

(F9-061, B1049-1)	CC-LC40				2018 Sep 12.97	26.82	407.33	18203	343	23305	0.631	177

2018 Sep 14.88	26.73	546.07	22131	324	31180	0.697	179

2018 Sep 16.41	26.75	632.55	24069	319	35743	0.726	180

2018 Sep 16.98	15.38	714.62	26478	4465	35743	0.591	180

2018 Sep 18.58	7.34	874.63	30296	12082	35752	0.391	180

2018 Sep 19.31	3.36	1069.95	34653	20808	35740	0.215	180

2018 Sep 20.93	0.35	1389.37	41246	34007	35726	0.021	176

2018 Sep 21.94	0.08	1432.10	42087	35704	35712	0.0001	121

2018 Sep 24.71	0.08	1434.43	42132	35712	35795	0.001	263

2018 Sep 26.70	0.07	1436.07	42164	35778	35793	0.0002	216

2018 Sep 30.74	0.06	1436.08	42165	35779	35793	0.0002	219

Falcon 9 2nd stage	2018 69 B	2018 Sep 10.281	Cylinder	13 long	2018 Sep 10.28	26.95	321.23	15538	258	18060	0.572	174

[43612]		3900	3.66 dia

*	Canadian telecommunication satellite to be located over 138° E. Aka Apstar 5C for service to Indonesia (57.5% of its capacity).

#	The 1st stage soft landed on the OCISLY drone ship in the Atlantic Ocean some 640 km east of Cape Carnaveral.

ICESat-2  *1	2018 70 A	2018 Sep 15.543	Box + panel	3.8 high	2018 Sep 15.60	93.02	93.82	6840	455	468	0.0009	307

[Delta 2 7420-10C]	[43613]		1514	2.5 x 1.9	2018 Sep 16.95	92.01	93.82	6840	459	464	0.0004	100

VDB-SLC2W

SurfSat *6	2018 70 B	2018 Sep 15.543	2U Cube	0.20x0.10	2018 Sep 15.66	93.04	93.72	6835	443	469	0.002	302

[43614]			x0.10

DAVE (CP-7)*5	2018 70 C	2018 Sep 15.543	1U Cube	0.10 side	2018 Sep 15.66	99.01	93.73	6836	449	465	0.001	281

[43615]		1

ELFIN-STAR *4	2018 70 D	2018 Sep 15.543	3U Cube	0.34x0.10	2018 Sep 15.66	93.03	93.72	6835	447	466	0.001	291

(ELFIN*)	[43616]		4	x0.10

Elfin *3	2018 70 E	2018 Sep 15.543	3U Cube	0.34x0.10	2018 Sep 15.66	93.04	93.70	6834	443	468	0.002	296

[43617]		4	x0.10

D	Delta 2 2nd stage *2	2018 70	2018 Sep 15.543	Cylinder

[NNA]	0.090 day

2018 Sep 15.633

*1	Ice, Cloud and land Elevation Satellite to study the Cryosphere (frozen part of the water on the Earth).

This the last launch using a Delta 2 rocket. Since 1989 154 Delta 2’s have been launched. It is the 381st launch of a Delta rocket since 1960.

*2	The 2nd stage was be de-orbited and decayed over the south Pacific Ocean west of Chili.

The four Cubesats were deployed from the 2nd stage after the 2nd restart and brief burn of the 2nd stage at 2018 Sep 15.596

*3	Electron Losses and Field Investigation from UCLA (University of California in Los Angeles to measure space weather.

*4	Electron Losses and Field Investigation with Spatio Temperal Ambiguity Resolution from University of California Los Angeles to measure the radiation environment in low Earth orbit.

*5	Damping and Vibration Experiment from California Polytechnic State University San Louis Obispo to test a mechanical damping technology in microgravity.

*6	From the University of Central Florida Orlando to measure static charging on spacecraft surfaces in orbit.

SSTL S1-4    #1	2018 71 A	2018 Sep 16.693	Trapzodial Box		2018 Sep 16.75	97.81	96.27	6958	569	591	0.002	250

[PSLV C42]	[43618]		430		2018 Sep 16.81	97.81	96.33	6961	574	591	0.001	250

SRI-LC1				2018 Sep 17.26	97.82	96.33	6961	576	590	0.001	250

2018 Sep 17.34	97.82	96.32	6961	574	591	0.001	245

NovaSAR 1    #2	2018 71 B	2018 Sep 16.693	Box + cylinder		2018 Sep 16.75	97.81	96.27	6958	568	591	0.002	246

[43619]		447		2018 Sep 18.54	97.82	96.33	6961	574	592	0.001	238

PSLV 4th stage	2018 71 C	2018 Sep 16.693	Cylinder		2018 Sep 17.00	97.71	96.58	6974	574	616	0.003	229

[43620]

#1	British high resolution Earth imaging satellite from Surrey Satellite Technology Ltd

#2	British synthetic aperture radar satellite to test a new and lighter radar imager. From British government, Surrey Satellite Technology Ltd and Airbus Defense and Space.

Beidou 3 M13	2018 72 A	2018 Sep 19	Box + 2 panels		2016 Sep 19.91	54.97	787.15	28240	21531	22192	0.012	177

[CZ-3B/YZ1]	[43622]				2018 Sep 22.19	54.97	787.20	28541	21533	22193	0.012	177

XI-LC2

Beidou 3 M14	2018 72 B	2018 Sep 19	Box + 2 panels		2018 Sep 19.92	54.97	787.52	28249	21545	22196	0.012	176

[43623]				2018 Sep 21.64	54.97	787.30	28244	21538	22193	0.012	177

CZ-3B 3rd stage	2018 67 C	2018 Sep 19	Cylinder	12.38 long	2018 Sep 19.73	54.96	326.42	15704	201	18450	0.581	171

[43624]		2740	3.0 dia

Yuangzheng-1	2018 67 D	2018 Sep 19			2018 Sep 19.86	54.81	810.95	28807	22192	22663	0.008	3

Upperstage	[43625]

$	Chinese navigation satellites.

D	Kounotori 7 $	2018 73 A	2018 Sep 22.745	Cylinder	10.06 long	2018 Sep 22.928	51.64	89.38	6622	186	301	0.009	314

(HTV 7)	[43630]	49.140 days	16500	4.27 dia	2018 Sep 23.44	51.64	90.30	6667	276	302	0.002	298

[H-IIB]	TAN-LC2	2018 Nov 10.885	10500 dry 		2018 Sep 26.13	51.64	91.95	6749	360	380	0.001	187

3397 cargo		2018 Sep 27.42	51.64	92.67	6784	402	408	0.0004	210

2018 Nov 6.61	51.64	92.67	6783	402	408	0.0005	18

2018 Nov 8.15	51.64	92.57	6779	396	404	0.0005	19

2018 Nov 9.37	51.64	92.20	6761	376	388	0.0009	270

2018 Nov 10.65	51.64	92.20	6761	377	388	0.0008	267

$	HTV 7 rendezvoused with ISS 2018 Sep 27 and was grappled by the station’s robotic arm 2018 Sep 27.482 and berthed 2017 Sep 28 to the nadir port

of the Harmony module. Unberthed 2018 Nov 7 and was released 2018 Nov 7.702 from the stations robotic arm.

After HTV 7 made the de-orbit burn the little HTV Space Return Capsule (HSRV) separated from the entrance door of the HTV, where it was mounted by the

ISS astronauts before the HTV was unbearthed. The capsule used a parachuted and soft-landed 2018 Nov 10.921 in the Pacific Ocean at the southwest coast

of Marcus (Minamitori) Island. On board were samples of protein crystals grown in microgravity of the ISS.

The capsule is a cylinder, ~0.50 dia, with a heatshield, 0.84 dia and a total height of 0.66 m; 180 kg empty.

The H-2B 2nd stage made a cold gas de-orbit manoeuvre at the end of the 1st orbit and decayed over the Pacific Ocean

Azerspace-2/  *1	2018 74 A	2018 Sep 25.943	Box + 2 panels		2018 Sep 26.01	5.96	631.63	24386	273	35742	0.727	178

Intelsat 38	[43632]	> million years	3500 full		2018 Sep 27.62	3.57	728.25	26813	4926	35944	0.578	173

[Ariane 5 ECA]	KOU-ELA3				2018 Sep 27.75	3.97	705.20	26244	4007	35725	0.604	179

(VA243)					2018 Sep 28.66	2.44	825.35	29146	9809	35727	0.445	179

2018 Oct 1.66	1.95	895.72	30780	13069	35735	0.368	179

2018 Oct 7.12	1.94	913.08	31177	13403	36194	0.366	179

2018 Oct 11.67	1.85	954.78	32119	14615	36866	0.346	183

2018 Oct 14.59	1.72	983.17	32753	15373	37375	0.336	180

2018 Oct 18.64	1.65	1021.92	33608	16325	38133	0.324	180

2018 Oct 22.73	1.55	1067.00	34589	17492	38929	0.310	183

2018 Oct 25.09	1.44	1091.07	35123	18141	39348	0.302	180

2018 Oct 29.73	1.28	1137.63	36099	19523	39918	0.282	187

2018 Nov 1.44	1.16	1163.05	36635	20576	39937	0.264	179

2018 Nov 5.53	1.06	1198.62	37378	21266	40733	0.260	181

2018 Nov 6.35	1.02	1207.27	37558	21820	40537	0.249	182

2018 Nov 7.64	0.99	1218.57	37792	22263	40562	0.242	183

2018 Nov 8.48	0.97	1224.63	37917	22271	40806	0.244	184

2018 Nov 9.34	0.99	1231.68	38062	23072	40295	0.226	182

2018 Nov 9.67	0.94	1224.50	37914	22955	40116	0.226	182

2018 Nov 12.88	0.84	1250.48	38448	24138	40001	0.206	182

2018 Nov 15.41	0.81	1272.41	38907	24536	40521	0.205	179

2018 Nov 19.75	0.65	1386.95	41197	28084	41553	0.163	165

2018 Nov 27.95	0.65	1367.43	40810	29895	38967	0.111	214

2018 Dec 5.62	0.25	1422.23	41893	33158	37871	0.056	182

2018 Dec 12.94	0.05	1434.00	42124	35711	35780	0.0008	57

2018 Dec 13.83	0.06	1436.12	42165	35780	35794	0.0002	8

2018 Dec 18.88	0.05	1436.08	42165	35778	35794	0.0002	29

Horizons 3e  *2	2018 74 B	2018 Sep 25.943	Box + 2 panels		2018 Sep 26.02	5.95	631.53	24383	275	35735	0.727	178

[43633]	> million years	6441 full		2018 Oct 1.36	0.83	893.75	30736	12969	35745	0.371	174

2018 Oct 2.81	0.11	1198.80	37382	26233	35773	0.128	117

2018 Oct 4.55	0.10	1386.43	41187	33833	35784	0.024	97

2018 Oct 8.57	0.09	1436.05	42164	35782	35788	0.00008	137

2018 Oct 9.49	0.09	1436.08	42165	35782	35790	0.0001	275

Ariane 5 2nd stage	2018 74 C	2018 Sep 25.943	Cylinder	5.84 long	2018 Sep 26.01	5.91	631.72	24388	284	35735	0.727	178

(ESC-A + VEB)	[43634]		5668	5.4 dia

Sylda upperpart	2018 74 D	2018 Sep 25.943	Barrel	6.4 high	2018 Sep 25.75	5.92	631.78	24390	269	35753	0.727	178

[43635]		~ 530

*1	Communication satellite for Azercosmos and Intelsat at 45° E. The Intelsat part replaces Intelsat 12.

*2	Communication satellite for Intelsat and Japanese Sky Perfect JSAT to replace Intelsat 805 at 169° E.

This was the 100th launch of an Ariane 5.

Centispace-1 S1 #	2018 75 A	2018 Sep 29.176	Box +2 panels		2018 Sep 29.43	98.22	98.82	7081	697	708	0.0008	265

[Kuaizhou-1A]	[43636]		97

(Y8)	JIUQ-MLP

Kuaizhou-1A 4th stage	2018 75 B	2018 Sep 29.176	Cylinder		2018 Sep 29.36	98.21	95.47	6920	262	820	0.040	40

[43637]

#	Small Chinese Earth monitoring satellite

SAOCOM-1A  *	2018 76 A	2018 Oct 8.098	Hexagonal	1.468 high	2018 Oct 8.17	97.90	97.10	6999	607	633	0.002	244

[Falcon 9b5]  #	[43641]		cylinder	~ 1.5 dia	2018 Oct 8.28	97.90	97.20	7003	615	634	0.001	229

(F9-062, B1048-2)	VDB-SLC4E		+ panels	~ 3.5x4.5	2018 Nov 13.28	97.89	97.13	7000	615	627	0.0009	118

+ antenna	3.5 x 10	2018 Dec 5.22	97.89	97.15	7001	621	624	0.0002	93

~1600

*	Argentine satellite with SAR (Synthetic Aperture Radar)

#	The first stage made the first return to launch site attempt for the west coast and landed at LZ-4.

The second stage was de-orbited and decayed at the end of the first orbit over the Pacific Ocean. De-orbit burn observed from NW Europe.

Yaogan-32 A #	2018 77 A	2018 Oct 9.113			2018 Oct 9.16	98.27	98.68	7074	688	704	0.001	241

[CZ-2C]	[43642]				2018 Oct 11.66	98.28	98.77	7078	694	705	0.0008	222

JUIQ				2018 Oct 16.15	98.28	98.68	7074	695	696	0.0001	99

Yaogan-32 B  #	2018 77 B	2018 Oct 9.113			2018 Oct 9.16	98.28	98.55	7068	681	698	0.001	258

[43643]				2018 Oct 9.78	98.28	98.70	7075	688	704	0.001	238

2018 Oct 16.22	98.28	98.68	7074	695	696	0.0009	104

Yuanzheng-1S	2018 77 C	2018 Oct 9.113			2018 Oct 9.16	98.27	98.68	7074	688	703	0.001	243

Upperstage (YZ-1S)	[43644]

#	Chinese remote sensing satellites.

#1	The first flight of the YZ-1S, a simplified version of the YZ-1 improving the payload capacity of the CZ-2C to Sun Synchronous Orbit from 1200 to 2000 kg.

Beidou 3 M15	2018 78 A	2018 Oct 15.183	Box + 2 panels		2018 Oct 15.42	54.99	787.28	28243	21537	22192	0.012	178

[CZ-3B/YZ1]	[43647]	1 million years			2018 Oct 17.05	54.98	787.40	28246	21541	22195	0.012	178

XI-LC2

Beidou 3 M16	2018 78 B	2018 Oct 15.183	Box + 2 panels		2018 Oct 15.46	55.00	787.13	28240	21530	22192	0.012	178

[43648]	1 million years			2018 Oct 17.63	54.99	787.22	28244	21537	22194	0.012	177

CZ-3B 3rd stage	2018 78 C	2018 Oct 15.183	Cylinder	12.38 long	2018 Oct 15.30	54.92	322.42	15736	296	18509	0.582	171

[43649]		2740	3.0 dia

Yuangzheng-1	2018 78 D	2018 Oct 15.183			2018 Oct 15.34	54.75	812.03	28832	22197	22710	0.009	10

Upperstage	[43650]				2018 Oct 15.68	54.80	810.03	28705	22193	22620	0.007	5

$	Chinese navigation satellites.

AEHF 4 (USA 288) *	2018 79 A	2018 Oct 17.260	Box +2 panels		No TLE’s issued.  Declassified in 2019 Jan.

[Atlas-V 551]	[43651]	> million years			2018 Oct 17.45	12.66	803.23	28623	9154	35335	0.457	180

(AV-073)	CC-LC41				2018 Oct 19.84	11.02	863.50	30038	11984	35335	0.389	180

2018 Oct 21.62	9.52	941.32	31817	15541	35335	0.311	181

2018 Oct 22.95	8.45	1017.48	33511	18929	35335	0.245	181

2018 Oct 25.41	7.67	1084.88	34975	21859	35333	0.193	182

2018 Nov 7.07	7.49	1108.05	35471	22629	35555	0.182	182

2018 Nov 24.67	6.99	1200.07	37408	24609	37450	0.172	185

2019 Jan 8.00	5.74	1308.92	39637	29848	36669	0.086	173

2019 Jan 30.79	5.17	1381.35	41096	32913	36502	0.044	171

2019 Feb 17.73	4.86	1429.68	42039	35519	35802	0.003	166

2019 Feb 21.42	4.83	1436.03	43163	35765	35804	0.0005	17

2019 Mar 4.62	4.80	1436.07	42164	35767	35804	0.0004	25

2019 Mar 7.91	0.07	1436.00	42163	35779	35790	0.0001	104

Atlas V 2nd stage #	2018 79 B	2018 Oct 17.260	Cylinder	12.68 long	No TLE’s issued. Declassified in 2019 Jan.

(Centaur)	[43652]		2243	3.05 dia	2018 Oct 17.45	12.45	785.38	28198	8593	35056	0.469	178

Fragments	2018 79 C-GF  	172 pieces, all in orbit	For orbital information see the extra pages at the end of the year.

*	USA military communication satellite.

#	In early April 2019 the stage fragmented. Fragments have been catalogued in 2019 Oct.

BepiColombo *	2018 80 A	2018 Oct 20.060	Spacecraft	6.3 x 3.9	Heliocentric orbit towards Mercury at ~ 3.9 deg inclination.

[Ariane 5 ECA]	[43653]		stack **	x 3.6	2025 Dec 5	90	138		420	1500	(MPO)

(VA245)	KOU-ELA3		4081		2025 Dec 5	90	558		590	11640	(MPO)

Ariane 5 2nd stage	2018 80 B	2018 Oct 20.060	Cylinder	5.84 long	Heliocentric orbit

[43654]		5668	5.4 dia

*	European-Japanese combined satellite to study Mercury.

Named after the Italian mathematician and engineer Giuseppe (Bepi) Colombo, the mission comprises dual science orbiters: the Mercury Planetary Orbiter (MPO), developed by ESA to map the planet by focusing on its surface and interior; and the Mercury Magnetospheric Orbiter (MMO) – developed and built by JAXA to investigate its magnetosphere by exploring the environment. The Mercury Composite Spacecraft (MCS) consists of the MTM, MPO, MMO, and MOSIF. The Mercury Transfer Module (MTM) will carry the two orbiters (MPO and MMO) to their destination and the MMO Sunshield and Interface Structure (MOSIF) will provide thermal protection. The expected arrival is scheduled in late 2025, with BepiColombo to be gravity captured after jettisoning the MTM. Its descent into Mercury orbit will be performed by chemical propulsion engine within the MPO. Once at Mercury, BepiColombo will endure temperatures in excess of 350°C. It will then conduct a one-year nominal mission, with a possible one-year extension.

BepiColombo will use 9 planet fly-by’s to slow down and spiral towards Mercury. Flyby of Earth on 10 Apr 2020, Venus on 16 Oct 2020 and 11 Aug 2021, Mercury on 2 Oct 2021, 23 Jun 2022, 20 Jun 2023, 5 Sep 2024, 2 Dec 2024 and 9 Jan 2025. Just before entering a polar orbit around Mercury on 5 Dec 2025 the spacecraft will jettison the MTM and with a small manoeuvre entering  a polar orbi. The MPO and MMO will then separate and use their onboard thrusters to achieve their orbits. The MTM will be in a similar heliocentric orbit as Mercury.

**	MTM is a trapzodial box + 2 panels, span 14m; MPO is a box 2.4x2.2x1.7 + panel and 1230 kg (BOL). On top of MPO is a shunshade to protect MMO before it is released. MMO is a short octagonal box 1.8 dia and 0.90 high + antenna, 255 kg (BOL).

Haiyang 2B  #	2018 81 A	2018 Oct 24.956	Box + panel		2018 Oct 25.39	99.35	103.75	7314	928	943	0.001	278

[CZ-4B]	[43655]				2018 Oct 25.87	99.35	103.80	7317	931	945	0.001	284

WUZ				2018 Oct 26.37	99.35	103.83	7319	933	947	0.0009	281

2018 Oct 26.48	99.35	104.00	7328	944	951	0.0005	286

2018 Oct 27.04	99.35	104.13	7332	949	957	0.0006	284

2018 Oct 27.48	99.36	104.37	7343	963	967	0.0003	68

2018 Oct 31.81	99.35	104.40	7345	965	967	0.0002	87

CZ-4B 3rd stage	2018 81 B	2018 Oct 24.956	Cylinder	4.92 long	2018 Oct 25.46	99.45	100.67	7168	640	940	0.021	6

[43656]		1700	2.9 dia

Fragments	2018 81 C-E		3 pieces, all in orbit	For orbital information see extra pages at end of year

#	Chinese oceanographic satellite

Cosmos 2528  #	2018 82 A	2018 Oct 25.010			2018 Oct 25.15	67.14	96.05	6948	239	900	0.048	92

[Soyuz-2.1B]	[43657]				2018 Oct 26.82	67.14	96.12	6951	244	900	0.047	91

PLE-LC43/4		~ 6000 full		2018 Oct 29.61	67.15	103.12	7284	902	909	0.0005	273

2018 Oct 31.88	67.15	103.10	7283	900	910	0.0007	265

Soyuz-2.1B 3rd stage	2018 82 B	2018 Oct 25.010	Cylinder	6.74 long	2018 Oct 25.15	67.14	95.87	6939	238	882	0.046	92

[43658]		2355	2.66 dia

#	Russian signals intelligence satellite Lotus-S No. 804

CFOSAT  *	2018 83 A	2018 Oct 29.030			2018 Oct 29.36	97.53	94.95	6895	510	523	0.001	269

[CZ-2C]	[43662]		650		2018 Oct 31.00	97.53	95.00	6897	511	526	0.001	242

(Y22)	JIUQ				2018 Oct 31.54	97.53	95.02	6900	513	529	0.001	247

2018 Nov 1.11	97.52	94.95	6895	514	519	0.0004	121

2018 Nov 8.79	97.53	94.95	6895	515	517	0.0001	81

D	CZ-2C 2nd stage	2018 83 F	2018 Oct 29.030	Cylinder	7.58 long	2018 Oct 29.22	97.61	91.77	6740	212	511	0.022	41

[43667]	99 days	3300	3.35 dia	2019 Feb 5.04	97.58	87.20	6514	130	141	0.0009	59

2019 Feb 5

Fragments ?? #	2018 83 B-E, G, H	6 pieces, all in orbit	For orbital information see extra pages at end of the year.

*	Chinese-France Oceanographic SATellite to study the interactions between the atmosphere and the oceans.

It's fitted with two radars: the French-made SWIM spectrometer, which will measure the direction and the wavelength of waves, and China's SCAT, a scatterometer that will analyse the force and direction of winds.

#	These objects are not yet ID-ed by Space-Track. McDowell has them as Changshagoaxin/TY-4-01, Xiaoxiang/TY-1-02, Tonmgchuan/TY-4-02, Xinghe/TY-1-03, Tiagi-1, CubeBel-1 (BSUSat-1). The 4 TY-sats were build by Spacety, China.

GOSAT 2  *1	2018 84 B	2018 Oct 29.172	Box +2 panels	5.3 x 2.0	2018 Oct 29.30	97.85	96.83	6985	596	617	0.001	285

(Ibuki 2)	[43672]		~ 1800 full	x 2.1

[H-2A](F40)	TAN-LC1		16.5 span

KhalifaSat  *2	2018 84 F	2018 Oct 29.172	Hexagonal cyl	2 high	2018 Oct 29.30	97.84	96.72	6980	591	612	0.001	313

[43676]		+ 4 panels	1.5 dia

~330	~3.3 span

Ten-Koh   *5	2018 84 G	2018 Oct 29.172	Quasi-sphere	~ 0.50 dia	2018 Oct 29.30	97.84	96.63	6976	586	608	0.002	335

[43677]		23

Diwata 2B  *3	2018 84 H	2018 Oct 29.172	Box +2 panels		2018 Oct 29.30	97.84	96.53	6971	595	601	0.001	359

[43678]		56

STARS-AO   *7	2018 84 J	2018 Oct 29.172	1U Cube	0.10 side	2018 Oct 29.30	97.86	96.52	6970	583	601	0.001	21

[43679]		1.6

AUTcube 2  *6	2018 84 K	2018 Oct 29.172	1U Cube	0.10 side	2018 Oct 29.75	97.83	96.53	6971	585	601	0.001	19

[43681]		1.4

H-2A 2nd stage  #	2018 84 L	2018 Oct 29.172			2018 Oct 29.75	98.85	95.83	6937	520	598	0.006	287

[43682]		3100

Fragments	2018 84 A, C-E, M-DG	100 pieces, 1 has decayed	For orbital information see extra pages at end of the year.

PROITERES 2   *4	2018 84 	2018 Oct 29.172	Cube	0.30 side	Not certain that this sat was on board.

+ boom

45

*1	Japanese Greenhouse Gases Observing SATellite to study human causes of climate change. Ibuki is Japanese for “breath”.

*2 Earth observing satellite from United Arab Emirates. The satellite was formerly known as DubaiSat-3. The camera has a resolution of 0.70 m.

*3	Diwata 2B, a satellite built in the Philippines by PHL Microsat, a consortium of students and engineers founded in a collaboration between the Philippines' Department of Science and Technology, University of the Philippines Diliman, and Japan’s Hokkaido University and Tohoku University. Diwata 2B carries optical cameras and an Earth-imaging telescope, plus an amateur radio payload.

*4	PROITERES 2, PRoject of Osaka Institute of Technology Electric-Rocket-Engine onboard Small Space Ship-2,  a replacement for the failed PROITERES spacecraft launched in 2012. The spacecraft built at the Osaka Institute of Technology in Japan will test an electric rocket thruster, a high-resolution camera and conduct communications experiments in orbit. A magnetic sensor is deployed on a ~1m boom.

*5	Ten-Koh is asatellite from the Kyushu Institute of Technology in Japan. Ten-Koh will collect data on the environment of low Earth orbit, and chart the degradation of advanced spacecraft materials during its mission. The satellite will measure radiation, magnetic flux density and electron density for a mission lasting at least six months.

*6	AUTcube 2 is a 1U CubeSat developed at the Aichi Institute of Technology in Japan. The multipurpose CubeSat will test optical communication technologies, virtual reality imaging cameras, conduct electromagnetic interference experiments, and test techniques for future deep space communications capabilities.

*7	STARS-AO, STARS Astronomical Observations, is a  1U CubeSat developed at Shizuoka University in Japan, will demonstrate astronomical observations using an ultra-sensitive miniature telescope.

#	Fragmented 2019 Feb 6. Fragment E experienced itself a fragmentation with resulted in 5 fragments.

Beidou 3G1 *	2018 85 A	2018 Nov 1.665			2018 Nov 1.79	28.47	631.57	24384	196	35815	0.730	180

[CZ-3B]	[43683]	> million years			2018 Nov 12.76	3.07	1436.22	42167	35783	35794	0.0001	310

XI				2018 Nov 13.72	3.07	1436.05	42164	35783	35787	0.0004	123

CZ-3B 3rd stage	2018 85 B	2018 Nov 1.665	Cylinder	12.38 long	2018 Nov 1.48	28.44	603.37	23653	158	34391	0.724	179

[43684]		2740	3.0 dia

*	Chinese navigation satellite; the first 3rd generation Beidou to geo stationairy orbit

Cosmos 2529  #	2018 86 A	2018 Nov 3.845	Cyl + box		2018 Nov 4.07	64.82	676.25	25521	19122	19163	0.0008	288

[Soyuz-2.1b/Fregat]	[43687]	1 million years	+ 2 panels		2018 Nov 11.67	64.82	677.62	25556	19145	19209	0.001	13

PLE		1400

Fregat stage	2018 86 B	2018 Nov 3.845	Torus+spheres	1.85 high	2018 Nov 7.12	64.82	677.62	25556	19146	19208	0.001	12

[43688]		930	3.35 dia

#	Glonass M navigation satellite No. 57 for plane 2 of the constellation.

MetOp-C  *	2018 87 A	2018 Nov 7.033	Box + panel		2018 Nov 7.38	98.74	101.00	7185	805	807	0.0001	290

[Soyuz ST-B/Fregat]	[43689]		4084		2018 Nov 18.12	98.74	101.20	7194	814	817	0.0002	110

KOU-ELS

Fregat stage	2018 87	2018 Nov 7.033	Torus+spheres	1.85 high	De-orbited after satellite deploy.

[NNA]		930	3.35 dia

*	European polar weather satellite.

Cicero 10   *1	2018 88 A	2018 Nov 11.160	6U Cube	0.34x0.20	2018 Nov 11.20	85.03	91.65	6734	204	506	0.022	223 #

[Electron] *	[43690]		+2 panels	x0.10	2018 Nov 13.48	85.03	94.62	6733	208	500	0.022	214 #

MA-LC1		10	0.60 span	2018 Nov 13.78	85.04	94.78	6886	499	517	0.001	285

D	Electron 2nd stage	2018 88 B	2018 Nov 11.160			2018 Nov 11.33	85.02	94.83	6889	505	516	0.0008	308 #

[43691]	48 days			2018 Nov 11.81	85.03	94.78	6886	499	517	0.001	293 #

2018 Dec 29			2018 Nov 13.76	85.03	91.62	6732	208	499	0.022	212

2018 Dec 28.63	84.99	87.58	6534	144	166	0.002	53

NABEO/Electron  *6	2018 88 C	2018 Nov 11.160	Box + sail	1.4 kg	2018 Nov 12.37	85.03	91.62	6732	208	499	0.022	212

Curie kick stage *2	[43692]		Truncated cone	?? long

1-1.2 dia

IRVINE01  *4	2018 88 D	2018 Nov 11.160	1U Cube	0.10 side	2018 Nov 11.81	85.04	94.70	6883	494	514	0.001	271

[43693]		+2 panels	0.54 span	2018 Nov 12.00	85.04	94.70	6882	493	514	0.002	270

1

Proxima 1   *3	2018 88 E	2018 Nov 11.160	1.5U Cube	0.15x0.10	2018 Nov 11.81	85.03	94.67	6881	489	516	0.002	260

[43694]		+2 panels	x0.10	2018 Nov 12.00	85.02	94.67	6881	491	514	0.002	268

0.30 span

Lemur-2 82  *5	2018 88 F	2018 Nov 11.160	3U Cube	0.34x0.10	2018 Nov 11.87	85.03	94.75	6885	496	517	0.002	293

Zupanski	[43695]		+ 2 panels	x0.10

0.51 span

Proxima 2   *3	2018 88 G	2018 Nov 11.160	1.5U Cube	0.15x0.10	2018 Nov 12.37	85.03	94.67	6881	491	514	0.002	266

[43696]		+2 panels	x0.10

0.30 span

Lemur-2 83  *5	2018 88 H	2018 Nov 11.160	3U Cube	0.34x0.10	2018 Nov 13.05	85.03	94.70	6883	496	512	0.001	269

Chanusiak	[43697]		+ 2 panels	x0.10

0.51 span

*	This launch is called “It’s Business Time” by Rocket Launch.

*1	Community Initiative for Cellular Earth Remote Observation is a commercial satellite for GeoOptics.

*2	The Curie kick stage circulized the orbit.

*6	NAnosat Bremssegel Entfaltversuch in Orbit is a German build payload that will remain attached to the Curie stage and after the cubesats have been released deploy a 2.5 m2 drag sail for faster decay.

*4	Build by students in Southern California,

*5	Ship and aircraft tracking and weather data collection satellites from Spir Global.

*3	Pathfinder data relay satellites from Fleet Space Technologies

#	Space-Track had these orbits interchanged for Cicero 10 and the Electron 2nd stage; corrected on 2018 Nov 13.

GSAT 29  #	2018 89 A	2018 Nov 14.485	Box +2 panels		2018 Nov 14.54	21.50	629.73	24337	180	35735	0.730	178

[GSLV Mk.3-D2]	[43698]	> million years	3423		2018 Nov 15.42	8.85	781.18	28097	7510	35928	0.506	178

SRI-LC2				2018 Nov 16.85	0.32	1368.57	40832	33062	35845	0.034	170

2018 Nov 18.85	0.08	1425.25	41952	35307	35840	0.006	72

2018 Nov 21.92	0.06	1446.28	42364	35846	36125	0.003	347

2018 Nov 26.84	0.06	1436.13	42166	35774	35800	0.0003	320

2018 Dec 4.90	0.04	1436.10	42165	35774	35798	0.0003	320

GSLV 3rd stage	2018 89 B	2018 Nov 14.485	Cylinder	13.55 long	2018 Nov 14.55	21.48	621.90	24135	175	35337	0.728	178

[43699]		5000	4.0 dia

#	Indian communication satellite at 55° East over the equator.

This was the 2nd development flight of the GSLV Mk.3 rocket.

Es’hail 2  *	2018 90 A	2018 Nov 15.865	Box +2 panels		2018 Nov 15.95	25.02	668.38	25323	201	37688	0.740	178

[Falcon-9b5] #	[43700]				2018 Nov 27.75	0.09	1436.08	42164	35781	35791	0.0001	0

(F9-063, B1047-2)	CC-LC39A				2018 Dec 7.93	0.06	1436.12	42165	35784	35789	0.00005	48

2018 Dec 29.97	0.03	1434.57	42135	35738	35774	0.0004	11

2019 Jan 3.64	0.03	1436.12	42165	35784	35789	0.0005	193

2019 Jan 8.63	0.04	1436.07	42164	35783	35788	0.00006	217

D	Falcon 9 2nd stage	2018 90 B	2018 Nov 15.865	Cylinder	13 long	2018 Nov 15.95	24.99	665.30	25245	194	37538	0.740	178

[43701]	151 days	3900	3.66 dia	2019 Apr 15.12	24.77	97.58	7022	109	1177	0.076	296

2019 Apr 15

*	Communication satellite from Qatar to be located over the equator at 26° East.

#	The 1st stage previously launched Telstar 19 Vantage on 2018 Jul 22 and then landed on the droneship OCISLY in the Atlantic Ocean.

It did so also this time and could be used for s 3rd launch.

D 	Progress MS-10 *	2018 91 A	2018 Nov 16.760	Cyl+beehive+	7.5 long	2018 Nov 16.75	51.63	88.60	6584	185	226	0.003	87

[Soyuz-FG]	[43702]	199.774 days	+spheroid+	2.72 maxdia	2018 Nov 17.07	51.64	89.70	6638	252	268	0.001	73

BAI-LC1	2019 Apr 6	2 panels	2.3 dia

7281

D	Soyuz-FG 3rd stage	2018 91 B	2018 Nov 16.760	Cylinder	6.74 long	2018 Nov 16.75	51.64	88.50	6579	186	215	0.002	84

[43703]	3 days	2355	2.66 dia	2018 Nov 19.45	51.64	87.53	6531	146	158	0.0009	83

2018 Nov 19

*	Progress Ms-10 docked 2018 Nov 18.811 with ISS (Zvezda port) with a cargo of 2495 kg of supplies, experiments, spare parts, water, qxygen and fuel.

D	Cygnus NG-10  *	2018 92 A	2018 Nov 17.376	Cylinder	6.39 long	2018 Nov 17.44	51.59	89.13	6610	211	252	0.003	142

(S.S. John Young)	[43704]	99.961 days	+2 panels	3.07 dia	2018 Nov 18.32	51.62	92.02	6752	348	398	0.004	9

[Antares 230]	WLI-LC0A	2019 Feb 25.337			2018 Nov 18.51	51.64	92.52	6777	396	401	0.0004	60

2018 Nov 19.41	51.64	92.65	6783	401	408	0.0005	62

2019 Feb 8.77	51.63	92.80	6790	405	418	0.0009	27

2019 Feb 8.90	51.64	93.43	6821	430	455	0.002	285

2019 Feb 8.97	51.64	93.72	6835	452	460	0.0006	338

2019 Feb 13.56	51.64	93.77	6838	453	465	0.0009	333

2019 Feb 13.83	51.67	92.52	6776	386	410	0.002	156

2019 Feb 14.09	51.64	90.50	6677	292	305	0.001	263

2019 Feb 14.88	51.64	90.70	6688	303	315	0.001	258

2019 Feb 24.89	51.64	90.68	6686	300	315	0.001	301

D	Antares 2nd stage	2018 92 B	2018 Nov 17.376	Cylinder	5.99 long	2018 Nov 17.44	51.59	89.35	6621	211	273	0.005	142

(Castor 30 XL)	[43705]	11 days	~2100	2.34 dia	2018 Nov 28.38	51.59	87.52	6530	145	157	0.0009	201

2018 Nov 28

Quantum Radar 1  *3	2018 92 C				2019 Feb 9.72	51.64	93.72	6835	454	458	0.0003	2

[44041]

Quantum Radar 2  *3	2018 92 D				2019 Feb 9.67	51.64	93.72	6835	456	457	0.00005	344

[44041]

CHEFSat 2   *2	2018 92 E	2019 Feb 13	6U Cube	0.34x0.10	2019 Feb 14.69	51.64	93.85	6841	454	471	0.001	0

[44044]		3.7	X0.10

MYSat 1  *1	2018 92 F	2019 Feb 13	1U Cube	0.10 side	2019 Feb 14.61	51.64	93.85	6841	455	471	0.001	3

[44045]		1

D	KickSat 2   *4	2018 92 G	2019 Feb 14	3U-Cube	0.34x0.10	2019 Feb 14.83	51.64	90.55	6680	297	305	0.0007	308

[44046]	47 days	5.5	x0.10	2019 Apr 1.99	51.63	87.73	6541	157	167	0.0008	240

2019 Apr 2

Objects not yet properly ID-ed.			C

D

*	Resupply cargo ship rendezvoused with ISS and was grappled by station’s robotic arm 2018 Nov 19.436; berthed to the Unity nadir port.

On board are 3273 kg of supplies. NG stands for Northrop Grumman that acquired Orbital ATK which developed and flew the Cygnus.

Released 2019 Feb 8.678 from the ISS. It removed about 2500 kg of no longer needed materials and trash from ISS.

The Cygnus deployed 5 cubesats from different altitudes, first 4 from a higher, then 1 at a lower altitude than the ISS.

*1	MYSat 1 from Masdar Institute of Science and Technology in Abu Dhabi with the support of Northrop Grumman Innovation Systems and Al Yah Satellite Communications Company in the United Arab Emirates.

*2	CHEFSat 2 (Cost-effective High E-Frequency SATellite from the U.S. Naval Research Laboratory to test off the shelf technology.

*3	Two passive cubesats with optical reflectors. With laser telescopes their orbits can be tracked by students.

The satellites were launched on board of the Dragon CRS-16 cargo mission together with the SEOPS Slingshot deployer prototype. This equipment was installed by astronauts on the Cygnus NG-10 entry hatch before the unberthing of Cygnus NG-10and the satellites were deployed from the spacecrafts SEOPS Slingshot deployer after departing from the ISS.

*4	Kicksat 2 a NASA-sponsored CubeSat mission led by principal investigator Zac Manchester at Stanford University. KickSat 2 released 2019 Mar 20 100 “sprites”, small 3.5x3.5 cm circuit boards with power, sensors and communication. They will test how far satellites can be miniaturized.

The lower release orbit of around 325 km will ensure the sprites re-enter in a few weeks.

Beidou 3 M17  #	2018 93 A	2018 Nov 18.755	Box + 2 panels		2018 Nov 19.71	54.99	787.00	28237	21523	22193	0.012	178

[CZ-3B/YZ1]	[43706]	1 million years

XI-LC2

Beidou 3 M18	2018 93 B	2018 Nov 18.755	Box + 2 panels		2018 Nov 19.64	54.99	787.18	28241	21531	22193	0.012	178

[43707]	1 million years			2018 Nov 22.46	54.98	784.62	28180	21532	22070	0.010	179

Yuangzheng-1	2018 93 C	2018 Nov 7.55			2018 Nov 19.64	54.99	787.00	28237	21523	22194	0.012	178

Upperstage	[43708]				2018 Nov 19.68	55.13	812.08	28834	22180	22729	0.010	7

D	CZ-3B 3rd stage	2018 93 D	2018 Nov 7.55	Cylinder	12.38 long	2018 Nov 19.21	54.96	330.87	15847	202	18734	0.585	171

[43709]	343 days	2740	3.0 dia 	2019 Oct 27.91	54.71	91.07	6705	109	545	0.033	318

2019 Oct 28

#	Chinese navigation satellites.

Tianzhi 1   #4	2018 94 A	2018 Nov 19.986			2018 Nov 20.11	97.40	94.53	6874	489	503	0.001	253

[CZ-2D]	[43710]

JIUQ-LC43

Shiyan-6  #1	2018 94 B	2018 Nov 19.986			2018 Nov 20.11	97.41	94.53	6874	488	504	0.001	268

Shiyan-6  #1	[43711]

Tianping 1A  #2	2018 94 C	2018 Nov 19.986			2018 Nov 20.23	97.40	94.53	6874	489	503	0.001	262

[43712]

Jiading-1   #3	2018 94 D	2018 Nov 19.986			2018 Nov 20.58	97.40	94.52	6874	487	504	0.001	269

(OKW 1)	[43713]		~45

Tianping 1B  #2	2018 94 E	2018 Nov 19.986			2018 Nov 20.65	97.41	94.53	6874	488	503	0.001	263

[43714]

CZ-2D 2nd  stage	2018 94 	2018 Nov 19.986	Cylinder	10.9 long

[NNA]		6050	3.35 dia

Fragments 	2018 94 F-H		3 pieces, all in orbit	For orbital information see extra pages at end of the year.

#1	Chinese satellite for space environment exploration experiments.

#2 Two satellites for equipment calibration at ground control stations.

#3	First satellite of the low earth orbit Xiangyun constellation.

#4	Software-defined satellite for conducting experiments on open-source satellite software research and development on Android platforms.

Mohammed VI-B  *	2018 95 A	2018 Nov 21.071	Hexagonal Box	~3.5 long	2018 Nov 21.14	97.95	96.73	6980	600	603	0.0002	126

[Vega]	[43717]		+3 panels	~1.5 dia	2018 Nov 24.50	97.95	96.80	6984	604	607	0.0002	68

(VV-13)	KOU-ZLV		1108	~4 span

*	Moroccan military reconnaissance satellite.

Vega AVUM upperstage de-orbited after satellite release.

HysIS   *1	2018 96 A	2018 Nov 29.186	Box +2 panels	2.158x1.386	2018 Nov 29.31	97.97	97.47	7016	628	647	0.001	238

[PSLV C43]	[43719]		380	x1.121	2018 Nov 29.37	97.96	97.47	7016	627	647	0.001	237

SRI-LC1			?? span	2018 Nov 30.51	97.97	97.47	7016	628	647	0.001	232

HSAT-1   *10	2018 96 B	2018 Nov 29.186	6U Cubesat	0.30x0.20	2018 Nov 29.64	97.48	94.38	6867	478	499	0.002	318

[43720]			0.10

+2 panels	1.3 span

+ antenna	~0.60 long

13

FACSat 1   *4	2019 96 C	2018 Nov 29.186	3U Cubesat	0.30x0.10	2018 Nov 29.64	97.49	94.37	6867	477	499	0.002	314

[43721]		x0.10

Centauri 2 *2	2018 96 D	2018 Nov 29.186	3U Cubesat	0.30x0.10	2018 Nov 29.64	97.48	94.37	6867	476	500	0.002	322

[43722]			x0.10

+2 panels	0.50 span

Flock 3r 09 *9	2018 96 E	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.64	97.48	94.38	6867	478	499	0.002	318

[43723]		+2 panels	x0.10

5	0.70 span

Flock 3r 12 *9	2018 96 F	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.51	97.47	94.35	6866	476	499	0.002	321

[43724]		+2 panels	x0.10

5	0.70 span

Flock 3r 11 *9	2018 96 G	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.51	97.48	94.35	6866	476	499	0.002	319

[43725]		+2 panels	x0.10

5	0.70 span

Flock 3r 05 *9	2018 96 H	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.64	97.48	94.35	6866	476	499	0.002	325

[43726]		+2 panels	x0.10

5	0.70 span

Flock 3r 08 *9	2018 96 J	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.58	97.50	94.35	6866	476	498	0.002	322

[43727]		+2 panels	x0.10

5	0.70 span

3Cat-1   *8	2018 96 K	2018 Nov 29.186	1U Cubesat	0.10 side	2018 Nov 29.58	97.50	94.35	6865	474	500	0.002	333

[43728]		1.2

Kepler 1   *3	2018 96 L	2018 Nov 29.186	3U Cubesat	0.30x0.10	2018 Nov 29.64	97.49	94.35	6865	475	499	0.002	330

(CASE)	[43729]			x0.10

+2 panels	0.70 span

Global-1   *11	2018 96 M	2018 Nov 29.186	Box +2 panels		2018 Nov 29.65	97.48	94.33	6865	473	499	0.002	329

[43730]		55

Lemur-2   *12	2018 96 N	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.58	97.49	94.32	6864	471	500	0.002	332

Orzulak	[43731]		+2 panels	x0.10

5	0.56 span

Lemur-2   *12	2018 96 P	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.58	97.49	94.32	6864	471	499	0.002	328

Kobyszcze	[43732]		+2 panels	x0.10

5	0.56 span

Flock 3r 04 *9	2018 96 Q	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.48	94.32	6864	471	499	0.002	329

[43733]		+2 panels	x0.10

5	0.70 span

Flock 3r 03 *9	2018 96 R	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.58	97.50	94.32	6864	470	500	0.002	334

[43734]		+2 panels	x0.10

5	0.70 span

Flock 3r 16 *9	2018 96 S	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.64	97.49	94.30	6863	469	500	0.002	335

[43735]		+2 panels	x0.10

5	0.70 span

Flock 3r 15 *9	2018 96 T	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 29.64	97.48	94.30	6863	471	499	0.002	331

[43736]		+2 panels	x0.10

5	0.70 span

Cicero 8   *5	2018 96 U	2018 Nov 29.186	6U cube	0.34x0.20	2018 Nov 29.64	97.48	94.28	6862	468	499	0.002	334

[43737]			x 0.10

+ 2 panels	0.60 span

~10

Innosat-2  *6	2018 96 V	2018 Nov 29.186	3U Cubesat	0.30x0.10	2018 Nov 29.64	97.48	94.25	6861	466	498	0.002	335

[43738]		4	x0.10

PSLV 4th stage	2018 96 W	2018 Nov 29.186	Cylinder	2.60 long	2018 Nov 29.57	97.43	93.63	6830	416	488	0.005	44

[43739]		920	2.02 dia

Flock 3r 10 *9	2018 96 X	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.37	6866	475	500	0.002	325

[43740]		+2 panels	x0.10

5	0.70 span

Flock 3r 06 *9	2018 96 Y	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.16	97.49	94.35	6866	476	499	0.002	325

[43741]		+2 panels	x0.10

5	0.70 span

Flock 3r 07 *9	2018 96 Z	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.16	97.49	94.35	6866	476	499	0.002	325

[43742]		+2 panels	x0.10

5	0.70 span

Reaktor Hello World	2018 96 AA	2018 Nov 29.186	2U Cubesat	0.20x0.10	2018 Nov 30.16	97.49	94.35	6865	475	498	0.002	325

*5	[43743]		2	0.10

Hiber-1   *7	2018 96 AB	2018 Nov 29.186	6U Cubesat	0.30x0.20	2018 Nov 30.16	97.49	94.35	6865	474	499	0.002	329

[43744]			x0.10

+ panel	0.30 span

Lemur-2   *12	2018 96 AC	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.32	6864	472	499	0.002	327

Duly	[43745]		+2 panels	x0.10

5	0.56 span

Lemur-2   *12	2018 96 AD	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.32	6864	471	499	0.002	328

Vladimir	[43746]		+2 panels	x0.10

5	0.56 span

Flock 3r 01 *9	2018 96 AE	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.32	6864	471	499	0.002	328

[43747]		+2 panels	x0.10

5	0.70 span

Flock 3r 02 *9	2018 96 AF	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.32	6864	471	499	0.002	329

[43748]		+2 panels	x0.10

5	0.70 span

Flock 3r 14 *9	2018 96 AG	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.48	94.30	6863	471	499	0.002	331

[43749]		+2 panels	x0.10

5	0.70 span

Flock 3r 13 *9	2018 96 AH	2018 Nov 29.186	3U cube	0.30x0.10	2018 Nov 30.03	97.49	94.30	6863	470	499	0.002	331

[43750]		+2 panels	x0.10

5	0.70 span

*1	Hyper-Spectral Imaging Satellite is an earth observing satellite to study the earth’s surface in visible, near infrared and shortwave infrared light.

After 2 engine burns to lower the orbit of the 4th stage the 30 smallsats were deployed.

*2	Centauri from Australia for remote Internet of Things Communication sevices.

*3	Kepler (CASE) from Canada for Internet of Things

*4	FACSAT from Columbia Air Force for Earth observations.

*5	Reaktor Hello World from Finland for Earth observations.

*6	InnoSAT-2 from Malaysia for Earth observations.

*7	HIBER-1 from the Netherlands for Earth observations.

*8	3Cat-1 from Universidad Politecnica de Cataluña in Spain for Scientific / Experimental operations

*9	16 Flock 3r satellites from USA for Earth observations.

*10 HSAT-1 from USA for remote Internet of Things Communication sevices.

*11 Global-1 from USA for Earth observations.

*12 4 Lemur-2 satellites from USA for Vessel Automatic Identification System (AIS).

Cosmos 2530  #	2018 97 A	2018 Nov 30.102			2018 Nov 30.32	82.50	115.87	7873	1482	1507	0.002	308

[Rockot/Breeze-KM]	[43751]				2018 Nov 30.42	82.51	115.87	7873	1483	1506	0.002	307

PLE-LC133/3

Cosmos 2531	2018 97 B	2018 Nov 30.102			2018 Nov 30.32	82.52	115.90	7875	1484	1508	0.002	321

[43752]				2018 Nov 30.43	82.51	115.88	7874	1484	1507	0.001	314

Cosmos 2532	2018 97 C	2018 Nov 30.102			2018 Nov 30.32	82.51	115.92	7875	1485	1508	0.001	322

[43753]

Breeze-KM stage	2018 97 D	2018 Nov 30.102			2018 Nov 30.32	82.51	112.48	7719	1176	1505	0.021	272

[43754]

Object E	2018 97 E	2018 Nov 30.102			2018 Nov 30.28	82.53	112.40	7715	1170	1503	0.022	272

[43755]				2018 Nov 30.42	82.52	112.42	7716	1172	1503	0.021	271

#	Three Rodnik military communication satellites.

D	Soyuz MS-11 *	2018 98 A	2018 Dec 3.480	Cyl+beehive+	7.48 long	2018 Dec 3.50	51.62	88.88	6598	200	238	0.003	114

3M [Soyuz FG]	[43756]	203.636 days	+spheroid+	2.72 maxdia	2018 Dec 3.56	51.60	88.75	6591	194	232	0.003	97

R		BAI-LC1/5	2019 Jun 25.117	2 panels	2.2 dia	2018 Dec 3.59	51.64	92.65	6783	401	408	0.0005	110

7167	10.6 span	2018 Dec 3.68	51.63	91.80	6741	358	368	0.0008	277

2018 Dec 4.20	51.64	92.65	6783	401	408	0.0005	112

D	Soyuz FG 3rd stage	2018 98 B	2018 Dec 3.480	Cylinder	6.74 long	2018 Dec 3.47	51.63	88.62	6595	189	224	0.003	72

[43757]	5 days	2355	2.66 dia	2018 Dec 7.76	51.62	87.30	6519	137	144	0.0006	139

2018 Dec 8

*	Soyuz MS-11 with 3 crewmembers (Kononenko, McClain, Saint-Jacques) docked 2018 Dec 3.721 with ISS (Poisk port). Undocked 2019 Jun 24.976 and landed

in Kazachstan SE of the town of Dzhezkazgan.

MinXSS-2	2018 99 A  	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 3.84	97.77	96.30	6960	574	589	0.001	259

[Falcon-9b5]	[43758]		+2 panels	0.10

(F9-064 ,B1046-3) 	VDB-SLW4		4	0.30 span

Sirion Pathfinder-2	2018 99 B	2018 Dec 3.774			2018 Dec 3.84	97.77	96.30	6960	572	591	0.001	262

[43759]

Elysium / Lower	2018 99 C	2018 Dec 3.774	Hexagonal		2018 Dec 3.84	97.77	96.30	6960	573	591	0.001	255

Free Flyer	[43760]		+ 1U Cube	0.10 side

STPSat-5	2018 99 E  	2018 Dec 3.774	Box +2 panels		2018 Dec 3.84	97.77	96.30	6960	573	589	0.001	259

[43762]

Upper Free Flyer	2018 99 F	2018 Dec 3.774	see text below		2018 Dec 3.84	97.77	96.27	6959	571	589	0.001	261

[43763]

ORS-7A	2018 99 G  	2018 Dec 3.774	6U cubesat	0.30x0.10	2018 Dec 4.44	97.77	96.25	6957	569	588	0.001	267

(Polar Scout Kodiak)	[43764]		+3 panels	x0.10

1.30 span

0.60 span

Hawk-A	2018 99 H  	2018 Dec 3.774	Box		2018 Dec 4.42	97.76	96.25	6958	570	588	0.001	270

[43765]		13.4

Spawar-Cal-O	2018 99 J	2018 Dec 3.774	1U cube	0.10 side	2018 Dec 4.51	97.77	96.35	6962	577	590	0.0009	250

[43766]

Landmapper-BC	2018 99 K 	2018 Dec 3.774	6U cubesat	0.30x0.20	2018 Dec 4.44	97.78	96.33	6962	574	592	0.001	295

(Corvus BC 4)	[43767]		+ 2 panels	x0.10

~0.40 span

AISTechSat 2	2018 99 L  	2018 Dec 3.774	6U Cubesat	0.30x0.20	2018 Dec 5.76	97.77	96.35	6962	577	590	0.001	254

[43768]		+2 panels	x0.10

0.60 span

Flock 3s-01	2018 99 M 	2018 Dec 3.774	3U cube	0.30x0.10	2018 Dec 6.66	97.77	96.33	6962	574	592	0.001	256

(Dove 105C)	[43769]		+2 panels	x0.10

5	0.70 span

AO-95	2018 99 N 	2018 Dec 3.774	1U cube	0.10 side	2018 Dec 6.65	97.77	96.33	6962	574	592	0.001	260

(Fox-1C)	[43770]		1

Range A	2018 99 R  	2018 Dec 3.774	1.5 cubesat	0.15x0.10	2018 Dec 6.66	97.77	96.33	6961	575	591	0.001	246

[43773]			x0.10

+2 panels	0.50 span

4

Hiber-2	2018 99 S  	2018 Dec 3.774	6U cubesat	0.30x0.20	2018 Dec 5.89	97.77	96.33	6961	575	590	0.001	250

[43774]			x0.10

+ panel	0.30 span

Spawar-Cal-R	2018 99 U	2018 Dec 3.774	1U cube	0.10 side	2018 Dec 5.65	97.77	96.32	6961	573	591	0.001	254

[43776]

LACMA-Enoch	2018 99 V	2018 Dec 3.774	3Ucube sledge	0.30x0.10	2018 Dec 6.70	97.77	96.33	6961	575	591	0.001	258

[43777]			x0.10

Spawar-Cal-OR	2018 99 W	2018 Dec 3.774	1U cube	0.10 side	2018 Dec 6.65	97.76	96.33	6961	574	592	0.001	261

[43778]

Move II	2018 99 Y 	2018 Dec 3.774			2018 Dec 6.70	97.77	96.32	6961	574	591	0.001	257

[43780]

VESTA-1	2018 99 Z  	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 6.76	97.76	96.32	6961	574	591	0.001	246

[43781]			x0.10

+4 panels	0.70 span

5

SNUSAT-2	2018 99 AA	2018 Dec 3.774			2018 Dec 6.36	97.77	96.32	6961	574	590	0.001	243

[43782]

KazSTSAT	2018 99 AB  2018 Dec 3.774	2018 Dec 3.774	Box	2018 Dec 6.65	97.77	96.32	6961	573	591	0.001	249

[43783]		~ 50

SNUGLITE	2018 99 AC 	2018 Dec 3.774	2U cubesat	0.20x0.10	2018 Dec 6.76	97.77	96.32	6960	573	591	0.001	257

[43784]			0.10

+2 panels	~0.20 span

+ boom	~0.50 long

Orbweaver 2	2018 99 AD	2018 Dec 3.774			2018 Dec 6.78	97.76	96.32	6961	573	590	0.001	242

[43785]

KazSciSat-1	2018 99 AF	2018 Dec 3.774			2018 Dec 6.83	97.76	96.32	6960	573	590	0.001	252

[43787]

Flock 3s-03	2018 99 AG  2018 Dec 3.774	3U cube	0.30x0.10	2018 Dec 6.76	97.77	96.32	6960	573	590	0.001	249

(Dove 210D)	[43788]		+2 panels	x0.10

5	0.70 span

Eaglet-1	2018 99 AJ 	2018 Dec 3.774	3U+ cubesat	0.34?x0.10	2018 Dec 6.65	97.77	93.28	6959	572	589	0.001	253

[43790]		+2 panels	x0.10

0.50 span

Capella-1	2018 99 AK 	2018 Dec 3.774	12U cubesat	0.20x0.20	2018 Dec 6.76	97.77	96.28	6959	573	588	0.001	259

[43791]		+2 panels	x0.30

+ SAR antenna	0.60 span

ESEO	2018 99 AL 	2018 Dec 3.774	Box	0.63x0.33	2018 Dec 6.71	97.77	96.28	6959	573	588	0.001	258

[43792]		44	0.33

CISM-FD	2018 99 AM 	2018 Dec 3.774	6U Cubesat	0.30x0.20	2018 Dec 6.83	97.76	96.28	6959	573	588	0.001	254

[43793]		+2 panels	x0.10

1.30 span

Hawk-B	2018 99 AN 	2018 Dec 3.774	Box		2018 Dec 6.83	97.77	96.28	6959	573	587	0.001	258

[43794]		13.4

Orbweaver 1	2018 99 AP	2018 Dec 3.774			2018 Dec 6.70	97.76	96.28	6959	572	588	0.001	258

[43795]

THEA	2018 99 AQ 	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 6.83	97.77	96.27	6959	571	589	0.001	236

[43]			x0.10

SkySat-C12	2018 99 AR  2018 Dec 3.774	Box		2018 Dec 6.70	97.77	96.27	6959	572	588	0.001	259

[43797]		120

Astrocast 0.1	2018 99 AS 	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 6.70	97.77	96.27	6959	572	587	0.001	234

[43]		+2 panels	x0.10

4	0.30 span

Hawk-C	2018 99 AT 	2018 Dec 3.774	Box		2018 Dec 6.76	97.76	96.27	6958	572	587	0.001	261

[43799]		13.4

ICEYE-X2	2018 99 AU 	2018 Dec 3.774	Box +2panels		2018 Dec 10.78	97.77	96.32	6961	573	591	0.001	235

[43800]		80

SkySat-C13	2018 99 AW	2018 Dec 3.774	Box		2018 Dec 10.19	97.77	96.32	6961	575	589	0.001	232

[43802]		120

JY1-Sat	2018 99 AX  2018 Dec 3.774	1U cubesat	0.10 side	2018 Dec 10.64	97.77	96.30	6960	572	591	0.001	241

[43803]

Suomi100	2018 99 AY	2018 Dec 3.774	1U cubesat	0.10 side	2018 Dec 10.64	97.77	96.30	6960	572	591	0.001	239

[43804]		2

Eu:CROPIS	2018 99 BB 	2018 Dec 3.774	Cylinder		2018 Dec 10.64	97.77	96.30	6960	573	589	0.001	236

[43807]		+4 panels

ORS-7B	2018 99 BC 	2018 Dec 3.774	6U cubesat	0.30x0.10	2018 Dec 10.18	97.77	96.30	6960	574	588	0.001	246

(Polar Scout Yukon)	[43808]			x0.10

+2 panels	1.30 span

+ panel	0.60 span

Centauri-1	2018 99 BD 	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 10.18	97.77	96.30	6960	572	590	0.001	242

[43809]		+2 panels	x0.10

0.50 span

NEXTSat-1	2018 99 BF  2018 Dec 3.774	Box + panel		2018 Dec 10.51	97.77	96.30	6960	573	589	0.001	238

[43811]		~100

Global-2	2018 99 BG  2018 Dec 3.774	Box +2 panels		2018 Dec 9.64	97.77	96.30	6960	573	589	0.001	243

(BlackSky-2)	[43812]		55

BRIO	2018 99 BH 	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 10.64	97.77	96.28	6959	572	589	0.001	232

[43813]			x0.10

PW-Sat 2	2018 99 BJ 	2018 Dec 3.774	2U cubesat	0.20x0.10	2018 Dec 13.12	97.77	96.32	6961	574	591	0.001	236

[43814]		+2 panels	x0.10

+ dragsail	0.30 span

2	?? m2

FalconSat-6	2018 99 BK 	2018 Dec 3.774	Box		2018 Dec 13.72	97.77	96.30	6960	573	590	0.001	233

[43815]		181

SpaceBee 7	2018 99 BL 	2018 Dec 3.774	0.25U cubesat	0.025x0.10 	2018 Dec 13.45	97.77	96.30	6960	573	590x	0.001	215

[43816]		0.3	x0.10

SpaceBee 5	2018 99 BM 	2018 Dec 3.774	0.25U cubesat	0.025x0.10	2018 Dec 13.72	97.77	96.30	6960	573	589	0.001	216

[43817]		0.3	x0.10

SpaceBee 6	2018 99 BN 	2018 Dec 3.774	1U cubesat	0.025x0.10	2018 Dec 13.45	97.77	96.30	6960	573	590	0.001	219

[43818]		0.3	x0.10

eXCITe	2018 99 BP 	2018 Dec 3.774	14 HiSat		2018 Dec 13.79	97.77	96.30	6960	573	589	0.001	230

(PTB-1)	[43819]		satlets

+2 panels

Seahawk-1	2018 99 BQ 	2018 Dec 3.774	3U cubesat	0.30x0.10	2018 Dec 13.72	97.77	96.30	6960	573	589	0.001	228

[43820]			x0.10

+4 panels	0.70 span

Flock 3s-02	2018 99 BR 	2018 Dec 3.774	3U cube	0.30x0.10	2018 Dec 13.45	97.77	96.30	6960	572	590	0.001	231

(Dove 2151)	[43821]		+2 panels	x0.10

5	0.70 span

Al Farabi-2	2018   	2018 Dec 3.774

[43]

Audacy Zero	2018   	2018 Dec 3.774	3U cubesat	0.30x0.10

[43]		+2 panels	x0.10

4	0.54 span

SpaceBee-8	2018   	2018 Dec 3.774	0.25U cubesat	0.025x0.10

[43]		0.3	x0.10

Copper	2018   	2018 Dec 3.774

[43]

Elysium Star-2	2018   	2018 Dec 3.774	1U cubesat	0.10 side

[43]		1

ExseedSat-1	2018   	2018 Dec 3.774	1U cubesat	0.10 side

[43]		1

ICE-Cap	2018   	2018 Dec 3.774	6U cubesat	0.30x0.10

[43]		+ antenna boom	x0.10

IRVINE 02	2018   	2018 Dec 3.774	1U cubesat	0.10 side	Deployed from STPSat-5 on 2018 ??

[43]		1

ITASAT-1	2018   	2018 Dec 3.774	6U cubesat	0.30x0.10

[43]		8	x0.10

KNACKSAT	2018   	2018 Dec 3.774	1U cubesat	0.10 side

[43]		1.3

Orbital Reflector	2018   	2018 Dec 3.774	3U cubesat	0.30x0.10

(ORS 1)	[43]		+4 panels	x0.10

+ double	0.70 span

Pyramid	30 long

4

RAAF-M1	2018   	2018 Dec 3.774	3U cubesat	0.30x0.10

[43]			x0.10

+2 panels	~0.25 span

+ antennapanel	0.30 long

4

ROSE-1	2018   	2018 Dec 3.774	6U cubesat	0.30x0.10

[43]			x0.10

+2 panels	~0.40 span

SeeMe	2018   	2018 Dec 3.774	Box + Cyl		Attached to eXCITe till 2018 ?? ??

[43]		+ panel

~25

VisionCube-1	2018   	2018 Dec 3.774	2U cubesat	0.20x0.10

[43]		2	x0.10

WeissSat 1	2018   	2018 Dec 3.774	1U cubesat	0.10 side

[43]		1

Falcon 9 2nd stage	2018	2018 Dec 3.774	Cylinder	13 long	De-orbited and decayed at end of 1st orbit south of Hawaii.

with MPC	[NNA]		3900	3.66 dia

D	2018 Dec 3.84	97.77	96.32	6961	574	590	0.001	257

P	2018 Dec 6.65	97.77	96.33	6962	574	592	0.001	256

Q	2018 Dec 6.31	97.77	96.33	6961	574	591	0.001	248

T	2018 Dec 6.16	97.77	96.32	6961	573	592	0.001	239

X	2018 Dec 5.63	97.77	96.32	6961	573	592	0.001	255

AE	2018 Dec 6.70	97.77	96.32	6960	573	591	0.001	257

AH	2018 Dec 6.44	97.77	96.28	6959	571	591	0.001	252

AV	2018 Dec 10.64	97.76	96.30	6960	572	591	0.001	226

AZ	2018 Dec 10.64	97.77	96.30	6960	572	591	0.001	242

BA	2018 Dec 10.64	97.77	96.30	6960	572	591	0.001	240

BE	2018 Dec 10.38	97.76	96.30	6960	572	590	0.001	238

BS	2019 Feb 1.17	97.76	96.32	6961	570	594	0.002	60

The 1st stage made its 3rd flight and soft-landed at the JRTI drone ship in the Pacific Ocean just 30 miles offshore of Vandenberg.

The satellites are launched atop the Falcon-9 2nd stage using the IPS (Integrated Payload Stack) that is formed by 4 major components:

- UFF (Upper Free Flyer) consists 4 primary structural elements:

- ESPA (EELV Secondary Payload Adapter) is an aluminium ring with 6x 15” ports for Microsats and Cubesats

- CubeStack is an aluminium flat cylinder and houses the avionics of UFF and has 5x 6UCubesat dispensers

- Hub is a composite ring similar to ESPA with 6x 24” ports for Microsats

- Top of MPC

- LFF (Lower Free Flyer) is a hexagonal aluminium structure and houses the LFF avionics and 12x 12U Cubesat dispensers. It is launched inside the MPC and

was deployed after the Microsats from the MPC were deployed.

- MPC (Multy Payload Carrier) with 4 platforms for Microsats

- Bottom of MPC remains attached to PAF Flacon 9 Payload Attach Fitting that remains attached to the Falcon-9 2nd stage.

The 71 payloads of SSO-A (Sun Sychronous Orbit – A):SmallSat Express in alphabetical order:

Yellow marked are sats that were not ready for the launch; replaced with ballast weight to keep the same mass distribution at launch.

Blue marked are sats believed to be on board according to an article on Spaceflightnow.com

• AISTechSat 2 for Earth observation of AISTech (Access to Intelligent Space Technologies), Barcelona, Spain.

• Al Farabi-2, a CubeSat technology demonstration mission of the Al-Farabi Kazakh National University, Kazakhstan.

• Astrocast, a technology demonstration mission of Astrocast, Switzerland, dedicated to the Internet of Things (IoT)

• Audacy Zero, a 3U CubeSat technology demonstration mission of Audacy, Mountain View, CA

• BeeSat-5 to -8 (Berlin Experimental and Educational Satellite) of TU Berlin, a picosatellite mission consisting of four 0.25 CubeSats.

. Blackhawk fron Viasat

• BlackSky-2, a microsatellite (55 kg) of BlackSky Global which will provide 1 m resolution imagery with improved geolocation accuracy.

• BRIO, a 3U CubeSat of SpaceQuest Ltd. of Fairfax, VA to test a novel communications protocol that uses SDR (Software Defined Radio).

• Capella-1, a 12U CubeSat of Capella Space, San Francisco, CA featuring a X-band SAR (Synthetic Aperture) payload.

• Centauri-2, a 3U CubeSat of Fleet Space Technologies, Adelaide, South Australia. Demonstration of IoT technologies.

• COPPER (Close Orbiting Propellant Plume and Elemental Recognition) CubeSat of Saint Louis University, Saint Louis, MO, USA.

• CSIM-FD (Compact Spectral Irradiance Monitor-Flight Demonstration), a 6U CubeSat of LASP (Laboratory for Atmospheric and Space Physics) at the University of Boulder, CO, USA. The goal is to measure solar spectral irradiance to understand how solar variability impacts the Earth's climate and to validate climate model sensitivity to spectrally varying solar forcing.

• Eaglet-1, the first 3U CubeSat of OHB Italia SpA for Earth Observation.

• Elysium Star-2, a 1U CubeSat of Elysium Space providing space burial services. Remained attached to LFF.

. Enoch from Los Angeles County Museum of Art is a golden statue in a 3U cube sledge.

• ESEO (European Student Earth Orbiter) sponsored by ESA, a microsatellite of ~40 kg with 6 instruments aboard.

• Eu:CROPIS (Euglena and Combined Regenerative Organic-Food Production in Space), a minisatellite (250 kg) of DLR, Germany. The objective is to study food production in space in support of future long-duration manned space missions (life sciences). The main payloads are two greenhouses, each maintained as a pressurized closed loop system, simulating the environmental conditions of the Moon or of Mars.

• eXCITe (eXperiment for Cellular Integration Technology aka Payload Test Bed 1), a DARPA (Defense Advanced Research Projects Agency) mission to demonstrate the 'satlets' technology. Satlets are a new low-cost, modular satellite architecture that can scale almost infinitely. Satlets are small modules that incorporate multiple essential satellite functions and share data, power and thermal management capabilities. Satlets physically aggregate in different combinations that would provide capabilities to accomplish diverse missions. It carries the SeeMe satellite to be deployed some time after launch.

• ExseedSat-1, a 1U CubeSat mission by the Indian company Exseed Space. The goal is to provide a multifunction UHF/VHF NBFM (Narrow Band Frequency Modulation) amateur communication satellite.

• FalconSat-6, a minisatellite (181 kg) of the USAFA (U.S. Air Force Academy) and sponsored by AFRL. FalconSat-6 hosts a suite of five payloads to address key AFSPC (Air Force Space Command) needs: SSA (Space Situational Awareness) and the need to mature pervasive technologies such as propulsion, solar arrays, and low power communications.

• Flock-3s 1, 2 and 3, three 3U CubeSats of Planet Labs to provide Earth observation.

• Fox-1C, a radio amateur and technology research 1U CubeSat developed by AMSAT and hosting several university developed payloads. Renamed to AO-95 after reaching orbit. It is a “spare” satellite from the 2015 launched CubeSat AO-85.

• Hawkeye, a formation-flying cluster of three microsatellites (13.4 kg each) of HawkEye 360, Herndon, VA, USA. The goal is to demonstrate high-precision RFI (Radio Frequency Interference) geolocation technology monitoring.

• Hiber-2 is 6U CubeSat pathfinder mission of Hiber Global, Noordwijk, The Netherlands, for Hiber Global's planned (IoT) communications CubeSat constellation.

• ICE-Cap (Integrated Communications Extension Capability), a 3U CubeSat of the US Navy. The objectives are to demonstrate a cross-link from LEO (Low Earth Orbit) to MUOS (Mobile User Objective System) WCDMA (Wideband Code Division Multiple Access) in GEO (Geosynchronous Orbit). The objective is to send to users on secure networks. ICE-Cap will deploy a ~0.5 m long boom with antennae.

• ICEYE-X2, a X-band SAR (Synthetic Aperture Radar) microsatellite (<100 kg) of Iceye Ltd, a commercial satellite startup company of Espoo, Finland.

. IRVINE 02 from Irvine Public School in California, USA with an electric propulsion system. Launched attached to STPSat-5 and deployed 2018 ??

• ITASAT-1 (Instituto Tecnológico de Aeronáutica Satellite), a Brazilian 6U Cubesat (~8kg) built by the Instituto Tecnológico de Aeronáutica (ITA). A former rescoped microsatellite mission.

• JY1-Sat, a 1U CubeSat of Jordan developed by students of various universities. The satellite will carry a UHF/VHF amateur radio.

. K2SAT from Korean Air Force Academy, South Korea.

. KazSciSat-1 from Ghalem LLP. Kazachstan.

• KazSTSAT (Kazakh Science and Technology Satellite), a microsatellite (105 kg) of Ghalam LLP, Astana, Kazakhstan. Developed by SSTL on a SSTL-50 platform including an SSTL EarthMapper payload designed for global commercial wide-area imaging with a resolution of 17.5 m on a swath of 250 km.

• KNACKSAT (KMUTNB Academic Challenge of Knowledge SATellite) of Thailand, a 1U technology demonstration CubeSat, the first entirely Thai-built satellite, developed by students of King Mongkut's University of Technology North Bangkok (KMUTNB). Use of an amateur radio for communication.

• Landmapper-BC (Corvus BC 4), a 6U CubeSat (11 kg) of Astro Digital (formerly Aquila Space), Santa Clara, CA, USA. The satellite features a broad coverage multispectral (Red, Green, NIR) imaging system with a resolution of 22 m.

• MinXSS-2 (Miniature X-ray Solar Spectrometer-2), a 3U CubeSat(4 kg) of LASP (Laboratory for Atmospheric and Space Physics) at the University of Colorado at Boulder,CO, USA. The objective is to study the energy distribution of solar flare SXR (Soft X-ray) emissions and its impact on the Earth's ITM (Ionosphere, Thermosphere, and Mesosphere) layers. — MinXSS-1 was launched on 06 December 2015 onboard of Cygnus CRS-4 to the ISS, were it was deployed into orbit on 16 May 2016. It reentered Earth's atmosphere on 6 May 2017.

. Move II from Technische Universität München, Germany.

• NEXTSat-1, a multi-purpose microsatellite (~100 kg) of Korea designed and developed at SaTReC (Satellite Technology Research Center) of KAIST (Korea Advanced Institute of Science and Technology). The goal is to conduct scientific missions such as star formation and space storm measurements and also technology demonstration in space. Instruments: ISSS (Instrument for the Study of Space Storms) developed at KAIST to detect plasma densities and particle fluxes of 10 MeV energy range near the Earth. NISS (NIR Imaging Spectrometer for Star formation history), developed at KASI (Korean Astronomy and Space Science Institute).

• Orbital Reflector, a 3U CubeSat project (4 kg) of the Nevada Museum of Art and artist Trevor Paylon. The Orbital Reflector is a 30 m sculpture constructed of a lightweight material similar to Mylar. On deployment, the sculpture self-inflates like a balloon. Sunlight reflects onto the sculpture making it visible from Earth with the naked eye — like a slowly moving artificial star as bright as a star in the Big Dipper.

• ORS-7 (Operationally Responsive Space 7), two 6U CubeSats (-7A and -7B) of the USCG (US Coast Guard) in cooperation with DHS (Department of Homeland Security), the ORS (Operationally Responsive Space Office) of DoD, and NOAA. The objective is to detect transmissions from EPIRBs (Emergency Position Indicating Radio Beacons), which are carried on board vessels to broadcast their position if in distress.

• PW-Sat 2 (Politechnika Warszawska Satellite 2), a 2U CubeSat of the Institute of Radioelectronics at the Warsaw University of Technology, Warsaw, Poland. The objective is to demonstrate a deorbitation system - a drag parachute opened behind the satellite - which allows faster removal of satellites from their orbit after it completes its mission.

• RAAF-M1 (Royal Australian Air Force-M1), an Australian 3U CubeSat (~4 kg) designed and built by UNSW (University of New South Wales) for the Australian Defence Force Academy, Royal Australian Air Force. RAAF-M1 is a technology demonstration featuring an AIS receiver, and ADS-B receiver, an SDR (Software Defined Radio).

• RANGE-A and -B (Ranging And Nanosatellite Guidance Experiment), two 1.5 CubeSats of Georgia Tech (Georgia Institute of Technology), Atlanta, GA, USA, flying in a leader-follower formation with the goal of improving the relative and absolute positioning capabilities of nanosatellites.

• ROSE-1, a 6U CubeSat of Phase Four Inc., El Segundo, CA, USA. ROSE-1 is an experimental spacecraft designed to provide an orbital test-bed for the Phase Four RFT (Radio Frequency Thruster), the first plasma propulsion system to fly on a nanosatellite.

• Spacewar-Cal-O, -R and –OR; 3 calibration cubsats for the US Navvy Space and Naval Warfare Systems Command to calibrate space tracking systems.

• SeaHawk, two 3U CubeSats of UNCW (University of North Carolina, Wilmington), NC. The goal is to measure the ocean color in project SOCON (Sustained Ocean Observation from Nanosatellites). They are considered prototypes for a larger constellation. The SOCON project is a collaboration between Clyde Space Ltd (spacecraft bus), the University of North Carolina Wilmington, Cloudland Instruments, and NASA/GSFC (Goddard Space Flight Center).

• SeeMe (Space Enabled Effects for Military Engagements)is a DARPA satellite to get satellite imagery on-demand for pre-mission planning. It is launched atop the eXICTe satellite and released some time after launch.

. Sirion Pathfinder 2 from Sirion Global, Australia

• SkySat-14 and -15. Planet of San Francisco has 13 SkySats in orbit. The commercial EO satellites were built by Terra Bella of Mountain View, CA, which Planet acquired from Google last year. At the time of the purchase, there were 7 SkySats in orbit. On 31 October 2017, Planet launched an additional six on a Minotaur-C rocket. The 100 kg SkySats are capable of sub-meter resolution – making them the most powerful in the constellation. Customers can request to have these high-resolution satellites target their locations of interest.

• SNUGLITE, a 2U CubeSat designed by the SNU (Seoul National University) for technology demonstrations and amateur radio communication.

. SNUSAT-2 fron Seoul National University, South Korea

• SpaceBEE, four picosatellites of Swarm Technologies (a US start-up), built to the 0.25U form factor to make up a 1U CubeSat.

• STPSat-5 is a science technology minisatellite of the US DoD STP (Space Test Program), managed by the SMC of the USAF. STPSat-5 will carry a total of five technological or scientific payloads to LEO (Low Earth Orbit) in order to further the DoD's understanding of the space environment. The satellite was built by SNC (Sierra Nevada Corporation) on the modular SN-50 bus with a payload capacity of 50-100 kg and compatible with ESPA-class secondary launch adaptors.

. SUOMI 100 from Aalto University Science and Technology, Finland to test a wide-view high detail camera and a low frequency receiver.

• THEA, a 3U CubeSat built by SpaceQuest, Ltd. of Fairfax, VA to demonstrate a spectrum survey payload developed by Aurora Insight, Washington DC. The objective is to qualify Aurora's payload, consisting of a proprietary spectrometer and components, and demonstrate the generation of relevant measurements of the spectral environment (UHF, VHF, S-band). The results of the experiment will inform future development of advanced instrumentation by Aurora and component development by SpaceQuest.

• VESTA (VdES Transmitting sAtellite system) is a 3U CubeSat, 4 kg, developed at SSTL in Guildford, UK. VESTA is a technology demonstration mission that will test a new two-way VHF Data Exchange System (VDES) payload for the exactEarth advanced maritime satellite constellation. Honeywell Aerospace is providing the payload. VESTA is a flagship project of the National Space Technology Program, funded by the UK Space Agency and managed by the Center for EO Instrumentation and Space Technology (CEOI-ST).

• VisionCube-1, a 2U CubeSat designed by the Korea Aerospace University (KAU) to perform research on Transient Luminous Events in the upper atmosphere. The image processing payload consists of a multi-anode photon multiplier tube(MaPMT), a camera, and a real-time image processing engine built by using SoC (System-on-Chip) FPGA technologies.

. WeissSat 1 from the Weiss School in Palm Beach Gardens to collect and transmit sensor data and validate a novel lab-on-a-chip system. Launched attached to STPSat-5 and deployed 2018 ??

GEO-KOMPSAT 2A	2018 100 A	2018 Dec 4.859	Box + panel	2.4 x 3.8	2018 Dec 4.66	3.54	631.05	24371	244	35741	0.728	178

[Ariane 5 ECA]	[43823]	> million years	3420	x 4.6	2018 Dec 7.54	3.51	631.48	24382	244	35763	0.728	180

(VA 246)	KOU-ELA3			8.9 span	2018 Dec 9.24	1.09	852.78	29789	11175	35646	0.411	183

2018 Dec 9.65	0.33	1145.48	36265	24060	35713	0.161	191

2018 Dec 14.36	0.06	1430.47	42055	35606	35745	0.002	262

2018 Dec 17.64	0.03	1432.10	42087	35668	35748	0.0009	307

2018 Dec 21.62	0.04	1436.18	42166	35785	35791	0.00007	10

2018 Dec 27.97	0.02	1436.10	42165	35784	35789	0.00006	129

GSAT-11  #	2018 100 B	2018 Dec 4.859	Box +2 panels		2018 Dec 5.02	3.51	630.47	24356	241	35713	0.728	178

[43824]	> million years	5854		2018 Dec 6.67	2.06	725.75	26752	4999	35748	0.575	178

2018 Dec 7.63	0.97	909.67	31099	13650	35791	0.356	176

2018 Dec 9.71	0.14	1358.08	40623	32637	35853	0.040	143

2018 Dec 10.62	0.08	1430.25	42050	35497	35846	0.004	108

2018 Dec 15.81	0.07	1432.08	42086	35603	35812	0.002	113

2018 Dec 17.79	0.07	1434.53	42134	35698	35813	0.001	117

2018 Dec 19.61	0.07	1436.27	42168	35766	35814	0.0006	127

2018 Dec 21.54	0.06	1436.80	42179	35783	35817	0.0004	131

2018 Dec 23.54	0.06	1436.10	42165	35778	35794	0.0002	179

Ariane 5 2nd stage	2018 100 C	2018 Dec 4.859	Cylinder	5.84 long	2018 Dec 5.00	3.49	631.22	24375	241	35752	0.728	178

(ESC-A + VEB)	[43825]		5668	5.4 dia

Sylda upperpart	2018 100 D	2018 Dec 4.859	Barrel	6.4 high	2018 Dec 4.92	3.56	629.83	24339	281	35640	0.726	178

[43826]		~ 530

#	Indian communication satellite at 74° East over the equator.

*	South Korean meteorological and space weather monitoring satellite at 128.2° East over the equator.

D	Dragon CRS-16 *	2018 101 A	2018 Dec 5.761	Blunt cone	4.4 high	2018 Dec 5.76	51.63	90.13	6659	204	357	0.012	46

R	[Falcon 95] #	[43827]	38.456 days	+ cylinder	3.66 dia	2018 Dec 8.42	51.64	92.65	6783	401	408	0.0005	124

(F9-065, B1050)	CC-LC40	2019 Jan 13.217	+ 2 panels	2.8 high 	2019 Jan 13.59	51.64	92.67	6784	404	407	0.0002	284

~ 8200 full	16.5 span

2647 cargo

D	Fragments	2018 101 B-D  3 pieces, orbital have decayed

*	Dragon CRS-16 rendez-vouzed with ISS and was grappled 2018 Dec 8.515 by the stations robotic arm. Berthed 2018 Dec 8. to the nadir port of Harmony.

Unbearthed and 2019 Jan 12.981 released from the stations robotic arm. The capsule landed in the Pacific Ocean southeast of Guadalupe Island west of

the coast of Baja California

#	The booster, in use for the first time, experienced a grid fin hydraulic pump stall on reentry, which caused it to spin out of control and touchdown at sea, heavily damaging the interstage section; this was the first failed landing targeted for a ground pad at CC.

SaudiSat 5A *1	2018 102 A	2018 Dec 7.175	Box 		2018 Dec 7.37	97.63	95.50	6921	534	551	0.001	260

[43831]		425

JIUQ-LC43/94

SaudiSat 5B *1	2018 102 C	2018 Dec 7.175	Box		2018 Dec 7.70	97.63	95.47	6920	532	551	0.001	278

[43832]		425

Piao Chong 1  *2	2018 102	2018 Dec 7.175

[438]

Piao Chong 2  *2	2018 102	2018 Dec 7.175

[438]

Piao Chong 3  *2	2018 102	2018 Dec 7.175

[438]

Piao Chong 4  *2	2018 102	2018 Dec 7.175

[438]

Piao Chong 5  *2	2018 102	2018 Dec 7.175

[438]

Piao Chong 6  *2	2018 102	2018 Dec 7.175

[438]

Tianyi X 1 *3	2018 102	2018 Dec 7.175

[438]

Tianyi X 2 *3	2018 102	2018 Dec 7.175

[438]

Tianyi X 3 *3	2018 102	2018 Dec 7.175

[438]

Weina 1-03  *4	2018 102	2018 Dec 7.175

[438]

CZ-2D 2nd stage	2018 102	2018 Dec 7.175	Cylinder	10.9 long

[NNA]		4000	3.35 dia

B	2018 Dec 7.70	97.63	95.47	6920	532	551	0.001	269

D	2018 Dec 7.70	97.63	95.47	6920	532	551	0.001	278

E	2018 Dec 7.70	97.63	95.47	6919	531	550	0.001	271

F	2018 Dec 7.70	97.62	95.45	6919	531	550	0.001	279

G	2018 Dec 7.70	97.63	95.43	6918	530	549	0.001	284

H	2018 Dec 7.70	97.63	95.43	6918	529	550	0.002	265

J	2018 Dec 7.70	97.64	95.42	6918	528	550	0.002	286

K	2018 Dec 7.70	97.63	95.42	6918	529	549	0.001	284

L	2018 Dec 7.70	97.63	95.42	6917	528	549	0.001	285

M	2018 Dec 7.70	97.60	95.40	6917	532	544	0.0008	325

N	2018 Dec 7.70	97.63	95.38	6916	527	548	0.002	294

P	2018 Dec 7.98	97.65	95.37	6915	530	542	0.0009	26

*1	Two Earth observation satellites from Saudi Arabia.

*2	Piao Chong means Lady Bird

*3

*4

D	Chang`e 4 *	2018 103 A	2018 Dec 7.766	Box + legs		2018 Dec 7.77	28.88	89.90	6648	263	276	0.001	103

R	[CZ-3B]	[43845]	25.335 days	3800 full		2018 Dec 7.8?	29.4			200	420000

XI	2019 Jan 2.101	1200 (lander)		2018 Dec 12.36				100	129			$

140 (rover)		2018 Dec 30.038				15	100			$

CZ-3B 3rd stage #	2018 103 B	2018 Dec 7.766	Cylinder	12.38 long	2018 Dec 7.77	28.88	89.90	6648	263	276	0.001	103

(Y30)	[43846]		2740	3.0 dia 	2018 Dec 7.8?	29.4			200	390000

2018 Dec 12	23.6			181000	735800

*	Chinese lunar probe with lander and a rover. Softlanded 2019 Jan 2.101 on far side of the moon in the Von Kármán crater at 177.6°E, 45.5°S.

Communications via the Queqiao satellite, launched 2018 May 20, and stationed around the Earth-Moon L2 point. Deployed 2019 Jan 3.599 the Yuti-2 rover.

#	The 2nd stage passed by the moon 2018 Dec 12.485 at 4840 km and entered an orbit around the Earth-Moon system.

$	Lunar orbit

Aerocube 11-	2018 104 A	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.32	85.02	91.72	6737	209	509	0.022	228

TOMSat R3	[43849]			x0.10	2018 Dec 17.62	85.04	94.65	6880	491	512	0.002	287

[Electron]	MAH-LC1

(This One’s for

Pickering) #

Shields-1	2018 104 B	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.38	85.04	94.67	6881	493	511	0.001	287

[43850]			x0.10	2018 Dec 17.75	85.03	94.67	6881	494	511	0.001	286

Electron Curie	2018 104 C	2018 Dec 16.273			2018 Dec 16.51	85.03	94.65	6880	491	511	0.001	287

Kick stage	[43851]

STF-1	2018 104 D	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 12.51	85.03	94.70	6883	498	510	0.0009	282

[43852]		4	x0.10	2018 Dec 17.35	85.03	94.72	6883	496	514	0.001	303

CHOMPTT	2018 104 G	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.70	85.04	94.60	6878	489	510	0.002	274

[43855]		1	x0.10	2018 Dec 17.22	85.04	94.60	6878	488	510	0.002	270

DaVinci	2018 104 J	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.92	85.04	94.70	6882	494	514	0.001	301

[43857]		+2 panels	x0.10

4	0.54 span

GOERGEN	2018 104 M	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.79	85.04	94.68	6882	495	511	0.001	295

(SHFT-1)	[43860]			x0.10

+ panel	0.30 ??

5

Aerocube 11-	2018 104 N	2018 Dec 16.273	3U Cubesat	0.34x0.10	2018 Dec 16.72	85.05	94.67	6881	492	512	0.001	288

EagleScout	[43861]			x0.10

TOMSat

D	Electron 3rd stage	2018 104 Q	2018 Dec 16.273	Truncated cone	?? long	2018 Dec 17.04	85.04	94.65	6880	491	513	0.002	288

[43863]	45 days		1-1.2 dia	2018 Dec 17.64	85.03	91.70	6737	210	507	0.022	224

2019 Jan 30			2019 Jan 30.41	84.99	87.17	6512	122	146	0.002	42

CeREs	2018 104	2018 Dec 16.273	3U Cubesat	0.34x0.10

x0.10

CubeSail	2018 104 	2018 Dec 16.273	2x1.5U cube	2x 0.15

x0.10x0.10

+ sail	0.077x260

NMTsat	2018 104 	2018 Dec 16.273	3U Cubesat	0.34x0.10

4	x0.10

RSat-P	2018 104	2018 Dec 16.273	3U Cubesat	0.34x0.10

x0.10

+2 arms	0.60 long

ISX	2018 104 	2018 Dec 16.273	3U Cubesat	0.34x0.10

4	x0.10

ALBus	2018 104 	2018 Dec 16.273	3U Cubesat	0.34x0.10

x0.10

+ 4 panels	0.30 long

5

E	2018 Dec 16.56	85.03	94.63	6879	489	511	0.002	283

F	2018 Dec 16.56	85.03	94.62	6878	489	510	0.002	272

H	2018 Dec 16.78	85.04	94.73	6884	497	515	0.001	311

K	2018 Dec 16.84	85.04	94.68	6882	493	513	0.001	296

L	2018 Dec 16.84	85.03	94.68	6882	495	511	0.001	293

P	2018 Dec 16.99	85.03	94.65	6880	491	512	0.002	287

#  In honor of  the late New Zealand-born scientist William Pickering, who was director of the Jet Propulsion Laboratory in California for 22 years until his retirement in 1976.

• CeREs (Compact Radiation Belt Explorer) of NASA/GSFC. The satellite is to measure radiation belt energization and loss electron spectra, and microbursts. A secondary objective is to measure solar electron spectra from > 5 keV. The instrument is MERiT (Miniaturized Electron and Proton Telescope).

• STF-1 (Simulation to Flight 1) of NASA/GSFC. STF-1 is a collaboration with West Virginia Space Grant Consortium (WVSGC) and West Virginia University (WVU) to demonstrate the utility of the NASA Operational Simulator (NOS) technologies across the CubeSat development cycle, from concept planning to mission operations.

• CubeSail two identical CubeSats for upper atmospheric research of the University of Illinois at Urbana-Champaign. The two satellites are launched as a unit, detumbled, and separated, with the 0.077x260 m, 20 m2 film unwinding symmetrically from motorized reels.

• CHOMPTT (CubeSat Handling Of Multisystem Precision Time Transfer) of the University of Florida to demonstrate nanosecond-level time transfer from Earth to a LEO CubeSat. Precision timing is a critical for satellite navigation systems, including GPS.

• NMTSat of New Mexico Institute of Mining and Technology to monitor space weather in low Earth orbit and correlate this data with results from structural and electrical health monitoring systems.

• DaVinci of North Idaho STEM Charter Academy for teaching students about radio waves, aeronautical engineering, space propulsion, and geography by sending a communication signal to schools around the world.

• RSat-P of USNA (U.S. Naval Academy). The goal is to demonstrate capabilities for in-orbit repair systems.

• ISX (Ionospheric Scintillation Explorer of California Polytechnic State University. ISX is a space weather investigation to better understand the physics of naturally occurring Equatorial Spread F ionospheric irregularities by deploying a passive ultra-high frequency radio scintillation receiver.

• Shields-1 of NASA/LaRC (Langley Research Center) with a radiation shielding research payload. A technology demonstration of environmentally durable space hardware to increase the technology readiness level of new commercial hardware through performance validation in the relevant space environment.

• ALBus (Advanced eLectrical Bus of NASA/GRC (Glenn Research Center). It is a technology demonstration mission of an advanced, digitally controlled electrical power system capability and novel use of Shape Memory Alloy technology for reliable deployable solar array mechanisms. The goals of the mission are to demonstrate: efficient battery charging in the orbital environment, 100 Watt distribution to a target electrical load, flexible power system distribution interfaces, adaptation of power system control on orbit, and successful deployment of solar arrays and antennas utilizing resettable shape memory alloy mechanisms.

• SHFT-1, Space-based High Frequency Testbed, of NASA/JPL (Jet Propulsion Laboratory) to collect radio frequency signals in the HF (5-30 MHz) band to study the galactic background emissions, the HF signals from Jupiter, and the signals from terrestrial transmitters after having passed through the Earth's ionosphere.

. TOMSat EagleScoutfrom Aerospace Corp. USA to test miniaturized imager.

. TOMSat R3 Aerospace Corp. USA to test miniaturized imager.

GSAT 7A #	2018 105 A 	2018 Dec 19.445	Box		2018 Dec 19.22	19.42	692.27	25923	154	38934	0.748	178

[GSLV Mk.2]	[43864]	> million years	+2 panels		2018 Dec 20.65	5.92	934.47	31662	11621	38946	0.432	178

(F11)	SRI-LP2		2250		2018 Dec 26.68	0.16	1591.87	45161	35552	42013	0.072	107

2018 Dec 27.89	0.18	1440.32	42248	35792	35945	0.002	76

2018 Jan 1.93	0.17	1436.12	42165	35776	35797	0.0002	7

2018 Jan 12.90	0.15	1436.07	42164	35776	35795	0.0002	359

D	GSLV 3rd stage	2018 105 B	2018 Dec 19.445	Cylinder	8.7 long	2018 Dec 19.23	19.45	689.00	25841	153	38771	0.747	178

[43865]	107 days	~2500	2.8 dia	2019 Apr 5.28	19.41	91.15	6710	95	567	0.035	297

2019 Apr 5

#	Indian military communication satellite at 63° East over the equator.

CSO 1  *	2018 106 A	2018 Dec 19.693	Octagonal Cyl		No TLE’s issued. Orbits from amateur observations.

[Soyuz ST-B/Fregat]	[43866]				2020 Sep 29.13	98.63	100.92	7181	801	804	0.0002	38

(VS 20)	KOU-ELS		+ 4 panels

3565

Fregat upperstage	2018 106 B	2018 Dec 19.693	Torus+spheres	1.85 high

[NNA]		930	3.35 dia

*	Composante Spatiale Optique military reconnaissance satellite for France.

Cosmos 2533  *	2018 107 A	2018 Dec 21.015			2018 Dec 22.07	0.19	1423.97	41927	35349	35748	0.005	175

(Blagovest No. 13L)	[43867]				2018 Dec 29.62	0.17	1427.15	41990	35421	35801	0.004	178

[Proton-M/Breeze-M]	BAI

Breeze-M stage	2018 107 B	2018 Dec 21.015	Cylinder	2.61 long	2018 Dec 27.62	0.16	1591.85	45161	35553	42011	0.071	107

[43868]		+ spheres	2.49 dia

Breeze-M tank	2018 107 C	2018 Dec 21.05	Torus	0.80 cross	2018 Dec 21.61	48.67	633.05	24422	400	35687	0.722	0

[43869]			4.0 dia

*	Russian military communication satellite.

Hongyun 1	2018 108 A 2018 Dec 21.994			2018 Dec 22.06	99.92	106.58	7447	1065	1072	0.0005	292

[CZ-11]	[43871]

JIUQ-SLS-E2

CZ-11 3rd stage	2018 108 B	2018 Dec 21.994	Cylinder		2018 Dec 22.13	100.43	102.78	7269	641	1139	0.034	323

[43872]

*	Chinese techno demo satellite for the Hongyun network of up to 156 satellites for global internet connectivity.

GPS 3-01(Vespucci)*	2018 109 A 	2018 Dec 23.577	Box +2 panels		2018 Dec 23.65	55.01	310.05	17074	1192	20199	0.557	270

(Navstar 77, USA289)	[43873]	1 million years			2019 Jan 4.00	54.93	717.90	26559	20171	20189	0.0003	276

[Falcon 9 b5] #	CC-LC40		4400		2019 Jan 7.32	55.00	717.93	26560	20167	20195	0.0005	270

(F9-066, B1054)

D	Falcon 9 2nd stage	2018	2018 Dec 23.577	Cylinder	13 long	De-orbited

[NNA]	~ 0.1 day	3900	3.66 dia

2018 Dec 23.67

*	USA Navigation satellite (SVN 74) to replace GPS 2R-2 (SVN 43).

#	The new 1st stage will not make a landing as all the fuel was needed for the launch of the heavy satellite and 2nd stage and the 55° inclination.

Also to save some fuel for the de-orbit burn of the 2nd stage after satellite release at 1h56min after launch.

TJS-3  *	2018 110 A	2018 Dec 24.703			2018 Dec 24.79	28.50	631.17	24374	180	35811	0.731	179

[CZ-3C]	[43874]	> million years			2018 Dec 26.32	28.48	630.47	24356	179	35776	0.731	180

XI				2018 Dec 31.62	0.11	1436.08	42165	35777	35795	0.0002	320

2018 Dec 31.96	0.11	1436.07	42164	35778	35793	0.0002	318

CZ-3C 3rd stage	2018 110 B	2018 Dec 24.703	Cylinder	12.38 long	2018 Dec 24.81	46	621.12	24115	232	35240	0.726	180

[43875]		740	3.0 dia

TJS-3 AKM	2018 110 C	2018 Dec 24.703			2018 Dec	0.10	1438.09		35788	35864	from SATCAT

[43917]	> million years

*	Tongxin Jishu Shiyan is a Chinese geostationary satellite to test technology.

Kanopus-V 5 *1	2018 111 A	2018 Dec 27.088	Box +2 panels		2018 Dec 27.43	97.47	94.77	6886	503	511	0.0005	84

[Soyuz 2-1a/	[43876]		473

Fregat M]	VOS-LC1S

Kanopus-V 6 *1	2018 111 B	2018 Dec 27.088	Box +2 panels		2018 Dec 27.43	97.47	94.72	6883	498	511	0.0009	86

[43877]		473

iSat   *7	2018 111 D	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.72	96.25	6958	571	588	0.001	241

[43879]			x0.10

UWE-4 *9	2018 111 E	2018 Dec 27.088	1U cube	0.10 side	2018 Dec 27.55	97.73	96.25	6957	571	586	0.001	243

[43880]		1

D-Star ONE Sparrow*8	2018 111 F	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.73	96.23	6957	571	586	0.001	239

[43881]

Lemur-2   *6	2018 111 G	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.73	96.23	6957	571	586	0.001	239

ChristinaHolt	[43882]		+2 panels	x0.10

5	0.56 span

Lemur-2   *6	2018 111 H	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.73	96.23	6956	571	585	0.001	243

Tinykev	[43883]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 J	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.72	96.22	6956	568	588	0.001	225

Remy-Colton	[43884]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 K	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.55	97.73	96.22	6956	570	585	0.001	241

Gustavo	[43885]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 L	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.41	97.73	96.22	6956	570	585	0.001	237

ZO	[43886]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 M	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.41	97.73	96.22	6956	570	584	0.001	237

NatalieMurray	[43887]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 N	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.41	97.73	96.20	6955	569	584	0.001	222

SarahBethTyboo	[43888]		+2 panels	x0.10

5	0.56 span

Lemur-2  *6	2018 111 P	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.41	97.73	96.20	6955	569	584	0.001	236

Daisy-Harper	[43889]		+2 panels	x0.10

5	0.56 span

GRUS-1   *2	2018 111 Q	2018 Dec 27.088	Box		2018 Dec 27.41	97.73	96.20	6955	571	582	0.0008	255

[43890]		110

Flock 3k-03   *3	2018 111 S 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6874	480	511	0.002	246

[43892]		+2 panels	x0.10

5	0.70 span

Flock 3k-04   *3	2018 111 T 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6874	479	511	0.002	246

[43893]		+2 panels	x0.10

5	0.70 span

Flock 3k-01   *3	2018 111 U 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6874	479	511	0.002	245

[43894]		+2 panels	x0.10

5	0.70 span

Flock 3k-02   *3	2018 111 V 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6874	479	511	0.002	245

[43895]		+2 panels	x0.10

5	0.70 span

Flock 3k-06   *3	2018 111 W 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6873	480	509	0.002	241

[4396]		+2 panels	x0.10

5	0.70 span

Flock 3k-05   *3	2018 111 Z 	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.52	6873	480	509	0.002	245

[43899]		+2 panels	x0.10

5	0.70 span

Flock 3k-08   *3	2018 111 AB	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6873	480	509	0.002	242

[43901]		+2 panels	x0.10

5	0.70 span

Flock 3k-07   *3	2018 111 AC	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6873	480	509	0.002	241

[43902]		+2 panels	x0.10

5	0.70 span

Flock 3k-12   *3	2018 111 AD	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6873	480	509	0.002	241

[43903]		+2 panels	x0.10

5	0.70 span

Flock 3k-11   *3	2018 111 AE	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6873	480	508	0.002	241

[43904]		+2 panels	x0.10

5	0.70 span

Flock 3k-10   *3	2018 111 AF	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6873	480	508	0.002	241

[43905]		+2 panels	x0.10

5	0.70 span

Flock 3k-09   *3	2018 111 AG	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.50	6872	479	508	0.002	240

[43906]		+2 panels	x0.10

5	0.70 span

ZACube-2   *4	2018 111 AH	2018 Dec 27.088	3U cube	0.30x0.10	2018 Dec 27.49	97.30	94.48	6872	479	507	0.002	241

+2 panels	x0.10

4	0.70 span

Lume 1   *5	2018 111 AJ	2018 Dec 27.088	2U cube	0.20x0.10	2018 Dec 27.49	97.30	94.48	6872	480	507	0.002	243

[43908]		2	X0.10

Fregat M stage 	2018 	2018 Dec 27	Torus+spheres	1.85 high	After Kanopus deploy Fregat made two burns before releasing the secondary

[NNA]		930	3.35 dia	payloads and was then de-orbited.

C	2018 Dec 27.43	97.58	95.15	6905	489	563	0.005	24

R	2018 Dec 27.49	97.30	94.55	6875	480	514	0.003	244

X	2018 Dec 27.49	97.30	94.50	6873	480	509	0.002	243

Y	2018 Dec 27.49	97.30	94.50	6873	480	510	0.002	243

AA	2018 Dec 27.49	97.30	94.50	6873	480	509	0.002	242

*1	Two Russian earth observation satellites.

*2	Earth imaging satellite from Axelspace, Japan

*3	12 imaging satellites from Planet Lab

*4	ZACube-2 (South African CubeSat-2), a 3U CubeSat of F'SATI (French South African Institute of Technology) at CPUT (Cape Peninsula University of Technology), Cape Town, South Africa (in collaboration with SANSA and Stellenbosch University).The payloads include a medium resolution matrix imager and a number of communication subsystems. The prime objective of ZACUBE-2 is to demonstrate AIS (Automatic Identification System) message reception using its SDR-based payload and to detect wildfires. The launch of ZACube was planned for 2018 on an Indian PSLV rocket but has been moved to a Falcon-9 and again moved to a Soyuz 2-1a rocket from Vostochny.

*5	Developed by a consortium of European universities and research institutions led by Spain’s University of Vigo. Lume carries a communications payload that will relay signals from sensors on the ground that have been placed to detect fires. The satellite can also relay data collected by drones sent to investigate alerts from these sensors, improving advance warning of wildfires breaking out.

*6	Eight Lemur-2 satellites for Spire Global. The Lemur spacecraft each carry two instruments: STRATOS uses GPS occultation to measure atmospheric conditions, including pressure, temperature and humidity. SENSE collects and relays Automatic Identification System (AIS) signals from ships at sea.

*7	From iSKY Technology, Czech Republic and it is equipped with an ADS-B received to relay tracking data from aircraft.

*8 From German Orbital Systems and it carries technology demonstration and amateur radio payloads.

*9	From the University of Wurzburg, the UWE-4 will test a miniaturized electric propulsion system with Nano Field Effect Electric Propulsion (NanoFEEP) thrusters.

Yunhai 2-01 *	2018 112 A	2018 Dec 29.333			2018 Dec 29.53	50.01	95.03	6899	517	524	0.0006	250

[CZ-2D]	[43909]

JIUQ

Yunhai 2-02	2018 112 B	2018 Dec 29.333			2018 Dec 29.53	50.01	95.02	6898	514	524	0.0007	264

[43910]

Yunhai 2-03	2018 112 C	2018 Dec 29.333			2018 Dec 29.53	50.01	94.95	6894	508	524	0.001	273

[43911]

Yunhai 2-04	2018 112 D	2018 Dec 29.333			2018 Dec 29.62	50.01	107.12	7471	1088	1098	0.0006	263

[43912]

Yunhai 2-05	2018 112 E	2018 Dec 29.333			2018 Dec 29.62	50.00	107.14	7473	1090	1098	0.0005	245

[43913]

Hongyan 1 **	2018 112 F	2018 Dec 29.333			2018 Dec 29.67	50.00	107.17	7474	1090	1100	0.0006	228

[43914]

Yunhai 2-06	2018 112 G	2018 Dec 29.333			2018 Dec 29.62	50.01	107.17	7474	1092	1099	0.0005	221

[43915]

D	CZ-2D 2nd stage	2018 112 H	2018 Dec 29.333			2018 Dec 29.52	50.00	88.30	6569	185	196	0.0009	328

[43916]	3 day			2018 Dec 29.87	50.00	88.23	6566	182	192	0.0008	324

2019 Jan 1

Yuanzheng 3 #	2018 112

Upperstage	[NNA]

*	Chinese atmospheric research satellites

**	Hongyan test satellite

#	New variant of the Yuanzheng upperstage capable of restarting 20 times over a period of 2 days.

Superview-1 03 & 04 CZ-2D 2nd stage fragments; 4 pieces, all in orbit

2018 02 D	[43102]				2018 Jan 9.52	97.47	95.45	6919	528	553	0.002	131

2018 02 E	[43103]				2018 Jan 9.52	97.72	95.78	6935	530	582	0.004	189

2018 02 F	[43104]				2018 Jan 9.52	97.45	94.53	6875	458	534	0.006	331

2018 02 G	[43105]				2018 Jan 10.72	97.70	94.72	6883	472	537	0.005	309

LKW-3 CZ-2D 2nd stage fragments; 4 pieces, all in orbit

2018 06 B	[43147]				2018 Jan 14.62	97.24	94.63	6880	490	511	0.002	100

2018 06 C	[43148]				2018 Jan 14.59	97.31	94.37	6867	476	500	0.002	284

2018 06 D	[43149]				2018 Jan 14.59	97.37	94.20	6859	465	495	0.002	348

2018 06 E	[43150]				2018 Jan 14.61	97.45	93.90	6844	432	499	0.005	312

Asnaro-2 Epsilon r/b fragment; 1 piece, it has decayed

D	2018 07 C	[43154]	2018 Jul 17			2018 Jan 18.00	97.80	93.32	6816	230	644	0.030	160

CZ-2D fragments; 4 pieces, all in orbit.

2018 15 B	[43193]				2018 Feb 2.45	97.33	94.62	6879	492	508	0.001	270

2018 15 G	[43198]				2018 Feb 2.59	97.21	94.12	6854	442	509	0.005	297

2018 15 J	[43200]				2018 Feb 2.92	97.42	94.13	6855	452	501	0.004	351

2018 15 L	[44615]				2019 Oct 2.88	97.51	93.73	6836	425	489	0.005	297

HII-A fragments; 2 pieces, both in orbit

2018 21 C	[43225]				No TLE’s issued

D	2018 21 D	[43240]	2020 Jan 8	680 days		2018 Mar 26.61	97.21	94.45	6870	485	499	0.001	291

2020 Jan 8.79	97.22	90.35	6671	279	305	0.002	329

LKW-4 CZ-2D fragments; 3 pieces, all in orbit

2018 25 C	[43505]				2018 Jun 15.79	97.48	94.85	6890	497	525	0.002	170

2018 25 D	[43506]				2018 Jun 15.29	97.46	94.10	6854	446	504	0.004	347

2018 25 E	[43507]				2018 Jun 15.56	97.23	93.83	6841	426	498	0.005	3

Gaofen 1-02, -03 and -04 CZ-4C 3rd stage fragments; 6 pieces, 1 has decayed

2018 31 C	[43261]				2018 Mar 31.26	98.03	97.52	7019	638	642	0.0003	275

2018 31 E	[43263]				2018 Mar 31.87	97.99	98.02	7042	632	695	0.005	252

2018 31 G	[43265]				2018 Mar 31.26	98.02	97.58	7021	639	647	0.0006	287

2018 31 H	[43266]				2018 Mar 31.99	98.08	97.08	6998	591	647	0.004	71

2018 31 J	[43270]				2018 Apr 3.10	98.02	97.55	7020	638	645	0.0005	257

2018 31 K	[44616]				2019 Oct 2.40	97.99	97.43	7014	631	640	0.0007	11

Dragon CRS-14 fragments; 2 pieces, both have decayed.

D	2018 32 B	[43268]	2018 Apr 7	5 days		2018 Apr 2.87	51.65	90.13	6660	204	359	0.012	49

2018 Apr 7.20	51.64	88.33	6570	170	213	0.003	64

D	2018 32 C	[43269]	2018 Apr 7	5 days		2018 Apr 2.87	51.63	90.07	6657	202	354	0.011	47

2018 Apr 7.13	51.64	88.22	6565	170	202	0.002	74

CZ-4C 3rd stage fragments; 4 pieces, both in orbit

2018 34 F	[43280]				2018 Apr 10.41	63.41	107.10	7471	1086	1099	0.0009	39

2018 34 G	[43281]				2018 Apr 10.64	63.41	107.12	7472	1087	1099	0.0008	43

2018 34 H	[43338]				2018 Apr 12.02	63.42	107.08	7470	1084	1100	0.001	34

2018 34 J	[44617]				2019 Oct 2.56	63.40	107.38	7484	1078	1133	0.004	10

2018 34 K	[44618]				2019 Oct 2.59	63.47	107.30	7480	1068	1135	0.004	354

Dragon CRS-15 fragments; 2 pieces, both have decayed.

D	2018 55 B	[43523]	2018 Jul 11	12 days		2018 Jun 29.61	51.64	90.38	6672	224	362	0.010	47

2018 Jul 11.17	51.63	87.55	6532	149	158	0.0007	110

D	2018 55 C	[43524]	2018 Jul 11	12 days		2018 Jun 29.61	51.63	90.35	6670	224	359	0.010	47

2018 Jun 10.42	51.65	87.77	6543	155	173	0.001	63

CZ-2C 2nd stage fragments; 6 pieces, 3 have decayed

Object C is probably the solid fuel upper stage.

D	2018 56 C	[43531]	2019 Mar 12	276 days		2018 Jul 9.35	97.94	93.35	6817	273	603	0.024	158

2018 Jul 9.68	97.82	91.93	6748	271	468	0.015	141

2019 Mar 11.93	97.77	87.33	6521	131	154	0.002	272

D	2018 56 E	[43533]	2018 Jul 31	54 days		2018 Jul 9.35	98.05	93.02	6801	233	611	0.028	171

2018 Jul 30.25	98.08	88.28	6568	168	212	0.003	90

2018 56 F	[43534]				2018 Jul 9.36	98.05	96.85	6986	588	627	0.003	286

2018 56 G	[43535]				2018 Jul 9.87	97.86	95.18	6906	235	820	0.042	159

D	2018 56 H	[43536]	2018 Aug 23	75 days		2018 Jul 9.87	98.30	95.23	6908	230	830	0.043	175

2018 Aug 23.00	98.23	87.55	6532	140	166	0.002	348

D	2018 56 J	[43555]	2020 Jan 12	582 days		2018 Jul 20.71	98.05	96.78	6984	584	625	0.003	244

2020 Jan 8.53	98.12	91.35	6719	328	353	0.002	308

Atlas V 2nd stage fragments; 172 pieces, all in orbit

2018 79 C	[44642]				2019 Oct 24.40	11.47	780.30	28079	8184	35211	0.481	248

2018 79 D	[44643]				2019 Oct 24.51	11.85	791.22	28337	8358	35560	0.480	254

2018 79 E	[44644]				2019 Oct 24.41	11.67	741.95	27149	8500	33040	0.452	243

2018 79 F	[44645]				2019 Oct 24.16	11.66	758.65	27555	8323	34029	0.466	252

2018 79 G	[44646]				2019 Oct 24.50	11.80	774.23	27930	8234	34870	0.477	255

2018 79 H	[44647]				2019 Oct 24.44	11.67	765.73	27726	8449	34245	0.465	251

2018 79 J	[44648]				2019 Oct 24.15	11.60	748.53	27309	8187	33673	0.467	245

2018 79 K	[44649]				2019 Oct 24.52	11.50	782.70	28134	8282	35228	0.479	247

2018 79 L	[44650]				2019 Oct 24.57	11.60	756.17	27494	8786	33445	0.448	242

2018 79 M	[44651]				2019 Oct 24.19	11.58	785.60	28203	8549	35101	0.471	244

2018 79 N	[44652]				2019 Oct 24.45	11.40	772.07	27878	8659	34341	0.461	244

2018 79 P	[44653]				2019 Oct 24.55	11.78	718.45	26572	7903	32484	0.463	263

2018 79 Q	[44654]				2019 Oct 24.26	11.67	796.75	28469	8655	35527	0.472	248

2018 79 R	[44655]				2019 Oct 24.06	11.84	783.00	28141	8183	35342	0.483	256

2018 79 S	[44656]				2019 Oct 24.16	11.82	785.48	28200	8492	35152	0.473	254

2018 79 T	[44657]				2019 Oct 24.19	11.65	766.85	27753	8061	34687	0.480	252

2018 79 U	[44658]				2019 Oct 23.16	11.74	792.38	28365	8503	35470	0.475	251

2018 79 V	[44659]				2019 Oct 24.41	11.69	755.58	27480	8556	33647	0.457	252

2018 79 W	[44660]				2019 Oct 23.96	11.46	776.27	27980	7657	35545	0.498	245

2018 79 X	[44661]				2019 Oct 24.40	11.50	834.03	29351	9231	36713	0.468	233

2018 79 Y	[44662]				2019 Oct 24.72	11.58	779.20	28050	8399	34943	0.473	246

2018 79 Z	[44663]				2019 Oct 23.93	11.34	771.98	27876	7956	35039	0.486	250

2018 79 AA	[44664]				2019 Oct 24.08	11.39	849.90	29722	8626	38061	0.495	234

2018 79 AB	[44665]				2019 Oct 23.07	11.50	853.13	29797	9277	37560	0.475	225

2018 79 AC	[44666]				2019 Oct 23.24	11.61	755.10	27268	8756	33423	0.449	241

2018 79 AD	[44667]				2019 Oct 24.18	11.60	754.88	27463	8235	33932	0.468	256

2018 79 AE	[44668]				2019 Oct 24.51	11.75	729.32	26839	8193	32728	0.457	259

2018 79 AF	[44669]				2019 Oct 9.14	11.35	796.00	28452	8630	35516	0.472	249

2018 79 AG	[44670]				2019 Oct 24.07	11.58	787.23	28242	8639	35088	0.468	244

2018 79 AH	[44671]				2019 Oct 23.96	11.66	769.90	27826	8528	34368	0.464	247

2018 79 AJ	[44672]				2019 Oct 18.99	11.07	780.10	28071	7503	35883	0.505	256

2018 79 AK	[44673]				2019 Oct 24.49	11.58	811.03	28809	8740	36120	0.475	242

2018 79 AL	[44674]				2019 Oct 24.16	11.89	742.83	27170	8615	32968	0.448	233

2018 79 AM	[44675]				2019 Oct 24.01	11.61	797.92	28497	8711	35525	0.470	245

2018 79 AN	[44676]				2019 Oct 23.03	11.74	787.52	28249	8412	35329	0.476	252

2018 79 AP	[44677]				2019 Oct 13.22	11.57	806.12	28692	9481	35146	0.447	235

2018 79 AQ	[44678]				2019 Oct 23.17	11.57	790.18	28313	8706	35162	0.467	246

2018 79 AR	[44679]				2019 Oct 24.64	11.60	802.65	28610	8697	35765	0.473	244

2018 79 AS	[44680]				2019 Oct 23.88	11.56	820.08	29025	8883	36405	0.474	240

2018 79 AT	[44681]				2019 Oct 23.78	11.20	836.23	29402	8875	37172	0.481	234

2018 79 AU	[44682]				2019 Oct 24.06	11.61	791.52	28345	8720	35213	0.467	245

2018 79 AV	[44683]				2019 Oct 23.15	11.58	785.82	28208	8459	35200	0.474	245

2018 79 AW	[44684]				2019 Oct 23.82	11.56	786.32	28220	8605	35079	0.469	244

2018 79 AX	[44685]				2019 Oct 21.90	11.53	850.53	29737	9381	37336	0.470	225

2018 79 AY	[44686]				2019 Oct 24.49	11.51	851.55	29760	9387	37376	0.470	225

2018 79 AZ	[44687]				2019 Oct 19.93	11.58	790.38	28317	8706	35171	0.467	242

2018 79 BA	[44688]				2019 Oct 21.97	11.63	805.42	28676	8790	35804	0.471	244

2018 79 BB	[44689]				2019 Oct 24.11	11.74	675.05	25491	6828	31397	0.482	264

2018 79 BC	[44690]				2019 Oct 21.15	11.59	763.27	27666	8953	33622	0.446	240

2018 79 BD	[44691]				2019 Oct 24.19	11.54	814.38	28888	9440	35578	0.452	239

2018 79 BE	[44692]				2019 Oct 24.46	11.75	739.00	29467	9181	36996	0.472	219

2018 79 BF	[44693]				2019 Oct 24.57	11.63	806.88	28710	8769	35894	0.472	245

2018 79 BG	[44694]				2019 Oct 24.64	11.66	811.72	28825	8738	36154	0.476	246

2018 79 BH	[44695]				2019 Oct 14.86	11.71	830.70	29272	8759	37028	0.483	252

2018 79 BJ	[44895]				2020 Jan 15.25	11.44	766.87	27753	9331	33418	0.434	258

2018 79 BK	[44896]				2020 Jan 15.94	11.72	717.62	26552	7948	32398	0.460	282

2018 79 BL	[44897]				2020 Jan 15.67	12.06	627.58	24282	5166	30640	0.525	341

2018 79 BM	[44898]				2020 Jan 6.49	11.33	708.85	26335	6602	33311	0.507	279

2018 79 BN	[44899]				2020 Jan 6.33	12.04	703.23	26196	6740	32894	0.499	303

2018 79 BP	[44980]				2020 Jan 6.21	11.80	664.95	25236	7451	30264	0.452	296

2018 79 BQ	[44981]				2020 Jan 6.04	11.75	617.77	24028	5420	29877	0.509	317

2018 79 BR	[44985]				2020 Jan 7.90	11.63	735.07	26980	8385	32818	0.453	276

2018 79 BS	[44986]				2020 Jan 7.36	11.36	782.27	28123	8393	35097	0.475	262

2018 79 BT	[45471]				2020 Apr 1.96	11.35	809.80	28780	8968	35834	0.467	270

2018 79 BU	[45472]				2020 Apr 1.66	11.39	791.85	28352	8402	35546	0.479	276

2018 79 BV	[45473]				2020 Apr 1.56	11.20	844.38	29593	9719	36709	0.456	256

2018 79 BW	[45474]				2020 Apr 1.76	11.26	826.07	29164	9713	35857	0.448	260

2018 79 BX	[45475]				2020 Apr 2.56	11.39	779.53	28058	8382	34976	0.474	277

2018 79 BY	[46485]				2020 Oct 8.34	11.94	716.27	26494	7785	32445	0.465	347

2018 79 BZ	[46601]				2020 Oct 10.97	11.23	775.03	27950	8711	34432	0.460	307

2018 79 CA	[46602]				2020 Oct 8.05	11.36	804.27	28648	8877	35662	0.467	307

2018 79 CB	[46603]				2020 Oct 7.99	11.68	822.07	29069	9426	35955	0.456	313

2018 79 CC	[46604]				2020 Oct 8.00	11.27	825.93	29160	9373	36190	0.460	298

2018 79 CD	[46605]				2020 Oct 7.99	11.32	751.50	27381	8796	33209	0.446	308

2018 79 CE	[46606]				2020 Oct 8.13	11.37	802.73	28612	8955	35511	0.464	307

2018 79 CF	[46607]				2020 Oct 8.18	11.50	701.90	26163	7902	31666	0.454	330

2018 79 CG	[46608]				2020 Oct 8.30	11.37	803.00	28618	8901	35578	0.466	307

2018 79 CH	[46655]				2020 Oct 12.94	11.57	704.78	26234	7604	32106	0.467	346

2018 79 CJ	[46656]				2020 Oct 15.29	11.62	731.00	26881	8359	32646	0.452	333

2018 79 CK	[46657]				2020 Oct 15.03	9.70	847.75	29672	6341	40245	0.571	315

2018 79 CL	[46658]				2020 Oct 14.26	10.27	969.08	32439	9125	42997	0.522	260

2018 79 CM	[46659]				2020 Oct 14.81	10.71	839.35	29475	8081	38112	0.509	288

2018 79 CN	[46660]				2020 Oct 15.15	11.26	795.22	28433	8964	35144	0.460	305

2018 79 CP	[46661]				2020 Oct 14.97	11.41	787.22	28242	9089	34638	0.452	310

2018 79 CQ	[46662]				2020 Oct 14.98	11.35	741.58	27139	6819	34703	0.514	331

2018 79 CR	[46663]				2020 Oct 15.30	11.29	783.07	28143	8588	34940	0.468	311

2018 79 CS	[46664]				2020 Oct 14.78	11.01	836.98	29420	9312	36770	0.467	292

2018 79 CT	[46665]				2020 Oct 14.93	11.24	839.90	29488	9566	36652	0.459	296

2018 79 CU	[46666]				2020 Oct 14.97	11.30	918.43	31299	9954	39886	0.478	304

2018 79 CV	[46667]				2020 Oct 14.95	11.38	738.80	27072	7982	33404	0.470	325

2018 79 CW	[46668]				2020 Oct 14.50	11.28	784.18	28169	8696	34885	0.465	309

2018 79 CX	[46842]				2020 Nov 4.98	11.11	823.35	29100	9415	36027	0.457	298

2018 79 CY	[46843]				2020 Nov 5.90	11.21	767.70	27773	7574	35215	0.498	328

2018 79 CZ	[46844]				2020 Nov 5.59	11.15	708.57	26328	6287	33612	0.519	351

2018 79 DA	[46845]				2020 Nov 5.09	11.32	745.80	27243	7573	34155	0.488	330

2018 79 DB	[46846]				2020 Nov 5.72	10.62	838.65	29459	9009	37151	0.478	298

2018 79 DC	[46847]				2020 Nov 5.65	11.36	812.28	28838	8935	35984	0.469	311

2018 79 DD	[46848]				2020 Nov 5.67	11.25	804.50	28654	9527	35023	0.445	304

2018 79 DE	[46849]				2020 Nov 6.04	11.39	879.65	30411	8345	39721	0.516	309

2018 79 DF	[46850]				2020 Nov 6.12	11.23	798.85	28519	8720	35561	0.471	311

2018 79 DG	[46851]				2020 Nov 6.16	12.08	731.62	26896	7451	33584	0.486	308

2018 79 DH	[46852]				2020 Nov 6.10	11.50	804.48	28653	8465	36084	0.482	321

2018 79 DJ	[46853]				2020 Nov 5.71	11.60	828.05	29210	9065	36598	0.471	315

2018 79 DK	[46854]				2020 Nov 5.28	8.66	844.50	29596	9755	36680	0.455	301

2018 79 DL	[46855]				2020 Nov 5.23	10.47	843.65	29576	9806	36589	0.453	287

2018 79 DM	[46856]				2020 Nov 4.92	11.35	747.88	27293	8285	33543	0.462	320

2018 79 DN	[46857]				2020 Nov 5.89	10.94	851.57	29761	9592	37172	0.463	283

2018 79 DP	[46858]				2020 Nov 5.97	11.40	736.78	27022	7801	33486	0.475	331

2018 79 DQ	[46859]				2020 Nov 6.03	11.50	703.95	26213	5753	33916	0.537	359

2018 79 DR	[46860]				2020 Nov 5.87	10.86	869.58	30179	9246	38354	0.482	292

2018 79 DS	[46861]				2020 Nov 5.19	11.08	809.02	28761	8085	36680	0.497	308

2018 79 DT	[46862]				2020 Nov 4.10	11.03	957.50	32180	9595	32180	0.504	286

2018 79 DU	[46863]				2020 Nov 8.68	11.18	740.20	27106	6697	34757	0.518	340

2018 79 DV	[46864]				2020 Nov 9.23	11.54	761.87	27632	8424	34084	0.464	331

2018 79 DW	[46865]				2020 Nov 8.36	11.28	762.55	27649	8828	33712	0.450	314

2018 79 DX	[46866]				2020 Nov 7.37	11.21	695.20	25996	7781	31453	0.455	4

2018 79 DY	[46867]				2020 Nov 5.96	13.35	662.48	25174	6771	30820	0.478	39

2018 79 DZ	[46868]				2020 Nov 5.97	13.17	714.73	26481	7110	33094	0.491	355

2018 79 EA	[46869]				2020 Nov 5.77	11.28	785.65	28204	8755	34896	0.463	314

2018 79 EB	[46870]				2020 Nov 10.50	12.03	701.42	26150	6951	32592	0.490	12

2018 79 EC	[46871]				2020 Nov 8.20	13.64	835.83	29393	8686	37342	0.487	344

2018 79 ED	[46872]				2020 Nov 8.02	13.80	799.80	28542	8550	35777	0.477	353

2018 79 EE	[47244]				2020 Dec 13.75	11.31	812.62	28846	8896	36039	0.470	317

2018 79 EF	[47245]				2020 Dec 14.91	11.42	769.17	27808	7805	35055	0.490	321

2018 79 EG	[47248]				2020 Dec 14.34	11.57	687.08	25793	6412	32417	0.504	9

2018 79 EH	[47249]				2020 Dec 14.52	11.60	788.43	28271	8410	35374	0.477	333

2018 79 EJ	[47250]				2020 Dec 15.19	11.26	742.58	27164	8080	33491	0.468	331

2018 79 EK	[47251]				2020 Dec 13.46	11.94	740.52	27114	7126	34343	0.502	354

2018 79 EL	[47339]				2021 Jan 19.03	11.27	745.82	27243	8886	32842	0.440	329

2018 79 EM	[47340]				2021 Jan 19.27	11.14	755.32	27473	9539	32650	0.421	342

2018 79 EN	[47341]				2021 Jan 19.17	10.92	836.47	29408	9720	36338	0.453	315

2018 79 EP	[47342]				2021 Jan 19.09	11.77	717.72	26554	7750	32601	0.468	348

2018 79 EQ	[47343]				2021 Feb 1.03	11.12	720.33	26618	9478	31001	0.404	333

2018 79 ER	[49340]				2021 Oct 27.27	11.35	816.87	28947	8715	36421	0.179	15

2018 79 ES	[49341]

2018 79 ET	[49342]

2018 79 EU	[49343]

2018 79 EV	[49344]

2018 79 EW	[49345]

2018 79 EX	[49346]

2018 79 EY	[49347]

2018 79 EZ	[49348]

2018 79 FA	[49349]

2018 79 FB	[49350]

2018 79 FC	[49351]

2018 79 FD	[49352]

2018 79 FE	[49353]

2018 79 FF	[49354]

2018 79 FG	[49355]

2018 79 FH	[49356]

2018 79 FJ	[49357]

2018 79 FK	[49358]

2018 79 FL	[49359]

2018 79 FM	[49360]

2018 79 FN	[49361]

2018 79 FP	[49362]

2018 79 FQ	[49363]

2018 79 FR	[49364]

2018 79 FS	[49365]

2018 79 FT	[49366]

2018 79 FU	[49367]

2018 79 FV	[49368]

2018 79 FW	[49369]

2018 79 FX	[49370]

2018 79 FY	[49371]

2018 79 FZ	[49372]

2018 79 GA	[49373]

2018 79 GB	[49374]

2018 79 GC	[49375]

2018 79 GD	[49376]

2018 79 GE	[49377]

2018 79 GF	[49378]				2021 Oct 27.30	10.72	894.08	30743	9475	39253	0.484	321

Haiyang 2B CZ-4B 3rd stage fragments; 3 pieces, all in orbit

2018 81 C	[43659]				2018 Oct 25.61	99.28	103.35	7295	886	947	0.004	315

2018 81 D	[43660]				2018 Oct 25.94	99.32	103.60	7308	919	939	0.001	333

2018 81 E	[43661]				2018 Oct 25.82	99.35	103.68	7312	924	942	0.001	292

CFOSAT CZ-3B 3rd stage fragments; 6 pieces, all in orbit. They could be secondary payloads, see footnote # in maun table.

2018 83 B	[43663]				2018 Oct 29.30	97.84	96.72	6980	591	612	0.001	313

2018 83 C	[43664]				2018 Oct 29.36	97.52	94.97	6895	513	521	0.0006	327

2018 83 D	[43665]				2018 Oct 29.36	97.52	94.93	6894	507	523	0.001	274

2018 83 E	[43666]				2018 Oct 29.36	97.54	94.92	6893	504	524	0.001	278

2018 83 G	[43668]				2018 Oct 29.69	97.52	94.95	6895	510	522	0.0009	268

2018 83 H	[43669]				2018 Oct 29.69	97.53	94.95	6895	509	524	0.001	257

GOSAT 2 H-2A 2nd stage fragments; 100 pieces, 1 has decayed

D	2018 84 A	[43671]	2019 Aug 1	276 days		2018 Oct 29.24	97.85	96.52	6971	589	595	0.0004	80

2018 Oct 29.64	97.85	96.53	6971	585	599	0.001	46

2019 Jul 30.30	97.68	90.67	6686	287	326	0.003	296

2018 84 C	[43673]				2018 Oct 29.30	97.84	96.80	6984	595	616	0.001	293

2018 84 D	[43674]				2018 Oct 29.30	97.86	96.78	6983	595	614	0.001	294

2018 84 E	[43675]				2018 Oct 29.30	97.85	96.75	6982	592	614	0.002	299

2018 84 M	[44051]				2019 Feb 26.75	97.85	96.00	6945	537	596	0.004	45

2018 84 N	[44052]				2019 Feb 26.31	97.85	96.13	6952	546	601	0.004	65

2018 84 P	[44053]				2019 Feb 26.89	97.85	96.30	6960	568	595	0.002	281

2018 84 Q	[44054]				2019 Feb 26.55	97.85	96.00	6945	539	594	0.004	8

2018 84 R	[44620]				2019 Oct 2.93	98.89	95.73	6932	516	591	0.005	259

2018 84 S	[46181]				2020 Aug 20.25	97.89	97.02	6995	589	643	0.004	279

2018 84 T	[46182]				2020 Aug 20.37	97.84	95.97	6944	504	626	0.009	207

2018 84 U	[46183]				2020 Aug 20.34	97.90	96.55	6972	583	605	0.002	229

2018 84 V	[46184]				2020 Aug 20.37	97.83	94.85	6890	420	602	0.013	187

2018 84 W	[46185]				2020 Aug 20.30	97.89	96.42	6965	568	605	0.003	215

2018 84 X	[46186]				2020 Aug 20.32	97.87	93.83	6840	388	535	0.011	184

2018 84 Y	[46187]				2020 Aug 20.54	97.87	96.52	6970	568	616	0.003	212

2018 84 Z	[46188]				2020 Aug 20.54	97.79	96.07	6948	488	652	0.012	221

2018 84 AA	[46189]				2020 Aug 20.25	97.92	97.27	7006	603	653	0.004	260

2018 84 AB	[46190]				2020 Aug 20.27	97.85	95.00	6897	416	621	0.015	204

2018 84 AC	[46191]				2020 Aug 20.35	97.87	96.63	6976	580	615	0.003	214

2018 84 AD	[46192]				2020 Aug 20.37	97.82	94.98	6897	450	585	0.010	195

2018 84 AE	[46193]				2020 Aug 20.32	97.89	96.70	6979	538	662	0.009	235

2018 84 AF	[46194]				2020 Aug 20.31	97.90	95.48	6920	475	608	0.010	179

2018 84 AG	[46195]				2020 Aug 20.29	97.90	96.03	6947	534	603	0.005	223

2018 84 AH	[46196]				2020 Aug 20.35	97.89	97.40	7013	603	665	0.004	306

2018 84 AJ	[46197]				2020 Aug 20.28	97.78	96.38	6964	535	636	0.007	228

2018 84 AK	[46198]				2020 Aug 20.21	97.81	95.90	6941	509	615	0.008	205

2018 84 AL	[46199]				2020 Aug 20.61	97.83	95.18	6906	461	594	0.010	174

2018 84 AM	[46200]				2020 Aug 20.26	97.88	96.65	6977	561	635	0.005	248

2018 84 AN	[46201]				2020 Aug 20.37	97.89	96.60	6975	580	612	0.002	254

2018 84 AP	[46202]				2020 Aug 20.29	97.87	96.78	6983	596	613	0.001	310

2018 84 AQ	[46203]				2020 Aug 20.31	97.86	96.13	6952	530	617	0.006	194

2018 84 AR	[46204]				2020 Aug 20.30	97.89	96.60	6975	578	614	0.003	237

2018 84 AS	[46205]				2020 Aug 20.29	97.88	96.28	6959	542	619	0.006	182

2018 84 AT	[46206]				2020 Aug 20.29	97.91	96.58	6974	581	610	0.002	206

2018 84 AU	[46207]				2020 Aug 20.35	97.82	94.23	6860	408	555	0.011	155

2018 84 AV	[46208]				2020 Aug 20.26	97.81	95.37	6915	450	623	0.013	211

2018 84 AW	[46209]				2020 Aug 20.11	97.73	95.95	6943	509	619	0.008	217

2018 84 AX	[46210]				2020 Aug 20.26	97.89	96.55	6972	530	657	0.009	231

2018 84 AY	[46211]				2020 Aug 20.30	97.78	95.90	6940	488	636	0.011	209

2018 84 AZ	[46212]				2020 Aug 20.27	97.78	97.15	7001	560	684	0.009	250

2018 84 BA	[46213]				2020 Aug 20.59	97.85	95.13	6903	438	611	0.012	201

2018 84 BB	[46214]				2020 Aug 20.32	97.72	94.90	6893	459	568	0.008	197

2018 84 BC	[46215]				2020 Aug 20.29	97.76	96.43	6966	563	612	0.003	129

2018 84 BD	[46216]				2020 Aug 20.31	97.88	96.52	6971	573	611	0.003	206

2018 84 BE	[46217]				2020 Aug 20.28	97.87	96.60	6975	563	629	0.005	225

2018 84 BF	[46218]				2020 Aug 20.31	97.82	95.10	6902	457	590	0.010	203

2018 84 BG	[46219]				2020 Aug 20.28	97.82	97.50	7018	610	668	0.004	285

2018 84 BH	[46220]				2020 Aug 20.25	97.87	96.33	6961	550	615	0.005	210

2018 84 BJ	[46221]				2020 Aug 20.30	97.89	96.60	6974	585	606	0.002	246

2018 84 BK	[46222]				2020 Aug 20.25	97.88	96.62	6975	587	607	0.001	219

2018 84 BL	[46223]				2020 Aug 20.29	97.86	96.48	6969	558	621	0.005	203

2018 84 BM	[46224]				2020 Aug 20.31	97.89	96.40	6965	570	602	0.002	219

2018 84 BN	[46225]				2020 Aug 20.26	97.90	96.57	6973	573	615	0.003	216

2018 84 BP	[46226]				2020 Aug 20.25	97.89	96.55	6972	547	639	0.007	223

2018 84 BQ	[46227]				2020 Aug 20.27	97.87	96.37	6963	563	606	0.003	225

2018 84 BR	[46228]				2020 Aug 20.05	97.84	96.35	6963	558	610	0.004	198

2018 84 BS	[46229]				2020 Aug 20.29	97.82	95.37	6915	461	611	0.011	205

2018 84 BT	[46230]				2020 Aug 20.30	97.87	96.12	6951	529	617	0.006	201

2018 84 BU	[46231]				2020 Aug 20.31	97.82	95.38	6916	461	613	0.011	204

2018 84 BV	[46414]				2020 Sep 8.56	97.84	95.38	6916	473	601	0.009	136

2018 84 BW	[46415]				2020 Sep 8.28	97.85	96.70	6979	557	644	0.006	193

2018 84 BX	[46416]				2020 Sep 8.10	97.88	95.90	6940	521	602	0.006	154

2018 84 BY	[46417]				2020 Sep 8.27	97.86	95.97	6944	529	601	0.005	173

2018 84 BZ	[46418]				2020 Sep 8.28	97.93	96.92	6990	574	648	0.005	215

2018 84 CA	[46419]				2020 Sep 8.28	97.88	96.40	6965	542	631	0.006	187

2018 84 CB	[46420]				2020 Sep 8.05	97.82	96.07	6949	526	614	0.006	156

2018 84 CC	[46421]				2020 Sep 8.29	97.79	95.52	6922	492	595	0.007	171

2018 84 CD	[46422]				2020 Sep 8.22	97.85	97.03	6995	606	627	0.001	201

2018 84 CE	[46423]				2020 Sep 8.29	97.85	96.17	6953	542	607	0.005	172

2018 84 CF	[46424]				2020 Sep 8.31	97.86	96.52	6970	565	619	0.004	177

2018 84 CG	[46425]				2020 Sep 8.29	97.86	95.92	6941	529	596	0.005	168

2018 84 CH	[46426]				2020 Sep 8.11	97.89	97.87	7035	574	739	0.012	234

2018 84 CJ	[46427]				2020 Sep 8.29	97.85	97.10	6999	582	658	0.005	210

2018 84 CK	[46428]				2020 Sep 8.31	97.86	97.13	7000	582	660	0.006	215

2018 84 CL	[46473]				2020 Sep 22.76	97.83	95.90	6941	536	589	0.004	151

2018 84 CM	[46474]				2020 Sep 22.24	97.82	96.47	6968	509	669	0.011	143

2018 84 CN	[46475]				2020 Sep 22.26	97.81	95.08	6901	487	558	0.005	132

2018 84 CP	[46476]				2020 Sep 22.27	97.80	93.10	6805	408	445	0.003	156

2018 84 CQ	[46477]				2020 Sep 22.57	97.83	92.93	6797	406	430	0.002	116

2018 84 CR	[46598]				2020 Oct 7.28	97.80	95.27	6910	518	845	0.002	146

2018 84 CS	[46599]				2020 Oct 7.24	97.82	95.18	6906	505	550	0.003	129

2018 84 CT	[46600]				2020 Oct 6.30	97.79	96.52	6970	533	650	0.008	158

2018 84 CU	[47187]				2020 Nov 25.25	97.90	96.72	6980	593	609	0.001	331

2018 84 CV	[47188]				2020 Nov 20.28	97.78	94.27	6861	457	508	0.004	253

2018 84 CW	[47189]				2020 Nov 25.26	97.88	97.00	6994	581	648	0.005	334

2018 84 CX	[47190]				2020 Nov 25.26	97.82	95.90	6940	542	581	0.003	265

2018 84 CY	[47191]				2020 Nov 25.28	97.83	95.78	6935	535	578	0.003	257

2018 84 CZ	[47192]				2020 Nov 23.07	97.85	95.82	6936	539	576	0.003	249

2018 84 DA	[47193]				2020 Nov 25.10	97.83	95.85	6938	535	585	0.004	216

2018 84 DB	[47194]				2020 Nov 22.57	97.89	96.30	6960	553	610	0.004	266

2018 84 DC	[47195]				2020 Nov 25.25	97.84	96.60	6975	563	629	0.005	322

2018 84 DD	[47196]				2020 Nov 25.33	97.82	92.93	6797	393	444	0.004	255

2018 84 DE	[47197]				2020 Nov 25.24	97.85	98.03	7043	599	731	0.009	38

2018 84 DF	[48551]				2021 May 12.22	98.19	98.68	7074	672	720	0.003	84

2018 84 DG	[48552]				2021 May 12.08	98.55	94.22	6859	477	483	0.0004	128

CZ-2D fragments; 3 pieces, all in orbit

2018 94 F	[43715]				2018 Nov 20.83	97.36	94.28	6862	469	498	0.002	327

2018 94 G	[43716]				2018 Nov 20.83	97.53	94.33	6865	461	511	0.004	277

2018 94 H	[43718]				2018 Nov 21.56	97.52	94.18	6858	460	498	0.003	359

Dragon CRS-16 fragments (2 solar panel covers); 3 pieces, in orbit.

D	2018 101 B	[43828]	2018 Dec 11	3 days		2018 Dec 5.76	51.64	90.17	6662	204	362	0.012	46

D	2018 101 C	[43829]	2018 Dec 11	3 days		2018 Dec 5.76	51.63	90.17	6661	204	362	0.012	46

D	2018 101 D	[43830]	2018 Dec 5	< 1 day		2018 Dec 5.76	51.62	90.10	6658	202	357	0.012	45

2018 Dec 5.96	51.62	90.08	6657	203	354	0.011	47

D	Soyuz MS-10 *	2018 F1	2018 Oct 11.361	Cyl+beehive+	7.48 long	A problem with the Soyuz booster at the time of separation of the 1st stage

2M [Soyuz FG]	[NNA]		+spheroid+	2.72 maxdia	caused the Soyuz capsule to an automatic abort.

R		BAI-LC1/5		2 panels	2.2 dia	The Soyuz made a ballistic re-entry and landed safely some 20 km east of

7167	10.6 span	the town of Dzhezkazgan in Kazakhstan 34 min after launch.

*	On board was a 2 person crew (Ovchinin and Hague) for 6 month stay at the ISS.

This incident comes 33.5 years after the last failure with a crewed Soyuz. On 1975 Apr 5 the flight of Soyuz 18 was aborted after almost 5 minutes.

D	Weilai 1  #	2018 F2	2018 Oct 27.333	Box +2 panels		A malfunction of the 3rd stage prevented it and the satellite to enter orbit

[Zhuque 1]	[NNA]		~ 45

JIUQ

#	First flight of the solid-fueled Zhuque 1 rocket from LandSpace with the Weilai 1 microsatellite for China Central Television.