D	Cosmos 787	1976-01 A	1976 Jan 6.21	Cylinder +	2 long?	1976 Jan 7.6	74.03	95.30	6911	518	547	0.002	16

[Kosmos 11K65M	[08530]	1802 days	paddles?	1 dia?	1980 Dec 12.22	73.99	87.60	6534	151	159	0.0006

53731-269]	PLE-LC132	1980 Dec 12	900?

D	Cosmos 787	1976-01 B	1976 Jan 6.21	Cylinder	7.4 long	1976 Jan 7.58	74.03	95.13	6904	506	544	0.003	16

2nd stage	[08531]	1895 days	2200?	2.4 dia	1976 Jan 15.4	74.04	95.19	6905	507	547	0.003	3

1981 Mar 15			1976 Mar 15.20	73.98	87.10	6510	126	136	0.0007	254

D	Fragments	1976-01 C-K	8 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 788	1976-02 A	1976 Jan 7.65	Sphere-	6.5 long?	1976 Jan 7.70	62.89	89.53	6630	120	383	0.020	74

R	[Voskhod 11A57]	[08551]	12.60 days	cylinder	2.4 dia	1976 Jan 8.4	62.81	89.53	6630	183	321	0.010	77

PLE	1976 Jan 20.25	6300?		1975 Jan 9.8	62.81	89.35	6621	169	317	0.011	73						1975 Jan 16.38	62.80	89.20	6613	167	303	0.010	74

1976 Jan 18.43	62.80	89.68	6637	166	350	0.014	72

1976 Jan 20.11	62.80	89.65	6635	166	347	0.014	72

D	Cosmos 788	1976-028	1976 Jan 7.65	Cylinder	7.5 long	1976 Jan 8.01	62.79	89.48	6627	177	320	0.011	76

Block I 3rd stage 	[08552]	7 days	2500?	2.6 dia	1976 Jan 8.4	62.79	89.42	6625	180	313	0.010	75			1976 Jan 14			1976 Jan 14.73	62.75	87.13	6511	130	135	0.0004	76

D	Cosmos 788	1976-02 D	1976 Jan 7.65	Cone	1.5 long?	1976 Jan 19.67	62.80	89.47	6627	166	330	0.012	70

motor*	[08588]	20 days	600? full	2 dia?	1976 Jan 20.4	62.81	89.45	6626	166	330	0.012

1976 Jan 27			1976 Jan 27.15	62.79	87.83	6546	140	194	0.004	74

D	Fragments	1976-02 C,E,F	  3 pieces, all have decayed		For orbital information see extra pages at the end of the year

*	Jettisoned about 1976 Jan 19.

Helios 2	1976-03 A	1976 Jan 15.23	Double-cone	1.75 to	Solar orbit	0	186 days		0.28	0.995	0.561	-

[Titan 3E TC-5	[08582]	Indefinate	376	2.77 dia	At perhelion 1976 Apr 17.

Centaur D-1T E-5]	CC-LC41			2.18 long

Helios 2	1976-03 B	1976 Jan 15.23	Cylinder	8.14 long	Solar orbit unknown

Centaur 5 2nd stage	[08583]	Indefinate	1815	3.05 dia

Helios 2	1976-03 C	1976 Jan 15.23	Sphere +	1.32 long	Orbit probably similar to 1976-03 A.

Star-37E stage	[08584]	Indefinate	Nozzle 66	0.94 dia

CTS 1** (Hermes)	1976-04 A	1976 Jan 17.98	Cylinder +	1.88 long	1976 Jan 18.66	27.18	627.47	24279	165	35635	0.730	180

[Delta 2914 606	[08585]	>million	2 wings	1.83 dia	1976 Jan 20.0	27.29	635.88	24491	205	36021	0.731	180

#119]	CC-LC17B	years	680 full?	16.8 span	1976 Jan 26.8	0.67	1442.2	42285	35786	36028	0.003	213

1976 Mar 1.0	0.55	1436.1	42165	35774	35800	0.0003	-

2004 Jul 9.58	14.76	1436.60	42175	35703	35889	0.002	62

2021 Nov 21.66	8.15	1435.11	42147	35700	35837	0.002	228

D	CTS 1	1976-04 B	1976 Jan 17.98	Cylinder +	6.4 long	1976 Jan 18.15	28.65	92.38	6770	178	604	0.031	168

Delta 2nd stage	[08586]	28 days	annulus	1.52 and	1976 Feb 11.0	28.66	89.02	6612	162	306	0.011	92

1976 Feb 14	350?	2.44 dia	1976 Feb 12.99	28.64	88.40	6574	152	238	0.007	117

D	CTS 1	1976-04 D	1976 Jan 17.98	Sphere-	1.32 long	1976 Jan 21.3	27.18	637.64	24548	180	36160	0.733	181

Star-37E PKM	[08598]	8266 days	cone	0.94 dia	1986 Dec 30.42	26.86	266.25	13710	219	14444	0.519	142

1998 Sep 4	66		1998	26.78	87.52		129	174	From Satcat

Fragments	1976-04 C, E, F	3 pieces, all in orbit	For orbital information see extra pages at the end of the year

**	Canadian Communications Technology Satellite, launched by NASA.

Cosmos 789	1976-05 A	1976 Jan 20.71	Cylinder?	2.1 long	1976 Jan 20.77	82.97	105.27	7386	1001	1013	0.0008	197

[Kosmos 11K65M	[08591]	1200 years	810	2.0 dia	1976 Jan 20.85	82.97	105.00	7373	981	1007	0.002	266

53749-164]	PLE-LC132				1976 Jan 24.8	82.97	105.05	7374	975	1016	0.003	263

2004 Jul 5.08	82.97	104.88	7368	968	1011	0.003	197

2021 Nov 21.86	82.97	104.87	7367	966	1011	0.003	176

Cosmos 789	1976-05 B	1976 Jan 20.71	Cylinder	7.4 long	1976 Jan 20.85	82.97	105.00	7373	981	1007	0.002	266

2nd stage	[08597]	600 years	2200?	2.4 dia	1976 Jan 21.5	82.97	104.94	7368	974	1006	0.002	259

2004 Jul 7.41	82.97	104.73	7361	962	1002	0.003	100

2021 Nov 21.94	82.97	104.70	7359	961	1000	0.003	30

Fragment	1976-05 C	[36299]			2010 Jan 22.16	82.97	104.88	7367	965	1013	0.003	323

2021 Nov 21.78	82.97	104.60	7354	952	999	0.003	133

Molniya-1 32	1976-06 A	1976 Jan 22.49	Windmill	3.4 long	1976 Jan 22.6	62.98	91.83	6743	233	497	0.020	63

[Molniya 8K78M]	[08601]	100 years?	+ 6 vanes	1.6 dia	1976 Jan 23.50	62.98	91.85	6744	239	492	0.019	65

BAI		1000?		1976 Jan 27.4	62.94	698.38	26074	465	38927	0.738	280

1976 Feb 5.8	62.91	717.74	26556	476	39879	0.742	280

2004 Jul 4.81	63.87	720.23	26616	1643	38832	0.699	274

2021 Nov 21.05	63.29	720.22	26616	647	39827	0.736	283

D	Molniya-1 32	1976-06 B	1976 Jan 22.49	Cylinder	7.5 long	1976 Jan 23.5	62.99	91.75	6739	234	488	0.019	61

Block I 3rd stage 	[08602]	71 days	2500?	2.6 dia	1976 Mar 30.73	62.98	88.93	6600	189	254	0.005	71			1976 Apr 2

D	Molniya-1 32	1976-06 C	1976 Jan 22.49	Irregular	-	1976 Jan 23.5	62.98	91.86	6745	240	493	0.019	65

4th stage casing 	[08603]	88 days			1976 Apr 19.63	62.96	87.82	6545	167	167	0	8

1976 Apr 19

D	Molniya-1 32	1976-06 D	1976 Jan 22.49	Cylinder	2.0 long	1976 Feb 17.1	62.96	695.47	26001	497	38749	0.735	280

Block L 4th stage 	[08701]	15079 days	440	2.0 dia	2004 Jul 2.54	64.61	694.10	25968	1333	37847	0.703	277

2017 May 5			2017 May 4.83	61.73	89.92	6649	93	447	0.027	279

D	Cosmos 790	1976-07 A	1976 Jan 22.94	Cylinder +	2 long?	1976 Jan 23.06	74.03	95.28	6911	502	563	0.004	0

[Kosmos 11K65M	[08604]	1756 days	paddles	1 dia.	1976 Jan 25.2	74.04	95.25	6908	511	549	0.003	353

53731-285]	PLE-LC132	1980 Nov 12	900?		1980 Nov 12.49	73.94	87.60	6534	151	159	0.0006	280

D	Cosmos 790	1976-07 B	1976 Jan 22.94	Cylinder	7.4 long	1976 Jan 23.2	74.05	95.12	6902	499	548	0.004	3

2nd stage	[08605]	1783 days	2200?	2.4 dia	1980 Dec 9.14	74.00	87.77	6543	161	167	0.0004	234

l980 Dec 9

Cosmos 791 *	1976-08 A	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.7	74.05	114.81	7824	1402	1490	0.006	11

[Kosmos 11K65M	[08607]	8000 years	40?	0.8 dia?	2004 Jul 5.18	74.06	114.73	7822	1401	1486	0.005	170

53731-281]	PLE-LC132				2021 Nov 21.67	74.05	114.73	7822	1400	1486	0.006	240

Cosmos 792 *	1976-08 B	1976 Jan 28.44	Spheroid	1.0 long7	1976 Jan 28.7	74.06	115.23	7843	1436	1494	0.004	133

[08608]	9000 years	40?	0.8 dia?	2004 Jul 4.18	74.05	115.17	7841	1435	1490	0.003	326

2021 Nov 21.64	74.06	115.15	7841	1436	1489	0.003	118

Cosmos 793 *	1976-08 C	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.7	74.06	115.02	7834	1418	1494	0.005	128

[08609]	8000 years	40?	0.8 dia?	2004 Jul 3.36	74.05	114.95	7832	1417	1490	0.005	256

2021 Nov 21.73	74.05	114.95	7832	1417	1489	0.005	5

Cosmos 794 *	1976-08 D	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.9	74.06	115.44	7853	1452	1497	0.003	148

[08610]	9000 years	40?	0.8 dia?	2004 Jul 5.33	74.05	115.37	7851	1451	1493	0.003	48

2021 Nov 21.90	74.05	115.37	7850	1450	1493	0.003	242

Cosmos 795 *	1976-08 E	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.9	74.05	115.66	7863	1467	1503	0.002	175

[08611]	10000 years	40?	0.8 dia?	2004 Jul 5.45	74.05	115.58	7861	1466	1498	0.002	144

2021 Nov 21.72	74.06	115.58	7860	1466	1497	0.002	17

Cosmos 796 *	1976-08 F	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.9	74.04	115.90	7874	1474	1518	0.003	202

[08612]	10000 years	40?	0.8 dia?	2004 Jul 4.95	74.06	115.83	7872	1471	1515	0.003	253

2021 Nov 21.79	74.06	115.83	7871	1471	1515	0.003	175

Cosmos 797 *	1976-08 G	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.9	74.05	116.13	7885	1480	1533	0.003	230

[08613]	10000 years	40?	0.8 dia?	2004 Jul 3.25	74.05	116.07	7882	1478	1529	0.003	352

2021 Nov 21.77	74.06	116.07	7882	1478	1529	0.003	315

Cosmos 798 *	1976-08 H	1976 Jan 28.44	Spheroid	1.0 long?	1976 Jan 28.9	74.05	116.40	7897	1481	1557	0.005	239

[08614]	10000 years	40?	0.8 dia?	2004 Jul 4.88	74.05	116.33	7895	1478	1553	0.005	80

2021 Nov 21.67	74.05	116.33	7894	1479	1553	0.005	97

Cosmos 791	1976-08 J	1976 Jan 28.44	Cylinder	7.4 long	1976 Feb 1.7	74.06	118.03	7970	1486	1698	0.013	259

2nd stage	[08615]	20000 years	2200?	2.4 dia	2004 Jul 6.55	74.05	117.95	7967	1482	1695	0.013	222

2021 Nov 21.85	74.05	117.93	7967	1482	1694	0.013	174

*	Strela-1M

D	Cosmos 799	1976-09 A	1976 Jan 29.36	Sphere-	5.0 long	1976 Jan 29.41	71.40	89.62	6634	199	311	0.008	49

R	[Voskhod 11A57]	[08616]	11.8 days	cylinder	2.4 dia	1976 Jan 30.5	71.40	89.64	6634	205	306	0.008	47

BAI	1976 Feb 10.2	5700?		1976 Feb 9.61	71.40	89.52	6629	201	299	0.007	26

D	Cosmos 799	1976-09 B	1976 Jan 29.36	Cylinder	7.5 long	1976 Jan 29.8	71.41	89.58	6631	208	297	0.007	47

Block I 3rd stage 	[08617]	13 days	2500?	2.6 dia	1976 Feb 11.09	71.43	87.87	6548	168	170	0.0002	334			1976 Feb 11

D	Fragment	1976-09 C	[08618]	1976 Jan 31	2 days	1976 Jan 29.66	71.45	89.27	6617	199	277	0.006	49

1976 Jan 29.97	71.44	89.10	6609	200	260	0.005	42

D	Fragment	1976-09 D	[08619]	1976 Feb 9	11 days	1976 Jan 29.79	71.41	89.70	6638	202	318	0.009	57

1976 Feb 1.90	71.42	89.53	6630	201	302	0.008	41

Intelsat 4A-2	1976-10 A	1976 Jan 29.997	Cylinder	2.82 long	1976 Feb 1.0	0.1	1420.2	41855	35084	35869	0.009	-

[Atlas SLV-3D(R)	[08620]	> million years	1500 full	2.39 dia	1976 May 1.0	0.1	1436.2	42167	35784	35794	0.0001	-

AC-37 Centaur D-1AR	 CC-LC36B		795 empty		1985 Nov 27.06	1.80	1436.05	42164	35759	35812	0.0006	126

5017D]			Graveyard orbit	1985 Dec 19.00	1.86	1443.60	42312	35910	35956	0.0005	228

2004 Jul 1.89	13.34	1444.43	42328	35908	35990	0.0001	76

2021 Nov 21.68	11.42	1444.60	42331	35933	35972	0.0005	240

Intelsat 4A-2	1976-10 B	1976 Jan 29.997	Cylinder	8.6 long	1976 Feb 13.75	21.71	655.25	24990	596	36627	0.721	189

Centaur 37 stage	[08621]	6000 years	1815	3.0 dia	1976 May 1.0	21.5	655.0	24984	605	36606	0.721	-

2004 Jul 4.84	21.89	652.97	24932	635	36472	0.719	32

2021 Nov 20.97	21.96	652.70	24925	594	36500	0.721	309

Cosmos 800	1976-11 A	1976 Feb 3.34	Cylinder?	1.3 long?	1976 Feb 3.40	82.95	105.30	7387	1002	1015	0.0008	60

[Kosmos 11K65M	[08645]	1200 years	700?	1.9 dia?	1976 Feb 3.55	82.95	105.07	7376	982	1013	0.002	279

53721-282]	PLE-LC132				1976 Feb 4.9	82.97	105.13	7378	984	1015	0.002	275

2004 Jul 5.23	82.97	104.97	7371	978	1007	0.002	285

2021 Nov 21.82	82.97	104.95	7371	977	1007	0.002	297

Cosmos 800	1976-11 B	1976 Feb 3.34	Cylinder	7.4 long	1976 Feb 3.5	82.98	105.00	7371	983	1003	0.001	250

2nd stage	[08646]	600 years	2200?	2.4 dia	2004 Jul 6.59	82.98	104.82	7365	981	991	0.0007	135

2021 Nov 21.68	82.97	104.80	7364	980	990	0.0007	102

D	Cosmos 801	1976-12 A	1976 Feb 5.61	Ellipsoid	1.8 long	1976 Feb 6.19	70.98	95.27	6910	266	797	0.038	85

[Kosmos 11K63]	[08658]	700 days	400?	1.2 dia	1976 Feb 13.3	70.98	95.28	6910	268	796	0.038	72

PLE-LC133/1	1978 Jan 5			1978 Jan 5.20	70.93	87.72	6540	149	174	0.002	284

D	Cosmos 801	1976-12 B	1976 Feb 5.61	Cylinder	8 long	1976 Feb 6.59	71.04	95.18	6906	280	775	0.036	83

rocket	[08659]	413 days	1500?	1.65 dia	1976 Feb 9.6	71.03	95.20	6906	283	773	0.036	78

1977 Mar 24			1977 Mar 23.53	70.98	88.30	6569	186	194	0.0006	70

D	Fragments	1976-12 C-S	15 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 802	1976-13 A	1976 Feb 11.37	Sphere-	6.5 long?	1976 Feb 11.42	65.02	89.57	6632	168	338	0.013	61

R	[Voskhod 11A57]	[08681]	13.84 days	cylinder	2.4 dia	1976 Feb 13.0	64.99	89.56	6631	172	334	0.012	62

BAI	1976 Feb 25.21	6300?		1976 Feb 13.7	64.98	89.33	6620	173	311	0.010	63						1976 Feb 18.44	64.98	89.23	6615	171	302	0.010	60

1976 Feb 19.12	64.98	89.40	6624	166	324	0.012	55

1976 Feb 24.46	64.98	89.28	6618	169	309	0.011	56

D	Cosmos 802	1976-13 B	1976 Feb 11.37	Cylinder	7.5 long	1976 Feb 11.55	64.99	89.45	6626	172	323	0.011	61

Block I 3rd stage 	[08686]	6 days	2500?	2.6 dia	1976 Feb 12.4	64.98	89.35	6621	170	316	0.011	58			1976 Feb 17			1976 Feb 16.12	64.98	88.37	6573	162	226	0.005	60

D	Cosmos 802	1976-13 D	1976 Feb 11.37	Cone	1.5 long?	1976 Feb 22.53	64.92	89.23	6616	163	311	0.011	58

motor*	[08707]	18 days	600? full	2 dia?	1976 Feb 22.7	64.98	89.25	6616	170	306	0.010	57

1976 Feb 29			1976 Feb 27.96	64.99	88.28	6568	153	226	0.006	52

D	Fragment	1976-13 C	[08706]	1976 Feb 25	14 days	1976 Feb 22.5	64.96	89.12	6609	171	290	0.009	61						1976 Feb 24.56	64.97	87.77	6542	148	180	0.002	55

D	Fragment	1976-13 E	[08708]	1976 Feb 26	15 days	1976 Feb 25.45	64.97	89.02	6604	169	282	0.009	61

1976 Feb 25.63	64.98	88.78	6593	162	266	0.008	59

*	Jettisoned from 1975-13 A about 1976 Feb 22.

Cosmos 803	1976-14 A	1976 Feb 12.54	Cylinder?	4 long?	1976 Feb 12.66	65.87	96.28	6959	547	613	0.005	5

[Kosmos 11K65M	[08688]	40 years		2 dia?	1976 Feb 15.3	65.85	96.39	6964	554	618	0.005	2

53731-286]	PLE-LC132				2004 Jul 6.87	65.85	94.50	6873	484	504	0.001	128

2021 Nov 21.81	65.85	93.72	6835	447	466	0.001	356

D	Cosmos 803	1976-14 B	1976 Feb 12.54	Cylinder	7.4 long	1976 Feb 12.66	65.87	96.28	6959	547	613	0.005	5

2nd stage	[08689]	2827 days	2200?	2.4 dia	1976 Feb 15.5	65.86	96.31	6960	546	618	0.005	5

1983 Nov 9			1983 Nov 9.34	65.81	87.18	6514	131	139	0.0007	258

D	Fragment	1976-14 C	[08690]	1981 Dec 9	2127 days	1976 Feb 13.33	65.86	96.35	6963	551	617	0.005	4						1981 Dec 9.65	65.80	87.72	6540	158	165	0.0005	238

D	Cosmos 804**	1976-15 A	1976 Feb 16.35	Cylinder?	4 long?	1976 Feb 16.4	65.15	93.08	6804	149	703	0.041	55

[Tsyklon 2]	[08694]	0.4 days?		2 dia?	1976 Feb 16.7	65.86	96.38	6964	556	615	0.004	3

BAI	1976 Feb 16.7?

D	Cosmos 804	1976-15 B	1976 Feb 16.35	Cylinder	8 long?	1976 Feb 17.7	65.12	92.36	6769	142	640	0.037	52

2nd stage	[08695]	10 days	1500?	2.5 dia?	1976 Feb 26.01	65.11	87.68	6538	121	198	0.006	62			1976 Feb 26

**	Cosmos 804 passed close to Cosmos 803 between 1976 Feb 16.41 and 16.681 then retrofired  with descent into Pacific Ocean?

D	DMSP 8 (OPS 5140)	1976-16 A	1976 Feb 19.33	Cone-	2.96 long?	1976 Feb 19.4	98.87	88.97	6601	90	355	0.020	328

[Thor Burner 2A 	[08696]	0.2 day?	cylinder?	0.94 to

#182]		1976 Feb 19	1355 full?	1.31 dia?

Marisat 1 *	1976-17 A	1976 Feb 19.94	Cylinder	2.4 long?	1976 Feb 25.7	2.4	1436.1	42163	35703	35867	0.002	-

Delta 2914 603	[08697]	>million years	655 full	1.9 dia?	1977 Apr 2.85	12.75	1436.13	42165	35775	35799	0.0003	31

#120]	CC-LC17B		362 empty		1997 Apr 2.85	12.76	1442.45	42289	35764	36057	0.003	81

Graveyard orbit	1997 Apr 14.91	12.79	1451.51	42466	36057	36119	0.001	272

2004 Jul 7.77	14.00	1451.30	42465	36034	36138	0.001	14

2021 Nov 21.88	9.70	1451.52	42466	36034	36141	0.001	163

D	Marisat 1	1976-17 B	1976 Feb 19.94	Cylinder	6.4 long	1976 Feb 20.31	28.63	92.42	6771	172	613	0.033	173

Delta 2nd stage	[08698]	26 days	annulus	1.52 and	1976 Feb 29.2	28.59	91.38	6729	175	527	0.026	219

1976 Mar 16	350?	2.44 dia	1976 Mar 15.50	28.57	88.13	6560	146	217	0.005	111

D	Marisat 1	1976-17 C	1976 Feb 19.94	Sphere-cone	1.32 long	1976 Mar 1.0	25.99	651.4	24895	182	36851	0.737	-

Star-37E PKM	[08702]	> 8615 days	66	0.94 dia	1977 Mar 1.0	25.1	624.0	24189	310	35311	0.724	-

After 1999 Sep 21#			1978 Jan 2.31	24.51	429.40	18854	191	24760	0.652	39

1995 Jan 1.14	24.38	139.07	8892	245	4781	0.255	82

1999 Sep 21.27	24.35	110.45	7626	233	2261	0.133	354

1999 ??	25.40	90.54		146	456	From Satcat

Marisat 1	1976-17 F	1976 Feb 19.94	-	-	Orbit similar to 1976-17 A

apogee motor	[NNA]	>million years	293 full

D	Fragment	1976-17 D	[08704]	1976 Mar 2	12 days	1976 Feb 20.95	28.59	92.27	6764	175	595	0.031	183

1976 Mar 2.52	28.58	90.18	6662	172	394	0.017	310

D	Fragment	1976-17 E	[08705]	1976 Feb 29	10 days	1976 Feb 21.01	28.59	92.33	6767	176	601	0.031	181

1976 Feb 24.84	28.58	91.60	6732	180	526	0.026	226

*	Maritime communication satellite

#	Space-Track has a decay date of 1982 Nov 27, 2473 days; but TLE’s were issued till 1999 Sep 21.

D	Cosmos 805*	1976-18 A	1976 Feb 20.59	Sphere-	7 long?	1976 Feb 20.8	67.13	89.72	6639	171	351	0.014	80

R	[Soyuz 11A511U]	[08699]	19.6 days	cylinder	2.4 dia	1976 Mar 5.42	67.13	89.02	6604	167	284	0.009	51

PLE-LC43/3	1976 Mar 11.2	6700?		1976 Mar 6.8	67.13	89.61	6634	168	343	0.013	55

1976 Mar 10.45	67.13	89.18	6613	159	310	0.011	51

D	Cosmos 805	1976-18 B	1976 Feb 20.59	Cylinder	7.5 long	1976 Feb 20.82	67.13	89.63	6635	166	347	0.014	80

Block I 3rd stage 	[08700]	7 days	2500?	2.6 dia	1976 Feb 24.1	67.13	89.00	6603	165	284	0.009	67			1976 Feb 27			1976 Feb 26.57	67.12	87.98	6553	149	200	0.004	67

D	Fragment	1976-18 C	[08703]	1976 Feb 22	2 days	1976 Feb 20.76	67.17	89.63	6635	165	347	0.014	80

1976 Feb 20.95	67.12	89.10	6608	139	320	0.014	80

*	No jettisoned engine was apparently tracked or designated. Yantar-2K #4

Ume 1 (ISS l)*	1976-19 A	1976 Feb 29.15	Cylinder	0.82 long	1976 Feb 29.41	69.63	105.15	7380	989	1014	0.002	230

[Nu-1 N-2(F)]	[08709]	1200 years	139	0.94 dia	1976 Mar 15.5	69.67	105.20	7382	994	1013	0.001	215

TAN-LC0				2004 Jul 10.74	69.67	105.02	7374	988	1003	0.001	137						2021 Nov 22.15	69.68	104.98	7372	988	1000	0.0008	135

Ume 1	1976-19 B	1976 Feb 29.15	Cylinder	1.74 long	1976 Feb 29.78	69.65	105.18	7382	992	1015	0.002	231

Nu 3rd stage	[08710]	600 years	667	1.65 dia	1976 Mar 15.5	69.68	105.22	7383	994	1015	0.001	207

2004 Jul 5.40	69.67	105.13	7379	991	1010	0.001	154

2021 Nov 21.82	69.68	105.12	7378	991	1008	0.001	162

*	Japanese Ionospheric Sounding Satellite.

D	Cosmos 806	1976-20 A	1976 Mar 10.34	Sphere-	6.5 long?	1976 Mar 10.39	71.46	89.65	6636	183	331	0.011	46

R	[Voskhod 11A57]	[08737]	12.89 days	cylinder	2.4 dia	1976 Mar 11.4	71.37	89.65	6634	178	334	0.012	41

BAI	1976 Mar 23.23	6300?		1976 Mar 21.3	71.37	89.82	6643	177	352	0.013	20

1976 Mar 22.40	71.37	89.77	6642	177	349	0.013	18

D	Cosmos 806	1976-20 B	1976 Mar 10.34	Cylinder	7.5 long	1976 Mar 10.58	71.37	89.50	6628	174	324	0.011	39

Block I 3rd stage 	[08738]	5 days	2500?	2.6 dia	1976 Mar 11.3	71.37	89.39	6621	174	312	0.010	35			1976 Mar 15			1976 Mar 14.53	71.37	88.22	6565	158	215	0.004	25

D	Cosmos 806	1976-20 C	1976 Mar 10.34	Cone	1.5 long?	1976 Mar 22.6	71.37	89.71	6637	173	345	0.013	17

Motor **	[08768]	20 days	600? full	2 dia?	1976 Mar 29.77	71.37	88.00	6554	154	198	0.003	1

1976 Mar 30

D	Fragment	l976-20 D	[08769]	1976 Mar 26	16 days	1976 Mar 22.65	71.37	89.48	6628	173	325	0.011	12

1976 Mar 25.31	71.35	88.23	6566	162	212	0.004	5

D	Fragment	l976-20 E	[08771]	1976 Mar 25	15 days	1976 Mar 23.46	71.38	89.62	6634	171	341	0.013	16

1976 Mar 24.64	71.36	88.72	6590	176	247	0.005	14

**	Jettisoned from 1976-20 A about 1976 Mar 22.

D	Molniya-1 33	1976-21 A	1976 Mar 11.83	Windmill +	3.4 long	1976 Mar 14.9	62.84	734.41	26965	491	40682	0.745	280

[Molniya 8K78M]	[08741]	5326 days	6 vanes	1.6 dia	1976 Mar 19.48	62.86	718.13	26565	470	39902	0.742	280

PLE	1990 Oct 10	1000?		1976 Mar 24.0	62.86	717.93	26560	487	39877	0.742	280

1976 Oct 9.70	62.64	98.33	7058	81	1278	0.085	268

D	Molniya-1 33	1976-21 B	1976 Mar 11.83	Cylinder	7.5 long	1976 Mar 12.83	62.83	91.48	6726	193	501	0.023	123

Block I 3rd stage 	[08742]	33 days	2500?	2.6 dia	1976 Apr 12.53	62.84	88.30	6569	167	212	0.003	133

1976 Apr 13

D	Molniya-1 33	1976-21 C	1976 Mar 11.83	Irregular	-	1976 Mar 11.87	62.80	91.50	6727	193	504	0.023	123

4th stage casing 	[08743]	25 days			1976 Mar 13.9	62.83	91.41	6722	192	496	0.023	129			1976 Apr 5			1976 Apr 5.05	62.84	88.10	6559	154	207	0.004	127

D	Molniya-1 33	1976-21 D	1976 Mar 11.83	Cylinder	2.0 long	1976 Sep 19.3	63.13	731.14	2688	451	40560	0.746	281

Block L 4th stage 	[09411]	5622 days	440	2.0 dia	1991 Jun 18.59	62.93	700.80	26135	121	39392	0.751	264

1991 Aug 2

Cosmos 807	1976-22 A	1976 Mar 12.56	-	-	1976 Mar 12.78	82.95	109.02	7560	395	1969	0.104	129

[Kosmos 11K65M	[08744]	35 years			1976 Mar 17.6	82.97	109.13	7564	398	1973	0.104	117

53746-310]	PLE-LC132				2004 Jul 11.15	82.93	102.35	7248	380	1395	0.067	294

2021 Nov 22.91	82.93	100.33	7153	369	1180	0.057	120

D	Cosmos 807	1976-22 B	1976 Mar 12.56	Cylinder	7.4 long	1976 Mar 13.01	82.96	108.92	7555	390	1963	0.104	128

2nd stage	[08745]	10698 days	2200?	2.4 dia	1976 Mar 20.3	82.97	109.00	7558	391	1968	0.104	109

2005 Jun 26			2004 Jul 5.27	82.89	92.93	6797	311	525	0.016	168

2005 Jun 26.70	82.85	87.50	6529	138	163	0.002	252

LES 8	1976-23 A	1976 Mar 15.06	Cylinder +	3.0 long	1976 Apr 1.0	25.0	1436.1	42165	35787	35787	0	-*

[Titan 3C 23C-12]	[08746]	>million	box	1.6 dia?	1977 Jan 24.98	25.21	1435.87	42160	35751	35812	0.0007	195

CC-LC40	years	454		2004 Jul 10.58	10.67	1436.05	42164	35726	35845	0.001	246

2021 Nov 22.35	19.14	1436.10	42165	35662	35911	0.003	100

LES 9	1976-23 B	1976 Mar 15.06	Cylinder	3.0 long	1976 Apr 1.0	25.0	1436.1	42165	35787	35787	0	-*

[08747]	>million	+ box	1.6 dia?	1977 Jan 21.79	25.20	1436.20	42167	35773	35803	0.003	289

years	454		2004 Jul 4.36	10.65	1436.17	72166	35673	35903	0.003	251

2021 Nov 21.30	19.10	1436.15	42166	35698	35877	0.002	127

Solrad 11A #	1976-23 C	1976 Mar 15.06	Annulus +	0.41 deep	1976 Jul 1.0	25.7	7344.3	125160	118383	119180	0.003	-*

[08748]	>million	4 vanes	0.61 inner	No current elements

years	181	1.47 outer	2020 Aug 6.09	28.79	7317.50	124854	117095	119855	0.011	70

diameter	2021 Oct 17.81	25.26	7318.20	124862	117094	119872	0.011	108

Solrad 11B	1976-23 D	1976 Mar 15.06	Annulus +	size	1976 Mar 27.36	25.19	7124.42	122648	115747	116792	0.004	118

[08749]	>million	4 vanes	same as	1976 Jul 1.0	25.6	7116.7	122560	115720	116645	0.004	-*

years	181	1976-23 C	No current elements

D	Titan 3C	1976-23 E	1976 Mar 15.06	Cylinder	6 long	1976 Mar 15.2	28.60	87.42	6532	148	160	0.001	130

Titan 3C 2nd stage	[08750]	< 1 day	1900	3.0 dia

1976 Mar 15

Transtage 30	1976-23 F	1976 Mar 15.06	Cylinder	6 long?	1976 Dec 3.30	25.38	1465.45	42737	35742	36975	0.014	216

[08751]	>million	1500?	3.0 dia	2004 Jul 6.98	10.52	1465.45	42738	35820	36898	0.013	173

years			2021 Nov 23.15	18.29	1464.50	42719	35808	36873	0.012	55

Solrad 11A 	1976-23 G	[08752]			No elements till 2020 Nov 20

Apogee motor					2020 Nov 20.80	24.02	3466.62	75875	36045	102947	0.441	24

2021 Nov 7.35	23.02	3467.17	75883	36160	102849	0.439	31

Solrad 11B	1976-23 H	[08753]			No elements till 2020 Dec 31

Apogee motor					2020 Dec 31.48	29.12	7694.47	129106	117332	128123	0.042	42

2021 Nov 17.49	25.90	7696.65	129130	117757	127746	0.039	60

Fragment Titan	1976-23 J	[08832]			1992 Jun 3.60	18.63	1465.48	42738	35709	37010	0.015	12

2nd stage					2004 Jul 5.08	10.53	1465.50	42738	35810	36910	0.013	173

2021 Nov 23.04	18.28	1465.47	42738	35753	36965	0.014	48

Fragment LES 8 9	1976-23 K	[13753]			1980 Nov 9.30	0.36	1420.92	41867	35479	35498	0.0002	278

Solrad 11A B					2004 Jul 10.95	14.17	1420.85	41886	35474	35501	0.0003	110

2021 Nov 23.55	8.90	1420.87	41866	35479	35496	0.0002	33

*	Approximate orbits.

#	Solar radiation.

D	Cosmos 808	1976-24 A	1976 Mar 16.73	Cylinder	5 long?	1976 Mar 16.71	81.26	97.18	7002	616	631	0.001	280

[Vostok 8A92M]	[08754]	6458 days	+ 2 vanes?	1.5 dia?	1976 Mar 17.46	81.25	97.03	6995	601	632	0.002	267

PLE	1993 Nov 20	2500?		1976 Mar 24.8	81.25	97.10	6996	602	634	0.002	247

1993 Nov 20.24	81.17	87.22	6515	129	143	0.001	245

D	Cosmos 808	1976-24 B	1976 Mar 16.73	Cylinder	3.8 long	1976 Mar 16.85	81.27	97.13	7000	599	643	0.003	222

Block E 3rd stage 	[08755]	8392 days	1440	2.6 dia	1976 Mar 22.5	81.26	97.18	7000	563	681	0.008	182				1999 May 8.30			1999 May 8.27	81.20	87.17	6513	128	140	0.0009	270

D	Cosmos 809	1976-25 A	1976 Mar 18.39	Sphere-	5.0 long	1976 Mar 18.44	65.01	89.42	6625	197	295	0.007	52

R	[Soyuz-U 11A511U]	[08758]	11.88 days	cylinder	2.4 dia	1976 Mar 18.63	65.01	89.55	6631	204	300	0.007	77

No.78026-222]	BAI	1976 Mar 30.27	5700?		1976 Mar 19.4	65.03	89.55	6631	205	300	0.007	61

1976 Mar 29.44	65.03	89.42	6624	200	291	0.007	54

D	Cosmos 809	1976-25 B	1976 Mar 18.39	Cylinder	7.5 long	1976 Mar 18.50	65.02	89.42	6624	202	290	0.007	55

Block I 3rd stage 	[08759]	8 days	2500?	2.6 dia	1976 Mar 20.2	65.03	89.26	6617	196	281	0.006	47			1976 Mar 26				1976 Mar 25.42	65.03	88.02	6555	172	181	0.0007	38

D	Fragment	1976-25 C	[08760]	1976 Mar 19	1 day	1976 Mar 18.69	65.05	89.13	6610	197	267	0.005	53

1976 Mar 19.25	65.02	88.58	6583	188	221	0.002	48

D	Fragment	1976-25 D	[08761]	1976 Mar 19	1 day	1976 Mar 18.75	65.12	90.05	6655	199	354	0.012	64

D	Molniya-1 34	1976-26 A	1976 Mar 19.82	Windmill +	3.4 long	1976 Mar 20.36	62.95	696.38	26025	418	38875	0.739	280

[Molniya 8K78M]	[08762]	3343 days	6 vanes	1.6 dia	1976 Mar 23.3	62.93	696.52	26027	416	38882	0.739	280

BAI	1985 May 14	10007		1976 Mar 29.2	62.73	717.38	26548	617	39722	0.737	280							1985 May 14.34	63.63	94.25	6861	81	884	0.059	260

D	Molniya-1 34	1976-26 B	1976 Mar 19.82	Cylinder	7.5 long	1976 Mar 19.93	63.00	91.03	6704	229	421	0.014	54

Block I 3rd stage 	[08763]	39 days	2500?	2.6 dia	1976 Mar 20.4	63.01	91.03	6704	231	421	0.014	52				1976 Apr 27			1976 Apr 26.06	63.00	89.20	6564	177	194	0.001	65

D	Molniya-1 34	1976-26 C	1976 Mar 19.82	Irregular	-	1976 Mar 20.06	63.01	91.03	6739	219	502	0.021	64

4th stage casing 	[08767]	49 days			1976 Mar 20.2	63.01	91.76	6740	220	503	0.021	64

1976 May 7			1976 May 6.52	63.02	88.23	6565	171	203	0.002	67

D	Molniya-1 34	1976-26 D	1976 Mar 19.82	Cylinder	2.0 long	1976 Apr 4.4	63.01	696.66	26031	494	38812	0.736	280

Block L 4th stage 	[08792]	744 days	440	2.0 dia	1976 Sep 6.29	62.97	696.63	26022	461	38845	0.737	280				1978 Apr 2			1984 Dec 23.15	63.84	91.58	6731	76	628	0.041	260

D	KH 8-46 (OPS 7600)	1976-27 A	1976 Mar 22.76	Cylinder	8 long?	1976 Mar 22.86	96.32	89.38	6622	135	352	0.016	123

[Titan 24B-18	[08770]	57 days	3000?	1.5 dia	1976 Mar 22.99	96.40	89.12	6614	129	333	0.015	137

(3B-52) Agena D]	VDB-SLC4W	1976 May 18			1976 Mar 24.7	96.40	89.25	6614	125	347	0.017	136							1976 May 16.29	96.44	88.85	6596	127	307	0.014	114

1976 May 18.94	96.42	87.37	6523	65	223	0.012	134

D	Cosmos 810	1976-28 A	1976 Mar 26.63	Sphere-	6.5 long?	1976 Mar 26.74	62.83	89.65	6636	180	335	0.012	76

R	[Voskhod 11A57]	[08772]	12.7 days	cylinder	2.4 dia	1976 Mar 27.4	62.82	89.67	6637	181	338	0.012	74

PLE	1976 Apr 8.3	6300?		1976 Mar 28.5	62.81	89.36	6622	169	318	0.011	66							1976 Apr 3.24	62.81	89.18	6612	167	301	0.010	67

1976 Apr 7.46	62.81	89.18	6613	165	303	0.010	67

D	Cosmos 810	1976-28 B	1976 Mar 26.63	Cylinder	7.5 long	1976 Mar 26.80	62.80	89.55	6631	178	327	0.011	74

Block I 3rd stage 	[08773]	6 days	2500?	2.6 dia	1976 Mar 27.2	62.80	89.49	6628	179	321	0.011	73

1976 Apr 1			1976 Mar 31.74	62.78	88.02	6555	152	201	0.004	71

D	Cosmos 810	1976-28 D	1976 Mar 26.63	Cone	1.5 long?	1976 Apr 6.59	62.71	89.07	6607	160	297	0.010	70

motor*	[08797]	15 days	600? full	2 dia?	1976 Apr 7.0	62.81	89.02	6605	166	288	0.009	67

1976 Apr 10			1976 Apr 10.59	62.80	87.68	6538	140	179	0.003	164

D	Fragment	1976-28 C	[08796]	1976 Apr 7	12 days	1976 Apr 6.53	62.80	88.87	6597	163	274	0.008	71

1976 Apr 7.45	62.81	88.02	6555	149	203	0.004	62

D	Fragment	1976-28 E	[08798]	1976 Apr 7	12 days	1976 Nov 6.59	62.83	87.92	6550	133	209	0.006	15

*	Jettisoned from 1976-28 A about 1976 Apr 6.

RCA Satcom 2 *	1976-29 A	1976 Mar 26.95	Box + vanes	1.62 high	1976 Jul 1.0	0.0	1436.2	42166	35759	35817	0.0007	-

[Delta 3914 610	[08774]	>million years	868 full	1.25 wide	1984 May 27.65	0.12	1436.08	42165	35779	35793	0.0002	275

#121]	CC-LC17A		463 empty	1.25 deep	1984 May 29.64	0.18	1438.45	42217	35828	35848	0.0002	278

1984 Jun 11.63	0.18	1438.70	42216	35830	35845	0.0002	284

1984 Jun 13.67	0.18	1440.03	42242	35854	35872	0.0002	352

1984 Jun 19.64	0.22	1440.05	42242	35838	35889	0.0006	259

1984 Jun 24.63	0.16	1436.45	42712	35789	35797	0.0001	345

1985 Jan 20.05	0.44	1435.97	42162	35779	35788	0.0001	156

Graveyard orbit	1985 Feb 15.19	0.53	1460.05	42632	35990	36518	0.006	189

2004 Jul 6.53	13.3	1460.10	42663	35997	36532	0.007	27

2021 Nov 21.65	12.26	1460.08	42633	35998	36511	0.006	194

D	RCA Satcom 2	1976-29 B	1976 Mar 26.95	Cylinder	6.4 long	1976 Mar 27.08	28.49	106.72	7453	176	1973	0.121	175

Delta 2nd stage	[08775]	251 days	annulus	1.52 and	1976 Mar 28.4	28.40	106.67	7457	191	1966	0.119	187

1976 Dec 2	350?	2.44 dia	1976 Nov 30.60	28.36	88.80	6594	148	283	0.010	102

D	RCA Satcom 2	1976-29 C	1976 Mar 26.95	Sphere-	1.32 long	1976 Mar 27.0	27.2	635.6	24487	185	36032	0.732	-

Star-37E PKM	[08793]	824 days	cone 66	0.94 dia	1976 Jul 4.87	27.10	625.80	24236	241	35473	0.727	240

1978 Jun 28			1977 May 4.50	26.35	601.38	23601	163	34282	0.723	79

*	Stationed over equator at 119ºW; in 1984 repositioned at 139ºW. In 1985 decommissioned and drifting at 5.9º W per day in graveyard orbit.

D	Cosmos 811	1976-30 A	1976 Mar 31.54	Sphere-	5.9 long	1976 Mar 31.59	72.87	89.90	6648	203	335	0.010	65

R	[Soyuz 11A511M]	[08781]	11.8 days	cylinder	2.4 dia	1976 Apr 1.3	72.85	89.95	6650	206	338	0.010	61

PLE	1976 Apr 12.3	5900?		1976 Apr 11.83	72.85	89.78	6643	202	326	0.009	35

D	Cosmos 811	1976-30 B	1976 Mar 31.54	Cylinder	7.5 long	1976 Apr 1.03	72.85	89.78	6642	201	325	0.009	57

Block I 3rd stage 	[08782]	10 days	2500?	2.6 dia	1976 Apr 1.3	72.85	89.80	6643	206	323	0.009	56				1976 Apr 10			1976 Apr 9.57	72.83	88.10	6559	169	191	0.002	28

D	Capsule	1976-30 E	1976 Mar 31.54	Ellipsoid	0.9 long	1976 Apr 12.3	72.85	89.70	6638	201	318	0.009	-

[08804]	15 days	200?	1.9 dia	1976 Apr 12.45	72.85	89.70	6638	201	318	0.009	35

1976 Apr 15			1976 Apr 14.99	72.84	88.13	6561	173	191	0.001	22

D	Fragment	1976-30 C	[08783]	1976 Apr 13	13 days	1976 Apr 1.21	72.85	89.37	6630	204	299	0.007	73

1976 Apr 5.00	72.84	89.15	6611	195	269	0.006	65

D	Fragment	1976-30 D	[08803]	1976 Apr 14	14 days	1976 Apr 1245	72.85	89.68	6638	201	317	0.009	35

1976 Apr 14.12	72.85	88.50	6579	169	231	0.005	18

D	Fragment	1976-30 F	[08805]	1976 Apr 15	15 days	1976 Apr 12.45	72.81	89.70	6638	205	314	0.008	34

D	Cosmos 812	1976-31 A	1976 Apr 6.18	Cylinder +	2 long?	1976 Apr 6.43	74.03	95.17	6905	506	547	0.003	342

[Kosmos 11K65M	[08794]	1668 days	paddles?	1 dia?	1976 Apr 12.5	74.03	95.21	6906	508	548	0.003	332

53731-280]	PLE-LC132	1980 Oct 30	900?		1980 Oct 30.00	73.97	87.95	6551	166	179	0.001	238

D	Cosmos 812	1976-31 B	1976 Apr 6.18	Cylinder	7.4 long	1976 Apr 7.09	74.03	95.05	6900	498	544	0.003	353

2nd stage	[08795]	1735 days	2200?	2.4 dia	1976 Apr 22.3	74.03	95.10	6901	499	546	0.003	332

1981 Jan 5			1980 Dec 31.26	74.00	88.82	6594	212	219	0.0006	174

D	Fragment	1976-31 C	[09836]	1978 Jul 18	864 days	1977 Feb 16.19	74.05	94.12	6855	445	506	0.004	299							1977 Sep 23.51	74.04	92.67	6783	385	424	0.003	153

D	Fragment	1976-31 D	[09990]	1978 Feb 27	692 days	1977 May 16.42	73.98	94.32	6864	468	503	0.003	135

1977 Dec 30.08	73.97	92.32	6767	375	401	0.002	307

Meteor-1 24	1976-32 A	1976 Apr 7.55	Cylinder +	5 long?	1976 Apr 7.61	81.27	102.30	7246	842	892	0.003	265

[Vostok 8A92M]	[08799]	500 years	2 vanes	1.5 dia?	1976 Apr 21.6	81.26	102.33	7246	843	893	0.003	233

PLE		2200?		2004 Jul 6.22	81.26	102.03	7234	831	889	0.003	280							2021 Nov 24.21	81.26	102.02	7232	829	878	0.003	263

Meteor-1 24	1976-32 B	1976 Apr 7.55	Cylinder	3.8 long	1976 Apr 9.39	81.26	102.37	7249	826	916	0.006	203

Block E 3rd stage [08800]	400 years	1440	2.6 dia	1976 Apr 20.6	81.26	102.43	7251	827	918	0.006	172

2004 Jul 6.90	81.25	102.15	7239	791	929	0.009	246

2021 Nov 24.31	81.25	102.10	7237	790	927	0.009	275

D	Cosmos 813	1976-33 A	1976 Apr 9.36	Sphere-	5.0 long	1976 Apr 9.7	81.34	88.98	6601	210	236	0.002	358

R	[Voskhod 11A57]	[08801]	11.85 days	cylinder	2.4 dia	1976 Apr 18.24	81.34	88.78	6593	203	226	0.002	320

PLE	1976 Apr 21.21	5700?

D	Cosmos 813	1976-33 B	1976 Apr 9.36	Cylinder	7.5 long	1976 Apr 9.7	81.34	88.93	6598	206	234	0.002	352

Block I 3rd stage 	[08802]	5 days	2500?	2.6 dia	1976 Apr 14.14	81.34	87.52	6530	151	151	0	17

1976 Apr 14

D	Cosmos 814*	1976-34 A	1976 Apr 13.72	Cylinder?	4 long?	1976 Apr 13.71	65.07	90.47	6676	116	479	0.027	41

[Tsyklon 2]	[08806]	< 0.28 day		2 dia?

BAI-LC90	1976 Apr 13

D	Cosmos 814	1976-34 B	1976 Apr 13.72	Cylinder	8 long?	1976 Apr 13.83	65.11	90.38	6672	139	447	0.023	46

2nd stage	[08807]	3 days	1500?	2.5 dia?	1976 Apr 16.14	65.11	88.62	6585	131	281	0.011	45

1976 Apr 16

*	Cosmos 814 passed close to Cosmos 803 about 1976 Apr 13.75, then intentionally re-entered?

NATO 3A	1976-35 A	1976 Apr 22.87	Cylinder	2.23 long	1976 Apr 23.5	26.99	630.89	24418	177	3590 2	0.732	184

Delta 2914 608	[08808]	>million years	720 full	2.2 dia	1976 May 1.0	2.9	1423.4	41914	35209	35863	0.008	-

#122]	CC-LC17B		310 empty		1976 Oct 1.0	2.65	1436.2	42166	35778	35797	0.0002	-

1988 Dec 13.02	6.87	1436.10	42165	35776	35797	0.0003	208							1989 Jan 30.00	6.99	1439.90	42239	35779	35942	0.002	225

1989 Jan 21.98	7.05	1439.98	42241	35779	35946	0.002	226

1989 Mar 28.98	7.12	1439.98	42241	35779	35945	0.002	230

Relocated		1989 Apr 11.97	7.17	1436.08	42165	35783	35789	0.00007	133

1991 Jul 4.23	9.01	1435.62	42155	35747	35807	0.0007	93

1991 Sep 9.00	9.12	1437.98	42202	35794	35853	0.0007	346

1991 Dec 30.00	9.35	1437.07	42184	35776	35834	0.0007	332

1992 Dec 14.59	10.03	1437.92	42201	35791	35853	0.0007	349

Graveyard orbit	1992 Dec 17.53	10.05	1442.35	42287	35806	36011	0.002	354

2004 Jul 7.65	13.27	1442.22	42285	35792	36020	0.003	104

2021 Nov 24.86	8.76	1442.18	42284	35807	36004	0.002	284

D	NATO 3A	1976-35 B	1976 Apr 22.87	Cylinder +	6.4 long	1976 Apr 23.4	28.23	93.39	6826	179	717	0.039	175

Delta 2nd stage	[08809]	38 days	annulus	1.52 and	1976 May 29.15	28.21	88.42	6575	152	240	0.007	241

1976 May 30	3507	2.44 dia

D	NATO 3A	1976-35 C	1976 Apr 22.87	Sphere-	1.32 long	1976 Apr 29.2	26.99	630.39	24404	201	35850	0.730	187

Star-37E PKM	[08810]	544 days	cone 66	0.94 dia	1977 Apr 12.47	26.41	585.50	23184	191	33419	0.717	55

1977 Oct 18

D	Cosmos 815	1976-36 A	1976 Apr 28.40	Sphere-	5.9 long	1976 Apr 29.13	81.34	88.57	6601	215	229	0.001	11

R	[Voskhod 11A57]	[08811]	12.9 days	cylinder	2.4 dia	1976 Apr 29.44	81.33	88.95	6601	214	232	0.001	16

PLE	1976 May 11.3	5900?		1976 May 9.45	81.33	88.83	6595	210	224	0.001	332

D	Cosmos 815	1976-36 B	1976 Apr 28.40	Cylinder	7.5 long	1976 Apr 28.45	81.34	88.83	6595	207	225	0.001	340

Block I 3rd stage 	[08813]	4 days	2500?	2.6 dia	1976 Apr 29.1	81.33	88.82	6593	207	222	0.001	337

1976 May 2			1976 May 1.65	81.33	88.12	6560	182	182	0	341

D	Capsule **	1976-36 F	1976 Apr 28.40	El1ipsoid	0.9 long	1976 May 10.68	81.30	88.78	6593	208	221	0.001	299

[08830]	22 days	200?	1.9 dia	1976 May 11.1	81.30	88.78	6591	207	219	0.001	297				1976 May 20			1976 May 19.83	81.31	87.35	6522	140	147	0.0005	310

D	Fragments	1976-36 C	[08815]	1976 May 1	3 days	1976 Apr 28.63	81.31	88.50	6579	190	211	0.002	192

D	Fragments	1976-36 D	[08816]	1976 May 1	3 days	1976 Apr 28.88	81.27	89.03	6605	218	234	0.001	17

1976 Apr 29.69	81.29	88.73	6590	208	216	0.0006	14

D	Fragments	1976-36 E	[08817]	1976 May 3	5 days	1976 Apr 28.76	81.32	89.53	6630	216	287	0.005	64

1976 Apr 29.69	81.32	89.38	6623	215	273	0.004	56

D	Fragments	1976-36 G	[08831]	1976 May 13	15 days	1976 May 10.68	81.31	88.58	6583	192	218	0.002	282

D	Fragments	1976-36 H	[08841]	1976 May 15	17 days	1976 May 14.05	81.38	88.73	6590	192	231	0.003	325

1976 May 15.11	81.29	88.68	6588	182	236	0.004	304

**	Ejected from 1976-36 A about 1976 May 10.

D	Cosmos 816	1976-37 A	1976 Apr 28.57	Cylinder?		1976 Apr 29.0	65.83	94.56	6876	481	515	0.002	357

[Kosmos 11K65M	[08812]	1305 days			1976 May 2.49	65.83	94.55	6875	480	514	0.003	359

53746-301]	PLE-LC132	1979 Nov 24			1979 Nov 19.58	65.80	89.43	6625	238	254	0.001	251

D	Cosmos 816	1976-37 B	1976 Apr 28.57	Cylinder	7.4 long	1976 Apr 29.40	65.83	94.45	6870	470	513	0.003	356

2nd stage	[08814]	1297 days	2200?	2.4 dia	1976 Apr 29.7	65.83	94.46	6871	471	515	0.003	356

1979 Nov 16			1979 Nov 16.53	65.80	87.38	6524	143	147	0.0003	265

D	Fragments **	1976-37 C-AA  23 pieces, all have decayed		For orbital information see extra pages at the end of the year

**	Romb radar callibration subsatellites; one not catalogued or deployed.

NOSS 1 (OPS6431) *	1976-38 A	1976 Apr 30.80	Cylinder	-	1976 May 1.4	63.46	107.47	7488	1092	1128	0.002	277

[Atlas 59 F	[08818]	1600 years			2004 Jul 7.10	63.31	106.53	7445	435	1697	0.085	44 #

Star-37E]	VDB-SLC3W				2021 Aug 24.96	63.33	103.65	7309	523	1339	0.056	158

Atlas stage	1976 38 B	1976 Apr 30.80			No elements available

[08819]

SSU 1-1	1976-38 C	1976 Apr 30.80	Box	0.3 x 0.9	1976 May 20.5	63.44	107.49	7489	1093	1129	0.002	88

[08835]	1600 years	aerials?	x 2.4?	2004 Jul 6.90	63.31	106.53	7444	437	1694	0.084	49 #

2019 May 8.21	63.33	104.30	7340	485	1438	0.065	145

2021 Nov 24.54	63.34	104.27	7338	548	1371	0.056	158

SSU 1-2	1976-38 D	1976 Apr 30.80	Box	0.3 x 0.9	1976 May 20.6	63.43	107.50	7490	1093	1130	0.002	73

[08836]	1600 years	aerials?	x 2.4?	2004 Jul 5.92	63.31	106.58	7447	437	1699	0.085	44 #

2019 Jul 1.65	63.33	104.32	7341	490	1434	0.064	146

2021 Nov 24.66	63.34	104.27	7339	549	1371	0.056	158

SSU 1-3	1976-38 J	1976 Apr 30.80	Box	0.3 x 0.9	1976 Jul 1.0	63.45	107.49	7489	1083	1139	0.004	-

[08884]	1600 years	aerials?	x 2.4?	2004 Jul 6.91	63.32	106.52	7444	438	1693	0.084	49#

2016 Jan 4.75	63.29	104.42	7346	419	1514	0.075	122#

2019 Apr 23.58	63.32	103.95	7324	472	1418	0.065	145

2021 Nov 24.48	63.34	103.90	7321	538	1348	0.055	160

Fragments	1976- 38 E	[08839]			No elements available

Fragments	1976- 38 F	[08842]			No elements available

Fragments	1976- 38 G	[08843]			No elements available

Fragments	1976- 38 H	[08859]			No elements available

Fragments	1976- 38 K	[09796]			No elements available

Fragments	1976- 38 L	[09996]			No elements available

*	Navy Ocean Surveillance Satellite: some of the objects listed as fragments may also be payloads. Aka Whitecloud 1.

#	Orbits from amateur observations. After 2019 Apr 23 TLE’s were issued for objects C, D and J.

L	Lageos*	1976-39 A	1976 May 4.33	Sphere	0.60 dia	1976 May 5.8	109.86	225.41	12269	5837	5945	0.004	258

[Delta 2913 609	[08820]	> million years	411		1976 Jun 14.11	109.86	225.47	12271	5840	5945	0.004	252

#123]	VDB-SLC2W				2004 Jul 6.33	109.86	225.28	12271	5838	5947	0.004	219

2021 Nov 24.54	109.85	225.47	12271	5837	5948	0.005	299

D	Lageos	1976-39 B	1976 May 4.33	Sphere-	1.32 long	1976 May 6.0	109.69	153.42	9493	309	5920	0.296	176

Delta 3rd stage	[08821]	5619 days	cone 77	0.94 dia	1991 Sep 21.94	109.48	87.57	6533	138	170	0.002	351

1991 Sep 22

Lageos	1976-39 C	1976 May 4.33	Sphere-	0.98 long?	1976 May 7.5	109.84	225.42	12269	5837	5945	0.004	260

Star-27 AKM	[08822]	50000 years	cone 50?	0.76 dia?	1976 May 10.35	109.87	225.40	12269	5836	5944	0.004	258

2004 Jul 6.47	109.86	225.38	12269	5837	5943	0.004	217

2021 Nov 23.56	109.85	225.38	12269	5833	5947	0.005	294

D	Fragment  (YO) #	1976-39 D	[14514]	1993 Dec 8	6488 days	1981 Jun 2.17	109.99	138.78	8880	302	4700	0.248	29

1993 Dec 8.33	109.90	88.05	6557	161	195	0.003	146

*	LAser GEOdynamic Satellite covered with retro-reflectors. # Piece of the de-spin mechanism.

D	Cosmos 817	1976-40 A	1976 May 5.33	Sphere-	5.9 long?	1976 May 5.45	64.99	89.48	6626	172	323	0.011	62

R	[Voskhod 11A57]	[08823]	12.9 days	cylinder	2.4 dia	1976 May 6.1	64.99	89.47	6627	173	324	0.011	63

BAI	1976 May 18.2	5900?		1976 May 17.48	64.99	89.22	6615	170	302	0.010	56

D	Cosmos 817	1976-40 B	1976 May 5.33	Cylinder	7.5 long	1976 May 5.57	65.00	89.38	6622	172	315	0.011	64

Block I 3rd stage 	[08824]	5 days	2500?	2.6 dia	1976 May 6.1	65.00	89.30	6618	173	307	0.010	62				1976 May 10			1976 May 9.64	65.00	88.15	6561	158	208	0.004	61

D	Capsule? **	1976-40 D	1976 May 5.33	-	-	1976 May 16.99	64.99	89.17	6612	170	296	0.010	56

[08848]	19 days		2 dia?	1976 May 17.5	64.98	89.11	6609	169	292	0.009	56

1976 May 24			1976 May 22.84	64.98	88.08	6558	154	205	0.004	51

D	Fragment	1976-40 C	[08825]	1976 May 6	1 day	1976 May 5.63	65.10	88.80	6594	161	270	0.008	45

1976 May 5.69	65.00	88.75	6591	158	267	0.008	45

D	Fragment	1976-40 E	[08849]	1976 May 19	14 days	1976 May 16.92	65.02	88.97	6602	165	282	0.009	51

1976 May 18.58	64.97	87.83	6546	131	204	0.006	46

D	Fragment	1976-40 F	[08850]	1976 May 18	13 days	1976 May 18.41	64.96	88.95	6601	170	275	0.008	61

**	Ejected from 1976-40 A about 1976 May 17; possibly an engine.

D	Molniya-3 5	1976-41 A	1976 May 12.75	Windmill +	4.2 long?	1976 May 12.80	62.81	736.73	27021	642	40642	0.740	288

[Molniya 8K78M]	[08833]	5016 days	6 vanes	1.6 dia	1976 May 17.4	62.81	736.64	27019	625	40657	0.741	288

PLE-LC41/1	1990 Feb 4	15007		1976 May 18.9	62.87	717.90	26559	629	39733	0.736	288

1990 Jan 1.24	62.14	664.58	25227	88	37609	0.744	262

D	Molniya-3 5	1976-41 B	1976 May 12.75	Cylinder	7.5 long	1976 May 12.86	62.81	92.77	6789	213	608	0.029	118

Block I 3rd stage 	[08834]	85 days	2500?	2.6 dia	1976 May 14.5	62.81	92.74	6788	214	606	0.029	117				1976 Aug 5			1976 Aug 5.22	62.79	88.00	6554	161	190	0.002	142

D	Molniya 3-5	1976-41 C	1976 May 12.75	Irregular	-	1976 May 12.93	62.82	92.85	6793	208	620	0.030	126

4th stage casing 	[08837]	119 days			1976 May 16.3	62.80	93.04	6803	217	632	0.031	123

1976 Sep 8			1976 Sep 7.66	62.79	87.70	6539	161	161	0	357

D	Molniya 3-5	1976-41 D	1976 May 12.75	Cylinder	2.0 long	1976 May 14.84	62.87	733.53	26943	618	40511	0.740	288

Block L 4th stage 	[08844]	5106 days	440	2.0 dia	1976 May 20.4	62.89	733.56	26944	621	40511	0.740	288

1990 May 5			1990 Feb 6.65	61.91	710.55	26377	128	39868	0.753	262

D	Molniya-3 5	1976-41 E	1976 May 12.75			1976 May 16.22	62.83	92.90	6795	212	622	0.030	121

Ullage motor	[08847]	5166 days			1976 Jun 15.43	63.22	91.22	6713	202	466	0.020	123

1976 Jul 4

Comstar 1A *	1976-42 A	1976 May 13.94	Cylinder	2.82 long	1976 May 14.0	21.83	640.9	24626	550	35945	0.719	179

[Atlas SLV-3D(R)	[08838]	>million years	1516 full	6.34 long #	1976 Aug 1.0	0.1	1436.0	42163	35782	35788	0	-

AC-38 Centaur	CC-LC36A		792 empty	2.38 dia	1977 Jan 25.16	0.05	1436.15	42166	35776	35798	0.0003	83

D-1AR 5020D]					1983 Oct 17.20	0.01	1436.10	42165	35781	35791	0.0001	268

1983 Oct 26.14	0.05	1434.58	42135	35730	35784	0.0006	178

1983 Nov 23.03	0.02	1434.70	42138	35730	35788	0.0007	241

1983 Nov 29.99	0.06	1434.70	42138	35730	35788	0.0007	241

Relocated		1983 Nov 30.00	0.006	1436.17	42166	35782	35794	0.0001	71

1984 Oct 25.00	0.55	1436.18	42166	35787	35789	0.00003	18

Graveyard orbit	1984 Oct 28.12	0.58	1442.62	42292	35907	35920	0.0002	325

2004 Jul 9.79	13.20	1442.42	42289	35892	35928	0.0004	68

2021 Nov 24.76	11.45	1442.45	42289	35901	35920	0.0002	325

Comstar 1A	1976-42 B	1976 May 13.94	Cylinder	8.6 long	1976 May 14.0	21.82	649.2	24836	559	36357	0.721	179

Centaur 38 stage	[08840]	6000 years	1815	3.0 dia	1976 May 31.26	21.81	649.32	24839	611	36310	0.719	190

2004 Jul 4.78	21.62	647.55	24794	604	36226	0.718	6

2021 Nov 22.19	21.72	647.28	24787	653	36163	0.716	307

US communication satellite

#	Length after skirt and antenna deploy.

Meteor-1 25	1976-43 A	1976 May 15.57	Cylinder +	5 long?	1976 May 15.62	81.24	102.45	7253	845	904	0.004	256

[Vostok 8A92M]	[08845]	500 years	2 vanes	1.5 dia?	1976 May 15.84	81.23	102.30	7246	843	892	0.003	251

PLE		2200?		1976 May 16.8	81.24	102.39	7249	846	895	0.003	270

2004 Jul 7.13	81.26	102.05	7234	826	884	0.004	357

2021 Nov 25.20	81.26	102.02	7232	825	882	0.004	341

Meteor-1 25	1976-43 B	1976 May 15.57	Cylinder	3.8 long	1976 May 15.77	81.24	102.45	7253	850	900	0.003	252

Block E 3rd stage	[08846]	400 years	1440	2.6 dia	1976 May 16.7	81.24	102.49	7254	846	905	0.004	218

2004 Jul 6.65	81.26	102.23	7243	836	893	0.004	39

2021 Nov 24.95	81.23	102.22	7242	836	892	0.004	120

D	Cosmos 818	1976-44 A	1976 May 18.46	Ellipsoid	1.8 long	1976 May 18.64	71.06	92.05	6753	269	480	0.016	81

[Kosmos 11K63]	[08851]	293 days	400?	1.2 dia	1976 May 19.3	71.05	92.08	6754	271	481	0.016	80

PLE-LC133/1	1977 Mar 7			1977 Mar 7.04	71.03	87.28	6518	133	146	0.001	279

D	Cosmos 818	1976-44 B	1976 May 18.46	Cylinder	8 long	1976 May 18.64	71.05	91.82	6742	271	455	0.014	82

2nd stage	[08852]	163 days	1500?	1.65 dia	1976 May 21.5	71.05	91.82	6742	275	452	0.013	76

1976 Oct 28			1976 Oct 28.67	71.03	87.68	6538	160	160	0	43

D	Cosmos 819	1976-45 A	1976 May 20.29	Sphere-	5.0 long	1976 May 20.41	65.00	89.43	6625	200	292	0.007	37

R	[Voskhod 11A57]	[08853]	11.9 days	cylinder	2.4 dia	1976 May 21.0	65.00	89.44	6626	202	293	0.007	36

BAI	1976 Jun 1.2	5700?		1976 May 31.21	64.99	89.32	6619	198	283	0.006	30

D	Cosmos 819	1976-45 B	1976 May 20.29	Cylinder	7.5 long	1976 May 20.47	65.01	89.35	6621	202	283	0.006	32

Block I 3rd stage	[08854]	10 days	2500?	2.6 dia	1976 May 21.5	65.01	89.27	6617	203	275	0.005	25

1976 May 30			1976 May 29.43	65.00	88.23	6566	179	196	0.001	355

D	Fragment	1976-45 C	[08855]	1976 May 22	2 days	1976 May 20.72	65.00	89.45	6626	205	289	0.006	52

D	Cosmos 820	1976-46 A	1976 May 21.29	Sphere-	6.5 long?	1976 may 21.35	81.36	88.72	6590	207	215	0.0006	264

R	[Soyuz 11A511U]	[08856]	11.8 days	cylinder	2.4  dia	1976 May 22.0	81.36	88.78	6591	209	217	0.001	251

PLE-LC43/3	1976 Jun 2.1	6300?		1976 May 22.3	81.36	88.97	6601	209	236	0.002	273							1976 Jun 1.27	81.33	88.78	6593	201	227	0.002	237

D	Cosmos 820	1976-46 B	1976 May 21.29	Cylinder	7.5 long	1976 May 21.41	81.36	88.60	6583	196	213	0.001	279

Block I 3rd stage [08857]	3 days	2500?	2.6 dia	1976 May 21.8	81.36	88.63	6584	199	212	0.001	285

1976 May 24			1976 May 24.11	81.34	87.67	6538	155	163	0.0006	314

D	Cosmos 820	1976-46 E	1976 May 21.29	Cone	1.5 long?	1976  Jun 1.6	81.36	88.74	6589	199	223	0.002	-

motor*	[08870]	20 days	600? full	2 dia?	1976 Jun 2.32	81.36	88.72	6589	198	223	0.002	239

1976 Jun 10			1976 Jun 10.48	81.35	87.48	6529	150	150	0	19

D	Fragment	1976-46 C	[08858]	1976 May 21	< 0.67 day	1976 May 21.590	81.35	87.90	6549	101	240	0.011	305

1976 May 21.591	81.67	87.92	6550	86	257	0.013	300

D	Fragment	1976-46 D	[08869]	1976 Jun 4	14 days	1976 Jun 1.64	81.36	88.60	6583	186	223	0.003	248							1976 Jun 2.87	81.35	88.22	6565	182	190	0.0006	263

*	Jettisoned from 1976-46 A about 1976 Jun 1

P76-5 **	1976-47 A	1976 May 22.32	Octagonal	-	1976 May 22.44	99.67	105.67	7404	995	1057	0.004	163

[Scout B-1 S179CR]	[08860]	1400 years	cylinder +		1976 May 24.8	99.68	105.73	7406	996	1060	0.004	159

VDB-SLC5		vanes, 72		2004 Jul 6.51	99.94	105.35	7389	980	1041	0.004	270							2021 Nov 24.38	99.85	105.28	7386	977	1038	0.004	270

Altair	1976-47 B	1976 May 22.32	Cylinder	1.50 long	1976 May 24.87	99.67	105.67	7404	992	1058	0.004	158

Scout 4th stage	[08861]	800 years	24	0.46 dia	1976 May 25.9	99.68	105.73	7406	996	1060	0.004	154

2004 Jul 4.94	99.20	105.43	7393	983	1046	0.004	139

2021 Nov 24.40	99.90	105.38	7391	981	1044	0.004	59

Fragment	1976-47 C	[08867]			1976 Jun 8.69	99.37	106.57	7446	1010	1125	0.008	155

2004 Jul 6.47	99.28	106.22	7430	996	1107	0.008	134

2021 Nov 24.18	99.38	106.13	7426	993	1102	0.007	213

Fragment	1976-47 D	[08868]			1976 May 30.24	100.00	104.95	7371	951	1033	0.006	78

2004 Jul 6.21	100.03	104.42	7346	929	1005	0.005	78

2021 Nov 25.01	100.11	104.30	7340	925	998	0.005	260

**	Transit navigation	satellite modified for ionospheric experiments

D	Cosmos 821	1976-48 A	1976 May 26.38	Sphere-	6.5 long?	1976 May 26.6	72.83	89.69	6637	204	314	0.008	68

R	[Voskhod 11A57]	[08862]	12.8 days	cylinder	2.4 dia	1976 Jun 2.1	72.82	89.50	6628	169	330	0.012	51

PLE	1976 Jun 8.2	6300?		1976 Jun 6.38	72.82	89.52	6629	168	333	0.012	44

D	Cosmos 821	1976-48 B	1976 May 26.38	Cylinder	7.5 long	1976 May 26.37	72.83	89.53	6630	194	309	0.009	61

Block I 3rd stage 	[08863]	12 days	2500?	2.6 dia	1976 May 27.4	72.82	89.57	6631	204	302	0.007	69

1976 Jun 7			1976 Jun 6.50	72.81	87.98	6554	168	182	0.001	37

D	Cosmos 821	1976-48 D	1976 May 26.38	Cone	1.5 long?	1976 Jun 7.3	72.82	89.45	6625	167	326	0.012	41

motor	[08875]	19 days	600? full	2 dia?	1976 Jun 12.99	72.82	88.18	6563	153	216	0.005	26

1976 Jun 14

D	Fragment	1976-48 C	[08864]	1976 Jun 2	7 days	1976 May 26.74	72.81	89.63	6635	204	309	0.008	72

1976 May 28.24	72.84	89.65	6636	203	311	0.008	63

D	Fragment	1976-48 E	[08876]	1976 Jun 9	14 days	1976 Jun 7.31	72.82	89.40	6624	160	330	0.013	41

1976 Jun 8.05	72.82	89.35	6621	166	318	0.012	39

D	Fragment	1976-48 F	[08879]	1976 Jun 9	14 days	1976 Jun 8.43	72.83	89.12	6609	164	297	0.010	40

1976 Jun 8.98	72.81	88.58	6583	163	245	0.006	39

D	Cosmos 822	1976-49 A	1976 May 28.63	Octagonal	1.8 long?	1976 May 29.99	74.05	94.50	6873	278	710	0.031	131

[Kosmos 11K65M	[08865]	802 days	ellipsoid?	1.5 dia?	1976 Jun 1.9	74.05	94.54	6874	280	711	0.031	124	53716-328]	PLE-LC132	1978 Aug 8	550?		1978 Aug 6.62	74.02	88.03	6556	162	193	0.002	293

D	Cosmos 822	1976-49 B	1976 May 28.63	Cylinder	7.4 long	1976 May 30.19	74.05	94.38	6867	275	702	0.031	129

2nd stage	[08866]	574 days	2200?	2.4 dia	1976 Jun 1.5	74.05	94.42	6868	276	704	0.031	123				1977 Dec 23			1977 Dec 22.69	74.02	87.77	6543	162	166	0.0003	166

SDS 2 (OPS 7837)	1976-50 A	1976 Jun 2	Cylinder?	-	1976 Jun 10	63.3	703.8	26226	380	39315	0.742	270*

[Titan 34B (3B-55)	[08871]	100 years?			No elements available

Ascent Agena D]	VDB-SLC4W

SDS 2	1976-50 B	1976 Jun 2	Cylinder	6 long?	1976 Jun 18	63.3	700.2	26120	310	39175	0.744	270*

Agena D stage	[08872]	100 years?	700	1.5 dia	No elements available

62.79	512.45		135	29534	From Satcat

Fragment	1976 50 C	[44230]	1 piece, in orbit		62.71	551.89		164	31655	From satcat

*	Approximate orbits.

Cosmos 823	1976-51 A	1976 Jun 2.94	Cylinder?	1.3 long?	1976 Jun3.00	82.92	105.45	7394	1003	1028	0.002	45

[Kosmos 11K65M	[08873]	1200 years	700?	1.9 dia?	1976 Jun 4.0	82.96	105.04	7374	980	1011	0.002	265

53731-283]	PLE-LC132				2004 Jul 6.33	82.97	104.87	7367	972	1004	0.002	198

2021 Nov 26.63	82.97	104.85	7366	970	1004	0.002	163

Cosmos 823	1976-51 B	1976 Jun 2.94	Cylinder	7.4 long	1976 Jun 3.22	82.97	104.85	7366	975	1000	0.002	212

2nd stage	[08874]	600 years	2200?	2.4 dia	1976 Jun 3.8	82.96	104.92	7368	979	1000	0.001	252

2004 Jul 6.72	82.96	104.75	7361	964	1001	0.002	161

2021 Nov 26.53	82.96	104.72	7360	962	1000	0.003	85

D	Cosmos 824	1976-52 A	1976 Jun 8.30	Sphere-	6.5 long?	1976 Jun 8.54	71.37	89.78	6642	203	324	0.009	50

R	[Voskhod 11A57]	[08877]	12.9 days	cylinder	2.4 dia	1976 Jun 9.4	71.37	89.82	6643	204	325	0.009	48

BAI	1976 Jun 21.2	6300?		1976 Jun 10.2	71.37	89.39	6621	169	317	0.011	58							1976 Jun 20.54	71.38	89.42	6624	166	325	0.012	37

D	Cosmos 824	1976-52 B	1976 Jun 8.30	Cylinder	7.5 long	1976 Jun 8.54	71.37	89.68	6638	202	316	0.009	47

Block I 3rd stage 	[08878]	12 days	2500?	2.6 dia	1976 Jun 9.8	71.38	89.65	6634	203	309	0.008	42

1976 Jun 20			1976 Jun 20.54	71.37	87.65	6537	157	159	0.0001	348

D	Cosmos 824	1976-52 E	1976 Jun 8.30	Cone	1.5 long?	1976 Jun 20.7	71.38	89.37	6620	166	318	0.011	37

motor*	[08905]	19 days	600? full	2 dia?	1976 Jun 26.46	71.36	88.13	6561	151	214	0.005	22

1976 Jun 27

D	Fragment	1976-52 C	[08880]	1976 Jun 16	8 days	1976 Jun 8.54	71.36	90.43	6674	204	387	0.014	53

1976 Jun 14.59	71.34	88.88	6598	194	244	0.004	39

D	Fragment	1976-52 D	[08881]	1976 Jun 10	2 days	1976 Jun 8.54	71.42	89.38	6623	202	286	0.006	46

1976 Jun 9.77	71.38	88.70	6589	195	226	0.002	38

D	Fragment	1976-52 F	[08906]	1976 Jun 23	15 days	1976 Jun 20.60	71.32	89.15	6611	158	306	0.011	30

1976 Jun 22.38	71.37	88.37	6572	160	227	0.005	34

D	Fragment	1976-52 G	[08907]	1976 Jun 22	14 days	1976 Jun 21.40	71.37	89.20	6614	157	313	0.012	325

1976 Jun 22.08	71.30	88.53	6580	165	238	0.006	33

*	Jettisoned from 1976-52 A about 1976 Jun 20.

Marisat 3	1976-53 A	1976 Jun 10.01	Cylinder	2.4 long?	1976 Jun 10.0	26.00	653.01	24933	185	36925	0.737	182

[Delta 2914 601	[08882]	> million	655 full	1.9 dia?	1976 Jun 17.6	2.5	1436.6	42176	35788	35807	0.0002	-

#124]	CC-LC17A	years	362 empty		1977 Feb 24.00	2.28	1436.17	42166	35781	35794	0.0002	161

1995 Dec 24.83	11.42	1436.07	42164	35776	35795	0.0002	306

1996 Jan 19.66	11.45	1436.08	42165	35694	35878	0.002	130

1996 Sep 23.72	11.78	1436.07	42164	35766	35806	0.0005	147

1996 Sep 25.63	13.13	1436.15	42166	35779	35796	0.0002	155

1996 Sep 27.00	13.09	1495.17	43313	36425	37444	0.012	72

Graveyard orbit	1996 Oct 10.13	13.37	1501.62	43438	36489	37629	0.013	57

2000 Jan 3.50	14.46	1501.57	43437	36522	37594	0.012	88

2000 Dec 30.32	14.65	1501.55	43436	36528	37587	0.012	96

2004 Jul 10.09	15.09	1501.57	43437	36500	37616	0.013	124

2021 Nov 26.73	11.53	1501.55	43437	36516	37600	0.012	294

D	Marisat 3	1976-53 B	1976 Jun 10.01	Cylinder +	6.4 long	1976 Jun 13.76	28.54	93.85	6841	274	652	0.028	197

Delta 2nd stage	[08883]	441 days	annulus	1.52 and	1976 Jun 15.9	28.54	93.66	6839	273	649	0.028	221

1977 Aug 25	350?	2.44 dia	1977 Aug 25.04	28.52	87.83	6546	158	176	0.001	261

D	Marisat 3	1976-53 F	1976 Jun 10.01	Sphere-	1.32 long	1976 Jun 27. 3	25.96	647.1	24780	190	36613	0.735	192

Star-37E PKM	[08910]	4286 days	cone 66	0.94 dia

1988 Mar 5

Marisat 3	1976-53 G	1976 Jun  10.01	-	-		Orbit similar to 1976- 53A

apogee motor	[NNA]	> million	293 full

years

D	Delta 2nd st Fragm.	1976-53 C	[08887]	1976 Jul 2	22 days	1976 Jun 13.00	28.57	92.68	6785	198	615	0.031	195

1976 Jun 24.79	28.55	90.55	6680	179	425	0.018	344

D	Delta 2nd st Fragm.	1976-53 D	[08888]	1976 Jun 30	20 days	1976 Jun 13.71	28.58	92.12	6757	177	580	0.030	210

1976 Jun 15.81	25.56	91.83	6743	172	556	0.028	235

D	Delta 2nd st Fragm.	1976-53 E	[08902]	1976 Jul 1	21 days	1976 Jun 17.97	28.58	91.57	6730	176	527	0.026	260							1976 Jun 22.84	28.58	90.77	6691	173	451	0.021	318

Cosmos 825  *	1976-54 A	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 16.81	74.00	114.70	7820	1395	1488	0.006	103

[Kosmos 11K65M	[08889]	7000 years	40?	0.8 dia?	1976 Jun 25.3	73.99	114.74	7821	1397	1489	0.006	91

53731-277]	PLE-LC132				2004 Jul 6.08	74.00	114.67	7819	1395	1486	0.006	55

2021 Nov 26.60	74.00	114.67	7819	1395	1486	0.006	145

Cosmos 826 *	1976-54 B	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 18.6	74.00	116.33	7893	1484	1546	0.004	238

[08890]	10000 years	40?	0.8 dia?	2004 Jul 6.25	74.00	116.27	7891	1481	1544	0.004	322

2021 Nov 26.63	74.00	116.27	7891	1481	1544	0.004	357

Cosmos 827 *	1976-54 C	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 16.26	74.01	114.92	7830	1414	1489	0.005	119

[08891]	8000 years	40?	0.8 dia?	1976 Jun 22.2	74.00	114.96	7831	1415	1491	0.005	106

2004 Jul 4.93	74.00	114.90	7829	1413	1489	0.005	138

2021 Nov 26.92	74.00	114.88	7829	1412	1489	0.005	270

Cosmos 828 *	1976-54 D	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 17.14	74.00	115.13	7840	1433	1490	0.004	118

[08892]	9000 years	40?	0.8 dia?	1976 Jun 24.8	73.99	115.18	7841	1435	1491	0.004	106

2004 Jul 5.90	74.00	115.12	7839	1432	1489	0.004	207

2021 Nov 26.43	74.00	115.10	7839	1432	1488	0.004	21

Cosmos 829 *	1976-54 E	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 16.26	74.00	115.35	7849	1451	1490	0.002	133

[08893]	9000 years	40?	0.8 dia?	1976 Jun 18.7	74.00	115.39	7851	1453	1492	0.003	127

2004 Jul 6.50	74.00	115.32	7849	1449	1490	0.003	285

2021 Nov 26.88	74.00	115.32	7848	1450	1489	0.003	143

Cosmos 830 *	1976-54 F	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 18.75	73.99	115.57	7860	1469	1492	0.001	149

[08894]	10000 years	40?	0.8 dia?	1976 Jun 24.3	74.00	115.61	7861	1471	1495	0.001	141

2004 Jul 5.72	74.00	115.55	7859	1468	1492	0.002	20

2021 Nov 26.76	74.00	115.53	7858	1467	1493	0.002	279

Cosmos 831 *	1976-54 G	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 17.55	74.00	115.80	7870	1476	1507	0.002	198

[08895]	10000 years	40?	0.8 dia?	1976 Jun 21.5	74.00	115.85	7872	1477	1510	0.002	193

2004 Jul 5.86	74.00	115.78	7869	1474	1507	0.002	136

2021 Nov 27.20	74.00	115.77	7869	1475	1506	0.002	78

Cosmos 832 *	1976-54 H	1976 Jun 15.55	Spheroid	1.0 long?	1976 Jun 17.07	74.00	116.02	7880	1482	1521	0.002	236

[08896]	10000 years	40?	0.8 dia?	1976 Jun 21.3	74.00	116.07	7882	1484	1523	0.002	228

2004 Jul 5.83	74.00	116.00	7880	1482	1520	0.002	240

2021 Nov 26.77	74.00	116.00	7879	1481	1520	0.003	227

Cosmos 825-832	1976-54 J	1976 Jun 15.55	Cylinder	7.4 long	1976 Jun 17.09	73.96	117.95	7967	1487	1689	0.013	263

2nd stage	[08897]	20000 years	2200?	2.4 dia	1976 Jun 19.3	73.99	117.99	7968	1488	1692	0.013	260

2004 Jul 6.94	74.00	117.92	7966	1488	1687	0.013	108

2021 Nov 29.70	74.00	117.92	7966	1488	1687	0.012	87

*	Strela-1M

D	Cosmos 833	1976-55 A	1976 Jun 16.55	Sphere-	5.9 long?	1976 Jun 16.66	62.84	89.73	6640	179	343	0.012	71

R	[Voskhod 11A57]	[08898]	12.6 days	cylinder	2.4 dia	1976 Jun 17.5	62.82	89.44	6626	180	316	0.010	68

PLE	1976 Jun 29.2	5900?		1976 Jun 27.40	62.82	89.28	6618	177	301	0.009	70

D	Cosmos 833	1976-55 B	1976 Jun 16.55	Cylinder	7.5 long	1976 Jun 16.8	62.81	89.36	6622	177	311	0.010	64

Block I 3rd stage 	[08899]	7 days	2500?	2.6 dia	1976 Jun 22.64	62.81	88.08	6558	165	194	0.002	58

1976 Jun 23

D	Capsule?	1976-55 E	1976 Jun 16.55	-	-	1976 Jun 28.45	62.83	89.22	6615	176	296	0.009	68

[08920]	22 days		2 dia?	1976 Jun 29.3	62.82	89.16	6612	177	291	0.009	69

1976 Jul 8			1976 Jul 4.87	62.82	88.47	6577	167	231	0.005	68

D	Fragment	1976-55 C	[08900]	1976 Jun 17	1 day	1976 Jun 16.78	62.77	88.90	6599	172	269	0.007	60

D	Fragment	1976-55 D	[08901]	1976 Jun 21	5 days	1976 Jun 17.47	62.85	89.15	6611	165	300	0.010	85

D	Fragment	1976-55 F	[08921]	1976 Jul 1	15 days	1976 Jun 28.51	62.83	89.00	6604	174	276	0.008	7

1976 Jun 30.54	62.89	88.25	6567	139	237	0.008	103

D	Fragment	1976-55 G	[08926]	1976 Jun 30	14 days	1976 Jun 29.81	62.79	88.68	6588	170	249	0.006	70							1976 Jun 30.12	62.78	88.58	6575	168	224	0.004	80

*	Possibly an engine.

D	Intercosmos 15	1976-56 A	1976 Jun 19.67	Octagonal	1.8 long?	1976 Jun 23.01	74.04	94.60	6878	486	516	0.002	355

[Kosmos 11K65M	[08903]	1247.2 days	ellipsoid?	1.5 dia?	1976 Jun 24.5	74.04	94.65	6879	484	518	0.002	351

53731-276]	PLE-LC132/1	1979 Nov 18.9	550?		1979 Nov 17.88	74.00	88.40	6574	188	203	0.001	290

D	Intercosmos 15	1976-56 B	1976 Jun 19.67	Cylinder	7.4 long	1976 Jun 20.90	74.04	94.52	6873	474	516	0.003	357

2nd stage	[08904]	1305 days	2200?	2.4 dia	1976 Jun 23.9	74.04	94.57	6875	477	517	0.003	354

1980 Jan 15			1980 Jan 15.25	74.01	87.97	6552	171	176	0.0004	136

D	Salyut 5	1976-57 A	1976 Jun 22.76	Cylinder +	14 long	1976 Jun 23.0	51.60	88.85	6599	208	233	0.002	130

r	[Proton-K 290-02]	[08911]	412 days	3 wings	4.15 to	1976 Jun 25.4	51.59	89.00	6606	212	244	0.002	1ll

BAI-LC81L	1977 Aug 8 **	19000?	2.0 dia	1976 Jun 27.4	51.59	89.15	6614	214	257	0.003	100

1976 Jul 3.32	51.59	89.17	6612	212	254	0.003	123

1976 Jul 8.11	51.59	89.88	6647	264	273	0.0007	264

1976 Oct 9.24	51.59	89.55	6631	249	256	0.0005	315

1976 Oct 10.11	51.59	89.75	6641	253	271	0.001	213

1977 Jan 10.77	51.58	89.12	6609	225	236	0.0008	227

1977 Jan 14.35	51.58	89.38	6623	230	258	0.002	347

1977 Mar 1.35	51.58	89.52	6629	247	255	0.0006	81

1977 Mar 7.51	51.58	89.75	6641	253	272	0.001	280

1977 Apr 14.39	51.57	89.47	6627	240	256	0.001	77

1977 Apr 16.32	51.57	89.73	6640	257	265	0.0007	276

1977 Aug 8.08	51.56	88.15	6561	181	184	0.0002	268

D	Salyut 5	1976-57 B	1976 Jun 22.76	Cylinder	6.5 long?	1976 Jun 23.1	51.61	88.80	6596	211	225	0.001	112

third stage	[08912]	8 days		4 dia	1976 Jun 30.36	51.60	87.62	6535	139	173	0.003	254

1976 Jun  30

D	Fragments #	1976-57 C-K	8 pieces, all have decayed		For orbital information see extra pages at the end of the year

**	Salyut 5 was de-orbited; a film-capsule was ejected 1977 Feb 22 and recovered on 1977 Feb 26.4.

#	Some fragments appeared during the mission.

D	Cosmos 834	1976-58 A	1976 Jun 24.30	Sphere-	5.0 long	1976 Jun 24.91	81.37	88.98	6603	218	230	0.0009	94

R	[Soyuz 11A511U]	[08914]	11.9 days	cylinder	2.4 dia	1976 Jun 25.4	81.37	89.05	6605	216	237	0.002	94

PLE	1976 Jul 6.2	5700?		1976 Jun 30.35	81.37	88.93	6600	212	231	0.001	76

D	Cosmos 834	1976-58 B	1976 Jun 24.30	Cylinder	7.5 long	1976 Jun 24.35	81.36	88.93	6600	214	229	0.001	96

Block I 3rd stage 	[08915]	6 days	2500?	2.6 dia	1976 Jun 25.2	81.37	88.95	6600	216	227	0.001	93

1976 Jun 30			1976 Jun 29.28	81.39	88.12	6560	182	182	0	322

IMEWS 6 (DSP 8)	1976-59 A	1976 Jun 26.13	-	-	1976 Jun 26.5	26.3	633.0	24445	295	35840	0.727	180*

(OPS 2112)	[08916]	> million years			1976 Jul 1.0	0.5	1433.3	42118	35620	35860	0.003	-

[Titan 3C 23C-10]	CC-LC40				No elements available

Graveyard orbit	2019 Jun 11.72	9.68	1447.55	42389	35989	36031	0.0005	136

2021 Nov 27.00	7.62	1447.68	42391	35990	36036	0.0005	192

D	Titan  3C	1976-59 B	1976 Jun 26.13	Cylinder	6 long	1976 Jun 26.2	28.60	90.41	6680	151	453	0.023	113

second stage	[08917]	4 days	1900	3.0 dia	1976 Jun 30.52	28.76	88.62	6585	119	293	0.013	185

1976 Jun 30

Transtage 28	1976-59 C	1976 Jun 26.13	Cylinder	6 long?		Orbits sim	ilar to 1976-59 A

[08918]	>million years	1500?	3.0 dia	No elements available

2019 Jul 14.69	8.97	1432.03	42085	35662	35751	0.001	172

2021 Nov 26.86	6.97	1432.03	42085	35662	35751	0.001	207

Fragment	1976-59 D	[08919]			No current elements

*	Unconfirmed orbits

D	Cosmos 835	1976-60 A	1976 Jun 29.31	Sphere-	5.9 long?	1976 Jun 29.49	64.98	89.52	6630	172	330	0.012	61

R	[Voskhod 11A57]	[08922]	12.84 days	cylinder	2.4 dia	1976 Jun 30.6	64.96	89.41	6624	174	317	0.011	59

BAI	1976 Jul 12.15	5900?		1976 Jul 11.15	64.96	89.20	6613	172	297	0.009	53

D	Cosmos 835	1976-60 B	1976 Jun 29.31	Cylinder	7.5 long	1976 Jun 29.7	64.97	89.33	6620	175	308	0.010	58

Block I 3rd stage 	[08925]	5 days	2500?	2.6 dia	1976 Jul 3.56	64.96	88.40	6574	164	226	0.005	55

1976 Jul 4

D	Capsule**	1976-60 C	1976 Jun 29.31	-	-	1976 Jul 11.5	64.98	89.12	6610	172	291	0.009	51

[09014]	21 days		2 dia?	1976 Jul 12.01	64.96	89.08	6607	169	288	0.009	51

1976 Jul 20

D	Fragment	1976-60 D	[09015]	1976 Jul 14	15 days	1976 Jul 11.52	64.89	88.95	6601	174	272	0.007	59

1976 Jul 12.01	64.97	88.73	6591	169	255	0.007	50

1976 Jul 12.50	64.96	88.53	6581	167	237	0.005	50

D	Fragment	1976-60 E	[09018]	1976 Jul 16	17 days	1976 Jul 13.90	64.98	89.88	6647	178	359	0.014	12

**	Ejected from 1976-60 A on 1976 Jul 11; possibly an engine.

Cosmos 836	1976-61 A	1976 Jun 29.34	Cylinder +	2 long?	1976 Jun 29.47	74.04	100.78	7174	740	851	0.008	148

[Kosmos 11K65M	[08923]	120 years	paddles?	1 dia?	1976 Jun 30.6	74.06	100.98	7183	791	818	0.002	106

53731-284]	PLE-LC132		750?		2004 Jul 6.55	74.05	100.53	7162	770	797	0.002	259							2021 Nov 26.75	74.05	100.47	7159	768	793	0.002	62

Cosmos 836	1976-61 B	1976 Jun 29.34	Cylinder	7.4 long	1976 Jun 29.89	74.07	100.83	7177	783	813	0.002	80

2nd stage	[08924]	100 years	2200?	2.4 dia	1976 Jun 30.0	74.07	100.88	7178	784	815	0.002	88

2004 Jul 7.02	74.06	100.28	7151	762	782	0.001	146

2021 Nov 26.83	74.06	100.18	7146	756	778	0.002	224

Fragment	1976-61 C	[R09572]	Re-assigned to 1975-112 C	1976 Jun 28.62	74.07	101.00	7185	800	812	0.0009	329

D	Fragment	1976-61 D	[14815]	2012 Sep 24	13236 days	1976 Jun 26.09	74.06	100.83	7177	783	813	0.002	333

2004 Jul 6.44	74.03	95.80	6936	555	560	0.0004	16

2012 Sep 23.47	73.95	88.22	6573	187	201	0.001	299

D	Cosmos 837 *	1976-62 A	1976 Jul 1.34	Windmill +	4.2 long?	1976 Jul 2.3	62.75	98.51	7065	438	936	0.035	259

[Molniya 8K78M]	[08927]	2696 days	6 vanes?	1.6 dia?	1983 Nov 18.82	62.98	87.25	6517	133	143	0.0008	8

PLE-LC43/3	1983 Nov 18	1250?

D	Cosmos 837	1976-62 B	1976 Jul 1.34	Cylinder	7.5 long	1976 Jul 2.3	62.80	90.73	6689	215	406	0.014	125

Block I 3rd stage 	[08928]	35 days	2500?	2.6 dia	1976 Aug 3.96	62.78	88.23	6565	175	199	0.002	120

1976 Aug 5

D	Cosmos 837	1976-62 C	1976 Jul 1.34	Irregular	-	1976 Jul 1.58	62.82	90.88	6697	186	451	0.020	123

4th stage casing 	[08929]	20 days			1976 Jul 2.3	62.82	90.87	6696	189	446	0.019	123

1976 Jul 21			1976 Jul 20.85	62.81	88.15	6561	156	209	0.004	123

D	Cosmos 837	1976-62 D	1976 Jul 1.34			1976 Jul 1.58	62.80	91.22	6713	214	454	0.018	125

Ullage motor	[08930]	19 days			1976 Jul 20.62	62.85	89.70	6638	203	316	0.009	132

1976 Jul 20

D	Cosmos 837	1976-62 E	1976 Jul 1.34	Cylinder	2.0 long	1976 Jul 1.87	62.75	98.40	7060	441	923	0.034	260

Block L 4th stage 	[08931]	2278 days	4800 full	2.0 dia	1976 Jul 2.3	62.75	98.39	7059	440	922	0.034	260

1982 Sep 26	440 empty		1982 Sep 26.28	62.68	87.60	6534	147	164	0.001	303

*	Probable Molniya attempt; final stage shut down prematurely.

D	Cosmos 838 **	1976-63 A	1976 Jul 2.44	Cylinder?	-	1976 Jul 2.56	65.05	93.27	6813	426	442	0.001	270

[Tsyklon 2]	[08932]	417 days			1976 Jul 6.4	65.06	93.30	6812	428	440	0.0009	271

BAI-LC90	1977 Aug 23			1977 May 16.94	65.06	93.15	6807	414	443	0.002	286

D	Cosmos 838	1976-63 B	1976 Jul 2.44	Cylinder	8 long?	1976 Jul 2.56	65.02	89.73	6640	114	409	0.022	51

2nd stage	[08933]	1 day	1500?	2.5 dia?	1976 Jul 2.8	65.03	89.46	6628	117	382	0.020	48

1976 Jul 3			1976 Jul 2.80	65.03	89.45	6626	114	380	0.020	48

D	Fragments	1976-63 C-AS  39 pieces, all have decayed		For orbital information see extra pages at the end of the year

**	Disintegrated during late June - early July 1977.

D	Soyuz 21*	1976-64 A	1976 Jul 6.51	Sphere-	7.5 long	1976 Jul 7.2	51.59	89.65	6638	246	274	0.002	249

2M	[Soyuz 11A511U]	[08934]	49.26 days	cylinder	2.2 dia	1976 Jul 8.36	51.59	89.52	6647	263	273	0.0008	265

R		BAI	1976 Aug 24.77	6570?		1976 Jul 19.4	51.59	89.80	6646	262	273	0.0008	324

1976 Aug 23.43	51.59	89.78	6642	258	268	0.0008	106

D	Soyuz 21	1976-64 B	1976 Jul 6.51	Cylinder	7.5 long	1976 Jul 7.2	51.60	88.46	6579	183	219	0.003	87

Block I 3rd stage 	[08935]	3 days	2500?	2.6 dia	1976 Jul 7.67	51.59	88.42	6575	180	213	0.003	91

1976 Jul 9			1976 Jul 9.32	51.57	87.63	6536	148	167	0.001	113

*	Soyuz 21 docked with Salyut 5 on l976 Jul 7.57; undocked 1976 Aug 24.63

D	KH 9-12 (OPS4699)	1976-65 A	1976 Jul 8.78	Cylinder	15 long	1976 Jul 8.81	97.00	88.42	6574	156	235	0.006	132

[Titan 3D 23D-14]	[09006]	158 days	13300? full	3.0 dia	1976 Jul 10.7	97.00	88.54	6579	159	242	0.006	131

VDB-SLC4E	1976 Dec 13			1976 Jul 12.60	96.86	88.68	6588	163	256	0.007	130

D	SESP 74-2 **	1976-65 B	1976 Jul 8.78	-	-	1976 Jul 16.1	97.53	179.00	10520	236	8048	0.371	291

(OPS3986, Farrah 1)	[09007]	3577 days			No TLE’s issued

1986 Apr 24

S3-3	1976-65 C	1976 Jul 8.78	Octagon?	0.3 long?	1976 Jul 18.7	96. 38	97. 34	7008	6 28	632	0.0003	21 9

(OPS 5366)	[09008]		60?	0.9 dia?	No TLE’s issued

D	Titan 3D	1976-65 D	1976 Jul 8.78	Cylinder	6 long	1976 Jul 8.99	97.01	88.22	6565	152	220	0.005	126

2nd stage	[09010]	1.41 days	1900	3.0 dia	1976 Jul 9.0	97.00	88.31	6567	150	228	0.006	130

1976 Jul 10.19			1976 Jul 9.91	96.99	87.57	6533	143	154	0.002	105

**	Small magnetospheric observatory

Palapa l #	1976-66 A	1976 Jul 8.98	Cylinder	1.56 long	1976 Jul 9.0	24.66	645.61	24744	231	36501	0.733	179

[Delta 2914 611	[09009]	> million	574 full	1.90 dia	1976 Sep 1.0	0.05	1436.1	42165	35764	35809	0.0005	-

#125]	CC-LC17A	years	282 empty		1978 Feb 23.09	0.03	1436.03	42164	35779	35791	0.0001	34

1984 Apr 21.00	0.50	1436.00	42163	35742	35826	0.001	42

1984 Jun 29.00	0.19	1436.40	42171	35728	35856	0.002	116

1984 Nov 28.64	0.09	1436.10	42165	35759	35814	0.0006	313

1984 Dec 27.56	0.02	1436.03	42164	35758	35812	0.0006	297

1987 Jul 14.00	1.66	1435.83	42160	35760	35802	0.0005	277

Graveyard orbit	1988 Apr 12.61	2.97	1466.77	42763	36322	36447	0.001	67

1989 Mar 24.03	4.55	1438.92	42220	35829	35854	0.0003	222

2004 Jul 2.66	13.01	1438.78	42218	35805	35872	0.0008	35

2021 Nov 27.57	11.34	1438.85	42219	35822	35859	0.0004	179

D	Palapa 1	1976-66 B	1976 Jul 8.98	Cylinder +	6.4 long	1976 Jul 9.1	28.73	87.97	6561	147	219	0.005	349

Delta 2nd stage	[09012]	2 days	annulus	1.52 and

1976 Jul 10	350?	2.44 dia

D	Palapa 1	1976-66 C	1976 Jul 8.98	Sphere-cone	1.32 long	1976 Jul 12.77	24.65	640.97	24625	234	36260	0.731	181

Star-37E PKM	[09017]	10378 days	66	0.94 dia	1976 Jul 16.3	24.65	638.71	24570	239	36145	0.731	183

2004 Dec 6			2004 Jul 5.32	24.43	117.25	7936	180	2935	0.174	303

2004 Dec 6.37	24.34	85.13	6411	-44	109	0.012	173

Fragment	1976-66 D	[28144]			2004 Jan 9.59	24.53	234.97	12614	449	12021	0.459	287

2004 Jul 8.66	24.55	234.87	12610	453	12010	0.458	276

2021 Nov 28.23	24.61	226.10	12294	323	11508	0.455	193

#	First Indonesian satellite, launched by NASA

Cosmos 839	1976-67 A	1976 Jul 8.88	Cylinder?	4 long?	1976 Jul 11.38	65.86	116.87	7918	982	2097	0.070	165

[Kosmos 11K65M	[09011]	disintegrated *		2 dia?	1976 Jul 15.4	65.86	116.88	7919	984	2098	0.070	163

53716-324]	PLE-LC132				2004 Jul 6.50	65.85	116.80	7916	982	2092	0.070	159

2021 Nov 27.42	65.85	116.80	7915	976	2097	0.071	213

Cosmos 839	1976-67 B	1976 Jul 8.88	Cylinder	7.4 long	1976 Jul 10.81	65.86	116.65	7909	971	2089	0.071	117

2nd stage	[09013]	4000 years	2200?	2.4 dia	1976 Jul 15.5	65.86	116.67	7910	972	2091	0.071	163

2004 Jul 6.51	65.86	116.57	7905	966	2086	0.071	125

2021 Nov 28.58	65.87	116.55	7905	963	2088	0.071	157

C 839 fragments	1976-67 C-BZ	70 pieces, 2 have decayed	For orbital information see extra pages at the end of the year

*	Cosmos 843 past close to Cosmos 839 and destroyed Cosmos 839

D	Cosmos 840	1976-68 A	1976 Jul 14.38	Sphere-	5.0 long	1976 Jul 14.43	72.87	89.60	6633	198	310	0.008	72

R	[Soyuz 11A511U]	[09019]	11.8 days	cylinder	2.4 dia	1976 Jul 15.6	72.87	89.73	6639	203	319	0.009	74

PLE	1976 Jul 26.2	5700?		1976 Jul 25.64	72.87	89.62	6634	200	310	0.008	48

D	Cosmos 840	1976-68 B	1976 Jul 14.38	Cylinder	7.5 long	1976 Jul 14.43	72.87	89.60	6633	198	310	0.008	72

Block I 3rd stage	[09020]	11 days	2500?	2.6 dia	1976 Jul 15.5	72.87	89.58	6632	198	309	0.008	66

1976 Jul 25			1976 Jul 21.01	72.87	88.90	6599	183	257	0.006	49

D	Fragment	1976-68 C	[09021]	1976 Jul 17	3 days	1976 Jul 14.93	72.83	89.70	6638	206	313	0.008	71

1976 Jul 16.42	72.85	89.20	6613	202	268	0.005	73

Cosmos 841	1976-69 A	1976 Jul 15.55	Cylinder	2 long?	1976 Jul 16.87	74.05	100.78	7174	785	806	0.001	5

[Kosmos 11K65M	[09022]	120 years	paddles?	1 dia?	1976 Jul 17.8	74.05	100.83	7176	787	808	0.001	3

53746-304]	PLE-LC132		750?		2004 Jul 7.13	74.04	100.35	7154	766	784	0.001	131

2021 Nov 27.79	74.04	100.28	7150	762	782	0.001	246

Cosmos 841	1976-69 B	1976 Jul 15.55	Cylinder	7.4 long	1976 Jul 17.57	74.05	100.68	7169	776	806	0.002	17

2nd stage	[09023]	100 years	2200?	2.4 dia	1976 Jul 25.5	74.05	100.74	7171	779	807	0.002	5

2004 Jul 6.48	74.04	100.12	7142	752	776	0.002	68

2021 Nov 28.43	74.04	100.02	7138	747	770	0.002	101

Fragment	1976-69 C	[09704]			1977 Jan 10.88	74.08	101.10	7190	806	816	0.0006	213

2004 Jul 5.40	74.06	97.90	7037	654	663	0.0006	264

2021 Nov 27.43	74.06	96.47	6968	587	591	0.0002	50

Fragment	1976-69 D	[13499]			1980 Jul 2.56	74.07	101.38	7203	803	845	0.003	195

2004 Jul 7.03	74.06	99.60	7118	727	752	0.002	25

2021 Nov 28.18	74.06	99.10	7094	703	727	0.002	189

Cosmos 842	1976-70 A	1975 Jul 21.43	Cylinder?	1.3 long?	1976 Jul 29.00	82.97	101.90	7368	974	1005	0.002	251

[Kosmos 11k65M	[09025]	1200 years	700?	1.9 dia?	1976 Aug 1.5	82.98	104.96	7370	972	1011	0.003	253

53731-266]	PLE-LC132				2004 Jul 5.54	82.99	104.82	7364	966	1005	0.003	295

2021 Nov 28.41	82.99	104.78	7363	965	1004	0.003	217

Cosmos 842	1976-70 B	1976 Jul 21.43	Cylinder	7.4 long	1976 Jul 24.5	82.98	104.84	7364	971	1000	0.002	269

2nd stage	[09044]	600 years	2200?	2.4 dia	1976 Jul 25.64	82.98	104.77	7362	969	998	0.002	266

2004 Jul 7.44	82.98	104.65	7356	968	987	0.001	185

2021 Nov 27.79	82.99	104.63	7355	966	988	0.002	62

D	Cosmos 843 *	1976-71 A	1976 Jul 21.64	Cylinder?	4 long?	1976 Jul 21.7	65.08	89.27	6617	132	346	0.016	36

[Tsyklon 2]	[09043]	1 day		2 dia?	1976 Jul 22.62	65.07	88.60	6583	134	275	0.011	40

BAI-LC90	1976 Jul 22

D	Cosmos 843	1976-71 B	1976 Jul 21.64	Cylinder	8 long?	1976 Jul 22.99	65.10	88.17	6563	125	243	0.009	37

2nd stage	[09045]	2 days	1500?	2.5 dia?

1976 Jul 23

*	Passed close to and destroyed Cosmos 839. De-orbited after test.

D	Cosmos 844 **	1976-72 A	1976 Jul 22.66	Sphere-	7 long?	1976 Jul 22.77	67.15	90.42	6674	170	421	0.019	80

[Soyuz 11A511U]	[09046]	39 days	cylinder	2.4 dia	1976 Jul 23.89	67.14	89.80	6643	171	357	0.014	72

PLE-LC43/3	1976 Aug 30	6700?		1976 Jul 25.4	67.15	89.76	6641	172	353	0.014	70							1976 Aug 8.10	67.15	88.77	6592	161	266	0.008	66

D	Cosmos 844	1976-72 B	1976 Jul 22.66	Cylinder	7.5 long	1976 Jul 23.95	67.14	89.65	6636	170	344	0.013	73

Block I 3rd stage 	[09048]	8 days	2500?	2.6 dia	1976 Jul 24.0	67.14	89.67	6637	171	346	0.013	73

1976 Jul 30			1976 Jul 29.46	67.13	88.27	6567	153	223	0.005	70

D	Fragments	1976-72C-KJ	246 pieces; all have decayed		For orbital information see extra pages at the end of the year

**	One of the solar panels would not unfold. Ground control activiated the destruct package and the spacecraft was destroyed on 1976 July 25.

Comstar 2 (1B)	1976-73 A	1976 Jul 22.92	Cylinder	2.82 long	1976 Jul 22.72	21.84	636.73	24517	548	35729	0.717	179

[Atlas SLV-3D(R)	[09047]	> million years	1520 full	2.36 dia	1976 Jul 22.9	21.81	641.03	24627	552	35946	0.719	179

AC-40 Centaur D-1AR	  CC-LC36B		792 empty		1976 Nov 1.0	0.1	1436.2	42166	35780	35795	0.0002	-

5022D]					1977 Jan 27.11	0.05	1436.08	42165	35758	35814	0.0007	47

1993 Dec 19.12	8.67	1436.15	42166	35783	35791	0.0001	262

Graveyard orbit	1993 Dec 26.49	8.65	1440.45	42250	35865	35878	0.0002	289

1994 Feb 25.25	8.78	1440.28	42247	35857	35880	0.0003	316

2004 Jul 9.80	13.07	1440.10	42243	35848	35881	0.0004	42

2021 Nov 27.90	11.37	1440.38	42249	35862	35878	0.0002	120

Comstar 2	1976-73 B	1976 Jul 22.92	Cylinder	8.6 long	1976 Jul 22.9	21.82	650.92	24880	561	36442	0.721	179

Centaur 40 stage	[09329]	6000 years	1815	3.0 dia	1976 Aug 10.11	21.88	648.18	24810	573	36290	0.720	191

2004 Jul 5.78	21.67	644.37	24713	617	36051	0.717	46

2021 Nov 28.29	22.16	643.88	24700	558	36085	0.719	47

D	Molniya-1 35	1976-74 A	1976 Jul 23.66	Windmill	3.4 long	1976 Jul 23.23	62.94	698.48	26.78	467	38931	0.738	280

[Molniya 8K78M]	[09049]	3963 days	+ 6 vanes	1.6 dia	1976 Jul 30.0	63.01	700.93	26139	476	39045	0.738	280

1976 Aug 13.01	62.96	717.68	26553	469	39880	0.742	280

BAI	1987 May 30	1000?		1976 Sep 1.0	62.9	717.67	26554	515	39836	0.740	-							1987 May 13.89	63.43	486.60	20493	126	28103	0.683	257

D	Molniya-1 35	1976-74 B	1976 Jul 23. 66	Cylinder	7.5 long	1976 Jul 23.8	62.90	91.54	6729	239	462	0.017	60

Block I 3rd stage 	[09050]	71 days	2500?	2.6 dia	1976 Oct 2.00	62.89	87.82	6545	162	171	0.0007	255

1976 Oct 2

D	Molniya-1 35	1976-74 C	1976 Jul 23.66	Irregular	-	1976 Jul 23.84	62.89	91.80	6741	216	510	0.022	59

4th stage casing 	[09051]	57 days			1976 Jul 26.0	62.89	91.77	6740	215	509	0.022	60

1976 Sep 18			1976 Sep 18.69	62.88	87.73	6540	151	173	0.002	58

D	Molniya-1 35	1976-74 D	1976 Jul 23.66			1976 Jul 23.65	62.87	91.42	6723	223	465	0.018	53

Ullage motor	[09052]	40 days			1976 Jul 23.84	62.89	91.80	6741	216	510	0.022	59

1976 Sep 1

D	Molniya-1 35	1976-74 E	1976 Jul 23.66	Cylinder	2.0 long	1976 Aug 5.2	62.90	698.49	26078	480	38919	0.737	280

Block L 4th stage 	09269]	5573 days	440	2.0 dia	1976 Aug 5.33	62.90	698.47	26077	472	38926	0.737	280

1991 Oct 26			1991 Sep 9.65	62.52	656.78	25029	108	37193	0.741	265

62.56	103.90		65	1821	from Satcat

D	Cosmos 845	1976-75 A	1976 Jul 27.23	Cylinder +	2 long?	1976 Jul 28.1	74.06	95.25	6908	514	546	0.002	1

[Kosmos 11K65M	[09053]	1572 days	paddles?	1 dia?	1976 Aug 4.88	74.05	95.20	6907	512	544	0.002	341

53746-307]	PLE-LC132	1980 Nov 15	9007		1980 Nov 14.10	74.03	88.23	6565	182	192	0.0007	256

D	Cosmos 845	1976-75 B	1976 Jul 27.23	Cylinder	7.4 long	1976 Jul 27.7	74.06	95.16	6904	504	547	0.003	356

2nd stage	[09054]	1677 days	2200?	2.4 dia	1981 Feb 27.87	74.03	95.37	6522	137	151	0.001	349

1981 Feb 28

D	Fragments	1976-75 C-H	6 pieces, all have decayed		For orbital information see extra pages at the end of the year

D	Intercosmos 16*	1976-76 A	1976 Jul 27.50	Octagonal	1.8 long?	1976 Jul 27.62	50.57	94.43	6870	464	518	0.004	18

[Kosmos 11K65M	[09055]	1078 days	ellipsoid?	1.5 dia?	1976 Aug 2.1	50.57	94.36	6869	464	517	0.004	38

53746-316]	KY-LC107/2	1979 Jul 10	550?		1979 Jul 4.93	50.54	89.38	6623	242	246	0.0003	11

D	lntercosmos 16	1976-76 B	1976 Jul 27.50	Cylinder	7.4 long	1976 Jul 28.1	50.57	94.23	6862	451	517	0.005	22

2nd stage	[09056]	1304 days	2200?	2.4 dia	1980 Feb 20.99	50.54	87.70	6539	160	161	0.00008	140

1980 Feb 21

*	Payload includes Swedish experiments.

NOAA 5 (ITOS H)	1976-77 A	1976 Jul 29.71	Box	1.25 long	1976 Jul 31.5	102.10	116.34	7894	1509	1522	0.0008	242

[Delta 2310 605	[09057]	10000 years	340	1.02 square	1976 Aug 1.51	102.09	116.27	7892	1505	1521	0.001	227

#126]	VDB-SLC2W				2004 Jul 6.70	102.19	116.30	7893	1507	1522	0.001	85

2021 Nov 27.69	102.07	116.33	7894	1508	1523	0.001	150

NOAA 5	1976-77 B	1976 Jul 29.71	Cylinder +	6.4 long?	1976 Aug 1.5	102.08	116.33	7893	1507	1523	0.001	227

Delta 2nd stage	[09063]	disintegrated	annulus?	1.52 and	2004 Jul 4.66	101.87	115.17	7841	1415	1510	0.006	321

350?	2.44 dia?	2021 Nov 27.72	101.83	115.05	7841	1414	1510	0.006	309

Fragments	1976-77 C-GS   183 pieces, 10 have decayed		For orbital information see extra pages at the end of the year

Cosmos 846	1976-78 A	1976 Jul 29.83	CylInder?	1.3 long?	1976 Jul 29.97	82.92	104.67	7358	954	1004	0.003	284

[Kosmos 11K65M	[09061]	1200 years	700?	1.9 dia?	1976 Aug 1.5	82.92	104.81	7363	954	1015	0.004	292

53716-329]	PLE-LC132				2004 Jul 5.30	82.93	104.63	7356	948	1006	0.004	267

2021 Nov 28.46	82.93	104.62	7355	945	1007	0.004	142

Cosmos 846	1976-78 B	1976 Jul 29.83	Cylinder	7.4 long	1976 Jul 30.3	82.93	104.68	7356	953	1003	0.003	303

2nd stage	[09062]	600 years	2200?	2.4 dia	2004 Jul 6.90	82.93	104.43	7348	949	991	0.003	158

2021 Nov 28.54	82.93	104.80	7348	948	990	0.003	345

D	Cosmos 847	1976-79 A	1976 Aug 4.56	Sphere-	5.9 long?	1976 Aug 4.74	62.79	89.40	6624	178	312	0.010	75

R	[Soyuz 11A511U]	[09214]	12.61 days	cylinder	2.4 dia	1976 Aug 5.0	62.82	89.50	6629	181	321	0.011	78

PLE	1976 Aug 17.17	5900?		1976 Aug 15.42	62.80	89.32	6618	166	313	0.011	72

D	Cosmos 847	1976-19 B	1976 Aug 4.56	Cylinder	7.5 long	1976 Aug 5.1	62.78	89.39	6623	179	311	0.010	71

Block I 3rd stage 	[09215]	7 days	2500?	2.6 dia	1976 Aug 10.12	62.79	88.23	6566	159	215	0.004	70				1976 Aug 11

D	Capsule ?*	1976-79 D	1976 Aug 4.56	-	-	1976 Aug 16.5	62.82	89.21	6614	165	307	0.011	-

[09376]	19 days		2 dia?	1976 Aug 23.30	62.80	87.43	6526	139	155	0.001	70

1976 Aug 23

D	Fragment	1976-79 C	[09216]	1976 Aug 5	1 day	1976 Aug 4.81	62.74	89.07	6607	173	283	0.008	68

1976 Aug 6.11	62.64	89.08	6607	160	298	0.010	58

D	Fragment	1976-79 E	[09377]	1976 Aug 18	14 days	1976 Aug 16.41	62.80	89.03	6606	164	289	0.009	65

*	Possibly an engine

D	SDS 3  (OPS 7940)	1976-80 A	1976 Aug 6	Cylinder?	-	1976 Aug 14	63.3	703.8	26225	380	39315	0.742	270*

[Titan 34B-6 3B-56	[09270]	16083 days			No elements available

Ascent Agena D]	VDB-SLC4W	2020 Aug 18			2019 Sep 8.71	61.77	714.67	26479	274	39926	0.749	271

2020 Apr 18.41	61.82	94.42	6869	78	903	0.060	283

SDS 3	1976-80 B	1976 Aug 6	Cylinder	6 long?	1976 Aug 22	63.3	700.2	26120	310	39175	0.744	270*

Agena D stage	[09271]	100 years?	700	1.5 dia	No elements available

2019 Apr 22.93	62.34	707.27	26296	238	39596	0.748	271

2021 Nov 27.82	62.70	547.87	22179	620	30982	0.684	286

*	Approximate orbits.

D	Luna 24 (DS+AS) **	1976-81 A	1976 Aug 9.63	Pyramid +	3.1 high	1976 Aug 14	120	119	1853	115	115	0	-$

[Proton 8K82K	[09272]	8.65 days	cylinder	3.2 wide	1976 Aug 17	120	114	1804	12	120	0.030	-$

288-02/11S824M]	BAI-LC81L	1976 Aug 18.28	5600? Full	3.3 deep

D	Proton platform 	1976-81 B	1976 Aug 9.63	-	-	1976 Aug 9.81	51.54	88.93	6599	194	248	0.004	342

[09273]	< 0.37 days

1976 Aug 9

D	Proton	1976-81 C	1976 Aug 9.63	Cylinder	6.5 long?	1976 Aug 10.0	51.54	88.74	6593	188	242	0.004	330

third stage	[09274]	6 days		4 dia	1976 Aug 14.41	51.55	87.82	6545	159	174	0.001	334

1976 Aug 15

Proton	1976-81 D	1976 Aug 9.63	Cylinder	3.9 long	1976 Aug 11.3	51.52	88.55	6584	186	225	0.003	339

4th stage	[09278}	5 days	1900?	3.9 dia	1976 Aug 14.41	51.51	87.72	6540	152	171	0.001	327

1976 Aug 14

D	Luna 24	1976-81 E	1976 Aug 9.63	Cylinder +	2.3 high	Relaunched from moon 1976 Aug 19.226

Return Vehicle	[09384]	13.12 days	3 spheres	1.6 wide	Landed on Earth 1976 Aug 22.747 with moon material.

1976 Aug 22.75	800? Full	1.5 deep

$	Moon orbits

**	Orbited moon 53 times? Soft-landed 1976 Aug 18 at 06:36 at 12.75(N; 62.2(E.

D	Cosmos 848	1976-82 A	1976 Aug 12.57	Sphere-	5.0 long	1976 Aug 12.67	62.80	89.48	6627	203	294	0.007	81

R	[Soyuz 11A511U]	[09280]	12.62 days	cylinder	2.4 dia	1976 Aug 13.11	62.80	89.57	6632	204	302	0.007	82

PLE	1976 Aug 25.19	6700?		1976 Aug 14.3	62.80	89.57	6633	206	303	0.007	87							1976 Aug 24.30	62.80	89.50	6628	203	296	0.007	86

D	Cosmos 848	1976-82 B	1976 Aug 12.57	Cylinder	7.5 long	1976 Aug 12.74	62.80	89.50	6628	204	295	0.007	82

Block I 3rd stage 	[09281]	12 days	2500?	2.6 dia	1976 Aug 13.5	62.79	89.46	6627	204	294	0.007	79			1976 Aug 24				1976 Aug 24.29	62.77	87.63	6536	157	157	0	294

D	Nauka-19KS	1976 82 D	1976 Aug 12.57			1976 Aug 15.72	62.80	89.50	6629	203	297	0.007	85

[09374]	20 days			1976 Apr 27.79	62.77	88.55	6581	189	216	0.002	86

1976 Sep 1

D	Fragments	1976-82 C, E 2 pieces, both have decayed		For orbital information see extra pages at the end of the year

D	Cosmos 849	1976-83 A	1976 Aug 18.40	Ellipsoid	1.8 long	1976 Aug 18.45	70.97	95.92	6941	262	863	0.043	87

[Kosmos 11K63]	[09382]	614 days	400?	1.2 dia	1976 Aug 20.4	70.97	95.95	6943	264	865	0.043	84

PLE-LC133/1	1978 Apr 24			1976 Aug 24.45	70.97	95.90	6940	264	860	0.043	76							1978 Apr 23.06	70.94	88.18	6563	169	199	0.002	57

D	Cosmos 849	1976-83 B	1976 Aug 18.40	Cylinder	8 long	1976 Aug 19.4	70.97	95.65	6928	268	831	0.040	85

2nd stage	[09383]	441 days	1500?	1.65 dia	1977 Nov 1.44	70.92	88.08	6559	173	186	0.001	346

1977 Nov 2

D	Fragment	1976-83 C	[09407]	1977 Feb 16	174 days	1976 Sep 4.88	71.16	95.58	6928	265	833	0.041	60

1977 Feb 10.53	71.13	90.02	6654	221	329	0.008	117

D	Cosmos 850	1976-84 A	1976 Aug 26.46	Ellipsoid	1.8 long	1976 Aug 26.6	70.94	92.20	6761	272	493	0.016	81

[Kosmos 11K63]	[09387]	263 days	400?	1.2 dia	1976 Aug 27.28	70.94	92.17	6759	269	492	0.016	81

PLE-LC133/1	1977 May 16			1977 may 15.62	70.91	87.83	6545	156	178	0.002	272

D	Cosmos 850	1976-84 B	1976 Aug 26.46	Cylinder	8 long	1976 Aug 27.22	70.94	91.98	6751	274	470	0.014	84

2nd stage	[09388]	141 days	1500?	1.65 dia	1976 Aug 28.3	70.94	91.99	6750	275	469	0.014	82

1977 Jan 14			1977 Jan 14.01	70.92	88.00	6554	171	181	0.0008	223

D	Cosmos 851	1976-85 A	1976 Aug 27.61	Cylinder +	5 long?	1976 Aug 28.7	81.20	96.78	6981	569	637	0.005	264

[Vostok 8A92M]	[09389]	4726 days	2 vanes?	1.5 dia?	1976 Aug 28.88	81.21	96.75	6982	545	661	0.008	215

PLE	1989 Aug 5	2500?		1989 Aug 5.35	81.15	87.33	6521	135	149	0.001	235

D	Cosmos 851	1976-85 B	1976 Aug 27.61	Cylinder	3.8 long	1976 Aug 28.7	81.21	96.80	6982	554	654	0.007	217

Block I 3rd stage 	[09390]	5686 days	1440	2.6 dia	1992 Mar 21.20	81.07	88.17	6562	179	188	0.0007	245

1992 Mar 22

D	Cosmos 852	1976-86 A	1976 Aug 28.38	Sphere-	5.9 long?	1976 Aug 28.49	65.00	89.53	6630	170	332	0.012	66

R	[Soyuz 11A511U]	[09391]	12.85 days	cylinder	2.4 dia	1976 Aug 29.1	64.99	89.54	6631	173	332	0.012	66

BAI	1976 Sep 10.23	5900?		1976 Sep 2.28	64.99	89.37	6621	170	315	0.011	63

D	Cosmos 852	1976-86 B	1976 Aug 28.38	Cylinder	7.5 long	1976 Aug 28.49	65.01	89.42	6624	167	324	0.012	63

Block I 3rd stage 	[09392]	5 days	2500?	2.6 dia	1976 Aug 29.1	64.99	89.36	6622	172	315	0.011	65

1976 Sep 2			1976 Sep 2.31	65.00	88.03	6556	161	194	0.003	57

D	Fragment 3rd stage	1976-86 C	[09393]	1976 Sep 11	14 days	1976 Aug 28.62	65.09	88.97	6602	167	279	0.008	71

1976 Sep 11.2	64.99	89.07	6607	167	291	0.009	-

D	Fragment C852	1976-86 D	[09412]	1976 Sep 16	19 days	1976 Sep 15.32	64.98	88.08	6558	155	203	0.004	56

D	Fragment C852	1976-86 E	[09413]	1976 Sep 11	14 days	1976 Sep 11.07	65.04	87.97	6552	172	175	0.0002	66

D	Fragment C852	1976-86 F	[09414]	1976 Sep 11	14 days	1976 Sep 10.58	64.92	88.63	6585	175	238	0.005	70

*	Possibly an engine

D	China 6 (JSSW 5)	1976-87 A	1976 Aug 30.49	Spheroid?	1.25 dia?	1976 Aug 30.99	69.16	108.77	7548	195	2145	0.129	139

[Feng Bao 1 FB1-6]	[09394]	817 days	270?		1978 Nov 25.55	69.06	107.65	6537	119	197	0.006	247

(CZ-2B0		1978 Nov 25

D	CZ-2B 2nd stage	1976-87 B	1976 Aug 30.49	Cylinder	7 long	1976 Aug 30.8	69.17	108.72	7546	190	2145	0.129	139			[09395]	523 days		3.35 dia	1976 Aug 31.37	69.15	108.68	7544	193	2139	0.129	139

1978 Feb 4			1978 Feb 3.58	69.09	88.47	6577	135	261	0.010	231

D	Cosmos 853*	1976-88 A	1976 Sep 1.14	Windmill +	4.2 long?	1976 Sep 1.70	62.82	91.78	6741	238	487	0.018	129

[Molniya 8K78M]	[09398]	121 days	6 vanes?	1.6 dia	1976 Sep 3.3	62.82	91.57	6730	243	461	0.016	137

PLE-LC43/3	1976 Dec 31	1250?		1976 Dec 30.97	62.79	88.03	6556	171	183	0.0009	146

D	Cosmos 853	1976-88 B	1976 Sep 1.14	Cylinder	7.5 long	1976 Sep 3.3	62.83	91.20	6712	213	454	0.018	129

Block I 3rd stage 	[09399]	39 days	2500?	2.6 dia	1976 Oct 9.39	62.81	88.22	6565	170	203	0.003	131

1976 Oct 10

D	Cosmos 853	1976-88 C	1976 Sep 1.14	Cylinder	2.0  long	1976 Sep 3.2	62.78	91.64	6734	240	471	0.017	130

Proton Platform	[09400]	261 days	4800 full	2.0  dia	1977 May 20.65	62.74	87.45	6527	147	149	0.0002	241

1977 May 20	440 empty

D	Cosmos 853	1976-88 D	1976 Sep 1.14	Irregular	-	1976 Sep 3.4	62.81	91.68	6736	242	473	0.017	133

Block L 4th stage	[09402]	99 days			1976 Dec 8.25	62.79	88.32	6570	176	206	0.002	140

1976 Dec 9

*	Cosmos 853 may be a failed Molniya satellite; final stage failed to ignite.

D	TIP 3	1976-89 A	1976 Sep 1.88	Dumb-bell?	7.3 long?	1976 Sep 1.99	90.30	95.95	6943	341	787	0.032	163

[Scout D-1 S197C]	[09403]	1732 days	94?	0.59 dia?	1976 Sep 4.3	90.31	96.02	6947	348	789	0.032	155			VDB-SLC5	1981 May 30			1981 May 30.34	89.24	87.30	6519	127	153	0.002	266

D	Altair rocket	1976-89 B	1976 Sep 1.88	Cylinder	1.50 long	1976 Sep 4.3	90.32	95.99	6945	348	786	0.031	154

Scout 4th stage	[09404]	667 days	24	0.46 dia	1978 Jun 27.77	90.27	88.85	6596	206	229	0.002	162

1978 Jun 29

D	Fragment	1976-89 C	[09409]	1978 Mar 1	546 days	1976 Sep 8.44	90.20	95.53	6923	330	759	0.031	126

1978 Jan 26.37	90.15	91.27	6715	284	389	0.008	340

D	Fragment	1976-89 D	[09410]	1978 May 17	624 days	1976 Sep 7.74	90.44	96.20	6955	346	808	0.033	154

1978 Apr 29.19	90.39	91.12	6708	273	386	0.008	53

D	Cosmos 854	1976-90 A	1976 Sep 3.39	Sphere-	6.5 long?	1976 Sep 3.7	81.35	89.27	6616	167	308	0.011	83

R	[Soyuz 11A511U]	[09405]	12.85 days	cylinder	2.4 dia	1976 Sep 5.1	81.35	89.02	6603	168	282	0.009	80

PLE	1976 Sep 16.24	6300?		1976 Sep 12.40	81.35	88.85	6596	171	264	0.007	51

D	Cosmos 854	1976-90 B	1976 Sep 3.39	Cylinder	7.5 long	1976 Sep 3.9	81.35	89.12	6608	166	294	0.010	82

Block I 3rd stage 	[09406]	4 days	2500?	2.6 dia	1976 Sep 6.89	81.35	87.77	6542	147	181	0.003	68

1976 Sep 7

D	Cosmos 854	1976-90 C	1976 Sep 3.39	Cone	1.5 long?	1976 Sep 17.2	81.35	88.77	6591	159	266	0.008	-

engine	[09422]	16 days	600? ful	2 dia?	1976 Sep 18.86	81.35	87.88	6548	156	183	0.002	27

1976 Sep 19

D	Fragment	1976-90 D	[09423]	1976 Sep 17	14 days	1976 Sep 16.34	81.33	87.83	6545	132	202	0.005	22

AMS 1(OPS 5721)*	1976-91 A	1976 Sep 11.34	Irregular	6.40 long	1976 Sep 14.3	98.70	101.60	7211	818	848	0.002	187

[Thor DSV-2U #172]	[09415]	80 years	450	1.68 dia	2004 Mar 21.79	99.00	101.02	7185	794	819	0.002	206#

VDB-SLC10W				2016 Jan 3.80	98.58	100.95	7182	790	817	0.002	323#

2019 Sep 10.61	98.42	101.00	7185	793	819	0.002	343

2021 Dec 1.59	98.31	100.93	7182	789	817	0.002	108

Fragments	1976-91 B-G	6 pieces, 2 have decayed		For orbital information see extra pages at the end of the year

*	USAF Advanced Meteorological Satellite (DMSP B5D1).

#	Orbits from amateur observations

Statsionar	1976-92 A	1976 Sep 11.77	-	-	1977 Sep 5.00	0.40	1436.23	42167	35770	35808	0.0004	102

Raduga 2	[09416]	>million years	2000?		1977 Dec 21.7	0.60	1436.03	42166	35772	35803	0.0004	285

[Proton 8K82K	BAI-LC81P				2004 Jul 7.95	14.72	1436.15	42166	35673	35901	0.003	158

289-01/11S86 5L]					2021 Dec 1.64	7.69	1436.32	42169	35676	35905	0.003	350

D	Raduga 2	1976-92 B	1976 Sep 11.77	Cylinder	6.5 long?	1976 Sep 9.94	51.49	88.18	6563	168	201	0.003	271

third stage	[09417]	3 days		4 dia	1976 Sep 12.4	51.50	88.15	6564	177	195	0.001	316

1976 Sep 14			1976 Sep 13.11	51.49	88.05	6556	172	184	0.001	351

D	Raduga 2	1976-92 C	1976 Sep 11.77	Irregular	-	1976 Sep 12.1	51.48	88.28	6571	189	196	0.001	27

4th stage casing 	[09418]	1 day			1976 Sep 12.43	51.48	88.07	6558	155	203	0.004	188

1976 Sep 12

D	Raduga 2	1976-92 F	1976 Sep 11.77	Cylinder	5.5 long	1977 Jul 23.84	0.28	1435.90	42161	35706	35859	0.002	68

fourth stage	[17872]	>million  years	17300 ful	4.0 dia	1987 Apr 13.4	7.89	1436.42	42173	35738	35852	0.001	142

2021 Dec 1.45	7.68	1436.73	42177	35724	35874	0.002	150

D	Raduga 2	1976-92 D	1976 Sep 11.77			1976 Oct 2.07	47.33	633.95	24446	331	35802	0.726	5

Ullage motor	[09440]	311 days			1977 Jul 10.96	46.34	159.23	9732	118	6589	0.332	111

1977 Jul 19

D	Raduga 2	1976-92 E	1976 Sep 11.77			1976 Nov 14.95	46.84	631.85	24392	169	35857	0.732	15

Ullage motor	[09441]	251 days			1977 Apr 24.93	46.63	167.70	10074	85	7305	0.358	87

1977 May 20

D	Soyuz 22	1976-93 A	1976 Sep 15.41	Sphere-	7.5 long	1976 Sep 15.5	64.75	89.31	6619	185	296	0.008	71

2M	[Soyuz 11A511U]	[09421]	7.91 days	cylinder	2.3 dia	1976 Sep 15.8	64.75	89.58	6632	248	259	0.0009	146

BAI	1976 Sep 23.32	+ 2 wings		1976 Sep 16.6	64.75	89.58	6632	249	259	0.001	149

1976 Sep 22.5	64.75	89.42	6624	239	253	0.001	140

6570?

D	Soyuz 22	1976-93 B	1976 Sep 15.41	Cylinder	7.5 long	1976 Sep 15.71	64.76	89.18	6613	184	285	0.008	68

Block I 3rd stage 	[09424]	5 days	2500?	2.6 dia	1976 Sep 16.8	64.76	89.03	6605	182	272	0.007	66

1976 Sep 20			1976 Sep 19.11	64.76	88.45	6576	169	227	0.004	65

D	Fragment*	1976-93 C	[09425]	1976 Sep 16	1 day	No TLE’s issued

*	Probably the MKF-6 multizonal camera shroud.

D	KH 8-47	1976-94 A	1976 Sep 15.79	Cylinder	8 long?	1976 Sep 15.89	96.40	89.20	6613	134	336	0.015	146

[Titan 24B-17	[09426]	51 days	3000?	1.5 dia	1976 Sep 16.4	96.39	89.18	6611	135	330	0.015	144

(3B-51) Agena D]	VDB-SLC4W	1976 Nov 5			1976 Sep 21.96	96.40	89.33	6620	132	351	0.017	139

1976 Oct 2.43	96.40	89.13	6610	131	333	0.015	125

1976 Oct 9.19	96.41	89.32	6619	130	352	0.017	139

1976 Oct 29.27	96.43	89.05	6606	128	326	0.015	129

D	Fragment	1976-94 B	[09427]	1976 Sep 17	2 days	1976 Sep 15.89	96.28	88.72	6590	138	285	0.011	124

D	Cosmos 855	1976-95 A	1976 Sep 21.49	Sphere-	5.9 long	1976 Sep 21.54	72.88	89.90	6648	201	338	0.010	78

R	[Soyuz 11A511U]	[09433]	11.80 days	cylinder	2.4 dia	1976 Sep 22.4	72.88	89.96	6650	202	341	0.010	76

PLE	1976 Oct 3.29	5900?		1976 Oct 2.34	72.87	89.82	6644	200	331	0.010	52

D	Cosmos 855	1976-95 B	1976 Sep 21.49	Cylinder	7.6 long	1976 Sep 21.79	72.86	89.78	6642	186	341	0.012	71

Block I 3rd stage 	[09434]	11 days	2500?	2.6 dia	1976 Sep 22.4	72.87	89.78	6641	197	328	0.010	69

1976 Oct 2			1976 Oct 1.45	72.86	87.95	6552	162	185	0.002	44

D	Capsule	1976-95 D	1976 Sep 21.49	El1ipsoid	0.9 long	1976 Oct 2.6	72.88	89.82	6643	199	330	0.010	-

[09446]	17 days	200?	1.9 dia	1976 Oct 3.40	72.87	89.80	6643	199	330	0.010	50

1976 Oct 8			1976 Oct 5.08	72.87	89.38	6622	196	291	0.007	47

D	Fragment	1976-95 C	[09445]	1976 Oct 6	15 days	1976 Oct 3.40	72.87	89.67	6637	196	320	0.009	47

1976 Oct 5.39	72.88	89.37	6622	192	294	0.008	41

D	Cosmos 856	1976-96 A	1976 Sep 22.40	Sphere-	5.9 long	1976 Sep 23.4	65.01	89.53	6630	203	300	0.007	65

R	[Soyuz 11A511U]	[09435]	12.87 days	cylinder	2.4 dia	1976 Oct 4.51	65.01	89.40	6624	199	291	0.007	59

BAI	1976 Oct 5.27	5900?

D	Cosmos 856	1976-96 B	1976 Sep 22.40	Cylinder	7.5 long	1976 Sep 23.1	65.02	89.37	6622	202	286	0.006	55

Block I 3rd stage 	[09436]	8 days	2500?	2.6 dia	1976 Sep 30.17	65.01	87.92	6550	168	176	0.0006	45

1976 Sep 30

D	Nauka-Capsule**	1976-96 E	1976 Sep 22.40	Ellipsoid	0.9 long	1976 Oct 3.7	65.01	89.41	6624	201	291	0.007	61

[09448]	24 days	200?	1.9 dia	1976 Oct 16.35	65.00	87.68	6538	152	167	0.001	45

1976 Oct 16

D	Fragment	1976-96 C	[09437]	1976 Sep 23	1 day		65.00	89.00		208	256	from Satcat

D	Fragment	1976-96 D	[09447]	1976 Oct 16	16 days	1976 Oct 3.70	64.99	89.23	6615	197	276	0.006	56

1976 Oct 6.97	64.99	88.28	6577	174	223	0.004	80

**	Ejected from 1976-96 A on 1976 Oct 3.

D	Cosmos 857	1976-97 A	1976 Sep 24.63	Sphere-	6.5 long?	1976 Sep 25.7	62.80	89.50	6629	179	323	0.011	73

R	[Soyuz 11A511U]	[09439]	12.61 days	cylinder	2.4 dia	1976 Oct 4.4	62.81	89.56	6632	177	331	0.012	74

1976 Oct 7.24	6300?		1976 Oct 7.10	62.80	89.52	6629	176	324	0.011	74

D	Cosmos 857	1976-97 B	1976 Sep 24.63	Cylinder	7.5 long	1976 Sep 24.8	62.79	89.39	6624	176	315	0.010	68

Block I 3rd stage 	[09442]	4.66 days	2500?	2.6 dia	1976 Sep 25.54	62.79	89.27	6617	173	303	0.010	67				1976 Sep 29.29			1976 Sep 28.99	62.07	87.77	6542	147	180	0.003	71

D	Cosmos 857	1976-97 C	1976 Sep 24.63	Cone	1.5 long?	1976 Oct 6.4	62.80	89.49	6629	176	325	0.011	73

motor*	[09449]	21 days	600? full	2 dia?	1976 Oct 15.49	62.80	87.50	6529	141	160	0.001	59

1976 Oct 15

D	Fragment	1976-97 D	[09450]	1976 Oct 8	14 days	1976 Oct 6.54	62.80	89.47	6627	173	323	0.011	74

1976 Oct 8.03	62.82	88.50	6579	159	241	0.006	74

D	Fragment	1976-97 E	[09451]	1976 Oct 9	15 days	1976 Oct 6.60	62.81	89.23	6615	173	300	0.010	76							1976 Oct 9.13	62.80	87.98	6553	164	185	0.002	76

D	Fragment	1976-97 F	[09470]	1976 Oct 11	17 days	1976 Oct 9.50	62.78	90.60	6683	210	398	0.014	24

1976 Oct 11.25	62.78	89.28	6617	198	279	0.006	24

*	Jettisoned from 1976-97 A on 1976 Oct 6

Cosmos 858	1976-98 A	1976 Sep 29.30	Cylinder +	2 long?	1976 Sep 29.77	74.06	100.77	7174	780	810	0.002	29

[Kosmos 11K65M	[09443]	120 years	paddles?	1 dia?	1976 Sep 30.6	74.06	100.93	7181	792	813	0.001	19

53716-333]	PLE-LC132		750?		2004 Jul 6.71	74.05	100.47	7159	770	791	0.001	343							2021 Dec 1.94	74.05	100.40	7156	768	786	0.001	124

Cosmos 858	1976-98 B	1976 Sep 29.30	Cylinder	7.4 long	1976 Sep 29.77	74.06	100.77	7174	780	810	0.002	29

2nd stage	[09444]	100 years	2200?	2.4 dia	1976 Sep 30.5	74.06	100.82	7175	783	811	0.002	33

2004 Jul 6.95	74.05	100.23	7148	759	779	0.001	223

2021 Dec 1.91	74.05	100.13	7143	754	775	0.001	279

Fragment	1976-98 C	[14816]			1985 Feb 5.25	74.04	101.02	7185	790	823	0.002	151

2004 Jul 6.57	74.04	99.48	7113	722	746	0.002	145

2021 Dec 1.90	74.04	98.97	7087	698	720	0.002	273

Fragment	1976-98 D	[14817]			1984 Feb 5.19	7.10	100.35	7154	758	792	0.002	175

2004 Jul 6.45	74.08	97.95	7039	652	669	0.001	139

2021 Dec 1.77	74.08	96.60	6974	589	603	0.001	303

Fragment	1976-98 E	[18504]			1985 Mar 26.30	74.06	100.57	7164	768	802	0.002	91

2004 Jul 7.68	74.05	98.53	7067	678	700	0.002	346

2021 Dec 1.80	74.04	97.65	7025	639	653	0.001	126

D	Cosmos 859	1976-99 A	1976 Oct 10.40	Sphere-	6.5 long?	1976 Oct 10.83	65.01	89.58	6633	171	337	0.012	67

R	[Soyuz 11A511U]	[09471]	10.9 days	cylinder	2.4 dia	1976 Oct 11.1	65.00	89.60	6633	173	337	0.012	67

BAI	1976 Oct 21.3	6300?		1976 Oct 13.4	64.99	89.36	6621	172	314	0.011	66

1976 Oct 20.69	64.99	89.30	6619	168	312	0.011	62

D	Cosmos 859	1976-99 B	1976 Oct 10.40	Cylinder	7.5 long	1976 Oct 10.6	65.00	89.52	6629	172	330	0.012	71

2nd stage	[09472]	5.27 days	2500?	2.6 dia	1976 Oct 15.34	64.99	87.87	6547	150	187	0.003	61

1976 Oct 15.67

D	Cosmos 859	1976-99 E	1976 Oct 10.40	Cone	1.5 long?	1976 Oct   20.6	64.99	89.01	6604	167	285	0.009	61

motor	[09492]	15 days	6007 full	2 dia?	1976 Oct 22.04	65.00	88.15	6561	161	205	0.003	63

1976 Oct 25

D	Fragment	1976-99 C	[09473]	1976 Oct 11	1 day	1976 Oct 10.64	65.05	88.98	6603	165	284	0.009	86

1976 Oct 11.14	64.98	88.87	6597	164	273	0.008	66

D	Fragment	1976-99 D	[09491]	1976 Oct 24	14 days	1976 Oct 20.69	64.99	89.17	6612	166	300	0.010	61

1976 Oct 24.02	64.97	88.08	6558	154	205	0.004	61

D	Soyuz 23*	1976-100 A	1976 Oct 14.74	Sphere-	7.5 long	1976 Oct 15.0	51.61	88.56	6584	188	224	0.003	74

2M	[Soyuz 11A511U]	[09477]	2.00 days	cylinder	2.3 dia	1976 Oct 15.04	51.59	89.50	6628	229	270	0.003	243

R		BAI	1976 Oct 16.74	6570?		1976 Oct 15.41	51.58	89.53	6630	235	267	0.002	225

1976 Oct 15.9	51.58	89.60	6636	246	269	0.002	233							1976 Oct 16.47	51.59	89.63	6635	246	266	0.001	264

D	Soyuz 23	1976-100 B	1976 Oct 14.74	Cylinder	7.5 long	1976 Oct 14.97	51.61	88.62	6584	188	224	0.003	74

Block I 3rd stage 	[09480]	2 days	2500?	2.6 dia	1976 Oct 15.4	51.61	88.46	6580	188	219	0.003	83

1976 Oct 16			1976 Oct 16

*	Soyuz 23 rendezvoused with Salyut 5 about 1976 Oct 15.8, but failed to dock.

Marisat 2	1976-101 A	1976 Oct 14.95	Cylinder	2.4 long?	1976 Oct 15.0	26.00	652.92	24931	185	36920	0.737	174

[Delta 2914 614	[09478]	>million years	655 full	1.9 dia?	1976 Oct 22.6	2.6	1436.2	42106	35051	36525	0.017	-

# 127]	CC-LC17A		362 empty		1977 Jan 18.97	2.10	1436.07	42164	35781	35791	0.0001	353

2000 Mar 2.00	12.82	1438.69	42216	35835	35840	0.0001	45

2004 Jul 11.07	13.31	1436.07	42164	35783	35788	0.0001	139

2004 Aug 8.02	13.31	1436.07	42164	35774	35798	0.0003	175

2008 Oct 29.25	13.59	1436.13	42166	35778	35796	0.0002	300

Graveyard orbit	2008 Oct 31.77	13.20	1475.90	42940	36120	37004	0.010	195

2015 Jun 10.68	12.81	1475.55	42934	36124	36986	0.010	252

2021 Dec 3.53	9.28	1475.55	42934	35108	37002	0.010	318

D	Marisat 2	1976-101 B	1976 Oct 14.95	Cylinder +	6.4 long	1976 Oct 15.12	28.60	92.72	6786	182	633	0.033	163

Delta 2nd stage	[09479]	32 days	annulus	1.52 and	1976 Oct 16.4	28.58	92.40	6778	182	618	0.032	178

1976 Nov 15	3507	2.44 dia	1976 Nov 14.73	28.57	88.02	6555	148	205	0.004	170

D	Marisat 2	1976-101 E	1976 Oct 14.95	Sphere-	1.32 long	1976 Oct 15.0	25.9	644.7	24717	200	36478	0.734	-

Star-37E PKM	[09542]	210 days	cone	0.94 dia	1976 Nov 12.89	25.86	644.58	24718	198	36481	0.734	192

1977 May 12	66		1977 Apr 4.30	26.64	617.78	24028	189	35110	0.727	99

Marisat 2	1976-101 F	1976 Oct 14.95	-	-		Orbit similar to 1976-101	A

apogee motor	[NNA]	>million years	293 full

D	2nd stage Fragment	1976-101 C	[09493]	1976 Nov 1	18 days	1976 Oct 20.88	28.59	91.67	6735	178	535	0.027	229

1976 Oct 28.50	28.59	89.90	6648	169	369	0.015	321

D	2nd stage Fragment	1976-101 D	[09498]	1976 Nov 4	21 days	1976 Oct 21.89	28.57	91.47	6725	179	514	0.025	245

1976 Oct 28.68	28.57	90.03	6655	175	377	0.015	327

Meteor-1 26	1976-102 A	1976 Oct 15.96	Cylinder +	5 long?	1976 Oct 16.02	81.28	102.42	7251	855	890	0.002	280

[Vostok 8A92M]	[09481]	500 years	2 vanes	1.5 dia?	1976 Oct 22.9	81.27	102.48	7253	857	892	0.002	263

PLE		2200?		2004 Jul 6.85	81.22	102.18	7240	848	875	0.002	188

2021 Dec 4.18	81.22	102.13	7238	843	876	0.002	273

Meteor-1 26	1976-102 B	1976 Oct 15.96	Cylinder	3.8 long	1976 Oct 17.8	81.27	102.59	7258	836	924	0.006	192

Block E 3rd stage 	[09482]	400 years	1440	2.6 dia	2004 Jul 6.51	81.27	102.33	7247	827	910	0.006	158

2021 Dec 4.10	81.26	102.30	7246	808	927	0.008	250

Cosmos 860*	1976-103 A	1976 Oct 17.76	Cone-	6 long?	1976 Oct 18.06	65.05	89.65	6636	250	264	0.001	298

[Tsyklon-2]	[09486]	600 years	cylinder	2 dia?	1976 Oct 23.4	65.04	89.66	6637	252	265	0.001	274

BAI-LC90				1976 Nov 12.9	64.70	104.33	7342	919	1008	0.006	350

2004 Jul 6.57	64.70	104.25	7338	911	1008	0.007	203

2021 Dec 3.40	64.70	104.25	7337	900	1018	0.008	279

D	Cosmos 860 *	1976-103 B	1976 Oct 17.76	Irregular	-	1976 Nov 12.1	65.04	89.54	6631	244	261	0.001	286

Platform (PELPS)	[09531]	73 days			1976 Dec 28.26	65.04	87.62	6535	156	157	0.00002	257

1976 Dec 29

D	Antenna	1976-103 C	[09537]	1976 Nov 14	28 days	1976 Nov 11.84	65.02	89.50	6628	24	256	0.0009	188

D	Cosmos 860 *	1976-103 D	1976 Oct 17.76	Cylinder	8 long?	1976 Nov 12.0	65.03	89.49	6628	243	257	0.001	200

rocket	[09538]	29 days	1500?	2.5 dia?	1976 Nov 14.74	65.03	88.48	6578	199	199	0	130

1976 Nov 15			1976 Nov 14.81	65.02	88.43	6576	197	197	0	130

D	Fragment	1976-103 E	[09539]	1976 Nov 15	29 days	1976 Nov 10.84	65.02	89.03	6605	224	228	0.0003	165

1976 Nov 12.15	65.10	89.48	6627	240	257	0.001	286

D	Fragment	1976-103 F	[19297]	1998 Apr 2	7837 days	1988 Apr 2.17	64.65	90.72	6688	297	322	0.002	210

Fragment Coolant	1976-103 G	[29194]			2006 Jun 5.96	64.69	103.38	7297	873	964	0.006	328

2021 Dec 3.75	64.69	103.10	7284	854	956	0.007	256

Fragment Coolant	1976-103 H	[29195]			2006 Jun 1.40	64.70	103.97	7325	900	993	0.006	334

2021 Dec 2.94	64.70	103.87	7320	885	998	0.008	268

Fragment Coolant	1976-103 J	[29196]			2006 Jun 4.34	64.70	103.97	7325	899	993	0.006	335

2021 Dec 2.91	64.70	103.87	7320	884	998	0.008	268

*	1976-103 B and 1976-103 D attached to 1976-103 A until orbit change on 1976 Nov 10.78

Cosmos 861	1976-104 A	1976 Oct 21.71	Cone-	6 long?	1976 Oct 22.63	65.96	89.63	6635	249	263	0.001	270

[Tsyklon 2]	[09494]	600 years	cylinder	2 dia?	1976 Oct 24.4	64.96	89.65	6636	251	265	0.001	269

BAI-LC90				1976 Dec 23.54	64.86	104.30	7340	918	1004	0.006	218

1977 Jan 24.5	64.86	104.31	7341	921	1005	0.006	210

2004 Jul 10.80	64.86	104.23	7337	933	984	0.003	45

2021 Dec 3.53	64.86	104.22	7336	911	1005	0.006	298

D	Cosmos 861 *	1976-104 C	1976 Oct 21.71	Irregular	-	1976 Dec 20.78	64.95	89.57	6631	244	262	0.001	254

platform (PELPS)	[09631]	107 days			1976 Dec 21.6	64.96	89.55	6631	244	262	0.001	260

1977 Feb 4			1977 Feb 3.19	64.95	87.82	6545	165	167	0.00009	272

D	Cosmos 861 *	1976-104 D	1976 Oct 21.71	Cylinder	8 long?	1976 Dec 20.78	64.95	89.45	6626	233	262	0.002	268

antenna	[09632]	65 days	1500?	2.5 dia?	1976 Dec 21.9	64.96	89.28	6618	226	253	0.002	264

1976 Dec 25			1976 Dec 25.28	64.94	87.60	6534	155	156	0.0001	279

D	Fragment	1976-104 B	[09633]	1976 Oct 21	< 0.29 day	1976 Oct 21	64.80	104.30		926	999	from Satcat

*	1976-104 C and 1976-104 D attached to 1976-104 A until orbit change about 1976 Dec 20

Cosmos 862 #	1976-105 A	1976 Oct 22.39	Windmill +	4.2 long?	1976 Oct 43	62.82	709.82	26359	527	39434	0.738	318

[Molniya 8K78M]	[09495]	disintegrated	6 vanes?	1.6 dia?	1976 Oct 22.9	62.81	712.32	26422	571	39516	0.737	318

PLE-LC43/4		12507		1976 Oct 26.39	62.81	712.48	26425	579	39514	0.737	318

1976 Nov 1.0	62.81	718.11	26565	598	39775	0.738	-

2004 Jul 4.41	68.36	718.37	26570	4601	35782	0.587	90

2021 Dec 2.69	69.74	717.77	26556	4057	36297	0.607	238

D	Cosmos 862	1976-105 B	1976 Oct 22.39	Cylinder	7.5 long	1976 Oct 22.5	62.79	92.20	6762	222	545	0.024	116

Block I 3rd stage  	[09496]	66 days	2500?	2.6 dia	1976 Dec 26.55	62.77	88.33	6571	173	211	0.003	118

1976 Dec 27

D	Cosmos 862	1976-105 C	1976 Oct 22.39	Irregular	-	1976 Oct 22.5	62.84	92.47	6775	198	596	0.029	114

4th stage casing 	[09497]	49 days			1976 Dec 10.20	62.83	88.10	6559	159	202	0.003	112

1976 Dec 10

D	Cosmos	1976-105 D	1976 Oct 22.39	Cylinder	2.0  long	1976 Oct 23.92	62.67	711.83	26409	599	39461	0.736	318

Block L 4th stage 	[09506]	6234 days	440	2.0  dia	1976 Oct 29.8	62.70	711.90	26411	606	39460	0.736	318

1993 Nov 16			1993 Oct 17.80	62.56	710.48	26376	206	39788	0.750	201

Fragments	1976-105 E-R   12 pieces, 7 have decayed		For orbital information see extra pages at the end of the year

#	Disintegrated on 1977 Mar 15

D	Cosmos 863	1976-106 A	1976 Oct 25.61	Sphere-	6.5 long?	1976 Oct 25.72	62.82	89.98	6652	182	366	0.014	78

R	[Soyuz 11A511U]	[09499]	10.68 days	cylinder	2.4 dia	1976 Oct 26.3	62.81	89.74	6641	178	348	0.013	85

PLE	1976 Nov 5.29	6300?		1976 Oct 26.7	62.81	89.40	6624	170	322	0.011	75

1976 Nov 2.41	62.80	89.23	6615	166	307	0.011	74

1976 Nov 3.90	62.80	89.52	6629	166	335	0.013	71

D	Cosmos 863	1976-106 B	1976 Oct 25.61	Cylinder	7.5 long	1976 Oct 25.84	62.81	89.67	6637	176	340	0.012	81

Block I 3rd stage 	[09500]	7 days	2500?	2.6 dia	1976 Oct 26.3	62.80	89.60	6634	178	334	0.012	82

1976 Nov 1			1976 Nov 1.58	62.77	87.73	6541	149	175	0.002	87

D	Cosmos 863	1976-106 E	1976 Oct 25.61	Cone	1.5 long?	1976 Nov 5.0	62.80	89.28	6618	167	313	0.011	71

motor	[09521]	17 days	600? full	2 dia?	1976 Nov 11.50	62.80	87.68	6538	135	183	0.004	77

1976 Nov 11

D	Fragments	1976-106 C,D,F-K    7 pieces, all have decayed	For orbital information see extra pages at the end of the year

Ekran 1 #	1976-107 A	1976 Oct 26.62	Cylinder	-	1976 Oct 27.5	0.2	1437	42228	35850	35850	0	-*

[Proton 8K82K	[09503]	>million years	+ plate		1977 Mar 19.94	0.09	1436.94	42165	35532	36041	0.006	221

290-01 11S86]	BAI-LC81P		2000?		2004 Jul 5.93	14.72	1436.17	42166	35528	36047	0.006	317							2015 Aug 27.79	12.18	1436.75	42178	35550	36048	0.006	70

2016 Oct 18.76	11.59	1435.37	42151	35526	36018	0.006	80

2018 Jan 5.88	10.84	1436.80	42179	35544	36056	0.006	90

2019 Jan 11.39	10.13	1435.35	42150	35511	36032	0.006	101

2020 Feb 2.76	9.32	1436.83	42179	35531	36070	0.006	114

2021 Mar 1.12	8.43	1435.35	42150	35493	36050	0.007	129

2021 Dec 3.82	7.78	1436.57	42174	35515	36076	0.007	139

D	Ekran 1	1976-107 B	1976 Oct 26.62	Cylinder	6.5 long?	1976 Oct 27.0	51.48	88.18	6565	178	196	0.001	305

third   stage	[09504]	3 days		4 dia	1976 Oct 28.44	51.50	87.83	6546	161	173	0.0009	338

1976 Oct 29

D	Ekran 1	1976-107 C	1976 Oct 26.62	Irregular	-	1976 Oct 26.98	51.47	88.17	6562	182	185	0.0002	16

4th stage casing 	[09505]	1 day			1976 Oct 27.0	51.47	88.08	6560	181	183	0.0002	16

1976 Oct 27

D	Ekran 1 **	1976-107 D	1976 Oct 26.62			1976 Nov 6.99	47.23	627.03	24267	315	35462	0.724	3

Ullage motor	[09540]	243 days			1977 Jun 12.87	46.45	277.90	14107	41	15415	0.545	69

1977 Jun 26

D	Ekran 1 **	1976-107 E	1976 Oct 26.62			1976 Nov 7.84	47.28	625.93	24239	254	35467	0.726	3

Ullage motor	[09541]	206 days			1977 May 5.91	46.58	129.68	8488	150	4068	0.231	63

1977 May 20

Ekran 1	1976-107 F	1976 Oct 26.62	Cylinder	5.5 long	Synchronous orbit similar to 1976-107 A

Block DM 4th stage	[11569]	> million	17300 full	4.0 dia	1977 Jan 31.97	0.16	1419.25	41835	35334	35578	0.003	287

years			2004 Jul 7.68	14.30	1419.32	41836	35414	35501	0.001	343

2021 Dec 3.73	6.94	1419.33	41836	35406	35508	0.001	152

*	Approximate orbit.

#	Ekran means screen.

Cosmos 864	1976-108 A	1976 Oct 29.53	Cylinder	2.1 long	1976 Oct 29.59	82.93	104.83	7365	968	1005	0.003	302

[Kosmos 11K65M	[09509]	1200 years	810	2.0 dia	1976 Oct 30.2	82.94	104.90	7367	966	1011	0.003	292

53772-414]	PLE-LC132				2004 Jul 4.93	82.94	104.72	7360	960	1002	0.003	196

2021 Dec 3.98	82.94	104.68	7358	957	1003	0.003	88

Cosmos 864	1976-108 B	1976 Oct 29.53	Cylinder	7.4 long	1976 Oct 10.73	82.94	104.73	7360	964	999	0.002	306

2nd stage	[09510]	600 years	2200?	2.4 dia	1976 Oct 30.1	82.94	104.79	7361	966	1000	0.002	291

2004 Jul 6.88	82.94	104.55	7352	953	994	0.003	103

2021 Dec 4.14	82.94	104.52	7351	954	990	0.002	297

Fragment	1976 108 C	[43294]			2018 Apr 13.74	82.94	104.68	7358	958	1001	0.003	198

2021 Dec 4.25	82.94	104.68	7358	956	1002	0.003	86

D	Cosmos 865	1976-109 A	1976 Nov 1.48	Sphere-	5.0 long	1976 Nov 1.53	72.85	89.65	6636	164	331	0.011	50

R	[Soyuz 11A511U]	[09515]	11.78 days	cylinder	2.4 dia	1976 Nov 2.4	72.88	89.81	6643	203	326	0.009	67

PLE	1976 Nov 13.26	5700?		1976 Nov 10.44	72.88	89.70	6638	200	319	0.009	50

D	Cosmos 865	1976-109 B	1976 Nov 1.48	Cylinder	7.5 long	1976 Nov 1.7	72.87	89.69	6637	206	311	0.008	66

Block I 3rd stage 	[09516]	13 days	2500?	2.6 dia	1976 Nov 2.09	72.87	89.63	6635	205	307	0.008	66

1976 Nov 14			1976 Nov 13.11	72.86	88.22	6565	175	198	0.002	36

D	Fragment	1976-109 C	[09517]	1976 Nov 5	4 days	1976 Nov 1.96	72.85	89.45	6626	196	299	0.008	65

1976 Nov 2.33	72.85	89.28	6618	200	279	0.006	69

D	Fragment	1976-109 D	[09519]	1976 Nov 7	6 days	1976 Nov 3.27	72.93	89.65	6636	194	321	0.010	87

1976 Nov 4.82	72.89	89.08	6608	196	262	0.005	67

D	Fragment	1976-109 E	[09520]	1976 Nov 22	21 days	1976 Nov 4.27	72.88	89.70	8638	199	320	0.009	66

1976 Nov 21.05	72.91	87.82	6545	166	166	0	195

D	Fragment	1976-109 F	[09523]	1976 Nov 10	9 days	1976 Nov 4.70	72.87	89.40	6623	199	291	0.007	69

1976 Nov 9.52	72.85	88.15	6560	178	186	0.0006	52

D	Fragment **	1976-109 G	[09525]	1977 Feb 10	101 days	1976 Nov 5.19	72.87	91.45	6724	218	473	0.019	98

1976 Nov 29.47	72.86	91.03	6704	215	436	0.017	41

D	Fragment	1976-109 H	[09526]	1977 Feb 5	96 days	1976 Nov 9.06	72.87	91.32	6717	217	460	0.018	88

1976 Nov 29.49	72.85	90.93	6699	215	426	0.016	41

**	May be a scientific Nauka-capsule.

D	Cosmos 866	1976-110 A	1976 Nov 11.45	Sphere-	6.5 long?	1976 Nov 11.9	64.98	89.16	6612	180	287	0.008	50

R	[Soyuz 11A511U]	[09532]	11.9 days	cylinder	2.4 dia	1976 Nov 12.7	64.98	89.45	6626	177	318	0.011	52

BAI	1976 Nov 23.3	6300?		1976 Nov 22.46	64.97	88.37	6573	170	218	0.004	66

D	Cosmos 866	1976-110 B	1976 Nov 11.45	Cylinder	7.5 long	1976 Nov 11.88	64.98	88.98	6603	171	278	0.008	50

Block I 3rd stage 	[09533]	3 days	2500?	2.6 dia	1976 Nov 12.1	64.98	88.93	6600	168	276	0.008	50

1976 Nov 14			1976 Nov 14.40	64.98	87.95	6551	158	187	0.002	53

D	Cosmos 866	1976-110 F	1976 Nov 11.45	Cone	1.5 long?	1976 Nov 22.71	64.98	89.23	6565	163	210	0.004	66

motor*	[09551]	13 days	600?	2 dia?	1976 Nov 23.1	64.97	88.06	6557	124	233	0.008	63

1976 Nov 24	full		1976 Nov 23.69	64.98	87.83	6546	161	174	0.001	63

D	Fragments	1976-110 C-E, G  4 pieces, all have decayed		For orbital information see extra pages at the end of the year

*	Jettisoned from 1976-11O A about 1976 Nov 22.

D	Cosmos 867	1976-111 A	1976 Nov 23.69	Sphere-	6.5 long?	1976 Nov 23.8	62.83	91.06	6704	250	402	0.011	114

R	[Soyuz 11A511U]	[09552]	12.64 days	cylinder	2.4 dia	1976 Nov 26.4	62.83	92.07	6755	352	401	0.004	88

PLE	1976 Dec 6.33	6300?		1976 Dec 2.67	62.82	92.07	6754	350	401	0.004	93

D	Cosmos 867	1976-111 B	1976 Nov 23.69	Cylinder	7.5 long	1976 Nov 23.93	62.81	90.93	6699	250	390	0.010	113

rocket	[09554]	71 days	2500?	2.6 dia	1976 Nov 30.6	62.80	90.83	6692	249	383	0.010	107

1977 Feb 1			1977 Jan 30.92	62.80	88.43	6575	187	207	0.001	109

D	Cosmos 867	1976-111 F	1976 Nov 23.69	Cone	1.5 long?	1976 Dec 6.4	62.82	92.02	6752	351	397	0.003	95

engine*	[09582]	410 days	600?	2 dia?	1976 Dec 7.97	62.83	92.02	6752	350	397	0.004	97

1978 Jan 7	full		1978 Jan 7.30	62.79	87.77	6542	161	166	0.0004	4

D	Fragments	1976-111 C-E,G-K    7 pieces, all have decayed	For orbital information see extra pages at the end of the year

*	Jettisoned from 1976-111 A about 1976 Dec 5.

D	Prognoz 5	1976-112 A	1976 Nov 25.17	Spheroid	1.8 dia?	1977 Jan 1.0	65.2	5728	106047	777	198560	0.933	-

[Molniya 8K78M/SOL]	[09557]	959 days	+ 4 vanes		1977 Sep 18.25	66.58	5728.73	106055	3869	195484	0.903	284

BAI	1979 Jul 12	930

D	Prognoz 5	1976-112 B	1976 Nov 25.17	Cylinder	7.5 long	1976 Nov 25.5	64.97	91.48	6726	231	464	0.017	66

Block I 3rd stage 	[09558]	59 days	2500?	2.6 dia	1977 Jan 23.17	64.96	87.85	6546	165	170	0.0004	50

1977 Jan 23

D	Prognoz 5	1976-112 C	1976 Nov 25.17	Irregular	-	1976 Nov 26.05	65.00	91.52	6728	204	494	0.022	65

4th stage casing 	[09559]	41 days			1977 Jan 4.95	64.98	88.20	6564	163	208	0.003	50

1977 Jan 5

D	Prognoz 5	1976-112 D	1976 Nov 25.17			1976 Nov 26.50	64.97	91.80	6741	236	489	0.019	66

Ullage motor	[09560]	60 days			1977 Jan 22.07	65.00	88.07	6557	160	197	0.003	64

1977 Jan 24

D	Prognoz 5	1976-112 E	1976 Nov 25.17	Cylinder	2.0 long			Orbit similar to 1976-112 A

rocket	[NNA]	10 years?	440	2.0 dia

D	Cosmos 868	1976-113 A	1976 Nov 26.61	Cylinder?	-	1976 Nov 26.6	65.05	89.94	6651	110	436	0.025	51

[Tsyklon 2]	[09561]	589 days			1976 Nov 26.9	65.04	93.29	6811	422	444	0.002	287

BAI-LC90	1978 Jul 8			1976 Nov 29.45	65.04	93.28	6814	428	442	0.001	287

1978 Jul 7.24	64.99	88.52	6580	190	211	0.002	257

D	Cosmos 868	1976-113 B	1976 Nov 26.61	Cylinder	8 long?	1976 Nov 26.97	64.00	89.00	6603	112	337	0.017	51

2nd stage	[09562]	1 day	1500?	2.5 dia?	1976 Nov 27.1	64.98	88.64	6586	113	303	0.014	53

1976 Nov 27			1976 Nov 27.12	65.04	89.30	6619	231	249	0.001	283

D	Cosmos 869 *	1976-114 A	1976 Nov 29.67	Sphere-	7.5 long	1976 Nov 29.78	51.78	89.35	6621	196	289	0.007	88

R	[Soyuz 11A511U]	[09564]	17.7 days	cylinder +2	2.2 dia	1976 Nov 30.0	51.76	89.36	6624	198	293	0.007	89

BAI	1976 Dec 17.4	wings 6570?		1976 Dec 2.45	51.77	89.27	6617	194	282	0.007	99

1976 Dec 4.00	51.76	89.73	6640	188	335	0.011	100

1976 Dec 4.93	51.77	90.45	6675	258	335	0.006	125

1976 Dec 9.35	51.78	91.12	6708	267	391	0.009	123

1976 Dec 10.3	51.78	91.06	6707	268	390	0.009	127

1976 Dec 12.7	51.77	90.56	6682	299	309	0.001	254

1976 Dec 12.28	51.77	90.62	6693	300	309	0.0007	271

D	Cosmos 869	1976-114 B	1976 Nov 29.67	Cylinder	7.5 long	1976 Nov 29.9	51.78	89.24	6618	193	286	0.007	89

Block I 3rd stage 	[09565]	7 days	2500?	2.6 dia	1976 Dec 5.88	51.72	87.90	6549	159	182	0.002	101

1976 Dec 6

*	Unmanned military Soyuz test flight.

D	Cosmos 870	1976-115 A	1976 Dec 2.01	Cylinder +	2 long?	1976 Dec 4.65	74.01	95.22	6908	511	547	0.003	355

[Kosmos 11K65M	[09573]	1479 days	paddles?	1 dia?	1976 Dec 6.6	74.00	95.26	6909	513	548	0.003	352

53731-273]	PLE-LC132	1980 Dec 20	900?		1980 Dec 20.19	73.91	87.68	6538	157	162	0.0004	344

D	Cosmos 870	1976-115 B	1976 Dec 2.01	Cylinder	7.4 long	1976 Dec 4.6	74.00	95.14	6903	501	548	0.003	1

2nd stage	[09576]	1549 days	2200?	2.4 dia	1981 Feb 28.66	73.96	87.23	6516	131	144	0.001	233

1981 Feb 28

D	Fragment	1976-115 C	[09577]	1978 Feb 10	435 days	1976 Dec 2.40	74.00	95.10	6902	505	542	0.003	0

1977 Dec 4.47	73.96	92.63	6782	396	411	0.001	118

D	Fragment	1976-115 D	[09991]	1978 Apr 30	514 days	1977 May 15.30	73.94	94.77	6886	485	530	0.003	324

1978 Apr 9.35	73.97	92.13	6757	365	393	0.002	188

D	Fragment	1976-115 E	[09992]	1978 Jun 11	556 days	1977 May 12.58	73.97	94.80	6888	487	531	0.003	352

1978 May 10.93	73.97	93.47	6823	415	473	0.004	311

D	Fragment	1976-115 F	[09993]	1980 Mar 7	1191 days	1977 May 18.28	74.03	94.82	6888	490	530	0.003	325

1980 Feb 26.46	73.94	89.67	6636	253	262	0.0007	272

D	Molniya-2 16	1976-116 A	1976 Dec 2.12	Windmill +	4.2 long?	1976 Dec 6.3	62.88	735.70	26996	637	40599	0.740	288

[Molniya 8K78M]	[09574]	5160 days	6 vanes	1.6 dia	1976 Dec 10.3	62.57	717.93	26560	575	39789	0.738	288

PLE	1991 Jan 18	12507		1977 Jan 2.21	62.93	717.68	26553	599	39750	0.737	288

1990 Dec 31.37	61.98	634.20	24452	76	36070	0.736	263

D	Molnlya-2 16	1976-116 B	1976 Dec 2.12	Irregular	-	1976 Dec 3.1	62.86	92.90	6796	211	624	0.030	119

Block I 3rd stage 	[09575]	92 days			1977 Jan 1.63	62.84	92.15	6758	210	549	0.025	124

1977 Mar 4			1977 Mar 3.56	62.83	87.63	6536	146	168	0.002	102

D	Molniya-2 16	1976-116 C	1976 Dec 2.12	Cylinder	7.5 long	1976 Dec 2.84	62.86	91.62	6733	192	515	0.024	119

4th stage casing 	[09578]	67 days	2500?	2.6 dia	1976 Dec 3.6	62.86	92.89	6795	214	620	0.030	121

1977 Feb 7			1977 Feb 6.96	62.84	88.05	6556	153	202	0.004	114

D	Molniya-2 16	1976-116 D	1976 Dec 2.12	Cylinder	2.0 long	1976 Dec 7.2	62.88	732.04	26907	629	40429	0.740	288

Block L 4th stage 	[09579]	5483 days	440	2.0 dia	1977 Jan 10.31	62.98	731.98	26905	596	40456	0.741	288

1991 Dec 7			1991 Dec 7.81	62.17	96.48	6968	68	1112	0.075	268

D	Molniya-2 16	1976-116 E	1976 Dec 2.12			1976 Dec 5.06	62.86	92.38	6770	198	584	0.028	116

Ullage motor	[09580]	73 days

1977 Feb 13

D	Molniya-2 16	1976-116 F	1976 Dec 2.12			1976 Dec 4.82	62.84	93.00	6800	212	631	0.031	121

Ullage motor	[09581]	40 days			1976 Dec 7.79	62.84	92.88	6794	210	621	0.030	120

1977 Jan 11

D	China 7 *(FSW-0 2)	1976-117 A	1976 Dec 7.19	Cylinder?	-	1976 Dec 7.36	59.45	91.10	6707	168	488	0.024	154

r	[CZ-2 C-2]	[09587]	26 days	lst 3 days		1976 Dec 10.3	59.45	91.01	6704	172	479	0.023	158

JIUQ-LA2	1977 Jan 2	3600, then 1200?	1976 Dec 11.3	59.45	90.92	6700	174	469	0.022	158

1977 Jan 1.48	59.43	87.90	6549	145	195	0.004	188

D	China 7	1976-117 B	1976 Dec 7.19	Cylinder	7 long	1976 Dec 7.43	59.45	91.03	6704	169	482	0.023	154

2nd stage	[09596]	22 days		3.35 dia	1976 Dec 7.8	59.45	91.00	6703	169	481	0.023	154

1976 Dec 29			1976 Dec 28.95	59.43	87.77	6543	146	182	0.003	181

D	Fragment	1976-117 C	[09597]	1976 Dec 9	2 day	1976 Dec 7.43	59.42	90.85	6695	168	465	0.022	156

1976 Dec 7.74	59.42	90.53	6679	152	449	0.022	156

*	Capsule, weight 1850 kg, returned to Earth on 1976 Dec 10.3.

Cosmos 871 *	1976-118 A	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.50	74.02	114.68	7820	1414	1469	0.004	218

[Kosmos 11K65M	[09588]	8000 years	40?	0.8 dia?	1976 Dec 12.4	74.03	114.74	7821	1420	1466	0.003	94

53716-330]	PLE-LC132				2004 Jul 5.65	74.03	114.67	7819	1417	1464	0.003	284

2021 Dec 3.91	74.03	114.68	7819	1416	1464	0.003	338

Cosmos 872 *	1976-118 B	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.73	74.02	114.48	7810	1399	1464	0.004	88

[09589]	7000 years	40?	0.8 dia?	1976 Dec 10.7	74.03	114.53	7812	1401	1466	0.004	84

2004 Jul 5.85	74.03	114.47	7809	1398	1463	0.004	203

2021 Dec 3.55	74.03	114.45	7809	1397	1463	0.004	220

Cosmos 873 *	1976-118 C	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.74	73.96	115.05	7836	1419	1496	0.005	250

[09590]	10000 years	40?	0.8 dia?	1976 Dec 12.5	74.03	115.60	7860	1466	1498	0.002	255

2004 Jul 5.20	74.03	115.53	7858	1464	1495	0.002	346

2021 Dec 3.56	74.03	115.53	7858	1463	1495	0.002	212

Cosmos 874 *	1976-118 D	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.74	74.04	115.77	7869	1464	1517	0.003	275

[09591]	10000 years	40?	0.8 dia?	1976 Dec 11.0	74.03	115.82	7870	1466	1518	0.003	270

2004 Jul 5.87	74.03	115.75	7868	1464	1515	0.003	67

2021 Dec 4.19	74.03	115.75	7868	1463	1516	0.003	333

Cosmos 875 *	1976-118 E	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.73	74.08	114.75	7823	1440	1448	0.0005	118

[09592]	9000 years	40?	0.8 dia?	1976 Dec 12.4	74.03	114.95	7831	1439	1466	0.002	87

2004 Jul 4.88	74.03	114.88	7828	1436	1463	0.002	342

2021 Dec 4.13	74.03	114.87	7828	1436	1463	0.002	79

Cosmos 876 *	1976-118 F	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.82	74.04	116.03	7881	1464	1540	0.005	271

[09593]	10000 years	40?	0.8  dia?	1976 Dec 11.7	74.03	116.07	7882	1466	1541	0.005	261

2004 Jul 4.96	74.03	116.00	7879	1464	1538	0.005	136

2021 Dec 3.83	74.03	116.00	7879	1464	1537	0.005	88

Cosmos 877 *	1976-118 G	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.81	74.04	115.10	7838	1450	1470	0.001	17

[09594]	9000 years	40?	0.8 dia?	1976 Dec 11.7	74.03	115.15	7840	1457	1466	0.001	100

2004 Jul 5.89	74.03	115.08	7837	1454	1463	0.0006	52

2021 Dec 3.66	74.03	115.07	7837	1454	1464	0.0006	197

Cosmos 878 *	1976-11B H	1976 Dec 7.43	Spheroid	1.0 long?	1976 Dec 7.82	74.04	115.32	7848	1460	1480	0.001	308

[09595]	10000 years	40?	0.8 dia?	1976 Dec 11.0	74.03	115.37	7850	1466	1477	0.001	274

2004 Jul 5.22	74.03	155.30	7847	1463	1474	0.0007	294

2021 Dec 3.62	74.03	115.30	7847	1464	1473	0.0006	117

Cosmos 871-878	1976-118 J	1976 Dec 7.43	Cylinder	7.4 long	1976 Dec 12.2	74.01	117.71	7956	1463	1692	0.014	265

2nd stage	[09598]	20000 years	2200?	2.4 dia	1976 Dec 14.93	74.01	117.67	7955	1462	1690	0.014	261

2004 Jul 6.80	74.02	117.63	7953	1465	1683	0.014	266

2021 Dec 3.80	74.02	117.63	7953	1465	1683	0.014	170

*	Strela-1M

D	Cosmos 879	1976-119 A	1976 Dec 9.42	Sphere-	5.0 long	1976 Dec 9.5	81.37	88.90	6597	213	225	0.001	336

R	[Soyuz 11A511U]	[09599]	12.83 days	cylinder	2.4 dia	1976 Dec 21.99	81.37	88.62	6585	203	209	0.0004	275

PLE	1976 Dec 22.25	5700?

D	Cosmos 879	1976-119 B	1976 Dec 9.42	Cylinder	7.5 long	1976 Dec 9.47	81.38	88.73	6591	203	221	0.001	305

Block I 3rd stage 	[09600]	3 days	2500?	2.6 dia	1976 Dec 10.3	81.38	88.66	6585	196	218	0.002	301

1976 Dec 12			1976 Dec 11.50	81.38	88.30	6569	170	210	0.003	289

D	Fragment	1976-119 C	[09602]	1977 Jan 3	25 days	1976 Dec 9.53	81.42	88.83	6596	207	227	0.002	332

1976 Dec 22.05	81.36	88.62	6585	204	208	0.0002	283

D	Fragment	1976-119 D	[09603]	1976 Dec 15	6 days	1976 Dec 10.15	81.40	88.68	6588	195	223	0.002	314

D	Cosmos 880 #	1976-120 A	1976 Dec 9.84	Cylinder?	4 long?	1976 Dec 10.56	65.85	96.43	6966	559	615	0.004	9

[Kosmos 11K65M	[09601]	disintegrated		2 dia?	1976 Dec 12.4	65.85	96.44	6967	560	617	0.004	359

53719-153]	PLE-LC132	1978 Dec 27			1991 Aug 31.55	65.79	88.55	6581	192	213	0.002	276

D	Cosmos 880	1976-120 B	1976 Dec 9.84	Cylinder	7.4 long	1976 Dec 13.1	65.85	96.33	6961	551	615	0.005	14

2nd stage	[09604]	2934 days	2200?	2.4 dia	1984 Dec 21.60	65.80	87.62	6535	151	161	0.0007	256

1984 Dec 21

Fragments	1976-12O C-BC   49 pieces, all have decayed		For orbital information see extra pages at the end of the year

#	Cosmos 886 passed close to Cosmos 880 on 1976 Dec 27.6 and exploded. Cosmos 880 was also destroyed.

*	In the USA, the 1976-120 A designation was subsequently transferred to a fragment which decayed on 1979 Oct 8

D	Cosmos 881*	1976-121 A	1976 Dec 15.07	Cone-cylinder	3.6 long	1976 Dec 15.18	51.60	88.90	6599	200	241	0.003	336

R?	[Proton 8K82K	[09606]	0.06 day	4250	2.8 dia	1976 Dec 15.4	51.60	88.75	6594	198	233	0.003	151

289-02]	BAI-LC81P	1976 Dec 15.13

D	Cosmos 882*	1976-121 B	1976 Dec 15.07	Cone-cylinder	3.6 long	1976 Dec 15.4	51.60	88.46	6579	189	213	0.002	204

R?		[09607]	0.06 day	4250	2.8 dia

1976 Dec 15.13

D	Cosmos 881	1976-121 C	1976 Dec 15.07	Cylinder	6.5 long?	1976 Dec 15.30	51.60	88.82	6595	196	236	0.003	337

third stage	[09608]	5 days		4 dia	1976 Dec 15.4	51.60	88.46	6579	189	213	0.002	204

1976 Dec 20			1976 Dec 19.83	51.59	87.58	6533	147	161	0.001	244

D	Fragment *1	1976-121 D	[09609]	1976 Dec 23	8 days	1976 Dec 15.36	51.60	88.82	6594	198	233	0.003	151

1976 Dec 23.28	51.59	87.48	6528	150	150	0	290

D	Fragment	1976-121 E	[09611]	1976 dec 26	11 days	1976 Dec 15.36	51.53	88.97	6602	208	238	0.002	127

1976 Dec 21.26	51.61	88.20	6564	179	192	0.0009	78

D	Fragment	1976-121 F	[09612]	1976 Dec 21	6 days	1976 Dec 15.42	51.58	88.75	6591	197	228	0.002	157

1976 Dec 16.35	51.59	88.58	6583	179	230	0.004	147

*	Probably manned-rel	ated; recovered after one orbit at 44(N, 73(E.

*1	http://planet4589.org/space/log/launchlog.txt gives 09609 as  82LB72 LVI-1 type TCS GVM.

Cosmos 883	1976-122 A	1976 Dec 15.58	Cylinder	2.1 long	1976 Dec 15.64	82.95	104.95	7370	981	1003	0.002	314

[Kosmos 11K65M	[09610]	1200 years	810	2.0 dia	1976 Dec 16.2	82.95	104.86	7365	961	1012	0.003	291

53782-426]	PLE-LC132				2004 Jul 5.20	82.95	104.67	7358	954	1004	0.003	301

2021 Dec 3.46	82.96	104.63	7356	951	1003	0.003	165

Cosmos 883	1975-122 B	1976 Dec 15.58	Cylinder	7.4 long	1976 Dec 15.93	82.96	104.68	7358	960	999	0.003	290

2nd stage	[09613]	600 years	2200?	2.4 dia	1976 Dec 17.0	82.95	104.74	7359	961	1000	0.003	287

2004 Jul 7.58	82.95	104.57	7352	953	995	0.003	207

2021 Dec 3.51	82.96	104.53	7351	950	995	0.003	42

D	Cosmos 884 #	1976-123 A	1976 Dec 17.40	Sphere-	5.5 long?	1976 Dec 17.45	65.19	89.63	6635	154	358	0.015	62

R	[Soyuz 11A511U]	[09614]	11.87 days	cylinder	2.4 dia	1976 Dec 17.7	65.05	89.63	6635	169	345	0.013	67

BAI	1976 Dec 29.27	6300?		1976 Dec 18.6	65.01	89.34	6621	166	319	0.012	74

1976 Dec 27.45	65.02	89..38	6622	169	319	0.011	59

D	Cosmos 884	1976-123 B	1976 Dec 17.40	Cylinder	7.5 long	1976 Dec 17.8	65.02	89.50	6629	171	330	0.012	67

Block I 3rd stage 	[09623]	6 days	2500?	2.6 dia	1976 Dec 23.34	65.03	88.37	6572	158	229	0.005	61

1976 Dec 23

D	Cosmos 884	1976-123 F	1976 Dec 17.40	Cone	1.5 long?	1976 Dec 29.63	65.05	88.97	6602	159	288	0.010	65

motor	[09646]	17 days	600? full	2 dia?	1976 Dec 30.6	65.05	88.98	6603	159	291	0.010	65

1977 Jan 3

D	Fragment	1976-123 C	[09624]	1977 Jan 31	45 days	1976 Dec 17.70	65.03	89.52	6629	168	333	0.012	66

D	Fragment	1976-123 D	[09639]	1976 Dec 31	14 days	1976 Dec 28.51	65.02	89.12	6609	168	293	0.009	62

1976 Dec 29.13	65.02	88.87	6597	166	271	0.008	56

D	Fragment	1976-123 E	[09640]	1977 Jan 1	15 days	1976 Dec 28.51	65.03	89.28	6618	167	311	0.011	56

1977 Jan 1.21	65.02	87.85	6546	147	188	0.003	64

#	Spacecraft was destroyed after a malfunction prevented re-entry and landing in the Soviet Union. Event identified by Russian officials during a joint

US-Russian investigation.

D	Cosmos 885 #	1976-124 A	1976 Dec 17.50	Cylinder?	4 long?	1976 Dec 20.6	65.84	94.40	6868	467	512	0.003	341

[Kosmos 11K65M	[09615]	1031 days		2 dia?	1979 Oct 12.66	65.82	88.82	6595	211	221	0.0007	241		53721-255]	PLE-LC132	1979 Dec 14

D	Cosmos 885	1976-124 B	1976 Dec 17.50	Cylinder	7.4 long	1976 Dec 20.6	65.85	94.26	6861	457	508	0.004	353

2nd stage	[09625]	992 days	2200?	2.4 dia	1979 Sep 4.22	65.82	88.40	6574	188	202	0.001	291

1979 Sep 5

D	Fragments  #1	1976-124 C-U    17 pieces, all have decayed		For orbital information see extra pages at the end of the year

#	Cosmos 885 disintegrated during Mar-Apr 1977

#1	These fragments are calibrating targets.

D	KH 11-1 (OPS 5705)*	1976-125 A	1976 Dec 19.77	Cylinder	15 long	1976 Dec 19.93	96.95	92.30	6765	242	532	0.021	170

[Titan 3D 23D-15]	[09627]	770 days	13300? full	3.0 dia	1976 Dec 22.8	96.95	92.37	6768	247	533	0.021	159

VDB-SLC4E	1979 Jan 28			1976 Dec 23.8	96.94	93.37	6816	341	535	0.014	149

1977 Mar 27.5	96.93	92.51	6775	264	530	0.020	164

1978 Jun 3.49	97.07	91.88	6745	357	376	0.001	4

1978 Jun 6.18	96.95	92.30	6766	357	417	0.004	355

1979 Jan 28.57	96.91	91.63	6733	346	363	0.001	238

D	Titan 3D	1976-125 B	1976 Dec 19.77	Cylinder	6 long	1976 Dec 20.00	96.93	92.20	6761	245	519	0.020	170

2nd stage	[09628]	141 days	1900	3.0 dia	1977 Jan 1.0	96.94	91.56	6728	254	445	0.014	-

1977 May 9			1977 May 8.87	96.88	87.62	6535	150	163	0.001	315

D	Fragment ##	1976-125 C	[09629]	1977 Feb 23	66 days	1976 Dec 20.19	96.94	92.47	6774	236	555	0.024	169

1976 Dec 21.1	96.93	92.26	6763	248	521	0.020	165

1976 Dec 24.15	96.98	91.50	6727	252	443	0.014	147

D	Fragment ##	1976-125 D	[09630]	1977 Feb 9	52 days	1976 Dec 21.2	97.01	92.46	6773	256	533	0.021	161

1976 Dec 26.69	96.87	91.43	6724	239	451	0.016	143

*	KH-11-1 manoeuvred on 1976 Dec 23; 1977 Mar 25 and during 1978 June

##	Possible a capsule?

Cosmos 886**	1976-126 A	1976 Dec 27.53	Cylinder?	4 long?	1976 Dec 27.6	65.85	102.96	7276	531	1265	0.050	81

[Tsyklon 2]	[09634]	disintegrated		2 dia?	1976 Dec 27.8	65.84	114.79	7823	594	2295	0.109	57

BAI-LC90				1977 Jan 7.73	65.83	114.93	7831	595	2310	0.109	53

2004 Jul 6.75	65.84	114.67	7819	583	2297	0.110	287

D	Cosmos 886	1976-126 D	1976 Dec 27.53	Cylinder	8 long?	1976 Dec 30.51	62.78	95.88	6940	140	983	0.061	53

2nd stage	[09645]	18 days	1500?	2.5 dia?	1977 Jan 13.55	62.78	95.88	6940	140	983	0.061	53

1977 Jan 14

Fragments	1976-126 B, C, E-CG	  77 pieces, 15 have decayed

**	Cosmos 886 passed close to Cosmos 880 on 1976 Dec 27.6 and exploded. Cosmos 880 was also destroyed.

D	Molniya-3 6	1976-127 A	1976 Dec 28.28	Windmill +	4.2 long?	1976 Dec 29.35	62.79	735.77	26998	613	40625	0.741	288

[Molniya 8K78M]	[09635]	4829 days	6 vanes	1.6 dia	1977 Jan 3.9	62.81	716.97	26537	544	39773	0.739	288

PLE-LC43/4	1990 Mar 19	1500?		1977 Jan 14.40	62.79	717.77	26555	608	39745	0.737	288

1990 Feb 5.95	62.36	496.55	20772	90	28696	0.689	255

D	Molniya-3 6	1976-127 B	1976 Dec 28.28	Irregular	-	1976 Dec 28.78	62.83	92.62	6782	215	591	0.028	120

Block I 3rd stage 	[09636]	78 days			1977 Jan 3.9	62.83	92.44	6773	217	573	0.026	121

1977 Mar 16			1977 mar 15.40	62.81	88.13	6561	167	197	0.002	119

D	Molniya-3 6	1976-127 C	1976 Dec 28.28	Cylinder	7.5 long	1976 Dec 28.71	62.85	92.70	6785	192	621	0.032	117

4th stage casing 	[09641]	49 days	2500?	2.6 dia	1977 Jan 4.9	62.84	92.30	6766	192	584	0.029	118

1977 Feb 15			1977 Feb 14.77	62.83	88.30	6569	159	221	0.005	118

D	Molniya-3 6	1976-127 D	1976 Dec 28.8			1977 Jan 1.91	62.83	92.68	6785	215	598	0.028	121

Ullage motor	[09642]	57 days			1977 Feb 14.66	62.81	89.85	6646	193	341	0.011	121

1977 Feb 23

D	Molniya-3 6	1976-127 E	1976 Dec 28.28	Cylinder	2.0 long	1977 Jan 3.4	62.90	732.48	26918	613	40466	0.740	288

Block L 4th stage 	[09647]	39.8 days	440	2.0 dia	1987 Sep 23.70	63.98	458.83	19706	85	26569	0.572	242				1987 Sep 30

Cosmos 887	1976-128 A	1976 Dec 28.32	Cylinder	2.1 long	1976 Dec 28.89	82.74	104.77	7362	951	1016	0.004	295

[Kosmos 11K65M	[09637]	1200 years	810	2.0 dia	1977 Jan 5.0	82.94	104.84	7364	954	1018	0.004	277

65072-415]	PLE-LC132				2004 Jul 6.04	82.94	104.65	7357	945	1011	0.005	332

2021 Dec 3.49	82.94	104.62	7355	944	1009	0.004	196

Cosmos 887	1976-128 B	1976 Dec 28.32	Cylinder	7.4 long	1977 Jan 1.1	82.94	104.72	7359	953	1008	0.004	286

2nd stage	[09638]	600 years	2200?	2.4 dia	2004 Jul 7.50	82.94	104.50	7350	949	993	0.003	237

2021 Dec 3.51	82.94	104.47	7348	946	994	0.003	51

Fragment	1976-128 C	[27881]			2003 Sep 6.32	82.94	104.48	7349	935	1006	0.005	92

2004 Jul 5.63	82.94	104.47	7348	937	1001	0.004	325

2021 Dec 3.60	82.94	104.07	7329	917	984	0.005	42

Text in box is from "History of on-orbit satellite fragmentations", 13th edition, May 2004.

Orbital Debris Program Office, Johnson Space Centre, NASA, Houston, TX 77058.

Cosmos 787 fragments; 8 pieces, all have decayed.

D	1976-01 C	[08549]	1977 Oct 20	653 days		1976 Jan 6.79	74.05	95.00	6897	493	543	0.004	348

1977 Oct 15.48	74.05	92.77	6788	393	426	0.002	241

D	1976-01 D	[08550]	1977 Mar 24	443 days		1976 Jan 23.05	74.05	94.87	6891	488	536	0.003	209

1977 Mar 21.54	74.02	90.23	6665	286	286	0	349

D	1976-01 E	[09731]	1978 Jul 15	921 days		1977 Jan 12.66	73.97	94.48	6872	473	515	0.003	241

1977 Oct 27.09	73.95	93.10	6805	415	437	0.002	273

D	1976-01 F	[09790]	1977 Aug 5	577 days		1977 Feb 1.45	74.07	93.63	6831	428	475	0.004	173

1977 Jul 22.86	74.04	91.95	6749	360	380	0.002	165

D	1976-01 G	[09791]	1977 Dec 1	695 days		1977 Jan 31.63	74.08	94.27	6861	458	507	0.004	197

1977 Oct 19.18	74.07	92.55	6778	390	408	0.001	228

D	1976-01 H	[09792]	1977 Dec 12	706 days		1977 Jan 31.01	74.01	94.35	6866	464	510	0.003	214

1977 Nov 14.87	73.98	92.03	6753	365	382	0.001	247

D	1976-01 J	[09837]	1977 Aug 27	599 days		1977 Feb 17.25	73.99	93.52	6826	424	469	0.003	147

1977 Jun 23.39	73.96	92.32	6766	372	404	0.002	184

D	1976-01 K	[09838]	1977 Jul 30	571 days		1977 Feb 16.27	74.01	93.43	6821	420	465	0.003	143

1977 Jul 15.57	74.00	90.92	6698	315	324	0.0007	152

Cosmos 788 fragments; 3 pieces, all have decayed.

D	1975-02 C	[08553]	1976 Jan 12	5 days		1976 Jan 8.20	62.80	89.45	6626	180	315	0.010	73

1976 Jan 11.60	62.85	88.93	6600	174	269	0.007	73

D	1975-02 E	[08589]	1976 Jan 23	16 days		1976 Jan 20.05	62.80	89.58	6632	162	345	0.014	72

1976 Jan 22.08	62.81	88.32	6570	152	230	0.006	71

D	1975-02 F	[08590]	1976 Jan 20	13 days			62.80	89.50		181	321	from Satcat

CTS-1 fragments; 3 pieces, all in orbit

1976-04 C	[08587]	1976 Apr 4	97 days		1976 Jan 19.56	28.64	92.23	6762	178	590	0.030	184

1976 Jan 23.70	28.66	91.50	6726	176	520	0.026	232

1976-04 E	[39688]				2014 Apr 24.54	12.54	1436.20	42167	35627	35950	0.004	81

2021 Dec 5.87	7.45	1436.02	42163	35684	35885	0.002	164

1976-04 F	[39689]				2013 Sep 26.94	12.77	1436.65	42176	35237	36357	0.013	284

2021 Dec 4.93	7.49	1436.70	42177	35100	36496	0.017

C is Delta 1 fragment; E and F are array covers.

Cosmos 801 fragments; 15 pieces, all have decayed.

Analyses indicate that the Cosmos 2 2nd stage is the most likely debris source.

D	1976-12 C	[08660]	1977 Apr 14	434 days		1976 Feb 7.86	71.31	96.13	6952	312	834	0.038	70

1977 Apr 11.70	71.27	89.35	6621	227	257	0.002	318

D	1976-12 D	[08661]	1976 Jul 28	174 days		1976 Feb 6.28	70.88	94.28	6863	233	735	0.037	95

1976 Feb 22.16	70.51	94.02	6849	187	755	0.041	65

D	1976-12 E	[08662]	1976 Oct 11	249 days		1976 Feb 6.85	70.67	95.10	6902	295	750	0.033	80

1976 Feb 24.08	70.70	94.15	6856	293	662	0.027	51

D	1976-12 F	[08663]	1976 Apr 5	60 days		1976 Feb 6.32	70.69	94.63	6879	264	736	0.034	90

1976 Feb 17.78	70.59	93.82	6840	259	664	0.030	71

D	1976-12 G	[08664]	1976 Oct 11	249 days		1976 Feb 6.72	70.63	95.00	6897	292	745	0.033	81

1976 Feb 13.24	70.63	94.67	6881	290	715	0.031	71

D	1976-12 H	[08665]	1976 Aug 17	194 days		1976 Feb 7.24	70.82	94.45	6871	238	746	0.037	91

1976 Aug 16.91	70.79	86.43	6476	98	98	0	164

D	1976-12 J	[08666]	1976 Jun 14	130 days		1976 Feb 8.42	70.84	94.53	6874	248	744	0.036	88

1976 Jun 13.03	70.80	88.57	6582	183	223	0.003	215

D	1976-12 K	[08667]	1976 Mar 18	42 days		1976 Feb 7.50	70.87	94.27	6862	233	733	0.036	93

1976 Mar 2.60	70.75	91.23	6714	117	553	0.033	6

D	1976-12 L	[08668] 	1976 Oct 11	249 days		1976 Feb 7.31	70.85	94.75	6885	248	765	0.037	88

1976 Mar 20.45	70.84	93.73	6835	235	679	0.032	17

D	1976-12 M	[08669] 	1976 Oct 11	249 days		1976 Feb 7.42	70.78	93.97	6847	254	683	0.031	93

1976 Mar 30.97	70.78	92.23	6763	241	527	0.021	358

D	1976-12 N	[08670] 	1976 Oct 11	249 days		1976 Feb 7.24	70.72	94.50	6873	268	720	0.033	93

D	1976-12 P	[08671] 	1976 Jul 28	174 days		1976 Feb 8.79	70.81	93.65	6832	232	674	0.032	95

D	1976-12 Q	[08672] 	1976 Oct 11	249 days		1976 Feb 8.27	70.85	94.33	6865	224	748	0.038	101

D	1976-12 R	[08673]	1976 Sep 25	233 days		1976 Feb 8.27	70.97	93.53	6826	226	668	0.032	94

D	1976-12 S	[08674]	1976 Jun 21	137 days		1976 Feb 8.80	70.87	93.70	6834	256	856	0.029	95

1976 Jun 17.90	70.67	88.83	6595	196	237	0.003	218

Cosmos 816 fragments; 23 pieces, all have decayed.

Analyses indicate that the Cosmos 816 payload is the most likely debris source.

D	1976-37 C	[08885]	1977 Jul 12	440 days		1976 Jun 12.67	65.83	94.53	6874	475	517	0.003	336

1977 Jul 2.74	65.81	90.93	6699	319	321	0.0001	198

D	1976-37 D	[08886]	1977 Jul 26	454 days		1976 Jun 14.84	65.83	94.55	6875	476	518	0.003	336

1977 Jul 15.15	65.80	90.68	6686	302	313	0.0008	220

D	1976-37 E	[09396]	1977 Jun 12	410 days		1976 Sep 1.36	65.83	94.37	6867	464	512	0.003	279

1977 Jun 11.63	65.81	89.45	6626	247	247	0	187

D	1976-37 F	[09397]	1977 Sep 17	507 days		1976 Sep 1.32	65.82	94.68	6882	474	532	0.004	310

1977 Sep 9.54	65.79	90.82	6693	309	321	0.0009	281

D	1976-37 G	[09428]	1977 Aug 9	468 days		1976 Sep 20.54	65.76	94.62	6870	464	519	0.004	295

1977 Jul 28.50	65.74	90.80	6692	313	314	0.00004	226

D	1976-37 H	[09429]	1977 Aug 10	469 days		1976 Sep 21.07	65.84	94.50	6873	469	520	0.004	290

1977 Aug 6.83	65.80	89.78	6642	261	266	0.0004	306

D	1976-37 J	[09430]	1977 Aug 29	488 days		1976 Sep 20.55	65.82	94.53	6874	470	522	0.004	288

1977 Jul 29.88	65.82	92.32	6767	382	395	0.0009	198

D	1976-37 K	[09431]	1977 Aug 24	483 days		1976 Sep 21.01	65.90	94.58	6877	474	523	0.004	281

1977 Aug 20.24	65.90	89.33	6620	231	251	0.001	304

D	1976-37 L	[09432]	1977 Sep 20	510 days		1976 Sep 21.01	65.85	94.57	6876	470	526	0.004	287

1977 Sep 7.57	65.81	91.13	6709	325	335	0.0008	291

D	1976-37 M	[09438]	1977 Aug 19	478 days		1976 Sep 25.53	65.81	94.47	6871	468	517	0.004	280

1977 Aug 12.39	65.79	90.53	6680	291	311	0.001	289

D	1976-37 N	[09475]	1977 Sep 2	492 days		1976 Oct 10.96	65.76	94.48	6872	466	521	0.004	277

1977 Aug 22.95	65.75	90.92	6698	310	329	0.001	315

D	1976-37 P	[09476]	1977 Sep 16	506 days		1976 Oct 10.97	65.87	94.55	6876	472	522	0.004	281

1977 sep 9.02	65.86	90.68	6687	301	316	0.001	320

D	1976-37 Q	[09485]	1977 Oct 28	544 days		1976 Oct 17.20	65.80	94.50	6873	468	520	0.004	274

1977 Oct 9.47	65.81	91.73	6738	359	359	0	197

D	1976-37 R	[09487]	1977 Sep 7	497 days		1976 Oct 13.99	65.86	94.53	6874	472	520	0.003	279

1977 Aug 31.57	65.83	90.53	6679	290	311	0.002	206

D	1976-37 S	[09488]	1977 Sep 27	517 days		1976 Oct 13.99	65.80	94.52	6874	471	519	0.004	278

1977 Sep 3.59	65.79	91.37	6720	339	345	0.0004	324

D	1976-37 T	[09489]	1977 Sep 24	514 days		1976 Oct 16.94	65.84	94.55	6875	471	521	0.004	277

1977 Sep 19.86	65.83	90.67	6686	299	316	0.001	214

D	1976-37 U	[09490]	1977 Sep 15	505 days		1976 Oct 16.94	65.81	94.50	6873	470	518	0.004	273

1977 Sep 8.57	65.79	90.60	6683	299	309	0.0007	279

D	1976-37 V	[09507]	1977 Aug 1	460 days		1976 Oct 28.68	65.86	94.28	6862	461	507	0.003	259

1977 Jul 22.96	65.83	90.75	6690	311	311	0	317

D	1976-37 W	[09508]	1977 Sep 17	507 days		1976 Oct 28.71	65.81	94.47	6872	467	519	0.004	277

1977 Sep 10.73	65.77	90.43	6674	285	306	0.002	240

D	1976-37 X	[09511]	1977 Oct 12	532 days		1976 Oct 31.13	65.81	94.62	6878	473	526	0.004	280

1977 Sep 8.51	65.78	92.53	6777	398	399	0.00006	233

D	1976-37 Y	[09512]	1977 Sep 3	493 days		1976 Oct 31.64	65.85	94.40	6868	463	515	0.004	257

1977 Aug 19.90	65.83	91.35	6719	338	343	0.0004	252

D	1976-37 Z	[09513]	1977 Sep 17	507 days		1976 Oct 31.64	65.82	94.43	6869	465	516	0.004	261

1977 Sep 10.91	65.77	90.75	6690	309	314	0.0004	304

D	1976-37 AA	[09514]	1977 Oct 17	537 days		1976 Nov 1.25	65.84	94.57	6876	471	523	0.004	275

1977 Sep 19.61	65.79	92.13	6758	376	382	0.0004	214

Salyut 5 fragments; 8 pieces, all have decayed. Some fragments appeared during the mission.

Analyses indicate that the Salyut 5 payload and the Proton 3rd stage are the most likely debris sources.

D	1976-57 C	[08913]	1976 Jun 24	2 days		1976 Jun 23.05	51.58	89.08	6607	213	244	0.002	98

1976 Jun 24.04	51.59	88.47	6577	193	204	0.0008	103

D	1976-57 D	[09059]	1976 Aug 13	52 days		1976 Jul 29.50	51.60	89.72	6639	257	264	0.0005	318

1976 Aug 7.62	51.58	88.97	6602	220	226	0.0004	279

D	1976-57 E	[09060] 	1976 Aug 13	52 days		1976 Jul 29.44	51.59	89.77	6641	258	269	0.0007	335

1976 Aug 9.59	51.59	88.47	6577	199	199	0	67

D	1976-57 F	[09275]	1976 Aug 17	56 days		1976 Aug 9.57	51.61	89.28	6618	239	239	0	64

1976 Aug 14.15	51.59	88.75	6592	213	213	0	92

D	1976-57 G	[09276]	1976 Sep 5	75 days		1976 Aug 11.58	51.58	89.55	6631	249	256	0.0005	40

1976 Sep 2.11	51.58	88.40	6574	196	196	0	195

D	1976-57 H	[09277] 	1976 Sep 5	75 days		1976 Aug 10.02	51.60	89.60	6634	252	258	0.0005	32

1976 Sep 3.83	51.55	88.05	6556	178	178	0	204

D	1976-57 J	[09385]	1976 Sep 13	83 days		1976 Aug 18.44	51.61	89.57	6632	249	257	0.0006	19

1976 Sep 10.99	51.59	87.62	6535	157	157	0	117

D	1976-57 K	[09386]	1976 Aug 22	61 days		1976 Aug 17.42	51.61	89.13	6610	231	231	0	107

Cosmos 838 fragments; 39 pieces, all have decayed.

Cosmos 838 was the third spacecraft of the Cosmos 699-type to experience a fragmentation on 1977 May 17 at 10:18 UT near 9ºS 284ºE . Spacecraft had been in a regime of natural decay for six months prior to the event. Much debris re-entered before being officially catalogued.

D	1976-63 C	[10047]	1977 Sep 13	438 days		1977 Jun 11.73	64.95	94.47	6871	410	575	0.012	208

1977 Jul 1.83	64.96	94.05	6851	396	549	0.011	198

D	1976-63 D	[10048]	1977 Aug 14	408 days		1977 Jun 12.06	64.92	95.83	6937	420	698	0.020	194

1977 Jul 28.67	64.92	93.32	6815	380	493	0.008	180

D	1976-63 E	[10049]	1978 Apr 10	647 days		1977 Jun 12.10	64.59	94.88	6891	427	598	0.012	160

1978 Mar 26.72	64.58	91.72	6737	327	390	0.005	35

D	1976-63 F	[10050]	1977 Jul 23	386 days		1977 Jun 12.07	65.08	94.30	6863	402	568	0.012	214

1977 Jul 15.35	65.10	92.60	6781	359	445	0.006	207

D	1976-63 G	[10051]	1977 Nov 1	487 days		1977 Jun 12.08	65.05	94.52	6874	410	580	0.012	218

1977 Oct 23.57	65.03	91.53	6728	350	350	0	33

D	1976-63 H	[10052]	1978 Mar 25	631 days		1977 Jun 12.11	64.58	94.43	6869	431	550	0.009	174

1978 Feb 22.66	64.56	92.60	6781	384	420	0.003	73

D	1976-63 J	[10053]	1977 Nov 15	501 days		1977 Jun 12.08	64.96	93.35	6817	427	450	0.002	198

1977 Oct 26.43	64.95	91.53	6728	344	356	0.0009	332

D	1976-63 K	[10054]	1978 Aug 8	767 days		1977 Jun 15.20	65.02	93.40	6819	425	456	0.002	234

1978 Aug 3.13	65.00	89.02	6604	212	238	0.002	257

D	1976-63 L	[10055]	1977 dec 2	518 days		1977 Jun 12.11	64.98	93.93	6845	424	509	0.006	151

1977 Nov 11.84	64.99	91.68	6736	351	364	0.001	124

D	1976-63 M	[10056]	1977 Nov 3	489 days		1977 Jun 11.72	64.72	93.68	6833	421	488	0.005	149

1977 Oct 26.80	64.69	91.43	6723	343	346	0.0002	99

D	1976-63 N	[10057]	1978 Apr 15	652 days		1977 Jun 12.07	65.06	93.10	6805	411	441	0.002	283

1978 Apr 14.10	65.03	88.88	6598	213	225	0.0009	266

D	1976-63 P	[10058]	1977 Sep 20	445 days		1977 Jun 12.10	64.98	93.60	6829	419	481	0.005	206

1977 Sep 8.13	65.03	90.98	6701	315	330	0.001	213

D	1976-63 Q	[10076]	1978 Feb 13	591 days		1977 Jun 19.59	64.89	93.87	6842	430	497	0.005	176

1978 Jan 4.57	64.85	91.63	6733	345	365	0.001	50

D	1976-63 R	[10077]	1978 Mar 12	618 days		1977 Jun 19.56	64.73	93.57	6847	423	512	0.006	147

1978 Jan 2.59	64.71	92.05	6754	356	394	0.003	42

D	1976-63 S	[10078]	1977 Nov 16	502 days		1977 Jun 19.55	64.68	93.35	6817	407	470	0.005	111

1977 Nov 5.28	64.67	90.83	6694	316	316	0	98

D	1976-63 T	[10079]	1977 Oct 3	458 days		1977 Jun 21.59	64.70	93.85	6841	399	527	0.009	128

1977 Sep 20.03	64.69	91.67	6735	345	367	0.002	99

D	1976-63 U	[10080]	1978 Sep 19	809 days		1977 Jun 21.57	65.04	93.87	6843	424	504	0.006	189

1978 Sep 12.59	64.97	89.32	6620	234	248	0.001	236

D	1976-63 V	[10081]	1978 Apr 18	655 days		1977 Jun 20.99	64.98	93.50	6825	417	475	0.004	210

1977 Sep 4.65	64.92	92.10	6756	362	393	0.002	195

D	1976-63 W	[10082]	1977 Sep 23	448 days		1977 Jun 19.15	64.56	94.37	6867	414	562	0.011	151

1977 Sep 12.54	64.49	92.12	6757	328	428	0.007	158

D	1976-63 X	[10083]	1977 Jul 27	390 days		1977 Jun 19.58	64.55	93.93	6845	410	524	0.008	155

1977 Jun 24.93	64.56	93.73	6835	406	508	0.007	154

D	1976-63 Y	[10097]	1978 Mar 3	609 days		1977 Aug 11.29	65.05	92.93	6797	402	435	0.002	273

1977 Dec 12.82	65.05	91.88	6745	357	376	0.001	252

D	1976-63 Z	[10098]	1977 Jul 23	386 days		1977 Jun 26.93	65.05	92.72	6786	393	422	0.002	259

1977 Jul 2.86	65.06	92.62	6781	385	420	0.003	268

D	1976-63 AA	[10099]	1977 Sep 5	430 days		1977 Jun 26.88	65.06	92.80	6791	397	426	0.002	274

1977 Aug 24.78	65.04	91.97	6750	361	381	0.002	257

D	1976-63 AB	[10100]	1977 Oct 29	484 days		1977 Jun 26.87	64.98	93.03	6801	412	434	0.002	214

1977 Oct 11.88	65.05	91.25	6715	329	343	0.001	305

D	1976-63 AC	[10101]	1977 Sep 20	445 days		1977 Jun 25.89	64.99	92.87	6793	404	426	0.002	244

1977 Jul 5.38	64.97	90.52	6678	281	318	0.003	247

D	1976-63 AD	[10102]	1977 Oct 25	480 days		1977 Jun 26.52	65.00	93.22	6810	413	451	0.003	234

1977 Oct 18.51	64.98	90.58	6681	297	308	0.0008	304

D	1976-63 AE	[10103]	1978 Jul 3	731 days		1977 Jun 29.89	65.06	93.17	6808	414	444	0.002	273

1978 May 19.66	65.04	91.43	6723	338	351	0.001	262

D	1976-63 AF	[10104]	1978 Jul 19	717 days		1977 Jul 6.80	65.08	93.13	6807	412	445	0.002	320

1978 May 30.87	65.05	90.37	6671	280	305	0.002	268

D	1976-63 AG	[10105]	1977 Aug 17	411 days		1977 Jun 26.88	65.01	92.92	6796	409	426	0.001	251

1977 Jul 26.18	65.22	92.50	6776	389	405	0.001	264

D	1976-63 AH	[10106]	1978 Apr 18	655 days		1977 Jun 26.52	64.99	93.12	6805	410	443	0.002	222

1978 Jan 8.80	65.06	92.68	6785	390	421	0.002	292

D	1976-63 AJ	[10107]	1977 Sep 3	428 days		1977 Jun 26.55	65.22	93.30	6815	410	462	0.004	174

1977 Aug 11.56	65.22	92.05	6753	368	381	0.001	169

D	1976-63 AK	[10108]	1977 Aug 27	421 days		1977 Jun 26.57	65.05	92.90	6795	405	428	0.002	240

1977 Aug 19.89	65.03	90.95	6700	311	331	0.001	248

D	1976-63 AL	[10109]	1977 Sep 22	447 days		1977 Jun 26.90	65.01	92.85	6792	404	423	0.001	264

1977 Sep 18.57	64.97	89.27	6617	226	251	0.002	284

D	1976-63 AM	[10110]	1978 Sep 3	793 days		1977 Jun 26.59	65.03	92.93	6797	402	435	0.002	276

1978 Jun 17.65	65.16	91.68	6735	348	364	0.001	319

D	1976-63 AN	[10122]	1977 Nov 9	495 days		1977 Jun 30.98	65.05	92.93	6796	403	432	0.002	277

1977 Oct 22.53	65.02	91.17	6711	324	340	0.001	314

D	1976-63 AP	[10123]	1977 Aug 18	412 days		1977 Jul 1.01	65.01	93.13	6806	405	450	0.003	231

1977 Jul 9.35	65.02	93.00	6800	401	442	0.003	230

D	1976-63 AQ	[10124]	1977 Aug 17	411 days		1977 Jun 30.97	64.95	92.75	6788	399	420	0.002	221

1977 Jul 29.50	64.95	91.83	6743	360	368	0.0006	315

D	1976-63 AR	[10125]	1977 Jul 28	391 days		1977 Jun 30.00	64.93	94.03	6850	399	545	0.011	201

1977 Jul 20.24	64.89	92.42	6772	360	427	0.005	219

D	1976-63 AS	[10126]	1978 Jan 12	559 days		1977 Jun 1.97	64.62	94.32	6864	430	540	0.008	163

1977 Dec 14.43	64.66	92.62	6781	383	422	0.003	113

Cosmos 839 2nd stage fragments; 70 pieces, 2 have decayed

Cosmos 839 was the first of three satellites of the same class to experience unexplained fragmentations. These satellites are used in conjunction with the Cosmos 249-type spacecraft which are deliberately fragmented; but the cause of the Cosmos 839-type events appears to be unrelated since they occur more than one year after tests with Cosmos 249-type spacecraft. In the case of Cosmos 839, 14 months elapsed between its test with a Cosmos 249-type spacecraft and its fragmentation on 1977 Sep 29 at 07:17 UT near 33ºS 162ºE. Russian officials have determined that battery malfunctions were the causes of these events.

1976-67 C	[09016]				1976 Jul 13.41	65.87	116.88	7919	985	2097	0.070	164

2004 Jul 4.64	65.87	116.83	7917	986	2090	0.070	143

2021 Dec 7.56	65.87	116.82	7916	982	2093	0.070	182

1976-67 D	[10410]				1977 Oct 17.02	66.09	116.82	7917	991	2085	0.069	344

2004 Jul 5.23	66.09	116.80	7915	994	2079	0.069	167

2021 Dec 7.76	66.09	116.78	7915	991	2081	0.069	346

1976-67 E	[10411]				1977 Oct 16.35	66.03	117.23	7935	1028	2085	0.067	344

2004 Jul 5.33	66.02	117.17	7932	1024	2083	0.067	304

2021 Dec 7.71	66.02	117.15	7931	1025	2081	0.067	215

1976-67 F	[10412]				1977 Sep 30.96	65.68	116.73	7913	988	2080	0.069	352

2004 Jul 5.87	65.67	116.72	7911	995	2071	0.068	58

2021 Dec 7.67	65.68	116.70	7911	982	2083	0.070	279

1976-67 G	[10413]				1977 Oct 17.30	65.88	117.55	7949	1015	2126	0.070	340

2004 Jul 6.29	65.88	117.22	7934	1014	2097	0.068	169

2021 Dec 7.62	65.87	117.12	7930	1008	2094	0.068	217

1976-67 H	[10414]				1977 Oct 17.31	65.88	118.20	7979	1096	2105	0.063	340

2004 Jul 5.06	65.88	118.18	7978	1094	2105	0.063	231

2021 Dec 7.83	65.88	118.18	7978	1095	2103	0.063	329

1976-67 J	[10415]				1977 Sep 30.98	65.83	118.17	7977	1051	2147	0.069	343

2004 Jul 5.76	65.85	118.15	7976	1047	2148	0.069	279

2021 Dec 7.84	65.83	118.13	7976	1058	2137	0.066	53

1976-67 K	[10416]				1977 Sep 30.97	65.72	118.02	7970	1069	2114	0.066	346

2004 Jul 6.29	65.72	118.00	7969	1077	2104	0.064	90

2021 Dec 7.90	65.72	117.98	7969	1067	2113	0.066	333

1976-67 L	[10417]				1977 Oct 16.70	65.58	115.78	7869	902	2078	0.075	348

2004 Jul 5.64	65.69	115.53	7858	906	2053	0.073	129

2021 Dec 7.93	65.98	115.48	7856	903	2051	0.073	26

1976-67 M	[10436]				1977 Oct 31.92	66.03	116.72	7912	976	2090	0.070	338

2004 Jul 5.29	66.04	116.40	7898	968	2070	0.070	235

2021 Dec 7.43	66.03	116.33	7894	976	2055	0.068	95

1976-67 N	[10437]				1977 Oct 25.68	65.83	117.42	7943	1020	2110	0.069	338

2004 Jul 4.73	65.83	117.08	7928	1008	2091	0.068	242

2021 Dec 7.48	65.82	117.00	7924	1011	2080	0.067	52

1976-67 P	[10438]				1977 Oct 26.30	65.95	119.47	8035	1123	2191	0.066	327

2004 Jul 5.46	65.95	119.15	8022	1112	2174	0.066	214

2021 Dec 7.49	65.94	119.08	8018	1111	2168	0.066	300

1976-67 Q	[10439]				1977 Oct 26.31	65.79	117.70	7956	1044	2111	0.067	338

2004 Jul 5.41	65.79	117.60	7861	1040	2105	0.067	320

2021 Dec 7.70	65.79	117.57	7950	1049	2094	0.066	117

1976-67 R	[10440]				1977 Oct 25.66	65.64	116.63	7908	942	2118	0.074	340

2004 Jul 4.55	65.64	116.20	7888	946	2073	0.071	90

2021 Dec 7.70	65.65	116.13	7885	935	2079	0.073	314

1976-67 S	[10441]				1977 Sep 30.99	65.73	118.93	8011	1138	2127	0.062	343

2004 Jul 4.63	65.73	118.85	8008	1143	2115	0.061	126

2021 Dec 7.66	65.74	118.82	8006	1140	2115	0.061	30

1976-67 T	[10442]				1977 Oct 26.30	66.01	118.38	7987	1082	2134	0.066	333

2004 Jul 5.68	66.01	118.35	7986	1088	2126	0.065	48

2021 Dec 7.86	66.01	118.35	7985	1086	2127	0.065	31

1976-67 U	[10443]				1977 Sep 30.94	65.81	115.93	7876	911	2084	0.074	353

2004 Jul 5.43	65.81	115.57	7860	911	2052	0.073	144

2021 Dec 7.83	65.81	115.48	7856	906	2048	0.073	170

1976-67 V	[10444]				1977 Sep 30.94	65.80	115.37	7851	879	2065	0.076	356

2004 Jul 5.39	65.79	115.13	7840	881	2042	0.074	126

2021 Dec 7.18	65.79	115.08	7838	878	2039	0.074	147

1976-67 W	[10445]				1977 Oct 26.27	65.96	119.35	8030	1116	2187	0.067	328

2004 Jul 4.46	65.96	119.12	8020	1113	2170	0.066	180

2021 Dec 7.18	65.96	119.08	8018	1108	2171	0.066	246

1976-67 X	[10446]				1977 Oct 26.30	65.89	118.37	7986	1096	2120	0.064	335

2004 Jul 5.01	65.88	118.35	7985	1093	2120	0.064	235

2021 Dec 7.78	65.88	118.33	7985	1095	2118	0.064	338

1976-67 Y	[10447]				1977 Sep 30.95	65.86	116.58	7906	962	2092	0.071	351

2004 Jul 5.31	65.85	116.45	7900	965	2077	0.070	127

2021 Dec 7.46	65.86	116.42	7898	962	2077	0.071	153

1976-67 Z	[10448]				1977 Sep 30.95	66.16	116.58	7906	929	2126	0.076	348

2004 Jul 5.69	66.17	116.43	7899	929	2111	0.075	14

2021 Dec 7.78	66.17	116.38	7897	932	2104	0.074	95

1976-67 AA	[10449]				1977 Sep 30.94	66.01	115.68	7864	888	2083	0.076	354

2004 Jul 5.32	66.03	116.62	7862	889	2078	0.076	164

2021 Dec 7.72	66.03	115.62	7862	885	2081	0.076	332

1976-67 AB	[10450]				1977 Sep 30.94	65.74	115.55	7859	887	2073	0.075	355

2004 Jul 4.72	65.76	115.50	7857	882	2074	0.076	229

2021 Dec 7.61	65.74	115.48	7856	883	2072	0.076	322

1976-67 AC	[10451]				1977 Sep 30.94	65.85	115.63	7863	875	2094	0.078	353

2004 Jul 4.34	65.85	115.58	7861	881	2083	0.076	59

2021 Dec 7.89	65.85	115.58	7860	879	2084	0.077	41

1976-67 AD	[10452]				1977 Sep 30.99	65.84	119.52	8038	1175	2143	0.060	340

2004 Jul 4.52	65.85	119.43	8034	1175	2136	0.060	5

2021 Dec 7.67	65.85	119.40	8033	1172	2136	0.060	197

1976-67 AE	[10453]				1977 Sep 29.98	65.80	116.12	7885	931	2081	0.073	353

2004 Jul 6.33	65.81	115.95	7877	928	2069	0.072	179

2021 Dec 7.77	65.81	115.92	7875	924	2069	0.073	231

1976-67 AF	[10454]				1977 Oct 26.28	65.67	115.48	7856	880	2074	0.076	346

2004 Jul 4.52	65.66	114.92	7830	869	2034	0.074	328

2021 Dec 7.47	65.66	114.78	7824	877	2015	0.073	114

1976-67 AG	[10463]				1977 Oct 27.94	65.83	116.98	7924	989	2101	0.070	339

2004 Jul 4.70	65.83	116.87	7919	986	2094	0.070	212

2021 Dec 7.52	65.82	116.83	7917	984	2094	0.070	295

1976-67 AH	[10464]				1977 Oct 31.94	65.82	116.20	7888	924	2095	0.074	340

2004 Jul 5.59	65.83	115.68	7865	923	2050	0.072	138

2021 Dec 8.18	65.83	115.55	7859	919	2042	0.071	153

1976-67 AJ	[10465]				1977 Sep 30.94	65.56	115.40	7852	861	2086	0.078	354

2004 Jul 6.18	65.57	114.60	7816	859	2015	0.074	98

2021 Dec 7.33	65.57	114.45	7809	846	2015	0.075	324

1976-67 AK	[10466]				1977 Oct 31.98	65.83	116.07	7882	918	2089	0.074	340

2004 Jul 5.47	65.84	115.43	7854	919	2031	0.071	106

2021 Dec 8.15	65.84	115.27	7846	912	2023	0.071	96

D	1976-67 AL	[10467]	1982 Jun 3 A	2156 days			65.80	115.70		911	2067	from Satcat

1976-67 AM	[10613]				1978 Jan 26.01	65.81	115.53	7858	875	2083	0.077	309

2004 Jul 6.19	65.80	114.43	7808	876	1983	0.071	99

2021 Dec 8.02	65.80	114.18	7796	870	1966	0.070	78

1976-67 AN	[10614]				1977 Sep 30.95	65.72	116.48	7901	926	2119	0.075	349

2004 Jul 4.69	65.74	116.08	7883	916	2094	0.075	303

2021 Dec 8.03	65.73	116.00	7879	924	2076	0.073	74

1976-67 AP	[10615]				1978 Apr 18.26	66.01	116.40	7897	934	2104	0.074	269

2004 Jul 5.66	66.01	114.88	7828	915	1984	0.068	190

2021 Dec 7.46	66.00	114.48	7811	910	1954	0.067	341

1976-67 AQ	[10616]				1978 Jan 25.97	65.60	115.97	7878	907	2091	0.075	312

2004 Jul 5.87	65.60	115.57	7859	913	2049	0.072	116

2021 Dec 7.64	65.60	115.45	7854	904	2048	0.073	2

1976-67 AR	[10617]				1977 Sep 30.95	65.63	116.52	7903	937	2111	0.074	350

2004 Jul 4.90	65.63	116.48	7901	944	2100	0.073	106

2021 Dec 7.56	65.63	116.47	7900	936	2107	0.074	354

1976-67 AS	[10618]				1977 Oct 31.92	65.85	116.42	7898	940	2099	0.073	339

2004 Jul 4.67	65.84	116.28	7892	944	2082	0.072	132

2021 Dec 7.42	65.84	116.23	7890	940	2083	0.072	165

1976-67 AT	[10619]				1977 Sep 30.96	65.83	116.80	7916	1008	2066	0.067	353

2004 Jul 6.28	65.83	116.77	7914	1006	2065	0.067	200

2021 Dec 7.07	65.83	116.77	7914	1003	2068	0.067	274

1976-67 AU	[10620]				1978 Jan 25.92	65.98	117.10	7929	997	2104	0.070	302

2004 Jul 4.47	65.97	116.27	7891	989	2035	0.066	343

2021 Dec 7.73	65.95	116.03	7881	987	2018	0.065	262

1976-67 AV	[10621]				1977 Sep 30.96	66.02	117.12	7930	1017	2085	0.067	350

2004 Jul 5.41	66.03	117.00	7924	1011	2080	0.067	284

2021 Dec 8.18	66.02	116.97	7923	1015	2074	0.067	180

1976-67 AW	[10622]				1977 Oct 31.94	65.91	116.77	7914	943	2128	0.075	336

2004 Jul 4.65	65.90	116.73	7912	950	2117	0.074	69

2021 Dec 7.34	65.90	116.72	7912	950	2116	0.074	62

1976-67 AX	[10623]				1977 Sep 30.95	65.79	116.45	7900	951	2092	0.072	351

2004 Jul 5.94	65.79	116.02	7880	942	2060	0.071	223

2021 Dec 7.67	65.78	115.92	7875	942	2051	0.070	306

1976-67 AY	[12332]				1979 Dec 12.93	66.06	116.88	7919	968	2113	0.072	12

2004 Jul 5.19	66.06	116.85	7918	963	2115	0.073	213

2021 Dec 7.83	66.06	116.85	7917	972	2105	0.072	64

1976-67 AZ	[12333]				1977 Sep 30.96	65.84	116.83	7917	979	2098	0.071	350

2004 Jul 4.63	65.93	115.65	7863	908	2062	0.073	331

2021 Dec 7.55	65.93	115.63	7863	905	2064	0.074	248

1976-67 BA	[12543]				1977 Oct 25.75	66.05	117.02	7925	1006	2087	0.068	340

2004 Jul 4.87	66.05	116.12	7885	987	2025	0.066	221

2021 Dec 7.57	66.03	115.87	7873	992	1997	0.064	54

1976-67 BB	[13501]				1981 Mar 1.67	66.05	117.40	7943	1039	2090	0.066	194

2004 Jul 9.01	66.05	116.57	7905	1016	2036	0.064	251

2021 Dec 7.85	66.03	116.27	7892	1021	2005	0.062	108

1976-67 BC	[13515]				1980 Jun 19.42	65.90	116.83	7917	987	2089	0.070	320

2004 Jul 8.27	65.89	116.20	7889	993	2027	0.066	84

2021 Dec 7.54	65.90	116.02	7880	987	2015	0.065	64

1976-67 BD	[13516]				1982 Apr 6.40	65.66	116.88	7920	966	2116	0.073	119

2004 Jul 8.28	65.66	116.85	7918	967	2111	0.072	89

2021 Dec 7.21	65.66	116.83	7917	956	2121	0.074	331

1976-67 BE	[13946]				1981 Jul 9.74	66.07	116.55	7904	977	2075	0.069	129

2004 Jul 8.30	66.06	115.55	7859	963	1998	0.066	150

2021 Dec 7.19	66.07	115.20	7843	948	1980	0.066	285

1976-67 BF	[13947]				1979 Feb 26.94	65.72	117.77	7959	1045	2116	0.067	162

2004 Jul 7.98	65.72	117.65	7954	1049	2102	0.066	66

2021 Dec 7.80	65.72	117.62	7952	1035	2113	0.068	293

1976-67 BG	[14919]				1978 Jan 25.91	65.80	117.10	7929	970	2130	0.073	303

2004 Jul 6.77	65.79	117.05	7927	968	2128	0.073	249

2021 Dec 7.90	65.80	117.03	7926	973	2122	0.073	0

1976-67 BH	[15523]				1977 Oct 23.96	65.94	115.50	7857	892	2064	0.075	346

2004 Jul 8.88	65.93	115.43	7854	885	2065	0.075	292

2021 Dec 7.68	65.93	115.42	7853	888	2061	0.075	191

1976-67 BJ	[17018]				1987 Jan 1.19	66.02	116.67	7909	1005	2056	0.066	27

2004 Jun 30.39	66.04	115.93	7876	986	2009	0.065	233

2021 Dec 7.48	66.02	115.62	7862	990	1976	0.063	62

1976-67 BK	[17838]				1987 Jan 2.26	66.00	116.72	7912	1005	2061	0.067	49

2004 Jun 23.42	66.15	116.02	7880	1005	1997	0.063	298

2021 Dec 7.71	65.99	115.70	7866	985	1989	0.064	170

1976-67 BL	[18272]				1999 Jul 7.24	65.85	116.40	7897	974	2064	0.069	134

2004 Jul 8.36	65.84	116.28	7892	973	2054	0.069	140

2021 Dec 6.70	65.85	116.15	7886	965	2049	0.069	167

1976-67 BM	[18428]				1984 Dec 18.04	65.74	118.53	7994	926	2304	0.086	90

2004 Jul 8.71	65.74	117.17	7932	909	2198	0.081	11

2021 Dec 7.55	65.73	116.67	7909	905	2157	0.079	181

1976-67 BN	[18471]				1987 Aug 11.98	65.76	118.95	8013	828	2440	0.101	48

2004 Jul 8.59	65.76	118.28	7982	818	2389	0.098	320

2021 Dec 7.86	65.77	118.07	7972	822	2366	0.097	151

1976-67 BP	[18606]				1984 Dec 18.23	65.86	116.60	7906	1001	2054	0.067	51

2004 Jul 8.22	65.83	115.83	7872	989	1997	0.064	139

2021 Dec 5.87	65.83	115.52	7857	981	1977	0.063	156

D	1976-67 BQ	[18673]	1988 Sep 10	4447 days		1987 Oct 31.96	64.65	118.43	7989	663	2557	0.119	259

1988 Sep 5.75	64.49	100.23	7149	456	1084	0.044	186

1976-67 BR	[18689]				1985 Mar 7.09	65.82	124.72	8269	1116	2665	0.094	117

2004 Jul 3.60	65.82	124.63	8266	1105	2669	0.095	300

2021 Dec 7.92	65.81	124.60	8264	1109	2662	0.094	352

1976-67 BS	[19439]				1989 Sep 17.17	65.88	116.77	7914	987	2083	0.070	79

2004 Jul 7.53	65.88	116.60	7906	984	2071	0.069	121

2021 Dec 7.25	65.87	116.52	7902	979	2069	0.069	142

1976-67 BT	[20014]				1985 Jan 22.97	65.91	116.77	7914	984	2087	0.070	30

2004 Jul 9.40	65.89	115.98	7879	983	2017	0.066	83

2021 Dec 7.85	65.90	115.63	7863	968	2000	0.066	44

1976-67 BU	[20030]				2003 Jul 7.68	65.69	117.90	7965	963	2210	0.078	264

2021 Dec 7.74	65.68	117.87	7964	962	2209	0.078	53

1976-67 BV	[R20282]	Re-assigned to 1989-80 D		1989 Oct 16.69	82.79	115.42	7853	498	2451	0.124	168

1976-67 BV	[21957]				1988 Aug 18.30	65.47	114.68	7819	851	2030	0.075	78

2004 Jun 13.42	65.36	114.10	7793	818	2010	0.077	249

2021 Dec 7.42	65.46	113.90	7784	836	1975	0.073	193

1976-67 BW	[20283]				1984 Dec 19.44	65.74	116.72	7911	1001	2065	0.067	81

2004 Jul 5.11	65.79	115.88	7874	977	2014	0.066	303

2021 Dec 7.64	65.71	115.55	7859	983	1978	0.063	80

1976-67 BX	[20503]				1985 Jan 21.47	65.75	112.40	7716	576	2098	0.099	160

2004 Jul 8.80	65.74	111.18	7659	576	1985	0.092	90

2021 Dec 7.40	65.74	110.90	7646	562	1973	0.092	301

1976-67 BY	[21128]				1990 Sep 21.46	66.05	116.63	7908	975	2084	0.070	177

2004 Jul 8.27	66.05	116.25	7891	969	2056	0.069	221

2021 Dec 7.36	66.04	116.05	7881	973	2032	0.067	57

1976-67 BZ	[36300]				2010 Jan 22.64	65.65	116.70	7911	988	2077	0.069	45

2021 Dec 7.92	65.68	116.58	7906	978	2075	0.069	277

Cosmos 844 fragments; 246 pieces, all have decayed.

One of the solar panels would not unfold. Ground control activated the destruct package and the spacecraft was destroyed on 25 July.

Spacecraft was apparently destroyed 1976 Jul 25 at 17:18 UT near 49ºN 100ºE, after a malfunction prevented controlled re-entry and landing in the Soviet

Union. No elements were catalogued on any of the official debris. Most fragments re-entered rapidly.

All orbital information from Satcat

D	1976-72 C	[09064]	1976 Aug 2	11 days			67.10	90.20		171	394

D	1976-72 D	[09065]	1976 Aug 2	11 days			67.30	89.20		179	294

D	1976-72 E	[09066]	1976 Aug 2	11 days			67.20	90.10		181	374

D	1976-72 F	[09067]	1976 Aug 2	11 days			67.10	90.20		184	386

D	1976-72 G	[09068]	1976 Aug 2	11 days			67.30	89.00		153	293

D	1976-72 H	[09069]	1976 Aug 2	11 days			67.30	89.60		184	327

D	1976-72 J	[09070]	1976 Aug 2	11 days			67.30	90.10		169	388

D	1976-72 K	[09071]	1976 Aug 2	11 days			67.30	89.70		191	325

D	1976-72 L	[09072]	1976 Aug 2	11 days			67.20	89.10		135	318

D	1976-72 M	[09073]	1976 Aug 2	11 days			67.20	89.80		155	378

D	1976-72 N	[09074]	1976 Aug 2	11 days			67.10	88.60		147	268

D	1976-72 P	[09075]	1976 Aug 2	11 days			67.10	89.10		169	300

D	1976-72 Q	[09076]	1976 Aug 2	11 days			67.10	88.60		147	266

D	1976-72 R	[09077]	1976 Aug 2	11 days			67.20	89.80		184	347

D	1976-72 S	[09078]	1976 Aug 2	11 days			67.20	89.60		144	369

D	1976-72 T	[09079]	1976 Aug 2	11 days			67.20	89.60		147	365

D	1976-72 U	[09080]	1976 Aug 2	11 days			67.10	90.30		178	397

D	1976-72 V	[09081]	1976 Aug 2	11 days			67.10	90.10		186	375

D	1976-72 W	[09082]	1976 Aug 2	11 days			67.20	89.20		149	324

D	1976-72 X	[09083]	1976 Aug 2	11 days			67.30	89.00		138	307

D	1976-72 Y	[09084]	1976 Aug 2	11 days			67.20	90.10		191	383

D	1976-72 Z	[09085]	1976 Aug 2	11 days			67.10	89.40		163	330

D	1976-72 AA	[09086]	1976 Aug 2	11 days			67.10	89.40		152	338

D	1976-72 AB	[09087]	1976 Aug 2	11 days			67.20	90.00		192	360

D	1976-72 AC	[09088]	1976 Aug 2	11 days			67.30	89.60		160	350

D	1976-72 AD	[09089]	1976 Aug 2	11 days			67.30	89.60		145	289

D	1976-72 AE	[09090]	1976 Aug 2	11 days			67.00	89.60		173	338

D	1976-72 AF	[09091]	1976 Aug 2	11 days			67.40	90.10		178	383

D	1976-72 AG	[09092]	1976 Aug 2	11 days			67.10	89.10		145	319

D	1976-72 AH	[09093]	1976 Aug 2	11 days			67.20	89.70		189	335

D	1976-72 AJ	[09094]	1976 Aug 2	11 days			67.20	89.70		206	318

D	1976-72 AK	[09095]	1976 Aug 2	11 days			67.00	89.70		180	340

D	1976-72 AL	[09096]	1976 Aug 2	11 days			67.00	89.50		169	334

D	1976-72 AM	[09097]	1976 Aug 2	11 days			67.20	90.10		177	379

D	1976-72 AN	[09098]	1976 Aug 2	11 days			67.20	89.20		149	329

D	1976-72 AP	[09099]	1976 Aug 2	11 days			67.20	89.70		146	376

D	1976-72 AQ	[09100]	1976 Aug 2	11 days			67.20	90.10		176	386

D	1976-72 AR	[09101]	1976 Aug 2	11 days			67.20	89.80		152	377

D	1976-72 AS	[09102]	1976 Aug 2	11 days			67.20	89.70		161	359

D	1976-72 AT	[09103]	1976 Aug 2	11 days			67.30	89.20		186	283

D	1976-72 AU	[09104]	1976 Aug 2	11 days			67.20	89.70		173	344

D	1976-72 AV	[09105]	1976 Aug 2	11 days			67.10	89.60		187	323

D	1976-72 AW	[09106]	1976 Aug 2	11 days			67.10	89.70		166	350

D	1976-72 AX	[09107]	1976 Aug 2	11 days			67.00	89.70		183	335

D	1976-72 AY	[09108]	1976 Aug 2	11 days			67.10	90.30		187	389

D	1976-72 AZ	[09109]	1976 Aug 2	11 days			67.30	89.40		160	328

D	1976-72 BA	[09110]	1976 Aug 2	11 days			67.30	89.60		174	333

D	1976-72 BB	[09111]	1976 Aug 2	11 days			67.10	89.50		166	331

D	1976-72 BC	[09112]	1976 Aug 2	11 days			67.00	89.30		185	300

D	1976-72 BD	[09113]	1976 Aug 2	11 days			67.30	89.50		192	311

D	1976-72 BE	[09114]	1976 Aug 2	11 days			67.10	89.60		143	271

D	1976-72 BF	[09115]	1976 Aug 2	11 days			67.10	89.40		177	316

D	1976-72 BG	[09116]	1976 Aug 2	11 days			67.20	89.70		178	345

D	1976-72 BH	[09117]	1976 Aug 2	11 days			67.10	89.90		200	342

D	1976-72 BJ	[09118]	1976 Aug 2	11 days			67.20	89.20		149	319

D	1976-72 BK	[09119]	1976 Aug 2	11 days			67.30	88.80		160	271

D	1976-72 BL	[09120]	1976 Aug 2	11 days			67.10	89.80		179	347

D	1976-72 BM	[09121]	1976 Aug 2	11 days			67.00	89.20		163	307

D	1976-72 BN	[09122]	1976 Aug 2	11 days			67.10	89.80		176	353

D	1976-72 BP	[09123]	1976 Aug 2	11 days			67.20	90.20		184	380

D	1976-72 BQ	[09124]	1976 Aug 2	11 days			67.20	90.20		195	375

D	1976-72 BR	[09125]	1976 Aug 2	11 days			67.20	88.70		145	279

D	1976-72 BS	[09126]	1976 Aug 2	11 days			67.20	90.40		193	394

D	1976-72 BT	[09127]	1976 Aug 2	11 days			67.20	90.10		174	384

D	1976-72 BU	[09128]	1976 Aug 2	11 days			67.20	88.60		126	281

D	1976-72 BV	[09129]	1976 Aug 2	11 days			67.10	90.10		178	377

D	1976-72 BW	[09130]	1976 Aug 2	11 days			67.20	89.70		147	373

D	1976-72 BX	[09131]	1976 Aug 2	11 days			66.90	90.30		193	385

D	1976-72 BY	[09132]	1976 Aug 2	11 days			67.10	90.00		177	368

D	1976-72 BZ	[09133]	1976 Aug 2	11 days			67.30	89.60		167	344

D	1976-72 CA	[09134]	1976 Aug 2	11 days			67.00	89.70		145	370

D	1976-72 CB	[09135]	1976 Aug 2	11 days			67.10	89.50		183	315

D	1976-72 CC	[09136]	1976 Aug 2	11 days			67.30	88.80		166	267

D	1976-72 CD	[09137]	1976 Aug 2	11 days			67.00	89.40		140	347

D	1976-72 CE	[09138]	1976 Aug 2	11 days			67.10	88.80		165	263

D	1976-72 CF	[09139]	1976 Aug 2	11 days			67.10	88.70		142	278

D	1976-72 CG	[09140]	1976 Aug 2	11 days			67.20	89.40		182	312

D	1976-72 CH	[09141]	1976 Aug 2	11 days			67.30	90.10		162	394

D	1976-72 CJ	[09142]	1976 Aug 2	11 days			67.20	90.30		181	396

D	1976-72 CK	[09143]	1976 Aug 2	11 days			67.30	88.70		155	263

D	1976-72 CL	[09144]	1976 Aug 2	11 days			67.20	90.20		175	390

D	1976-72 CM	[09145]	1976 Aug 2	11 days			67.00	90.20		177	395

D	1976-72 CN	[09146]	1976 Aug 2	11 days			67.10	88.60		134	277

D	1976-72 CP	[09147]	1976 Aug 2	11 days			No info

D	1976-72 CQ	[09148]	1976 Aug 2	11 days			67.10	90.40		195	397

D	1976-72 CR	[09149]	1976 Aug 2	11 days			67.20	89.60		155	356

D	1976-72 CS	[09150]	1976 Aug 2	11 days			67.10	89.00		134	314

D	1976-72 CT	[09151]	1976 Aug 2	11 days			67.20	89.40		178	308

D	1976-72 CU	[09152]	1976 Aug 2	11 days			67.00	89.90		198	341

D	1976-72 CV	[09153]	1976 Aug 2	11 days			67.10	90.20		174	395

D	1976-72 CW	[09154]	1976 Aug 2	11 days			67.10	89.80		190	337

D	1976-72 CX	[09155]	1976 Aug 2	11 days			67.00	90.00		182	369

D	1976-72 CY	[09156]	1976 Aug 2	11 days			67.10	89.70		174	345

D	1976-72 CZ	[09157]	1976 Aug 2	11 days			67.20	90.00		188	366

D	1976-72 DA	[09158]	1976 Aug 2	11 days			67.00	88.40		134	256

D	1976-72 DB	[09159]	1976 Aug 2	11 days			67.10	88.90		124	313

D	1976-72 DC	[09160]	1976 Aug 2	11 days			67.10	88.90		149	293

D	1976-72 DD	[09161]	1976 Aug 2	11 days			67.10	89.40		144	350

D	1976-72 DE	[09162]	1976 Aug 2	11 days			67.30	89.80		158	367

D	1976-72 DF	[09163]	1976 Aug 2	11 days			67.00	89.80		175	354

D	1976-72 DG	[09164]	1976 Aug 2	11 days			67.20	89.50		160	337

D	1976-72 DH	[09165]	1976 Aug 2	11 days			67.10	89.90		168	373

D	1976-72 DJ	[09166]	1976 Aug 2	11 days			67.30	90.00		152	394

D	1976-72 DK	[09167]	1976 Aug 2	11 days			67.20	89.40		177	309

D	1976-72 DL	[09168]	1976 Aug 2	11 days			67.10	89.90		192	347

D	1976-72 DM	[09169]	1976 Aug 2	11 days			67.00	89.30		150	326

D	1976-72 DN	[09170]	1976 Aug 2	11 days			67.00	89.20		141	328

D	1976-72 DP	[09171]	1976 Aug 2	11 days			67.00	89.70		173	345

D	1976-72 DQ	[09172]	1976 Aug 2	11 days			67.30	90.00		175	371

D	1976-72 DR	[09173]	1976 Aug 2	11 days			67.20	90.20		175	392

D	1976-72 DS	[09174]	1976 Aug 2	11 days			67.10	88.60		124	288

D	1976-72 DT	[09175]	1976 Aug 2	11 days			67.10	89.30		184	292

D	1976-72 DU	[09176]	1976 Aug 2	11 days			67.10	89.50		185	318

D	1976-72 DV	[09177]	1976 Aug 2	11 days			67.00	89.30		149	330

D	1976-72 DW	[09178]	1976 Aug 2	11 days			67.20	89.00		124	323

D	1976-72 DX	[09179]	1976 Aug 2	11 days			67.10	90.00		182	370

D	1976-72 DY	[09180]	1976 Aug 2	11 days			67.20	88.60		123	287

D	1976-72 DZ	[09181]	1976 Aug 2	11 days			67.10	89.70		167	354

D	1976-72 EA	[09182]	1976 Aug 2	11 days			67.10	88.70		131	283

D	1976-72 EB	[09183]	1976 Aug 2	11 days			67.00	89.90		185	353

D	1976-72 EC	[09184]	1976 Aug 2	11 days			67.10	89.60		163	344

D	1976-72 ED	[09185]	1976 Aug 2	11 days			67.10	89.30		157	328

D	1976-72 EE	[09186]	1976 Aug 2	11 days			67.10	89.50		133	362

D	1976-72 EF	[09187]	1976 Aug 2	11 days			67.20	89.80		173	355

D	1976-72 EG	[09188]	1976 Aug 2	11 days			67.10	90.40		201	390

D	1976-72 EH	[09189]	1976 Aug 2	11 days			67.30	90.30		180	393

D	1976-72 EJ	[09190]	1976 Aug 2	11 days			67.10	90.20		195	377

D	1976-72 EK	[09191]	1976 Aug 2	11 days			67.20	88.90		150	286

D	1976-72 EL	[09192]	1976 Aug 2	11 days			67.00	90.20		174	392

D	1976-72 EM	[09193]	1976 Aug 2	11 days			67.20	90.10		178	377

D	1976-72 EN	[09194]	1976 Aug 2	11 days			67.00	89.90		178	359

D	1976-72 EP	[09195]	1976 Aug 2	11 days			67.20	89.90		192	347

D	1976-72 EQ	[09196]	1976 Aug 2	11 days			67.00	89.30		184	299

D	1976-72 ER	[09197]	1976 Aug 2	11 days			67.10	88.70		128	287

D	1976-72 ES	[09198]	1976 Aug 2	11 days			67.10	89.80		185	341

D	1976-72 ET	[09199]	1976 Aug 2	11 days			67.10	89.40		181	308

D	1976-72 EU	[09200]	1976 Aug 2	11 days			67.10	89.70		127	385

D	1976-72 EV	[09201]	1976 Aug 2	11 days			67.00	89.60		164	342

D	1976-72 EW	[09202]	1976 Aug 2	11 days			67.20	90.10		191	373

D	1976-72 EX	[09203]	1976 Aug 2	11 days			67.20	89.00		173	281

D	1976-72 EY	[09204]	1976 Aug 2	11 days			67.10	88.80		163	269

D	1976-72 EZ	[09205]	1976 Aug 2	11 days			67.40	89.80		146	376

D	1976-72 FA	[09206]	1976 Aug 2	11 days			67.20	89.40		140	347

D	1976-72 FB	[09207]	1976 Aug 2	11 days			67.20	88.90		128	307

D	1976-72 FC	[09208]	1976 Aug 2	11 days			67.10	90.20		177	388

D	1976-72 FD	[09209]	1976 Aug 2	11 days			67.20	90.10		192	367

D	1976-72 FE	[09210]	1976 Aug 2	11 days			67.10	90.40		185	399

D	1976-72 FF	[09211]	1976 Aug 2	11 days			67.30	88.80		123	304

D	1976-72 FG	[09212]	1976 Aug 2	11 days			67.10	89.70		189	327

D	1976-72 FH	[09213]	1976 Aug 2	11 days			67.10	90.30		183	391

D	1976-72 FJ	[09217]	1976 Aug 5	14 days			67.20	89.70		183	329

D	1976-72 FK	[09218]	1976 Aug 5	14 days			67.20	90.00		166	387

D	1976-72 FL	[09219]	1976 Aug 5	14 days			67.20	89.40		145	340

D	1976-72 FM	[09220]	1976 Aug 5	14 days			67.00	89.10		138	318

D	1976-72 FN	[09221]	1976 Aug 5	14 days			67.00	89.80		175	356

D	1976-72 FP	[09222]	1976 Aug 5	14 days			67.10	89.10		148	317

D	1976-72 FQ	[09223]	1976 Aug 5	14 days			67.10	89.60		167	340

D	1976-72 FR	[09224]	1976 Aug 5	14 days			67.10	90.20		176	395

D	1976-72 FS	[09225]	1976 Aug 5	14 days			67.20	89.90		164	375

D	1976-72 FT	[09226]	1976 Aug 5	14 days			67.20	89.90		176	362

D	1976-72 FU	[09227]	1976 Aug 5	14 days			67.40	89.90		200	338

D	1976-72 FV	[09228]	1976 Aug 5	14 days			67.10	89.80		151	381

D	1976-72 FW	[09229]	1976 Aug 5	14 days			67.10	89.00		173	281

D	1976-72 FX	[09230]	1976 Aug 5	14 days			67.10	90.00		168	378

D	1976-72 FY	[09231]	1976 Aug 5	14 days			67.10	90.10		190	370

D	1976-72 FZ	[09232]	1976 Aug 5	14 days			67.20	90.10		174	387

D	1976-72 GA	[09233]	1976 Aug 5	14 days			67.20	89.20		180	287

D	1976-72 GB	[09234]	1976 Aug 5	14 days			67.10	89.10		184	278

D	1976-72 GC	[09235]	1976 Aug 5	14 days			67.30	89.70		172	348

D	1976-72 GD	[09236]	1976 Aug 5	14 days			67.20	89.20		203	270

D	1976-72 GE	[09237]	1976 Aug 5	14 days			67.10	90.10		171	389

D	1976-72 GF	[09238]	1976 Aug 5	14 days			67.10	88.60		132	281

D	1976-72 GG	[09239]	1976 Aug 5	14 days			67.30	88.90		173	263

D	1976-72 GH	[09240]	1976 Aug 5	14 days			67.10	89.60		174	336

D	1976-72 GJ	[09241]	1976 Aug 5	14 days			67.10	88.60		134	277

D	1976-72 GK	[09242]	1976 Aug 5	14 days			67.20	90.10		176	383

D	1976-72 GL	[09243]	1976 Aug 5	14 days			67.10	89.50		196	306

D	1976-72 GM	[09244]	1976 Aug 5	14 days			67.10	89.30		164	315

D	1976-72 GN	[09245]	1976 Aug 5	14 days			67.30	89.40		187	301

D	1976-72 GP	[09246]	1976 Aug 5	14 days			67.10	90.20		175	398

D	1976-72 GQ	[09247]	1976 Aug 5	14 days			67.00	89.00		150	299

D	1976-72 GR	[09248]	1976 Aug 5	14 days			67.40	89.30		175	300

D	1976-72 GS	[09249]	1976 Aug 5	14 days			67.20	89.00		133	318

D	1976-72 GT	[09250]	1976 Aug 5	14 days			67.20	89.90		167	372

D	1976-72 GU	[09251]	1976 Aug 5	14 days			67.20	89.70		182	332

D	1976-72 GV	[09252]	1976 Aug 5	14 days			67.30	89.50		157	337

D	1976-72 GW	[09253]	1976 Aug 5	14 days			67.00	90.00		190	355

D	1976-72 GX	[09254]	1976 Aug 5	14 days			67.00	90.40		194	398

D	1976-72 GY	[09255]	1976 Aug 5	14 days			67.10	90.30		188	389

D	1976-72 GZ	[09256]	1976 Aug 5	14 days			67.20	89.70		156	358

D	1976-72 HA	[09257]	1976 Aug 5	14 days			67.30	89.50		190	352

D	1976-72 HB	[09258]	1976 Aug 5	14 days			67.20	90.20		191	374

D	1976-72 HC	[09259]	1976 Aug 5	14 days			67.30	89.70		162	350

D	1976-72 HD	[09260]	1976 Aug 5	14 days			67.30	90.00		165	382

D	1976-72 HE	[09261]	1976 Aug 5	14 days			67.20	89.30		183	294

D	1976-72 HF	[09262]	1976 Aug 5	14 days			66.90	89.40		172	318

D	1976-72 HG	[09263]	1976 Aug 5	14 days			67.30	89.50		180	322

D	1976-72 HH	[09264]	1976 Aug 5	14 days			67.10	89.00		138	314

D	1976-72 HJ	[09265]	1976 Aug 5	14 days			67.00	90.20		172	393

D	1976-72 HK	[09266]	1976 Aug 5	14 days			67.10	89.80		183	343

D	1976-72 HL	[09331]	1976 Aug 13	22 days			67.30	88.90		167	278

D	1976-72 HM	[09332]	1976 Aug 13	22 days			67.10	89.40		178	310

D	1976-72 HN	[09333]	1976 Aug 13	22 days			67.20	89.90		153	383

D	1976-72 HP	[09334]	1976 Aug 13	22 days			67.10	89.20		198	274

D	1976-72 HQ	[09335]	1976 Aug 13	22 days			67.20	89.30		188	295

D	1976-72 HR	[09336]	1976 Aug 13	22 days			67.10	89.90		185	358

D	1976-72 HS	[09337]	1976 Aug 13	22 days			67.20	89.60		168	342

D	1976-72 HT	[09338]	1976 Aug 13	22 days			67.00	89.90		189	348

D	1976-72 HU	[09339]	1976 Aug 13	22 days			67.20	89.60		158	350

D	1976-72 HV	[09340]	1976 Aug 13	22 days			67.20	90.00		173	372

D	1976-72 HW	[09341]	1976 Aug 13	22 days			67.10	90.00		162	385

D	1976-72 HX	[09342]	1976 Aug 13	22 days			67.20	89.70		149	372

D	1976-72 HY	[09343]	1976 Aug 13	22 days			67.10	88.80		160	269

D	1976-72 HZ	[09344]	1976 Aug 13	22 days			67.10	90.10		185	376

D	1976-72 JA	[09345]	1976 Aug 13	22 days			67.20	88.50		140	264

D	1976-72 JB	[09346]	1976 Aug 13	22 days			67.00	90.00		200	345

D	1976-72 JC	[09347]	1976 Aug 13	22 days			67.10	88.80		140	288

D	1976-72 JD	[09348]	1976 Aug 13	22 days			No info

D	1976-72 JE	[09349]	1976 Aug 13	22 days			67.00	89.60		154	353

D	1976-72 JF	[09350]	1976 Aug 13	22 days			67.10	89.60		157	346

D	1976-72 JG	[09351]	1976 Aug 13	22 days			67.30	89.60		157	352

D	1976-72 JH	[09352]	1976 Aug 13	22 days			67.20	89.70		168	349

D	1976-72 JJ	[09353]	1976 Aug 13	22 days			67.10	90.30		189	387

D	1976-72 JK	[09354]	1976 Aug 13	22 days			67.20	89.70		153	369

D	1976-72 JL	[09355]	1976 Aug 13	22 days			67.10	89.20		162	305

D	1976-72 JM	[09356]	1976 Aug 13	22 days			67.30	88.90		168	269

D	1976-72 JN	[09357]	1976 Aug 13	22 days			67.10	89.80		159	369

D	1976-72 JP	[09358]	1976 Aug 13	22 days			67.00	90.40		203	382

D	1976-72 JQ	[09359]	1976 Aug 13	22 days			67.10	89.10		142	320

D	1976-72 JR	[09360]	1976 Aug 13	22 days			67.10	89.80		163	366

D	1976-72 JS	[09361]	1976 Aug 13	22 days			67.10	89.70		186	326

D	1976-72 JT	[09362]	1976 Aug 13	22 days			67.20	90.10		170	389

D	1976-72 JU	[09363]	1976 Aug 13	22 days			67.20	90.30		193	385

D	1976-72 JV	[09364]	1976 Aug 13	22 days			67.30	89.20		154	315

D	1976-72 JW	[09365]	1976 Aug 13	22 days			67.10	88.90		150	290

D	1976-72 JX	[09366]	1976 Aug 13	22 days			67.10	89.70		202	314

D	1976-72 JY	[09367]	1976 Aug 13	22 days			67.10	89.30		147	331

D	1976-72 JZ	[09368]	1976 Aug 13	22 days			67.10	89.70		177	343

D	1976-72 KA	[09369]	1976 Aug 13	22 days			67.20	88.70		139	280

D	1976-72 KB	[09370]	1976 Aug 13	22 days			67.20	89.80		178	342

D	1976-72 KC	[09371]	1976 Aug 13	22 days			67.00	89.30		202	274

D	1976-72 KD	[09372]	1976 Aug 13	22 days			67.20	89.80		167	366

D	1976-72 KE	[09373]	1976 Aug 13	22 days			67.10	89.50		161	343

D	1976-72 KF	[09378]	1976 Aug 17	26 days			67.10	89.60		157	355

D	1976-72 KG	[09379]	1976 Aug 17	26 days			67.00	89.90		192	349

D	1976-72 KH	[09380]	1976 Aug 17	26 days			67.20	90.30		186	388

D	1976-72 KJ	[09381]	1976 Aug 17	26 days			67.20	89.00		133	316

Cosmos 845 fragments; 6 pieces, all have decayed.

D	1976-75 C	[09058]	1978 Jul 18	721 days		1976 Aug 8.81	74.07	94.92	6893	486	544	0.004	317

1978 Apr 24.35	74.05	92.37	6769	374	407	0.002	249

D	1976-75 D	[09267]	1978 Oct 14	809 days		1976 Aug 6.88	74.01	97.20	7003	498	752	0.018	77

1978 Sep 23.91	73.94	90.70	6688	300	315	0.001	165

D	1976-75 E	[09268]	1979 Feb 27	935 days		1976 Aug 7.56	74.03	97.22	7004	508	743	0.017	65

1979 Jan 23.03	73.99	93.03	6802	394	452	0.004	192

D	1976-75 F	[09665]	1978 Jul 18	721 days		1977 Jan 10.51	73.99	94.80	6888	482	536	0.004	318

1978 May 1.33	73.96	92.32	6766	377	398	0.002	235

D	1976-75 G	[09718]	1978 Mar 27	608 days		1977 Jan 13.04	74.11	94.78	6886	479	536	0.004	316

1978 Feb 17.01	74.09	92.43	6773	390	398	0.0006	92

D	1976-75 H	[09789]	1978 Jun 24	697 days		1977 Jan 31.37	74.03	94.87	6891	487	538	0.004	290

1978 Jan 31.46	74.01	93.43	6821	426	460	0.002	145

NOAA 5 Delta 2nd stage fragments; 183 pieces, 10 have decayed.

This was the sixth Delta Second Stage to experience a severe fragmentation. The event occurred 1977 Dec 24 at 11:33 UT near 40ºS 146ºE, 17 months after the successful deployment of the NOAA 5 payload. Cause of the explosion is assessed to be related to the estimated 250 kg of residual propellants on board and characteristics of the sun-synchronous orbit.

1976-77 C	[10642]				1978 Feb 3.55	102.36	118.87	8009	1507	1754	0.015	262

2004 Jul 6.09	102.74	117.87	7963	1503	1667	0.010	209

2021 Dec 12.91	102.01	117.87	7963	1503	1666	0.010	94

1976-77 D	[10643]				1978 Jan 31.56	102.09	119.10	8019	1505	1776	0.017	266

2004 Jul 4.87	102.14	119.02	8015	1501	1772	0.017	335

2021 Dec 12.86	102.09	118.98	8014	1500	1771	0.017	17

1976-77 E	[10644]				1978 Feb 1.34	101.67	114.33	7804	1336	1514	0.011	41

2004 Jul 6.50	101.86	114.18	7797	1329	1507	0.011	59

2021 Dec 13.00	101.19	114.15	7795	1336	1497	0.10	71

1976-77 F	[10645]				1977 Dec 31.92	102.31	120.18	8067	1507	1870	0.022	313

2004 Jul 4.76	102.41	120.10	8064	1504	1866	0.022	116

2021 Dec 13.15	102.30	120.08	8063	1504	1865	0.022	120

1976-77 G	[10646]				1978 Jan 31.98	102.35	118.63	7998	1502	1736	0.015	270

2004 Jul 5.21	102.80	118.58	7996	1502	1732	0.014	241

2021 Dec 12.43	102.42	118.57	7995	1501	1732	0.014	333

1976-77 H	[10647]				1978 Feb 1.60	102.34	119.02	8015	1503	1770	0.017	268

2004 Jul 6.33	102.84	118.92	8011	1499	1765	0.017	294

2021 Dec 12.87	102.80	118.88	8009	1499	1763	0.016	44

1976-77 J	[10648]				1978 Feb 2.10	101.96	118.53	7993	1501	1729	0.014	268

2004 Jul 4.92	101.94	118.07	7973	1490	1698	0.013	326

2021 Dec 12.54	102.03	118.03	7971	1492	1693	0.013	65

1976-77 K	[10649]				1977 Dec 31.96	102.24	122.17	8156	1462	2092	0.039	339

2004 Jul 4.66	102.30	122.03	8150	1465	2078	0.038	302

2021 Dec 12.95	102.28	122.02	8149	1464	2077	0.038	281

1976-77 L	[10650]				1978 Feb 1.60	102.07	124.55	8262	1508	2259	0.045	263

2004 Jul 4.44	102.07	124.45	8257	1515	2243	0.044	117

2021 Dec 12.89	102.06	124.42	8256	1516	2238	0.044	105

D	1976-77 M	[10651]	1989 Nov 15	4857 days		1978 Feb 1.60	101.53	114.42	7808	1398	1460	0.004	51

1989 Nov 14.44	102.14	93.93	6846	413	522	0.008	267

1976-77 N	[10652]				1978 Feb 2.63	102.82	120.90	8099	1506	1935	0.027	254

2004 Jul 5.33	103.05	120.42	8078	1492	1906	0.026	102

2021 Dec 12.92	102.95	120.28	8072	1497	1889	0.024	74

1976-77 P	[10653]				1977 Dec 31.93	102.78	117.68	7955	1471	1682	0.013	356

2004 Jul 6.31	102.58	117.67	7955	1473	1679	0.013	18

2021 Dec 12.82	102.60	117.63	7953	1473	1676	0.013	73

1976-77 Q	[10654]				1978 Feb 1.12	102.51	112.53	7722	1179	1507	0.021	54

2004 Jul 5.20	102.49	111.62	7680	1144	1458	0.020	67

2021 Dec 12.48	102.49	111.82	7666	1126	1448	0.021	288

1976-77 R	[10655]				1978 Feb 1.59	102.32	118.98	8014	1417	1854	0.027	307

2004 Jul 5.33	102.77	118.93	8011	1414	1851	0.027	292

2021 Dec 12.83	102.85	118.88	8010	1412	1850	0.027	31

1976-77 S	[10656]				1978 Feb 2.25	102.25	116.53	7904	1466	1584	0.008	321

2004 Jul 4.91	102.40	116.43	7899	1459	1582	0.008	159

2021 Dec 13.03	101.72	116.40	7898	1458	1581	0.008	321

1976-77 T	[10657]				1978 Feb 2.10	102.20	117.53	7949	1504	1636	0.008	269

2004 Jul 6.17	102.43	117.48	7947	1502	1634	0.008	11

2021 Dec 12.86	102.37	117.48	7946	1501	1634	0.008	93

1976-77 U	[10658]				1978 Feb 2.28	102.21	117.10	7929	1506	1595	0.006	268

2004 Jul 5.16	102.38	117.08	7928	1504	1595	0.006	137

2021 Dec 12.92	102.26	117.07	7928	1504	1594	0.006	84

1976-77 V	[10659]				1977 Dec 31.95	102.11	119.22	8025	1505	1787	0.018	318

2004 Jul 4.90	102.18	119.12	8020	1499	1783	0.018	17

2021 Dec 12.97	102.04	119.08	8018	1500	1779	0.017	78

1976-77 W	[10660]				1978 Feb 2.11	102.22	123.42	8212	1508	2158	0.040	252

2004 Jul 6.20	102.23	123.37	8210	1509	2153	0.039	278

2021 Dec 12.81	102.25	123.35	8209	1503	2156	0.040	152

1976-77 X	[10661]				1977 Dec 31.93	101.75	115.18	7842	1416	1512	0.006	146

2004 Jul 5.69	101.16	109.77	7594	1118	1314	0.013	11

2021 Dec 12.94	101.18	108.37	7530	1062	1241	0.012	193

1976-77 Y	[10662]				1978 Feb 2.24	101.26	112.83	7735	1190	1524	0.022	31

2004 Jul 5.24	101.22	111.87	7691	1147	1477	0.021	328

2021 Dec 12.66	100.88	111.60	7679	1092	1508	0.027	131

1976-77 Z	[10663]				1978 Feb 2.07	100.57	111.70	7683	1076	1533	0.030	20

2004 Jul 6.15	100.65	106.83	7459	941	1219	0.019	177

2021 Dec 13.11	100.60	104.72	7360	873	1090	0.015	93

D	1976-77 AA	[10705]	2021 Mar 2	16287 days		1978 Mar 8.04	101.69	115.18	7842	1416	1511	0.006	20

2004 Jul 5.70	102.16	102.13	7238	554	1165	0.042	344

2010 Mar 2.42	101.99	90.10	6658	265	293	0.002	22

1976-77 AB	[10706]				1977 Dec 31.94	101.58	114.03	7790	1253	1570	0.020	73

2004 Jul 6.32	101.54	112.65	7727	935	1762	0.054	36

2021 Dec 12.93	101.51	112.40	7715	1049	1624	0.037	293

1976-77 AC	[10707]				1978 Mar 7.99	102.24	121.03	8106	1499	1955	0.028	197

2004 Jul 5.27	102.25	120.42	8078	1479	1920	0.027	220

2021 Dec 13.06	102.26	120.18	8068	1467	1911	0.027	223

1976-77 AD	[10708]				1978 Mar 7.97	101.95	115.33	7849	1381	1560	0.011	295

2004 Jul 4.49	101.75	114.42	7807	1298	1559	0.017	308

2021 Dec 12.08	101.34	114.12	7793	1289	1541	0.016	63

1976-77 AE	[10709]				1978 Mar 7.98	101.98	116.35	7895	1494	1539	0.003	221

2004 Jul 6.34	101.99	115.45	7854	1460	1491	0.002	179

2021 Dec 12.92	101.91	115.52	7858	1472	1487	0.0009	53

1976-77 AF	[10710]				1978 mar 7.97	101.79	121.17	8111	1500	1965	0.029	188

2004 Jul 5.98	101.79	120.43	8079	1487	1913	0.026	253

2021 Dec 12.81	101.81	120.15	8066	1468	1906	0.027	31

1976-77 AG	[10711]				1978 Mar 8.00	102.26	117.17	7932	1503	1604	0.006	214

2004 Jul 4.69	102.41	117.15	7931	1502	1603	0.006	175

2021 Dec 12.91	102.25	117.13	7931	1502	1603	0.006	146

1976-77 AH	[10712]				1978 Mar 7.58	102.11	117.27	7937	1493	1624	0.008	214

2004 Jul 5.69	102.25	116.40	7898	1461	1577	0.007	13

2021 Dec 12.55	102.21	116.40	7897	1454	1584	0.008	239

1976-77 AJ	[10713]				1978 Mar 8.03	101.52	114.90	7830	1399	1503	0.007	29

2004 Jul 4.69	101.41	111.98	7696	1194	1441	0.016	206

2021 Dec 12.81	101.48	111.00	7652	1174	1371	0.013	167

1976-77 AK	[10714]				1978 Mar 8.00	103.19	126.70	8357	1447	2510	0.064	190

2004 Jul 5.22	103.37	125.14	8292	1447	2380	0.056	225

2021 Dec 12.92	103.42	125.00	8282	1409	2397	0.060	248

1976-77 AL	[10715]				1978 Mar 8.00	102.50	123.90	8233	1490	2219	0.044	186

2004 Jul 4.53	102.47	123.78	8228	1490	2208	0.044	225

2021 Dec 12.72	102.56	123.73	8226	1487	2207	0.044	300

1976-77 AM	[10716]				1978 Mar 7.71	102.63	118.15	7976	1369	1825	0.029	254

2004 Jul 5.41	102.77	114.78	7824	1215	1677	0.030	75

2021 Dec 12.96	102.71	113.22	7752	1276	1472	0.013	13

1976-77 AN	[10717]				1978 Mar 7.74	102.30	117.80	7960	1501	1662	0.010	212

2004 Jul 5.02	102.50	117.73	7958	1499	1659	0.010	146

2021 Dec 12.87	102.42	117.72	7957	1498	1658	0.010	316

1976-77 AP	[10718]				1978 Mar 8.00	102.22	116.15	7885	1466	1547	0.005	275

2004 Jul 4.84	102.10	115.93	7876	1457	1539	0.005	257

2021 Dec 12.96	101.82	115.88	7874	1454	1536	0.005	309

1976-77 AQ	[10719]				1978 Mar 7.64	101.91	120.87	8098	1496	1943	0.028	185

2004 Jul 3.53	101.94	120.17	8067	1490	1886	0.024	275

2021 Dec 12.16	101.93	119.97	8058	1496	1862	0.023	68

1976-77 AR	[10720]				1978 Mar 7.97	102.02	119.65	8044	1372	1958	0.036	251

2004 Jul 5.60	101.99	119.48	8036	1368	1948	0.036	100

2021 Dec 12.81	101.98	119.45	8035	1368	1945	0.036	175

1976-77 AS	[10721]				1978 Mar 7.98	101.80	115.22	7844	1429	1502	0.005	353

2004 Jul 4.52	101.78	114.47	7810	1392	1470	0.005	202

2021 Dec 12.27	101.78	114.05	7791	1372	1452	0.005	4

1976-77 AT	[10746]				1977 Dec 31.93	101.71	113.88	7783	121	1689	0.037	192

2004 Jul 5.92	101.83	110.80	7642	964	1563	0.039	55

2021 Dec 12.94	101.91	109.80	7596	988	1447	0.030	252

1976-77 AU	[10747]				1978 Mar 28.14	101.02	111.83	7689	1128	1493	0.024	303

2004 Jul 4.99	101.04	107.98	7512	997	1270	0.018	62

2021 Dec 12.95	101.11	106.63	7449	968	1173	0.014	1

1976-77 AV	[10748]				1978 Mar 28.08	102.18	107.23	7935	1497	1617	0.008	185

2004 Jul 5.72	102.36	117.13	7931	1493	1611	0.007	200

2021 Dec 12.87	102.26	117.10	7929	1493	1608	0.007	161

1976-77 AW	[10749]				1978 Mar 28.55	102.01	117.72	7957	1506	1651	0.009	164

2004 Jul 5.43	102.70	117.70	7956	1505	1650	0.009	18

2021 Dec 12.84	102.41	117.68	7955	1505	1649	0.009	43

1976-77 AX	[10750]				1978 Mar 29.12	101.59	114.10	7793	1341	1488	0.009	305

2004 Jul 5.51	101.75	110.43	7625	803	1690	0.058	333

2021 Dec 12.92	101.68	107.55	7492	701	1526	0.055	22

1976-77 AY	[10751]				1977 Dec 31.95	102.08	126.32	8340	1418	2505	0.065	273

2004 Jul 4.60	102.12	125.07	8285	1388	2424	0.063	32

2021 Dec 13.09	102.08	124.83	8274	1427	2364	0.057	93

1976-77 AZ	[10752]				1978 Mar 28.54	101.74	115.10	7839	1424	1496	0.005	324

2004 Jul 6.16	101.76	113.65	7772	1314	1474	0.010	324

2021 Dec 12.93	101.73	112.65	7727	1048	1649	0.039	114

D	1976-77 BA	[10753]	1982 Jan 2	1983 days		1978 Mar 30.61	101.57	113.03	7744	1289	1443	0.010	268

1982 Jan 2.10	101.85	92.93	6797	385	451	0.005	192

1976-77 BB	[10754]				1977 Dec 31.94	102.33	117.90	7965	1488	1684	0.012	344

2004 Jul 6.18	102.52	117.87	7964	1487	1684	0.012	224

2021 Dec 12.85	102.48	117.87	7964	1487	1683	0.012	83

1976-77 BC	[10755]				1978 Mar 28.53	102.15	117.50	7947	1504	1633	0.008	171

2004 Jul 5.66	102.43	117.47	7945	1502	1631	0.008	357

2021 Dec 12.87	102.33	117.45	7945	1501	1631	0.008	61

1976-77 BD	[10756]				1977 Dec 31.98	101.06	118.38	7987	1320	1895	0.036	235

2004 Jul 5.38	101.07	116.90	7920	1426	1657	0.015	9

2021 Dec 12.81	101.13	116.10	7884	1370	1641	0.017	42

1976-77 BE	[10757]				1978 Mar 28.55	101.90	120.55	8084	1500	1911	0.025	159

2004 Jul 4.42	101.94	120.15	8066	1509	1866	0.022	220

2021 Dec 12.94	101.89	120.00	8059	1493	1869	0.023	17

1976-77 BF	[10758]				1977 Dec 31.92	102.38	118.88	8009	1503	1758	0.016	322

2004 Jul 5.68	102.95	118.77	8004	1502	1748	0.015	345

2021 Dec 12.82	102.24	118.73	8003	1500	1748	0.016	174

1976-77 BG	[10759]				1978 mar 28.11	102.48	117.17	7932	1491	1616	0.008	130

2004 Jul 5.37	102.47	116.35	7895	1465	1568	0.007	177

2021 Dec 12.74	102.54	116.00	7879	1448	1553	0.007	147

1976-77 BH	[10760]				1977 Dec 31.93	101.31	119.03	8016	1507	1768	0.016	315

2004 Jul 6.30	101.39	117.83	7962	1407	1760	0.022	0

2021 Dec 12.88	101.50	117.00	7925	1108	1984	0.055	341

1976-77 BJ	[10761]				1978 Mar 29.55	100.78	120.33	8074	1501	1890	0.024	152

2004 Jul 5.86	101.16	118.60	7997	950	2286	0.083	215

2021 Dec 13.09	101.43	116.22	7889	596	2425	0.116	24

1976-77 BK	[10762]				1977 Dec 31.92	102.95	128.87	8451	1411	2734	0.078	342

2004 Jul 5.99	102.91	124.88	8276	1283	2512	0.074	139

2021 Dec 13.12	102.83	123.68	8224	1276	2414	0.069	32

1976-77 BL	[10763]				1978 Mar 28.54	102.25	116.80	7915	1499	1575	0.005	189

2004 Jul 6.54	102.41	116.73	7912	1497	1570	0.005	319

2021 Dec 12.89	102.00	116.72	7911	1496	1569	0.005	158

1976-77 BM	[10764]				1978 Mar 28.53	102.07	119.67	8045	1478	1854	0.023	189

2004 Jul 5.16	102.07	119.58	8041	1479	1845	0.023	165

2021 Dec 12.53	102.08	119.55	8039	1478	1843	0.023	306

1976-77 BN	[10765]				1978 Mar 28.53	102.07	118.38	7987	1503	1713	0.013	170

2004 Jul 5.20	102.27	118.37	7986	1503	1712	0.013	131

2021 Dec 12.97	102.22	118.37	7986	1503	1712	0.013	41

1976-77 BP	[10766]				1978 Mar 28.54	102.23	117.00	7924	1502	1590	0.006	177

2004 Jul 4.94	102.41	116.97	7923	1501	1587	0.005	78

2021 Dec 12.91	102.16	116.95	7922	1501	1586	0.005	346

1976-77 BQ	[10767]				1978 Mar 28.15	102.16	117.02	7925	1495	1598	0.007	191

2004 Jul 5.12	102.33	116.92	7921	1490	1594	0.007	89

2021 Dec 12.87	102.20	116.90	7920	1489	1593	0.007	335

1976-77 BR	[10768]				1978 Jan 1.00	102.63	117.42	7943	1506	1623	0.007	319

2004 Jul 4.85	102.17	117.27	7937	1500	1616	0.007	170

2021 Dec 12.89	102.55	117.22	7934	1499	1613	0.007	9

1976-77 BS	[10769]				1977 Dec 31.94	101.84	115.07	7837	1386	1531	0.009	27

2004 Jul 5.12	101.97	114.98	7833	1379	1529	0.010	157

2021 Dec 12.86	101.59	114.95	7832	1377	1530	0.010	60

1976-77 BT	[10823]				1977 Dec 31.98	101.71	115.93	7876	1462	1533	0.005	198

2004 Jul 6.17	102.09	115.82	7871	1460	1525	0.004	67

2021 Dec 12.82	101.76	115.78	7870	1456	1526	0.004	249

1976-77 BU	[10824]				1978 May 3.67	101.78	115.08	7837	1414	1503	0.006	223

2004 Jul 5.78	102.02	109.30	7873	1145	1243	0.006	127

2021 Dec 12.45	101.86	116.17	7427	1014	1084	0.005	29

1976-77 BV	[10825]				1977 Dec 31.95	101.91	116.70	7911	1498	1567	0.004	258

2004 Jul 5.16	102.26	116.63	7908	1496	1563	0.004	213

2021 Dec 12.89	102.04	116.62	7907	1494	1563	0.004	333

1976-77 BW	[10826]				1978 May 4.11	102.25	119.50	8037	1431	1886	0.028	138

2004 Jul 4.62	101.42	116.10	7884	1378	1633	0.016	263

2021 Dec 12.55	101.51	115.05	7836	1332	1583	0.016	45

D	1976-77 BX	[10827]	1988 Sep 11	4427 days		1978 May 4.06	101.22	111.58	7678	1176	1423	0.016	229

101.04	95.42		513	565	from Satcat

1992 May 30.73	28.80	104.52	7350	477	1466	0.067	186

1976-77 BY	[10828]				1978 May 4.07	102.16	117.83	7962	1504	1664	0.010	106

2004 Jul 4.67	102.56	117.80	7961	1503	1662	0.010	186

2021 Dec 12.87	102.32	117.80	7961	1502	1661	0.010	2

1976-77 BZ	[10829]				1977 Dec 31.95	101.74	116.73	7913	1504	1564	0.004	274

2004 Jul 4.89	101.80	116.52	7903	1495	1554	0.004	268

2021 Dec 12.95	101.62	116.47	7900	1490	1553	0.004	316

1976-77 CA	[10830]				1977 Dec 31.99	101.77	117.30	7938	1492	1627	0.009	262

2004 Jul 5.16	101.76	117.25	7935	1485	1628	0.009	156

2021 Dec 12.94	101.73	117.23	7935	1486	1626	0.009	340

1976-77 CB	[10831]				1978 May 3.98	102.05	118.18	7978	1469	1730	0.016	100

2004 Jul 5.43	101.95	116.02	7880	1189	1814	0.040	120

2021 Dec 12.76	101.28	114.73	7822	1014	4873	0.055	63

1976-77 CC	[10832]				1977 Jan 1.00	102.07	118.18	7978	1503	1696	0.012	269

2004 Jul 6.54	102.21	118.07	7973	1497	1691	0.012	30

2021 Dec 12.85	102.12	118.03	7971	1497	1688	0.012	228

1976-77 CD	[10833]				1978 May 4.06	102.25	117.38	7942	1471	1655	0.012	35

2004 Jul 4.32	102.37	116.53	7919	1446	1635	0.012	65

2021 Dec 12.95	101.93	116.17	7911	1440	1625	0.012	297

1976-77 CE	[10834]				1978 May 4.02	100.56	119.72	8051	1504	1840	0.021	86

2004 Jul 6.09	100.48	118.78	8005	1476	1776	0.019	258

2021 Dec 11.56	100.38	118.35	7985	1444	1770	0.020	149

1976-77 CF	[10835]				1978 May 4.00	101.76	115.43	7854	1434	1516	0.005	183

2004 Jul 5.20	102.16	110.08	7609	1188	1273	0.006	129

2021 Dec 12.79	102.10	107.22	7476	1049	1146	0.006	20

1976-77 CG	[10836]				1978 Jan 31.99	102.02	119.43	8034	1507	1804	0.018	250

2004 Jul 5.57	101.98	119.28	8028	1502	1796	0.018	357

2021 Dec 12.54	101.98	119.25	8026	1501	1793	0.018	44

1976-77 CH	[10837]				1978 Jan 31.94	102.23	119.78	8050	1507	1836	0.020	253

2004 Jul 5.34	102.31	119.63	8043	1504	1824	0.020	271

2021 Dec 12.25	102.16	119.57	8040	1503	1821	0.020	134

1976-77 CJ	[10838]				1978 Jan 31.97	102.26	116.10	7884	1474	1536	0.004	344

2004 Jul 4.88	102.19	116.05	7882	1472	1535	0.004	288

2021 Dec 13.13	101.78	116.05	7881	1471	1534	0.004	35

1976-77 CK	[10839]				1978 Jan 31.95	101.76	114.60	7815	1393	1481	0.006	64

2004 Jul 6.20	101.99	117.88	7507	1119	1139	0.001	194

2021 Dec 12.88	101.96	103.32	7294	885	946	0.004	329

1976-77 CL	[10840]				1978 Jan 31.95	102.22	118.52	7993	1500	1729	0.014	274

2004 Jul 5.90	102.77	118.43	7989	1497	1724	0.014	55

2021 Dec 12.86	102.65	118.42	7988	1497	1722	0.014	356

1976-77 CM	[10841]				1978 May 4.10	101.72	115.05	7836	1406	1509	0.007	220

2004 Jul 4.66	101.85	114.95	7832	1398	1508	0.007	164

2021 Dec 12.84	101.72	114.92	7830	1399	1505	0.007	37

1976-77 CN	[10842]				1978 Jan 31.96	102.18	114.63	7817	1206	1672	0.030	355

2004 Jul 6.22	102.11	114.48	7810	1204	1660	0.029	277

2021 Dec 12.78	102.09	114.38	7806	1204	1650	0.029	331

1976-77 CP	[10843]				1978 Dec 31.93	101.71	114.55	7813	1346	1523	0.011	31

2004 Jul 4.64	101.85	114.27	7809	1339	1522	0.012	219

2021 Dec 12.90	101.47	114.42	7808	1338	1521	0.012	278

1976-77 CQ	[10844]				1978 May 4.14	101.35	112.00	7697	1128	1509	0.025	210

2004 Jul 6.02	101.27	117.80	7504	997	1253	0.017	323

2021 Dec 12.86	101.21	116.13	7426	942	1153	0.014	249

1976-77 CR	[10845]				1978 May 3.04	102.20	119.22	8024	1501	1791	0.018	110

2004 Jul 6.16	102.18	119.07	8017	1496	1781	0.018	98

2021 Dec 12.93	102.19	119.00	8015	1494	1778	0.018	188

1976-77 CS	[10864]				1978 Jan 26.55	101.09	122.97	8191	1503	2122	0.038	269

2004 Jul 4.73	101.10	122.63	8176	1489	2107	0.038	34

2021 Dec 12.97	101.07	122.52	8172	1485	2101	0.038	304

1976-77 CT	[10865]				1978 May 11.08	102.14	118.02	7970	1503	1681	0.011	96

2004 Jul 4.72	102.72	118.00	7969	1502	1680	0.011	285

2021 Dec 12.86	102.15	118.00	7696	1502	1680	0.011	186

1976-77 CU	[10866]				1978 May 11.39	102.72	117.17	7932	1432	1675	0.015	145

2004 Jul 4.96	102.77	117.05	7927	1429	1668	0.015	204

2021 Dec 12.52	102.60	117.02	7925	1429	1665	0.015	103

1976-77 CV	[10867]				1978 May 11.36	101.76	115.20	7843	1423	1506	0.005	228

2004 Jul 5.69	102.01	112.37	7714	911	1759	0.055	265

2021 Dec 12.52	101.79	111.57	7677	1120	1476	0.023	98

1976-77 CW	[10868]				1978 May 11.09	102.25	117.82	7961	1502	1663	0.010	97

2004 Jul 6.25	102.44	116.73	7913	1459	1609	0.009	192

2021 Dec 12.91	102.37	116.35	7895	1433	1600	0.011	188

1976-77 CX	[10869]				1978 May 11.10	102.33	116.10	7884	1478	1532	0.003	162

2004 Jul 4.75	102.17	115.90	7875	1474	1517	0.003	195

2021 Dec 13.00	102.18	115.83	7871	1471	1514	0.003	317

1976-77 CY	[10870]				1978 Jan 31.99	102.05	116.42	7898	1503	1536	0.002	276

2004 Jul 5.95	102.09	115.65	7864	1472	1498	0.002	268

2021 Dec 12.99	101.62	115.43	7854	1464	1486	0.001	87

1976-77 CZ	[10871]				1978 May 11.10	102.04	117.12	7930	1338	1765	0.027	350

2004 Jul 5.58	102.26	116.55	7904	1303	1748	0.028	210

2021 Dec 12.97	101.77	116.47	7900	1298	1745	0.028	325

1976-77 DA	[10872]				1978 Jan 31.93	101.53	117.72	7957	1501	1656	0.010	225

2004 Jul 4.91	101.55	117.47	7946	1489	1645	0.010	77

2021 Dec 12.26	101.60	117.38	7941	1482	1643	0.010	188

1976-77 DB	[10873]				1978 May 11.09	102.09	118.67	7999	1508	1733	0.014	78

2004 Jul 4.41	102.17	118.63	7998	1507	1732	0.014	226

2021 Dec 12.81	102.02	118.62	7998	1507	1731	0.014	186

1976-77 DC	[10874]				1978 May 11.06	101.77	115.02	7835	1412	1500	0.006	226

2004 Jul 6.24	102.03	111.38	7669	1163	1417	0.017	31

2021 Dec 12.77	102.09	110.07	7608	1192	1267	0.005	160

1976-77 DD	[10875]				1978 May 10.48	101.49	115.60	7891	1455	1511	0.004	95

2004 Jul 5.14	101.93	115.52	7857	1451	1505	0.003	66

2021 Dec 12.73	101.76	115.48	7856	1451	1503	0.003	111

1976-77 DE	[10876]				1978 Dec 11.46	102.55	115.52	7858	1397	1562	0.011	177

2004 Jul 6.55	102.51	115.38	7851	1393	1551	0.010	267

2021 Dec 12.74	102.49	115.33	7849	1391	1550	0.010	63

1976-77 DF	[12274]				1978 Jun 8.09	102.43	117.83	7962	1498	1668	0.011	68

Re-assigned 2011 Jun from 1978 26 DT; old 1976 77 DF to EL moved 1 character down to 1976 77 DG to EM

1976-77 DG	[12527]				2004 Jul 4.62	102.31	116.35	7895	1485	1548	0.004	150

2021 Dec 12.88	101.91	116.32	7894	1485	1545	0.004	205

1976-77 DH	[12528]				1978 May 30.94	102.18	117.42	7943	1502	1627	0.008	61

2004 Jul 6.18	102.41	117.35	7941	1500	1624	0.008	304

2021 Dec 12.89	102.33	117.33	7940	1499	1623	0.008	341

1976-77 DJ	[12529]				1978 May 30.94	103.64	131.22	8554	1376	2974	0.093	132

2004 Jul 6.25	103.47	129.47	8478	1428	2771	0.079	332

2021 Dec 13.06	103.41	128.27	8425	1288	2805	0.090	273

1976-77 DK	[12530]				1978 May 30.99	102.25	117.40	7942	1462	1665	0.013	95

2004 Jul 6.19	102.42	117.37	7941	1461	1663	0.013	322

2021 Dec 12.90	102.34	117.35	7940	1461	1663	0.013	5

1976-77 DL	[12531]				1978 May 30.96	101.77	118.30	7983	1499	1709	0.013	11

2004 Jul 4.63	101.80	118.22	7979	1489	1712	0.014	153

2021 Dec 12.67	101.83	118.18	7978	1492	1706	0.013	204

1976-77 DM	[12532]				1978 May 2.59	101.58	113.88	7783	1348	1461	0.007	249

2004 Jul 6.96	101.76	113.85	7782	1345	1461	0.007	181

2021 Dec 12.54	102.11	113.05	7745	1175	1557	0.025	304

1976-77 DN	[12533]				1978 May 30.94	101.91	116.33	7894	1424	1607	0.012	110

2004 Jul 5.61	102.04	115.73	7867	1410	1567	0.010	1

2021 Dec 12.96	101.60	116.53	7858	1398	1561	0.010	166

1976-77 DP	[12534]				1978 May 30.95	102.18	116.47	7900	1471	1572	0.006	110

2004 Jul 5.21	102.08	116.20	7889	1453	1567	0.007	131

2021 Dec 12.82	102.03	116.40	7898	1465	1574	0.007	235

1976-77 DQ	[12535]				1978 May 29.95	102.27	102.27	8217	1507	2169	0.040	68

2004 Jul 5.71	102.35	123.48	8215	1506	2166	0.040	3

2021 Dec 12.10	102.34	123.47	8214	1505	2165	0.040	294

1976-77 DR	[12536]				1980 Aug 4.93	101.96	125.87	8320	1450	2433	0.059	302

2004 Jul 6.06	101.88	123.53	8217	1361	2316	0.058	102

2021 Dec 13.04	101.82	123.55	8173	1367	2222	0.052	73

1976-77 DS	[12537]				1980 Oct 21.97	102.19	118.97	8013	1503	1766	0.016	337

2004 Jul 4.94	102.31	118.88	8009	1500	1761	0.016	110

2021 Dec 12.80	102.19	118.87	8008	1500	1760	0.016	270

1976-77 DT	[12538]				1978 May 30.99	102.44	119.63	8043	1503	1825	0.020	68

2004 Jul 5.16	102.46	119.48	8036	1499	1816	0.020	158

2021 Dec 12.86	102.78	119.43	8034	1496	1815	0.020	151

1976-77 DU	[12539]				1978 May 30.99	101.96	115.90	7875	1471	1522	0.003	206

2004 Jul 6.11	101.70	114.10	7793	1348	1481	0.009	313

2021 Dec 10.55	101.60	113.03	7744	1107	1624	0.033	0

1976-77 DV	[12540]				1978 May 27.99	102.48	116.30	7893	1459	1570	0.007	124

2004 Jul 5.73	102.48	115.65	7864	1453	1517	0.004	335

2021 Dec 13.10	102.50	115.48	7856	1440	1514	0.005	157

D	1976-77 DW	[12541]	1992 May 10	5764 days		1980 Jun 14.83	102.47	112.48	7720	1001	1681	0.044	122

1992 May 9.59	102.22	91.48	6726	328	367	0.003	191	1976-77 DX	[12542]				1980 Jun 67	101.61	115.18	7842	1416	1511	0.006	220

2004 Jul 4.97	101.86	115.05	7836	1412	1503	0.006	286

2021 Dec 12.88	101.73	115.00	7834	1409	1502	0.006	201

1976-77 DY	[12580]				1980 Jul 24.11	102.45	127.78	8404	1500	2551	0.063	9

2004 Jul 5.06	102.46	127.70	8400	1500	2543	0.062	110

2021 Dec 12.91	102.43	127.63	8398	1503	2536	0.062	91

1976-77 DZ	[12581]				1978 May 25.92	102.40	123.12	8199	1505	2134	0.038	69

2004 Jul 5.64	102.46	123.07	8196	1504	2131	0.038	343

2021 Dec 12.80	102.41	123.05	8195	1504	2130	0.038	262

1976-77 EA	[12647]				1980 Aug 5.99	100.70	122.77	8183	1528	2080	0.034	118

2004 Jul 6.12	100.68	121.87	8143	1469	2059	0.036	10

2021 Dec 12.56	100.68	121.52	8127	1441	2056	0.038	273

1976-77 EB	[13529]				1980 Jul 26.53	102.05	117.93	7966	1474	1701	0.014	94

2004 Jul 8.72	101.88	123.55	8218	1524	2154	0.038	72

2021 Dec 11.79	101.87	123.50	8215	1525	2148	0.038	185

1976-77 EC	[13530]				1980 Jun 15.59	102.33	118.42	7988	1492	1727	0.015	213

2004 Jul 8.77	102.30	116.77	7914	1433	1637	0.013	124

2021 Dec 12.81	102.35	116.50	7902	1423	1623	0.013	123

1976-77 ED	[13531]				1980 Feb 11.96	74.04	117.60	7951	1453	1692	0.015	268

2004 Jul 8.66	102.67	118.33	7985	1491	1722	0.014	116

2021 Dec 12.89	102.52	118.30	7983	1493	1717	0.014	135

1976-77 EE	[13532]				1979 Dec 1.81	101.86	122.83	8186	1508	2107	0.037	238

2004 Jul 8.83	102.27	120.63	8088	1477	1942	0.029	205

2021 Dec 12.64	102.20	120.60	8087	1476	1940	0.029	265

1976-77 EF	[13533]				1979 Jul 10.90	101.82	123.47	8214	1507	2163	0.040	123

2004 Jul 8.29	101.87	122.68	8179	1504	2097	0.036	190

2021 Dec 12.96	101.84	122.62	8176	1505	2090	0.036	122

1976-77 EG	[13534]				1979 Jul 11.44	102.16	116.25	7891	1494	1531	0.002	83

2004 Jul 8.28	101.83	123.30	8207	1502	2154	0.040	340

2021 Dec 12.91	101.82	123.27	8205	1499	2154	0.040	13

1976-77 EH	[13535]				1979 Jun 28.38	101.75	122.58	8175	1450	2142	0.042	158

2004 Jul 8.93	102.35	116.22	7889	1492	1529	0.002	18

2021 Dec 12.85	101.66	116.22	7889	1492	1529	0.002	129

1976-77 EJ	[13536]				1979 Jul 17.36	102.16	117.43	7944	1505	1626	0.008	30

2004 Jul 8.18	101.76	122.50	8171	1448	2136	0.042	74

2021 Dec 12.89	101.79	122.47	8169	1447	2134	0.042	271

1976-77 EK	[13537]				1980 Aug 9.03	87.48	166.27	10016	3351	3924	0.029	92

2004 Jul 8.29	102.42	117.37	7941	1503	1622	0.008	297

2021 Dec 12.85	102.32	117.35	7940	1501	1622	0.008	343

1976-77 EL	[13538]				1980 Jul 24.21	101.90	123.78	8228	1509	2189	0.041	237

2004 Jul 8.09	102.70	117.88	7965	1498	1674	0.011	235

2021 Dec 13.02	102.08	117.85	7963	1497	1671	0.011	173

1976-77 EM	[13539]				2004 Jul 8.52	101.90	123.62	8221	1499	2185	0.042	108

Old 1976 77 EM re-assigned 2011 Jun to 1973 86 GP			2021 Dec 12.42	101.88	123.58	8219	1505	2176	0.041	218

1976-77 EN	[14471]				1983 Jan 9.94	102.13	117.83	7962	1481	1687	0.013	323-

2004 Jul 9.04	102.51	117.63	7953	1471	1678	0.013	150

2021 Dec 12.71	102.25	117.55	7949	1467	1674	0.013	288

1976-77 EP	[14472]				1982 Nov 29.56	102.25	118.43	7989	1486	1735	0.016	84

2004 Jul 9.36	102.66	118.40	7988	1484	1734	0.016	140

2021 Dec 12.89	102.60	118.38	7987	1484	1732	0.016	186

1976-77 EQ	[14509]				1980 Aug 31.64	102.26	118.90	8010	1504	1759	0.016	71

2004 Jul 8.68	103.01	118.82	8007	1501	1755	0.016	350

2021 Dec 16.95	102.23	118.78	8005	1500	1753	0.016	232

1976-77 ER	[14510]				1982 Jun 3.36	102.33	120.10	8064	1505	1866	0.022	94

2004 Jul 8.36	102.41	120.07	8062	1505	1863	0.022	108

2021 Dec 16.79	102.25	120.05	8062	1504	1862	0.022	119

1976-77 ES	[14904]				1981 Dec 17.26	102.80	116.00	7879	1420	1582	0.010	189

2004 Jun 29.38	102.74	113.63	7772	1387	1400	0.008	105

2021 Dec 16.45	102.72	113.30	7757	1368	1388	0.001	232

1976-77 ET	[14905]				1979 Jul 10.53	102.16	119.38	8032	1504	1803	0.019	78

2004 Jul 8.90	102.14	119.28	8028	1500	1798	0.019	162

2021 Dec 16.84	102.35	119.28	8027	1501	1796	0.018	318

1976-77 EU	[15540]				1978 May 1.43	102.65	124.23	8248	1467	2271	0.049	132

2004 Jul 9.05	102.67	123.63	8221	1363	2322	0.058	12

2021 Dec 12.96	102.71	123.37	8209	1365	2296	0.057	107

D	1976-77 EV	[16997]	1997 Oct 7	7740 days		1986 Oct 4.52	103.61	130.33	8523	1531	2758	0.072	57

1997 Oct 3.27	102.75	97.72	7028	416	883	0.033	31

102.70	91.22		291	378	from Satcat

D	1976-77 EW	[16999]	1988 Aug 1	4386 days		1986 Apr 27.98	102.58	109.40	7578	867	1531	0.043	290

1988 Jul 28.85	102.40	93.60	6829	223	679	0.033	289

1976-77 EX	[17000]				1978 May 30.98	102.50	128.72	8445	1454	2679	0.072	88

2004 Jul 8.60	102.49	127.97	8412	1441	2625	0.070	309

2021 Dec 12.15	102.52	127.33	8385	1398	2614	0.073	303

1976-77 EY	[18232]				1977 Dec 31.94	102.92	114.03	7790	1315	1509	0.012	111

2004 Jul 9.62	103.10	119.33	7575	1029	1363	0.022	106

2021 Dec 12.96	102.87	106.52	7444	975	1156	0.012	98

1976-77 EZ	[18429]				1985 May 7.00	102.54	119.52	8038	1473	1845	0.023	87

2004 Jul 6.48	103.26	119.42	8033	1472	1837	0.023	208

2021 Dec 12.79	102.68	119.38	8031	1469	1837	0.023	116

1976-77 FA	[18463]				1985 Apr 20.96	102.12	117.78	7960	1503	1659	0.010	238

2004 Jul 9.17	102.51	117.70	7956	1501	1654	0.010	134

2021 Dec 12.83	102.35	117.68	7955	1501	1652	0.009	295

D	1976-77 FB	[18466]	2014 Jan 14	13683 days		1976 Nov 3.57	102.95	120.18	8068	1420	1959	0.033	50

2004 Jul 8.27	103.33	118.83	7552	1074	1272	0.013	104

2014 Jan 12.34	102.95	92.78	6790	373	449	0.006	355

1976-77 FC	[18540]				1984 Feb 18.69	50.69	92.85	6793	333	496	0.012	113

2004 Jul 9.17	103.81	119.30	8028	1282	2017	0.046	230

2021 Dec 12.77	103.83	117.58	7951	1208	1936	0.046	262

1976-77 FD	[18591]				1976 Mar 22.38	101.76	139.25	8900	1447	3595	0.121	321

2004 Jul 8.10	101.36	135.50	8739	1276	3445	0.124	15

2021 Dec 12.63	100.99	136.23	8771	1397	3387	0.113	270

1976-77 FE	[18599]				1976 Jan 2.29	100.84	130.65	8529	1329	2971	0.096	49

2004 Jul 9.68	100.79	123.87	8231	1144	2561	0.086	318

2021 Dec 12.88	100.61	121.75	8137	1216	2302	0.067	72

1976-77 FF	[18600]				1983 Dec 7.13	102.02	131.92	8584	1523	2888	0.079	152

2004 Jul 8.12	102.05	131.98	8587	1529	2889	0.079	76

2021 Dec 12.85	102.04	131.92	8584	1525	2886	0.079	197

D	1976-77 FG	[18677]	2002 Dec 17	9637 days		1987 Dec 8.14	104.20	124.25	8249	1456	2284	0.050	175

2002 Dec 16.46	104.10	95.07	6900	475	568	0.007	113

1976-77 FH	[19000]				1985 May 7.92	102.02	117.40	7942	1502	1626	0.008	158

2004 Jul 9.08	102.39	117.38	7942	1501	1625	0.008	307

2021 Dec 12.85	102.37	117.38	7942	1500	1625	0.008	359

1976-77 FJ	[19306]				1985 Jul 27.99	102.20	118.57	7995	1500	1733	0.015	122

2004 Jul 7.62	102.06	118.52	7993	1498	1730	0.015	166

2021 Dec 13.03	102.03	118.48	7991	1498	1727	0.014	77

1976-77 FK	[19316]				1985 May 3.98	102.18	119.73	8048	1498	1840	0.021	31

2004 Jul 6.58	102.10	119.67	8045	1498	1834	0.021	208

2021 Dec 11.57	102.12	119.63	8043	1495	1834	0.021	28

D	1976-77 FL	[19858]	2011 May 2	12695 days		1989 Sep 17.80	102.23	126.37	8342	970	2957	0.119	178

2004 Jul 10.49	102.82	108.40	7531	914	1391	0.032	238

2011 May 1.26	103.62	93.22	6811	418	446	0.002	265

1976-77 FM	[20012]				1986 Apr 14.95	102.07	114.60	7816	1395	1480	0.005	72

2004 Jul 9.23	102.05	112.63	7726	1299	1396	0.006	315

2021 Dec 12.51	102.07	111.83	7689	1260	1361	0.007	97

1976-77 FN	[20051]				1989 Jan 21.80	102.53	118.68	8000	1503	1740	0.015	134

2004 Jul 3.62	102.84	118.60	7997	1498	1739	0.015	260

2021 Dec 12.88	102.33	118.40	7995	1493	1740	0.015	12

1976-77 FP	[20088]				1985 Apr 19.99	102.05	117.50	7947	1502	1635	0.008	206

2004 Jul 4.07	102.44	117.42	7944	1503	1627	0.008	0

2021 Dec 12.88	102.30	117.38	7942	1496	1631	0.008	50

1976-77 FQ	[20309]				1989 May 11.66	102.61	119.55	8039	1501	1820	0.020	102

2004 Jul 10.37	102.50	119.30	8028	1492	1807	0.020	19

2021 Dec 12.70	102.64	119.17	8022	1489	1797	0.019	11

1976-77 FR	[20349]				1986 Jun 22.15	102.57	127.45	8390	1469	2553	0.065	132

2004 Jul 10.10	102.55	127.22	8380	1472	2530	0.063	143

2021 Dec 12.87	102.54	127.08	8373	1472	2518	0.062	100

1976-77 FS	[27727]				2003 Apr 13.56	102.63	123.27	8205	1484	2169	0.042	166

2004 Jul 4.46	102.60	123.27	8205	1488	2164	0.041	179

2021 Dec 13.08	102.63	123.25	8204	1487	2184	0.041	236

1976-77 FT	[27728]				2003 Apr 13.39	102.51	122.23	8159	1480	2101	0.039	302

2004 Jul 5.30	102.45	122.20	8157	1456	2102	0.040	297

2021 Dec 12.88	102.47	121.68	8135	1431	2081	0.040	356

1976-77 FU	[28979]				2006 Mar 19.68	102.00	131.57	8569	1505	2876	0.080	277

2021 Dec 12.90	102.01	131.50	8567	1505	2871	0.080	108

1976 77 FV	[40752]				2015 Aug 7.97	102.18	126.58	8352	1501	2445	0.056	14

2021 Dec 11.16	102.19	126.58	8351	1502	2443	0.056	102

1976 77 FW	[40753]				2015 Aug 6.45	101.94	117.07	7928	1499	1599	0.006	21

2015 Nov 20.43	101.94	117.07	7928	1500	1597	0.006	186

1976 77 FX	[40754]				2015 Aug 7.95	101.99	117.55	7949	1496	1645	0.009	7

2021 Dec 13.13	102.29	117.53	7949	1496	1644	0.009	156

1976 77 FY	[40755]				2015 Aug 7.46	101.62	115.72	7866	1472	1504	0.002	161

2021 Dec 11.13	101.83	115.70	7865	1474	1499	0.002	72

1976 77 FZ	[40756]				2015 Aug 4.88	102.03	117.45	7945	1505	1628	0.008	270

2021 Dec 12.70	102.33	117.45	7945	1505	1628	0.008	57

1976 77 GA	[40757]				2015 Aug 5.20	101.38	114.82	7825	1442	1451	0.0006	322

2021 Dec 11.63	101.69	114.78	7824	1441	1450	0.0005	75

1976 77 GB	[40758]				2015 Aug 8.23	102.01	117.53	7948	1499	1640	0.009	359

2021 Dec 12.77	102.29	117.52	7948	1500	1639	0.009	149

1976 77 GC	[40759]				2015 Aug 9.79	102.23	113.73	7776	1169	1626	0.029	93

2021 Dec 11.28	102.24	113.72	7775	1169	1625	0.029	279

1976 77 GD	[40760]				2015 Aug 8.30	103.40	124.57	8263	1496	2272	0.047	149

2015 Oct 10.31	103.32	124.57	8263	1500	2268	0.047	56

1976 77 GE	[40761]				2015 Aug 7.06	102.27	118.95	8013	1492	1776	0.018	28

2021 Dec 9.32	102.37	118.93	8011	1490	1775	0.018	321

1976 77 GF	[40762]				2015 Aug 10.60	102.35	121.72	8136	1489	2025	0.033	80

2021 Dec 12.60	102.34	121.70	8135	1491	2022	0.033	230

1976 77 GG	[40763]				2015 Aug 12.31	101.49	114.58	7815	1414	1458	0.003	62

2021 Dec 12.74	101.42	114.50	7811	1412	1453	0.003	189

1976 77 GH	[40764]				2015 Aug 2.81	101.70	116.08	7883	1503	1505	0.00008	267

2021 Dec 12.17	101.97	116.07	7882	1503	1504	0.00009	277

1976 77 GJ	[40765]				2015 Aug 9.19	101.68	115.72	7866	1466	1510	0.003	323

2021 Dec 12.34	102.00	115.65	7864	1463	1507	0.003	264

1976 77 GK	[40766]				2015 Aug 7.93	101.88	117.73	7958	1497	1661	0.010	125

2021 Dec 10.73	102.15	117.73	7957	1497	1660	0.010	277

1976 77 GL	[40767]				2015 Jul 4.81	102.11	117.88	7965	1495	1676	0.011	318

1976 77 GM	[40768]				2015 Aug 9.35	101.43	114.17	7796	1378	1457	0.005	31

2021 Dec 11.71	101.28	114.07	7792	1373	1454	0.005	89

1976 77 GN	[40769]				2015 Aug 3.00	101.69	115.95	7877	1491	1506	0.0009	297

2021 Dec 8.88	101.86	115.92	7876	1490	1504	0.0008	242

1976 77 GP	[40770]				2015 Aug 3.88	101.42	114.82	7826	1407	1487	0.005	1

2021 Dec 10.18	101.60	114.77	7823	1407	1482	0.005	141

1976 77 GQ	[40771]				2015 Aug 7.50	101.72	116.17	7887	1496	1520	0.002	46

2021 Dec 12.87	102.98	116.15	7886	1495	1519	0.002	20

1976 77 GR	[40772]				2015 Aug 4.56	102.28	119.50	8037	1507	1810	0.019	53

2021 Dec 12.83	102.15	119.50	8037	1507	1810	0.019	23

1976 77 GS	[40773]				2015 Aug 7.26	102.00	117.35	7940	1497	1626	0.008	231

2021 Dec 5.13	102.24	117.33	7940	1495	1627	0.008	12

Cosmos 848 fragments; 2 pieces, both have decayed.

D	1976-82 C	[09328]	1976 Aug 17	5 days		1976 Aug 13.05	62.79	89.60	6634	206	304	0.007	93

1976 Aug 14.17	62.81	89.18	6613	205	263	0.004	108

D	1976-82 E	[09375]	1976 Aug 24	12 days		1976 Aug 16.65	62.80	89.23	6615	203	270	0.005	88

1976 Aug 21.58	62.55	88.12	6559	124	238	0.009	319

AMS 1 fragments; 6 fragments, 2 have decayed.

1976 91 B	[09419]				No elements available

1976-91 C	[09420]				1976 Sep 19.99	98.70	101.53	7210	817	846	0.002	159

1977 Jun 10.99	98.70	101.52	7209	815	846	0.002	120

D	1976-91 D	[09474]	1980 Sep 20	1470 days			98.70	101.50		822	837	from Satcat

D	1976-91 E	[09483]	1983 Aug 24	2538 days		No elements available

1976-91 F	[09484]				No elements available

1976-91 G	[09518]				No elements available

Cosmos 862 fragments; 12 pieces, 7 have decayed.

Cosmos 862 was the first of a new class of operational satellites in highly elliptical, semi-synchronous orbits, which experienced a total of 16 fragmentations during the period 1977-1986. Due to the nature of these orbits, which result in high altitudes over the Northern Hemisphere where most surveillance sensors are located, debris detection and tracking is extremely difficult. Only the largest fragments can be seen. Cosmos 862 spacecraft were equipped with self-destruct packages in the event that spacecraft control was lost; this was the cause of break-ups until the explosives were removed after Cosmos 1481. First event occurred 1977 Mar 15 at 12:56 UT near 39º 114ºE.

1976-105 E	[09888]				1977 Mar 27.02	63.03	719.82	26606	704	39750	0.734	318

1992 Aug 10.33	64.41	718.95	26585	863	39550	0.727	190

D	1976-105 F	[09889]	2014 May 29	13733 days		1977 Mar 27.00	63.14	718.12	26564	772	39559	0.731	318

1994 Apr 30.47	64.25	718.52	26574	484	39906	0.742	174

2014 May 29.81	61.80	96.38	6964	99	1072	0.070	56

1976-105 G	[09890]				1977 Apr 9.98	63.16	717.90	26559	822	39538	0.729	319

1979 Apr 10.31	65.85	718.73	26579	1468	38993	0.705	310

D	1976-105 H	[09891]	1999 Jul 26	8312 days		1977 Mar 24.02	63.08	718.02	26576	775	39619	0.731	318

1993 Mar 21.72	64.26	118.63	26577	688	39709	0.734	182

D	1976-105 J	[09892]	1995 Feb 13	6688 days		1977 Mar 26.99	63.10	717.43	26547	783	39555	0.730	318

2004 Jul 5.09	66.88	718.85	26582	3958	36449	0.611	107

2010 Oct 29.49	65.37	717.32	26544	1654	38677	0.697	51

D	1976-105 K	[09893]	1994 Jun 10	6440 days		1977 Mar 29.95	62.98	716.42	26522	586	39701	0.737	317

1977 Apr 7.91	62.95	716.47	26523	585	39704	0.737	317

D	1976-105 L	[09894]	1993 May 22	6056 days		1977 Mar 27.00	63.17	715.35	26496	785	39450	0.730	319

1978 Aug 4.93	63.87	702.55	26179	558	39042	0.735	325

1976-105 M	[09895]				1977 Mar 27.02	63.13	719.85	26607	788	39668	0.731	319

1979 Apr 10.31	65.85	718.73	26579	1468	38933	0.705	310

1976-105 N	[09896]				1977 Mar 24.08	63.14	724.52	26722	794	39892	0.732	319

2004 Jul 3.14	67.99	721.43	26646	4342	36192	0.598	99

2021 Jul 17.73	68.97	750.77	26629	2992	37509	0.648	311

1976-105 P	[09902]				1977 May 6.93	63.53	729.08	26834	655	40256	0.738	317

1993 Jan 4.72	64.56	727.17	26787	1112	39704	0.720	193

D	1976 105 Q	[39752]	2014 Jun 06	13741 days		2014 Jun	61.74	108.06		119	2155	from Satcat

D	1976 105 R	[39753]	2014 May 22	13724 days		2014 May	61.89	117.79		109	3054	from Satcat

Cosmos 863 fragments; 7 pieces, all have decayed.

D	1976-106 C	[09501]	1976 Oct 29	4 days		1976 Oct 25.84	62.82	90.20	6663	177	391	0.016	86

1976 Oct 28.58	62.82	88.98	6603	172	276	0.008	86

D	1976-106 D	[09502]	1976 Oct 26	1 day		1976 Oct 25.84	62.74	89.30	6618	172	307	0.010	76

1976 Oct 26.21	62.77	88.78	6593	163	266	0.008	69

D	1976-106 F	[09522]	1976 Nov 7	13 days		1976 Nov 4.46	62.81	89.30	6618	156	324	0.013	71

1976 Nov 6.43	62.81	88.15	6562	152	214	0.005	71

D	1976-106 G	[09524]	1976 Nov 7	13 days		1976 Nov 5.46	62.81	89.37	6621	164	321	0.012	77

1976 Nov 6.07	62.83	89.00	6603	166	283	0.009	76

D	1976-106 H	[09527]	1976 Nov 9	15 days		1976 Nov 6.35	62.75	91.08	6706	204	452	0.018	24

D	1976-106 J	[09528]	1976 Nov 10	16 days		1976 Nov 6.35	62.72	91.20	6712	203	464	0.019	29

1976 Nov 6.61	62.82	89.82	6644	185	346	0.012	29

D	1976-106 K	[09529]	1976 Nov 7	13 days		1976 Nov 5.96	63.02	89.28	6617	204	273	0.005	28

Cosmos 866 fragments; 4 pieces, all have decayed.

D	1976-110 C	[09534]	1976 Nov 16	5 days		1976 Nov 11.81	65.02	88.20	6564	151	220	0.005	3

D	1976-110 D	[09535]	1976 Nov 14	3 days		1976 Nov 11.88	65.08	88.70	6589	173	247	0.006	60

1976 Nov 12.12	65.03	88.93	6585	169	245	0.006	65

D	1976-110 E	[09536]	1976 Nov 13	2 days		1976 Nov 11.82	64.94	89.62	6634	180	331	0.011	62

1976 Nov 12.31	64.98	89.20	6614	172	298	0.010	53

D	1976-110 G	[09553]	1976 Nov 23	12 days		1976 Nov 22.71	64.98	87.82	6545	157	176	0.001	93

Cosmos 867 fragments; 7 pieces, all have decayed.

D	1976-111 C	[09555]	1976 Dec 16	23 days		1976 Nov 23.86	62.79	90.65	6685	251	363	0.008	111

1976 Dec 2.12	62.78	89.43	6625	228	265	0.003	114

D	1976-111 D	[09556]	1976 Dec 8	15 days		1976 Nov 23.86	62.85	91.15	6709	250	411	0.012	117

1976 Dec 4.19	62.83	90.07	6656	234	321	0.006	116

D	1976-111 E	[09566]	1976 Dec 11	18 days		1976 Nov 29.74	62.78	90.95	6700	244	398	0.011	107

1976 Dec 6.64	62.77	89.82	6644	227	303	0.006	113

D	1976-111 G	[09583]	1977 May 26	184 days		1976 Dec 5.54	62.83	91.88	6746	350	384	0.002	99

1977 May 22.86	62.80	88.97	6602	222	224	0.0002	346

D	1976-111 H	[09584]	1977 Mar 20	117 days		1976 Dec 6.12	62.86	92.05	6753	352	397	0.003	78

1977 Mar 18.13	62.81	90.55	6680	276	327	0.004	337

D	1976-111 J	[09585]	1977 Jul 7	226 days		1977 Mar 13.18	62.80	91.60	6731	245	460	0.016	133

1977 Jun 15.79	62.74	89.45	6626	230	265	0.003	144

D	1976-111 K	[09586]	1977 Mar 5	102 days		1976 Dec 6.44	62.82	92.07	6755	348	404	0.004	96

1977 Feb 21.42	62.81	90.07	6656	273	282	0.0006	117

Cosmos 880 (D-BC) and 2nd stage (C) fragments; 49 pieces, all have decayed

Cosmos 880 was the second spacecraft of the Cosmos 839-type to experience a fragmentation 1978 Nov 27 at 17:03 UT near 65S 306ºE. Although these satellites are used in conjunction with the Cosmos 249-type spacecraft which are deliberately fragmented, the cause of the Cosmos 839-type events appears to be unrelated. In the case of Cosmos 880, 23 months elapsed since its test with a Cosmos 249-type spacecraft. Russian officials have determined that battery malfunctions were the cause of these events.

D	1976-120 C	[09605]	1981 Nov 1	1788 days		1976 Dec 16.59	65.85	96.45	6967	559	617	0.004	5

1981 Nov 1.33	65.77	87.58	6534	151	159	0.0006	14

D	1976-120 D	[11178]	1981 Jun 12	1646 days		1979 Jan 3.11	65.86	97.05	6996	552	683	0.009	259

1981 Jun 10.16	65.81	88.57	6582	196	211	0.001	236

D	1976-120 E	[11179]	1980 Mar 6	1183 days		1979 Jan 3.14	65.85	96.48	6969	549	632	0.006	278

1980 Feb 27.47	65.81	90.97	6701	313	331	0.001	2

D	1976-120 F	[11180]	1979 Feb 25 A	808 days		1979 Jan 1.16	65.85	96.57	6972	542	545	0.007	241

1979 Jan 22.89	65.84	96.03	6947	529	609	0.006	230

D	1976-120 G	[11181]	1979 Jul 20	953 days		1979 Jan 3.17	65.85	95.73	6933	528	580	0.004	312

1979 Jun 27.98	65.80	91.83	6743	356	373	0.001	234

D	1976-120 H	[11182]	1979 Oct 27	1052 days		1979 Jan 3.13	65.85	96.97	6992	555	671	0.008	241

1979 Aug 16.23	65.79	93.88	6843	455	475	0.001	152

D	1976-120 J	[11183]	1979 Apr 14	856 days		1979 Jan 3.25	65.86	95.15	6905	509	543	0.002	1

1979 Mar 10.36	65.82	92.70	6786	402	412	0.0007	309

D	1976-120 K	[11184]	1979 Jul 6	939 days		1979 Jan 3.26	65.85	97.48	7017	555	721	0.012	243

1979 Jun 27.74	65.81	91.68	6736	336	378	0.003	199

D	1976-120 L	[11185]	1979 Apr 5	847 days		1979 Jan 3.27	65.85	95.42	6917	515	562	0.003	343

1979 Mar 26.95	65.83	91.08	6706	315	339	0.002	224

D	1976-120 M	[11186]	1980 Nov 13	1435 days		1979 Jan 3.16	65.85	96.57	6973	553	635	0.006	269

1980 Nov 2.66	65.79	89.05	6606	220	235	0.001	303

D	1976-120 N	[11187]	1979 Apr 2	844 days		1979 Jan 3.26	65.86	95.25	6909	497	564	0.005	353

1979 Mar 20.83	65.84	92.48	6775	383	410	0.002	305

D	1976-120 P	[11188]	1979 Mar 5	816 days		1979 Jan 3.17	65.86	94.75	6885	479	533	0.004	25

1979 Feb 25.30	65.84	92.42	6771	373	412	0.003	27

D	1976-120 Q	[11189]	1979 Feb 23	806 days		1979 Jan 3.15	65.85	95.82	6937	537	579	0.003	257

1979 Feb 6.72	65.85	94.15	6856	469	486	0.001	281

D	1976-120 R	[11190]	1979 Mar 26	837 days		1979 Jan 3.15	65.81	97.28	7008	553	705	0.011	239

1979 Mar 20.42	65.85	93.12	6806	409	445	0.003	187

D	1976-120 S	[11191]	1979 Jun 16	919 days		1979 Jan 3.28	65.83	96.87	6988	546	672	0.009	224

1979 Feb 21.76	65.81	94.90	6892	501	526	0.002	216

D	1976-120 T	[11192]	1979 Jul 5	938 days		1979 Jan 3.23	65.85	96.30	6960	546	617	0.005	278

1979 Jul 2.09	65.83	91.45	6724	332	359	0.002	212

D	1976-120 U	[11193]	1991 Sep 3	5381 days			65.79	87.62		150	164	from Satcat

D	1976-120 V	[11194]	1979 Jul 12	945 days		1979 Jan 3.17	65.87	96.17	6953	547	602	0.004	281

1979 Jun 9.47	65.78	92.92	6796	403	430	0.002	222

D	1976-120 W	[11195]	1979 Feb 23	806 days		1979 Jan 3.18	65.86	95.22	6908	512	546	0.002	330

1979 Feb 14.66	65.85	93.25	6812	430	437	0.0005	327

D	1976-120 X	[11196]	1979 Apr 7	849 days		1979 Jan 3.16	65.86	95.52	6922	515	571	0.004	333

1979 Mar 9.96	65.84	93.95	6846	448	486	0.003	310

D	1976-120 Y	[11197]	1979 Mar 31	842 days		1979 Jan 3.07	65.86	95.45	6919	512	568	0.004	338

1979 Mar 8.32	65.85	93.58	6828	434	465	0.002	314

D	1976-120 Z	[11198]	1979 Mar 15	826 days		1979 Jan 3.09	65.85	95.17	6905	500	553	0.004	4

1979 Mar 5.65	65.83	93.15	6807	414	442	0.002	331

D	1976-120 AA	[11199]	1979 Feb 18	801 days		1979 Jan 3.28	65.85	94.63	6879	476	525	0.004	38

1979 Jan 21.69	65.85	93.97	6847	453	483	0.002	20

D	1976-120 AB	[11200]	1979 Jul 10	943 days		1979 Jan 3.13	65.86	96.92	6990	542	681	0.010	277

1979 Jun 6.41	65.85	93.33	6816	421	454	0.002	201

D	1976-120 AC	[11201]	1979 Dec 9	1095 days		1979 Jan 3.12	65.85	95.90	6941	528	595	0.005	320

1979 Dec 7.40	65.82	90.17	6662	276	290	0.001	143

D	1976-120 AD	[11202]	1979 Jul 13	946 days		1979 Jan 3.06	65.83	97.13	7000	552	691	0.010	260

1979 Jun 19.84	65.76	92.82	6791	404	421	0.001	203

D	1976-120 AE	[11203]	1979 Sep 10	1005 days		1979 Jan 3.26	65.85	96.60	6974	553	639	0.006	260

1979 Aug 15.58	65.84	91.72	6738	352	366	0.001	277

D	1976-120 AF	[11204]	1991 Aug 1	5348 days		1979 Jan 3.20	65.85	96.70	6980	559	643	0.006	243

1991 Jul 31.89	65.83	87.85	6547	157	179	0.002	262

D	1976-120 AG	[11205]	1990 Jul 11	4962 days		1979 Jan 3.26	65.83	96.50	6969	537	644	0.008	297

1990 Jul 11.40	65.80	87.48	6528	141	159	0.001	258

D	1976-120 AH	[11206]	1979 Feb 26 A	809 days		1979 Jan 2.09	65.86	96.53	6971	545	639	0.007	241

1979 Jan 22.88	65.84	95.98	6945	532	600	0.005	228

D	1976-120 AJ	[11207]	1985 Nov 20	3268 days		1979 Jan 3.23	65.84	95.90	6941	558	565	0.0005	227

1985 Nov 18.56	65.81	88.22	6565	179	193	0.001	265

D	1976-120 AK	[11208]	1979 Nov 11	1067 days		1979 Jan 3.16	65.84	96.72	6980	554	649	0.007	261

1979 Oct 27.78	65.80	92.68	6785	398	414	0.001	20

D	1976-120 AL	[11209]	1982 Dec 1	2183 days		1979 Jan 3.24	65.84	95.57	6924	516	575	0.004	356

1982 Nov 29.59	65.82	88.13	6561	178	187	0.0007	262

D	1976-120 AM	[11210]	1983 Jul 30	2424 days		1979 Jan 3.25	65.83	95.77	6934	534	577	0.003	341

1983 Jul 30.06	65.81	87.55	6532	143	163	0.002	272

D	1976-120 AN	[11211]	1979 Mar 29	840 days		1979 Jan 3.10	65.86	95.53	6923	519	569	0.004	328

1979 mar 26.35	65.83	91.33	6718	328	352	0.002	229

D	1976-120 AP	[11212]	1984 Jul 15	2775 days		1979 Jan 328	65.84	96.02	6946	521	613	0.007	322

1984 Jul 14.90	65.81	87.18	6514	126	144	0.001	271

D	1976-120 AQ	[11213]	1990 Nov 22	5096 days		1979 Jan 3.25	65.86	96.63	6976	540	655	0.008	290

1990 Nov 22.89	65.82	87.42	6525	142	151	0.0007	204

D	1976-120 AR	[11214]	1991 Sep 15	5393 days		1979 Jan 3.23	65.86	96.78	96.78	552	657	0.008	273

1981 Sep 14.91	65.84	88.07	6558	168	189	0.002	273

D	1976-120 AS	[11215]	1979 May 24	896 days		1979 Jan 3.24	65.86	96.87	6987	550	667	0.008	262

1979 May 7.77	65.84	92.92	6796	411	424	0.001	233

D	1976-120 AT	[11216]	2001 Dec 9	9131 days		1979 Jan 3.24	65.85	97.35	7010	556	707	0.011	259

2001 Dec 8.10	65.83	88.43	6575	192	201	0.0007	206

2001 Dec 9.75	65.81	87.32	6520	137	146	0.0006	253

D	1976-120 AU	[11217]	1989 Dec 24	4763 days		1979 Jan 3.27	65.86	96.37	6963	557	611	0.004	264

1989 Dec 24.08	65.84	87.63	6536	154	160	0.0005	282

D	1976-120 AV	[11218]	1980 Feb 5	1153 days		1979 Jan 3.26	65.85	95.77	6934	524	586	0.004	333

1980 Jan 30.80	65.82	89.37	6622	235	251	0.001	4

D	1976-120 AW	[11219]	1982 Nov 19	2171 days		1979 Jan 3.23	65.86	95.70	6931	515	590	0.005	341

1982 Nov 18.87	65.83	88.57	6582	197	210	0.001	266

D	1976-120 AX	[11220]	1983 May 19	2352 days		1979 Jan 3.27	65.85	95.63	6928	536	562	0.002	17

1983 May 19.21	65.82	87.40	6524	137	154	0.001	299

D	1976-120 AY	[11221]	2000 Sep 26	8692 days		1979 Jan 7.07	65.85	97.28	7007	548	709	0.011	272

2000 Sep 25.69	65.82	87.43	6526	140	155	0.001	308

D	1976-120 AZ	[11222]	1979 Jun 16	919 days		1979 Jan 3.12	65.84	96.88	6988	550	668	0.008	253

1979 Mar 16.94	65.81	95.58	6925	512	581	0.005	219

D	1976-120 BA	[11223]	1991 Aug 14	5361 days		1979 Jan 7.62	65.83	97.13	7000	557	686	0.009	255

1991 Aug 14.01	65.79	87.63	6536	151	163	0.0009	232

D	1976-120 BB	[11224]	1979 Jun 3	906 days		1979 Jan 4.98	65.88	96.15	6953	547	601	0.004	205

1979 May 19.60	65.88	92.27	6764	382	389	0.0005	165

D	1976-120 BC	[11225]	1979 Aug 19	983 days		1979 Jan 5.85	65.84	95.37	6915	506	566	0.004	357

1979 Aug 10.66	65.82	90.50	6680	286	316	0.002	272

Cosmos 885 fragments; 17 pieces, all have decayed.

Analyses indicate that the Cosmos 885 payload is the most likely debris source.

D	1976-124 C	[09626]	1977 Oct 29	316 days		1977 Feb 16.99	65.82	94.35	6866	467	507	0.003	217

1977 Oct 9.43	65.81	91.95	6748	369	370	0.00005	225

D	1976-124 D	[09897]	1977 Nov 22	340 days		1977 Mar 29.54	65.84	94.32	6864	458	513	0.004	291

1977 Nov 4.06	65.82	91.37	6720	341	341	0	58

D	1976-124 E	[09901]	1977 Nov 11	329 days		1977 Apr 2.48	65.84	94.33	6865	460	513	0.004	289

1977 Oct 27.52	65.83	91.58	6731	351	353	0.0002	70

D	1976-124 F	[09914]	1977 Dec 9	357 days		1977 Apr 24.76	65.85	94.35	6866	461	513	0.004	277

1977 Oct 17.76	65.84	93.02	6801	419	426	0.0005	211

D	1976-124 G	[09915]	1977 Nov 29	347 days		1977 May 13.43	65.79	94.27	6862	458	508	0.004	273

1977 Nov 26.26	65.76	90.30	6668	289	289	0	130

D	1976-124 H	[09916]	1977 Nov 16	334 days		1977 Apr 14.27	65.84	94.27	6862	451	515	0.005	286

1977 Oct 26.53	65.81	92.00	6752	373	373	0	332

D	1976-124 J	[09917]	1977 Nov 5	323 days		1977 Apr 15.38	65.84	94.18	6858	445	514	0.005	288

1977 Oct 25.00	65.82	91.32	6718	339	339	0	27

D	1976-124 K	[09918]	1977 Nov 20	338 days		1977 Apr 24.23	65.83	94.25	6861	452	512	0.004	281

1977 Nov 12.30	65.81	91.07	6705	327	327	0	84

D	1976-124 L	[09919]	1977 Nov 10	328 days		1977 Apr 13.95	65.85	94.22	6859	447	515	0.005	287

1977 Nov 1.46	65.82	90.77	6690	312	312	0	50

D	1976-124 M	[09920]	1977 Dec 22	370 days		1977 Apr 15.39	65.84	94.50	6873	473	515	0.003	275

1977 Nov 26.37	65.83	91.95	6749	365	375	0.0007	152

D	1976-124 N	[09922]	1977 Nov 16	334 days		1977 Apr 30.77	65.89	94.23	6860	451	511	0.004	275

1977 Nov 10.50	65.88	90.78	6692	313	313	0	77

D	1976-124 P	[09923]	1977 Dec 9	357 days		1977 Apr 16.77	65.83	94.45	6871	470	514	0.003	279

1977 Dec 3.65	65.80	90.95	6700	315	327	0.0009	222

D	1976-124 Q	[09924]	1977 Dec 14	362 days		1977 Apr 16.44	65.84	94.43	6869	467	515	0.003	279

1977 Nov 12.93	65.83	92.13	6758	379	379	0	82

D	1976-124 R	[09925]	1977 Nov 22	340 days		1977 May 24.88	65.81	94.18	6858	453	505	0.004	265

1977 Nov 14.53	65.79	91.30	6717	334	343	0.0006	170

D	1976-124 S	[09926]	1977 Dec 1	349 days		1977 Apr 16.44	65.87	94.32	6864	456	515	0.004	283

1977 Nov 5.88	65.86	91.52	6744	365	365	0	61

D	1976-124 T	[09999]	1977 Oct 17	304 days		1977 May 12.46	65.86	93.40	6820	405	478	0.005	273

1977 Oct 12.22	65.84	90.43	6675	288	304	0.001	143

D	1976-124 U	[10391]	1978 Jan 11	390 days		1977 Oct 3.36	65.87	93.95	6846	450	485	0.003	225

1977 Dec 28.54	65.85	91.52	6728	339	359	0.001	326

Cosmos 886 fragments; 77 pieces, 15 have decayed

Cosmos 886 was launched on a two-revolution rendezvous with Cosmos 880. After a close approach, Cosmos 886 continued on before its warhead was intentionally fired 1976 Dec 27 at 18:40 UT near 65ºS 210ºE. Cosmos 886 was part of test series begun with Cosmos 249.

D	1976 126 B	[09643]	1976 Dec 30	3 days		1976 Dec 29.8	62.74	91.56	6730	132	571	0.033	50

D	1976-126 C	[09644]	1976 Dec 31	4 days

1976-126 E	[09648]				2004 Jul 5.57	65.80	100.93	7181	460	1145	0.048	18

1976-126 F	[09649]				2004 Jul 4.46	65.92	113.73	7776	677	2118	0.093	129

1976-126 G	[09650]				2004 Jul 5.85	65.82	109.60	7587	499	1917	0.093	49

1976-126 H	[09651]				2004 Jul 5.20	65.80	109.60	7587	553	1863	0.086	84

1976-126 J	[09652]				2004 Jul 6.32	65.83	112.00	7697	596	2041	0.094	184

1976-126 K	[09653]				2004 Jul 6.25	65.81	109.95	7603	570	1879	0.086	114

1976-126 L	[09654]				2004 Jul 6.22	65.77	109.15	7566	583	1793	0.080	96

1976-126 M	[09655]				2004 Jul 6.24	65.80	106.93	7463	480	1689	0.081	305

1976-126 N	[09656]				2004 Jul 4.89	65.83	112.47	7718	633	2046	0.092	236

D	1976-126 P	[09657]	1991 Jan 6	5123 days

D	1976-126 Q	[09719]	1978 Jul 11	561 days

D	1976-126 R	[09720]	1981 Oct 9	1747 days

1976-126 S	[09721]				2004 Jul 5.33	65.84	113.07	7746	531	2204	0.108	168

1976-126 T	[09722]				2004 Jul 6.51	65.76	115.77	7869	826	2154	0.084	252

1976-126 U	[09723]				2004 Jul 6.52	65.77	112.17	7704	734	1917	0.077	23

1976-126 V	[09724]				2004 Jul 5.29	65.81	110.22	7615	586	1888	0.085	134

D	1976-126 W	[09725]	1992 Dec 21	5838 days

1976-126 X	[09797]				2004 Jul 4.40	65.82	113.17	7750	636	2107	0.095	289

1976-126 Y	[09798]				2004 Jul 3.51	65.76	105.83	7412	931	1136	0.014	302

1976-126 Z	[09799]				2004 Jul 4.48	65.60	112.88	7738	576	2142	0.101	124

1976-126 AA	[09807]				2004 Jul 5.53	65.81	105.05	7375	516	1477	0.065	260

D	1976-126 AB	[09815]	1999 Oct 4	8316 days

1976-126 AC	[09816]				2004 Jul 6.46	65.81	106.53	7444	502	1630	0.076	297

D	1976-126 AD	[09817]	1982 Jul 12	2023 days

1976-126 AE	[09818]				2004 Jul 5.34	65.78	112.52	7256	511	1244	0.051	187

1976-126 AF	[09819]				2004 Jul 5.42	65.91	105.08	7377	525	1471	0.064	58

1976-126 AG	[09820]				2004 Jul 5.59	65.80	120.78	8095	1016	2416	0.086	100

1976-126 AH	[09821]				2004 Jul 5.91	65.78	103.55	7305	513	1340	0.057	233

1976-126 AJ	[09822]				2004 Jul 5.29	65.80	112.08	7701	568	2077	0.098	239

1976-126 AK	[09823]				2004 Jul 4.88	65.80	111.70	7684	566	2044	0.096	210

1976-126 AL	[09824]				2004 Jul 5.63	65.82	109.62	7587	500	1918	0.093	47

D	1976-126 AM	[09825]	1982 Mar 12	1901 days

1976-126 AN	[09826]				2004 Jul 5.26	65.85	108.97	7557	546	1812	0.084	52

1976-126 AP	[09827]				2004 Jul 4.96	65.81	103.52	7304	519	1331	0.056	215

D	1976-126 AQ	[09828]	2002 Jan 5	9140 days		2002 Jan 5.81	65.73	89.15	6611	220	244	0.002	63

1976-126 AR	[09951]				2004 Jul 5.80	65.80	109.80	7596	562	1872	0.086	107

D	1976-126 AS	[09952]	1980 Oct 11	1415 days

1976-126 AT	[09953]				2004 Jul 5.21	65.82	110.90	7646	575	1960	0.091	132

1976-126 AU	[09954]				2004 Jul 6.23	65.70	110.95	7649	568	1972	0.092	132

1976-126 AV	[09955]				2004 Jul 4.34	65.84	114.10	7793	572	2256	0.108	250

1976-126 AW	[09956]				2004 Jul 5.82	65.80	116.52	7903	793	2255	0.093	144

1976-126 AX	[09957]				2004 Jul 5.64	65.78	101.67	7216	526	1149	0.043	321

1976-126 AY	[09958]				2004 Jul 4.45	65.87	114.60	7816	719	2156	0.092	296

D	1976-126 AZ	[09959]	1982 Jun 20	2001 days

1976-126 BA	[09960]				2004 Jul 4.92	65.87	112.62	7726	654	2040	0.090	179

1976-126 BB	[09961]				2004 Jul 5.68	65.82	106.70	7453	534	1614	0.072	330

1976-126 BC	[09962]				2004 Jul 6.14	65.78	106.98	7466	544	1630	0.073	7

1976-126 BD	[09963]				2004 Jul 5.49	65.80	109.47	7581	547	1857	0.086	76

1976-126 BE	[09964]				2004 Jul 5.86	65.81	110.90	7646	597	1938	0.088	178

1976-126 BF	[09965]				2004 Jul 4.64	65.81	118.77	8004	912	2338	0.089	323

1976-126 BG	[09966]				2004 Jul 5.77	65.79	118.28	7526	586	1709	0.075	81

D	1976-126 BH	[09967]	1991 Mar 5	5181 days

D	1976-126 BJ	[10396]	1984 Jan 8	2568 days

1976-126 BK	[13507]				2004 Aug 13.96	65.75	120.83	8096	1005	2431	0.088	148

D	1976-126 BL	[13683]	2002 Jun 17	9303 days		2002 Jun 15.80	65.59	89.73	6639	240	282	0.003	296

1976-126 BM	[13943]				2004 Jul 8.89	65.59	102.65	7262	829	939	0.008	114

1976-126 BN	[14501]				2004 Jul 8.84	65.76	103.52	7304	506	1344	0.057	242

1976-126 BP	[14502]				2004 Jul 9.09	65.79	108.90	7554	557	1795	0.082	69

1976-126 BQ	[14503]				2004 Jul 9.18	65.85	117.25	7936	756	2358	0.101	128

1976-126 BR	[14799]				2004 Jul 1.82	65.82	123.25	8204	1096	2556	0.089	240

1976-126 BS	[14800]				2004 Jul 8.28	65.78	125.63	8310	1426	2436	0.061	99

1976-126 BT	[15555]				2004 Jul 8.68	65.79	115.30	7848	710	2228	0.097	93

1976-126 BU	[15762]				2004 Jul 8.55	65.67	114.53	7812	841	2027	0.076	296

D	1976-126 BV	[17670]	2003 Jun 27	9678 days		2003 Jun 21.98	65.61	90.02	6654	246	305	0.004	258

1976-126 BW	[18518]				2004 Jul 8.95	65.76	112.90	7738	792	1927	0.073	72

D	1976-126 BX	[18891]	1990 Jan 3 A	4755 days

1976-126 BY	[18907]				2004 Jul 10.40	65.82	109.57	7585	501	1912	0.093	49

1976-126 BZ	[19112]				2004 Jul 10.21	65.81	110.15	7612	502	1965	0.096	71

1976-126 CA	[19244]				2004 Jul 9.82	66.05	114.82	7826	885	2009	0.072	86

1976-126 CB	[19221] 				2004 Jul 3.56	65.82	113.45	7763	700	2069	0.088	249

1976-126 CC	[19425]				2004 Jul 10.10	66.56	113.27	7755	1125	1627	0.032	46

1976-126 CD	[19475]				2004 Jul 10.14	65.82	110.95	7649	602	1938	0.087	158

D	1976-126 CE	[19480] 	1990 Jan 3	4755 days

1976-126 CF	[19980]				2004 Jul 10.45	65.71	99.18	7098	479	961	0.034	135

1976-126 CG	[20673]				2004 Jul 9.87	65.62	104.12	7331	543	1363	0.056	52